MIRAGE B-108-G  RF Amplifier

The Mirage B-108-G is an RF power amplifier for 144-148 MHz.  A GaAsFET

receive pre-amplifier provides high gain and low-noise amplification for

weak signal applications.  The pre-amp includes a switchable attenuator to

reduce signal output level.  This is useful in preventing receiver overload

and subsequent intermodulation distortion caused by strong signals.  Provision

is made for automatic or remote (external) keying, and for remote control of

all front-panel functions using the Mirage RC-1 Remote Control Unit. The

Mirage B-108-G is capable of FM, SSB, and CW operational modes.  10 Watts of

drive power will produce 80 Watts of output.

Specifications:

Frequency range: 144 to 148 MHz

RF input power (Drive):	5 Watts to 15 Watts

RF output power: 80 Watts (maximum) with 10 Watts drive

Duty cycle: Intermittent (ICAS)

Modes:  FM, SSB, CW

Receive pre-amp:   GaAsFET, Gain 21/15 dB-Nominal.  Noise figure less than

0.6 dB. 1 dB compression point greater than -13 dBm input (Nominal)

VSWR power shut-down point:   3:1 approximately

RF input power shut-down point:	5 Watts Nominal

Temperature power shut-down point: 175 Degrees F.

Keying:  Automatic (RF sensing) or remote (external)

Input/Output impedance:   50 Ohms

RF connectors:	SO-239 (UHF)

Remote keying connector:     RCA phono

Remote control connector:   6 pin Molex

Supply voltage:  13.8 Vdc (for full RF power output)

Supply current: 25 Amps (Nominal)

Fuse:	Low voltage, fast-blow, 35 Amps

Physical dimensions: 12" x 3" x 5 1/2"

Weight: 5 Lb.

Use with HT's:

The Mirage B-108-G may be 'keyed' with as little as 200mW.  It makes an

excellent amplifier to be used with HT's, as 2 Watts of drive will produce 30

to 35 Watts of output.

Installation:

The Mirage B-108-G must have adequate ventilation around the heat-sink.  Use

of #8 or larger wire to connect the B-108-G to the battery is recommended.

Use good quality 50 Ohm coaxial between the radio and the B-108-G.  RG-8U or

the equivalent should be used between the B-108-G and the antenna.  For the

best performance, the antenna should be matched to better than 1.5:1.  Higher

SWR will not damage the amplifier but it will degrade the overall system

performance.

Caution:	With extended use, the heat sink becomes very hot!

Front Panel Functions:

Power ON/OFF:

Turns the power amplifier ON and OFF.

Fault Light:

This light indicates amplifier shut-down due to excessive SWR, input power,

or heat.  Power to the unit must be turned OFF and then back ON to reset the

protection circuit before the amplifier will return to normal operation.

SSB/FM:

Selects the relay time delay for the mode of operation.  In either the SSB

or FM position, the amplifier is still biased for linear operation.

Pre-amp ON/OFF:

Turns the pre-amplifier ON and OFF.  This switch works independent of the

Power ON/OFF switch.  When either the Pre-amp or Power amp is turned on, the

amplifier automatically switches the antenna using its internal circuitry.

If it is desired to key the antenna relay externally, a connection is provided

on the rear panel (see Rear Panel Functions).

Rear Panel Functions:

RADIO:  This connects to the transmitter or transceiver.

ANTENNA: This connects to the antenna.

13.8 Vdc:   Pin 1 is for remote keying; connect to ground to key antenna

relay.  Pin 2 is +13.6 Vdc.  Pin 3 is ground.

FUSE:	Low voltage, fast-blow, 15 Amps.  Input power should not exceed 15

Watts.  Higher power than this may cause failure of the input

transistor.  This will VOID ANY WARRANTY.

EXTERNAL REMOTE:  The optional Mirage RC-1 Remote Control Head connects here.

See the Remote Control Head documentation for further details.

Internal Adjustments: SSB Delay:  This allows the transmit delay to be

adjusted to different delay times.  It can be accessed

through the right side of the cover in a position that is

located halfway between the front and rear of the panel.

Pre-amp Tuning:  The gain adjustment switch is located on the right side of

the unit, located approximately 1.5" behind the front panel

and approximately 1" in from the side of the unit.  It should

be switched DOWN for HIGH gain, and UP for LOW gain.

B-108-G TUNING PROCEDURE

These procedures should only be accomplished by an RF technician with the

appropiate test equipment. The information contained below is for general

information only. You are not required to perform these alignment procedures

to make the amplifier operational as they have already been completed at the

factory.

Setting the Idling Current

1.	Connect the amplifier to a dummy load before making any other

connections to prevent damage.

2.	Ensure that your DC voltage from the power supply is off.

3.	Connect the power supply and all other connections to the amplifier.

Ensure that the exciter radio is off until directed.

4.	Short the bottom pin of the 3 pen molex connector located on the rear

to ground. This will cause the transmit relay to energize when the

amplifier power is switched on.

5.	Insert a meter capable of reading current from 0 milliamps to 5 amps

into the red power lead going into the amplifier and the power supply.

6.	Apply power to the amplifier and turn the unit on while observing the

current reading on the meter.

CAUTION:      If the current surges too high, immediately remove power!

7.	Upon application of power, the intial reading should be approximately

.22 amps of current.

8.	Locate and adjust the power amplifier bias pot, R4 to reflect an

additional 10 milliamps on the meter, for a reading of approximately

.34 milliamps

9.	Turn the unit off and remove the DC power.

10.	Remove the shorted pin from the 3 pin molex connector.

11.	Disconnect the meter from the circuit and place the fuse back in the

holder.

Measurement of Insertion Loss

1.	Ensure that the power is in the off position on the front panel.

2.	Set the frequency of the exciter radio to the center of the allocated

band (In the case of the Amateur band, 146.000 MHz)

3.	Turn the exciter radio on and adjust the output power to 5 watts FM

or CW when keyed.

4.	Verify that there is no reflected power.

5.	Increase the power to 10 watts and measure the insertion loss through

the relay contacts.

6.	With 10 watts injected, the output watt meter should read 8.2 watts

or more.  The difference is the insertion loss, which should be no

more than 1.8 watts. The input reflected should read less than 400

milliwatts.

Tuning the Amplifier

NOTE:	Key-up by applying RF during test only.  while tuning & testing,

always observe the current     draw, spectrum analyzer, and input

VSWR.

1.	Key the exciter radio and adjust the output power to 2 watts FM or CW.

2.	Turn the DC power supply on.

3.	Place the front panel power switch in the on position.

4.	Quickly, and with minimum key up time, adjust the C37 trimmer

capacitor on the output side of the final power transistor for the

maximum power output as shown on the output power meter and minimum

current draw.

5.	Simultaneously observe the input reflected power meter and adjust C37

for minimum VSWR on the input while maintaining the maximum power that

can be obtained on the output.

6.	Observe the spectrum analyzer and readjust C37 if any spurs or

oscillations are present.

7.	Adjust capacitor C38, located on the input side of the power

transistors for minimum reflected power on the input meter and

maximum output power.

8.	Again, observe the sprectrum analyzer and readjust if any spurs or

oscillations are present.  Unkey the transmitter.

9.	Place the power switch on the front panel in the OFF position.

10.	Increase the drive on the exciter radio to 10 watts

11.	Place the power switch on the front panel in the on position.

12.	Repeat steps 4 through 8 above.

13.	Check the power out and input reflected for tollerances at 144, 146,

and 148 MHz. The power should read at least 80 watts.  Current at

full power output should not exceed 12 amps at 13.8 Vdc.

Adjusting the Receive Preamp

1.	Remove the input and output coax cables for the amplifier radio and

antenna connectors.  MAKE SURE YOU TURN THE TRANSMIT RADIO OFF.

2.	Connect a coax from a signal generator through a 5 dB pad to the

output/antenna connector of the amplifier.  Set generator to mid-band,

146 MHz with a -55dBm signal.

3.	Connect a coax from the sprectrum analyzer to the input/radio

connector  of the amplifier.

4.	Set the sprectrum analyzer to read 10dB per cm vertical deflection.

Apply a 3cm reference signal from generator (appoximately -55dBm).

5.	Turn on receive amplifier.  Signal should increase 1.5 cm (15dB) with

dip switch SW4 in low gain position and 2.1 cm (21dB) in the high

gain position.  (Note: Because of the devices used, 12dB gain is

possibly all the gain that may be achieved in a worst case event in

the high gain position.)

6.	If you do not have sufficient gain, adjust the variable capacitor C31

for 15dB gain with S4 dip switch in low gain position.

Troubleshooting:

The Mirage B-108-G is designed for long, trouble-free performance and should

not require extensive troubleshooting in the field.  Many causes of common

malfunctions are eliminated by the built-in protective circuitry.

Note:  In the event of automatic power shut-down, the amplifier must be turned

off     and the cause of the shut-down determined and removed!

In case of difficulty, check the following before assuming amplifier

malfunction:

a.	Loose antenna or power supply connections

b.	VSWR of antenna system

c.	Coaxial cables from radio to amplifier, and amplifier to antenna

d.	Output voltage of power supply

e.	Power output of radio

f.	Improper fuse rating

Technical Assistance

If you have any problem with this unit, first check the appropriate section

of this manual. If the manual does not reference your problem or your problem

is not solved by reading the manual, you may call MIRAGE at 601-323-8287.

You will be best helped if you have your unit, manual and all information on

your station handy so you can answer any questions the technicians may ask.

You can also send questions by FAX to 601-323-6551.  Send a complete

description of your problem, an explanation of exactly how you are using

your unit, and a complete description of your station.