1. CENTER OFF-SET VOLTAGE	2. BAR METER SENSITIVITY ADJUSTMENT

ADJUSTMENT (Refer to Figs. 5, 6)		(Refer to Figs. 5, 6)

Connect the Digital Voltmeter or DC Voltmeter to	The Meter Switch should be set to “x1”.

the Speaker terminal. Adjust the VR1 (1 kB) on the	Connect a load resistor (RL: 8 ohms) to the Speaker

Main Amp P.C Board, so that the Voltmeter reading	terminal, and input 1 kHz through the AUX terminal.

is 0 ±10mV.	Adjust the VR2 (2 kB) on the Main Amp P.C Board

until the voltage at both ends of the load resistor is

10.95 V (AC voltmeter) where the Power Meter

indicate 15 watts.

1.  P.C BOARD TITLES AND IDENTIFICATION NUMBERS

| P.C Board title | P.C Board Number |
| --- | --- |
| Main Amp P.C Board | AMU-4001 A |
| Push Switch P.C Board | AMU-4001 B |
| LED P.C Board (B) | AMU-4001C |
| Selector P.C Board | AMU-4002 |
| Tone Control P.C Board | AMU-4003 |
| Pin Jack P.C Board | AMU-4005 |
| Fuse P.C Board (U/T) | AMU-4006 |
| Fuse P.C Board (CSA, AAL) | AMU-4058 |
| Fuse P.C Board (JPN) | AMU-4060 |
| Fuse P.C Board (CEE, UK, SAA) | AMU-4059 |
| LED P.C Board (A) | AMU-4007 |
| Slide Volume P.C Board | AMU-4008 |
| Loudness P.C Board | AMU-2003 |
| Bar Meter P.C Board | AMU-2006 |

Chart-1