1. 	MOTOR LEAF SWITCH TIMING	2. 	MUTE LEAF SWITCH INSTALLATION

ADJUSTMENT (Refer to Fig. 17) 	POSITION ADJUSTMENT (Refer to Fig. 18)

The FF key has been depressed and when the 	When in the playback mode, the space A should

capstan gear turns before points A and B gears 	be 0.5 to 1.0 mm as in Fig. 18. To adjust, turn the

are engaged, they screech because the middle 	leaf switch installation screw.

gear which was engaged springs off. Adjust the 	Confirm the switch stays in the same position

timing of the motor revolutions to prevent this.	when the FF and PLAY or RWD and PLAY keys

Gently depress the FF key and adjust the 	are depressed together.

installation position of the motor leaf switch until

the motor's switch is activated after the points A

and B gears have been engaged slightly.

3. 	FLYWHEEL LOOSE PLAY 	5. 	WINDING TORQUE MEASUREMENT

ADJUSTMENT (Refer to Fig. 19) 			IN EACH MODE

Insert the various washers in the three places 		Insert cassette torque meter and measure in each

between the prop and the flywheel hold plate and 		mode.

adjust to give 0.1 to 0.2 mm loose play when the 		For fast forward and rewind measure at the end of

flywheel is moved in the direction of the arrows.		the tape when the tape has stopped running.

The specified torque is:

4. 	PINCH ROLLER PRESSURE  			Playback 	: 	35 to 60 g-cm

MEASUREMENT (Refer to Fig. 20)		Fast Forward, Rewind 	: 	80 to 120 g-cm

At playback mode, push the pinch roller with a spring 		In case specified take-up torque cannot be attained.

gauge until the pinch roller separates from the 		Playback mode : Replace Take-up Reel Table Block.

capstan by about 1 mm to 2 mm and then gently return. 		Fast Forward of Rewind mode:

Take a reading of the spring gauge indication at the 			Replace Middle Gear Block.

moment the pinch roller touches the capstan and begins

to rotate	6. 	TAPE SPEED ADJUSTMENT

Specified Pinch Roller Pressure: 330 ± 30 grm			(Refer to Fig. 21)

In case specified pressure cannot be attained, replace 		Connect the frequency counter to the line output

the pinch roller spring.		terminals. Playback a 1.000 Hz pre-recorded test tape

and adjust tape speed adjustment screw to obtain a

tape speed of 1,000 11z ± 1%.

1. 	TAPE GUIDE HEIGHT ADJUSTMENT  	2. 	REC/PB HEAD PROJECTION  ADJUSTMENT

(Refer to Figs. 22, 23) 		Set the AKAI Head Projection Gauge (Fig. 24) and

1) 	When using an ordinary cassette, the tape 		adjust (a) and (b) screws (Fig. 22) so that it reads:

guides and heads, etc. are not visible. As 		1.9 to 2.2 mm in the WLS Mode, 3.55 ± 0.1 mm

shown in Fig. 23 use a cassette tape from 		in the Play Mode.

which part of the cassette case has been cut 		NOTE: 	Raise or lower by exactly the same amount

out and a mirror installed for easy visibility of 			the head hanger's left and right and adjust

the head area when making tape guide height 			so that the head does not lean to the left or

adjustment.			right.

2) 	At playback mode, using the tape guide (A)

shown in Fig. 22 as standard for height, adjust

tape guide (B) height with tape guide height

adjustment nut so that the tape runs smoothly

and does not catch on the tape guides.

3. RECORDING/PLAYBACK HEAD HEIGHT

ADJUSTMENT (Refer to Figs. 22, 23)

1)	Utilize the cassette tape used in Tape Guide Height Adjustment above, and playback the leader tape part of cassette tape.

2) 	As shown in Fig. 22, adjust head height with screws (c), (d) and (c) until the upper edge of the tape is the same height as the upper edge of the left channel REC/PB head core.

3) 	After completing adjustment step 2), playback the Head Height Adjustment tape (4 track, 1,000 Hz) and adjust Head Height Adjustment screws (c), (d), (e) to put the output power from both channels to maximum.

4. 	RECORDING/PLAYBACK HEAD

AZIMUTH ALIGNMENT ADJUSTMENT

(Refer to Fig. 22)

1) 	Playback a 10 kHz pre-recorded cassette azimuth alignment test tape and adjust screw (d) shown in Fig. 22 to obtain maximum output on both channels.

2) 	Invert cassette and confirm that the output level does not change from that obtained in Item 4-1) above. If the output level differs, adjust in the same way as in Item 4-1) above until both sides of the test tape display equal output.

3) 	After adjustment, better to check again head height and azimuth alignment.

NOTES:

1. 	Be sure to clean the heads prior to head adjustment.

2. 	Be careful not to use a magnetized driver or other magnetized tools in the vicinity of the heads.

3. 	Be sure to demagnetize the heads with a Head Demagnetizer before and after head adjustment.

4. 	When a mirror installed cassette test tape as shown in Fig. 24 is required, it can be ordered from AKAI Electric Co.

| Step | Adjustment Item | Test Tape Supply Signal | Mode | Adjustment Point | Results | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Playback Level | 333 Hz, 0 VU Test Tape | PB | VR4 50 kB | -5.5 ± 0.5 dBm (410 mV) |  |
| 2 | Bar Meter Sensitivity | 1,000 Hz -5,5 dBm from oscillator | REC | VR6 30 kB | 0 VU indication |  |
| 3 | Playback Equalizer | 10 kHz Test Tape | PB | VR3 5 kB | -19.0 ± 0.5 dBm |  |
| 4 | Rec Peaking adjustment | 16.7 kHz -25.5 dBm from oscillator | REC | VL 1 10 mH | AC Voltmeter indicates to maximum | Tape selector to LN. See the Figs. 25, 26, 27. NOTES 7, 10 |
| 5 | LN Position Frequency Response | Low Noise Blank tape. 1,000 Hz 10,000 Hz - 25.5 dBm recording | RECIPB | VR 10 100 kB | 1,000 Hz to 10,000 Hz flat |  |
| 6 | W Position Frequency Response | LH Blank tape 1,000 Hz 10,000 Hz -25.5 dBm recording | REC/PB | VR 7 50 kB | 1,000 Hz to 10,000 Hz flat | Set tape selector to LH Position |
| 7 | Cr02 Position Frequency Response | CrO2 Blank tape 1,000 Hz 10,000 Hz -25.5 dBm recording | REC/PB | VR 8 50 kB | 1,000 Hz to 10,000 Hz flat | Set tape selector to Cr02 Position |
| 8 | Metal Position Frequency Response | Metal Blank tape 1,000 Hz 10,000 Hz -25.5 dBm recording | REC/PB | VR 9 20 kB | 1.000 Hz to 10,000 Hz flat | Set tape selector to Metal Position |
| 9 | Recording Level | LN Blank tape 1,000 Hz -5.5 dBm recording | REC/PB | VR 5 30 kB | -5.5 ± 0.5 dBm | Set the Mic Volume to Minimum |
| 10 | Distortion Factor Confirmation | 1,000 Hz -5.5 dBm recording | REC/PB |  | LN < 0.8% W < 0.8% CrO2 < 0,7% Metal < 0.6% | NOTE 8 |
| 11 | Bias Filter | No signal input | REC | FL 1 D07-003 | AC Voltmeter indicates to minimum | Set tape selector to Metal Position Set REC Volume to Maximum. NOTE 10 |
| 12 | 19 kHz Filter adjustment | 19 kHz from oscillator | REC | FL 2 D07-001 | AC Voltmeter indicates to minimum | Set Dolby NR Switch to ON, filter ON Position. NOTES 9, 10 |

Chart-3

NOTES: 	1.	The Output Level Control should be at maximum.

2. 	Input selector switch to LINE. (The JPN, AAL Models do not have this facility.)

3. 	Because each of these adjustments is vital to perfect Dolby NR circuit operation, ensure that they are carried out with as few errors as possible.

4. 	Except for Step 6 thru 8 and 10, set Tape Selector to LN Position.

5. 	Except for Step 12, set Dolby NR switch to OFF Position.

6. 	Use the following cassette measuring tapes:

LN tape TDK LN2 C-60

LH tape Maxell UD C-60

Cr02 tape : TDK SA C-60

Metal tape : TDK MA-C  C-60

7. 	Stop the recording bias oscillator while making record peaking adjustment (Refer to Fig. 27).

8. 	If it does not comply with the specifications, repeat Steps 5 to 9 and readjust.

9. 	Adjust the oscillator's frequency to give a frequency counter reading of 19.00 kHz.

10. 	Unless the core is moved unintentionally this adjustment is not necessary.