# OmniBER 718 OPTION 355 Extract of Technical Specification

### Service Disruption Measurement

Note: Requires Option 012.  Features marked * require Option 355.

Protection switch times Service disruption test measures error burst length for measurement of protection switching times to ITU-T G.783 (linear architecture)/G.841 (ring network topology).

Results: longest burst length, shortest burst length, last burst length, timestamping of service disruption events*, history of first 10 service disruption events*, AIS indicator*.

#### Measurement parameters

|  | Display Resolution | 1 (s. |
| --- | --- | --- |
|  | Measurement Accuracy | 50 (s or better (for unframed signals). |
|  | Pattern | All current supported PRBS patterns, which are 29-1, 211-1, 215-1, 220-1 & 223-1 normal or inverted. Bulk filled. PDH/T-carrier mapped payloads (longest burst, shortest burst, last burst only) POS (Using PRBS). ATM (Using ITU-T O.191 test cell). |
|  | Start condition | Single bit error. |
|  | Stop condition | Error burst assumed complete when greater than 200ms have elapsed without any errors being received. |
|  | Measurement Period | The elapsed time between the first bit error received and the last error received when the stop and start conditions have been met. |

### AIS Duration Measurement

Note: Requires Option 355

SONET: AIS refers to AIS-P

SDH: AIS refers to AU-AIS

AIS Duration measurements are available on all optical rates up to the highest rate fitted.

Results: AIS duration measurement, timestamping of AIS events, history of first 10 AIS events.  Flags and timestamping allow correlation of service disruption and alarms,

#### Measurement parameters

|  | Resolution | 1 (s |
| --- | --- | --- |
|  | Measurement Accuracy | 125 (s (1 SONET/SDH frame) |
|  | Start condition | Detection of an all ones pattern in the H1 and H2 bytes, present for three consecutive frames |
|  | Stop condition | The absence of all ones in the H1 and H2 bytes for three consecutive frames or by the single occurrence of an active NDF with a valid (in range) pointer value. |
|  | Measurement Period | The elapsed time between the start of the frames in which the start and stop conditions are met, respectively. |