High resolution progressive scan monochrome CCD camera

(Frame shutter)

KP-F100BCL

Specifications (preliminary)

1.	  Outline

Hitachi's KP-F100BCL is a 2/3-inch size black and white CCD camera designed for high resolution

and versatile functions.  Progressive scan with full pixel independent readout and full frame shutter

provide images of unparalleled quality at 15 frames per second non-interlaced output.

Effective picture elements number 1.45 million, while the broad array of functions includes digital

output, multi-step electronic shutter, HD/VD external sync and frame on demand.  The square lattice

pixel format also provides excellent suitability for image processing applications.

2.	Outstanding features

(1)	High resolution

High grade CCD with 1392 (H) x 1040 (V) effective pixels.

(2)	Frame shutter

The frame shutter function improves vertical resolution of moving objects..

(3)	Multistep electronic shutter

The shutter speed can be selected in 8 steps from 1/30th to 1/50,000th of a second.

(4)Frame on demand

An external trigger signal input can be used to capture an image at a desired timing for instant

view or processing.  The capture time can be adjusted by the trigger and shutter.

(5) The self-contained CPU permits using remote control for setting each function.  The functions

can also be set from rear panel switches.

(6)	Digital output

CAMERA LINK

(7)Trigger input pulse reversal function

It is able to reverse to a positive pulse with the remote control, although trigger

input is an usually negative pulse.

3.	Specifications

(1)	Pickup element	2/3-inch interline CCD

Total pixels	1432 (H) x 1050 (V)

Effective pixels	1392 (H) x 1040 (V)

Pixel pitch	6.45 (H) x 6.45 (V) um (square lattice)

(2)	Imaging area	8.98 (H) x 6.71 (V) mm

(3)	Scanning system	Non-interlaced

(4)	Aspect ratio	4 : 3

(5)	Frame rate	15frames/second (full pixel readout)

60 fps (4×accelerated mode)

Factory setting is 15 fps.

Selected by rear panel switch.

(6)	Horizontal scanning frequency	16 kHz

(7)	Vertical scanning frequency	15 Hz

(8)	Synchronization	Internal/external (automatic switching)

(9)	Lens mount	C mount

(10)	Flange focal distance	17.526 mm

(11)	Video output	Digital output or analog output for image checking

Analog　output

Digital output                 CAMERA LINK

Data : Base configuration 10bit x 1

Clk = 28.64MHz

(12)External sync input	HD/VD LVDS level negative

Input impedance:  100

Frequency deviation:  +1%

(13)Electronic shutter speed	Selectable by external switches:  Off (frame rate), 1/30,

1/125, 1/250, 1/1000, 1/2000, 1/4000, 1/10000

1/50000 second.

Off:  Normal exposure (frame rate)

Set by external switch; factory setting is off (1/15 second).

(14) Gamma compensation 	r = 1

(15)Frame on demand            External switch setting on/off and modes (fixed shutter, two

trigger and one trigger).  Factory setting is all off.

Fixed shutter mode

Two trigger mode

One trigger mode

(16)Power supply voltage	12 + 1 VDC

(17)	 Current consumption	Approx. 330 mA

(18)Ambient, operating	0 to + 40   (+32 to ; 104 F), less than 90 % RH

Ambient, storage	-10 to + 50   (+14 to +122 F), less than 70 % RH

Note:	If operated continuously, be sure to use at less than +40   (104 F) for long term stable

performance.

(19)	Vibration endurance	29.42 m/s2 (3 directions, 30 minutes each)

(20)	Shock endurance	294.2 m/s2 (vertical, horizontal, once each face)

(21)	External dimensions	44 (W) x 44 (H) x 78 (D) mm

(22)	Mass	Approx. 180 g

(23)  Remote control

(a) Signal system

Control system                  Start-stop synchronization system

Transmission rate               9600 bps

Data length                     8 bits

Start bit                        1

Stop bits                        2

Parity                          None

Bit transfer                     LSB first

(b) Communications control system

Full control by remolte control software, data send/receive by text data transfer to

camera microprocessor (BSC system handshake)

(C) Control items

1. Shutter speed (1/30, 1/125, 1/250, 1/1000, 1/2000, 1/4000, 1/10000,1/50000 second)

2. FD (frame on demand)           On/off

3. Mode                           Fixed shutter, two trigger, one trigger

4. 4×accelerated mode             On/off

5. Gain                            Variable in 50 steps

6. Black level                      Variable in 50 steps

7.Input trigger                     Negative/Positive

4.	Composition

(1)	Camera (with infrared blocking filter)

(2)	Operating instructions

5.	Optional accessories

(1)	Tripod adaptor	TA-M1

(2)	12 pin plug	HR10A-10P-12S(01)

(3)	D. OUT connector (26 pins)	10226-5202JL or equivalent

(4)	Junction box	JU-M1A ,  JU-F1*

(5)	Dummy glass (AR coated)	ARC1214

(6)	Camera cable

|  | Molded type | Assembly type | Shield type |
| --- | --- | --- | --- |
| 2 m | C-201-KSM | C-201KS | C-201KSS |
| 5 m | C-501KSM | C-501KS | C-501KSS |
| 10 m | C-102KSM | C-102KS | C-102KSS |

Note : Assembly type made to order.

In the CE Marking region ,use the shield type.

* 12-pin connector output pin differences

| Pin | JU-F1 | KP-F100BCL output |
| --- | --- | --- |
| 4 | VIDEO 1 | VIDEO |

6.	DC input and sync connections

(1)	Connections to DC IN and SYNC

| Pin No. | Int. sync | Ext. sync |
| --- | --- | --- |
|  |  | Ext. HD/VD | Frame on demand |
|  |  |  | Fixed shutter | Two trigger | One trigger |
| 1 | GND | GND | GND | GND | GND |
| 2 | +12V | +12V | +12V | +12V | +12V |
| 3 | GND | GND | GND | GND | GND |
| 4 | VIDEO | VIDEO | VIDEO | VIDEO | VIDEO |
| 5 | GND | GND | GND | GND | GND |
| 6 | --------- | --------- | --------- | --------- | --------- |
| 7 | --------- | --------- | --------- | --------- | --------- |
| 8 | GND | GND | GND | GND | GND |
| 9 | --------- | --------- | --------- | --------- | --------- |
| 10 | GND | GND | GND | GND | GND |
| 11 | +12V | +12V | +12V | +12V | +12V |
| 12 | GND | GND | GND | GND | GND |

Connector (camera side)	:  Hirose HR10A-10R-12PB(01)

Plug (matching cable plug)	:  Hirose HR10A-10P-12S  (01)

(2)	Signal connections to D. OUT (26 pin)

| PIN No. | Signal | PIN No. | Signal |
| --- | --- | --- | --- |
| 1 | GND | 14 | GND |
| 2 | TxOUT0(-) | 15 | TxOUT0(+) |
| 3 | TxOUT1(-) | 16 | TxOUT1(+) |
| 4 | TxOUT2(-) | 17 | TxOUT2(+) |
| 5 | TxCLKOUT(-) | 18 | TxCLKOUT(+) |
| 6 | TxOUT3(-) | 19 | TxOUT3(+) |
| 7 | RX(+) | 20 | RX(-) |
| 8 | TX(-) | 21 | TX(+) |
| 9 | TRIG-A/VD[CC1(-)] | 22 | TRIG-A/VD[CC1(+)] |
| 10 | TRIG-B(+)[CC2(+)] | 23 | TRIG-B(+)[CC2(-)] |
| 11 | EXT-HD(-)[CC3(-) | 24 | EXT-HD(-)[CC3(+)] |
| 12 | NC[CC4(+)] | 25 | NC[CC4(-)] |
| 13 | GND | 26 | GND |
|  |  | Shield | GND |

Connector (camera side)  	:  Sumitomo 3M  10226-5202JL or an equivalent

Plug(matching cable plug)	:  Sumitomo 3M  10126-6000 or an equivalent

The digital out cable should be comprised of a twisted pair of wires having 100

characteristic impedance and an outer sheath shield type conductor.  Connect the shield

(ground) of the digital out cable to the ground terminal of the video eqquipment, frame

grabber, etc.

7.	Rear panel switches

The rear panel includes switches for electronic shutter data, remote on/off, and field on demand on/off

and mode switches.

(1) Electronic shutter switches

(2) REMOTE ON/OFF switch

(Factory setting)

(3)Frame on demand (FD) on/off switch

(4) Frame on demand mode switch

8.	Input/output signal levels and timing

(1) Digital output

H sync phase relationship

1clk = 28.64MHz

V sync phase relationship

(2)KP-F100ACL Transmitter LVDS Output Pulse Position Measurement

(3)TRIG-A input and HD & VD phase during Fixed shutter mode

Transmit TRIG-A at LVDS level

(4)TRIG-A & B input phase and HD & VD phase during Two trigger mode

Transmit TRIG-A & B at LVDS level

(5)One trigger mode

Transmit TRIG-A at LVDS level

(6) External HD & VD input levels and phase

Level:  LVDS

Align falling edges of external HD and VD.

VD output is delayed 2H compared to EXTVD

Notice: These specifications are subject to change without prior notice due to product improvement. Confirm the most recent specifications at time of order. Hitachi Kokusai certifies this product complies with the standard warranty conditions of Hitachi Kokusai, and that quality control is implemented to the extent required to comply with these conditions.

Warranty and service:

- The guarantee period is one year after the data purchase. However, the defects due to erroneous use or intentional act are excluded.

- As the defect after expiration of the guarantee period, where product repair is possible, repair will be performed at charge. .

- The present Warranty pertains only to the camera unit. Secondary malfunctions attributable to camera failure as well as expenses incurred by disassembly and reassembly of the related system, are beyond the scope of this Warranty.

(4)  Compensation for loss of business, loss or damage to software, database and other contingent losses are beyond the scope of this Warranty.

- Hitachi Kokusai Electric Inc. is not liable for the losses caused when the equipment is used in a system, use for business trades, production process, medical fields, crime prevention applications, etc.

(6) The parts used in the equipment have their respective lives. The lives of such parts will be shortened under the environments of high temperature or high humidity.

When the stable operation is required for a long time, it is recommended to perform periodical maintenance and inspection every year or every two years.

# Text boxes

Tokyo Japan

DWN

DSGN

CHKD

APPD

・ ・

・ ・

・ ・

・ ・

1

2

3

4

1

2

3

Ａ

Ｂ

Ｃ

Ｄ

Ｅ

Ｆ

1/15

Tokyo Japan

DWN

DSGN

CHKD

APPD

・ ・

・ ・

・ ・

・ ・

1

2

3

4

1

2

3

Ａ

Ｂ

Ｃ

Ｄ

Ｅ

Ｆ

2/15

Tokyo Japan

DWN

DSGN

CHKD

APPD

・ ・

・ ・

・ ・

・ ・

1

2

3

4

1

2

3

Ａ

Ｂ

Ｃ

Ｄ

Ｅ

Ｆ

3/15

Tokyo Japan

DWN

DSGN

CHKD

APPD

・ ・

・ ・

・ ・

・ ・

1

2

3

4

1

2

3

Ａ

Ｂ

Ｃ

Ｄ

Ｅ

Ｆ

4/15

14/15

Ｆ

Ｅ

Ｄ

Ｃ

Ｂ

Ａ

3

2

1

4

3

2

1

・ ・

・ ・

・ ・

・ ・

DWN

DSGN

CHKD

APPD

Tokyo Japan

6/15

Ｆ

Ｅ

Ｄ

Ｃ

Ｂ

Ａ

3

2

1

4

3

2

1

・ ・

・ ・

・ ・

・ ・

DWN

DSGN

CHKD

APPD

Tokyo Japan

Tokyo Japan

DWN

DSGN

CHKD

APPD

・ ・

・ ・

・ ・

・ ・

1

2

3

4

1

2

3

Ａ

Ｂ

Ｃ

Ｄ

Ｅ

Ｆ

7/15

Tokyo Japan

DWN

DSGN

CHKD

APPD

・ ・

・ ・

・ ・

・ ・

1

2

3

4

1

2

3

Ａ

Ｂ

Ｃ

Ｄ

Ｅ

Ｆ

9/15

(Factory setting)

N.C

D9

N.C

N.C

N.C

N.C

N.C

D9-1

N.C

N.C

N.C

N.C

N.C

HD

VD

N.C

N.C

HD

Tokyo Japan

DWN

DSGN

CHKD

APPD

・ ・

・ ・

・ ・

・ ・

1

2

3

4

1

2

3

Ａ

Ｂ

Ｃ

Ｄ

Ｅ

Ｆ

10/15

N.C

D6

EXT HD

1 ~ 2 H

+2 us

VD

EXT VD

REMOTE ON : Control by REMOTE

REMOTE OFF : Control by REAR Panel switch

OFF

ON

1H = 16KHz = 1790clk

13/15

Ｆ

Ｅ

Ｄ

Ｃ

Ｂ

Ａ

3

2

1

4

3

2

1

・ ・

・ ・

・ ・

・ ・

DWN

DSGN

CHKD

APPD

Tokyo Japan

TCLK

Next Cycle

Prevlous Cycle

TxOUT0

TxOUT1

TxOUT2

TxOUT3

TxCLK OUT

D0

D1

D2

D3

D4

D5

D8

D0-1

D1-1

0 + 3 nS

LVDS LEVEL

Tokyo Japan

DWN

DSGN

CHKD

APPD

・ ・

・ ・

・ ・

・ ・

1

2

3

4

1

2

3

Ａ

Ｂ

Ｃ

Ｄ

Ｅ

Ｆ

5/15

Tokyo Japan

DWN

DSGN

CHKD

APPD

・ ・

・ ・

・ ・

・ ・

1

2

3

4

1

2

3

Ａ

Ｂ

Ｃ

Ｄ

Ｅ

Ｆ

11/15

12/15

Ｆ

Ｅ

Ｄ

Ｃ

Ｂ

Ａ

3

2

1

4

3

2

1

・ ・

・ ・

・ ・

・ ・

DWN

DSGN

CHKD

APPD

Tokyo Japan

Tokyo Japan

DWN

DSGN

CHKD

APPD

・ ・

・ ・

・ ・

・ ・

1

2

3

4

1

2

3

Ａ

Ｂ

Ｃ

Ｄ

Ｅ

Ｆ

8/15

D7

N.C

N.C

N.C

N.C

N.C

D6-1

D7-1

(DVAL) (FVAL) (LVAL)

+ 0.5

+ 1