INSTRUCTIONS FOR

INSTALLATION AND OPERATION

OF THE

MEISSNER SIGNAL SHIFTER  MODEL EX

I.     INTRODUCTION

A.     The MEISSNER SIGNAL SHIFTER is a variable frequency exciter, with output over the entire ranges of the 10, 11, 15, 20, 40 and 80 meter amateur bands, designed for placement within easy reach of the operator.

The SIGNAL SHIFTER uses a 6V6GT/G tube in a highly stable electron-coupled oscillator circuit.  The oscillator frequency is doubled in the tuned plate circuit of the oscillator and again in the plate circuit of the 807 doubler-amplifier.  The high order of stability of the SIGNAL SHIFTER is achieved by the use of a high-C circuit, high quality components, including zero temperature-coefficient capacitors, efficient turret mounted inductors, and a stand-by circuit which maintains steady plate currents in the tubes during either operating or stand-by conditions.  In addition, stability and reliability are insured by operating the tubes well within their ratings, and by voltage regulation of the oscillator tube plate and screen voltages.

The SIGNAL SHIFTER becomes an excellent crystal controlled exciter when a suitable crystal is plugged into the crystal socket and the ECO-XTAL switch is thrown to XTAL.  Thus, the SIGNAL SHIFTER can be used for net operation or band-edge operation without additional equipment.

The power output on all bands is sufficient: 1. To drive a low or medium powered amplifier, using triodes.  2. To drive a medium or high powered amplifier using beam tubes, or 3. To allow its use as a low powered transmitter.  The power output on all bands is in excess of six watts, except for the 10 meter band, which is slightly lower.

B.     The SIGNAL SHIFTER is designed for operation from a MEISSNER Model PX power supply.  The Model P operates on 110 - 120 V., 50-60 cycle supply.  A 25 cycle model may be had on special order.

C.     The SIGNAL SHIFTER is furnished in either a gray or a black wrinkle metal cabinet, 13-13/16" long by 12-1/4" wide by 8-3/4" high.

A conversion kit is available to change the cabinet model to a standard rack panel model, 8-3/4" by 19".  This may also be obtained in either gray or black wrinkle finish.

Another conversion kit is available to allow the Model PX power supply to be removed from the SIGNAL SHIFTER cabinet and be placed remotely in a cabinet of its own, approximately 12" by 3-7/8" by 6-3/4".  This conversion, to provide the utmost in stability, may be made with either the table or rack panel version of the SIGNAL SHIFTER.

MEISSNER SIGNAL SHIFTER

D.     Selection of the desired amateur band is accomplished by rotating the coil turret with the band switch knob on the front panel.

Output frequency on any band is continuously variable by means of the precision vernier dial calibrated 0 to 500.  The calibration sheets at the back of this book give approximate dial settings for frequencies in each band.

Rapid rotation of the dial is possible with the handle provided.

Two jacks on the front panel allow a telegraph key with ordinary phone plug to be used for either oscillator keying or amplifier keying.

A knob on the front panel allows the operator to select any of the four follow-ing operating conditions:

1.   OFF

2.   AUTOMATIC

3.   STAND-BY

4.   ON

AUTOMATIC allows control of the SIGNAL SHIFTER by the stand-by switch in the higher-powered amplifier.  This is accomplished automatically by the built-in stand-by relay.

A tuning eye indicates grid current on the 807 and serves as a visual check on keying, crystal operation, and general oscillator operation.

II.     INSTALLATION

A.     Space Limitation

The SIGNAL SHIFTER should be installed to allow free circulation of air.  Nothing should be placed on or too close to the top of the cabinet.

B.     For Use as an Exciter to Higher          Powered Amplifier Stage(s).

In using the SIGNAL SHIFTER as an exciter, it is necessary to match the 300 ohm output impedance of the SIGNAL SHIFTER to obtain maximum output.  A few of the coupling circuits which may be employed are shown in Figures 1 to 4.

NOTE: In using Fig. 3, it is necessary to terminate the transmission line properly to avoid undesirable reflections.  (R may be 300 ohms or more and about 10 watts).

The transmission line should have a characteristic impedance of about 300 ohms for efficient transfer of power over any appreciable distance, although concentric cable, the standard transmission cables, or twisted pair will be satisfactory for the usual line lengths.

Do not ground either side of the transmission line at the SIGNAL SHIFTER end.  If it is desired to ground the transmission system, one side of the line at the link coil may be grounded, or the center of the link coil itself grounded as shown in Fig. 5

MEISSNER SIGNAL SHIFTER

The number of turns in the link is very important in the proper impedance matching of the SIGNAL SHIFTER to the driven stage.  The actual number of turns to give the maximum excitation should be determined by experimental cut and try.  DO NOT DISTURB THE COILS IN THE SIGNAL SHIFTER!  Vary only the number of turns and degree of coupling at the driven stage.  The best way to determine when the most excita-tion is obtained is by means of a milli-ammeter in the grid circuit of the driven stage.  The number of link turns should be varied until the desired grid current is obtained.  A loop of wire with a pilot bulb in series and held in the field of the grid coil of the driven stage is also a good indicator, as well as a neon bulb held near the grid coil, grid lead or stator plates of the grid tuning condenser.

After the link adjustments have been made, the cathode current (plate plus screen current) of the 807 tube in the SIGNAL SHIFTER should be measured.  A 0-100 MA. meter, fitted with a phone plug and plugged into the jack marked AMP, will read the 807 cathode current.  The normal cathode current of the 807, with load, is about 72 MA.  For PHONE work, this current should not exceed 80 MA.  For CW operation, slightly higher current is permissible.  In every case, use the least coupling which provides the required excitation, even if the 807 cathode current is, say, only 60 MA.

The AUTOMATIC terminals at the rear of the SIGNAL SHIFTER chassis and the AUTO position of the front panel switch are provided to allow control of the SIGNAL SHIFTER from the stand-by switch on the succeeding amplifier stage(s).  The AUTO terminals may be connected directly across the primary of the H.V. power transformer of the higher powered amplifier, as shown in Fig. 6.

Turning the on-standby switch of the higher powered stage to stand-by will automatically switch the SIGNAL SHIFTER from an ON position to a STAND-BY position, by action of the built-in relay.

C.	For Use as a Low Powered 	Transmitter.

The SIGNAL SHIFTER may be employed as a low powered transmitter without the use of additional amplifiers.  With a good antenna, very satisfactory results may be obtained.  Several methods of feeding antennas may be employed.  A few are shown in drawings 1 to 13.

With the exception of Fig. 10, the same procedure of loading and link adjustment should be followed as described under B above.  In Fig. 10, no adjustments should necessary.  If more or less loading is desired, the arrangement of Fig. 7 may be used.

MEISSNER SIGNAL SHIFTER

A check should be made before actual operation is begun, to be sure that harmonics are not being radiated, although the coupling methods shown tend to discriminate against harmonics.  In the event that harmonics are radiated, one of the methods of harmonic suppression described in the handbooks should be used.

III.	OPERATION

A.	General

After making the proper AUTO and OUTPUT connections, the line cord should be plugged in.  The SIGNAL SHIFTER may now be warmed up by turning the four position switch to STAND-BY.  A warm-up period of at least 15 minutes is required to insure stability.

In the STAND-BY position, the contacts of the AUTO relay allow normal plate currents to flow in the 6V6GT/G oscillator tube, but prevent oscillations (regardless of the position of the telegraph key) by shorting the cathode tap to the cold end of the oscillator grid coil.  This same condition may be obtained with the switch in the AUTO position, and the switch of the higher-powered amplifier thrown to STAND-By.  A warmed-up condition is thereby maintained during STAND-BY periods.

The band on which SIGNAL SHIFTER output is desired is selected by rotating the band switch.  Bands, with a 2% frequency overlap at each end, are:

80 Mtrs.	20 Mtrs.

40 Mtrs.	15 Mtrs.

10 & 11 Mtrs.

Any additional band, such as 75 Mtr. Phone band spread, may be ordered separately and installed by the operator.

B.	E.C.O.

Approximate dial settings for any frequency may be obtained from the calibration charts incorporated in this instruction book.  It is highly advisable to calibrate your SIGNAL SHIFTER, since the printed calibration charts are approximate only.

Calibration of the SIGNAL SHIFTER, after allowing a sufficient warm-up period, may be carried out using the standard frequency checking procedure as described in the radio technical handbooks.  A heterodyne frequency meter of known accuracy or a precision type frequency standard, such as the Meissner Crystal Controlled Signal Calibrator, should be used.  As many calibration points may be determined as desired, and the appropriate dial settings marked on the blank calibration charts provided.  The calibration procedure may be repeated on as many bands as desired.

When the calibration has been completed, the SIGNAL SHIFTER may be set for output in any part of the band.  Extreme care must be used in approaching the band edges.  A sub-stantial margin of safety should be allowed.

MEISSNER SIGNAL SHIFTER

Assuming that the SIGNAL SHIFTER has warmed up and is tuned to the desired frequency, the 4 - posi-tion switch should be placed in the ON position.  The procedure outlined under INSTALLATION #B should be followed to adjust the link to the driven stage to give the proper excitation and 807 cathode current.  Once the link turns and position have been determined, no changes should be necessary unless the driven stage is changed in some way.

The driven stage may now be put into operation in the normal way.  The 4-position switch should be turned to AUTO, in which position manipulation of the ON-STAND-BY switch in the higher-powered stage will automatically switch the SIGNAL SHIFTER to ON or to STAND-BY.

For CW., keying may be done in either the OSC or the AMP position, Oscillator keying is recommended for break-in operation, as amplifier keying allows the oscillator to run when the key is up.  The second harmonic of the oscillator plate circuit may be strong enough to interfere with reception of a signal near the frequency of the SIGNAL SHIFTER.

If the driven amplifier stage has no STAND-BY switch, the 4-position switch on the SIGNAL SHIFTER should be placed in the ON position during transmission periods and in the STAND-BY position during STAND-BY.  This should be done with oscillator keying to minimize drift, even though it is possible to operate without moving the switch from ON.

For phone operation, the key may either be left out of the key jacks or plugged in with the shorting bar on the key closed.

C.	Crystal Control

If crystal controlled operation is desired, the ECO-XTAL switch should be thrown to XTAL.  In this position, the 6V6GT/G becomes a very efficient grid-plate crystal oscillator which has extremely low crystal current.  The crystal socket accommodates either a holder with  inch pin spacing or a holder with 3/4 inch pin spacing, the two most common types.  The crystal used must have a frequency one-half that desired in the output, since the 807 doubles frequency.  For example, for output on 3,600 Kc. In band A, a crystal ground for 1,800 Kc. Must be used.  The crystal will usually operate best when the tuning dial is set for the output frequency with E.C.O.  However, it may be found necessary to rock the tuning dial slightly to one side or the other to obtain best keying characteristics with some crystals.  It is usually possible to shift from E.C.O. to XTAL, with output on the same frequency, without moving the tuning dial.

The tuning eye may be used to check crystal operation.  Sluggish keying and weak output will be readily visible.  Ordinarily, the eye will close instantaneously on keying, and will close more completely on XTAL than on E.C.O.   In purchasing crystals, buy only those made by some reliable manufacturer.

MEISSNER SIGNAL SHIFTER

In using the SIGNAL SHIFTER as an exciter or as a transmitter, it will usually be possible to shift frequency over a moderate range without retuning of the amplifiers or antenna.  This depends upon the characteristics of the amplifiers(s) and antenna used, how-ever, and will vary from one installation to another.  It should be possible to obtain a useful frequency variation without retuning the amplifier(s) or antenna.  Steps taken toward this end will repay the operator in convenience and operating pleasure.  In shifting frequencies, the STAND-BY switch in the driven stage should be left at STAND-BY and the SIGNAL SHIFTER placed ON.  This gives a signal in the receiver without placing the carrier on the air to cause unnecessary interfer-ence.

The SIGNAL SHIFTER is design-ed to increase the operating efficiency and pleasure of the amateur.  It must be used correctly to realize the many advantages which variable frequency control give.  The operator may select interference free channels to operate on, may shift frequency to escape interference, and may shift frequency to call a station on a different frequency.  The good operator never varies his frequency with his carrier on the air.  Swishing across the band is one of the worst offences of the variable frequency oscillator operator.  The good operator will not zero-beat his SIGNAL SHIFTER to the frequency of the station being called.  He will call on a frequency nearby, so that his carrier will not interfere with the called station in case the called station comes back to someone else.

IV.	SERVICE NOTES

The MEISSNER SIGNAL SHIFTER is equipped with a glass 6V6GT/G tube.  If it is ever necessary to replace the oscillator tube, a glass 6V6GT/G tube should be used.  The calibration should be re-checked whenever the tubes are changed and occasionally even when tubes are not replaced.

In case it is necessary to re-align the SIGNAL SHIFTER, as it may be when a new set of tubes is installed, or when the output becomes low, the following adjustments must be made:

Step 1-

a.   	With band switch on the 80 meter          	 band, E.C.O.-XTAL switch on              	E.C.O., tuning 0', and key 
           closed, turn the SIGNAL SHIFTER            to STAND-BY and allow it to 
           warm 	up 30 minutes.  The driven 
           stages should not have plate 
           voltage applied.

b.   	After the SIGNAL SHIFTER has             warmed up, turn the 4-position               switch to ON, and with a good            heterodyne frequency meter or            	crystal controlled frequency 	standard, carefully adjust the 	trimmer condenser C1, Fig. 14, 	with a screw driver, until a zero 	beat note is heard in the receiver 	at 1020 Kc., 2040 Kc., 3060 Kc., or 	4080 Kc.  Be sure you are listening 	to the correct signal!!

This aligns the oscillator grid circuit.

MEISSNER SIGNAL SHIFTER

Step 2-

Turn the band switch to the 10 	meter band and, without touching 	the tuning dial, adjust trimmer C2 	with a screw driver to obtain the 	maximum closing of the tuning

eye.  This aligns the oscillator plate circuit.

Step 3-

Turn the tuning dial to 110, band            switch again to the 10 meter band  	and adjust trimmer C3 with a screw          	driver to obtain maximum output as         	 indicated by the grid current or by 	a neon bulb, etc., in the driven 	stage,  which has its 10 meter grid 	coil inserted. If the SIGNAL 	SHIFTER is being used as a 	transmitter, a neon bulb at the 	antenna tuning circuit can be used 	to indicate alignment of the 807 	plate circuit.  If possible, a  dummy 	antenna should be used to  	prevent interference to other  	stations.

When this alignment procedure is completed, the SIGNAL SHIFTER will be aligned on all bands.  It will probably be necessary to recalibrate the SIGNAL SHIFTER, since the process of  align-ment usually changes the calibration.

COILS:

The following table indicates the catalog number and frequency range of each coil strip.

Note:   The calibration charts in the back of this book were made with the 80-40-20-15 and 10-11 meter bands in the turret in the positions A,B,C,D, and E respectively, and with one special band occupying position F.  For other arrangements of coil strips in the turret, the actual calibration may differ slightly from the published calibration.

CATALOG

NO.    BAND  FREQUENCY RANGE

18-3574   80 Mtr.  3430 to 4080 Kc.

18-3573   40 Mtr.  6860 to 7448 Kc.

18-3572   20 Mtr.  13,720 to 14,700 Kc.

18-3571   15 Mtr.  20,600 to 21,940 Kc.

18-3570   10-11Mtr26,600 to 30,300 Kc.

SPECIAL COILS AVAILABLE

18-3575 160 Mtr.  1715 to 1836 Kc.

(Disaster)

18-3576   75 Mtr.   3773 to 4080 Kc.

(Phone)

18-3577   20 Mtr.

(Phone)

18-3578    6 Mtr.    24.50 to 27.54 Mc.

( Output of SIGNAL SHIFTER

Is on 12 Mtrs.)

Write in your requests to Meissner Mfg. Division, Maguire Industries, Incorporated, for information and prices on special coil sets.

MEISSNER SIGNAL SHIFTER

STANDARD WARRANTY

This SIGNAL SHIFTER was carefully tested, inspected, and

packed in an approved shipping container and left our factory in

perfect condition.  Should any damage occur while in transit, file

claim with carrier at once.

We warrant this instrument to be free from defect in material

and workmanship and to give satisfactory performance under normal

use.  Our obligation under this warranty is limited to making good at

our factory any part or parts thereof (except tubes) which shall, within

90 days from date of purchase, be returned to our factory, carefully

packed and transportation charge prepaid.

This warranty does not apply, if, in our judgement, this set has

been misused, abused, tampered with, or connected otherwise than in

accordance with instructions.  Should this instrument become inoperative

within the warranty period, it should be returned to the factory.

MEISSNER SIGNAL SHIFTER

CALIBRATION SHEETS

80 MTR. BAND		40 MTR. BAND		20 MTR. BAND		15 MTR. BAND

FREQ.KC. 	DIAL		FREQ.KC.	DIAL		FREQ.KC.	DIAL		FREQ.KC.	DIAL

3430		500		6860		500		13720		500		20600		500

3450		474		6900		457		13800		451		20900		386

3500		428		7000		375		13900		403		21000		352

3520		411		7025		355		14000		356		21040		338

3550		385		7050		335		14020		346		21080		325

3600		345		7075		316		14050		332		21120		311

3650		306		7100		296		14100		308		21160		297

3700		269		7125		277		14150		285		21200		283

3750		232		7150		257		14170		275		21240		269

3800		197		7175		237		14200		260		21260		262

3850		164		7200		216		14250		235		21280		254

3870		152		7225		196		14300		212		21320		240

3900		133		7250		176		14350		189		21360		236

3950		101		7260		168		14380		176		21400		212

3980		083		7275		156		14400		167		21440		198

4000		073		7300		137		14500		122		21500		177

4050		041		7400		062		14650		050		21600		142

4080		000		7448		000		14700		000		21940		000

MEISSNER SIGNAL SHIFTER

CALIBRATION SHEETS

6 MTR.BAND

10-11 MTR. BAND		160 MTR. BAND	     75 MTR. PHONE BAND	(12 MTR. OUTPUT)

FREQ.KC. 	DIAL		FREQ.KC.	DIAL		FREQ.KC.	DIAL		FREQ.KC.	DIAL

26600		500		1715		500		3773		500		24500		500

26800		461		1720		470		3800		449		25000		408

27000		433		1745		369		3850		369		25200		375

27185		407		1750		349		3860		354		25300		359

27200		405		1755		330		3870		339		25400		343

27300		391		1760		310		3880		325		25500		327

27400		377		1765		291		3890		310		25600		312

27455		370		1770		272		3900		296		25700		296

28000		298		1775		252		3910		282		25800		280

28300		260		1780		233		3920		267		25900		265

28500		234		1785		214		3930		253		26000		249

28700		209		1790		195		3940		239		26100		234

28900		185		1795		177		3950		223		26200		218

29100		162		1800		159		3960		208		26300		203

29300		138		1805		140		3970		193		26400		187

29500		115		1830		050		3980		177		26500		173

29700		093		1836		000		3990		161		26600		158

29900		069						4000		145		26700		144

30300		000						4050		071		26800		130

4080		000		27000		101

27540		000