Nikon Firmware Update for Coolpix E950, Ver.1.3

1999/12/17

This Software and Firmware is Licensed and Copyright of Nikon Corporation.

System requirements Macintosh users

Mac® OS 7.1 or later

Verified models:

Power Macintosh 7600/133

Power Macintosh 9600

Power Macintosh 7100/80AV

Power Macintosh G3

Power Macintosh 9600

Power Macintosh Performa

Power Book G3

Power Macintosh 8500/132

*The software application does not operate properly with the Power Book 1400 or on Macintosh computers that do not have a serial port fitted such as G3, iMac or G4.

System requirements Windows Users

Microsoft Windows®95

Microsoft Windows®98

Microsoft Windows®NT4.0

About software and firmware

The Firmware Updater Software for the E950 Ver.1.3 is a computer program, which will update the firmware in your COOLPIX 950 (E950). The firmware is a program, which runs inside the camera and controls its operation. By running the Updater Software you will install the new firmware in the camera.

The entire package (Updater software and new firmware for the camera) is supplied in a single file, which is compressed for distribution over the Internet. Before executing a firmware update, you must de-compress the files back to their original format.

- The process of transferring the new firmware from the computer to the camera is sometimes called Uploading.

- The process of updating firmware is sometimes also called upgrading.

This firmware version (1.3) has been introduced to correct bugs, which were present in the previous version, 1.2.

If your camera is version 1.0 or 1.1, it is recommended that you update the firmware in your camera to 1.3 in order to benefit from improved operating performance.

If your firmware is version 1.2 please update to 1.3 as a bug fix.

Version 1.2 and 1.3 improvements.

- Increased general brightness of LCD monitor

- Added function: Auto Sensitivity, increases sensitivity in low light.

- Matrix Auto White Balance

- Auto File Numbering setting in [A]-REC mode (was previously only available in M-Rec)

- Improved brightness of LCD monitor in low-light shooting

Improvements and bug fixes in version 1.3 (in addition to 1.2)

•	Improvement in white balance control in fixed aperture mode

If you select fixed aperture mode in manual white balance mode, the image sometimes becomes green. This problem has been solved.

•	Improved manual focus accuracy

With some cameras, when manual focus is set to infinity, the focus became inaccurate. This has also been overcome.

•	Condition under which Preset white balance data is reset changed

With Ver. 1.2, the set value by preset white balance was reset when fixed aperture mode is set to off. With Ver.1.3, the value is not reset when this mode is turned off.

Restrictions on Usage

This utility will update the firmware in your COOLPIX 950 to version 1.3. It can only be used if the version of the firmware in your COOLPIX 950 is any one of either 1.0, 1.1 or 1.2.

This version of the firmware can only update PAL cameras. It will not convert an NTSC camera to the PAL standard.

It is not suitable for use with any other model of Coolpix camera.

Perform the following procedure to confirm the version of the firmware in your COOLPIX 950.

Confirming the current firmware version

1.	Turn the select dial off.

2.	Hold down the MENU button, and set the select dial to A-REC. Continue holding down the MENU button until the image appears.

3.	The screen will display

E950V*.*

"*.*" represents the version number. If it reads 1.0,1.1 or 1.2, you can use this utility.

If the version number is anything else, such as 1.3, do not use this utility.

4.	Turn the select dial off.

This completes the version confirmation procedure.

Please read the following carefully:

# Warning

If any of the following problems should occur while using the update, it is possible that the COOLPIX 950 will malfunction. Please exercise extreme care during the procedure. Nikon’s authorized service centers can also handle the version upgrade, and we recommend that you make use of their assistance if you are unsure about performing the procedure yourself.

When using the Updater Software, the COOLPIX 950 may cease functioning normally if one of the following occurs:

•	Camera’s power goes off during the upload of firmware.

•	Serial cable becomes disconnected

•	Excessive electrical noise in vicinity (e.g. nearby electrical appliance)

•	The operation of the Updater Software is forcibly terminated

•	Other applications interfere with the Updater Software use during upload

Before launching the Updater Software, please be sure to terminate all other applications.

Caution:

This Firmware Update procedure may not be possible with all makes and models of personal computer.

1.	After the update procedure is finished, the following message may appear:

“Error in writing Firmware”

In this case, click “Close” to close the Updater Software. Disconnect the serial cable from the camera and confirm that you are using the correct version of the firmware.

If the screen displays “E950V1.3”, the update was successfully completed.

If another indication appears, such as “E950V1.2”, it is impossible to update the firmware with your PC. Take your camera to the nearest Nikon service center for updating.

2.	Certain PCs may have compatibility problems with the Updater Software, making correct data transfer with the COOLPIX 950 impossible. The firmware update may suddenly stop and restart. It is possible that the update procedure may even enter a cyclical stop/restart pattern. If this occurs, press “Ctrl”, “Alt” and “Delete” simultaneously.

The Program Compulsory Quit menu appears. Double click “NIKON firmware uploader” to terminate the update procedure.

If this kind of trouble occurs, you cannot update your camera’s firmware with your PC. Take your camera to the nearest Nikon service center for updating.

The following preparation is required to update the firmware of your COOLPIX 950.

Preparation

1.	Power source

•Nikon EH-30 AC Adapter

If not available,...

•Four new alkaline or other high capacity batteries, within three months of date of manufacture

or

•Four fully charged rechargeable batteries (size SUM-3 or AA)

2.	Serial cable

•Nikon SC-EW2 serial cable (Windows)

or

Nikon SC-EW2 serial cable and SC-EM2 conversion cable (Macintosh)

3.	User’s manual

•COOLPIX 950 users manual

NOTE: Please use only authentic Nikon AC adapters and serial cables. Other products may damage the COOLPIX 950.

Update procedure

## Connection of Coolpix to your Computer

1.	Connect the serial cable to the personal computer.

•Windows users — connect the Nikon SC-EW2 cable to the serial communication port.

•Macintosh users — connect the Nikon SC-EM2 conversion cable to the serial communication port. Connect the Nikon SC-EW2 to the SC-EM2 conversion cable.

For details, refer to the COOLPIX 950 user’s manual.

2.	Turn on the COOLPIX 950.

If you have a Nikon EH-30 AC adapter, please connect it to the COOLPIX 950, and plug it into an AC outlet.

If you do not have a Nikon EH-30 AC adapter, please install four new alkaline batteries within three months of manufacture, or four fully charged rechargeable batteries.

3.	If you are using batteries, be sure to set the auto power-off time (on the SETUP menu) to 30 minutes, to prevent the camera power from going off automatically during the upgrade. For details, refer to the user’s manual. This setting is not required if you are using the AC adapter.

5.	Connect the serial cable from the personal computer to the serial port on the COOLPIX 950.

For details on connection, refer to the COOLPIX 950 user’s manual.

6.	Set the COOLPIX 950 select dial to A-REC.

## Running the Update Software

Note: before starting the upgrade procedure you must first decompress the files, which you have downloaded.

In the case of Windows computers, just double-click the file. For Mac users, use a suitable program such as Stuffit( from Aladdin( systems (www.aladdinsys.com) to decompress the file.

When you have successfully decompressed the files you will see two new files. “Uploader” and “Firmware”

1.	If you are using batteries, confirm that the auto power-off time (on the SETUP menu) is set to 30 minutes.

- Launch the Updater Software program.

•Windows users — open Explorer, and double-click on the UPLOADER file.

•Macintosh users — double-click on the UPLOADER icon.

The file called “Firmware” is the actual firmware, which will be transferred to the camera.

3.	When the text “Click ‘Upload’ button to start uploading” appears in the dialog box, click the Upload button. Once you have pressed this button, do not stop or interrupt utility execution while it is in progress, or damage to the COOLPIX 950 may result.

4.	The firmware upgrade process will begin.

This should take about three minutes, but may take as long as ten depending on your specific personal computer and settings.

The following messages will be displayed during execution:

Uploading: The firmware is being transferred to the COOLPIX 950.

Writing Firmware: The firmware is being updated.

Checking Firmware: The new firmware is being verified.

5.	When the text “Writing Firmware is complete” appears in the dialog box, the process is complete. Click Close to close the utility.

6.	Turn the COOLPIX 950 select dial to off.

7.	Disconnect the serial cable.

This completes the firmware update.

Please verify that the COOLPIX 950 firmware version number is 1.3, using the procedure explained earlier. If you changed the auto power-off setting to 30 minutes before the upgrade procedure, you may now return it to the previous setting.

Nikon ETO

Friday, December 17, 1999