Instruction Book

TONE KEYER

Type 102 Model 1

CONTENTS

GENERAL

Purpose

Description

Technical Data

DESCRIPTION OF OPERATION

Audio Oscillator

Keyed Amplifier

Keying Amplifier

DESCRIPTION OF CONTROLS

Output Frequency

Output Level

Keying Wave

INSTALLATION

Mechanical Installation

Electrical Installation

OPERATING INSTRUCTIONS

MAINTENANCE

TUBE VOLTAGE DATA

ELECTRICAL PARTS LIST

SCHEMATIC DIAGRAM

PANEL LAYOUT

BLOCK DIAGRAM

10/9/51 p

|  | 1. | GENERAL |
| --- | --- | --- |

Purpose

The Type 102 Model 1 Tone Keyer is used in communication

systems for remote keying of a radio transmitter, or teleprinter machine.

The intelligence pulses amplitude modulate any one of six audio tones.

The amplitude modulated tones are then impressed on a telephone line,

through a fixed attenuator.

Description:

The Tone Keyer makes use of a high stability RF oscillator

with an adjustment for setting any of the desired frequencies to the

exact value of 425, 765, 1105, 1445, 1785 or 2125 cycles per second.

The oscillator drives a balanced modulated amplifier which is modulated

by a special "mark" and "space" limiter. This keyer is complete with

power supply. An external tone may be introduced instead of the local

audio oscillator.

Technical Data:

Input Signals:

1.	Polar relay contacts shorting to

ground.

2.	Amplitude modulated (keyed) audio

tone 300 – 10,000 cps

3.	DC pulses positive or negative with

respect to ground

Input Level:

a.	Audio:	0 db

b.	DC:	( 10 volts

c.	DC current pulses ( 30 ma polar

Input Impedance:

1.	Tone:		  600 ohms

2.	DC Voltage:	  100,000 ohms, one side

grounded

3.	DC Current:  1800 ohms external load

(one side grounded)

Output Frequencies:

425, 765, 1105, 1445, 1785 or 2125 cps

Output Level:

Mark and Space: 0 db (6 mw)

Technical Data: (cont´d)

Output Impedance:

600 ohms balanced "H" pad

Keying Speed:

0 – 400 dot cycles per second

Controls:

Primary power switch

Output tone selector

Output Level Control

Keying wave selector switch

Power Requirements:

110/220 volts 50/60 cycles

Approximately 75 watts

Connection at rear of chassis

Dimensions:

3-1/2" x 19" x 13-1/2"

Weight:

Approximately 30 pounds

Tube Complement:

1 – 6SJ7			Oscillator

1 – 6V6GT			Keyer Tube

1 – 6SN7			Keyed Amplifier

1 – 6SL7			Keyed Amplifier

1 – 5W4 or 5Y3GT 	Power Supply

1 – 6H6			Tone Rectifier

1 – 6V6GT			Oscillator

Metering:

2-1/2" AC Voltmeter across output

2.

DESCRIPTION OF OPERATION

Audio Oscillator:

The purpose of the audio oscillator is to provide a continu-

ous stable audio frequency to be modulated in accordance with the in-

telligence. The oscillator tubes V1 and V2 operate as a conventional

amplitude stabilized oscillator commonly called  "Wien"  Bridge

oscillator.

Since the behavior of this type of circuit is well known in  the

radio art, no further explanation of its operation is necessary.

Keyed Amplifier:

The Keyed Amplifier (V4) is essentially a modulator stage in

which the continuous audio tone from the audio oscillator is combined

with  the output of  the keying  amplifier to obtain  a tone  keyed on or

off in accordance with the intelligence.

For satisfactory operation in a communication system where

many tones may be impressed on a pair of telephone lines in multiplex,

the tone keyer output must be reasonably free from harmonic distortion

of the output tone and transients generated from the keying should be

of negligible duration and magnitude.

Accordingly, when the keyed amplified is keyed on, it operates

as a push-pull class A amplifier, having a pure sinusoidal output.

Since the keying voltage is impressed in a "push-push" manner,

the transients generated in each half of V4 can be cancelled out effectively

from the balanced output circuit.

Keying Amplifier:

The keying amplifier is effectively a limiter which removes

the effect of input signal amplitude variations from the keyed output

tones.

The actual keyer tube (V5) is connected from the cathode end

of the cathode bias resistor R37 to +B. When the control grid of V5

is at chassis potential, the plate current of V5 is zero; (V5 bias is

beyond cut-off) the output tube V4 then functions as an amplifier.

Keying Amplifier: (cont´d)

When the control grid voltage of V5 is sufficiently positive with

respects to the chassis, the plate current of V5 flowing through R37

causes V4 to be cut-off, thus reducing the output tone level to zero.

The variation of grid potential of V5 is obtained from the

keyer amplifier tube V5 through one of neon coupling tubes V10 or V11.

For the explanation of the operation of V6, consider that S2

has been turned to positive DC polar keying (DC=) and that the input

keying to terminals 2 – 3, is zero. The grid of V5 is then connected to

V10 and current of plate 2 of V6 is cut off by bias voltage appearing

across R47. Since the current through R44 is small, V10 is lit and the

voltage impressed on the grid of  V5  is sufficiently positive to cause

cut-off of the output tube V4.

Applying sufficient positive voltage to grid #1 of V6 causes

the plate current of plate #2 to flow through R44; the increased voltage

drop across R44 extinguishes V10, thus the voltage drop across R41 becomes

zero. Since this cut off V5, V4 passes the tone.

For a negative polar keying voltage, the first section of V8

operates as a phase inverter and plate #5 controls V5 through V11.

For a keyed tone input signal, the tone is rectified by V7

and impressed to the keying circuit as a positive polar signal; the rest

of the keying circuit operates in the manner outlined before.

For polar relay keying, V6 is connected in a usual "flip-flop"

circuit; namely, grid 1 to plate 5, and grid 4 to plate 2.  Shorting

first one and then the other, grid to ground, causes keying as outlined

before.

3.

DESCRIPTION OF CONTROLS

Output Frequency:

The output frequency control inserts the proper R-C combina-

tion  in  the  audio  oscillator  circuit  to  provide  the  specified  fixed

output frequencies.

Output Level:

The output level control is a balanced "L" pad by which the

output level to the telephone line can be varied while keeping the

load on the amplifier V4 nearly constant.

Keying Wave:

By the keying wave control, the connection of the keying

amplifier can be altered to suit the type of keying input desired.

4.

INSTALLATION

Mechanical Installation:

The Tone Keyer may be installed in any convenient location

so that access is provided to the rear of the equipment for periodic

maintenance checks.

Electrical Installation:

Before connecting the electrical lines to the Tone Keyer,

it is desirable to check if the source of primary power is correct,

the nature of the keying input and the load on the equipment.

The keying lines to the equipment should be twisted shielded

pair, only one type of keying line should be connected to the equipment

at any time to prevent one keying signal from interfering with another.

If  it  is  necessary  to  alternate frequently between various types  of

keying, it is usually best to bring out all the keying connections to

a patch panel, so that quick changes in keying connections can be made.

If the keying is obtained from a current source such as used

for teleprinting (60 ma in 1800 ohms) an 1800 ohms resistance of suffi-

cient power rating should be bridged across the DC keying terminals

(2, 3 on E1). Similarly, for other keying devices requiring output

leads less than 500K ohms, a suitable resistance should be bridged

across the DC keying terminals, to make the effective load on the keying

device the desired value.

When keying by a polar sending head, no external resistance

must be bridged across terminal 1, 2 and 3 on terminal board E1.

If it is desired that an external tone be keyed, remove the

connecting link from the "external tone" terminal board (E2) and connect

the source of external tone from the center terminal to ground. The external

generator impedance can be any value from 200 ohms to 100,000 ohms.

The external tone level should be set as high as possible without over-

loading the output amplifier V4; the desired output level then should be

set by the "Output Level" control.

If the local audio oscillator is to be used, the various out-

put frequencies should be checked against a suitable standard of audio

frequencies; objectionable discrepancies should be corrected by the proper

frequency trimmer at the rear of the Tone Keyer. For this test no external

connections should be made to any part of the audio oscillator. The check

Electrical Installation: (cont´d)

should be made on tone obtained at the output of monitor terminals.

The Tone may be turned on by setting the "Keying Wave" switch to

"Relay" (no external connections to relay terminals 1 and 3).

If aural monitoring is desired, the Tone Keyer "Monitor"

terminal may be connected to a loud speaker having about 1000 ohms

balanced impedance. (For 600 ohms speaker, insert a 6 db pad, having

1000 ohms input and 600 ohms output impedances). A front panel jack

for earphone monitoring is also provided.

The output of the keyed amplifier is connected through a

fixed attenuator providing about 20 db attenuation for a 600 ohm ex-

ternal load. The fixed attenuator effectively isolates the level

meter and keyed amplifier V4 from other signals which may be simultane-

ously impressed across the same pair of telephone lines. With the fixed

attenuator, the maximum output level of the Tone Keyer is approximately

0 db (6 mw).

5.

OPERATING INSTRUCTIONS

A.   Polar Positive DC Keying:

Set "Output Frequency" to the desired value, set " Keying

Wave " to " DC + " and set output level to desired value. Note that

output level is best set with a steady tone on, since during keying

the level indicated by the output level meter is less than the tone

level; the output meter will also fluctuate when the keying is rela-

tively slow.

B.   Polar Negative DC Keying:

Proceed as in "A", but set "Keying Wave" to "DC –".

C.   Reception of CW Signals by Diversity Receivers:

For this type of service, usually the second detectors of

all diversity receivers are connected to the same diode load, and no

receiver BFO is used. Connect the common diode load directly to the

DC keying terminals 2 and 3 on terminal board E1. Set "Keying Wave"

to "DC +" or "DC –" according to the polarity of the receiver output

pulse. Set output frequency and level as in "A".

After the receiver is tuned accurately to the signal, lower

the receiver RF gain control (or gain controls when receiver AVC circuits

are independent) until satisfactory keying occurs.   ( If the RF gain

control is set too high, the noise output of the receiver may be high

enough to key the Tone Keyer.)

If the quality of the received signal is very poor, it may

be necessary to install a fixed bias, which  opposes the receiver out-

put, in the input lead to alter the quality of keying signal to better

advantage.

D.   Reception of CW Signals by Single Receiver:

For this type of service, the receiver output is usually

an on-off audio tone obtained by beating the received signal with the

receiver BFO.

D.   Reception of CW Signals by Single Receiver: (cont´d)

Connect the receiver output to the keyed tone input (Terminals

4 and 5 on terminal board E1). After the receiver is accurately tuned

to the signal, adjust the receiver output tone to about 2000 cps and

10-15 volt level. Set the "Keying Wave" control to "Tone", then pro-

ceed as in "A".

In some instances, better results are obtained if the receiver

RF gain control is set for an intermediate value before adjusting the

receiver output level.

E.   Keying by Polar Relay:

The most common source of this type of keying is a polar sending

head. To operate, connect the armature to ground (terminal 2) and the

"mark" and "space" contact terminals 1 and 3. When the relay is in

"mark" position, tone is on.

Set "Keying Wave" control to "Relay" and proceed as in "A".

It should be pointed out that the leakage resistance across the

telephone lines connected to the keying terminals must be high, other-

wise the keying circuit will not operate reliably.

6.

MAINTENANCE

To obtain long and trouble-free operation from the Tone

Keyer, it is recommended that a few routine checks be performed at

reasonable intervals.

Check all tubes periodically for emission and mutual con-

ductance. When any tube shows a mutual conductance and emission less

than the minimum acceptable for its type, it should be replaced.

The output tone frequencies should be compared to a stand-

ard approximately once a month, and deviations rectified.

Similarly, the keyed amplifier balance should be checked

monthly. This test can be easily performed in the following manner:

Connect an oscilloscope across the monitoring terminals.

Set the "Keying Wave" to "DC –". Connect a 60 cps 50 - 100 volt sinus-

oidal keying voltage to the DC keying terminals.

Disable the local audio oscillator by holding the "output

frequency" switch between detents. Adjust the balancing control R27

(at the rear) for minimum transient output indicated by the oscilloscope.

If a reasonably good balance is unobtainable, change V4.

* * * * * * * * * * * *

TABLE OF TUBE SOCKET VOLTAGES

DATE:    July 27, 1950      EQUIPMENT:	    Tone Keyer    TYPE:    102   MODEL:   1

| Symbol | Function | Type | Pins | Volts | Pins | Volts | Pins | Volts | Pins | Volts | Pins | Volts | Pins | Volts |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| V1 | Audio Oscillator | 6SJ7 | 1-3 | 1.15 | 1-4 | 0 | 1-5 | 1.15 | 1-6 | 55 | 1-8 | 158 | 2-7 | AC 6.2 |
| V2 | Audio Oscillator | 6V6 | 1-3 | 195 | 1-4 | 175 | 1-5 | 0 | 1-8 | 12 | 2-7 | AC 6.2 |
| V4 | Output Amplifier | 6SN7 | G-1 | 37.5 | G-2 | 275 | G-3 | 46 | G-4 | 32.5 | G-5 | 278 | G-6 | 46 |
| V5 | Keyer Tube | 6V6 | 1-3 | 285 | 1-4 | 285 | 1-5 | 0 | 1-8 | 45 | 2-7 | AC 6.2 |
| V6 | Keyer Amplifier | 6SL7 | G-1 | 0 | G-2 | 100 | G-3 | 6.75 | G-4 | * 6 | G-5 | 30 | G-6 | 6.3 |
| V7 | Tone Rectifier | 6H6 | 1-3 | 0 | 1-4 | .25 | 1-5 | 0 | 1-8 | .25 | 2-7 | AC 6.2 |
| V8 | Power Rectifier | 5W4 or 5Y3GT | G-4 | AC 300 | G-6 | AC 300 | 2-8 | AC 5 |

NOTE:     All voltages measured with a 20,000 ohms/volt

DC Voltmeter

CONTROL SETTINGS

| Control | Function | Setting |
| --- | --- | --- |
| ..REMARKS: * 50 volt Range |
| S5 | Freq. Sel. | 2125 cps. |
| R53 | Output Level | Maximum |
| S2 | Keying Switch | Relay |

8.

ELECTRICAL PARTS LIST

Sym-bol

|  | Function | Description | Mfr. | Part. No. |
| --- | --- | --- | --- | --- |
| C1 | Series frequency determin-ing capacitor |

120 mmfd ( 2( 500 volt

| Silver mica | SAN | KR1312 |
| --- | --- | --- |
| C2 | Shunt frequency determin-ing capacitor |

110 mmfd ( 2( 500 volt

| Silver mica | SAN | KR1311 |
| --- | --- | --- |
| C3 | Audio oscillator coupling capacitor |

0.1 mfd ( 10( 400 volt

| Paper capacitor | SAN | 300401 |
| --- | --- | --- |
| C4 | Audio oscillator plate bypass capacitor |

.1 - .1 mfd ( 20( 600 volt

paper dual bathtub, side

| terminal. Part of C12 | SAN | 5006-.1 x 2 |
| --- | --- | --- |
| C5 | Audio oscillator plate bypass capacitor |

1 mfd ( 20( 600 volt

paper bathtub capacitor,

| side terminal. | SAN | 5006-1 |
| --- | --- | --- |
| C6 | Audio oscillator feedback capacitor |

2 mfd ( 20( 600 volt

paper bathtub capacitor,

| side terminal. | SAN | 5006-2 |
| --- | --- | --- |
| C7 | Power supply filter | 4 mfd ( 20( 600 volt dykanol | CDC | TLA-6040 |
| C9 | Output amp. grid coupling |

0.01 mfd ( 20( 400 volt

| paper capacitor | SAN | 300411 |
| --- | --- | --- |
| C10 | Output amp. grid coupling | Same as C9 |
| C12 | Output amp. plate bypass | Same as and part of C4 |
| C13 | Tone rectifier filter | 500 mfd ( 20( 500 volt mica | SAN | E1350 |
| C16 | Power supply filter cap. | 4 mfd 600 volt dykanol | CDC | TLA-6040 |
| C17 | Same as C16 | Same as C16 |
| C18 | Audio osc. Trimmer cap. | 7-45 mmfd ceramic trimmer | ERC | TS2A |
| C19 | Same as C18 | Same as C18 |
| C20 | Same as C18 | Same as C18 |

Sym-bol

|  | Function | Description | Mfr. | Part. No. |
| --- | --- | --- | --- | --- |
| C21 | Same as C18 | Same as C18 |
| C22 | Same as C18 | Same as C18 |
| C23 | Same as C18 | Same as C18 |
| E1 | Keyer Input terminal | 5 terminal screw post | ICA | 2405 |
| E2 | External tone input | 3 terminal screw post | ICA | 2414 |
| E3 | Tone Output | Same as E2 |
| E5 | Monitoring bridging 2 | 2 terminal screw post | ICA | 2420 |
| F1 | Primary power fuse | 1/2 amp. Slo-Blo glass fuse | LFU | 3AG |
| I1 | Primary power pilot light |

Pilot light assembly with

| 6-8 volt bayonet base lamp | DLA | 67BD |
| --- | --- | --- |
| J1 | Primary power connector | 2 pole male chassis type connector | HUN | 6808 |
| J2 | Output tone monitor jack | Open circuit telephone jack Insulated | BUD | 232 |
| L1 | Power supply filter choke | 10 henries 250 ohms 75 ma | NRC | 112 |
| L2 | Same as L1 | Same as L1 |
| M1 | Output level meter |

0-20 V. rectifier type AC  meter (1000 ohms per volt)

in 2-1/2" square bakelite

| case. | WET | 506 |
| --- | --- | --- |
| P1 | Primary power connector | 2 pole female cable connector | HUB | 7257 |
| P2 | Same as P1 | 2 pole male cable connector | HUB | 9972 |
| R1 | Audio osc. series freq. determining resistor | 2.07 megohm ( 1( precision resistor 1/2 watt | CCC | X-1/2 |
| R2 | Same as R1 | 1.15 megohm ( 1( precision resistor 1/2 watt | CCC | X-1/2 |
| R3 | Same as R1 | 793K ohms ( 1( precision resistor 1/2 watt | CCC | X-1/2 |

Sym-bol

|  | Function | Description | Mfr. | Part. No. |
| --- | --- | --- | --- | --- |
| R4 | Audio osc. series freq. determining resistor | 610K ohms ( 1( precision resistor 1/2 watt | CCC | X-1/2 |
| R5 | Same as R4 | 492K ohms ( 1( precision resistor 1/2 watt | CCC | X-1/2 |
| R6 | Same as R4 | 414K ohms ( 1( precision resistor 1/2 watt | CCC | X-1/2 |
| R7 | Shunt freq. determining resistor | 2.07 megohms ( 1( precision resistor 1/2 watt | CCC | X-1/2 |
| R8 | Same as R7 | 1.15 megohms ( 1( precision resistor 1/2 watt | CCC | X-1/2 |
| R9 | Same as R7 | 793K ohms ( 1( precision resistor 1/2 watt | CCC | X-1/2 |
| R10 | Same as R7 | 610K ohms ( 1( precision resistor 1/2 watt | CCC | X-1/2 |
| R11 | Same as R7 | 492K ohms ( 1( precision resistor 1/2 watt | CCC | X-1/2 |
| R12 | Same as R7 | 414K ohms ( 1( precision resistor 1/2 watt | CCC | X-1/2 |
| R14 | Shunt negative feedback resistor | 6 watt 115 volt incandescent lamp with candelabra base | GEC | 68-6 |
| R15 | Same as R14 | Same as R14 |
| R16 | Audio oscillator screen bleeder | 33K ohms ( 5( 1/2 watt | ALB | EB |
| R17 | Same as R16 | 100K ohms ( 10( 1 watt | ALB | GB |
| R18 | Audio oscillator plate load | 51K ohms ( 5( 1/2 watt | ALB | EB |
| R19 | Audio oscillator plate filter | 10K ohms ( 10( 1/2 watt | ALB | EB |
| R20 | Audio oscillator grid res. | 510K ohms ( 5( 1/2 watt | ALB | EB |
| R21 | Audio oscillator cathode resistor | 470 ohms ( 10( 1 watt | ALB | GB |
| R22 | Audio oscillator screen bleeder | 51K ohms ( 5( 2 watt | ALB | HB |

Sym-bol

|  | Function | Description | Mfr. | Part. No. |
| --- | --- | --- | --- | --- |
| R23 | Audio oscillator screen bleeder | 20K ohms ( 5( 2 watt | ALB | HB |
| R24 | Audio oscillator plate load | 5000 ohms 5 watts wirewound potentiometer, screwdriver adjustment | MAL | M5MP |
| R25 | Audio oscillator plate filter | 1000 ohms ( 10( 2 watt | ALB | HB |
| R26 | Keyer grid leak | 470K ohms ( 10( 1/2 watt | ALB | EB |
| R27 | Keyer amplifier balance control | 500 ohms wirewound miniatu-re potentiometer with screw-driver slot on shaft | IRC |

034

| W-500 |
| --- |
| R28 | Audio oscillator negative feedback control | 3000 ohms wirewound minia-ture potentiometer for screw-driver adjustment | MAL | M3MP |
| R29 | Output Pad | 1000 ohms( 10( 1/2 watt | ALB | EB |
| R31 | Keyed amplifier bias res. | 91K ohms ( 5( 2 watt | ALB | HB |
| R32 | Tone Transformer Load | 100K ohms ( 10( 1/2 watt | ALB | EB |
| R33 | Output Pad | 1000 ohms ( 10( 1/2 watt | ALB | EB |
| R34 | Output amp. grid res. | 100K ohms ( 10( 1/2 watt | ALB | EB |
| R35 | Same as R34 | Same as R34 |
| R36 | Keyed amp. bias resistor | 15K ohms ( 10( 1/2 watt | ALB | EB |
| R37 | Output amp. cathode res. | 5100 ohms ( 5( 2 watt | ALB | HB |
| R38 | Output amp. plate filter | 1000 ohms ( 10( 1 watt | ALB | GB |
| R39 | Keyer amp. plate bleeder | 120K ohms ( 10( 1/2 watt | ALB | EB |
| R40 | Same as R39 | 100K ohms ( 10( 1/2 watt | ALB | EB |
| R41 | Keyer tube grid resistor | 820 ohms ( 10( 1/2 watt | ALB | EB |
| R42 | Same as R41 | Same as R41 |

Sym-bol

|  | Function | Description | Mfr. | Part. No. |
| --- | --- | --- | --- | --- |
| R44 | Keyer amp. plate load | 150K ohms ( 10( 1/2 watt | ALB | EB |
| R45 | Same as R44 | Same as R44 |
| R47 | Keyer amp. cathode | 1000 ohms ( 10( 1/2 watt | ALB | EB |
| R48 | Keyer amp. grid current limiter | 470K ohms ( 10( 1/2 watt | ALB | EB |
| R49 | Keyer amp. grid resistor | 470K ohms ( 10( 1/2 watt | ALB | EB |
| R50 | Negative feedback resistor | 3000 ohms ( 5( 1/2 watt | ALB | EB |
| R51 | Keyer amp. bias | 50K ohms ( 10( 10 watts | SPR | 10KT |
| R52 | Keyer amp. bias | 1000 ohms ( 10( 1/2 watt | ALB | EB |
| R53 | Output level control | 600 ohms balanced L pad (T pad connected for this operat.) | CLA | T-pad CIT 200 ohms |
| R54 | Keyer amp. grid current limiter | 470K ohms ( 10( 1/2 watt | ALB | EB |
| R55 | Audio oscillator cathode resistor | 240 ohms ( 5( 1/2 watt | ALB | EB |
| R56 | Keyer amp. bias | 50K ohms ( 10( 10 watts | SPR | 10KT |
| R57 | Keyer amp. grid res. | 240K ohms ( 5( 1/2 watt | ALB | EB |
| S1 | Main power switch | DPST toggle 115 volt 3 amp. | AHH | 81024 |
| S2 | Keying selector switch | 3 circuit 4 position rotary | MAL | 1325L |
| S5 | Frequency selector wxitch | 2 pole 6 position rotary | MAL | 3226J |
| T1 | Power supply transformer |

Primary: 115 volts 50/60 cps

Sec. #1: 295-0-295 volt 50 ma.

Sec. #2: 6.3 V. 2 A.

| Sec. #3: 5 V. 2 A. | NRC | 109 |
| --- | --- | --- |
| T2 | Output Transformer |

P P Plate to balanced line,

20K ohms to 600 ohms,

| primary to carry 8 ma DC | NRC | 111 |
| --- | --- | --- |
| T3 | Keyed tone input transformer |

Balanced line to full wave

diode 600 to 100K ohms:

| Secondary center tapped | NRC | 110 |
| --- | --- | --- |

Sym-bol

|  | Function | Description | Mfr. | Part. No. |
| --- | --- | --- | --- | --- |
| V1 | Audio oscillator | Standard | GEC | 6SJ7 |
| V2 | Audio oscillator | Standard | GEC | 6V6 |
| V4 | Output tube | Standard | GEC | 6SN7 |
| V5 | Keyer tube | Standard | GEC | 6V6 |
| V6 | Keyer amplifier | Standard | GEC | 6SL7 |
| V7 | Tone rectifier | Standard | GEC | 6H6 |
| V8 | Rectifier | Standard | GEC | 5W4 or 5Y3GT |
| V10 | Keyer coupling tube |

1/28 watt neon lamp,

| bayonet base | GEC | NE51 |
| --- | --- | --- |
| V11 | Same as V10 | Same as V10 |
| X1 | Socket for V1 | Octal with ground lugs | AMP | 15-8 |
| X2 | Socket for V2 | Same as X1 |
| X4 | Socket for V4 | Same as X1 |
| X5 | Socket for V5 | Same as X1 |
| X6 | Socket for V6 | Same as X1 |
| X7 | Socket for V7 | Same as X1 |
| X8 | Socket for V8 | Same as X1 |
| X10 | Socket for V10 | Bayonet base pilot light socket | DLA | 705 |
| X11 | Socket for V11 | Same as X10 |
| X14 | Socket for R14 | Candelabra size lamp socket | DLA | 615 |
| X15 | Socket for R15 | Same as X14 |
| X16 | Primary power fuse holder |

Extractor type fuse holder

| For type 3AG fuse | LFU | 342001 |
| --- | --- | --- |

MANUFACTURERS' DESIGNATION SYMBOLS

AHH	. . . . . . . . . . . . . . . . . . . . . . . Arrow-Hart & Hegeman Co.

ALB	. . . . . . . . . . . . . . . . . . . . . . . Allen Bradley Corp.

AMP	. . . . . . . . . . . . . . . . . . . . . . . American Phenolic Corp.

BUD	. . . . . . . . . . . . . . . . . . . . . . . Bud Radio, Incorporated

CCC	. . . . . . . . . . . . . . . . . . . . . . . Continental Carbon Company

CDC	. . . . . . . . . . . . . . . . . . . . . . . Cornell-Dubilier Electric Corp.

CLA	. . . . . . . . . . . . . . . . . . . . . . . Clarostat Manufacturing Company

DRA	. . . . . . . . . . . . . . . . . . . . . . . Drake Manufacturing Company

DLA	. . . . . . . . . . . . . . . . . . . . . . . Dial Light Corp. Of America

ERC	. . . . . . . . . . . . . . . . . . . . . . . Erie Resistor Corporation

GEC	. . . . . . . . . . . . . . . . . . . . . . . General Electric Company

HUB	. . . . . . . . . . . . . . . . . . . . . . . Harvey Hubbell, Inc.

ICA	. . . . . . . . . . . . . . . . . . . . . . . Insuline Corporation of America

IRC	. . . . . . . . . . . . . . . . . . . . . . . International Resistance Co.

LFU	. . . . . . . . . . . . . . . . . . . . . . . Littlefuse, Incorporated

MAL	. . . . . . . . . . . . . . . . . . . . . . . P.R. Mallory & Co., Inc.

NRC	. . . . . . . . . . . . . . . . . . . . . . . Northern Radio Company, Inc.

SAN	. . . . . . . . . . . . . . . . . . . . . . . Sangamo Electric Corp.

SPR	. . . . . . . . . . . . . . . . . . . . . . . Sprague Products Co.

WEI	. . . . . . . . . . . . . . . . . . . . . . . Western Electrical Instrument Co.

************************