# Instructions for cleaning optics

1.	Turn LD player upside down

2.	Remove bottom cover. (7 screws)

3.	Remove 5 green screws from bracket that hold the VSOP board.  (this will allow you to lift the VSOP board up and out of the way)

4.	Remove black plastic cover.  (2 screws and black electrical tape)

5.	Using freon TF and lens cleaning tissue, clean the following:

End of laser tube

#1 and #2 fixed mirrors

Square prism

¼” wave plate

Tracking and tangential mirrors

(CAUTION:  Light pressure should be used on the tracking and tangential mirrors)

6.	Replace slider cover. (new tape should be used)

7.	Replace bottom cover.

(CAUTION:  Do not clean grating!)

(SEE PAGE 2 AND 3 FOR DIAGRAMS)