| RCI-6300F HP RCI-6300F TB |  | TABLE OF CONTENTS |
| --- | --- | --- |

|  | PAGE |
| --- | --- |
| CHAPTER 1 |  |
| SPECIFICATIONS |  |
| 1.0 | General . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 2 |
| 1.1 | Transmitter . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 2 |
| 1.2 | Receiver . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 2 |
| CHAPTER 2 |  |
| OPERATION |  |
| 2.0 | Introduction . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 3 |
| 2.1 | Control & Connections . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 3 |
| 2.1.1 | Front Panel . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 3 |
| 2.1.2 | Rear Panel . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 6 |
| 2.1.3 | Frequency Chart . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 7 |
| 2.2 | Microphone . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 8 |
| 2.3 | Operation . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 8 |
| 2.3.1 | Procedure To Receive . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 8 |
| 2.3.2 | Procedure To Transmit . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 8 |
| 2.4 | Alternate Microphones And Installation . . . . . . . . . . . . . . . . . . . . . . . . | 9 |
| CHAPTER 3 |  |
| CIRCUIT DESCRIPTION |  |
| 3.0 | Introduction . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 10 |
| 3.1 | PLL Circuit . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 10 |
| 3.2 | Receiver Circuit . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 10 |
| 3.3 | Transmitter Modulation Circuit . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 10 |
| 3.4 | Transmitter Amplifier Circuit . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 10 |
| CHAPTER 4 |  |
| ALIGNMENT |  |
| 4.0 | Required Test Equipment . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 15 |
| 4.1 | Alignment Procedures . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 15 |
| 4.1.1 | PLL Alignment . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 15 |
| 4.1.2 | Transmitter Alignment . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 16 |
| 4.1.3 | Receiver Alignment . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 17 |
| CHAPTER 5 |  |
| MAINTENANCE |  |
| 5.0 | Precautions . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 20 |
| 5.1 | Periodic Inspection . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 20 |
| 5.2 | Fuse Replacement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 20 |
| CHAPTER 6 |  |
| DIAGRAMS AND PART LIST |  |
| 6.0 | PCB Layout & Part List . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 21 |
| RCI-6300F HP RCI-6300F TB |  | CHAPTER 1 SPECIFICATIONS |

| 1.0 GENERAL |  |
| --- | --- |
| Model | RCI-6300F HP / RCI-6300F TB |
| Frequency Range | 28.245 - 29.655MHz. |
| Emission Modes | AM/FM (A3/F3) |
| Frequency Control | Phase Lock Loop (PLL) synthesizer. |
| Frequency Tolerance | ( 0.005 %. |
| Frequency Stability | ( 0.001 %. |
| Operating Temperature Range | -20(C to +50(C. |
| Microphone | Dynamic PTT, 500 ( |
| Input Voltage | 13.8V DC nominal (15%. |
| Current Drain: Transmit (AM full mod.) | RCI-6300F HP < 5A; RCI-6300F TB < 15A. |
| Current Drain: Receiver (Squelched) | ( 0.25A. |
| (Max. audio output) | < 0.5A. |
| Antenna Connector | UHF, SO239. |
| Dimensions (RCI-6300F HP) | 2-3/8”(H) x 7-7/8”(W) x 10-3/4”(D). |
| Dimensions (RCI-6300F TB) | 3-7/8”(H) x 7-7/8”(W) x 9-1/4”(D). |
| Weight | 5 lb. (RCI-6300F HP) ; 7lb 6oz (RCI-6300F TB) |
| 1.1 TRANSMITTER |  |
| RF Power Output (AM/FM) (DC Carrier Power) | 10 W (RCI-6300F HP) 50W (RCI-6300F TB) |
| RF Transmit Modes | AM/FM. |
| AM Modulation | High and low level Class B, Amplitude Modulation. |
| Spurious Emissions | -50 dB. |
| Audio Frequency Response | 300 to 2500 Hz |
| Antenna Impedance | 50 Ohms. |
| Output Indicators | Meter shows relative RF output power, receive signal and SWR. Transmit LED glows red when transmitter is in operation. |
| 1.2 RECEIVER |  |
| Sensitivity For 10dB S/N (AM) | < 0.5 (V. |
| Sensitivity For 12dB S/N (FM) | < 0.25 (V. |
| IF Frequency | AM: 10.695 MHz 1st IF, 455 KHz 2nd IF. |
| Image Rejection | > 50 dB. |
| Adjacent Channel Selectivity | > -55 dB. |
| RF Gain Control | 45 dB adjustable for optimum signal reception. |
| Automatic Gain Control (AGC) Figure Of Merit | 100 mV for 10 dB Change in Audio Output. |
| Squelch | Adjustable; threshold less than 0.5 (V. |
| Noise Blanker | RF type. |
| Audio Output Power | 2.5W @ 10% THD. |
| Audio Frequency Response | 300 to 2500 Hz. |
| Built-in Speaker | 8 Ohms, 4 Watts. |
| External Speaker (Not Supplied) | 8 Ohms; 4 Watts. |

(SPECIFICATIONS SUBJECT TO CHANGE WITHOUT NOTICE)

| RCI-6300F HP RCI-6300F TB |  | CHAPTER 2 OPERATION |
| --- | --- | --- |

Figure 2-1 Front Panel

2.0 INTRODUCTION

This section explains the basic operating procedures for the RANGER RCI-6300F HP / RCI-6300F TB mobile transceiver.

2.1 CONTROL AND CONNECTIONS

2.1.1 FRONT PANEL

Refer to the above Figure 2-1 for the location of the following controls.

1. ON/OFF VOLUME CONTROL

This knob controls the volume and the power to the radio. To turn the radio on, rotate the knob clockwise. Turning the knob further will increase the volume of the receiver.

2. SQUELCH CONTROL

This switch is used to eliminate background noise being heard through the receiver which can be disturbing when no transmissions are being received. To use this feature, turn the switch fully counterclockwise and then turn clockwise slowly until the background noise is just eliminated. Further clockwise rotation will increase the threshold level which a signal must overcome in order to be heard. Only strong signals will be heard at a maximum clockwise setting.

3. MIC GAIN CONTROL

Adjusts the microphone gain in the transmit and PA modes. This controls the gain to the extent that full talk power is available several inches away from the microphone. In the Public Address (PA) mode, the control functions as the volume control.

4. RF GAIN CONTROL

This control is used to reduce the gain of the RF amplifier under strong signal conditions.

5. MODE SWITCH

This control allows you to select one of the following operating modes: PA/FM/AM.

In the PA position, the radio acts as a public address amplifier. Your voice will come out of the speaker that is plugged into the PA. SP. jack on the rear panel. The radio does not operate when you are in the PA mode. In the FM/AM position, the PA function is disabled and the unit will transmit and receive on the speaker that is connected to the radio.

6. FR. POOL SELECTOR

This switch is used to select the frequency range of operation (1 - 6).

7. ECHO SWITCH

This control is used for echo effect.

8. TIME CONTROL

This time control is used to control the intervals of the echo sound.

9. TALKBACK CONTROL

Adjust this knob for desired volume of Talkback. This is used to monitor your own voice. For example, you could use this feature to compare different microphones.

10. RF POWER CONTROL

This control allows the user to adjust RF power output.

11. CHANNEL SELECTOR

This control is used to select a desired transmit and receive channel.

12. FRONT PANEL METER

The Front Panel Meter allows the user to monitor signal strength, RF output power and SWR level.

13. TX/RX LED

The red LED indicates the unit is in the transmit mode. The green LED indicates the unit is in the receive mode.

14. FREQUENCY COUNTER

This display indicates the frequency of operation.

15. DIM/BRT SWITCH

This switch controls the level of brightness for the meter lamp, frequency display and the channel display. Press this switch (DIM) for the meter lamp, frequency display and the channel display to be dimly lighted. Depress this switch (BRT) for brighter effects.

16. HI/LO SWITCH

This switch selects received audio tone quality. In LO position, bass is increased and in HI position, treble is increased.

17. S-RF/SWR SWITCH

This is a two-function switch. In the S-RF position, the meter will indicate the strength of the signal being received, as well as the relative RF output of transmission. To use the meter to measure the standing wave ratio, turn the switch to the SWR position. The SWR function is self-calibrating.

18. NB/ANL/OFF SWITCH

In the NB/ANL position, the RF Noise Blanker and the Automatic Noise Limiter in the audio circuits are also activated. The Noise Blanker is very effective in eliminating repetitive impulse noise such as ignition interference.

19. R.B./OFF SWITCH

In the Roger Beep position, the radio transmits an audio tone at the end of your transmission to indicate that transmission has ended. As a courtesy to others, use the Roger Beep only when necessary.

20. +10KHz/OFF SWITCH

When the switch is pressed the frequency is shifted 10KHz up.

21. CHANNEL DISPLAY

The channel display indicates the current selected channel.

2.1.2 REAR PANEL

Figure 2-2 represents the location of the following connections:

Figure 2-2 Rear Panel

1. ANTENNA

This jack accepts 50 ohms coaxial cable with a PL- 259 type plug.

2. POWER

This connector accepts 13.8V DC power cable with built-in fuse. The power cord provided with the radio has a black and red wire. The black goes to negative and the red goes to positive.

3. PA. SP.

This jack is for PA operation. Before operating, you must first connect a PA speaker (8 ohms, 4W) to this jack.

4. EXT. SP.

This jack accepts 4 to 8 ohms, 4 watts external speaker. When the external speaker is connected to this jack, the built-in speaker will be disabled.

2.1.3 FREQUENCY CHART

|  | FR. POOL |
| --- | --- |
| CHANNEL | 1 (MHz) | 2 (MHz) | 3 (MHz) | 4 (MHz) | 5 (MHz) | 6 (MHz) |
| 1 | 28.245 | 28.695 | 29.145 | 28.315 | 28.765 | 29.215 |
| 2 | 28.255 | 28.705 | 29.155 | 28.325 | 28.775 | 29.225 |
| 3 | 28.265 | 28.715 | 29.165 | 28.335 | 28.785 | 29.235 |
| 4 | 28.285 | 28.735 | 29.185 | 28.355 | 28.805 | 29.255 |
| 5 | 28.295 | 28.745 | 29.195 | 28.365 | 28.815 | 29.265 |
| 6 | 28.305 | 28.755 | 29.205 | 28.375 | 28.825 | 29.275 |
| 7 | 28.315 | 28.765 | 29.215 | 28.385 | 28.835 | 29.285 |
| 8 | 28.335 | 28.785 | 29.235 | 28.405 | 28.855 | 29.305 |
| 9 | 28.345 | 28.795 | 29.245 | 28.415 | 28.865 | 29.315 |
| 10 | 28.355 | 28.805 | 29.255 | 28.425 | 28.875 | 29.325 |
| 11 | 28.365 | 28.815 | 29.265 | 28.435 | 28.885 | 29.335 |
| 12 | 28.385 | 28.835 | 29.285 | 28.455 | 28.905 | 29.355 |
| 13 | 28.395 | 28.845 | 29.295 | 28.465 | 28.915 | 29.365 |
| 14 | 28.405 | 28.855 | 29.305 | 28.475 | 28.925 | 29.375 |
| 15 | 28.415 | 28.865 | 29.315 | 28.485 | 28.935 | 29.385 |
| 16 | 28.435 | 28.885 | 29.335 | 28.505 | 28.955 | 29.405 |
| 17 | 28.445 | 28.895 | 29.345 | 28.515 | 28.965 | 29.415 |
| 18 | 28.455 | 28.905 | 29.355 | 28.525 | 28.975 | 29.425 |
| 19 | 28.465 | 28.915 | 29.365 | 28.535 | 28.985 | 29.435 |
| 20 | 28.485 | 28.935 | 29.385 | 28.555 | 29.005 | 29.445 |
| 21 | 28.495 | 28.945 | 29.395 | 28.565 | 29.015 | 29.465 |
| 22 | 28.505 | 28.955 | 29.405 | 28.575 | 29.025 | 29.475 |
| 23 | 28.535 | 28.985 | 29.435 | 28.605 | 29.005 | 29.505 |
| 24 | 28.515 | 28.965 | 29.415 | 28.585 | 29.035 | 29.485 |
| 25 | 28.525 | 28.975 | 29.425 | 28.595 | 29.045 | 29.495 |
| 26 | 28.545 | 28.995 | 29.445 | 28.615 | 29.065 | 29.495 |
| 27 | 28.555 | 29.005 | 29.455 | 28.625 | 29.075 | 29.515 |
| 28 | 28.565 | 29.015 | 29.465 | 28.635 | 29.085 | 29.525 |
| 29 | 28.575 | 29.025 | 29.475 | 28.645 | 29.095 | 29.535 |
| 30 | 28.585 | 29.035 | 29.485 | 28.655 | 29.105 | 29.545 |
| 31 | 28.595 | 29.045 | 29.495 | 28.665 | 29.115 | 29.555 |
| 32 | 28.605 | 29.055 | 29.505 | 28.675 | 29.125 | 29.565 |
| 33 | 28.615 | 29.065 | 29.515 | 28.685 | 29.135 | 29.575 |
| 34 | 28.625 | 29.075 | 29.525 | 28.695 | 29.145 | 29.585 |
| 35 | 28.635 | 29.085 | 29.535 | 28.705 | 29.155 | 29.595 |
| 36 | 28.645 | 29.095 | 29.545 | 28.715 | 29.165 | 29.605 |
| 37 | 28.655 | 29.105 | 29.555 | 28.725 | 29.175 | 29.625 |
| 38 | 28.665 | 29.115 | 29.565 | 28.735 | 29.185 | 29.635 |
| 39 | 28.675 | 29.125 | 29.575 | 28.745 | 29.195 | 29.645 |
| 40 | 28.685 | 29.135 | 29.585 | 28.755 | 29.205 | 29.655 |

2.2 MICROPHONE

The receiver and transmitter are controlled by the push-to-talk switch on the microphone. Press the switch and the transmitter is activated, release switch to receive. When transmitting, hold the microphone two inches from the mouth and speak clearly in a normal voice. The radio comes complete with low impedance (500 ohm) dynamic microphone.

2.3 OPERATION

2.3.1 PROCEDURE TO RECEIVE

1. Be sure that power source, microphone and antenna are connected to the proper connectors before going to the next step.

2. Turn unit on by turning VOL knob clockwise on transceiver.

3. Set the VOL to a comfortable listening level.

4. Set the MODE switch to the desired mode.

5. Listen to the background noise from the speaker. Turn the SQ knob slowly clockwise until the noise just disappears. The SQ is now properly adjusted. The receiver will remain quiet until a signal is actually received. Do not advance the control too far or some of weaker signals will not be heard.

6. Set the CHANNEL selector switch to the desired channel.

7. Set the RF GAIN control fully clockwise for maximum RF gain.

2.3.2 PROCEDURE TO TRANSMIT

1. Select the desired channel of transmission

2.  Set the MIC GAIN control fully clockwise.

3. If the channel is clear, press the push-to-talk switch on the microphone and speak in a normal voice.

2.4 ALTERNATE MICROPHONES AND INSTALLATION

For best results, the user should select a low impedance dynamic type microphone or a transistorized microphone. Transistorized type microphones have a low output impedance characteristic. The microphones must be provided with a four-lead cable. The audio conductor and its shielded lead comprise two of the leads. The third lead is for transmit control and the fourth is for receiving control. The microphone should provide the functions shown in schematic below (Figure 2-3).

4 WIRE MIC CABLE

|  | Pin Number | Mic Cable Lead |  |
| --- | --- | --- | --- |
|  | 1 | Audio Shield |  |
|  | 2 | Audio Lead |  |
|  | 3 | Transmit Control |  |
|  | 4 | Receive Control |  |

Figure 2-3 Your Transceiver Microphone Schematic

Figure 2-4 Microphone plug pin numbers viewed from rear of pin receptacle.

| RCI-6300F HP RCI-6300F TB |  | CHAPTER 3 CIRCUIT DESCRIPTION |
| --- | --- | --- |

3.0 INTRODUCTION

This section explains the technical theory of operation for the RCI-6300F HP / RCI-6300F TB mobile transceiver.

3.1 PLL CIRCUIT

The Phase Lock Loop (PLL) circuit is responsible for developing the receiver’s first local oscillator signal and the transmitter’s exciter signal. The PLL circuit consists primarily of IC2, IC3, IC4, IC5 Q25, Q27, Q28, Q29 and Q61. The PLL circuit is programmed by the rotary channel switch GPS-0501. The switch communicates the correct binary data information to the programmable divider inside of IC3. IC3 then controls the VCO (Voltage Controlled Oscillator), consisting of VCO to oscillate on the correct frequency. This signal is fed either into the receiver’s first mixer (for receive operation) or the transmitter’s mixer (for transmit operation).

3.2 RECEIVER CIRCUIT

The incoming RF signal comes into the radio via the antenna and into the front-end pre-amp, Q17. The RF signal is fed into the mixer circuit Q18 & Q19 and then into the IF section of the receiver (depending on the mode of operation). The signals is then detected by either the AM detector or FM detector and then fed to the audio amplifier section of the receiver and finally out to the speaker.

3.3 TRANSMITTER MODULATION CIRCUIT

(i) The transmitter modulation circuit modulates the low-level RF signal from the PLL exciter circuit with the user’s audio voice signal from the microphone. The audio from the microphone is then amplified and fed into the transmit amplifier circuit.

(ii) If the transceiver is in the AM mode, the AF power amplifier modulates the last RF amplifier which produces a true amplitude modulated RF signal.

3.4 TRANSMITTER AMPLIFIER CIRCUIT

The transmitter takes the basic exciter signal from the TX mixer and amplifies it through a series of amplifiers consisting of Q50, Q51, Q49, Q47, Q48 and EPA010010A (only for RCI-6300F TB) where it is sent out to the antenna connector.

RCI-6300F HP / RCI-6300F TB FREQUENCY COUNTER CIRCUIT DIAGRAM

RCI-6300F HP / RCI-6300F TB ECHO BOARD (EB-99) CIRCUIT DIAGRAM

| RCI-6300F HP RCI-6300F TB |  | CHAPTER 4 ALIGNMENT |
| --- | --- | --- |

4.0 REQUIRED TEST EQUIPMENT

| ( DC Power Supply (13.8VDC, 20A) ( RF Wattmeter (25~60 MHz, 100W) ( Multimeter (Digital) ( Automatic Modulation Meter ( Audio Signal Generator | ( Frequency Counter (100 MHz) ( RF Signal Generator (100 MHz) ( Automatic Distortion Meter ( Oscilloscope (50 MHz) ( Sinad Meter |
| --- | --- |

4.1 ALIGNMENT PROCEDURES

This transceiver has been aligned at the factory and does not require any adjustments at installation. The required test equipment listed are used for the test setup or alignment shown in Figure 4-1 Transmitter Test Setup and Figure 4-2 Receiver Test Setup. These test setup are used in part or total during the following adjustments and refer to Figure 4-3 for adjustment location.

4.1.1 PLL ALIGNMENT

| ITEM | U.U.T. SETTING | ADJUST POINT | MEASUREMENT |
| --- | --- | --- | --- |
| VCO Voltage | Disconnect the “short PCB” from TP7, TP8 and TP9. Set radio to Fr Pool 6, CH 40 AM RX mode. Set the +10KHz switch to OFF position. Connect Multimeter to TP2. Connect Oscilloscope to TP3. | L14 L15 | 6.5 VDC ( 0.1 Maximum Output and Balance. (CH 1 & CH 40) |
| AM Frequency | Set radio to Fr Pool 1, CH 1 AM RX mode. Set radio to Pool 6, CH 40 AM RX mode. Connect Frequency Counter to TP3. | L20 L17 | 17.5500 MHz + 20Hz 18.9600 MHz + 20Hz |
| TX Frequency | Set radio to Fr Pool 1, CH 1 AM TX mode. Connect Frequency Counter to TP3. | VR7 | 17.5500 MHz + 20Hz |
| AM OSC | Set radio to Fr Pool 1, CH 1 AM TX mode. Connect Frequency Counter to TP5. | L23 | 10.6950 MHz + 20Hz |

4.1.2 TRANSMITTER ALIGNMENT

| ITEM | U.U.T. SETTING | ADJUST POINT | MEASUREMENT |
| --- | --- | --- | --- |
| TX Power | Set radio to Fr Pool 2, CH 19 AM TX mode. Connect “short PCB” to TP7, TP8 and TP9. Connect RF Power Meter to antenna jack. Set RF Power Fully Clockwise. | L40,L42,L43,L44 L40,L42 | Power MAX. Spurious emission Min. Balance Power between CH 1 and CH 40. |
| AM TX Power | Set radio to Fr Pool 2, CH 19 AM TX mode. Modulation off. | VR14 | 10W (RCI-6300F HP) 50W (RCI-6300F TB) |
| RF Power Meter | Set radio to Fr Pool 2, CH 19 AM TX mode. Set SWR/S-RF switch to S/RF position. Modulation off. | VR9 | Adjust RF Power meter needle until it is in-between the green and red bar on PWR scale. |
| AM Modulation | Set radio to Fr Pool 2, CH 19 AM TX mode. Set Mic Gain Fully Clockwise. AF signal 30 mV, 1 KHz to microphone. | VR16 | 90% |
| FM Deviation | Set radio to Fr Pool 2, CH 19 FM TX mode. Set Mic Gain Fully Clockwise. AF signal 30 mV, 1 KHz to microphone. | VR5 | 4KHz |
| Frequency Counter Adjust | Set radio to Fr Pool 2, CH 19 AM RX mode. Set DIM/BRT switch to BRT position. | VC1 on frequency counter | Display should be 28.9150 |

4.1.3 RECEIVER ALIGNMENT

| ITEM | U.U.T. SETTING | ADJUST POINT | MEASUREMENT |
| --- | --- | --- | --- |
| AM Sensitivity | Set radio to Fr Pool 2, CH 19 AM RX mode. Set RF Gain Fully Clockwise. Set SQ Fully Counter Clockwise. Set VOL Control at 2 o’clock. Set NB-ANL/OFF switch to OFF position. Connect RF SG to antenna jack Frequency 28.915 MHz, 1uV. Mod 30%. Set radio to Pool 6, CH 40 AM mode. RF SG setting 29.655 MHz. Set radio to Pool 1, CH 1 AM mode. RF SG setting 28.245 MHz. | L2,3,5,6,7,8, 9,10 L5,L6 L5,L6 | Audio output > 2V S/N > 10 dB. For Balance between CH 1 and CH 40. |
| FM Sensitivity | Set radio to Fr Pool 2, CH 19 FM RX mode. Set MODE switch to FM mode. RF SG setting 28.915 MHz, 0.5uV. Mod 3KHz. | L4 | Audio output Max S/N > 20 dB. |
| NB Adjust | Set radio to Fr Pool 2, CH 19 AM RX mode RF SG setting 28.915 MHz, 100uV. Mod off. Set NB-ANL/OFF switch to NB/ANL position. Connect Voltmeter to TP1. | L1 | DC voltage to max. ( >2.0V ) |
| AM Squelch | Set radio to Fr Pool 2, CH 19 AM RX mode. Set SQ control fully clockwise. RF SG setting 28.915 MHz, 1 mV. Mod 30%. | VR4 Slowly | Adjust very slowly until squelch just open |
| AM S/RF Meter | Set radio to Fr Pool 2, CH 19 AM RX mode. Set SWR/S-RF switch to S/RF position. RF SG setting 28.915 MHz, 100uV. Mod 30%. | VR1 | Meter needle to S9 on the S scale |

Figure 4-1 Transmitter test setup

Figure 4-2 Receiver test setup

Figure 4-3 Main PCB Adjustment Location

| RCI-6300F HP RCI-6300F TB |  | CHAPTER 5 MAINTENANCE |
| --- | --- | --- |

5.0 PRECAUTIONS

The inherent quality of the solid-state components used in this transceiver will provide many years of continuous use. Taking the following precautions will prevent damage to the transceiver.

(i) Never key the transmitter unless an antenna or suitable dummy load is connected to the antenna receptacle.

(ii) Ensure that the input voltage does not exceed 16 VDC or fall below 11 VDC.

(iii) During alignment, do not transmit for more than 10 seconds at a time. Transmitting over long periods can cause heat built-up and cause transmitter damage.

5.1 PERIODIC INSPECTION

This unit is aligned at the factory to deliver maximum performance. However, continued performance cannot be expected without periodic inspection and maintenance. Important points to be checked regularly are as follows;

| Check Item | Action |
| --- | --- |
| Whip antenna (option) | If cracked or broken, replace it. |
| Coaxial cable | If sheath is cracked, seal with vinyl tape. If immersed with water, install new coaxial cable. |
| Coaxial & power plug connections | If loosened, reconnect. If corroded, clean contacts. |
| Battery connection | If corroded, clean power terminals. |
| Ground terminal | If corroded, clean terminal. |

5.2 FUSE REPLACEMENT

To protect the equipment from serious damage, a fuse is provided on the power supply lines. The fuse protect against overvoltage / reverse polarity and internal fault of the equipment. If the fuse has blown, first find out the cause of the trouble before replacing it. A fuse rated for more than the transceiver requirement should not be used, since it may permanently damage the equipment. Damage due to overfusing is not covered by the warranty.

| RCI-6300F HP RCI-6300F TB |  | CHAPTER 6 DIAGRAMS & PARTS LIST |
| --- | --- | --- |

6.0 GENERAL

Information on most electrical and mechanical parts is included in the parts list. The reference designators are in alphanumeric order.

6.1 ORDERING REPLACEMENT PARTS

Parts orders should be referred to the Parts Department at:

( Ranger Communications, Inc.

3377 Carmel Mountain Road

San Diego, CA 92121

Tel: 858-259-0287

Fax: 858-259-0437

PART LIST:

RCI-6300F HP / RCI-6300F TB ROTARY SW P.C.B

| ITEM | REFERENCE NUMBER | RANGER PART NUMBER | DESCRIPTION |
| --- | --- | --- | --- |
| 1 |  | EPT690020Z | ROTARY SW P.C.B |
| 2 | R300-R310,D325, D331,D336 | RCY010004Z | 0 OHM 0.1W |
| 3 | R312-R325 | RCY011024Z | 1K OHM 0.1W |
| 4 | R327 | RCY012224Z | 2.2K OHM 0.1W |
| 5 | R326 | RCY014724Z | 4.7K OHM 0.1W |
| 6 | D340 | EDSS00355Y | DIODE 1SS355 |
| 7 | Q304 | TY2SC2712G | TR 2SC2712GR |
| 8 | J303-J305 | EX07N48223 | PCB CONN/S 2PIN |
| 9 | J301 | EX07N48209 | PCB CONN/S 10PIN |
| 10 | S301 | EWRT32000S | ROTARY SW |

REMARK:

LEFT: COMPONENT SIDE (BLUE)

RIGHT: COPPER SIDE (BLUE)

PART LIST:

RCI-6300F HP ANT P.C.B

| ITEM | REFERENCE NUMBER | RANGER PART NUMBER | DESCRIPTION |
| --- | --- | --- | --- |
| 1 |  | EPT360042Z | ANT P.C.B |
| 2 | R9 | RCY010004Z | 0 OHM 0.1W |
| 3 | R1 | RCY014714Z | 470 OHM 0.1W |
| 4 | R3,R4 | RCY011014Z | 100 OHM 0.1W |
| 5 | R2 | RCY013314Z | 330 OHM 0.1W |
| 6 | R5,R11 | RCY011024Z | 1K OHM 0.1W |
| 7 | R10 | RCY012224Z | 2.2K OHM 0.1W |
| 8 | R12 | RCY014724Z | 4.7K OHM 0.1W |
| 9 | R7 | RCY011034Z | 10K OHM 0.1W |
| 10 | C5 | RCY012234Z | 22K OHM 0.1W |
| 11 | C7 | CK1059AB1A | 0.5PF 50WV |
| 12 | C6 | CK1030AB1A | 3PF 50WV |
| 13 | C3,C4 | CK2104AB7R | 0.1uF 25WV |
| 14 | C1,C2 | CK1103AB7L | 0.001uF 50WV |
| 15 | Q1 | TY2SC2712G | TR 2SC2712GR |
| 16 | D3 | EDSS00355Y | DIODE 1SS355 |
| 17 | D1,D2 | EDHM0198SY | DIODE HSM198S |
| 18 | D4 | EDMA0028TY | DIODE MA28T |
| 19 | L1 | ECRFZ10053 | RF COIL C3RH0610 |
| 20 | VR1 | RE10300009 | S/F/R 10K OHM |
| 21 | JP1 | WX01070715 | JUMPER WIRE |

REMARK:

COPPER SIDE (BLUE)

PART LIST:

RCI-6300F TB POWER P.C.B

| ITEM | REFERENCE NUMBER | RANGER PART NUMBER | DESCRIPTION |
| --- | --- | --- | --- |
| 1 |  | EPA010010A | POWER P.C.B |
| 2 | R904 | RCU141094Z | 1 OHM 1/4W |
| 3 | R905,R906 | RCU141004Z | 10 OHM 1/4W |
| 4 | R909 | RCP141034Z | 10K OHM 1/4W |
| 5 | R902 | RCM141024A | 1K OHM 1/4W |
| 6 | R911 | RCP121034Z | 10K OHM 1/2W |
| 7 | R903 | RCP202204Z | 22 OHM 2W |
| 8 | R901,R909(R910) | RE10200046 | S/F/R 1K OHM |
| 9 | BETWEEN C901 & GROUND | RCP141024Z | 1K OHM 1/4W |
| 10 | T901,T902 | RFP202214Z | 220 OHM 2W |
| ITEM | REFERENCE NUMBER | RANGER PART NUMBER | DESCRIPTION |
| 11 | COPPER SIDE | RCY011014Z | 100 OHM 0.1W |
| 12 | C901 | CC0501015A | 100PF 50WV |
| 13 | C943 | CC0500591A | 0.5PF 50WV |
| 14 | C906,C926,C932, C937,TERMINALx2 | CC0501037L | 0.01uF 50WV |
| 15 | C905,C920,C921,C923x2,C924x2,C925,C935,C939,C941,T901-902x2, C927-C931,C933,C940 | CC0501047L | 0.1uF 50WV |
| 16 | C918 | CD3006804Z | 68PF 300WV |
| 17 | C916 | CD3001514Z | 150PF 300WV |
| 18 | C917 | CD5001018Z | 100PF 500WV |
| 19 | C908,C910,C936 | CD3001814Z | 180PF 300WV |
| 20 | C945 | CD5005614Z | 560PF 500WV |
| 21 | C909 | CD5008214Z | 820PF 500WV |
| 22 | C904 | CD1001024Z | 0.001uF 100WV |
| 23 | C919 | CX0071037Z | HV DISC/ C 0.01(F |
| 24 | C922 | CE0162277Z | 220uF 16WV |
| 25 | C938 | CE0352277Z | 220uF 35WV |
| 26 | TR903 | T2SD02531Z | TR 2SD2531 |
| 27 | TR901,TR902 | T2SC02290Z | TR 2SC2290 |
| 28 | D903,D904 | ED1N04148Z | DIODE 1N4148 |
| 29 | D901,D902 | ED1N04001Z | DIODE 1N4001 |
| 30 | L903,L904 | ECSPG18069 | SPRING COIL |
| 31 | L901 | ECBAD18553 | BEAD COIL |
| 32 | L902 | ECCHK16098 | CHOKE COIL |
| 33 | T901 | ECRFZ10096 | RF COIL |
| 34 | T902 | ECRFZ10097 | RF COIL |
| 35 | J901,J902 | EX07N41226 | PCB CONN/S 2PIN |
| 36 | RL901 | EX05N40825 | RELAY |
| 37 | J903,J904 | GZZZ50062Z | V TYPE JACK |
| 38 | J905,J906 | GZZZ50011Z | C PIN |

REMARK:

TOP: COMPONENT SIDE (WHITE)

BOTTOM: COPPER SIDE (WHITE)

PART LIST:

RCI-6300F HP / RCI-6300F TB BAND SWITCH P.C.B

| ITEM | REFERENCE NUMBER | RANGER PART NUMBER | DESCRIPTION |
| --- | --- | --- | --- |
| 1 |  | EPT630030Z | BAND SWITCH P.C.B |
| 2 | R1 | RCP164704Z | 47 OHM 1/16W |
| 3 | R2,R3 | RCP161024Z | 1K OHM 1/16W |
| 4 | D1 | ED1N04148Z | DIODE 1N4148 |
| 5 | Q1 | T2SC00945P | TR 2SC945P |
| 6 | J1,J2,J12-J14 | EX07N48223 | PCB CONN/S 2PIN |
| 7 | J7,J10 | EX07N48350 | PCB CONN/S 3PIN |
| 8 | J6 | EX07N48490 | PCB CONN/S 4PIN |
| 9 | J9 | EX07N48224 | PCB CONN/S 7PIN |
| 10 | J11 | EX07W48824 | PCB CONN/S 3PIN |
| 11 | J3 | EX07W48826 | PCB CONN/S 5PIN |
| 12 | J4 | EX07W48827 | PCB CONN/S 6PIN |
| 13 | JP3 | WX01070705 | JUMPER WIRE |
| 14 | JP1 | WX01070710 | JUMPER WIRE |
| 15 | MIC/RF | RV10203524 | VR 1KB/1KA |
| 16 | TALK BACK/RF PWR | RV20303560 | VR 20KB/5KB |
| 17 | VOL/SQ,ECHO/TIME | RV50303522 | VR 50KB/50KA W/SW |
| 18 | MODE | EWRT32084S | ROTARY SW 3N |
| 19 | BAND | EWRT32094S | ROTARY SW 6N |

REMARK:

COPPER SIDE (WHITE)

PART LIST:

RCI-6300F HP / RCI-6300F TB MIC P.C.B

| ITEM | REFERENCE NUMBER | RANGER PART NUMBER | DESCRIPTION | REMARK |
| --- | --- | --- | --- | --- |
| 1 |  | EPT690050Z | MIC P.C.B |  |
| 2 | C502-C504 | CC0501027L | 0.001uF 50WV |  |
| 3 | C501 | CC0501027L | 0.001uF 50WV | RCI-6300F HP |
| 4 | C505,C506 | CC0501037L | 0.01uF 50WV |  |
| 5 | L501 | ECCHK16001 | CHOKE COIL 5.6uH |  |
| 6 | L502 | ECBAD18526 | BEAD COIL |  |
| 7 | 1-4 | EX06N41020 | MIC JACK |  |
| 8 | MIC/GND/PTT | EX07N48903 | WIRE CONN/H 3PIN |  |

REMARK:

COPPER SIDE (BLUE)

PART LIST:

RCI-6300F HP / RCI-6300F TB COUNTER P.C.B

| ITEM | REFERENCE NUMBER | RANGER PART NUMBER | DESCRIPTION |
| --- | --- | --- | --- |
| 1 |  | EPT900040Z | COUNTER P.C.B |
| 2 | R40 | RCY010004Z | 0 OHM 0.1W |
| 3 | R19-R39 | RCY011014Z | 100 OHM 0.1W |
| 4 | R6 | RCY013314Z | 330 OHM 0.1W |
| 5 | R9 | RCY014714Z | 470 OHM 0.1W |
| 6 | R4,R5 | RCY012224Z | 2.2K OHM 0.1W |
| 7 | R7 | RCY014724Z | 4.7K OHM 0.1W |
| 8 | R3,R10,R12 | RCY011034Z | 10K OHM 0.1W |
| 9 | R13-R18 | RCY012234Z | 22K OHM 0.1W |
| 10 | R11 | RCY013334Z | 33K OHM 0.1W |
| 11 | R41,R42 | RCY014734Z | 47K OHM 0.1W |
| 12 | C15 | CK1150AB4A | 15PF 50WV |
| 13 | C14 | CK1330AB4A | 33PF 50WV |
| 14 | C2,C6,C8,C10,C11,C12, C17,C19,C21,C29,C31, C32,C33,C35,C36,C28 | CK2104AB7R | 0.1uF 25WV |
| 15 | C5,C7,C16,C20,C22, C25,C38,C40 | CK1103AB6U | 0.01uF 50WV |
| 16 | C13 | CK1102AB7L | 0.001uF 50WV |
| 17 | C9,C18,C27,C30,C34 | CK5105AA7R | 1uF 16WV |
| 18 | U3 | YNRG0GX3SP | IC LC7232N 18PIN |
| 19 | U2 | YNTA04073B | IC TC4093BFN 14PIN |
| 20 | U4,U5,U6 | YNR006250F | IC BA6250F 16PIN |
| 21 | U1 | YNT011650U | IC TK11650U 3PIN |
| 22 | Q3 | TY25C2714Z | TR 2SC2714 |
| 23 | Q1,Q2 | TY2SC2712G | TR 2SC2712GR |
| 24 | D2,D3 | EDSS00355Y | DIODE 1SS355 |
| 25 | L1 | YCCHK16259 | CHOKE COIL 1000UH |
| 26 | VC1 | CV038200AY | TRIMMER/C 20PF |
| 27 | C1,C3 | CEM161077A | 100UF 16WV |
| 28 | X1 | EYCAP04500 | CRYSTAL 4.500MHz |
| 29 | C37 | CE0161087Z | 1000UF 16WV |
| 30 | COUNTER PCB x2 | EX07N48927 | PCB CONN/S 12PIN |
| 31 | CN1 | EX07N48223 | PCB CONN/S 2PIN |
| 32 | CN2 | EX07N48224 | PCB CONN/S 7PIN |

REMARK:

TOP: COMPONENT SIDE (BLUE)

BOTTOM: COPPER SIDE (BLUE)

PART LIST:

RCI-6300F HP / RCI-6300F TB LED DISPLAY P.C.B

| ITEM | REFERENCE NUMBER | RANGER PART NUMBER | DESCRIPTION |
| --- | --- | --- | --- |
| 1 |  | EPT900022Z | LED DISPLAY P.C.B |
| 2 | DISPLAY PCB | EX03N40003 | LED DISPLAY |
| 3 | 1,2,3,4,5,6 | EX03N40476 | LED DISPLAY |
| 4 | TX/RX | EX01N40004 | LED |
| 5 | ON,NB/ANL,R.B,S/RF, SWR,+10K | EWPS33033X | PUSH SW. |
| 6 | DISPLAY PCB | EX07N48928 | PCB CONN/S 12PIN |
| 7 | TOJ10,+10K,S/RF, M-M+ | EX07N48223 | PCB CONN/S 2PIN |
| 8 | TOJ2,TOJ6 | EX07N48350 | PCB CONN/S 3PIN |
| 9 | RX/G/TX | EX07N48947 | PCB CONN/S 3PIN |
| 10 | TOJ13 | EX07W48824 | PCB CONN/S 4PIN |

REMARK:

TOP: COMPONENT SIDE (BLUE)

BOTTOM: COPPER SIDE (BLUE)

PART LIST:

RCI-6300F HP / RCI-6300F TB ECHO P.C.B (EB-99)

| ITEM | REFERENCE NUMBER | RANGER PART NUMBER | DESCRIPTION |
| --- | --- | --- | --- |
| 1 |  | EPT0SSB50F | ECHO P.C.B |
| 2 | R3,R16 | RCY011014Z | 10 OHM 0.1W |
| 3 | R28 | RCY014714Z | 470 OHM 0.1W |
| 4 | R27 | RCY011024Z | 1K OHM 0.1W |
| 5 | R7 | RCY012224Z | 2.2K OHM 0.1W |
| 6 | R17,R29 | RCY014724Z | 4.7K OHM 0.1W |
| 7 | R1,R23,R24,R30,R26 | RCY011034Z | 10K OHM 0.1W |
| 8 | R18 | RCY012234Z | 22K OHM 0.1W |
| 9 | R2,R5,R6,R13,R15,R22 | RCY013334Z | 33K OHM 0.1W |
| 10 | R14,R20,R4 | RCY014734Z | 47K OHM 0.1W |
| 11 | R21 | RCY011044Z | 100K OHM 0.1W |
| 12 | C26 | CK1331AB5A | 330PF 50WV |
| 13 | C5 | CK1561AB5A | 560PF 50WV |
| 14 | C12,C14 | CK1102AB7L | 0.001uF 50WV |
| 15 | C4,C11,C23,C34 | CK2103AB7R | 0.01uf 25WV |
| 16 | C2,C3,C10,C16,C28,C29,C30,C32,C33,C36,C37, C38,C39,C40,C18,C35 | CK2104AB7R | 0.1Uf 25WV |
| 17 | C6,C31,C20,C22 | CK510AB7R | 1uF 16WV |
| 18 | C13 | CK1152AB7R | 0.0015uF 50WV |
| 19 | C19 | CK1472AB6U | .0047uF 50WV |
| 20 | C25 | CK5105ZZ7R | 1uF 16WV |
| 21 | C1 | CK5225AA7R | 2.2uF 16WV |
| 22 | IC1 | YNJR04558M | IC NJM4558M 8PIN |
| 23 | IC2 | YNES56033S | IC ES56033S 16PIN |
| 24 | Q1,Q3 | TY2SC2712G | TR 2SC2712GR |
| 25 | D1,D2,D4,D5,D6 | EDSS00355Y | DIODE 1SS355 |
| 26 | D3 | EDZD05569Y | ZENER DIODE 5.6V |
| 27 | C27 | CE0164767Z | 47uF 16WV |
| 28 | J3 | EX07N41216 | PCB CONN/S 3PIN |
| 29 | J2 | EX07N41227 | PCB CONN/S 3PIN |
| 30 | J1 | EX07N48223 | PCB CONN/S 2PIN |
| 31 | J6 | EX07N48331 | PCB CONN/S 6PIN |

REMARK:

TOP: COMPONENT SIDE (WHITE)

BOTTOM: COPPER SIDE (BLUE)

RCI-6300F HP / RCI-6300F TB MAIN PCB.

REMARK:

COPPER SIDE (WHITE)

PART LIST

RCI-6300F HP MAIN PCB

| REFERENCE NUMBER | RANGER PART NO. | DESCRIPTION |
| --- | --- | --- |
|  | EPT690010Z | MAIN P.C.B |
| R246 | RCP164794Z | 4.7 ( 1/16W |
| R267 | RCP161504Z | 15 ( 1/16W |
| R241,242 | RCP162204Z | 22 ( 1/16W |
| R133,213,253,282, VR10,VR11 | RCP164704Z | 47 ( 1/16W |
| R130,215,220 | RCP165604Z | 56 ( 1/16W |
| R11 | RCP166804Z | 68 ( 1/16W |
| R3,5,8,30,33,76,81, 259,260,263,JP237 | RCP161014Z | 100 ( 1/16W |
| R32,249 | RCP161514Z | 150 ( 1/16W |
| R23 | RCP161814Z | 180 ( 1/16W |
| R140,163,177 | RCP162214Z | 220 ( 1/16W |
| R31 | RCP162714Z | 270 ( 1/16W |
| R6,10,16,24,248,254,300 | RCP163314Z | 330 ( 1/16W |
| R141,188,268,293 | RCP164714Z | 470 ( 1/16W |
| R258,266 | RCP165614Z | 560 ( 1/16W |
| R4,50,209 | RCP166814Z | 680 ( 1/16W |
| R74 | RCP168214Z | 820 ( 1/16W |
| R36,62,64,67,72,115, 116,118,123,136-138, 143,144,160,164,179, 186,189,205,214,232,261,291,292,295,303, 206,237 | RCP161024Z | 1K( 1/16W |
| R192 | RCP161224Z | 1.2K( 1/16W |
| R132,207,233,247,255,273,79,80 | RCP161524Z | 1.5K( 1/16W |
| R226 | RCP161824Z | 1.8K( 1/16W |
| R20,27,71,73,75,134, 162,122,283 | RCP162224Z | 2.2K( 1/16W |
| R9,25,28 | RCP162724Z | 2.7K( 1/16W |
| R18,22,58,66,128,129,191,219,274,277 | RCP163324Z | 3.3K( 1/16W |
| R52,57 | RCP163924Z | 3.9K( 1/16W |
| R26,35,131,165,190, 195,196 | RCP164724Z | 4.7K( 1/16W |
| R264,265 | RCP165624Z | 5.6K( 1/16W |
| R14,40,41,82,127,148,297 | RCP166824Z | 6.8K( 1/16W |
| R275 | RCP168224Z | 8.2K( 1/16W |
| R1,13,17,37,38,65, 142,145,159,161,168,175,181,202,216,227-231,272,276,294,296,262,68 | RCP161034Z | 10K( 1/16W |
| R178 | RCP161234Z | 12K( 1/16W |
| R180 | RCP161534Z | 15K( 1/16W |
| R187,208 | RCP162234Z | 22K( 1/16W |
| R121 | RCP162734Z | 27K( 1/16W |
| R2 | RCP163334Z | 33K( 1/16W |
| R46 | RCP163934Z | 39K( 1/16W |
| R7,29,61,63,126,185, 218,234,235,236,224, 222. | RCP164734Z | 47K( 1/16W |
| R21,85,105,107 | RCP166834Z | 68K( 1/16W |
| R45 | RCP168234Z | 82K( 1/16W |
| R12,42-44,51,53,77, 78,104,108,112,182, 184,225,256,257,278, 221 | RCP161044Z | 100K( 1/16W |
| R47,59,117,135,139, 194 | RCP162244Z | 220K( 1/16W |
| R49,55,176 | RCP162744Z | 270K( 1/16W |
| R15,34,111,183 | RCP164744Z | 470K( 1/16W |
| R48 | RCP168244Z | 820K( 1/16W |
| R106 | RCP161054Z | 1M( 1/16W |
| R193 | RCP161554Z | 1.5M( 1/16W |
| R124 | RCP161064Z | 10M( 1/16W |
| JP264 | RCP142204Z | 22 ( 1/4W |
| R243,244 | RCP121514Z | 150 ( 1/2W |
| R239 | RCP121034Z | 10K( 1/2W |
| C1,49,108,119,122, 279,147 | CC0501004L | 10PF 50WV |
| C224 | CC0501504L | 15PF 50WV |
| C195 | CC0501804L | 18PF 50WV |
| C24,287 | CC0503304L | 33PF 50WV |
| C8 | CC0508204L | 82PF 50WV |
| C4,53 | CC0501015L | 100PF 50WV |
| C137 | CC0501515L | 150PF 50WV |
| C56,222 | CC0501815L | 180PF 50WV |
| C28 | CC0502215L | 220PF 50WV |
| C31,136 | CC0502715L | 270PF 50WV |
| C11,14 | CC0503315L | 330PF 50WV |
| C23 | CC0505615L | 560PF 50WV |
| C197 | CC0500101A | 1PF 50WV |
| C225 | CC0500201A | 2PF 50WV |
| C286 | CC0500301A | 3PF 50WV |
| C61,62,90,226,218 | CC0500501A | 5PF 50WV |
| C89 | CC0501504A | 15PF 50WV |
| C43 | CC0501804A | 18PF 50WV |
| C84 | CC0502704A | 17PF 50WV |
| C202 | CC0504704A | 47PF 50WV |
| C88,116,117 | CC0506804A | 68PF 50WV |
| C192 | CC0508204A | 82PF 50WV |
| C194 | CC0501515A | 150PF 50WV |
| C196,295 | CC0501815A | 180PF 50WV |
| C139 | CC0503904D | 39PF 50WV |
| C281 | CC0501015G | 100PF 50WV |
| C282 | CC0501815G | 180PF 50WV |
| C124 | CC0506804G | 68PF 50WV |
| C123 | CC0501215G | 120PF 50WV |
| C220 | CC0502215G | 220PF 50WV |
| C86 | CC0502715G | 270PF 50WV |
| C85,201,203 | CC0503915G | 390PF 50WV |
| C209,210 | CC0504715G | 470PF 50WV |
| C199 | CD3005614Z | 560P 300WV |
| C7,47,50,74,95,99, 100,110,118,120,174,183,244,246,245, | CC0501027L | 0.001UF 50WV |
| C161 | CC0501537L | 0.015UF 50WV |
| C81,83,111,113,126, 173,193,206,207,211-213,228,234,236,249,250,256,259,268,272,280,288,292,296 (COPPER SIDE),C270, C177,R302 | CC0501047L | 0.1UF 50WV |
| C5,18,20,48,65,87,92,96,102,105,106,151,160,233,251-253,257, 258,260-263,240 | CC0504737L | 0.047uF 50WV |
| C32,42,45,46,221,162,163 | CC0504727L | 0.0047UF 50WV |
| C155 | CC0502237L | 0.022UF 50WV |
| C200 | CC1001037L | 0.01UF 100WV |
| C2,3,6,9,15-17,19, 25,51,57,58,60,109, 114,121,138,188,189,205,216,217,219,223,229,230,232,247,254,255,265,267,269,271,277,278,285,184 | CC0501037L | 0.01UF 50WV |
| C154 | CT0162246Z | 0.22UF 16WV |
| C97 | CT0164746Z | T/C0.47UF 16WV |
| C98 | CT0162256Z | 2.2UF 16WV |
| C112 | CT0161056Z | 1UF 16WV |
| C40,178,171,235 | CM0501045Z | 0.1UF 50WV |
| C26,27,237 | CM0501025Z | 0.001UF 50WV |
| C29,78,185,41 | CM0501035Z | 0.01UF 50WV |
| C39 | CM0502235Z | 0.022UF 50WV |
| C176 | CM0504725Z | 0.0047UF 50WV |
| C34 | CM0504735Z | .047UF 50WV |
| C12,30,101 | CM0502225Z | .0022UF 50WV |
| C10 | CE0504747Z | 0.47UF 50WV |
| C67,75,153,157,170, 186,187,198 | CE0501057Z | 1UF 50WV |
| C159,214,148 | CE0502257Z | 2.2UF 50WV |
| C38,103,182 | CE0504757Z | 4.7UF 50WV |
| C13,21,22,44,82,115,158,275,276 | CE0251067Z | 10UF 25WV |
| C80,181 | CE0252267Z | 22UF 25WV |
| C37,175 | CE0254767Z | 47UF 25WV |
| C107,156,238,293 | CE0161077Z | 100UF 16WV |
| C152,179 | CE0163377Z | 330UF 16WV |
| C91 | CE0104777Z | 470UF 10WV |
| C243,248 | CE0251087Z | 1000UF 25WV |
| C35 | CEM254767Z | 47UF 25WV |
| FL1 | EFCFW455HT | C/FILTER 455HT |
| FL2 | EFCFE107MX | C/FILTER 10.7MX RED |
| X1 | EYCAB10240 | CRYSTAL 10.240MHZ |
| X2 | EYCAA15360 | CRYSTAL 15.360MHZ |
| X3 | EYBAA12660 | CRYSTAL 12.660MHZ |
| X4 | EYBAE10697 | CRYSTAL 10.6975MHZ |
| IC1 | ENJR00324D | NJM324D |
| IC3 | ENMC45106P | MC145106 |
| IC4,5 | ENMC14008B | MC14008BCP |
| IC7 | ENJR04558D | NJM4558D |
| IC9 | ENSM06130Z | TDA6130 |
| VCO | ENRG0IC090 | IC090 10PIN |
| Q8,17 | T2SC01674L | 2SC1674L |
| Q51 | T2SC02538Z | 2SC2538 |
| Q52 | T2SC01906Z | 2SC1906 |
| Q26,36 | TDTC0124ES | DTC124ES |
| Q24,43 | TDTC0114ES | DTC114S |
| Q30,33,62 | T2SA01282E | 2SA1282AE |
| Q1,2,9,10-12,25,27, 28,29,46,61 | T2SC01675L | 2SC1675 |
| Q60 | TDTA0124ES | DTA124ES |
| Q3-5,7,14,16,31,35, 39,42,44,53,57,58,40 | T2SC00945P | 2SC945P |
| Q6,38 | T2SA00733P | 2SA733P |
| Q55 | T2SA01869Z | 2SA1869 |
| Q18,19 | FM0J00310Z | F.E.T J310 |
| D3,5,7-10,13,14,20-23,27,33,34,35,37, 40,53,60-65,69,75-82,84,85,88-91,97, 102,106,107,111-141, 143,144,147,149,150,JP191 | ED1N04148Z | DIODE 1N4148 |
| D1,2,11,12,30,31 | ED1N00060P | 1N60P |
| D110 | ED1N04003Z | 1N4003 |
| D109 | ED1N04007Z | 1N4007 |
| D16,17 | EDSS00053Z | ISS53 |
| D59,72 | EDMA00027W | MA27W-A |
| D71,145 | EDMA00027T | MA27T-A |
| D18,19,42,99,100, 146,148 | EDSV00251Z | SVC-251SPA |
| D70 | EDZD05519Z | 5.1V 0.5W |
| D73 | EDZD05759Z | 7.5V 0.5W |
| L2,3 | ECIFT12002 | I.FT |
| L6 | ECIFT12290 | I.F.T |
| L17,20 | ECIFT12012 | I.F.T |
| L23 | ECIFT12016 | I.F.T |
| L1 | ECIFT12252 | I.F.T |
| L44 | ECIFT12255 | I.F.T |
| L9,10 | ECIFT12256 | I.F.T |
| L15,43 | ECIFT12258 | I.F.T |
| L40 | ECIFT12262 | I.F.T |
| L14 | ECIFT12558 | I.F.T |
| L5 | ECIFT12253 | I.F.T |
| L7,42 | ECIFT12440 | I.F.T |
| L8 | ECIFT12492 | I.F.T |
| L4 | ECIFT12526 | I.F.T |
| L503,504 | ECCHK16000 | CHOKE COIL |
| T1 | ECCHK16004 | CHOKE COIL |
| L34,37,33 | ECCHK16070 | CHOKE COIL |
| L47 | ECCHK16176 | CHOKE COIL |
| L16 | ECCHK16246 | CHOKE COIL |
| L28 | ECSPG18003 | SPRING COIL |
| L30 | ECSPG18077 | SPRING COIL |
| L29 | ECSPG18075 | SPRING COIL |
| L31 | ECSPG18365 | SPRING COIL |
| L35 | ECSPG18001 | SPRING COIL |
| L38 | ECRFZ10048 | RF COIL |
| L13,39,41 | ECBAD18526 | BEAD COIL |
| VR16 | RE10200041 | S/F/R 1K |
| VR14,18 | RE50200042 | S/F/R 5K |
| VR1,5 | RE10300031 | S/F/R 10K |
| VR9 | RE10400043 | S/F/R 100K |
| VR4 | RE50400087 | S/F/R 500K |
| RA1 | RCS0870014 | R/ARRAY |
| RA2 | RCS0970015 | R/ARRAY |
| RA3 | RCS0670025 | R/ARRAY |
| C165-R223 | WL0007009Z | LEAD WIRE |
| C167-R223 | WL0207009Z | LEAD WIRE |
| J29 | WX01070703 | J/W 7x3x7 |
| JP1-3,4,7,9,23,24-26 ,32,33,38,39,50,54-57,59,61,62,63,65,66,71,72,79,80,82,85, 86,87,93,100,105,106,114,115,118-122,124 -126,190,135,138-140 ,144,145,152,153,156,157,159,160,128,165,166,168,170,172,174,175,177-179,181,184 ,188,91,190 | WX01060605 | J/W 6x5x6 |
| JP200-202,204,205, 209-211,212,214,217, 219,220,224,226,231-233,235,236,238,239,242,243,245,250,252,253,255-260,262,263, 265,271-273,276,278- 280,285,267x2,R245, R305,R89,C142,C291, D26,D46,D50,D95,D49-L46,TP8,C133 | WX01070705 | J/W 7x5x7 |
| R19,119 | WX01070706 | J/W 7x6x7 |
| D25 | WX01070708 | J/W 7x8x7 |
| JP6,11,12,16-19,34- 37,40-49,51-53,58,60 ,67,70,88,96,101-104 ,107-109,116,117,127 ,129,133,136,137,143,147,148,151,161,167,169,176,131,132,111,130 | WX01060610 | J/W 6x10x6 |
| JP215,218,222,223, 225,227,228,230,234,241,244,246-249,251, 254,261,266,277,286,287,240,IC6,C128-L45 ,L36 | WX01070710 | J/W 7x10x7 |
| JP75-78,81,193 | WX01070712 | J/W 7x12x7 |
| JP99 | WX01070713 | J/W 7x13x7 |
| FL3 | WX01070715 | J/W 7x15x7 |
| TP7-TP8,TP8-TP9 | WX01070718 | J/W 7x18x7 |
| J7x2,10,17,22,Q41 | EX07N48223 | P/C/S 3P |
| J2,3,6,11,18 | EX07N48350 | P/C/S 3P |
| J21 | EX07N48490 | P/C/S 4P |
| J5,20 | EX07N48222 | P/C/S 5P |
| J13 | EX07N48331 | P/C/S 6P |
| J14 | EX07N48224 | P/C/S 7P |
| J1 | EX07N48543 | P/C/S 9P |
| J28 | EX07N48244 | P/C/S 3P |
| J12 | EX07N41227 | P/C/S 3P |
| J16 | EX07N41330 | P/C/S 2P |
| J4 | EX07N49140 | P/C/S 2P |
| J28 | EX07N48151 | P/C/H |
| TP2,3,5 | EX07N48612 | P/C/S 1PIN |
| EXT SP,CW/PA | EX06N41045 | EAR JACK |
| DC SOCKETx2 | CC0501037L | 0.01uF 50WV |
| IC8 | ENTA07222A | IC TA7222AP |
| Q54 | T2SB00754Y | TR 2SB754Y |
| Q49 | T2SC02166C | TR 2SC2166C |
| Q47,48 | T2SC02312C | TR 2SC2312C |
| Q37 | T2SA01869Z | TR 2SA1869 |
| DC SOCKET | EDLT6A400Z | DIODE LT6A400 |

RCI-6300F HP MISC. PARTS

| REFERENCE NUMBER | RANGER PART NO. | DESCRIPTION |
| --- | --- | --- |

| - | MM7878041B | HEAT SINK |
| --- | --- | --- |
| - | MT3001021X | SET CHASSIS |
| - | MT3600050X | DC SOCKET HOLDER |
| 2SB754Y | XZZZ90020Z | INSULATING PLATE |
| Q47,48,49 | XZZZ90003Z | INSULATING PLATE |
| Q47,48,49 | XZZZ90358Z | INSULATING PLATE |
| IC8 | LZZZ61008Z | IC SHIELD B |
| DC(2) | JS053006MN | SET SCREW |
| Q37 | JS052006MN | SET SCREW |
| Q47,48,49 | JS052012MN | SET SCREW |
| IC8 | JS013006MV | SET SCREW |
| Q54 | JS052010MN | SET SCREW |
| HEAT SINK | JS013008TN | SET SCREW |
| ANT JACK(1),MIC JACK(1) | XZZZ90098Z | SOLDER PLATE |
| - | ES300835SQ | SPEAKER |
| - | PT9000060K | FRONT PANEL |
| - | PT9000020E | CH KNOB |
| - | PT9000040E | INNER KNOB |
| - | PT9000050E | OUTER KNOB |
| - | PT3600080A | SIGNAL METER HOLDER |
| - | PT9000070E | BAND KNOB |
| - | PT2100031C | COUNT WINDOW |
| - | PT2100041C | DISPLAY WINDOW |
| - | PT7001070C | PUSH KEY |
| - | MT9000010X | FRONT CHASSIS |
| - | MT3600040S | CHANNEL BRACKET |
| - | MT3600061X | TOP HOUSING |
| - | MT36000710 | BOTTOM HOUSING |
| - | MT3600030S | HANDLER |
| - | XZZZ90004Z | FOAM |
| - | XZZZ90005Z | FOAM |
| - | XZZZ90367A | SPONGE |
| - | GZZZ50000Z | CLAMP |
| - | XZZZ90098Z | SOLDER PLATE |
| - | XZZZ90021Z | FOAM |
| - | XZZZ90064Z | INSULATING PLATE |
| COUNTER | XZZZ90363Z | PVC STAND OFF |
| COUNTER | JS013016WH | SET SCREW |
| FRONT PANEL(4) | JS033008MN | SET SCREW |
| TONE(2),CH9(2), WB/ANL(2) | JS052004MN | SET SCREW |
| SWR SW(2) | JS052605MN | SET SCREW |
| CH BKT(2), CHASSIS(12) | JS053006MN | SET SCREW |
| SPK(4) | JS053008MN | SET SCREW |
| MAIN PCB(5) | JS053006TN | SET SCREW |
| SPK(4) | JN263035ZS | NUT WITH WASHER |
| - | HZZZ76005Z | SSEBRIH K 905 |

PART LIST

RCI-6300F TB MAIN PCB

| REFERENCE NUMBER | RANGER PART NO. | DESCRIPTION |
| --- | --- | --- |
|  | EPT690010Z | MAIN P.C.B |
| R246 | RCP164794Z | 4.7 ( 1/16W |
| R267 | RCP161504Z | 15 ( 1/16W |
| R241,VR10 | RCP162204Z | 22 ( 1/16W |
| J3(2-4P) | RCP163304Z | 33 ( 1/16W |
| R133,213,253,282 | RCP164704Z | 47 ( 1/16W |
| R130,215,220,249 | RCP165604Z | 56 ( 1/16W |
| R11 | RCP166804Z | 68 ( 1/16W |
| R3,5,8,30,33,76,81, 259,260,263,JP237 | RCP161014Z | 100 ( 1/16W |
| R32 | RCP161514Z | 150 ( 1/16W |
| R23 | RCP161814Z | 180 ( 1/16W |
| R140,163,177 | RCP162214Z | 220 ( 1/16W |
| R31 | RCP162714Z | 270 ( 1/16W |
| R6,10,16,24,248,254,300 | RCP163314Z | 330 ( 1/16W |
| R141,188,268,293 | RCP164714Z | 470 ( 1/16W |
| R258,266 | RCP165614Z | 560 ( 1/16W |
| R4,50,209 | RCP166814Z | 680 ( 1/16W |
| R74 | RCP168214Z | 820 ( 1/16W |
| R36,62,64,67,72,115, 116,118,123,136-138, 143,144,160,164,179, 186,189,205,214,232,261,291,292,295,303, 206,L5 | RCP161024Z | 1K( 1/16W |
| R192 | RCP161224Z | 1.2K( 1/16W |
| R132,207,233,247,255,273,79,80 | RCP161524Z | 1.5K( 1/16W |
| R226 | RCP161824Z | 1.8K( 1/16W |
| L7 | RCP162024Z | 2K( 1/16W |
| R20,27,71,73,75,134, 162,122,283 | RCP162224Z | 2.2K( 1/16W |
| R9,25,28 | RCP162724Z | 2.7K( 1/16W |
| R18,22,58,66,128,129,191,219,274,277 | RCP163324Z | 3.3K( 1/16W |
| R52,57 | RCP163924Z | 3.9K( 1/16W |
| R26,35,131,165,190, 195,196 | RCP164724Z | 4.7K( 1/16W |
| R264,265 | RCP165624Z | 5.6K( 1/16W |
| R14,40,41,82,127,148,297,70 | RCP166824Z | 6.8K( 1/16W |
| R275 | RCP168224Z | 8.2K( 1/16W |
| R1,13,17,37,38,65, 142,145,159,161,168,175,181,202,216,227-231,272,276,294,296,262,68 | RCP161034Z | 10K( 1/16W |
| R178 | RCP161234Z | 12K( 1/16W |
| R180 | RCP161534Z | 15K( 1/16W |
| R187,208 | RCP162234Z | 22K( 1/16W |
| R121 | RCP162734Z | 27K( 1/16W |
| R2 | RCP163334Z | 33K( 1/16W |
| R46 | RCP163934Z | 39K( 1/16W |
| R7,29,61,63,126,185, 218,234,235,236,224, 222. | RCP164734Z | 47K( 1/16W |
| R21,85,105,107 | RCP166834Z | 68K( 1/16W |
| R45 | RCP168234Z | 82K( 1/16W |
| R12,42-4,51,53,77,78 ,104,108,112,182,184,225,256,257,278,221 |  |  |
| R47,59,117,135,139, 194 | RCP162244Z | 220K( 1/16W |
| R49,55,176 | RCP162744Z | 270K( 1/16W |
| R15,34,111,183 | RCP164744Z | 470K( 1/16W |
| R48 | RCP168244Z | 820K( 1/16W |
| R106 | RCP161054Z | 1M( 1/16W |
| R193 | RCP161554Z | 1.5M( 1/16W |
| R124 | RCP161064Z | 10M( 1/16W |
| JP264 | RCP142204Z | 22 ( 1/4W |
| R244 | RCP121514Z | 150 ( 1/2W |
| R239 | RCP121034Z | 10K( 1/2W |
| C1,49,108,119,122, 279,147 | CC0501004L | 10PF 50WV |
| C224 | CC0501504L | 15PF 50WV |
| C195 | CC0501804L | 18PF 50WV |
| C24,287 | CC0503304L | 33PF 50WV |
| C8 | CC0508204L | 82PF 50WV |
| C4,53 | CC0501015L | 100PF 50WV |
| C137 | CC0501515L | 150PF 50WV |
| C56,222 | CC0501815L | 180PF 50WV |
| C28 | CC0502215L | 220PF 50WV |
| C31,136 | CC0502715L | 270PF 50WV |
| C11,14 | CC0503315L | 330PF 50WV |
| C23 | CC0505615L | 560PF 50WV |
| C197 | CC0500101A | 1PF 50WV |
| C225,52 | CC0500201A | 2PF 50WV |
| C61,62,90,226,218 | CC0500501A | 5PF 50WV |
| C89 | CC0501504A | 15PF 50WV |
| C43 | CC0501804A | 18PF 50WV |
| C84 | CC0502704A | 17PF 50WV |
| C202 | CC0504704A | 47PF 50WV |
| C88,116,117 | CC0506804A | 68PF 50WV |
| C192,8 | CC0508204A | 82PF 50WV |
| C194 | CC0501515A | 150PF 50WV |
| C196,295 | CC0501815A | 180PF 50WV |
| C139 | CC0503904D | 39PF 50WV |
| C281 | CC0501015G | 100PF 50WV |
| C282 | CC0501815G | 180PF 50WV |
| C124 | CC0506804G | 68PF 50WV |
| C123 | CC0501215G | 120PF 50WV |
| C220 | CC0502215G | 220PF 50WV |
| C86 | CC0502715G | 270PF 50WV |
| C85,201,203 | CC0503915G | 390PF 50WV |
| C209,210 | CC0504715G | 470PF 50WV |
| C199 | CD3005614Z | 560P 300WV |
| C7,47,50,74,95,99, 100,110,118,120,174,183,244,246,245 | CC0501027L | 0.001UF 50WV |
| C161 | CC0501537L | 0.015UF 50WV |
| C81,83,111,113,126, 173,193,206,207,211,213,228,234,236,249,250,256,259,268,272,280,288,292,296 (COPPER SIDE),C270, C177,R302 | CC0501047L | 0.1UF 50WV |
| C5,18,20,48,65,87,92,96,102,105,106,151,160,233,251-253,257, 258,260-263,240 | CC0504737L | 0.047uF 50WV |
| C32,42,45,46,221,162,163 | CC0504727L | 0.0047UF 50WV |
| C155 | CC0502237L | 0.022UF 50WV |
| C200 | CC1001037L | 0.01UF 100WV |
| C2,3,6,9,15-17,19,25 ,51,57,58,60,109,114,121,138,188,189,205,216,217,219,223,229,230,232,247,254,255,265,267,269,271,277,278,285,184 | CC0501037L | 0.01UF 50WV |
| C154 | CT0162246Z | 0.22UF 16WV |
| C97 | CT0164746Z | 0.47UF 16WV |
| C98 | CT0162256Z | 2.2UF 16WV |
| C112 | CT0161056Z | 1UF 16WV |
| C40,178,171,235 | CM0501045Z | 0.1UF 50WV |
| C26,27,237,39 | CM0501025Z | 0.001UF 50WV |
| C29,185 | CM0501035Z | 0.01UF 50WV |
| C41 | CM0502235Z | 0.022UF 50WV |
| C176 | CM0504725Z | 0.0047UF 50WV |
| C34 | CM0504735Z | .047UF 50WV |
| C12,30,101 | CM0502225Z | .0022UF 50WV |
| C78 | CM0502245Z | .22UF 50WV |
| C10 | CE0504747Z | 0.47UF 50WV |
| C67,75,153,157,170, 186,187,198 | CE0501057Z | 1UF 50WV |
| C159,214,148 | CE0502257Z | 2.2UF 50WV |
| C38,103,182 | CE0504757Z | 4.7UF 50WV |
| C13,21,22,44,82,115,158,275,276 | CE0251067Z | 10UF 25WV |
| C80,181 | CE0252267Z | 22UF 25WV |
| C37,175 | CE0254767Z | 47UF 25WV |
| C107,156,238,293 | CE0161077Z | 100UF 16WV |
| C152,179 | CE0163377Z | 330UF 16WV |
| C91 | CE0104777Z | 470UF 10WV |
| C243,248 | CE0251087Z | 1000UF 25WV |
| C35 | CEM254767Z | 47UF 25WV |
| FL1 | EFCFW455HT | C/FILTER 455HT |
| FL2 | EFCFE107MX | C/FILTER 10.7MX RED |
| X1 | EYCAB10240 | CRYSTAL 10.240MHZ |
| X2 | EYCAA15360 | CRYSTAL 15.360MHZ |
| X3 | EYBAA12660 | CRYSTAL 12.660MHZ |
| X4 | EYBAE10697 | CRYSTAL 10.6975MHZ |
| IC1 | ENJR00324D | I.C.NJM324D |
| IC3 | ENMC45106P | MC145106 |
| IC4,5 | ENMC14008B | MC14008BCP |
| IC7 | ENJR04558D | NJM4558D |
| IC9 | ENSM06130Z | TDA6130 |
| VCO | ENRG0IC090 | IC090 10PIN |
| Q8,17 | T2SC01674L | 2SC1674L |
| Q51 | T2SC02538Z | 2SC2538 |
| Q52 | T2SC01906Z | 2SC1906 |
| Q26,36 | TDTC0124ES | DTC124ES |
| Q24,43 | TDTC0114ES | DTC114S |
| Q30,33,62 | T2SA01282E | 2SA1282AE |
| Q1,2,9,10-12,25,27, 28,29,46,61 | T2SC01675L | 2SC1675 |
| Q60 | TDTA0124ES | DTA124ES |
| Q3-5,7,14,16,31,35, 39,42,44,53,57,58,40 | T2SC00945P | 2SC945P |
| Q6,38 | T2SA00733P | 2SA733P |
| Q55 | T2SA01869Z | 2SA1869 |
| Q18,19 | FM0J00310Z | F.E.T J310 |
| D3,5,7-10,13,14,20-23,27,33,34,35,37,40,53,60-65,69,75-82, 84,85,88-90,97,102, 106,107,111-141,143, 144,147,149,150, JP191 | ED1N04148Z | DIODE 1N4148 |
| D1,2,11,12,30,31 | ED1N00060P | 1N60P |
| D110 | ED1N04003Z | 1N4003 |
| D109 | ED1N04007Z | 1N4007 |
| D16,17 | EDSS00053Z | ISS53 |
| D59,72 | EDMA00027W | MA27W-A |
| D71,145 | EDMA00027T | MA27T-A |
| D18,19,42,99,100,146,148 | EDSV00251Z | SVC-251SPA |
| D70 | EDZD05519Z | 5.1V 0.5W |
| D73 | EDZD05759Z | 7.5V 0.5W |
| L2,3 | ECIFT12002 | I.FT |
| L6 | ECIFT12290 | I.F.T |
| L17,20 | ECIFT12012 | I.F.T |
| L23 | ECIFT12016 | I.F.T |
| L1 | ECIFT12252 | I.F.T |
| L44 | ECIFT12255 | I.F.T |
| L9,10 | ECIFT12256 | I.F.T |
| L15,43 | ECIFT12258 | I.F.T |
| L40 | ECIFT12262 | I.F.T |
| L14 | ECIFT12558 | I.F.T |
| L5 | ECIFT12253 | I.F.T |
| L7,42 | ECIFT12440 | I.F.T |
| L8 | ECIFT12492 | I.F.T |
| L4 | ECIFT12526 | I.F.T |
| L503,504 | ECCHK16000 | CHOKE COIL |
| T1 | ECCHK16004 | CHOKE COIL |
| L37,33 | ECCHK16070 | CHOKE COIL |
| L47 | ECCHK16176 | CHOKE COIL |
| L16 | ECCHK16246 | CHOKE COIL |
| L28 | ECSPG18003 | SPRING COIL |
| L30 | ECSPG18077 | SPRING COIL |
| L29 | ECSPG18075 | SPRING COIL |
| L31 | ECSPG18365 | SPRING COIL |
| L35 | ECSPG18001 | SPRING COIL |
| L38 | ECRFZ10048 | RF COIL |
| L13,39,41 | ECBAD18526 | BEAD COIL |
| VR16,18 | RE10200041 | S/F/R 1K |
| VR14 | RE50200042 | S/F/R 5K |
| VR1,5 | RE10300031 | S/F/R 10K |
| VR9 | RE10400043 | S/F/R 100K |
| VR4 | RE50400087 | S/F/R 500K |
| RA2 | RCS0870014 | R/ARRAY |
| RA1 | RCS0970015 | R/ARRAY |
| RA3 | RCS0670025 | R/ARRAY |
| R201-R223 | WL0007009Z | LEAD WIRE |
| R223-R198 | WL0207009Z | LEAD WIRE |
| JP1-3,4,7,9,23,24-26 ,32,33,38,39,50,54-57,59,61,62,63,65,66,71,72,79,80,82,85, 86,87,93,100,105,106,114,115,118-122,124 -126,190,135,138-140 ,144,145,152,153,156,157,159,160,128,165,166,168,170,172,174,175,177-179,181,184 ,188,125 | WX01060605 | J/W 6x5x6 |
| JP200-202,204,205, 209,211,212,214,217,219,220,224,226,231-233,235,236,238,239,242,243,245,250,252,253,255-260,262,263, 265,271-273,276,278- 280,285,267x2,R119, R305,R89,R19,C142, C291,C128,C129,D26, D46,D50,D49-L46,TP8, C133,D95 | WX01070705 | J/W 7x5x7 |
| R19,119 | WX01070706 | J/W 7x6x7 |
| D25 | WX01070708 | J/W 7x8x7 |
| JP6,11,12,16-19,34- 37,40-49,51-3,58,60, 67,70,88,96,101-104, 107-109,116,117,127, 129,133,136,137,143,147,148,151,161,167,169,176,131,132,240 | WX01060610 | J/W 6x10x6 |
| JP215,218,222,223, 225,227,228,230,234,241,244,246-249,251, 254,261,266,277,286,287,IC6,L36 | WX01070710 | J/W 7x10x7 |
| JP75-78,81 | WX01070712 | J/W 7x12x7 |
| JP99 | WX01070713 | J/W 7x13x7 |
| FL3 | WX01070715 | J/W 7x15x7 |
| TP7-TP8,TP8-TP9 | WX01070718 | J/W 7x18x7 |
| J7x2,10,17,22,Q41 | EX07N48223 | P/C/S 3P |
| J2,3,6,11,18 | EX07N48350 | P/C/S 3P |
| J21 | EX07N48490 | P/C/S 4P |
| J5,20 | EX07N48222 | P/C/S 5P |
| J13,7 | EX07N48331 | P/C/S 6P |
| J14 | EX07N48224 | P/C/S 7P |
| J1 | EX07N48543 | P/C/S 9P |
| J28 | EX07N48244 | P/C/S 3P |
| J12 | EX07N41227 | P/C/S 3P |
| J16 | EX07N41330 | P/C/S 2P |
| J28 | EX07N48151 | P/C/H |
| TP2,3,5 | EX07N48612 | P/C/S 1PIN |
| IC8 | ENTA07222A | IC TA7222AP |
| Q54 | T2SB00754Y | TR 2SB754Y |
| Q49 | T2SC02166C | TR 2SC2166C |
| Q47 | T2SC01969C | TR 2SC1969C |
| Q37 | T2SA01869Z | TR 2SA1869 |

RCI-6300F TB MISC. PARTS

| REFERENCE NUMBER | RANGER PART NO. | DESCRIPTION |
| --- | --- | --- |

| - | PT9000060K | FRONT PANEL |
| --- | --- | --- |
| - | PT9000020E | CH KNOB |
| - | PT9000070E | BAND KNOB |
| - | PT9000040E | INNER KNOB |
| - | PT9000050E | OUTER KNOB |
| - | PT2100041C | DISPLAY WINDOW |
| - | PT3600080A | SIGNAL METER HOLDER |
| - | PT2100031C | COUNT WINDOW |
| - | PT7001070C | PUSH KEY |
| - | MT9000010X | FRONT CHASSIS |
| - | MT3600040S | CHANNEL BRACKET |
| - | MT3600061X | TOP HOUSING |
| - | MT3600071N | BOTTOM HOUSING |
| - | MT3600030S | HANDLER |
| - | XZZZ90004Z | FOAM |
| - | GZZZ50000Z | CLAMP |
| - | LZZZ60001Z | SHIELD CLOTH |
| - | XZZZ90098Z | SOLDER PLATE |
| - | XZZZ90021Z | FOAM |
| - | XZZZ90064Z | INSULATING PLATE |
| - | BA0112010P | MIC PLATE |
| COUNTER | XZZZ90363Z | PVC STAND OFF |
| COUNTER | JS013016WH | SET SCREW |
| FRONT PANEL(4) | JS033008MN | SET SCREW |
| CH BKT(2), CHASSIS(12) | JS053006MN | SET SCREW |
| SPK(4) | JS053008MN | SET SCREW |
| MAIN PCB(5) | JS053006TN | SET SCREW |
| SPK(4) | JN263035ZS | NUT |
| - | XZZZ90008Z | MIC STOPPER |
| - | XZZZ90007Z | MOUNTING SCREW |
| - | JS015010WH | SET SCREW |
| - | JS013509TH | SET SCREW |
| - | JW315510CN | OUT-TOOTH WASHER |
| - | XZZZ90188Z | FIBER WASHER |
| - | HZZZ76005Z | SSSEBRIH K 905 |
| - | MT3600200X | SET CHASSIS |
| 2SB754Y | XZZZ90020Z | INSULATING PLATE |
| Q47,49 | XZZZ90003Z | INSULATING PLATE |
| Q47,49 | XZZZ90358Z | INSULATING PLATE |
| IC8 | LZZZ61008Z | IC SHIELD B |
| Q37 | JS052006MN | SET SCREW |
| Q47,49 | JS052012MN | SET SCREW |
| IC8 | JS013006MV | SET SCREW |
| - | JS052010MN | SET SCREW |
| Q47,49 | JN242012ZS | NUT |