| TR-296GK/DX |  | TABLE OF CONTENTS |
| --- | --- | --- |

|  | PAGE |
| --- | --- |
| CHAPTER 1 |  |
| SPECIFICATIONS |  |
| 1.0 | General . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 2 |
| 1.1 | Transmitter . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 2 |
| 1.2 | Receiver . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 2 |
| CHAPTER 2 |  |
| OPERATION |  |
| 2.0 | Introduction . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 3 |
| 2.1 | Control & Connections . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 3 |
| 2.1.1 | Front Panel . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 3 |
| 2.1.2 | Rear Panel . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 5 |
| 2.1.3 | Frequency Chart . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 6 |
| 2.2 | Microphone . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 7 |
| 2.3.1 | Procedure To Receive . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 7 |
| 2.3.2 | Procedure To Transmit . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 7 |
| 2.4 | Alternate Microphones And Installation . . . . . . . . . . . . . . . . . . . . . . . . | 7 |
| CHAPTER 3 |  |
| CIRCUIT DESCRIPTION |  |
| 3.0 | Introduction . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 9 |
| 3.1 | PLL Circuit . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 9 |
| 3.2 | Receiver Circuit . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 9 |
| 3.3 | Transmitter Modulation Circuit . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 9 |
| 3.4 | Transmitter Amplifier Circuit . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 9 |
| CHAPTER 4 |  |
| ALIGNMENT |  |
| 4.0 | Required Test Equipment . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 11 |
| 4.1 | Alignment Procedures . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 11 |
| 4.1.1 | PLL Alignment . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 11 |
| 4.1.2 | Transmitter Alignment . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 12 |
| 4.1.3 | Receiver Alignment . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 13 |
| CHAPTER 5 |  |
| MAINTENANCE |  |
| 5.0 | Precautions . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 16 |
| 5.1 | Periodic Inspection . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 16 |
| 5.2 | Fuse Replacement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 16 |
| CHAPTER 6 |  |
| DIAGRAMS AND PART LIST |  |
| 6.0 | PCB Layout & Part List . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | 17 |
| TR-296GK/DX |  | CHAPTER 1 SPECIFICATIONS |

| 1.0 GENERAL |  |
| --- | --- |
| Model | TR-296GK / TR-296DX (B),(C) |
| Frequency Range | 26.965 - 27.405MHz. |
| Emission Modes | AM/USB/LSB |
| Frequency Control | Phase Lock Loop (PLL) synthesizer. |
| Frequency Tolerance | ( 0.005 %. |
| Frequency Stability | ( 0.001 %. |
| Operating Temperature Range | -30(C to +50(C. |
| Microphone | Plug-in dynamic; with push-to-talk switch and coiled cord. |
| Input Voltage | 13.8V DC nominal (15%. |
| Current Drain: Transmit (AM full mod.) | <3.5A. |
| Current Drain: Receiver (Squelched) | <0.5A. |
| (Max. audio output) | <1.0A. |
| Antenna Connector | UHF, SO239. |
| Dimensions | 2-3/8”(H) x 7-7/8”(W) x 9-1/4”(D). |
| Weight | 5 lb. |
| 1.1 TRANSMITTER |  |
| RF Power Output | AM : 4W ; USB/LSB : 12W PEP |
| RF Transmit Modes | AM/USB/LSB |
| Modulation | High and low level Class B, Amplitude Modulation: AM and SSB. |
| Spurious Emissions | -55 dB. |
| Carrier Suppression | -55 dB. |
| Audio Frequency Response | 300 to 2500 Hz |
| Antenna Impedance | 50 Ohms. |
| Output Indicators | Meter shows relative RF output power, signal strength and SWR. Transmit LED glows red when transmitter is in operation. |
| 1.2 RECEIVER |  |
| Sensitivity For 10dB S/N (AM) | <0.5 (V. |
| Sensitivity For 10dB S/N (SSB) | <0.25 (V. |
| IF Frequency | AM: 10.695 MHz 1st IF, 455 KHz 2nd IF. |
| Image Rejection | -65 dB. |
| Adjacent Channel Selectivity | -60 dB. |
| RF Gain Control | 45 dB adjustable for optimum signal reception. |
| Automatic Gain Control (AGC) Figure Of Merit | 100 mV for 10 dB Change in Audio Output. |
| Squelch | Adjustable; threshold less than 0.5 (V. |
| Noise Blanker | RF type. |
| Audio Output Power | 4 watts into 8 Ohms. |
| Audio Frequency Response | AM and SSB: 300 to 2500 Hz. |
| Built-in Speaker | 8 Ohms, 5 Watts. |
| External Speaker (Not Supplied) | 8 Ohms; disables internal speaker when connected. |

(SPECIFICATIONS SUBJECT TO CHANGE WITHOUT NOTICE)

| TR-296GK/DX |  | CHAPTER 2 OPERATION |
| --- | --- | --- |

Figure 2-1 Front Panel

2.0 INTRODUCTION

This section explains the basic operating procedures for the TEXAS RANGER TR-296GK / TR-296DX mobile transceiver.

2.1 CONTROLS AND CONNECTIONS

2.1.1 FRONT PANEL

Refer to the above Figure 2-1 for the location of the following controls.

1. ON/OFF VOLUME CONTROL

Turn clockwise to apply power to the radio and to set the desired listening level.

2. SQUELCH CONTROL

This control is used to control or eliminate receiver background noise in the absence of an incoming signal. For maximum receiver sensitivity, it is desired that the control be adjusted only to the point where the receiver background noise is eliminated. Turn fully counter-clockwise, then slowly clockwise until the receiver noise disappears. Any signal to be received must now be slightly stronger than the average received noise. Further clockwise rotation will increase the threshold level which a signal must overcome in order to be heard. Only strong signals will be heard at a maximum clockwise setting.

3. RF GAIN CONTROL

This control is used to reduce the gain of the receive amplifier under strong signal conditions.

4. SWR CAL CONTROL

This SWR CAL control allows the user to calibrate the SWR meter.

5. MIC GAIN CONTROL

Adjusts the microphone gain in the transmit and PA modes. This controls the gain to the extent that full talk power is available several inches away from the microphone. In the Public Address (PA) mode, the control functions as the volume control.

6. S-RF/CAL/SWR SWITCH

In the S-RF position, the meter swings proportionally to the strength of the received signal. When transmitting, the meter indicates relative RF output power. When in the CAL position, the SWR meter can be calibrated by adjusting the SWR CAL control. When in the SWR position, the Standing Wave Ratio is measured.

7. MODE CONTROL

This control allows you to select one of the following operating modes: LSB/AM/USB.

8. CLARIFY CONTROL

Allows tuning of the receive frequency above or below the channel frequency by up to 1.5 KHz. Although this control is intended primarily to tune in SSB signals, it may be used to optimize AM signals.

9. CHANNEL SELECTOR

This control is used to select a desired transmit and receive channel.

10. FRONT PANEL METER

The Front Panel Meter allows the user to monitor signal strength, RF output power and SWR level.

11. NB/ANL/OFF SWITCH

In the ANL position, the automatic noise limiter in the audio circuits is activated. When the switch is placed in the NB/ANL position, the RF noise blanker is also activated. The noise blanker is very effective in eliminating repetitive impulse noise such as ignition interference.

12. CB/PA SWITCH

The CB is a normal operation of the radio. In the CB position, the PA function is disabled and the unit will transmit and receive on the speaker that is connected. In the PA position, the radio acts as a public address amplifier. Your voice will come out of the speaker that have plugged in to the PA. SP. jack on the rear panel. The radio does not operate when you are in the PA mode.

13. TONE HI/LO SWITCH

This switch is used to shape the tone of the received signal. In LO position, bass is increased and in HI position, treble is increased.

14. BRIGHT/DIM SWITCH

This switch controls the level of brightness for the meter lamp and channel display LED.

15. TX/RX LED

The red LED indicates the unit is in the transmit mode. The green LED indicates the unit is in the receive mode.

16. CHANNEL DISPLAY

The channel display indicates the current selected channel.

2.1.2 REAR PANEL

Figure 2-2 represent the location of the following connections:

Figure 2-2 Rear Panel

1. ANTENNA

This jack accepts 50 ohms coaxial cable with a PL-259 type connector.

2. POWER

This connector accepts 13.8V DC power cable with built-in fuse. The power cord provided with the radio has a black and red wire. The black goes to negative and the red goes to positive.

3. FREQUENCY COUNTER CONNECTOR

This F. C. connector is used for an external frequency counter which indicates the frequency of the selected channel.

4. PA. SP.

This jack is for PA operation. Before operating, you must first connect a PA speaker (8 ohms, 4W) to this jack.

5. EXT. SP.

This jack accepts 4 to 8 ohms, 5 watts external speaker. When the external speaker is connected to this jack, the built-in speaker will be disabled.

2.1.3 FREQUENCY CHART

| CHANNEL | CHANNEL FREQUENCY | CHANNEL | CHANNEL FREQUENCY |
| --- | --- | --- | --- |
| 1 | 26.965 | MHz | 21 | 27.215 | MHz |
| 2 | 26.975 | MHz | 22 | 27.225 | MHz |
| 3 | 26.985 | MHz | 23 | 27.255 | MHz |
| 4 | 27.005 | MHz | 24 | 27.235 | MHz |
| 5 | 27.015 | MHz | 25 | 27.245 | MHz |
| 6 | 27.025 | MHz | 26 | 27.265 | MHz |
| 7 | 27.035 | MHz | 27 | 27.275 | MHz |
| 8 | 27.055 | MHz | 28 | 27.285 | MHz |
| 9 | 27.065 | MHz | 29 | 27.295 | MHz |
| 10 | 27.075 | MHz | 30 | 27.305 | MHz |
| 11 | 27.085 | MHz | 31 | 27.315 | MHz |
| 12 | 27.105 | MHz | 32 | 27.325 | MHz |
| 13 | 27.115 | MHz | 33 | 27.335 | MHz |
| 14 | 27.125 | MHz | 34 | 27.345 | MHz |
| 15 | 27.135 | MHz | 35 | 27.355 | MHz |
| 16 | 27.155 | MHz | 36 | 27.365 | MHz |
| 17 | 27.165 | MHz | 37 | 27.375 | MHz |
| 18 | 27.175 | MHz | 38 | 27.385 | MHz |
| 19 | 27.185 | MHz | 39 | 27.395 | MHz |
| 20 | 27.205 | MHz | 40 | 27.405 | MHz |

2.2 MICROPHONE

The receiver and transmitter are controlled by the push-to-talk switch on the microphone. Press the switch and the transmitter is activated, release switch to receive. When transmitting, hold the microphone two inches from the mouth and speak clearly in a normal voice. The radio comes complete with a low impedance (500 ohm) dynamic microphone. For installation instructions of the microphone, see section 2.4 “ALTERNATE MICROPHONES AND INSTALLATION”.

2.3 OPERATION

2.3.1 PROCEDURE TO RECEIVE

1. Be sure that power source, microphone and antenna are connected to the proper connectors before going to the next step.

2. Turn unit on by turning VOL knob clockwise on transceiver.

3. Set the VOL to a comfortable listening level.

4. Set the MODE switch to the desired mode.

5. Listen to the background noise from the speaker. Turn the SQ knob slowly clockwise until the noise just disappears. The SQ is now properly adjusted. The receiver will remain quiet until a signal is actually received. Do not advance the control too far or some of weaker signals will not be heard.

6. Set the CHANNEL selector switch to the desired channel.

7. Set the RF GAIN control fully clockwise for maximum receive gain.

8. Adjust the CLARIFY control to clarify the SSB signals or to optimize AM signals.

2.3.2 PROCEDURE TO TRANSMIT

1. Select the desired channel of transmission.

2.  Set the MIC GAIN control fully clockwise.

3. If the channel is clear, depress the push-to-talk switch on the microphone and speak in a normal voice.

2.4 ALTERNATE MICROPHONES AND INSTALLATION

For best results, the user should select a low impedance dynamic type microphone or a transistorized microphone. Transistorized type microphones have a low output impedance characteristic. The microphones must be provided with a five-lead cable. The audio conductor and its shielded lead comprise two of the leads. The third lead is for receive control, the fourth is for grounding and fifth is for transmit control. The microphone should provide the functions shown in schematic below (Figure 2-3).

5 WIRE MIC CABLE

|  | Pin Number | Mic Cable Lead |  |
| --- | --- | --- | --- |
|  | 1 | Audio Shield |  |
|  | 2 | Audio Lead |  |
|  | 3 | Receive Control |  |
|  | 4 | Grounding |  |
|  | 5 | Transmit Control |  |

Figure 2-3 Transceiver Microphone Schematic

Figure 2-4 Microphone Plug Wiring

Figure 2-5 Microphone plug pin numbers viewed from rear of pin receptacle.

| TR-296GK/DX |  | CHAPTER 3 CIRCUIT DESCRIPTION |
| --- | --- | --- |

3.0 INTRODUCTION

This section explains the technical theory of operation for the TR-296GK / TR-296DX mobile transceiver.

3.1 PLL CIRCUIT

The Phase Lock Loop (PLL) circuit is responsible for developing the receiver’s first local oscillator signal and the transmitter’s exciter signal. The PLL circuit consists primarily of IC1, IC2, TR20, TR29 and TR30. The PLL circuit is programmed by the rotary channel switch GPS-0668. The GPS-0668 communicates the correct binary data information to the programmable divider inside of IC1. IC1 then controls the VCO (Voltage Controlled Oscillator) to oscillate on the correct frequency. This signal is fed either into the receiver’s first mixer (for receive operation) or the transmitter’s mixer (for transmit operation).

3.2 RECEIVER CIRCUIT

The incoming receive signal comes into the radio via the antenna and into the first RF amplifier, TR14. The RF signal is fed into the mixer, TR15 and then into the AM IF section of the receiver (depending on the mode of operation). The signal is then detected by either the AM detector or product detector and then fed to the audio amplifier section of the receiver and finally out to the speaker.

3.3 TRANSMITTER MODULATION CIRCUIT

(i) The transmitter modulation circuit modulates the low level RF signal from the PLL exciter circuit with the user’s audio voice signal from the microphone. The audio from the microphone is then amplified and fed into the balanced modulator circuit.

(ii) If the transceiver is in the AM mode, the AF amplifier controls the gain of the last RF amplifier which produces a true AM signal.

(iii) If the transceiver is in the SSB mode, the audio signal is mixed with 7.800MHz oscillator in IC3.

3.4 TRANSMITTER AMPLIFIER CIRCUIT

The transmitter takes the basic exciter signal from the TX mixer and amplifies it through a series of amplifiers consisting of TR39, TR38 and TR36 where it is sent out to the antenna connector.

TR-296GK/DX BLOCK DIAGRAM

| TR-296GK/DX |  | CHAPTER 4 ALIGNMENT |
| --- | --- | --- |

4.0 REQUIRED TEST EQUIPMENT

| ( DC Power Supply (13.8VDC, 10A) ( RF Wattmeter (25~60 MHz, 25W) ( Multimeter ( Automatic Modulation Meter ( Audio Signal Generator | ( Frequency Counter (100 MHz) ( RF Signal Generator (100 MHz) ( Automatic Distortion Meter ( Oscilloscope (50 MHz) ( Sinad Meter |
| --- | --- |

4.1 ALIGNMENT PROCEDURES

This transceiver has been aligned at the factory and does not require any adjustments at installation. The required test equipment listed are used for the test setup or alignment shown in Figure 4-1 Transmitter Test Setup and Figure 4-2 Receiver Test Setup. These test setup are used in part or total during the following adjustments and refer to Figure 4-3 for adjustment location.

4.1.1 PLL ALIGNMENT

| ITEM | U.U.T. SETTING | ADJUST POINT | MEASUREMENT |
| --- | --- | --- | --- |
| VCO Voltage | Set radio to CH 1, AM RX mode. Clarify setting in 12 o’clock position. Connect DC Voltmeter to TP9 (R207). Connect Oscilloscope to TP10 (R101). Connect Oscilloscope to TP1 (R106). | L19 L21 L20 | 2.5 VDC ( 0.1 CH 1 & CH 40 Max. Output and Balance. |
| AM Frequency | Set radio to CH 1, AM RX mode. Connect frequency counter to TP1 (R106). | L23 | 34.76500 MHz + 20 Hz |
| LSB Freq. | Set radio to CH 1, LSB RX mode. Connect frequency counter to TP1 (R106). | L22 | 34.76350 MHz + 20 Hz |
| USB Freq. | Set radio to CH 1, USB RX mode. Connect frequency counter to TP1 (R106). | L59 | 34.76650 MHz + 20 Hz |
| TX Frequency | Set radio to CH 1, AM TX mode. Connect frequency counter to TP1 (R106). | VR5 | 34.76500 MHz + 20 Hz |
| AM TX Freq. | Set radio to CH 19, AM TX mode. Set Mic Gain fully counter clockwise. | L31 | 27.18500 MHz + 20 Hz |
| LSB TX Freq. | Set radio to CH19, LSB TX mode. Set Mic Gain fully clockwise. AF signal 25 mV, 1 KHz to microphone. | L30 | 27.18400 MHz + 20 Hz |
| USB TX Freq. | Set radio to CH19, USB TX mode. Set Mic Gain fully clockwise. AF signal 25 mV, 1 KHz to microphone. | CT2 | 27.18600 MHz + 20 Hz |

4.1.2 TRANSMITTER ALIGNMENT

| ITEM | U.U.T. SETTING | ADJUST POINT | MEASUREMENT |
| --- | --- | --- | --- |
| BIAS Current | Set radio to CH 19, USB TX mode. MOD off. Connect current meter to TP8 (+) and green lead wire (-). Connect current meter to TP7 (+) and violet lead wire (-). | VR9 VR8 | 30 mA 50 mA |
| AM TX Power | Set radio to CH 19, AM TX mode. Connect RF power meter to antenna jack. MOD off. | L48, L47, L46, L45, L38, L36 L38 VR10 | RF Power Output MAX Balance Power between CH 1 and CH 40. 4W. |
| SSB ALC | Set radio to CH 19, USB TX mode. Set Mic Gain fully clockwise. AF signal 25 mV, 1 KHz to microphone. | VR11 | 12 W. |
| SSB Carrier Balance | Set radio to CH 19, USB TX mode. Connect Oscilloscope to L44 (TR39C). Mic Gain off. | VR4 | Spurious Emission to minimum. |
| AM Modulation | Set radio to CH 19, AM TX mode. Set Mic Gain fully clockwise. AF signal 30 mV, 1 KHz to microphone. | VR7 | 95% |
| RF Power Meter | Set radio to CH 19, AM TX mode. MOD off. | VR6 | Adjust RF Power meter needle until it is in-between the green and red bar on PWR scale. |

4.1.3 RECEIVER ALIGNMENT

| ITEM | SETTINGS | ADJUST POINT | MEASUREMENT |
| --- | --- | --- | --- |
| AM Sensitivity | Set radio to CH 20, AM RX MODE. Clarify setting in 12 o’clock. Set RF gain fully clockwise. Set SQ fully counter clockwise. Set VOL control to 2 o’clock. Set NB/ANL to OFF position. Connect RF SG to antenna jack. Frequency 27.205 MHz, Level 1 uV. MOD 30%, 1KHz. Set radio to CH 40 AM mode. RF SG setting 27.405 MHz. Set radio to CH 1 AM mode. RF SG setting 26.965 MHz. | L13, L15, L3, L4, L5, L6, L7, L8, L9, L10 | Audio output > 2V S/N > 10 dB |
| USB Sensitivity | Set radio to CH 20, USB RX mode. MOD off. Set VOL control fully clockwise. RF SG setting 27.206 MHz, Level 1 uV. | L12, L14 | Audio output > 4.5V S/N > 20 dB |
| LSB Sensitivity | Set radio to CH 20, LSB RX mode. MOD off. VOL control fully clockwise. RF SG setting 27.204 MHz, Level 1 uV. | L12, L14 | Audio output > 4.5V S/N > 20 dB |
| NB/ANL Adjust | Set radio to CH 20, AM RX mode. RF SG setting 27.205 MHz, Level 100 uV. MOD 30%, 1KHz. Set NB/ANL/OFF switch to NB/ANL. Connect Voltmeter to D2 (Cathode). | L1, L2 | DC voltage to max. ( >1.5V ) |
| AM Squelch | Set radio to CH 20, AM RX mode. Set SQ control at fully clockwise. RF SG setting 27.205 MHz, Level 1 mV. MOD 30%, 1KHz. | VR3 Slowly | Adjust very slowly until quelch just open |
| AM S/RF Meter | Set radio to CH 20 AM RX mode. MOD off. Set S-RF/CAL/SWR switch to S/RF position. RF SG setting 27.205 MHz, Level 100 uV. | VR1 | Meter needle to S9 on the S scale |
| SSB S/RF Meter | Set radio to CH 20, USB RX mode. MOD off. Set S-RF/CAL/SWR switch to S/RF position. RF SG setting 27.206 MHz, Level 100 uV | VR2 | Meter needle to S9 on the S scale |

Figure 4-1 Transmitter test setup

Figure 4-2 Receiver test setup

Figure 4-3 Main PCB Adjustment Location

| TR-296GK/DX |  | CHAPTER 5 MAINTENANCE |
| --- | --- | --- |

5.0 PRECAUTIONS

The inherent quality of the solid-state components used in this transceiver will provide many years of continuous use. Taking the following precautions will prevent damage to the transceiver.

(i) Never key the transmitter unless an antenna or suitable dummy load is connected to the antenna receptacle.

(ii) Ensure that the input voltage does not exceed 16 VDC or fall below 11 VDC.

(iii) During alignment, do not transmit for more than 10 seconds at a time. Transmitting over long periods can cause heat built-up and cause transmitter damage.

5.1 PERIODIC INSPECTION

This unit is aligned at the factory to deliver maximum performance. However, continued performance cannot be expected without periodic inspection and maintenance. Important points to be checked regularly are as follows;

| Check Item | Action |
| --- | --- |
| Whip antenna (option) | If cracked or broken, replace it. |
| Coaxial cable | If sheath is cracked, seal with vinyl tape. If immersed with water, install new coaxial cable. |
| Coaxial & power plug connections | If loosened, reconnect. If corroded, clean contacts. |
| Battery connection | If corroded, clean power terminals. |
| Ground terminal | If corroded, clean terminal. |

5.2 FUSE REPLACEMENT

To protect the equipment from serious damage, a fuse is provided on the power supply lines. The fuse protect against overvoltage / reverse polarity or internal fault of the equipment. If the fuse has blown, first find out the cause of the trouble before replacing it. A fuse rated for more than 4A should not be used, since it may permanently damage the equipment. Damage due to overfusing is not covered by the warranty.

| TR-296GK/DX |  | CHAPTER 6 DIAGRAMS & PARTS LIST |
| --- | --- | --- |

6.0 GENERAL

Information on most electrical and mechanical parts is included in the parts list. The reference designators are in alphanumeric order.

6.1 ORDERING REPLACEMENT PARTS

Parts orders should be referred to the parts department at:

( Ranger Communications, Inc.

401 W. 35th Street

National City, CA 91950

Tel: 800-446-5778

Fax: 619-426-3788

PART LIST:

TR-296GK/DX ROTARY SW. P.C.B

| ITEM | REFERENCE NUMBER | RANGER PART NUMBER | DESCRIPTION |
| --- | --- | --- | --- |
| 1 |  | EPT014831Z | ROTARY SW. P.C.B |
| 2 | ROTARY SW PCB | EWRT32059S | ROTARY SW |
| 3 | R401-R414 | RCU146814Z | 680 ohm 1/4W |
| 4 | J402 | WX01070705 | JUMPER WIRE |
| 5 | J401 | WX01070715 | JUMPER WIRE |
| 6 | J403 | WX01070712 | JUMPER WIRE |

REMARK:

SOLDER SIDE (BLUE)

PART LIST:

TR-296GK/DX MIC P.C.B

| ITEM | REFERENCE NUMBER | RANGER PART NUMBER | DESCRIPTION |
| --- | --- | --- | --- |
| 1 |  | EPT014840Z | MIC P.C.B |
| 2 | C404-C407 | CC0501027L | 0.001(F 50V |
| 3 | L404,L405 | ECBAD18558 | BEAD COIL |

REMARK:

LEFT: COMPONENT SIDE

RIGHT: SOLDER SIDE

PART LIST:

TR-296GK/DX CH DISPLAY P.C.B

| ITEM | REFERENCE NUMBER | RANGER PART NUMBER | DESCRIPTION |
| --- | --- | --- | --- |
| 1 |  | EPT014821Z | CH DISPLAY P.C.B |
| 2 | CH DISPLAY PCB | EX03N40003 | LED DISPLAY |

REMARK:

SOLDER SIDE (BLUE)

TR-296GK/DX MAIN PCB.

REMARK:

COMPONENT SIDE

TR-296GK/DX MAIN PCB.

REMARK:

COPPER SIDE

PART LIST

TR-296GK/DX MAIN PCB

| REFERENCE NUMBER | RANGER PART NO. | DESCRIPTION |
| --- | --- | --- |
|  | EPT014813Z | MAIN P.C.B |
| R208 | RCU141094Z | 1 ( 1/4W |
| R68 | RCU143394Z | 3.3 ( 1/4W |
| R181,183 | RCU141004Z | 10 ( 1/4W |
| R122 | RCU141504Z | 15 ( 1/4W |
| R62 | RCU142204Z | 22 ( 1/4W |
| R9,76,198 | RCU146804Z | 68 ( 1/4W |
| R38,51,52,55,105,108,139.186,188,190,241,501,179,189,242. | RCU141014Z | 100 ( 1/4W |
| R75,177 | RCU141514Z | 150 ( 1/4W |
| R61 | RCU141814Z | 180 ( 1/4W |
| R25,37,60,70,143,150,209,5 | RCU142214Z | 220 ( 1/4W |
| R8,15,31,191,233,184,176,3 | RCU143314Z | 330 ( 1/4W |
| R255 | RCU143914Z | 390 ( 1/4W |
| R4,57,67,117,256 | RCU144714Z | 470 ( 1/4W |
| R111,164,228,257 | RCU145614Z | 560 ( 1/4W |
| R94,199 | RCU146814Z | 680 ( 1/4W |
| R59,232 | RCU148214Z | 820 ( 1/4W |
| R20,24,33,36,48,49, 56,87,90,92,104,115,121,138,140,146,211,153,168,170,173,194, 195,222,503 | RCU141024Z | 1K ( 1/4W |
| R30,185,205 | RCU141224Z | 1.2K ( 1/4W |
| R26,64,95,74,112,135,165 | RCU141524Z | 1.5K ( 1/4W |
| R27 | RCU141824Z | 1.8K ( 1/4W |
| R41,50,97,102,103, 120,141,175,259 | RCU142224Z | 2.2K ( 1/4W |
| R7,91,144,187,210 | RCU142724Z | 2.7K ( 1/4W |
| R47,109,227 | RCU143924Z | 3.9K ( 1/4W |
| R17,28,58,88,116,134,162,197,201,235,166,1 | RCU143324Z | 3.3K ( 1/4W |
| R46,72,196 | RCU144724Z | 4.7K ( 1/4W |
| R18,40,124 | RCU145624Z | 5.6K ( 1/4W |
| R69,100,200 | RCU146824Z | 6.8K ( 1/4W |
| R44,123,147,148,160,236 | RCU148224Z | 8.2K ( 1/4W |
| R11,12,14,16,19,22, 53,65,78,89,93,237, 119,126,131,142,145,152,154,157,158,161, 203,223,238,239,132,23 | RCU141034Z | 10K ( 1/4W |
| R98,39 | RCU141234Z | 12K ( 1/4W |
| R66,79 | RCU141534Z | 15K ( 1/4W |
| R2,149,159 | RCU141834Z | 18K ( 1/4W |
| R125,128,151,156,163,202,174 | RCU142234Z | 22K ( 1/4W |
| R114 | RCU142734Z | 27K ( 1/4W |
| R73,96,129,99 | RCU143334Z | 33K ( 1/4W |
| R6,118,133,226 | RCU144734Z | 47K ( 1/4W |
| R155 | RCU145634Z | 56K ( 1/4W |
| R81,84 | RCU146834Z | 68K ( 1/4W |
| R82,83 | RCU141044Z | 100K ( 1/4W |
| R110 | RCU141544Z | 150K ( 1/4W |
| R35,54 | RCU141844Z | 150K ( 1/4W |
| R206 | RCU142744Z | 270K ( 1/4W |
| R13,85 | RCU144744Z | 470K ( 1/4W |
| R234 | RCU145644Z | 560K ( 1/4W |
| R80,127,258 | RCU141054Z | 1M ( 1/4W |
| R167 | RCM143914A | 390( 1/4W |
| R77 | RCM143324A | 3.3K ( 1/4W |
| R21 | RCM141014B | 100 ( 1/4W |
| R29,254 | RCM141514B | 150 ( 1/4W |
| R42,137 | RCM141024B | 1K ( 1/4W |
| R45 | RCM141524B | 1.5K ( 1/4W |
| R43 | RCM141824B | 1.8K ( 1/4W |
| R34,224 | RCM143324B | 3.3K ( 1/4W |
| R32 | RCM143924B | 3.9K ( 1/4W |
| R113 | RCM141034B | 10K ( 1/4W |
| R225 | RCM141044B | 100K ( 1/4W |
| R107-D53 | RCP145604Z | 56 ( 1/4W |
| R106 | RCP141514Z | 150 ( 1/4W |
| R212 | RCP141524Z | 1.5K ( 1/4W |
| R207 | RCP142724Z | 2.7K ( 1/4W |
| R101 | RCP141034Z | 10K ( 1/4W |
| R86 | RCP144734Z | 47K ( 1/4W |
| R178 | RCP121034Z | 10K ( 1/4W |
| R10 | RCP141044Z | 100K ( 1/4W |
| R193 | RCP102214Z | 220 ( 1W |
| R180 | RCP122714Z | 270 ( 1/2W |
| R169 | RCP124704Z | 47 ( 1/2W |
| R182 | RCP123314Z | 330 ( 1/2W |
| RA1 | CCS0573002 | C/ARRAY 0.001uF 5P |
| C145 | CC0500301A | 3PF 50WV |
| C130 | CC0500101A | 1PF 50WV |
| C41,47,163 | CC0500201A | 2PF 50WV |
| C38 | CC0500401A | 4PF 50WV |
| C48,65,116,125 | CC0500501A | 5PF 50WV |
| C98 | CC0500802A | 8PF 50WV |
| C131 | CC0501004A | 10PF 50WV |
| C31 | CC0501204A | 12PF 50WV |
| C68 | CC0501504A | 15PF 50WV |
| C142 | CC0502704A | 27PF 50WV |
| C1,128,85 | CC0503304A | 33PF 50WV |
| C26,86 | CC0503904A | 39PF 50WV |
| C89,147,162,207,502 | CC0504704A | 47PF 50WV |
| C127,141 | CC0508204A | 82PF 50WV |
| C88 | CC0501015A | 100PF 50WV |
| C9 | CC0508204G | 82PF 50WV |
| C15,17,45 | CC0501015G | 100P 50WV |
| C143 | CC0501815G | 180PF 50WV |
| C123,64,66 | CC0502215G | 220PF 50WV |
| C156 | CC0502715G | 270PF 50WV |
| C146,150,152 | CC0503915G | 390PF 50WV |
| C117,212 | CC0504715G | 470PF 50WV |
| C161 | CC0503315G | 330PF 50WV |
| C213 | CC0500602D | 6PF 50WV |
| C149 | CC0501015D | 100PF 50WV |
| C122 | CC0501215D | 120PF 50WV |
| C158 | CC0501815L | 180PF 50WV |
| C139,137 | CC0500591L | 0.5PF 50WV |
| C236,237 | CC0503315L | 330PF 50WV |
| C155,192,195,111 | CC0251047L | 0.1uF 25WV |
| C93,96,97,106,112, 113,114,119,120,126,129,164,198,199,40 | CC0501037L | 0.01uF 50WV |
| C8,11,14,35,37,39,42,5,43,44,170,185,208,201,202 | CC0501027L | 0.001uF 50WV |
| C3,4,6,7,16,22,27,50,51,52,53,54,61,83, 87,124,196,197,204, 215,227,229,2 | CC0502237L | 0.022uF 50WV |
| C188 | CC0504737L | 0.047uF 50WV |
| C32,34,140,151,171, 157,160,165,169,200,223,224,30,138,167, 166,168,159 | CC0504725T | 0.0047uF 50WV |
| C194 | CCM254737I | 0.047uF 50WV |
| C36,77,79,82,177,183,187,136 | CM0501045Z | 0.1uF 50WV |
| C76,78,107,110,118 | CM0501035Z | 0.01uF 50WV |
| C70,71,178 | CM0501024Z | 0.001uF 50WV |
| C21,46,49,55,58,182,63 | CM0502235Z | 0.022uF 50WV |
| C19,56,59,60,75,225,235,91,94 | CM0504735Z | 0.047uF 50WV |
| C69,105 | CM0502225Z | 0.0022uF 50WV |
| C102 | CM0504725Z | 0.0047uF 50WV |
| C132 | CE0502257H | 2.2uF 50V |
| C23,25,108,135,230, 231 | CE050474Z | 0.47uF 50WV |
| C33,134,144,174,191,505 | CE0501057Z | 1uF 50WV |
| C99,232 | CE0502257Z | 2.2uF 50WV |
| C24,92,180 | CE0504757Z | 4.7uF 50WV |
| C181,133,173 | CE0251067Z | 10uF 25WV |
| C73,109 | CE0252267Z | 22uF 25WV |
| C95,153,154,176 | CE0164767Z | 47uF 16WV |
| C18 | CE0163377Z | 330uF 16WV |
| C84,175 | CE0161087Z | 1000uF 16WV |
| C172 | CE0251087Z | 1000uF 25WV |
| C186 | CE0162277Z | 220uF 16WV |
| C101 | CT0161046Z | 0.1uF 16WV |
| C10 | CT0162246Z | 0.22uF 16WV |
| C29,90,104 | CT0164746Z | 0.47uF 16WV |
| C62,67 | CT0161056Z | 1uF 16WV |
| C80,81 | CT0162256Z | 2.2uF 16WV |
| C103 | CT0161066Z | 10uF 16WV |
| C100,179 | CT0162266Z | 22uF 16WV |
| C72 | CT0163366Z | 33uF 16WV |
| C74 | CT0164766Z | 47uF 16WV |
| J401,J402 | EX06N41045 | EAR JACK 3.5mm |
| IC3 | ENMA00612Z | I.C AN-612 7PIN |
| IC5 | ENSM06130Z | I.C TDA6130 14PIN |
| IC1 | ENRG871997 | I.C 8719 18PIN |
| IC2 | ENNOHIC070 | I.C UHIC070 |
| TR14 | T2SC01674L | TR2SC1674L |
| TR1,2,9,11,15,17,20,29,30,32,34 | T2SC01675L | TR 2SC1675L |
| TR4,5,6,8,10,12,19, 21,22,23,24,26,31,33,35,42,43,52,53 | T2SC00945P | TR 2SC945P |
| TR7,13,25,27,47,48 | T2SA00733P | TR 2SA733P |
| TR3,18 | T2SC01906Z | TR2SC1906 |
| TR28,37 | T2SC01846Z | TR 2SC1846 |
| TR39 | T2SC02538Z | TR 2SC2538 |
| TR16 | T2SC01675K | TR 2SC1675K |
| FET1 | F3SK00085B | F.E.T 3SK85B |
| FET3 | F2SK00192R | F.E.T 2SK192A-GR |
| FET2 | F2SK00192L | F.E.T 2SK192ABL |
| X2 | EYCAB10240 | CRYSTAL 10.240MHZ |
| X4 | EYCAM07800 | CRYSTAL 7.800MHZ |
| X1 | EYCAE07345 | CRYSTAL 7.3455MHZ |
| X3 | EYCAL11325 | CRYSTAL 11.325MHZ |
| FL1 | EFCFW455HT | C/FILTER CFW-455HT |
| FT2 | EFX2078002 | C/FILTER 7.800MHZ |
| FT3 | EFX27Z22C9 | C/FILTER 7.800MHZ |
| D44 | EDZD05180Z | ZENER DIODE UZ-18V 0.5W |
| D3,5,6,7,8,9,11,14, 15,16,17,18,19,20,23,24,31,32,33,34,36, 37,38,39,40,41,42,43,47,48,51,58,59,60, 61,62,63,65,66,67,68,76,77,R107-TP2 | ED1N04148Z | DIODE 1N4148 |
| D2,10,21,22,45,46,54,71,1,73,79 | ED1N00060P | DIODE 1N60P |
| D12,13 | EDMA00859Z | DIODE MA859 |
| D55,78 | ED1N04003Z | DIODE 1N4003 |
| D52,75 | EDMA00027W | DIODE MA27W-A |
| L1 | ECIFT12366 | I.F.T |
| L2 | ECIFT12367 | I.F.T |
| L3 | ECIFT12248 | I.F.T |
| L4 | ECIFT12369 | I.F.T |
| L5 | ECIFT12005 | I.F.T |
| L6 | ECIFT12006 | I.F.T |
| L7 | ECIFT12372 | I.F.T |
| L8 | ECIFT12373 | I.F.T |
| L9 | ECIFT12374 | I.F.T |
| L10 | ECIFT12375 | I.F.T |
| L12 | ECIFT12376 | I.F.T |
| L13 | ECIFT12377 | I.F.T |
| L14 | ECIFT12378 | I.F.T |
| L15 | ECIFT12379 | I.F.T |
| L19 | ECIFT12380 | I.F.T |
| L20 | ECIFT12381 | I.F.T |
| L21 | ECIFT12382 | I.F.T |
| L22 | ECIFT12383 | I.F.T |
| L23 | ECIFT12384 | I.F.T |
| L30 | ECIFT12385 | I.F.T |
| L31 | ECIFT12161 | I.F.T |
| L45 | ECIFT12387 | I.F.T |
| L46 | ECIFT12015 | I.F.T |
| L47 | ECIFT12389 | I.F.T |
| L48 | ECIFT12390 | I.F.T |
| L59 | ECIFT12391 | I.F.T |
| L35,37 | ECSPG18200 | SPRING COIL |
| L34,41 | ECRFZ10053 | TDK BRAND CORE |
| L36 | ECRFZ10115 | RF COIL0 |
| L44 | ECRFZ10116 | RF COIL 50UH |
| L38 | ECRFZ10001 | RF COIL 0.23UH |
| L39,DCx2 | ECCHK16000 | CHOKE COIL 0.47UH |
| L16,33 | ECCHK16002 | CHOKE COIL 100UH |
| L17,27,28,29,32,57, 58,60 | ECCHK16003 | CHOKE COIL 470UH |
| L24,25,26 | ECCHK16089 | CHOKE COIL 220UH |
| L42 | ECCHK16158 | CHOKE COIL 1UH |
|  | ECCHK16159 | CHOKE COIL 5.6UH |
| L51,52 | ECBAD18504 | BEAD COIL 3.5x6X1.2 |
| l40,43,49 | ECBAD18506 | BEAD COIL 3.5x6x1.2 |
| CT2 | CV050200AZ | TRIMMER/C 20PF 5Q |
| VR3,7,9,8 | RE10200003 | 1K ( L |
| VR1,2,5 | RE30200019 | 3K ( L |
| VR10 | RE50200006 | 5K ( |
| VR4,11 | RE10300009 | 10K ( L |
| VR6 | RE10400020 | 100K ( L |
| T1 | ETP2820101 | TRANSFORMER EI-28 |
| C148-TP8 | WK0519017F | SHIELD WIRE |
| D510-TP7 | WK0719017F | SHIELD WIRE |
| J41 | WX01070705 | JUMPER WIRE |
| J12,J42,L501 | WX01070706 | JUMPER WIRE |
| J10,13,17,21,28,29, 32,35,44 | WX01070708 | JUMPER WIRE |
| J4,6,8,18,27,34 | WX01070710 | JUMPER WIRE |
| J24 | WX01070712 | JUMPER WIRE |
| J30 | WX01070709 | JUMPER WIRE |
| J5,9,16,26,33,38 | WX01070713 | JUMPER WIRE |
| J31,37,40 | WX01070715 | JUMPER WIRE |
| J1,7 | WX01070718 | JUMPER WIRE |
| J2,11,15,19,25 | WX01070720 | JUMPER WIRE |
| J14 | WX01070722 | JUMPER WIRE |
| J3,43 | WX01070723 | JUMPER WIRE |
| J39 | WX01070727 | JUMPER WIRE |
| B-B | WL0408009Z | LEAD WIRE |
| R130-VR7(H) | WL1212009Z | LEAD WIRE |
| N-N | WL0316009Z | LEAD WIRE |
| K-K | WL0517009Z | LEAD WIRE |
| C184-A | WL0814009Z | LEAD WIRE |
| A-A | WL0916009Z | LEAD WIRE |
| C-D44 | WL0017009Z | LEAD WIRE |
| E-C148 | WL0620009Z | LEAD WIRE |
| M-M | WL0120009Z | LEAD WIRE |
| I-I | WL0421009Z | LEAD WIRE |
| O-O | WL0217009Z | LEAD WIRE |
| D-D | WL0125009Z | LEAD WIRE |
| J-J | WL0725009Z | LEAD WIRE |
| MAIN | WP0818005Z | SHIELD WIRE |
| MAIN | WP0923005Z | SHIELD WIRE |
| TP7,8 | GZZZ50145Z | PIN |
| D35,69(COPPER SIDE) | EDHU00200Y | DIODE(SMD) |
| R502(COPPER SIDE) | RCP146804Z | 68 ( 1/4W |
| MAIN(COPPER SIDE) | WP0812005Z | SHIELD WIRE |
| FREQ. COUNTER | EX07N48793 | WIRE CONN/H |
| DCx1 | CC0501027L | 0.001uF 50WV |
| DCx1 | CC0501037L | 0.01uF 50WV |
| DCx1 | CC0502237L | 0.022uF 50WV |
| D49 | EDNV00001Z | DIODE NVS-01 |
| D50 | EDNV00002Z | DIODE NVS-02 |
| IC4 | ENFU03756Z | IC MB3756 |
| IC6 | ENTA07222A | IC TA7222AP |
| TR36 | T2SC01969C | TR 2SC1969C |
| TR38 | T2SC02166C | TR 2SC2166C |
| TR41 | T2SD01135Z | TR 2SD1135 |