Alumast Aluminium Alloy

Masting System

Installation Instructions

TABLE OF CONTENTS

Specifications	1

Brief Description	1

Preparation/Ground Installation	2-3

Mast section Assembly 	4

Top Plate Assembly	5

Rotor Mount Assembly 	5

Mast Assembly 	5

Parts Lists 	6-11

DIAGRAMS:

1.	Erection Guide part 1	ALU-1

2.	Erection Guide part 2	ALU-2

3.	Erection Guide part 3	ALU-3

4.	Guy Radius………………………………………………………….ALU-4

ALUMINIUM LATTICE

MAST SYSTEM

SPECIFICATIONS

Dimensions:	3050mm (10’) long sections

giving optional heights of 10’-200’

Face width  375 (1’ 2-1/4”)

Section weight:	11.8Kg

Materials:	High grade Aluminium Alloy

Using Stainless Steel Nuts/Bolts

Finish:	Natural or Painted to Specification

## BRIEF DESCRIPTION

Alumast  is a lattice aluminium  guyed masting system, designed for ultimate flexibility in design, manufacture and installation.

The system comprises high quality extrusions in high grade 6082 TF aluminium alloy, using stainless steel bolts and all galvanised steel guys and guy fittings. The design allows low volume, high-density packing specifications, for ease of shipping, and inland transportation (especially for remote sites).

Note: Before Starting the installation carefully unpack and identify the parts against parts list on drawing supplied.

GROUND INSTALLATION

- Prepare concrete foundations as FIG.1. Ensure that the surface of the concrete is level in both directions. It is important to allow concrete to harden for about three days.

| MAST HEIGHT | DIM ‘A’ | DIM ‘B’ | CUBIC CONCRETE VOLUME |
| --- | --- | --- | --- |
| 30’ | 0.8M | 0.8M | 0.32M |
| 40’ | 0.8M | 0.8M | 0.32M |
| 50’ | 0.8M | 0.8M | 0.32M |
| 60’ | 0.8M | 0.8M | 0.32M |
| 70’ | 0.8M | 0.8M | 0.32M |
| 80’ | 0.8M | 0.8M | 0.32M |
| 90’ | 0.8M | 0.8M | 0.32M |
| 100’ | 0.9M | 0.9M | 0.405M |
| 120’ | 0.9M | 0.9M | 0.405M |
| 140’ | 1.0M | 1.0M | 0.50M |
| 160’ | 1.1M | 1.1M | 0.605M |
| 180’ | 1.1M | 1.1M | 0.605M |
| 200’ | 1.2M | 1.2M | 0.72M |

FIG.1

B)	Ensure that the base mounting surface is level in both directions otherwise the Alumast will not erect vertical.

C)	The foundation should be concreted in position using the mast  and mast base plate as template. See FIG.2 below.

Note:     It is important to ensure that the three-hair pin anchors (item 8) are concreted in line with the three corners on the mast base.

D)	Install the hairpin anchors at 120 degrees in plan to base and to a distance stated on the drawing supplied (dependant on height).

FIG.2

MAST SECTION ASSEMBLY

- Assemble the leg sections with the yellow leg (colour coded top end) to the left of the red leg and the blue leg to the right of the red leg, ensuring the diagonals are fitted on the outside starting at the base (plain end), see FIG.3. Attach in position with steps, securing loosely using M6 bolts, nuts and washers. Tighten all bolts securely.

- Continue to assemble remaining sections as operation A.

## TOP MAST PLATE & ROTOR PLATE ASSEMBLY

TOP PLATE ASSEMBLY

- Assemble support rails to mast legs using M10 bolts.

- Attach top plate to support rails using M6 bolts.

- Assemble top plate tube clamps to top plate using M8 bolts.

## Assemble guy brackets to mast legs using M10 bolts.

- Slide guy bush through thimble of guy assembly and assemble to guy bracket using M10X50 bolts

## ROTOR MOUNT ASSEMBLY

- Assemble one rotor support rail (coded blue) to corresponding blue mast leg and two remaining support rails to mast legs using M6 bolts.

NOTE: It will be required to remove exhisting fitted M6 bolts attaching diagonals to enable support rails to be fitted on all 3 sides.

- Assemble rotor support plate to rails using M6 bolts. Assemble rotor tube clamp to plate using M8 bolts.

Parts Identification

## ALUMAST 10’ SECTION – P/N 050037500

| REF | p/no | description | Qty |
| --- | --- | --- | --- |
| 1 | 290102000 | alumast main leg red | 1 |
| 2 | 290102100 | alumast main leg yellow | 1 |
| 3 | 290102200 | alumast main leg blue | 1 |
| 4 | 290102300 | alumast diagonal | 24 |
| 5 | 290102400 | alumast coupler | 3 |
| 6 | 290102500 | alumast step | 8 |
| 7 | 507026000 | screw m6X20 hx hd ST/st | 47 |
| 8 | 507036100 | screw m10X25 hx hd ST/st | 27 |
| 9 | 607010600 | nut full m6 st/st | 47 |
| 10 | 607011000 | nut full m10 st/st | 27 |
| 11 | 681200600 | washer m6 flat st/st | 47 |
| 12 | 681201000 | washer m10 flat st/st | 27 |
| 13 | 691200600 | washer m6 s/coil spring | 47 |
| 14 | 691201000 | washer m10 s/coil spring | 27 |

## ALUMAST FIXED BASE– P/N 050037700

| REF | p/no | description | Qty |
| --- | --- | --- | --- |
| 1 | 290200804 | alumast BASE CLAMPING PLT | 3 |
| 2 | 300100500 | alumast TRIANGULAR PLATE | 1 |
| 3 | 495048504 | RAG BOLT M16x200 MS GALV | 3 |

ALUMAST HINGED BASE – P/N 050037600

| REF | p/no | description | Qty |
| --- | --- | --- | --- |
| 1 | 290102600 | L/H HINGE PIVOT | 2 |
| 2 | 290102700 | L/H BASE HINGE PIVOT | 2 |
| 3 | 290102800 | R/H HINGE PIVOT | 2 |
| 4 | 290102900 | R/H BASE HINGE PIVOT | 2 |
| 5 | 290200804 | alumast BASE CLAMPING PLATE | 3 |
| 6 | 300100500 | alumast TRIANGULAR BASE | 1 |
| 7 | 407041600 | BOLT M12x50 HX HD ST/ST | 2 |
| 8 | 495042404 | RAGBOLT M12x100 MS GALVANISED | 2 |
| 9 | 495048504 | RAGBOLT M16x200 MS GALVANISED | 3 |
| 10 | 507036200 | SCREW M10x30 HX HD ST/ST | 4 |
| 11 | 607011000 | nut full m10 st/st | 4 |
| 12 | 607012000 | NUT FULL M12 ST/ST | 2 |
| 13 | 681201000 | Washer m10 flat st/st | 4 |
| 14 | 681201200 | WASHER M12 FLAT ST/ST | 2 |
| 15 | 691201000 | washer m10 s/coil spring | 4 |
| 16 | 691201200 | WASHER M12 S/COIL SPRING | 2 |

ALUMAST HEAD PLATE TP-1 – P/N 050037800

| REF | p/no | description | Qty |
| --- | --- | --- | --- |
| 1 | 050038500 | MAST TUBE CLAMP MODIFIED | 1 |
| 2 | 102204969 | ALUMINIUM TUBE | 1.5M |
| 3 | 283277800 | TUBE INSERT | 1 |
| 4 | 290103100 | ALUMAST SUPPORT RAIL | 3 |
| 5 | 290103200 | ALUMAST ROTOR MOUNTING | 1 |
| 6 | 507026000 | SCREW M6x20 HX HD ST/ST | 3 |
| 7 | 507036100 | SCREW M10x25 HX HD ST/ST | 6 |
| 8 | 607000800 | NUT FULL M8 ST/ST | 4 |
| 9 | 607010600 | NUT FULL M6 ST/ST | 3 |
| 10 | 607011000 | NUT FULL M10 ST/ST | 6 |
| 11 | 681200600 | WASHER M6 FLAT ST/ST | 3 |
| 12 | 681200800 | WASHER M8 FLAT ST/ST | 4 |
| 13 | 681201000 | WASHER M10 FLAT ST/ST | 6 |
| 14 | 691200600 | WASHER M6 S/COIL ST/ST | 3 |
| 15 | 691201000 | WASHER M10 S/COIL ST/ST | 6 |

ALUMAST ROTOR MOUNTING PLATE – P/N 050037900

| REF | p/no | description | Qty |
| --- | --- | --- | --- |
| 1 | 290103200 | ALUMAST ROTOR MOUNTING PLATE | 1 |
| 2 | 290103700 | ALUMAST SUPPORT RAIL | 2 |
| 3 | 290103900 | ALUMAST SUPPORT RAIL (BLUE LEG) | 1 |
| 4 | 507026000 | SCREW M6x20 HX HD | 9 |
| 5 | 607000800 | NUT FULL M8 ST/ST | 4 |
| 6 | 607010600 | NUT FULL M6 ST/ST | 9 |
| 7 | 681200600 | WASHER M6 FLAT ST/ST | 9 |
| 8 | 681200800 | WASHER M8 FLAT ST/ST | 4 |
| 9 | 691200600 | WASHER M6 S/COIL SPRING | 9 |
| 10 | GC-038B | MAST CLAMP | 1 |

## GUY ANCHOUR BRACKETS  GB-1    - P/N 050038000

| REF | p/no | description | Qty |
| --- | --- | --- | --- |
| 1 | 290103300 | GUY BRACKET | 3 |
| 2 | 290103100 | SUPPORT RAIL | 3 |
| 3 | 407036600 | BOLT M10x50 ST/ST | 3 |
| 4 | 607011000 | NUT FULL M10 ST/ST | 3 |
| 5 | 290103600 | GUY BRACKET BUSH | 3 |
| 6 | 691201000 | WASHER M10 S/COIL | 3 |

## GUY ANCHOUR BRACKETS  GB-2    - P/N 050038100

| REF | p/no | description | Qty |
| --- | --- | --- | --- |
| 1 | 290103400 | GUY BRACKET | 3 |
| 2 | 290103100 | SUPPORT RAIL | 3 |
| 3 | 407036600 | BOLT M10x50 ST/ST | 3 |
| 4 | 607011000 | NUT FULL M10 ST/ST | 3 |
| 5 | 290103600 | GUY BRACKET BUSH | 3 |
| 6 | 691201000 | WASHER M10 S/COIL | 3 |

## ALUMAST CABLE SUPPORT CLAMP

| REF | p/no | description | Qty |
| --- | --- | --- | --- |
| 1 | 283200400 | CABLE CLAMP POLYMID | 3 |
| 2 | 547026100 | SCREW M6x25 PAN HD SLTD | 3 |
| 3 | 607010600 | NUT FULL M6 FLAT ST/ST | 3 |
| 4 | 681200600 | WASHER M6 FLAT ST/ST | 3 |
| 5 | 691200600 | WASHER M6 S/COIL | 3 |