Operating instructions DM8000/SL55

The “auxiliary” button on the side of the radio is used to toggle between encrypted and clear speech modes.

- Hold the “auxiliary” button down and a ‘low’ tone will be heard, this indicates that the radio is in clear mode.

- Hold the “auxiliary” button down and a ‘high’ tone will be heard, this indicates that the radio is in secure mode.

- During ‘clear’ mode transmissions the receiving party will hear a beep tone; this indicates that the transmission is unsecure.

- A secure transmission to a radio listening in ‘clear’ mode will force the receiving radio into ‘secure’ mode and vice-versa, a pip tone will be heard indicating unsecure transmissions.

- In the event of a physical ‘compromise’ then the radio digital code can be erased. This is done by holding down the “auxiliary” and “squelch confidence” buttons simultaneously, a two-tone warning will be heard, after 4 seconds the key code is erased. This should only be done in extreme circumstances, as the radio then has to be returned to HQ to be ‘revived’ and re-programmed.

SMC 1st June 2002.