ASSEMBLY INSTRUCTION

TFD SERIES ANTENNA

1.	When a site has been selected, remove the antenna from its packing.

2.	Remove both fibreglass spreaders from the element assemblies taking care not to misplace the spring pins.

3.	Lay out the antenna element assemblies onto the ground.

Carefully remove the cable ties, securing one of the coiled copper wires and fully unwind removing all twists.

Continue this operation on the remaining three copper coils.

4.	Re-assemble the fibreglass spreaders to the antenna elements.

5.	Assemble the load housing and balun transformer to the antenna elements.

Attach the cable assembly to the balun transformer.

6.	The antenna is now ready for installation.

Note:	Care should be taken during installation not to kink or damage the copper wire.