3 3/4 DIGITAL MULTIMETER OPERATION MANUAL

1.SPECIFICATIONS

1.1 GENERAL SPECIFICATIONS

Display            : 3 3/4 digit LCD with a max reading of 3999.

Polarity            : Automatic negative polarity indication.

Sampling rate       :3 times/second

Measuring Method   : dual-slope A/D converter

Over range indication : Only the MSD “OL” displays.

Low battery indication : The “ ” displays.

Safety standards     :  EMC/LVD. The meter is up to the standards of IEC1010 Pollution Degree 2, Over voltage categoryⅡor double insulationⅡ.

Operating environment:

Temperature 0℃ to 40℃, humidity<80%RH.

Storage environment : Temperature -10℃ to 50℃, humidity<80%RH.

Power        : Single, standard 9 volt battery. NEDA 1604IEC6F22

Dimension         : 155mm (H)X90 mm (W)X48mm (D)

Weight            : Approx. 270g(including battery)

Accessories        :Operating Manual, Conform Card, 9V Battery (Zinc-Carbon type), Test Leads (Red & Black 1 Pair), shock-proof cover, Gift box, etc.

1.2 ELECTRICAL SPECIFICATIONS

Accuracy is ±(percentage of reading + number of digit) at 23±5℃,<75%RH.

DC Voltage

| Range | Accuracy | Resolution |
| --- | --- | --- |
| 400mV | ±(0.5%+4d) | 0.1mV |
| 4V |  | 1mV |
| 40V |  | 10mV |
| 400V |  | 100mV |
| 1000V | ±(1.0%+4d) | 1V |

Impedance：400mV range: more than 100M

V-1000V range:10M

Overload protection: 1000V DC/700VAC rms

AC Voltage

| Range | Accuracy | Resolution |
| --- | --- | --- |
| 4V | ±(0.8%+6d) | 1mV |
| 40V |  | 10mV |
| 400V |  | 100mV |
| 700V | ±(1.0%+6d) | 1V |

Impedance： 10M

Overload protection: 1000VDC/700VAC rms

Frequency response：700V range: 40-100Hz

4V-400Vrange: 40-400Hz

indication: Average ( rms of sine wave)

Resistance

| Range | Accuracy | Resolution |
| --- | --- | --- |
| 400Ω | ±(0.8%+5d) | 0.1Ω |
| 4kΩ | ±(0.8%+4d) | 1Ω |
| 40kΩ |  | 10Ω |
| 400kΩ |  | 100Ω |
| 4MΩ |  | 1kΩ |
| 40MΩ | ±(1.2%+5d) | 10kΩ |

Open circuit voltage: 400mV

Overload protection：250V DC/AC RMS

DC Current

| Range | Accuracy | Resolution |
| --- | --- | --- |
| 40mA | ±(0.8%+6d) | 10uA |
| 400mA |  | 100uA |
| 10A | ±(1.2%+10d) | 10mA |

Max measuring voltage: full scale mA range: 4V; A range: 100mV.

Max input current: 10A

Overload protection：FAST 0.5A/250V fuse, 10A /250V fuse.

AC Current

| Range | Accuracy | Resolution |
| --- | --- | --- |
| 40mA | ±(1.0%+6d) | 10uA |
| 400mA |  | 100uA |
| 10A | ±(2.0%+15d) | 10mA |

Max measuring voltage: full scale mA range: 4V; A range: 100mV.

Max input current: 10A (max. 15 second)

Overload protection：FAST 0.5A/250V fuse, 10A/250V fuse.

Frequency response：40-400mA range: 40-400Hz

10A range: 40-100Hz

Capacitance

| Range | Accuracy | Resolution |
| --- | --- | --- |
| 4nF | ±(2.5%+6d) | 1pF |
| 40nF |  | 10pF |
| 400nF | ±(3.5%+8d) | 100pF |
| 4uF |  | 1nF |
| 40uF |  | 10nF |
| 200uF | ±(5%+8d) | 100nF |

Overload protection：250V DC/AC RMS

Diode and Continuity Test

| Range | Description | Test Condition |
| --- | --- | --- |
|  | Display read approx. forward voltage of diode | Forward DC Current approx. 0.5mA . Reversed DC voltage approx. 1.5V |
|  | Buzzer sounds if resistance Between terminals V/Ωand COM is less than about 50Ω. | Open voltage approx. 0.5V |

Overload Protection: 250VDC/AC RMS

Warning: Do not input voltage.

Frequency

| Range | Accuracy | Resolution |
| --- | --- | --- |
| 100Hz | ±(0. 1%+4d) | 0.01Hz |
| 1000Hz |  | 0.1Hz |
| 10kHz |  | 1Hz |
| 100kHz |  | 10Hz |
| 1MHz |  | 100Hz |
| 30MHz |  | 10kHz |

Input sensitivity: 0.7V

Overload Protection: 250V DC/AC RMS

2. FRONT PANEL DESCRIPTION

1. LCD

2. REL key

3. DC/AC Key

4. FUNCTION/RANGE Switch

5. V/Hz/CxInput Jack Terminal

6. COM Input Jack Terminal

7. Less Than 400mA Input Jack Terminal

8. 10A Input Jack Terminal

3.OPERATION

1.The mark, or sign next to the lead jacks, is for warning that the input voltage or current should not exceed the indicated values.

This is to prevent from damaging the internal circuits.

2.The function switch should be set to the range that you want to test before operation.

3.1 DC and AC Voltage measurement

1) Connect the BLACK test lead to “COM” jack and RED test lead to “VΩHz Cx” jack.

2) LCD displays “AUTO” for auto range.

3) Set the FUNCTION switch to desired V position

4) Press the "DC/AC" to select DC/AC measure mode.

5) Connect the probes across the source or load under measurement. Measuring value will be displayed on screen.

Note:

1).     :Do not apply more than DCV1000V/ACV700Vrms to the input. Indication is possible at higher voltages but there is danger of damaging the internal circuit.

2) Be careful when measuring high voltage.

3.2 DC and AC Current measurement

- Connect the BLACK test lead to “COM” jack and RED test lead the “mA” or “10A” jack.

- LCD displays “AUTO” for auto range.

3) Set the FUNCTION switch to desired current position.

4) Press the "DC/AC" to select DC/AC measure mode.

5) Connect the probes in series with the current source to be measured. Measurement value will be displayed on screen.

Note:

:The max input current is 400mA or 10A depending upon the jack used.

Excessive current will blow the fuse so and must be replaced.

3.3 Resistance measurement

1) Connect the BLACK test lead to “COM” jack and RED test lead the “VΩHz Cx” jack.

2) Set the FUNCTION Switch to desired resistance position.

3) Connect the probes across circuit to be tested.

4) It is Auto range, than display “AUTO”.

Caution: Ensure that the circuit to be tested is “dead”.

5) To measure small resistance, should short two test leads and press "REL" key.

6) Connect the test leads to measuring points and read the displayed value without counting leads resistance.

Note:

- When the input is not connected, i.e. at open circuit, the figure "OL" will be displayed over   range condition.

- When checking in-circuit resistance, be sure the circuit under test has all power removed and all capacitance has fully discharged.

- Do not input voltage.

3.4 Capacitance measurement

- Set the FUNCTION switch to desired “—││— position .

- If it s Auto range,  "AUTO" will display.

3) Press “REL” once to adjust to zero.

4) Use the probes to connect the test capacitor to "COM" jack and " VΩHz Cx" jack , measure value will be displayed on screen.

Note:

1) Before measuring, press "REL" once, to ensure that accuracy of the test value.

2)     : Do not connect an external voltage or a charged capacitor (especially larger capacitors) to the measuring terminals. Capacitors should be discharged before insert into Cx socket.

3.5 Diode and continuity Test

1) Connect the BLACK test lead to “COM” jack and RED test lead the “VΩHz Cx” jack..

(Note: The polarity of the red test probe is “+”).

- Set the FUNCTION switch to “   ” position. Press " DC/AC " key which select diode measure method.

3) Forward measure: Connect RED test lead to the positive of the test diode, BLACK test lead to the negative, then, reading of approx. forward voltage of this diode displays.

4) Reverse measure: Connect BLACK test lead to the positive of the test diode, RED test    lead to the negative, the mark "OL" will be displayed.

5) Proper diode testing should include both steps.

6) Press "DC/AC" to select continuity mode.

7) Connect the test probes to two points of circuit, if the resistance is lower than approx. 50Ω. Buzzer sounds.

3.6 Frequency measurement

1) Connect test leads or shield cable to “COM” and “VΩHz Cx” jack.

2) Set the FUNCTION switch to the “Hz” range, and connect test leads or cable across the source load under test.

Note:

1) Do not apply more than 250V DC/ACrms to the input. Indication is possible at voltage higher than 10VACrms, but readings may be out of specification.

2) In noisy environment, it is preferable to use shield cable for measuring small signal.

3) Be careful when measurement high voltage.

3.7 Auto power off and sleep mode

1) Stop working after 15min, instrument is auto off.

2) First, press "REL" key, the instrument is opened again.

4. WARNING

1) When measuring voltage ensure that instrument is not connected or switched to a current or resistance range, or to the diode check. Always ensure that the correct terminals are used for the type of measurement to be made.

2) Use extreme care when measuring voltage above 50V, especially from sources where high energy is existed.

3) Avoid making connections to “live” circuits whenever possible.

4) When making current measurements ensure that the circuit is not “live” before opening it in order to connect the test leads.

5) Before making resistance measurements or diode test, ensure that the circuit under test is de-energized.

6) Always ensure that the correct function and range is selected. If in doubt about the correct range to use, start from the highest and work downwards.

7) Extreme care should be taken when using the instrument to conjunction with a current   transformer connected to the terminals if an open circuit occurs.

8) Ensure that the test leads and probes are good condition with no damage to the insulation.

9) Take care not to exceed the over-load limits as given in the specification.

10) FUSE FOR REPLACEMENT MUST BE OF THE CORRECT TYPE AND RATING.

11) Before opening the case of the instrument to replace battery or fuse, disconnect the test leads from any external circuit, set the selector switch to “OFF” position.

5. CARE AND MAINTENANCE

5.1Care for your multimeter

Your Digital Multi-meter is an example of superior design and craftsmanship. The following suggestions will help you care for the multi-meter so you can enjoy it for year.

- Keep the multimeter dry. If it gets wet, wipe it dry immediately. Liquids can contain minerals that can corrode electronic circuits.

- Use and store the multi-meter only in normal temperature environments. Temperature extremes can shorten the life of electronic devices, damage batteries, and distort or melt plastic part.

- Handle the multimeter gently and carefully. Dropping it can damage the circuit boards and case and can cause the multi-meter to work improperly although the holster can provide enough protection.

- Keep the multi-meter away from dust and dirt, which can cause premature wear of parts.

- Wipe the multi-meter with a damp cloth occasionally to keep it looking new. Do not use harsh chemicals, cleaning solvents, or strong detergents to clean the multi-meter.

- Use only fresh battery of the required size and type. Always remove old or weak batteries.

They can Leak chemicals that destroy electronic circuits.

5.2 Maintenance

1) 9-Volt battery replacement

a. Ensure the instrument does not connected to any external circuit. Set the selector switch to OFF position and remove the test leads from terminals.

b. Remove the screw on the bottom case and lift the bottom case.

c. Remove the spent battery and replace it with a battery of the same type.

2) Fuse replacement

a. Ensure the instrument does not connected to any external circuit. Set the selector switch to OFF position and remove the test leads from terminals.

b. Remove the screw on the bottom case and lift the bottom case.

c. Replace the fuse with same type and rating fuse or as the replacements.

VC96A