XR5450, XR5550 Subject EXTENSION CABLE FOR REPAIRING DISPLAY MCB (J-2502-009-5)

SYMPTOMS

It may be difficult to repair the display MCB without using an extension cable.

RESOLUTION

An extension cable is available from the National Parts Center under part number J-2502-009-5.

XR5550 Subject EXTERNAL AMP GOES INTO PROTECTION MODE WHEN MODE IS CHANGED

SYMPTOMS

External amp connected to the line out goes into protect when the mode is changed, for example when switching from tuner to tape.

RESOLUTION

Found Q102 and Q202 leaking base to collector, causing 12V DC to appear on the collector when the muting signal was activated. This DC voltage appeared on the input of the external amp.

| 872992021 | Q102 | TRANSISTOR (DTC314TKH04) |
| --- | --- | --- |