HCDRX70 Subject USE KSS213/BA/F IN PLACE OF KSS213/Q-NP

SYMPTOMS

The optic assy used in this model, which has a cover assy, is on NBO until September of 97. We tried a KSS213/BA/F (884837901) which operates normally but it does not have a cover assy. The cover cannot be swapped from the 213.Q-NP to the KSS213/BA/F.

RESOLUTION

Use the KSS213/BA/F (88437901) until WRPC-AS recieves stock of the original part.

| Part Number | Reference Number | Description |
| --- | --- | --- |
| 884837901 |  | KSS213/BA/F |

HCDRX70 Subject CORRECT P/N FOR RY141 ON MAIN BOARD

SYMPTOMS

P/N in s/m for RY141 is incorrect. Pin configuration is different.

RESOLUTION

Order p/n 175516811.

HCDRX70 Subject DISTORTION IN AUDIO

SYMPTOMS

Speakers are distorting.

RESOLUTION

Replace and/or resolder C951.

HCDRX70 Subject PART NUMBER FOR REF 67 INCORRECT - USE A4392651A

SYMPTOMS

Part number 166400211 ref 67 subs to A4392350. This is incorrect. A4392350A is the TCSW board.

RESOLUTION

HCDRX70 is similar to the HCDRX100 A4392651A.

| Part Number | Reference Number | Description |
| --- | --- | --- |
| A4392651A | 67 | CD SW |