| GDM20SE1: Features |
| --- |
| SCREEN | 20 INCHES MEASURED DIAGONALLY |
| ACT VISUAL AREA | 19 INCHES |
| BRIGHTNESS CTRL | PLUS(+) AND MINUS(-) BUTTONS |

| Model GDM20SE1: Specifications |
| --- |
| CRT | 20" SUPER FINE PITCH W/90 DEFLECTION |
| APERTURE PITCH | 0.30MM // 0.31 PHOSPHOR PITCH |
| PICTURE SIZE | EFFECTIVE SIZE: 15 X 11 1/2 INCHES (W/H) |
|  | 13 7/8"X 11 1/8"OR 14 1/4"X 10 3/4"(W/H) |
|  | HORIZ: 29 TO 85 KHZ, VERT: 50 TO 150 HZ |
| MAX RESOLUTION | HORIZ: MAX 1280 DOTS, VERT: MAX 1024 LINES |
| MAC ADAPTER | ============================================ |
| INCLUDED? | NO |
| FREE? | YES: 5-RES |
| BAND WIDTH | ============================================ |
| HORIZONTAL SYNC | 31.5-85 KHZ |
| VERTICAL SYNC | 50-150 KHZ |
| POWER REQUIRE. | 100-120V(50/60HZ), 220-240V(50/60HZ) |
| OPERATING TEMP | 50*F TO 104*F(10*C TO 40*C) |
| OP. HUMIDITY | 10%TO 80%, NO CONDENSING |
| SIGNAL INPUTS | ============================================ |
| ANALOG RGB: | Y-0.714V P-P, POS |
| EXT. SYNC. | Y-COMPOSITE1-5V P-P,NEG OR POS |
| SYNC ON GRN | Y-0.286VP-P, NEG |
| INPUT CONNCT | RGB-(BNC5) |
| INPUT CONNCT | N |
| REG COMPLIANCE | =========================================== |
| SAFETY: | UL1950 |
| SAFETY: | CSA C22.2 NO 950 |
| SAFETY: | IEC-950(TUV, GS MARK |
| EMMISSIONS | MPR-II |
| EMMISSIONS | ENERGY STAR |
| X-RAY: | DHHS,DNHW,PTB |
| PNP: | N/A |
| ERGONOMICS | TILT SWIVEL BASE / BONDED A/R PANEL |
| OP. SYS.: | WIN/MAC |
| DIMENSIONS | 18 3/4 X 18 3/4 X 19 3/4 INCHES (W/H/D) |
| WEIGHT | APPROX 66 LB, 2OZ |
| POWER MANGMENT | ============================================ |

ARCING PICTURE TUBE, Q511 FAILURE

SYMPTOMS

Q511 failures have occurred due to CRT arcing.

RESOLUTION

After modifying about 40 GDM20SE1 unit for the last 3 months, none have come back. Modifications included, Flash 47R1, Service Bulletin 89, remove C511, and relocate D504.

Flash 47R1 and Service Bulletin 89 modifications provide alternate CRT arc current paths. These changes have been verified to be affective in protecting Q511. C511 and D504 also have Q511 protection functions.

Parts

Part Number Reference Number Description Symptom Code Section Code PCB Reference Defect Code Repair Code 872901528 Q511 TRANSISTOR IRF19630GS D-BRD

H PIN/KEY BAL, CENTERING, AND D FOCUS OFF

SYMPTOMS

Unable to adjust Horiz. Pincushion and Keystone Balance. Horiz. Centering and Dynamic Focus were wrong.

RESOLUTION

IC404 dual Op Amp was replaced on the D Board. Unit operation was restored.

IC404 has a high failure rate. SB CSI-111 No. 99 gives countermeasure to protect from CRT arcing. IC404 is used in dynamic focus and Horiz. geometry correction circuits. Failure can affect one or both circuits. IC404 failure can result in shorting  condition that affects power supply to other circuits. FPR Q1756 describes similar problems.

Parts

Part Number Reference Number Description Symptom Code Section Code PCB Reference Defect Code Repair Code 875950391 IC404 IC TLO82ACP D

NO OPERATION, CENTER LIGHT ON, PWR SAVE BLINKING,Q511 FAILED

SYMPTOMS

No operation, Has high voltage but no picture, center light works power saving light is blinking.

RESOLUTION

It is same problem for 19 units, serial numbers attached. Replacing Q511 made them work again. During first 5 hours, 5 units failed again and this time I had to replace Q511 and picture tube. Picture tube is arcing.

Parts

Part Number Reference Number Description Symptom Code Section Code PCB Reference Defect Code Repair Code 872901528 Q511 TRANSISTOR D

NO PICTURE, NO HV, GEOM LIGHT ON

SYMPTOMS

Unit has no high voltage Geom light is on. Power Save and Power lights are flashing.

RESOLUTION

Check pin 15 of IC801. It has a sawtooth waveform and is noisy. Waveform at IC801/15 should be square and reverse from input pin 9 IC801. Replace IC801 unit works ok.

IC801 Pin 15 drives the gate of HV FET switch Q804. The IC is low power but can have voltage spike damage from FBT components. Failure history is low so part may have been faulty.

Parts

Part Number Reference Number Description Symptom Code Section Code PCB Reference Defect Code Repair Code 875924049 IC801 IC DIG HEX INV D

PICTURE JITTER HORIZONTALLY, CN910 PIN 11 N-BRD UNSOLDERED

SYMPTOMS

At first, picture would shake and change size horizontally. A few minutes later, the picture would stabilize.

RESOLUTION

Found pin 11 of connector CN910 was not soldered. Remounted CN910, resoldered pin 11 and unit tested OK.

I really appreciate this type of detail information. Please keep it up. Also, the pictures are excellent. Thank you....

PICTURE OFFSET RIGHT 2 INCHES

SYMPTOMS

Picture was moved to right 2 inches in all modes. Normal VGA mode had enough range to set back to center, but Mode 5 and above did not have enough range.

RESOLUTION

Replaced IC404, thanks to a tip from Phuc Ngjuyen, San Jose RRC. Part was sent to Tech. Dept.

Frequent IC404 failures in these units are being investigated. Service Bulletin CSI-111 No. 99 describes some countermeasures. Failed IC404 in dynamic focus circuit could load or short +15VDC and -12VDC lines affecting H phase, centering, etc.

Parts

Part Number Reference Number Description Symptom Code Section Code PCB Reference Defect Code Repair Code 875950391 IC404 IC, TLO82CP D

SCAN SHUTDOWN

SYMPTOMS

Set in Shutdown. Flashing Power and Power Save LED's. Centering LED Lighted.

RESOLUTION

Found Q511 leaky. Replaced FET. Restored operation.

Repair tracking data shows Q511 failure is No. 1 problem for this unit. Shorted Q511 is due to excessive voltage and temperature stress. This information is being provided to design group.

Parts

Part Number Reference Number Description Symptom Code Section Code PCB Reference Defect Code Repair Code 87290152 Q511 SCAN CONVERTER D

UNIT SHUTDOWN, FOUND D824 SHORTED AND PS500 OPEN

SYMPTOMS

Unit came in with scan failure shutdown. Found D824 shorted and PS500 open. After replacing these components, the unit came up and worked but front panel buttons were locked up. I ran through the HSI white balance procedure per TF C/P0044 listed for  the GDM17SE1 clicking OK on all the screens. Although it unlocked the unit it totally ruined the White Balance. I then went back and re-adjusted white balance.

RESOLUTION

The shutdown was caused by the shorted diode which eventually puts a strain on the unit and takes out the fuse link PS500. As far as the TF C/P0044, I would recommend saving your adjustments prior to attempting this process. Then reload after unlocking  the unit.

Parts

Part Number Reference Number Description Symptom Code Section Code PCB Reference Defect Code Repair Code 871991119 D824 1SS119 DIODE D

SHUTDOWN AT TURN ON

SYMPTOMS

Unit shut down at turn on.

RESOLUTION

Replace shorted C822 and burned R868.

C822 couples brightness compensation waveform from H. Out transformer to FBT HV. Shorted C822 conducts B+ current via R868. Partially shorted B+ causes HV or Scan failure Shutdown mode. If CRT arcing is noted, SG800 may be faulty also. FPR's Q1756 &  Q1871 describe related IC404 problems.

Parts

Part Number Reference Number Description Symptom Code Section Code PCB Reference Defect Code Repair Code 110222800 C822 470 PF 500V CAP D

SHUTDOWN CAUSED BY SCAN FAIL

SYMPTOMS

Power Save and Power indicators flash with Center indicator on. Found IC404 caused the problem.

RESOLUTION

Replaced IC404 and adjusted the set.

IC404 is a dual Op Amp used in the Dynamic Focus and H Centering circuits. LED light pattern indicates shutdown due to scan failure. Faulty IC404 disrupted H deflection operation. Note that SB CSI-111 No. 99 gives corrections to protect IC404 from  damage.

Parts

Part Number Reference Number Description Symptom Code Section Code PCB Reference Defect Code Repair Code 875950391 IC404 IC TLO82CP D

VERT. LINE IN PICTURE

SYMPTOMS

Picture shows faint Vert bar, 5 mm wide, 1/3 from left side. Subtle effect noticeable on white raster at 640x480 and 1024x768 re

RESOLUTION

Line location on CRT uneffected by moving raster side to side. One customer complained about it, the other didn't. Replaced CRT and D board. No change. Also occurs on GDM17SE1 units. -SOLUTION: Clean or tighten the A Board ground connections to  Shield, Video Cable, & PS Connectors.

Crosstalk like this is usually from D Board to A Board ground loops conducting Sync signal energy into the video signal circuits.

Parts

Part Number Reference Number Description Symptom Code Section Code PCB Reference Defect Code Repair Code 893458300 VIDEO AMP MCB A