CCDTRV68 Subject Doesn't power up with battery or AC adapter, flashes battery low indicator.

SYMPTOMS

No Battery operation. Battery with slash mark in LCD.

CAUSE

Dosen't detect battery. Shows battery symbol with slash mark across it.

RESOLUTION

Please use RadarW and run CAM01PATCH to correct this problem.
NOTE: if CCD-TRV68 is not available in your CAM01PATCH file, you may use CCD-TRV88.

CCDTRV58, CCDTRV68, CCDTRV78, CCDTRV88, CCDTRV98 Subject LCD / FP-260 Flex Board Supply Method Changed.

SYMPTOMS

LCD / FP-260 Flex Board Supply Method Changed.

CAUSE

The LCD and FP-260 Flex Board will no longer be supplied as separate parts, instead they will be supplied as one assembly (LCD Block Assy).

RESOLUTION

If the LCD and/or the FP-260 Flex Board need to be replaced, order LCD Block Assy P/N A-7096-917-A

CCDTRV68 Subject No EVF Video - Replaced bad FFC-256/289 Flex.

SYMPTOMS

No EVF Video - Replaced bad FFC-256/289 Flex.

CAUSE

No EVF Video. Technician had replaced VF-129 board.

RESOLUTION

Found FFC-256/289 flex cable bad between VC-251 board and VF-129 board. Multiple conductors test open or intermittent.

Parts

Part Number Reference Number Description Symptom Code Section Code PCB Reference Defect Code Repair Code 179245411 FFC-256 Flex Board 1313 IMG NA D A

CCDTRV68 Subject Unit Shuts Down On AC Adapter or Battery.

SYMPTOMS

Unit Shuts Down On AC Adapter or Battery.

CAUSE

Unit shuts down on AC adapter or battery operation.Technician had replaced VC 251 board in camcorder. After initializing all data pages manually with RM-95B and loading new data from a good CCDTRV68 using Radar W, above symptom presented itself. Ran  CAM01 patch in RadarW. Ineffective. Same power shutdown problem.

RESOLUTION

Loaded CCD-TRV98 data to Fixed data-2 address locations on D page manually. Changed model ID data bytes to those of a CCD-TRV68.

CCDTRV68, CCDTRV88, CCDTRV98, DCRTRV130 Subject Caution when Replacing VC Board or CCD Imager - Parts Compatibity

SYMPTOMS

Caution when Replacing VC Board or CCD Imager - Parts Compatibity

CAUSE

A new CCD imager (made by Matsushita) was used in mid production which is not compatible with the original VC board.

RESOLUTION

When replacing the CCD imager and/or the VC board, you must use the right VC board / CCD imager combination. See the attached html file for compatible combination chart. Refer to attached jpg images for board diffrences in CCD & DCR models.

SUPPORTING DOCUMENTS AND GRAPHICS

ccd_imager_combo: Shows correct CCD/VC Board combination:

vc-251.jpg: Shows VC Board version differences in CCD models.

dcr-trv130_Q1333.jpg: Shows VC Board version differences in DCR-TRV130

ccd_imager_combo

When replacing the VC board and/or the CCD imager, be sure to use the correct combination.

| Model | Part Name. | Sony CCD Imager | Matsushita CCD Imager |
| --- | --- | --- | --- |
| CCD-TRV68, CCD-TRV88, CCD-TRV98 | CCD Block Assy | A-7031-207-A | A-7031-301-A |
|  | VC-251 Board | A-7096-405-A | A-7096-815-A |
| DCR-TRV130 | CCD Block Assy | A-7030-821-A | A-7031-203-A |
|  | VC-256 Board | A-7096-408-A | A-7096-407-A |

Applicable  S/N List:

CCD-TRV68 	( 159717 ~

CCD-TRV88 	( 31901 ~

( 30401 ~

CCD-TRV98 	( 61801 ~

NOTE:  You can verify each board as follows.

CCD-TRV68/78/88/98

VC-board does not have Q028----> Sony CCD combination

VC-board A side has Q028 ----> Matsushita CCD combination

DCR-TRV130

VC-board has Transistor Q1333---->Matsushita CCD combination

VC-board does not have Transistor Q1333---->Sony CCD combination