Supporting Information

Preparation of [AlMe(C6F5)(μ-Me)]2  (1)

A solution of Al2Me6∙(0.24 g, 1.67 mmol) in toluene (15 mL) was added to a solution of Al(C6F5)3∙PhMe (1.03 g, 1.67 mmol) in toluene (80 mL) at room temperature.  The mixture was stirred (48 h) and the volatile materials were removed in vacuo.  The residue was dissolved in toluene (10 mL) and cooled (-20 ˚C) to give clear colorless crystals of 1.  Yield, 0.95 g, 75%. M.P. 115 ˚C.

Crystal data for (1): C8H6AlF5, Mr 224.11, triclinic, space group P1 (No. 2), a = 7.1912(14) Ǻ, b = 7.4838(15) Ǻ, c = 18.436(4) Ǻ, α = 84.47(3)˚, β = 88.73(3)˚, γ = 64.68(3)˚, V = 892.5(3) Ǻ3, Z = 4, Dcalc = 1.668 g cm-3, T = 123 K, R = 0.0159, WR = 0.1174, GOF = 1.524.  1H NMR (300 MHz, C7D8, 25 ˚C) δ -0.058 (s, AlMe); 13C{1H}(C7D8), δ -7.125 (s, AlMe), δ 135-155 (multiplets, C6F5); 19F{1H} δ -159.06 (m, 2F, m-C6F5), -149.80 (m, 1F, p-C6F5), -120.45 (m, 2F, o-C6F5), 27Al{1H}, δ -149.4 (s,br,w1/2 = 3280 Hz).

Preparation of GaMe(C6F5)2  (2)

A solution of Me3Ga (0.266 g, 2.31 mmol was added to a solution of (C6F5)3B (0.789 g, 1.54 mmol) in toluene (80 mL) at room temperature.  The reaction mixture was allowed to stir for approximately 48 h then all volatiles were removed in vacuo.  Clear colorless crystals of (C6F5)2GaMe were obtained by slow sublimation (0.1 Torr, 50 ˚C), 0.90 g, 85%, mp 93 ˚C.

Crystal data for 2: C13H3F10Ga, Mr 418.87, monoclinic, apce group P21/n, (No. 14) a = 13.979(5) Ǻ, b = 6.507(5) Ǻ, c = 15.782(50 Ǻ, β = 114.748(5)˚, V = 1303.7 (12) Ǻ3, Z = 4, Dcalc = 2.134 g cm-3, T = 153 K, R = 0.0226, WR = 0.0595, GOF = 1.087. 1H NMR (300 MHz, C7D8), δ 0.227 (s, GaMe), 13C{1H}NMR (75.5 MHz, C7D8); δ 1.880 (s, GaMe), δ 135-155 (multiplets, C6F5); 19F{1H}NMR (169 MHz, C7D8); δ -159.322 (m-C6F5, 2F), -149.425 (p-C6F5, 1F), -120.893 (o-C6F5, 2F).  CI  HRMS: calcd. for C13H3GaF10 (M+H)+, 417.9331; found 417.9337; calcd. for C12GaF10 (M-CH3)+, 402.9096; found 402.9101.

X-Ray Crystallography

Crystals of 1 and 2 suitable for X-ray diffraction studies were coated in perfluoro(poly)ether prior to data collection.  The data were collected on a Nonius Kappa CCD diffractometer using a graphite monochromator with MoKα radiation (λ = 0.71073Å).  For 1, a total of 505 frames of data were collected using ω-scans with a scan range of 1( and a counting time of 200 seconds per frame.  For 2, a total of 304 frames of data were collected using ω-scans with a scan range of 2( and a counting time of 120 seconds per frame.  The data were collected at 123 K (1) or 153 K (2) using an Oxford Cryostream low temperature device.  Details of crystal data, data collection and structure refinement are listed in Table 1.  Data reductions were performed using DENZO-SMN.1 Both structures were solved by direct methods using SIR972 and refined by full-matrix least-squares on F2 with anisotropic displacement parameters for all the non-H atoms using SHELXL-93.3  All hydrogen atoms were located by subsequent Fourrier syntheses.  The functions, (w(|Fo|2 - |Fc|2)2, were minimized, where w = 1/[(σ(Fo))2 + (0.0394*P)2 + (0*P)] (1) or w = 1/[(σ(Fo))2 + (0.0280*P)2 + (1.0111*P)] (2) and P = (|Fo|2 + 2|Fc|2)/3.  No corrections for secondary extinction effects were necessary.  Neutral atom scattering factors and values used to calculate the linear absorption coefficients are taken from the International Tables for X-ray Crystallography (1992).5  All figures were generated using SHELXTL/PC.6

Table 1.  Summary of crystallographic data for  (1) and (2).

| Compound | 1 | 2 |
| --- | --- | --- |
| Empirical formula | C8H6AlF5 | C13H3F10Ga |
| Formula weight | 224.11 | 418.87 |
| Temperature (K) | 123(2) | 153(2) |
| Wavelength (Å) | 0.71073 | 0.71073 |
| Monochromator | graphite | graphite |
| Crystal Habit | prism | prism |
| Crystal Size (mm) | 0.1 x 0.1 x 0.1 | 0.3 x 0.3 x 0.3 |
| Crystal system | Triclinic | Monoclinic |
| Space group | P-1 | P21/n |
| Unit cell dimensions: |  |  |
| a (Å) | 7.1912(14) | 13.979(5) |
| b (Å) | 7.4838(15) | 6.507(5) |
| c (Å) | 18.436(4) | 15.782(5) |
| ( (°) | 84.47(3) | 90 |
| ( (°) | 88.73(3) | 114.748(5) |
| ( (°) | 64.68(3) | 90 |
| Volume (Å3) | 892.5(3) | 1303.7(12) |
| Z | 4 | 4 |
| Density (calculated) (g cm-3) | 1.668 | 2.134 |
| Absorption coefficient (mm-1) | 0.261 | 2.229 |
| F(000) | 448 | 808 |
| Diffractometer | Nonius KAPPA-CCD | Nonius KAPPA-CCD |
| ( range for data collection (°) | 3.03 to 26.11 | 3.28 to 25.01 |
| Limiting indices | -8 ( h ( 8, -9 ( k ( 9, -21 ( l ( 22 | -16 ( h ( 16, -7 ( k ( 7, -18 ( l ( 18 |
| Reflections collected | 10520 | 18949 |
| Independent reflections | 3385 | 2297 |
| Rint | 0.0595 | 0.0557 |
| Absorption correction | None | None |
| Refinement Method | Full-matrix least-squares on F2 | Full-matrix least-squares on F2 |
| Data / restraints / parameters | 3383 / 0 / 301 | 2297 / 0 / 229 |
| Goodness-of-fit on F2 | 1.524 | 1.087 |
| Final R indices [I>2((I)] | R1 = 0.0519, wR2 = 0.1174 | R1 = 0.0226, wR2 = 0.0595 |
| R indices (all data) | R1 = 0.0739, wR2 = 0.1257 | R1 = 0.0250, wR2 = 0.0610 |
| Largest diff. peak and hole (e Å-3) | 0.290 and -0.308 | 0.452 and -0.285 |

References

- DENZO-SMN.  (1997). Otwinowski , Z. and Minor, W. Methods in Enzymology 276: Macromolecular Crystallography, part A, 307 – 326, C. W. Carter, Jr. and R. M. Sweets, Editors, Academic Press.

2)	SIR97.  (1997).  A program for crystal structure solution. Altomare, A.; Burla, M. C.; Camalli, M.;  Cascarano, G., Giacovazzo, C.; Guagliardi, A.; Moliterni, A. G. G.; Polidori, G. & Spagna, R.

SIR92.  (1993).  A program for crystal structure solution. Altomare, A., Cascarano, G., Giacovazzo, C. & Guagliardi, A.  J. Appl. Cryst. 26, 343-350.

3)	Sheldrick, G. M. (1994).  SHELXL93.  Program for the Refinement of Crystal Structures.  University of Gottingen, Germany.

4)	Rw(F2) =  {(w(|Fo|2 - |Fc|2)2/(w(|Fo|)4}1/2 where w is the weight given each reflection.

R(F) =  ( (|Fo| - |Fc|)/(|Fo|} for reflections with Fo > 4(( (Fo)).

S =  [(w(|Fo|2 - |Fc|2)2/(n - p)]1/2, where n is the number of reflections and p is the number of refined parameters.

- International Tables for X-ray Crystallography (1992). Vol. C, Tables 4.2.6.8 and 6.1.1.4, A. J. C. Wilson, editor, Boston: Kluwer Academic Press.

6)	Sheldrick, G. M. (1994).  SHELXTL/PC (Version 5.03).  Siemens Analytical X-ray Instruments, Inc., Madison, Wisconsin, USA.

F36—C63	3.599 Å

F36—C64	3.335 Å

F35—C63	3.298 Å

F35—C62	3.190 Å

F32—C66	4.705 Å

F32—C65	4.658 Å

F34—C62	3.967 Å

F34—C61	3.542 Å

F33—C61	4.611 Å

F33—C66	4.309 Å

View of the "short" π-π interaction in 1 with F-C contacts listed.

C35—F62	4.063 Å

C35—F63	4.176 Å

C36—F63	4.303 Å

C36—F64	3.764 Å

C32—F65	3.882 Å

C32—F66	3.934 Å

C34—F62	4.442 Å

C33—F66	3.673 Å

Alternative view of "short" π-π interaction in 1 with F-C contacts listed.

F34—C62	4.122 Å

F34—C61	4.891 Å

F33—C61	3.439 Å

F33—C66	3.639 Å

F36—C63	5.621 Å

F36—C64	5.859 Å

F35—C63	5.296 Å

F35—C62	5.749 Å

F32—C66	4.187 Å

F32—C65	3.433 Å

View of the "long" π-π interaction in 1 with F-C contacts listed.

C35—F62	4.931 Å

C35—F63	3.811 Å

C36—F63	3.981 Å

C36—F64	4.530 Å

C32—F65	4.528 Å

C32—F66	5.593 Å

C34—F62	4.057 Å

C33—F66	5.342 Å

Alternative view of the "long" π-π interactions in 1 with F-C contacts listed.