## Slide 1
INTER-SERVICE TRAINING
REVIEW ORGANIZATION
CRAWLER
TRACTOR
PHASE
AIR FORCE
MARINES
ARMY
NAVY
INTER-SERVICE TRAINING
REVIEW ORGANIZATION
CRAWLER
TRACTOR
PHASE
AIR FORCE
MARINES
ARMY
NAVY
Name:
Class#:
Service:
BLDG 5085 / 12518
Phone: 6-2557
STUDENT HANDOUT
1 FEBRUARY 2006

## Slide 2
TABLE OF CONTENTS
CHAPTER TITLE PAGE
1. Introduction to the crawler tractor 03-18
2. Preventive Maintenance Checks and Services 19-56
3. Starting, operating, and shut-down procedures 57-59
4. Construct a stockpile 60-61
5. Spread a stockpile 62-63
6. Construct a ditch 64-66
Notes 67

## Slide 3
INTRODUCTION TO THE CRAWLER TRACTOR
PURPOSE: To prepare the student to be able to understand the technical training lessons that will
follow. It will include a briefing on the characteristics, capabilities, limitations,
components, instruments and controls, attachments, and operating techniques.
SAFETY: Hard hats must be worn at all times. Hearing protection must be worn while vehicle is
running. Use 3 points of contact when mounting or dismounting crawler tractor. Use
caution around moving parts and hot radiators. Remove all jewelry and do not wear
loose clothing. Clear all personnel before starting engine.
REFERENCES: FM 5-434, earth moving operations, 15 June 2000, TM 5-2410-237-10, Tractor, Full Tracked, Low Speed, Diesel Engine Driven, Medium Drawbar Pull, D7G January 1993 with change 1.
LESSON OUTLINE:
1. Characteristics
a. Nomenclature: Tractor, Full Tracked, Low Speed, Diesel Engine Driven, Medium Drawbar Pull.
b. Dozers are classified by:
1. Weight.
2. Drawbar pull.
c. There are three types of classifications for dozers.
1. Light (D5/Case 1150) 0 to 39,000 pounds (0 to 17,706 kg).
2. Medium (D7) 39,001 to 88,999 pounds (17,706 to 40,406 kg).
3. Heavy (D8) 89,000 pounds and up (40,406 kg).

## Slide 4
2. Capabilities
a. The dozer is standard equipment for most earth moving operations.
b. Dozers with the ripper attachment are designed for dozing and ripping soil, rocks, asphalt and
concrete.
c. Dozers with the winch attachment can winch loads of 50,000 lbs (22,700 kg). at a line speed of 80 ft per minute (24.4m).
d. Dozers with the winch attachment deliver 35,000 lbs (15,890 kg). of drawbar pull at a speed of 1.4 mph (2.3 kph).
e. Dozers are capable of operating in all types of weather and terrain due primarily to their low ground
bearing pressure of 10.3 psi (71.01 kps) and high Ground clearance of 13.7 inches (34.79 cm).
f. Dozers are capable of fording water at depths up to 30 inches deep (76.2 cm) without fording kit and up to 60 inches ( 152.4 cm) when equipped with a fording kit.
g. The dozer is capable of negotiating a fore and aft slope of 45o and a side slope of 35o under
optimum conditions.
h. When equipped with a reinforced blade, the dozer is capable of assisting scrapers in push loading
operations.
3. Limitations
a. Dozers are very slow moving (6.2 mph [10 kph]. Forward, 7.4 mph [11.90 kph]. Reverse).
b. Optimum operating range of the dozer is from 0-300 ft (0-91.5m). Any earthmoving operations over 300 ft (91.5 cm) requires the use of other equipment.
c. When crossing improved surfaces, dunnage (tires, wood, AM-2 matting) is required to keep from
damaging surface.
d. Dozers must be transported long distances due to their slow speed and tracks. They may be moved
under their own power (up to a distance of 1 mile [1.61 km]) at slow speeds, however this shortens their operational life.
e. Due to their large size and weight, transportation is made difficult (road permits may be required).

## Slide 5
1
2
5
3
4
7
6
8
4. Major Components
a. Left side view of tractor with rippers.
1. Radiator. Contains coolant, which provides engine cooling.
2. Ether starting aid compartment. Location of the ether canister for cold weather starting.
3. Pre-cleaner. Prevents debris from entering the air intake system. Primary and Secondary filters.
Operator maintains the primary filter only.
4. Operators station. Location of all the controls and indicators which the operator uses during
operation.
5. Rollover protection structure (ROPS). Protects the operator in the event of an accidental rollover.
6. Battery box. Holds the batteries, which provide current for the electrical system. 24 volt neg.
ground. Army (2) batteries and Marine (4) batteries.
7. Ripper. Used for loosening soil and for ripping through hard compacted soil.
8. Track assembly. 6 major components-track plates, chain, upper carrier rollers, lower rollers, idler
wheel and drive sprocket.
INTRODUCTION TO THE CRAWLER TRACTOR

## Slide 6
INTRODUCTION TO THE CRAWLER TRACTOR
1
2
7
4
3
8
6
5
9
b. Right side view of tractor with winch and winterized cab.
1. Winch. Used for all types of winching operations
2. Drawbar. Used for towing compaction equipment and other vehicles.
3. Fuel Tank. Contains diesel fuel for engine operation.
4. Hydraulic Oil Tank. Contains hydraulic fluid for hydraulic systems operation.
5. Winterized Cab. Protects the operator from severe weather.
6. Door Stop. The door can be secured to this arm to keep it in the open position.
7. Tool Box. Contains the drawbar pin assembly for tractor with winch.
8. Straight Blade (also called a Bull Blade). Used for earth moving operations.
9. Engine. Caterpillar model 3306, 6 cylinder, in line, turbo charged, diesel driven. Produces
200 horsepower at 2000 RPM's.
CAUTION: Allow 3 to 5 minutes warm up and cool down time to avoid damage to the turbo charger.

## Slide 7
INTRODUCTION TO THE CRAWLER TRACTOR
5. Instruments and Controls
A2
A1
B1
B2
B3
B4
A3
a. Steering and Brake Controls
1. Left/Right Steering Control Levers. Pulling the steering lever to the first detent causes the tractor
to make a gradual turn in the direction relative to the lever being pulled. When the lever is pulled
all the way back, the brake engages and causes the tractor to make a sharp turn.
2. Left/Right Brake Pedals. Depress the pedal to slow or stop the movement of the track relative to
the pedal.
3. Brake Lock Lever. To engage, depress the left brake pedal firmly. Push brake lock lever down,
and then depress right pedal firmly. To release, depress both brake pedals and pull lock lever up.
b. Transmission and Engine Speed Controls
1. Governor Control Lever. This lever controls the speed of the engine. Pull the lever toward you to
increase the engine speed, and push the lever away to decrease engine speed. To shut off the
engine, push forward past detent.
2. Transmission Control Lever. This lever controls direction and speed of the tractor. The
transmission has three forward speeds and three reverse speeds. Maximum forward speed is
6.2 mph (10 kph) and maximum reverse speed is 7.4 mph (11.90 kph).
3. Transmission Lock Lever. The transmission is locked in NEUTRAL by pushing the lock
lever down. Pull the lever up to unlock the transmission selector lever.
NOTE: In many Dozers with cabs, this lever also locks the brakes. Both brakes must be pushed
down before moving this lever to the unlocked position, in these Dozers only.

## Slide 8
INTRODUCTION TO THE CRAWLER TRACTOR
C1
C2
C3
4. Decelerator. Depress the pedal to override the governor control lever and reduce engine speed.
Release the pedal to return engine speed to the governor control lever setting.
c. Implement Controls
1. Blade Control Lever. (6 positions) This lever controls blade lift and tilt. The lever is normally
in the HOLD position. When the lever is moved to the right, the blade tilts so the right side is
lower than the left side, and when it is moved to the left the blade will be lower on the left.
Move the lever backward to raise the blade, and forward to lower it. If the lever is pushed
forward, past the lower position, it will go into the FLOAT position. The float position is the
only position with a detent. In this position, the blade is free to move up or down according to
outside forces.
2. Ripper Control Lever. (3 positions) This lever controls ripper lift and lower. When the lever is
moved to the right, the ripper will lower. Move the lever to the left and the ripper will rise. The
ripper can be lowered when the engine is not running.
3. Winch Control Lever. (4 positions) This lever controls movement in and the movement out of
the winch cable. The lever is normally in the BRAKE ON (Neutral) position, and returns
automatically from all positions but the BRAKE OFF detent position.

## Slide 9
INTRODUCTION TO THE CRAWLER TRACTOR
d. Gauges on Dash Panel
1. Horn button. Push this button to sound the horn.
2. Service Meter. This meter operates whenever the engine is operating. It indicates the total
operating hours of the tractor.
3. Ammeter. This meter measures the discharge current from the battery when the engine is off
and key is on. When the engine is running, it measures the charging current from the alternator
to the battery.
4. Oil Pressure Gauge. This gauge indicates oil pressure when the engine is running. The green
portion of the gauge indicates normal operating pressure at high idle. The white portion is normal
for low idle, and the red portion of the gauge indicates low oil pressure.
5. Water Temperature Gauge. This gauge indicates the temperature of the engine coolant. The green
portion of the gauge indicates normal operating temperature. The red portion indicates engine
overheat.
6. Torque Converter Temperature Gauge. This gauge indicates the temperature of the torque
converter oil. The green portion of the gauge indicates normal operating temperature. The red
band indicates overheating.
D1
D2
D3
D4
D5
D6

## Slide 10
e. Fuel Pressure and Fluid Level Gauges.
1. Fuel Pressure Gauge. This gauge indicates fuel transfer pump delivery pressure. The green
portion of the gauge indicates normal pressure, and the red portion indicates that pressure is low.
2. Fuel Level Gauge. This gauge indicates the amount of fuel present in the fuel tank. 115 gal (435 L). Capacity marked in 10% increments.
NOTE: When fuel level is at 30% or less notify the instructor.
3. Oil Level Gauge (Dipstick). This gauge indicates the amount of engine lubricating oil that is
present in the reservoir. Located on the left side of engine, 7.25 gal (27 L). Capacity of 15/40, cold and hot checks.
4. Air filter indicator. When the red band is visible it indicates that the air filter needs servicing.
Reset by pushing the button on the bottom. Located on the left side of the engine.
5. Transmission Oil Level Gauge (Dipstick). This gauge indicates the amount of transmission oil that is present in the reservoir. Located under the operators seat, 18.5 gal (70 L). Capacity of 15/40. Check at normal operating temperature. Check with transmission in neutral and engine at a low idle.
NOTE: This gauge is located on left side near battery compartment on Marine dozers.
6. Hydraulic Oil Level. This is a sight gauge on the oil tank, which indicates oil level for
the hydraulic implements. 21 gal (80L). Capacity of 15/40.
CAUTION: NEVER remove cap when oil is hot.
7. Winch Hydraulic Oil Level Gauge. This gauge is a sight gauge on the winch. It indicates oil level
for the hydraulic system of the winch. 16 gal (60 L). Capacity of 15/40.
8. Final Drives. Plugs are located in the rear on both left and right side. Proper level is at bottom of
threads. 9 gal (34 L). Capacity each of 80/90 gear oil.
9. Coolant system. Proper coolant level is ½“ (one-half inch) (1.27 cm)from bottom of filler neck.
12 gallon (45 L) Capacity of 50/50 mix.
CAUTION: Never remove cap when radiator is hot.
INTRODUCTION TO THE CRAWLER TRACTOR

## Slide 11
INTRODUCTION TO THE CRAWLER TRACTOR
f. Switches and Indicators.
F1
F2
F3
F4
F5
1. Start switch. Located on the lower right side of the dash panel. Turn the key / switch fully
clockwise to start the engine. Release the key when the engine starts, and the switch will return
to the ON position.
2. Circuit breaker. A 60-amp circuit breaker protects the starting and charging circuits should a
malfunction occur. Press to reset.
3. Exterior light switch. Turn the switch fully clockwise to turn on the exterior lights. Turn the
switch fully counter­clockwise to turn off.
4. Starting aid button. Pressing the button causes ether to be injected into the air intake. It is used
to help start the tractor in cold weather.
5. Dash light switch. Flip up to turn dash light on, down for off.
6. Battery disconnect switch. This switch is key operated. In the OFF position, electrical power to
all systems is interrupted. In the ON position, power is available for all systems. Located on the
left side of the operators seat.

## Slide 12
INTRODUCTION TO THE CRAWLER TRACTOR
6. Attachments
a. Types of Blades: A dozer blade consists of a moldboard, (3) cutting edges and (2) end bits. Blades
vary in size and design based on their different earthmoving functions. At 3/4" (1.91 cm) from moldboard the cutting edges may be rotated, however the end bits must be replaced.
1. Straight blade (also called a Bull Blade).
a. Used for cutting ditches and breaking through crusted material. It is mounted in a fixed
position, perpendicular to the line of travel.
b. It can be tilted laterally 12 inches (30.48 cm) left or right of center with the use of the hydraulic controlled tilt cylinder, and the blade top can be pitched either forward or backward within a 10-degree arc using the manual adjustment assembly.
2. Angle blade.
a. Effectively used to side cast material for backing filling or making side hill cuts. It is also used
for rough grading, spreading piles, or windrowing materials.
b. This blade can be set at 90 degrees for normal dozing operations or at angles of 25 degrees left
or right for side casting operations.
3. Special purpose blades: The D7G can also be equipped with several other & special purpose
blades such as the mine clearing blade, "V" tree cutter (stringer blade),
and various rakes.
b. Ripper: Dozers equipped with rippers normally have only three teeth mounted at the rear. Most
ripping operations should be performed in first gear. Maximum penetrating depth is the
length of the shank.
CAUTION: Turning and backing with ripper down can cause damage to the shanks and shank assembly.
c. Winch: Used for recovery of other equipment or self recovery.

## Slide 13
INTRODUCTION TO THE CRAWLER TRACTOR
7. Operating Techniques
ENVIRONMENTAL: During operation, damage caused by erosion due to rain, must be limited by
dressing off the work area at the end of each day. Dust and exhaust created by
equipment also affects the environment, avoid any unnecessary equipment usage.
a. Winching.
1. Dozers equipped with winches can be used for recovery of vehicles, towing, and holding a load.
2. The winch can not be used to pull when there is less than three wraps of cable on the winch drum.
(177 ft. (53.9 m) of 1 inch wire rope).
3. The winch line speed is controlled by the engine speed. For maximum service life of the winch,
engage winch at lowest practical engine speed (max 80 ft/min [24.4 m/min]).
4. Must keep the winch cable in a direct line with the object being pulled and no more than a 2 degree
deflection angle to keep from damaging cable and winch.
5. Has a maximum load pull of 50,000 lbs (22,700 kg).
CAUTION: To avoid injury, ensure personnel on the ground are cleared up to twice the distance of wire
rope that is reeled out.
b. Ripping: For ripping soft material, all three shanks can be used. For medium material the outer two
shanks should be used. For hard material, use only the middle shank.
c. Leveling.
1. Also known as straight dozing, leveling is simply cutting high areas and filling the low areas to
create a level surface.
2. If the blade digs in, the rear of the tractor will rise. To keep a level cut, raise the blade until the
tractor is again level.
3. If the blade starts to ride over the material, the front of the tractor raises. To keep a level cut, lower
the blade until the tractor is again level.

## Slide 14
INTRODUCTION TO THE CRAWLER TRACTOR
d. Stockpiling is a basic function of the crawler tractor in which large quantities of material are pushed
into a pile and or leveled.
e. Ditching.
1. Flat Bottom Ditching (Slot Dozing)
a. Slot dozing is recommended for stockpiling because of its high production output. Slot dozing
uses the spillage from the first few passes to hold the material in the slot for all sequential passes.
b. To increase production output, move the dozer over to either side leaving a narrow uncut section
between slots.
c. Used for large amounts of water drainage.
d. Can be used to hide equipment.
e. Increases work productivity by 50%.
2. V-Ditching.
a. The tilt cylinder on the dozer blade is designed to allow the dozer to cut shallow v-ditches by
tilting the blade, allowing the corner of the blade to penetrate the ground.
b. The dozer can be used to cut larger ditches by cutting at right angles to the centerline of the ditch.
c. Once the desired depth has been reached, complete the ditch by smoothing the sides and bottom.

## Slide 15
f. Push Loading (this task will be learned at the Scraper Phase).
1. The dozer can also be used to assist scrapers in loading operations.
2. By centering the reinforced portion of the straight blade (also called a bull blade) on the push block of
the scraper, the dozer can be used to help the scraper load in all types of material.
g. Blade to Blade Dozing.
INTRODUCTION TO THE CRAWLER TRACTOR
1. Also known as "Buddy Dozing", blade to blade dozing is normally used for moving large amounts
of material from 50 to 300 feet (15.25 to 91.5 m).
2. By putting both bull blades together, you can increase production output due to the larger area of
excavation.
3. Remove the uncut section by normal dozing, and if the soil conditions are good, production output
can be increased by as much as 50%.
h. Downhill Dozing.
2. After several loads are piled at the brink of the hill, push them all to the bottom at the same time
(Gravity will permit you to push more than one load down hill).
3. Use caution when steering on steep down grades, as the tractor may responds to steering controls
differently.
(Gravity may cause the tractor’s weight to push the machine downward on the disengaged side).
4. To move gradually to the right, you may have to pull the left steering clutch to the first detent.
5. To move gradually to the left, you may have to pull the right steering clutch to the first detent.
6. This “backward steering” does not normally occur while pushing a full load down hill.
1. When using the downhill dozing method,
first push several loads of material to the
brink of the hill.

## Slide 16
1. Brush and Small Trees – Travel forward with your blade lowered into the ground only as far as it
takes to cut the brush and tree roots. It may be necessary to back up occasionally to clear the blade
of roots.
INTRODUCTION TO THE CRAWLER TRACTOR
i. Brush and Tree Removal.
2. Medium Trees – Raise the blade as high as it will go, ease into the tree in low track speed and push.
As the tree falls over, back up and lower the blade under the exposed roots. Raise the blade to lift
out the trunk and roots of the tree as the dozer travels forward.

## Slide 17
3. Large Trees – First check and see if it is a push over. If the tree doesn’t push over, you need to cut
its roots.
a. Determine the direction in which the tree will fall, then make a cut in the roots on the opposite
side to a depth sufficient enough to cut some of the large ones.
INTRODUCTION TO THE CRAWLER TRACTOR
b. Make similar cuts on both adjacent sides.
c. Once you have completed cutting the roots on three sides, fill in the first cut and make a ramp.
Proceed up the ramp with you blade lifted high and push. As the tree starts to fall, reverse the
tractor quickly to get away from the raising root mass. Move forward into the fallen tree,
pushing and raising your blade at the same time to extract the roots.

## Slide 18
INTRODUCTION TO THE CRAWLER TRACTOR
j. Berms and Dikes can provide protection against fragments and eliminate the risk of explosions
caused from low-angle, high-speed fragments. Earth filled barricades can be used as an effective
and expedient means of supplying the necessary protection.
3 FT. (0.915 m) MIN.
2:1 SLOPE
1. Earth, 20 feet (6.1 m) or less in height, should have a crest (berm) at least 3 feet (0.915 m) wide.
2. Earth more than 20 feet (6.1 m) in height, should be at least 5 feet (1.525 m) wide at the top.
3. The slope shouldn’t be steeper than 2 horizontal to 1 vertical to reduce erosion and ease
maintenance.

## Slide 19
PREVENTIVE MAINTENANCE CHECKS and SERVICES
PURPOSE: To provide the student with the skills and knowledge necessary to maintain and operate
a crawler tractor.
SAFETY: Know and adhere to all hand signals. Maintain three points of contact when mounting or
dismounting equipment. Perform 360 walk around before mounting or dismounting
equipment. Wear double hearing protection, hard hats, and seat belts when operating
equipment. Do not wear lose clothing or jewelry. Always look to the rear when backing
up. Raise blade (and ripper if equipped) before backing up. Use caution when working
on hills, banks, or slopes to avoid tipping . Do not place transmission in neutral to allow the
crawler tractor to coast.
REFERENCES: FM 5-434, earth moving operations, 15 June 2000, TM 5-2410-237-10, Tractor, Full Tracked, Low Speed, Diesel Engine Driven, Medium Drawbar Pull, D7G January 1993 with change 1, TM 5-2410-237-20, Tractor, Full Tracked, Low Speed, Diesel Engine Driven, Medium Drawbar Pull, D7G January 1993.
PROCEDURES:
1. Any equipment operator or mechanic can be trained to detect a breakdown and get it fixed. The real
skill is to recognize a potential problem and prevent it from happening. That’s where preventive
maintenance comes in.
2. The key to successful preventive maintenance is the equipment record folder. You will be mainly
concerned with a DA Form 5988E or a DA Form 2404. When completed, they must be:
Concise
Easy to read
Up to date
Complete
a. These records should indicate what has been done, when it was done, and what needs to be done.
b. Each deficiency discovered will be annotated on the correct form.
c. Each deficiency will have an item number (Found on the PMCS checklist), the fault date,
and the fault noted in the correct block.
d. Deficiencies that are operator level maintenance will be corrected immediately and not annotated
on the maintenance inspection form.
e. Deficiencies that are previously noted on the form will be verified.
1. Faults that no longer exists will be lined out and the word “REPAIRED” or “REPLACED”
will be written in the corrective actions column, along with the operators initials.
2. Faults that still exist will not be annotated again on the form.

## Slide 20
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 21
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 22
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 23
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 24
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 25
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 26
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 27
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 28
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 29
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 30
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 31
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 32
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 33
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 34
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 35
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 36
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 37
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 38
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 39
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 40
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 41
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 42
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 43
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 44
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 45
Ripper Cap
3/4 “ (1.905 cm) From Transition
Check Clevis
Never Saddle A Dead Horse
Check Cable
For Damage

## Slide 46
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 47
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 48
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 49
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 50
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 51
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 52
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 53
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 54
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 55
PREVENTIVE MAINTENANCE CHECKS and SERVICES

## Slide 56
PREVENTIVE MAINTENANCE CHECKS and SERVICES
To be distributed in accordance with DA Form 12-25-E, Block 5974, requirements for LO 5-2410-237-12.
NOTES

## Slide 57
STARTING, OPERATING, and SHUT-DOWN PROCEDURES
1. Engine starting procedures.
a. Perform a 360 degree walk around.
b. Mount dozer left side using three points of contact.
c. Ensure you are wearing double hearing protection.
d. Buckle and adjust the seatbelt.
e. Turn main battery switch to the on position.
f. Pull governor control completely back, then push forward until you feel resistance.
g. Insert starter ignition switch key, turn to start.
h. Observe all the gauges.
i. Allow 3 to 5 minute warm up at low RPM.
NOTE: Do not crank the engine longer than 30 seconds, or damage to the starter motor may occur.
If the engine fails to start after 30 seconds, allow the starter to cool for 2 minutes before
attempting to start the engine again.
NOTE: If oil pressure does not register within 15 seconds after the engine starts, stop the engine or
serious damage may occur. Stop engine by pushing the governor control lever forward past the
detent.
2. Operating Procedures.
a. Moving the tractor.
1. Raise lowered attachments high enough to clear obstructions.
2. Release transmission safety lock by placing lever in the up position.
3. Depress both brake pedals and release brake lock.
4. Move transmission selector lever to desired direction gear position.
5. Pull governor control lever toward you until desired speed is obtained.

## Slide 58
STARTING, OPERATING, and SHUT-DOWN PROCEDURES
b. Changing gears and directions.
1. Decrease engine speed by depressing decelerator.
2. Move transmission selector to desired gear.
3. Return to desired engine speed.
CAUTION: Keep tractor under control at all times. DO NOT NEUTRALIZE TRANSMISSION to
allow tractor to coast. Select gear range before starting on downgrade. DO NOT SHIFT
TRANSMISSION WHILE ENGINE IS AT HIGH RPM.
c. Steering procedures.
1. To make a gradual right turn, pull the right steering clutch lever to the 1st position. Release
lever to end turn.
2. To make a sharp right turn, pull the right steering clutch lever all the way out. Release lever to
end turn.
3. To make gradual left turn, pull the left steering clutch lever to the 1st position. Release lever to
end turn.
4. To make a sharp left turn, pull the left steering clutch lever all the way out. Release lever to
end turn.
CAUTION: When steering on a steep downgrade the tractor will respond differently to the steering
controls.
d. Stopping procedures.
1. Reduce engine speed by pushing governor control lever.
2. Move transmission selector lever to NEUTRAL.
3. Push transmission safety lock down to the lock position.
4. Depress left brake, engage brake lock, and depress right brake firmly.
5. Lower all equipment.
CAUTION: Always park the tractor on level ground. Before leaving the tractor, always stop the engine.
CAUTION: When being approached by another student or an instructor: place the transmission in neutral;
lower the blade to the ground and place in float; reduce the RPM’s to idle; and place your
hands on top of your hard hat.

## Slide 59
STARTING, OPERATING, and SHUT-DOWN PROCEDURES
3. Shut-down procedures.
a. After engine has operated at low idle for 3 to 5 minutes, Push governor control lever past detent
to stop engine.
b. Turn start switch to the off position and remove the key.
c. Turn disconnect switch to the off position and remove the key.
CAUTION: Never turn disconnect switch OFF when the engine is running. Serious damage to the
electrical system will result.
4. Cold weather starting procedures.
a. Try starting the engine using the Engine starting procedures on the previous page.
b. If engine does not start, push the starting aid button while cranking the engine, and hold for three
seconds (time required to fill the chamber). Ether is injected when aid switch is released. Use
additional starting fluid once every two seconds until engine runs smoothly.
c. If oil pressure does not register within first 15 seconds, stop engine immediately and investigate.
If oil pressure is normal, proceed to step (d).
d. Run engine at reduced speed only long enough to circulate the oil through the engine, then
increase speed and warm up the engine.
e. Cover the radiator if necessary to bring engine temperature up to operating level.

## Slide 60
CONSTRUCT A STOCK PILE WITH A CRAWLER TRACTOR
PURPOSE: To provide the student with the guidelines and knowledge necessary to construct a stockpile
with the crawler tractor.
SAFETY: Know and adhere to all hand signals. Maintain three points of contact when mounting or
dismounting equipment. Perform 360 walk around before mounting or dismounting equipment.
Wear double hearing protection, eye protection, hard hats, and seat belts when operating
equipment. Do not wear loose clothing or jewelry. Always look to the rear when backing up.
Raise blade (and ripper if equipped) before backing up. Use caution when working on hills,
banks, or slopes to avoid tipping. Do not place transmission in neutral to allow the crawler
tractor to coast.
REFERENCES: FM 5-434, earth moving operations, 30 September 1999; TM 5-2410-237-10, Tractor, Full
Tracked, Low Speed, Diesel Engine Driven, Medium Drawbar Pull, D7G January 1993 with change 1.
PROCEDURES:
1. Start the crawler tractor IAW TM 5-2410-237-10 (page 57 of this handout).
ENVIRONMENTIAL: While moving in off road terrain, avoid unnecessary damage to water ways or
vegetation. Dust and exhaust created by the use of equipment also affects the
environment, avoid any unnecessary equipment usage. Damage is caused by
erosion due to rain, this erosion damage can be minimized by dressing off the
work area at the end of each day.
2. Construct a stock pile.
NOTE: Stock piles must be a minimum of 5’ (1.525 m) in height (school standard only).
a. Start on a level surface within designated area.
b. Slowly lower the blade into the ground. Do not excavate deeper than 4” to 6“ (10.16 to 15.24 cm), while maintaining a smooth cut.
c. On the first pass, start pushing material from a designated start point to a stockpile area
approximately 75' (22.88 m) away.
d. As you reach the stockpile area, begin to raise the blade one tractor length from the stockpile
point, letting the material fall under the blade, forming a ramp at the completion of your cut and
creating an approximate 2:1 slope ratio.
e. Back the crawler tractor to the beginning of the pass.

## Slide 61
CONSTRUCT A STOCK PILE WITH A CRAWLER TRACTOR
f. Position the crawler tractor at the start point, with approximately 1/3 of the blade overlapped
onto the first pass. Maintain a direction directly toward the original stockpile. Do not build a berm.
g. Stockpile by pushing the material on successive cuts, in the same manner, working the crawler
tractor from the start point, all the way around the work area in either a clockwise or a counter
clockwise direction, always ending at the same stockpile and maintaining the 2:1 slope.
CAUTION: Keep tractor under control at all times. DO NOT place transmission in neutral and allow the
machine to coast downhill. Select gear range necessary before starting down grade. Do not
change gears while going downhill.
h. Ensure the area that material is being cut from remains level + 4". DO NOT back blade to level.
NOTE: Do not stop the forward motion or cause tracks to spin while pushing material.
i. Make successive cuts the same as in step (b), constructing the stockpile higher on each pass until
it reaches the desired height.
3. Proceed to Spread a Stockpile task (Page 60 of this handout), (School requirement only).
2
3
1

## Slide 62
SPREAD A STOCK PILE WITH A CRAWLER TRACTOR
PURPOSE: To provide the student with the guidelines and knowledge necessary to spread a stockpile
with the crawler tractor.
SAFETY: Know and adhere to all hand signals. Maintain three points of contact when mounting or
dismounting equipment. Perform 360 walk around before mounting or dismounting equipment.
Wear double hearing protection, eye protection, hard hats, and seat belts when operating
equipment. Do not wear loose clothing or jewelry. Always look to the rear when backing up.
Raise blade (and ripper if equipped) before backing up. Use caution when working on hills,
banks, or slopes to avoid tipping. Do not place transmission in neutral to allow the crawler
tractor to coast.
REFERENCES: FM 5-434, earth moving operations, 30 September 1999; TM 5-2410-237-10, Tractor, Full
Tracked, Low Speed, Diesel Engine Driven, Medium Drawbar Pull, D7G January 1993 with change 1
PROCEDURES:
1. Start the crawler tractor, as needed, IAW TM 5-2410-237-10 (page 57 of this handout).
.
ENVIRONMENTIAL: While moving in off road terrain, avoid unnecessary damage to water ways or
vegetation. Dust and exhaust created by the use of equipment also affects the
environment, avoid any unnecessary equipment usage. Damage is caused by
erosion due to rain, this erosion damage can be minimized by dressing off the
work area at the end of each day.
2. Spread a stock pile
a. Start the crawler tractor moving forward and lower the blade to desired height.
b. Adjust the blade to the height of the surrounding area and move the crawler tractor into the side of
the pile using 1/3 of the blade to cut.
NOTE: Using the left side of the blade, continue to work to the left. Using the right side of the blade,
continue to work to the right.
c. Raise and lower the blade to maintain a smooth pass.
d. Slowly raise the blade until all material is feathered evenly while moving forward.
e. Place the tractor in reverse after the blade has been emptied.
f. Raise the blade all the way and back the tractor to the stockpile.
g. Reposition for another cut, again cutting into the stockpile using 1/3 of the blade.

## Slide 63
SPREAD A STOCK PILE WITH A CRAWLER TRACTOR
CAUTION: The operator must be satisfied that no one will be endangered before and while
backing the machine.
h. Repeat steps until the stockpile is evenly spread over the designated area. Do not back blade
to “level’.
i. Restore the area as close as possible to its original state to match the surrounding area and existing
drainage.
NOTE: Depending on the size of the pile, you should not cut into he pile straight on. Large piles should
be worked from the side, cutting material away from the stockpile, using 1/3 of the blade. When
spreading materials that are higher than the midpoint on the ROPS, adjust the height of the cut to
eliminate the danger of falling overhangs. On the successive cuts, follow the procedures for
normal spreading operations, using the first cut height as a guide for blade depth
3. Perform stopping procedures IAW TM 5-2410-237-10 (page 58 of this handout).
Align 1/3 Blade…
Match Surrounding Area…

## Slide 64
CONSTRUCT A DITCH WITH A CRAWLER TRACTOR
PURPOSE: To provide the student with the guidelines and knowledge necessary to construct a ditch
with the crawler tractor.
SAFETY: Know and adhere to all hand signals. Maintain three points of contact when mounting or
dismounting equipment. Perform 360 walk around before mounting or dismounting equipment.
Wear double hearing protection, eye protection, hard hats, and seat belts when operating
equipment. Do not wear loose clothing or jewelry. Always look to the rear when backing up.
Raise blade (and ripper if equipped) before backing up. Use caution when working on hills,
banks, or slopes to avoid tipping. Do not place transmission in neutral to allow the crawler
tractor to coast.
REFERENCES: FM 5-434, earth moving operations, 30 September 1999; TM 5-2410-237-10, Tractor, Full
Tracked, Low Speed, Diesel Engine Driven, Medium Drawbar Pull, D7G January 1993 with change 1
PROCEDURES:
1. Start the crawler tractor IAW TM 5-2410-237-10 (page 57 of this handout).
ENVIRONMENTIAL: While moving in off road terrain, avoid unnecessary damage to water ways or
vegetation. Dust and exhaust created by the use of equipment also affects the
environment, avoid any unnecessary equipment usage. Damage is caused by
erosion due to rain, this erosion damage can be minimized by dressing off the
work area at the end of each day.
2. Construct a ditch
a. Start with the crawler tractor in as level a position as possible.
b. Adjust blade for ditching and ensure the blade is level.
c. Position blade approximately 1/2 foot (15.24 cm) off the ground.
d. Place tractor in motion.
e. Lower blade gradually to make cut 4” to 6” (10.16 to 15.24 cm) deep.
4:1 slope
4:1 slope

## Slide 65
CONSTRUCT A DITCH WITH A CRAWLER TRACTOR
f. Maintain depth of cut for length of ditch.
g. Gradually raise blade to make exit ramp that is no steeper than a 4:1 slope ratio.
h. Raise the blade all the way, and back the crawler tractor to the starting point, keeping the crawler
tractor in the same path.
i. After initial marking cut, strive to cut as much material as possible while maintaining control
of machine not to exceed 6 inches (15.24 cm).
j. Maintain a flat ditch bottom and a slope of 4:1 on the entrance and exit ramps.
k. Continue same process, each pass dumping dirt off back side of exit ramp.
NOTE: The ramp should increase in length and not in height.
3. Correcting Errors
NOTE: The slower the engine RPM’s, the more sluggish your blade control. If you attempt to cut too
deep, a hump will be formed in the bottom of the ditch.
a. Cut off top of hump if necessary. Do not attempt to straighten with one pass.
b. If bottom of ditch is not level:
(1) Back out of cut onto level ground.
(2) Make pass, cutting just enough to straighten out ditch bottom.
(3) Start on level ground to make a level cut.
c. Do not over control.
4:1 slope
4:1 slope
Dig ditch to 3 foot (0.915 m) deep, dumping dirt off end of ramp.
3 foot (0.915 m) deep

## Slide 66
4. Backfill and Level
NOTE: No one goes over ramp the first time without instructor supervision.
a. Go approximately ½ way up ramp.
b. Lower blade smoothly but quickly to obtain full load.
c. Proceed over top with full load.
d. Raise blade gradually to build ramp on backside of stockpile.
e. Repeat procedures until you can drive down backside of stockpile.
f. Reverse tractor direction.
g. Align the crawler tractor with the right or left side of the stockpile and begin backfilling the ditch.
NOTE: Use Spread a Stockpile technique to backfill ditch.
5. Perform shutdown operations IAW TM 5-2410-237-10 (page 58 of this handout).
CONSTRUCT A DITCH WITH A CRAWLER TRACTOR
4:1 slope
4:1 slope
Half way up ramp, lower the blade all the way, pushing the top half of pile through
3 (0.915 m) foot deep

## Slide 67
Notes