# Small Arms

Integration Book

Prepared:  March 2002

An electronic copy of the Small Arms Integration Book (in Microsoft Word format)

can be located on the

General Dennis J. Reimer Training and Doctrine Digital Library

http://www.adtdl.army.mil

This copy of the Small Arms Integration Book can be downloaded to your computer for your personal use.

# Warnings

## General Warnings

If devices are to be secured to the weapon by additional means (i.e. tape, rubber bands, etc.) insure that the device is fully secured in its final configuration prior to conducting zeroing of the device to the weapon.  Failure to do so will result in an invalid zero and the firer’s inability to successfully engage targets.

# When handling any weapon always insure that the weapon has been cleared.

Periodically check the weapon mount to insure that it has not loosened during transportation or operation.

## AN/PAQ-4B/C Light, Aiming, Infrared

WARNING

INVISIBLE LASER LIGHT

The AN/PAQ-4B and AN/PAQ-4C are military lasers, and have been exempted from FDA radiation safety performance standards prescribed in the Code of Federal Regulations, Title 21, Chapter I, Subchapter J, pursuant to exemption No. 76 EL-01 DOD issued on 7-26-76. These devices must be used IAW the precautions contained in TM 11-5855-301-12&P.

The infrared beam is considered eyesafe based on military standards. Suitable precautions must be taken to avoid overexposure to the infrared beam.

- Do not stare into the infrared laser beam.

- Do not look into the infrared laser beam through binoculars or telescopes.

- Do not shine the infrared laser beam into mirror surfaces.

- Do not shine the infrared laser beam into other individuals' eyes.

WARNING

RISK OF DETECTION BY ENEMY

To reduce the risk of detection by an enemy wearing NVG's (Night Vision Goggles), avoid prolonged activation of the IAL (Infrared Aiming Light) prior to firing.

WARNING

The infrared beam is more detectable to an enemy using NVG's when shining through smoke, fog and rain. Avoid prolonged activation of the Aiming Light in these conditions.

## AN/PEQ-2A Laser Pointers/Illuminators

DANGER

INVISIBLE LASER RADIATION – AVOID DIRECT EXPOSURE TO THE BEAM

- Do not stare into the infrared laser beam.

- Do not look into the infrared laser beam through binoculars or telescopes.

- Do not point the infrared laser beam at mirror like surfaces.

- Do not shine the infrared laser beam into other individuals' eyes.

WARNING

Make sure the weapon is CLEAR and on SAFE before proceeding.

WARNING

RISK OF DETECTION BY ENEMY

To reduce the risk of detection by an enemy using Night Vision Devices, avoid prolonged activation of the AN/PEQ-2A.

WARNING

The infrared beam is more detectable to an enemy using Night Vision Devices when used in smoke, fog and rain. Avoid prolonged activation of the AN/PEQ-2A in these conditions.

WARNING

Do not store the AN/PEQ-2A with batteries installed.

CAUTION

# Do not overadjust the adjusters.

# Invisible Laser Radiation – Avoid Direct Exposure to the Beam

The AN/PEQ-2A makes use of a high power aiming laser and presents a serious eye hazard within 25 meters, when used in the training mode, and within 220 meters, when used in the tactical mode.  A safety block installed in the training mode (Blue Side Up) prevents the operator from accessing the non-eye safe modes (AIM HI, DUAL LO/HI, DUAL HI/HI).  A .050 hex head allen wrench is needed to unscrew the block from the body and re-install it in the tactical mode (Black Side Up).  Tactical mode should not be used unless authorized by the unit’s commander.

## AN/PAS-13 Thermal Weapon Sight (TWS)

- If operated with eyecup missing, light emitting from eyepiece may be visible to enemy night vision devices.

- Do not install a BA-5847 Lithium Sulfur Dioxide battery in the battery compartment.  Cover may rupture or fragment, causing serious injury in the event of battery venting.

- DO NOT crush, puncture or otherwise mutilate battery.  Avoid bringing battery into contact with water. Turn battery in to unit maintenance for disposal in accordance with unit standard operating procedures (SOP).

- The AN/PAS-13 (H/MTWS) uses a primary (non-rechargeable battery) BA-5847 battery or secondary (rechargeable) BB2847/U battery.  NEVER attempt to change a non-rechargeable battery.  To do so, may cause the battery to leak or vent.

- Ensure weapon is not loaded and safety is on before installing and removing bracket/Thermal Weapon Sight (AN/PAS-13 (H/MTWS)) to and from weapon.  A loaded weapon may accidentally discharge, causing injury or death.

- Ensure safeties are in place before sight aligning weapon.  Weapon may accidentally discharge, causing injury or death.

- Remove eye from eyecup before firing MK19 Grenade Machine Gun.  Recoil of MK19 may cause injury to personnel.

- DO NOT touch, ingest or inhale particles of a broken lens.  Lens contains germanium, which is slightly toxic if ingested or inhaled.  Glass may be sharp enough to cut personnel if touched.

- Isopropyl alcohol is flammable and toxic.  To avoid injury, keep away from open fire and use in a well-ventilated area.

## AN/PVS-4 Night Vision Sight

WARNING

To avoid equipment damage and personnel injury when using the sight, carefully read and understand the following warnings:

- The sight effectiveness is impaired by rain, fog, sleet, snow, smoke, and other reflective matter.

- DO NOT use sight without eyeguard attached or weapon recoil may cause personal injury.

- Extreme care should be taken to see that no stray light is visible from sight when in operation (to prevent detection by the enemy).

- Make sure there are no ammunition rounds in the weapon before attempting to install mounts. Weapon must be on SAFE.

- The batteries used in sight require special handling to avoid possible physical harm or equipment damage. Return all used or damaged batteries to Property Disposal.

WARNING

The BA-5567/U (lithium) battery contains sulphur dioxide gas under pressure and should be handled in the following manner:

- If the battery compartment becomes hot to touch and you hear a hissing sound (i.e., battery venting) or smell irritating sulfur dioxide gas, IMMEDIATELY turn off the equipment. Wait until battery has cooled before removing it.

- DO NOT heat, puncture, disassemble, test for capacity, short circuit, attempt to recharge, or otherwise tamper with battery.

- Batteries have a safety vent to prevent explosion.  When they are venting gas, you will smell gas, your eyes may become irritated, or you may hear the sound of gas escaping.  When safety vents have operated, batteries are fairly safe from bursting, but will be hot and must be handled with care.

WARNING

- DO NOT open plastic storage bag if card-board box inside bag is stained or there is liquid visible inside bag.

- You can tell the difference between Mercury battery, BA-1567/U, and lithium battery, BA-5567/U, by the plastic sleeve.  The lithium battery has a black band around the top and bottom of plastic sleeve.  The lithium battery may be disposed of only in a sanitary landfill.

- DO NOT use batteries which look bulged or have burst. Turn these batteries in to the Property Disposal Office. Contact your unit safety officer for help with large quantities of bulged or burst batteries.

- DO NOT use water to extinguish lithium battery fire if a shock hazard exists due to high voltage electrical equipment in the immediate vicinity (i.e., greater than 30 volts, alternating current (ac) or direct current (dc).

WARNING

DO NOT use two lithium batteries in the sight at the same time.

NBC DECONTAMINATION

- If the sight is exposed to NBC (nuclear, biological, chemical) decontamination chemicals, replace those parts of the sight that absorb the chemicals, such as the eyeguard cushion, and carrying case insert. Decontamination chemicals absorbed into these items could irritate the skin.

TOXIC MATERIAL

- The image intensifier phosphor screen contains toxic materials.

- A broken image intensifier maybe caused from damage to the sight, especially if the sight housing is cracked by force.

- If an image intensifier breaks, be extremely careful to avoid inhaling the phosphor screen material.  Do not allow the material to come in contact with the mouth or open wounds on the skin.

- If the phosphor screen material contacts your skin, wash it off immediately with soap and water.

- If you inhale/swallow any phosphor screen material, drink a lot of water, induce vomiting, and seek medical attention as soon as possible.

FIRST AID

- For first aid or artificial respiration, see FM 21- 11, First Aid for Soldiers.

## AN/PVS-10, Sight, Night Vision Sniper Scope (SNS)

WARNING

- DO NOT leave the lens caps open when SNS is not in use.  This may permit detection by the enemy.

WARNING

- Remove air pressure inside shipping/storage case by pressing pressure relief valve located near carrying handle before opening the case.

WARNING

- DO NOT mix alkaline and lithium batteries.  Failure to comply may result in injury or death.

I

WARNING

- nsure that only 1.5V batteries are used.  Use of 3.0V batteries may result in injury or damage to the sight.  DO NOT use 3.0V batteries.

WARNING

- DO NOT disassemble the SNS, or personal injury and equipment damage may result.

WARNING

- DO NOT use the sight without eye-guard attached or personal injury from weapon recoil may result.

## AN/PVS-14 Monocular Night Vision Device

WARNING

Do not carry batteries in pockets containing metal objects such as coins, keys, etc.  Metal objects can cause the batteries to short circuit and become very hot.

WARNING

Toxic Material

The image intensifier’s phosphor screen contains toxic materials.

- If an image intensifier breaks, be extremely careful to avoid inhaling the phosphor screen material.  Do not allow the material to come in contact with the mouth or open wounds on the skin.

- If the phosphor screen material contacts your skin, wash it off immediately with soap and water.

- If you inhale/swallow any phosphor screen material, drink a lot of water, induce vomiting, and seek medical attention as soon as possible.

WARNING

- The IR source is a light that is invisible to the unaided eye for use during conditions of extreme darkness.  However, the light from the IR source can be detected by the enemy using night vision devices.

WARNING

The monocular will not be turned off automatically when flipped up.  The monocular must be turned off by the power switch.

WARNING

EQUIPMENT LIMITATIONS

To avoid personal injury and property damage when using the MNVD carefully read and understand the following safety precautions.

- The MNVD requires some ambient (moonlight, starlight, or artificial light, etc.) to operate.  The level of performance depends on the level of light.

- Night light is reduced by passing cloud cover, while operating under trees, in building shadows, etc.

- The MNVD is less effective viewing into shadows and other darkened areas.

- The MNVD is less effective through rain, fog, sleet, snow, smoke, and other reflective material.

- The MNVD will not “see” through dense smoke.

WARNING

The compass illuminator can be seen by others using night vision devices.

WARNING

Do not use contaminated eyecup or eyeguard.  They must be replaced.

WARNING

When installing the headmount over the protective mask, be careful not to break the protective mask seal around your face.

The image intensifier’s phosphor screen contains toxic materials.

- If an image intensifier breaks, be extremely careful to avoid inhaling the phosphor screen material.  Do not allow the material to come in contact with the mouth or open wounds on the skin.

- If the phosphor screen material contacts your skin, wash it off immediately with soap and water.

- If you inhale/swallow any phosphor screen material, drink a lot of water, induce vomiting, and seek medical attention as soon as possible.

FIRST AID

For first aid or artificial respiration, see FM 21-11, First Aid for Soldiers.

## AN/TVS-5, Night Vision Sight

WARNING

- Do not press eyeguard except with eye area of face for operation of sight. Sight emits illumination which can be detected by enemy if eyeguard is used improperly.

- Do not use sight without eyeguard attached or personal injury from weapon recoil may result.

- The contents of the mercury batteries are extremely irritating to the eyes, oral, and nasal passages, therefore, be careful when discarding the batteries. To prevent explosion, batteries should not be disposed of by burning.

- Do not short circuit.

- Do not recharge.

- Do not store the night vision sight with the batteries in it.

- Always replace both Mercury batteries at the same time.

LITHIUM BATTERIES BA-5567

WARNING

A lithium-sulfur dioxide (Li-S02) battery used with the AN/TVS-5 contains pressurized sulfur dioxide (S02) gas. The gas is toxic, and the battery MUST NOT be abused in any way which may cause the battery to rupture.

WARNING

DO NOT heat, short circuit, crush, puncture, mutilate, or disassemble batteries.

WARNING

DO NOT USE any battery which shows signs of damage, such as bulging, swelling, disfigurement, brown liquid in the plastic wrap, a swollen plastic wrap, etc.

WARNING

DO NOT test Li-SO2 batteries for capacity.

WARNING

DO NOT recharge Li-SO2 batteries.

WARNING

DO NOT use water to extinguish Li-SO2 battery fires if a Shock hazard exists due to high voltage electrical equipment in the immediate vicinity [i.e., greater than 30 volts, alternating current (at) or direct current (dc)].

WARNING

If the battery compartment becomes hot to the touch, if you hear a hissing sound (i.e., battery venting), or smell irritating sulfur dioxide gas, IMMEDIATELY Turn Off the equipment. Remove the equipment to a well ventilated area or leave the area.

WARNING

DO NOT use a HaIon type fire extinguisher on a lithium battery fire.

WARNING

In the event of a fire, near a lithium battery(ies), rapid cooling of the battery(ies) is important. Use a carbon dioxide (CO2) extinguisher. Control of the equipment fire, and cooling, may prevent the battery from venting and potentially exposing lithium metal. In the event that lithium metal becomes involved in fire, the use of a graphite based Class D fire extinguisher is recommended, such as Lith-X or MET-L-X.

WARNING

DO NOT store lithium batteries with other hazardous materials and keep them away from open flame or heat.

CORROSIVE CHEMICAL FIRST AID

- In the event of contact with the eyes, immediately flush the eyes with water and continue to flush for 15 minutes.

  - The first few seconds after contact are critical and immediate flushing of the eyes may prevent permanent damage.

  - An eyewash fountain is preferred, but an eyewash hose or any other water source should be used in an emergency.

  - Alkali (base) burns are usually more serious than acid burns.

- Strong chemicals burn the skin rapidly.  There is no time to waste. Flush the area with water immediately. Remove and discard clothing, socks and shoes (obtain other clothes and shoes). Continue to flood the area, while clothing is being removed.

- Consult warnings on the product label for full first-aid information. Give the label information to the attending physician.

- Neutralizers and solvents (alcohol, etc.) should not be used by the first aider. The spread of skin absorbing corrosive poison, like phenol, can cause death. Don’t depend on spilled chemicals to evaporate from your clothes. Exposure of skin can kill you.

## M68 Close Combat Optic (CCO)

WARNING

At higher intensity settings, red dot is visible through front of sight. For night vision operations, close front lens cover before turning rotary switch to position 1 or 2. Check light for proper intensity before opening front lens cover. Close front lens cover before turning rotary switch counterclockwise to the OFF position. Failure to follow this warning could reveal your position to your enemy.

FIRST AID

For first aid procedures, refer to FM 21-11, First Aid for Soldiers.

## M145 Telescope, Machine Gun Optics (MGO)

This warning summary includes general safety precautions and instructions that must be understood and applied during the operation and maintenance of the Telescope to ensure personnel against injury, death, or long term health hazards.  A summary of safety and hazardous material warnings that should be heeded in conduct of operation and maintenance is provided below.

LASER LIGHT – laser light hazard symbol indicates extreme danger for eyes from laser beams and reflections.

- Use of the Telescope without laser filter is not eyesafe.

- Removal of the anti-reflection device (ARD) could lead to your detection by the enemy.

- Ensure the reticule illumination is turned to the OFF position when not required.

FIRST AID

For first aid procedures, refer to FM 21-11, First Aid for Soldiers.

# Preface

This document is intended as a Leader’s Guide and quick reference for the soldier in the field.  It is our intent to provide a clear, easy-to-use document that outlines interface requirements between weapons, their accessories and sights.  This is a reference book and not intended to replace Technical Manuals.  Detailed procedures and guidance on the operation and employment of devices is contained in the appropriate Technical Manual.  (See Annex A – References)

This book has been prepared using the most up-to-date data available and in some instances varies from the information available in fielded Technical Manuals.  When in doubt as to what configuration should be used contact the below listed point of contact for further guidance:

Commander United States Army Infantry School ATTN: ATZB-CDE Fort Benning, GA 31905-5400 Telephone: DSN 835-4952 COMM 706-545-4952

Feel free to disassemble this booklet and to reproduce those items required for training or operations.  The booklet has been formatted to specifically enhance your ability to reproduce the information contained within.

# How to Use this Booklet

Organization:

- The Small Arms Integration Book is organized into Weapon Chapters (M16A2, M4/M4A1, M4 Modular Weapon System (MWS), M16A4 Modular Weapon System (MWS), M24, M249, etc.), with sections for each of the components or sights contained in that chapter.

- Each chapter starts with an overview photo of the weapon with all applicable Sights and Accessories depicted.  Lines indicate the general location of that item on the weapon.

- Following the overview picture you will find sections for each of the components or accessories associated with that weapon (AN/PAQ-4B/C, AN/PAS-13, AN/PEQ-2A, AN/PVS-4, etc.).

- Within a given section you will find a diagram and instructions explaining how to mount or install the item on the weapon.  Next you will find 25 meter zero targets and 10 meter bore light targets.

- Annexes contained at the rear of this booklet include:

- A list of References (Annex A)

- Accessory/Component Operating Instructions (Annex B)

- Modular Weapon System Description (Annex C)

- Battery Quick Reference Guide (Annex D).

- Machine Gun/Mount Cross Reference (Annex E)

- Infantry Platoon Organization/Equipment Diagrams (Annex F)

- Borelight Alignment Procedure (Annex G)

- Target Offset Summary (Annex H)

- Acronyms and Abbreviations (Annex I).

Instructions:

- Locate your weapon in the Table of Contents.

- Locate the Sight or Accessory that you are attempting to mount or install below that weapon then turn to the designated page.

- Follow the instructions provided to install the Sight or Accessory.  Use the installation diagram and instructions to assist with your installation.

- When preparing to qualify or familiarize with a Sight or Accessory refer to the appropriate 25-meter zero target or Boresight target for correct preparation/configuration of the target for that weapon/accessory combination.

- If a confirmed boresight target is available (as indicated on the enclosed boresight targets) the firer may omit the requirement to conduct a 25-meter live fire zero confirmation for the AN/PEQ-2A and the AN/PAQ-4B/C.  If however the firer is zeroing an AN/PAS-13, Thermal Weapon Sight, or M68, Close Combat Optic, he must conduct a 25-meter live fire confirmation to ensure proper mounting and alignment of the weapon/sight.

# Integration Matrices

A checkmark indicates that the accessory or sight listed in the left-hand column is applicable to the weapon listed at the top of the table.

## Integration Matrix (Individual Wpns)

| Accessory | M16A2 | M16/ M203 | M4/A1 | M4/ M203A1 | MWS (Note 1) | MWS M203 | M24 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| AN/PAQ-4B/C | ( | ( (Note 2) | ( | ( (Note 2) | ( | ( |  |
| AN/PAS-13, TWS | ( |  | ( |  | ( |  |  |
| AN/PEQ-2A | ( |  | ( |  | ( |  |  |
| AN/PVS-4(A) | ( | ( | ( | ( | ( | ( |  |
| AN/PVS-10, SNS |  |  |  |  |  |  | ( |
| AN/PVS-14 |  |  |  |  | ( |  |  |
| AN/TVS-5 | ( |  |  |  |  |  |  |
| M68, CCO | ( | ( | ( | ( | ( | ( |  |
| M145, MGO |  |  |  |  |  |  |  |
| Optical Sight |  |  |  |  |  |  | ( |
| BIS |  |  | ( | ( | ( | ( |  |
| MILES | ( | ( | ( | ( | ( | ( | ( |

Note 1 – 	MWS-Modular Weapon System (MWS) is a generic term that is applied to either a M4 Carbine with the M4 Adapter Rail System installed, or a M16A4 Rifle with the M5 Adapter Rail System installed.

Note 2 -	When mounting the AN/PAQ-4B/C to the M203 the Grenadier must first have the Quadrant Sight removed.

## Integration Matrix (Crew Served Wpns)

| Accessory | M249 | M240B | M2 | MK19 |
| --- | --- | --- | --- | --- |
| AN/PAQ-4B/C | ( | ( (Note 3) |  |  |
| AN/PAS-13, TWS | ( | ( | ( | ( |
| AN/PEQ-2A | ( | ( | ( | ( |
| AN/PVS-4(A) | ( | ( |  |  |
| AN/PVS-10, SNS |  |  |  |  |
| AN/PVS-14 |  |  |  |  |
| AN/TVS-5 |  |  | ( | ( |
| M68, CCO |  |  |  |  |
| M145, MGO | ( (Note 4) | ( |  |  |
| BIS |  |  |  |  |
| MILES | ( | ( | ( |  |

Note 3 – 	Objective configuration would be with the AN/PEQ-2A, however, the AN/PAQ-4B/C may be used if the AN/PEQ-2A is unavailable.

Note 4 – 	The MGO will be used on the M249 only when the M249 is employed in the Light Machine Gun role.

# Table of Contents

Warnings	iii

General Warnings	iii

AN/PAQ-4B/C Light, Aiming, Infrared	iii

AN/PEQ-2A Laser Pointers/Illuminators	v

AN/PAS-13 Thermal Weapon Sight (TWS)	viii

AN/PVS-4 Night Vision Sight	ix

AN/PVS-10, Sight, Night Vision Sniper Scope (SNS)	xiii

AN/PVS-14 Monocular Night Vision Device	xv

AN/TVS-5, Night Vision Sight	xviii

M68 Close Combat Optic (CCO)	xxii

M145 Telescope, Machine Gun Optics (MGO)	xxiii

Preface	xxiv

How to Use this Booklet	xxv

Integration Matrices	xxvii

Integration Matrix (Individual Wpns)	xxvii

Integration Matrix (Crew Served Wpns)	xxviii

Table of Contents	xxix

Individual Weapons	1

M16A2 Rifle	1

M16A2—Iron Sight Target, 10m Boresight Target	2

M16A2—AN/PAQ-4B/C Mounting Instructions and Targets	3

M16A2—AN/PAQ-4B/C Zero and Boresight Targets	4

M16A2—AN/PAS-13 Mounting Instructions and Targets	6

M16A2—AN/PAS-13 (H/MTWS) Zero and Boresight Targets	8

M16A2—AN/PEQ-2A Mounting Instructions and Targets	10

M16A2—AN/PEQ-2A Zero and Boresight Targets	11

M16A2—AN/PVS-4 Mounting Instructions and Targets	13

M16A2—AN/PVS-4 Zero and Boresight Targets	14

M16A2—M68 Mounting Instructions and Targets	16

M16A2—CCO Zero and Boresight Targets	17

M16/M203 Grenade Launcher	19

M16/M203—AN/PAQ-4B/C Mounting Instructions and Targets	20

M16/M203—AN/PAQ-4B/C Zero and Boresight Targets	21

M16/M203—AN/PVS-4 Mounting Instructions and Targets	23

M16/M203—AN/PVS-4 Zero and Boresight Targets	24

M4/M4A1 Carbine	26

M4/M4A1—Iron Sight Target	27

M4/M4A1—AN/PAQ-4B/C Mounting Instructions and Targets	28

M4/M4A1—AN/PAQ-4B/C Zero and Boresight Targets	29

M4/M4A1—AN/PAS-13 Mounting Instructions and Targets	31

M4/M4A1—AN/PAS-13 Zero and Boresight Targets	32

M4/M4A1—AN/PEQ-2A Mounting Instructions and Targets	34

M4/M4A1—AN/PEQ-2A Zero and Boresight Target	35

M4/M4A1—AN/PVS-4 Mounting Instructions and Targets	37

M4/M4A1—AN/PVS-4 Zero and Boresight Targets	38

M4/M4A1—AN/PVS-4 Zero and Boresight Targets	39

M4/M4A1—M68 Mounting Instructions and Targets	41

M4/M4A1—CCO Zero and Boresight Targets	42

M4/M203 Grenade Launcher	44

M4/M203 Back Up Iron Sight 10m Boresight Target Offset	45

M4/M203—AN/PAQ-4B/C Mount Procedures	46

M4/M203—AN/PAQ-4B/C Zero and Boresight Targets	47

M4/M203—AN/PVS-4 Mount Procedures	49

M4/M203—AN/PVS-4 Zero and Boresight Targets	49

M4/M203—AN/PVS-4 Zero and Boresight Targets	50

Modular Weapon System, M4 MWS	52

M4 MWS Back Up Iron Sight Boresight Target	53

M4 MWS—AN/PAQ-4B/C Mounting Instructions and Targets Utilizing Mounting Bracket/Picatinny Rail Grabber	54

M4 MWS—AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Left Rail)	55

M4 MWS—AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Top Rail)	57

M4 MWS—AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Right Rail)	59

M4 MWS—AN/PAQ-4B/C Mounting Instructions and Targets Utilizing “Insight” Low Profile Rail Grabber	61

M4 MWS—AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Left Rail)	63

M4 MWS—AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Top Rail)	65

M4 MWS—AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Right Rail)	67

M4 MWS—AN/PAS-13 (Medium/Heavy) Mounting Instructions and Targets	69

M4 MWS—AN/PAS-13 Zero and Boresight Targets	70

M4 MWS—AN/PEQ-2A Mounting Instructions and Targets Utilizing Mounting Bracket/Picatinny Rail Grabber	72

M4 MWS—AN/PEQ-2A Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Left Rail)	74

M4 MWS—AN/PEQ-2A Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Top Rail)	76

M4 MWS—AN/PEQ-2A Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Right Rail)	78

M4 MWS—AN/PEQ-2A Mounting Instructions and Targets Utilizing “Insight” Low Profile Rail Grabber	80

M4 MWS—AN/PEQ-2A Targets Utilizing “Insight” Low Profile Rail Grabber (Left Rail)	81

M4 MWS—AN/PEQ-2A Targets Utilizing “Insight” Low Profile Rail Grabber (Top Rail)	83

M4 MWS—AN/PEQ-2A Targets Utilizing “Insight” Low Profile Rail Grabber (Right Rail)	85

M4 MWS—AN/PVS-14 Mounting Instructions and Targets	87

M4 MWS—AN/PVS-4 Mounting Instructions and Targets	89

M4 MWS—AN/PVS-4 Zero and Boresight Targets	89

M4 MWS—AN/PVS-4 Zero and Boresight Targets	90

M4 MWS—M68 Mounting Instructions and Targets	92

M4 MWS—M68 CCO Zero and Boresight Targets	93

M4 MWS M203 Grenade Launcher	95

M4/M203 Back Up Iron Sight 10m Boresight Target Offset	96

Mounting—M203 w/Quick Release Bracket to the M4 Carbine	97

M4 MWS M203 —AN/PAQ-4B/C Mounting Instructions and Targets Utilizing Mounting Bracket/Picatinny Rail Grabber	103

M4 MWS M203 —AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Left Rail)	104

M4 MWS M203 —AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Top Rail)	106

M4 MWS M203 —AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Right Rail)	108

M4 MWS M203 —AN/PAQ-4B/C Mounting Instructions and Targets Using “Insight” Low Profile Rail Grabber	110

M4 MWS M203 —AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Left Rail)	111

M4 MWS M203 —AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Top Rail)	113

M4 MWS M203 —AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Right Rail)	115

M4 MWS/M203—AN/PVS-4 Mount Procedures	117

M4 MWS/M203—AN/PVS-4 Zero and Boresight Targets	118

M16A4 MWS	119

M16A4 MWS	120

M16A4 MWS Back Up Iron Sight Boresight Target	121

M16A4 MWS—AN/PAQ-4B/C Mounting Instructions and Targets Utilizing Mounting Bracket/Picatinny Rail Grabber	122

M16A4 MWS—AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Left Rail)	123

M16A4 MWS—AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Top Rail)	125

M16A4 MWS—AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Right Rail)	127

M16A4 MWS—AN/PAQ-4B/C Mounting Instructions and Targets Utilizing “Insight” Low Profile Rail Grabber	129

M16A4 MWS—AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Left Rail)	131

M16A4 MWS—AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Top Rail)	133

M16A4 MWS—AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Right Rail)	135

M16A4 MWS—AN/PAS-13 (Medium/Heavy) Mounting Instructions and Targets	137

M16A4 MWS—AN/PAS-13 Zero and Boresight Targets	138

M16A4 MWS—AN/PEQ-2A Mounting Instructions and Targets Utilizing Mounting Bracket/Picatinny Rail Grabber	140

M16A4 MWS—AN/PEQ-2A Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Left Rail)	142

M16A4 MWS—AN/PEQ-2A Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Top Rail)	144

M16A4 MWS—AN/PEQ-2A Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Right Rail)	146

M16A4 MWS—AN/PEQ-2A Mounting Instructions and Targets Utilizing “Insight” Low Profile Rail Grabber	148

M16A4 MWS—AN/PEQ-2A Targets Utilizing “Insight” Low Profile Rail Grabber (Left Rail)	149

M16A4 MWS—AN/PEQ-2A Targets Utilizing “Insight” Low Profile Rail Grabber (Top Rail)	151

M16A4 MWS—AN/PEQ-2A Targets Utilizing “Insight” Low Profile Rail Grabber (Right Rail)	153

M16A4 MWS—AN/PVS-14 Mounting Instructions and Targets	155

M16A4 MWS—AN/PVS-4 Mounting Instructions and Targets	156

M16A4 MWS—AN/PVS-4 Zero and Boresight Targets	156

M16A4 MWS—AN/PVS-4 Zero and Boresight Targets	157

M16A4 MWS—M68 Mounting Instructions and Targets	159

M16A4 MWS—M68 Targets	160

M16A4 MWS M203 Grenade Launcher	162

M4/M203 Back Up Iron Sight 10m Boresight Target Offset	163

Mounting—M203 w/Quick Release Bracket to the M16A4 Rifle	164

M16A4 MWS M203 —AN/PAQ-4B/C Mounting Instructions and Targets Utilizing Mounting Bracket/Picatinny Rail Grabber	172

M16A4 MWS M203 —AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Left Rail)	173

M16A4 MWS M203 —AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Picatinny Rail Grabber (Top Rail)	175

M16A4 MWS M203 —AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Picatinny Rail Grabber (Right Rail)	177

M16A4 MWS M203 —AN/PAQ-4B/C Mounting Instructions and Targets Using “Insight” Low Profile Rail Grabber	179

M16A4 MWS M203 —AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Left Rail)	180

M16A4 MWS M203 —AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Top Rail)	182

M16A4 MWS M203 —AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Right Rail)	184

M16A4 MWS/M203—AN/PVS-4 Mount Procedures	186

M16A4 MWS/M203—AN/PVS-4 Zero and Boresight Targets	187

M24 System Diagram	189

M24—Sniper System Day Optic Mounting Instructions	190

M24—AN/PVS-10, Sight, Night Vision Sniper Scope Mount Procedures	192

M24—AN/PVS-10 Zero Procedure	193

M24—AN/PVS-10 Zero Procedure	194

M249 Machine Gun System/Squad Automatic Weapon Diagram	195

M249 Iron Sight 25m Zero and 10m Boresight Target Offsets	196

M249—AN/PAQ-4B/C Mount Procedures Mounting Bracket/Picatinny Rail Grabber on Feed Tray Cover Rail	198

M249—AN/PAQ-4B/C Zero and Boresight Tgts, Mounting Bracket/Picatinny Rail Grabber on Feed Tray Cover Rail	199

M249—AN/PAQ-4B/C Mount Procedures “Insight” Low Profile Rail Grabber on Feed Tray Cover Rail	201

M249—AN/PAQ-4B/C Zero and Boresight Tgts, “Insight” Low Profile Rail Grabber on Feed Tray Cover Rail	202

M249—AN/PAQ-4B/C Mounting Instructions w/ AN/PVS-4 Mounting Bracket & Plastic AN/PAQ-4B/C Bracket Adapter	204

M249—AN/PAQ-4B/C Zero and Boresight Targets Using AN/PVS-4 Mounting Bracket	205

M249 —AN/PAQ-4B/C Mounting Instructions Utilizing Mounting Bracket/Picatinny Rail Grabber on Forward Rails	207

M249 —AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber on Left Rail	208

M249 —AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber on Right Rail	210

M249 —AN/PAQ-4B/C Mounting Instructions Utilizing “Insight” Low Profile Rail Grabber on Forward Rails	212

M249 —AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber on Left Rail	213

M249 —AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber on Right Rail	215

M249—AN/PAS-13 TWS Mount Procedures, Feed Tray Cover Rail	217

M249—AN/PAS-13 TWS Zero and Boresight Targets, Feed Tray Cover Rail	218

M249—AN/PEQ-2A Mount Procedures, Integrated Feed Tray Cover	220

M249—AN/PEQ-2A Targets w/ Mounting Bracket/Picatinny Rail Grabber on Feed Tray Cover Rail	221

M249—AN/PEQ-2A Targets w/ “Insight” Low Profile Rail Grabber on Feed Tray Cover Rail	223

M249—AN/PEQ-2A Mount Procedures Using AN/PVS-4—M249 Mounting Bracket	225

M249—AN/PEQ-2A Zero and Boresight Targets, (With AN/PVS-4 Mount)	226

M249—AN/PEQ-2A Mounting Instructions Utilizing Mounting Bracket/Picatinny Rail Grabber on Forward Rails	228

M249—AN/PEQ-2A Targets, Using Mounting Bracket/Picatinny Rail Grabber on Left Rail	229

M249—AN/PEQ-2A Targets, Using Mounting Bracket/Picatinny Rail Grabber on Right Rail	231

M249 —AN/PEQ-2A Mounting Instructions Utilizing “Insight” Low Profile Rail Grabber on Forward Rails	233

M249—AN/PEQ-2A Targets, Using “Insight” Low Profile Rail Grabber on Left Rail	234

M249—AN/PEQ-2A Targets, Using “Insight” Low Profile Rail Grabber on Right Rail	236

M249—AN/PVS-4 Mount Procedures, Integrated Feed Tray Cover	238

M249—AN/PVS-4 Zero and Boresight Targets, Feed Tray Cover Rail	239

M249—AN/PVS-4 Mount Procedures, Units without AN/PAS-13 (H/MTWS)	241

M249—AN/PVS-4 Zero and Boresight Targets, with AN/PVS-4 Bracket	242

M249—M145 MGO Mount Procedures, Integrated Feed Tray Cover Rail	244

M249—M145 MGO Zero and Boresight Targets, Feed Tray Cover Rail	245

M60 Machine Gun System Diagram	247

M60—AN/PAQ-4B/C Mount Procedures	248

M60—AN/PAQ-4 B/C Zero and Boresight Targets	250

M60—AN/PAS-13 (MTWS) Mount Procedures	252

M60—AN/PAS-13 Zero and Boresight Targets	253

M60—AN/PEQ-2A Mount Procedures	255

M60—AN/PEQ-2A Zero and Boresight Targets	257

M60—AN/PVS-4 Mount Procedures	259

M60—AN/PVS-4 Zero and Boresight Targets	261

M60—M145, Machine Gun Optic, Mount Procedures	263

M60—M145 MGO Zero and Boresight Targets	264

M240B Machine Gun System Diagram	266

M240B Iron Sight 25m Zero and 10m Boresight Offset Targets	267

M240B—AN/PAQ-4B/C Mount Procedures, Feed Tray Cover Rail	269

M240B—AN/PAQ-4B/C Targets Using Mounting Bracket/Picatinny Rail Grabber on Feed Tray Cover Rail	270

M240B—AN/PAQ-4B/C Targets Using “Insight” Low Profile Rail Grabber on Feed Tray Cover Rail	272

M240B—AN/PAQ-4B/C Mounting Instructions Utilizing Mounting Bracket/Picatinny Rail Grabber on Forward Rails	274

M240B—AN/PAQ-4B/C Targets Using Mounting Bracket/Picatinny Rail Grabber on Left Rail	275

M240B—AN/PAQ-4B/C Targets Using Mounting Bracket/Picatinny Rail Grabber on Right Rail	277

M240B —AN/PAQ-4B/C Mounting Instructions Utilizing “Insight” Low Profile Rail Grabber on Forward Rails	279

M240B—AN/PAQ-4B/C Targets Using “Insight” Low Profile Rail Grabber on Left Rail	280

M240B—AN/PAQ-4B/C Targets Using “Insight” Low Profile Rail Grabber on Right Rail	282

M240B—AN/PAS-13 (MTWS) Mount Procedures	284

M240B—AN/PAS-13 Zero and Boresight Targets	286

M240B—AN/PEQ-2A Mount Procedures on Feed Tray Cover Rail	288

M240B—AN/PEQ-2A Targets Using Mounting Bracket/Picatinny Rail Grabber on Feed Tray Cover Rail	289

M240B—AN/PEQ-2A Targets Using “Insight” Low Profile Rail Grabber on Feed Tray Cover Rail	291

M240B—AN/PEQ-2A Mounting Instructions Utilizing Mounting Bracket/Picatinny Rail Grabber on Forward Rails	293

M240B—AN/PEQ-2A Targets Using Mounting Bracket/Picatinny Rail Grabber on Left Rail	294

M240B—AN/PEQ-2A Targets Using Mounting Bracket/Picatinny Rail Grabber on Right Rail	296

M240B—AN/PEQ-2A Mounting Instructions Utilizing “Insight” Low Profile Rail Grabber on Forward Rails	298

M240B—AN/PEQ-2A Targets Using “Insight” Low Profile Rail Grabber on Left Rail	299

M240B—AN/PEQ-2A Targets Using “Insight” Low Profile Rail Grabber on Right Rail	301

M240B—AN/PVS-4 Mount Procedures	303

M240B—AN/PVS-4 Zero and Boresight Targets	304

M240B—M145, Machine Gun Optic, Mount Procedures	306

M240B—MGO Zero and Boresight Targets	307

M2 Machine Gun System Diagram	309

M2 MG Iron Sight Offset Target	310

M2—AN/PAS-13 (HTWS) Mount Procedures	312

M2—AN/PAS-13 Zero and Boresight Targets	314

M2—AN/PEQ-2A Mount Procedures	316

M2—AN/PEQ-2A Zero and Boresight Targets	317

M2—AN/TVS-5 Mount Procedures	319

M2—AN/TVS-5 Zero and Boresight Targets	320

MK19 Grenade Machine Gun System Diagram	322

MK19 Grenade Machine Gun Iron Sight Target Offset	323

MK19—AN/PAS-13 (HTWS) Mount Procedures	325

MK19—AN/PAS-13, TWS Zero and Boresight Targets	327

MK19—AN/PEQ-2A Mount Procedures	329

MK19—AN/PEQ-2A Zero and Boresight Targets	330

MK19—AN/TVS-5 Mount Procedures	332

MK19—AN/TVS-5 Zero and Boresight Targets	333

Annex A—References	335

Annex B—Sight/Accessory Operating Instructions	337

AN/PAQ-4B/C, Light Aiming, Infrared	337

AN/PAS-13 Thermal Weapon Sight	341

AN/PAS-13 Zero and Boresight Targets Preparation Procedures	343

AN/PEQ-2A, Target Pointer Illuminator/Aiming Light (TPIAL)	345

AN/PVS-4, Night Vision Sight, Individual Served Weapon	352

AN/PVS-10, Sight, Night Vision Sniper Scope (SNS)	355

AN/PVS-14, Monocular Night Vision Device	359

AN/TVS-5, Night Vision Sight, Crew Served Weapon	362

M203 Grenade Launcher	365

M68-Close Combat Optic	367

M145 Machine Gun Optic	371

M145, MGO Zero Procedures	374

MILES – Multiple Integrated Laser Engagement System	377

Annex C—Modular Weapon System Reference Data	383

M4 Carbine Version	383

M16 Version Modular Weapon System	385

M203 Components-Modular Weapon System	387

Annex D—Battery Quick Reference Guide	390

Annex E-Machine Gun/Mount Cross Reference	392

Annex F—Infantry Platoon Equipment/Organization Guide	395

Airborne/Air Assault Infantry Platoon	395

Light Infantry Platoon	397

Mechanized Infantry Platoon (Bradley)	399

Force XXI (3x9) Mechanized Infantry Platoon	401

IBCT Infantry Platoon	404

Annex G—Borelight Dry Zero Procedures	406

Annex H—Target Offset Summary	421

Annex I—Acronyms and Abbreviations	442

# Individual Weapons

## M16A2 Rifle

### M16A2—Iron Sight Target, 10m Boresight Target

### M16A2—AN/PAQ-4B/C Mounting Instructions and Targets

# M16A2 – AN/PAQ-4B/C Mounting Instructions

The AN/PAQ-4B/C is mounted to the M16A2 using the M4/M16A2 Bracket Assembly, Part No. A3186958, NSN 5340-01-390-3812.  Only a Small Arms Repairman MOS 45B may install the Bracket Assembly (comprising the bracket and bracket caps, hidden under hand guards, and the mounting rail).

- Install mounting rail through top hand guard to barrel mounting bracket.  (Note:  Unit armorer installs mounting bracket.)

- Place the switch lever shroud over the mounting rail.

- Secure the AN/PAQ-4B/C to the rail with the thumbscrew.

- Attach the remote switch, at a comfortable location, using the provided cable hangers

# NOTE

# When mounting the AN/PAQ-4B/C in conjunction with a MILES device a Training Extender (Part No. A3267739) must be attached to the mounting rail before attaching the AN/PAQ-4B/C.  This allows the laser beam to clear the MILES device.

#### M16A2—AN/PAQ-4B/C Zero and Boresight Targets

### M16A2—AN/PAS-13 Mounting Instructions and Targets

M16A2 – AN/PAS-13 Mounting Instructions

(See Annex B for Target Prep Instructions)

The AN/PAS-13, TWS is mounted to the M16A2 using the M16A2 Bracket Assembly (Part No. 80063-A3170580) IAW TM 11-5855-302-12&P.

NOTE : For the M16A2 rifle, ensure rear sight is lowered (elevation knob turned fully counter-clockwise).

- Install M16A2 bracket (1) on weapon handle (5).

  - Place threaded rod (3) of bracket (1) through hole (4) of weapon handle (5).

  - Install thumbwheel (6) on threaded rod (3) and hand tighten.Install TWS (7) on rail (8).

- Loosen knob (9) on mount (10).

- Select slot (11) on rail (8) for mounting.  Any slot may be used as long as mount (10) does not hang over edge of rail.

- Place bar (12) of mount (10) in slot (11) of rail (8) and hand tighten knob (9) on mount until two clicks are heard.

NOTE:  Rail grabber/mount (10) is shown up-side-down in the diagram at left in order to show item 12 more clearly.  The rail grabber/mount will normally already be attached to the TWS by the unit armorer prior to the soldier receiving the sight.

#### M16A2—AN/PAS-13 (H/MTWS) Zero and Boresight Targets

### M16A2—AN/PEQ-2A Mounting Instructions and Targets

# M16A2 – AN/PEQ-2A Mounting Instructions

The AN/PEQ-2A is mounted to the M16A2 using the M4/M16A2 Bracket Assembly, Part No. A3186958, NSN 5340-01-390-38112.  The Bracket Assembly (comprising the bracket and bracket caps, hidden under hand guards, and the mounting rail) may only be installed by a Small Arms Repairman MOS 45B.

1.  Install mounting rail through top hand guard to barrel mounting bracket.  (Note:  Unit armorer installs mounting bracket.)

2.  Secure the AN/PEQ-2A to the rail with the thumbscrew. (Hand Tight)

3.  Attach the remote switch, at a comfortable location, using the provided cable hangers

# NOTE

When mounting the AN/PEQ-2A in conjunction with a MILES device a Training Extender (Part No. A3267739) must be attached to the mounting rail before attaching the AN/PEQ-2A.  This allows the laser beams to clear the MILES device.

#### M16A2—AN/PEQ-2A Zero and Boresight Targets

### M16A2—AN/PVS-4 Mounting Instructions and Targets

###### M16A2 – AN/PVS-4 Mounting Instructions

The AN/PVS-4 is mounted to the M16A2 using Mounting Knob Assembly (NSN 5355-01-039-2834) per instructions contained in TM 11-5855-213-10.

1.	Position the sight in the groove on top of the carrying handle and align the threaded hole in the base of the sight-mounting adapter over the hole in the handle.

2.	Insert the mounting knob assembly in the hole in the handle and turn firmly clockwise into sight mounting adapter.

3.	If difficulty is encountered, turn the sight and the rifle upside down.  Place the rifle handle onto the sight-mounting adapter, lining up the hole in the handle onto the sight-mounting adapter.  Place the mounting knob assembly through the hole in the handle and rotate clockwise.

# NOTE:  Continually check tightness of mounting knob during weapon firing.

NOTE:  Insure that you use the correct Mounting Knob Assembly for the M16, not the M60 Knob, which looks very similar.

#### M16A2—AN/PVS-4 Zero and Boresight Targets

### M16A2—M68 Mounting Instructions and Targets

###### M16A2 – M68, CCO Mounting Instructions

The CCO is mounted to the M16 using sight mount (Components 1,2 and 3) (NSN 1240-01-410-7427) as outlined in TM 9-1240-413-12&P.

- The Close Combat Optic is attached to the M16A2 by using the “Gooseneck” rail (1) depicted to the left.

- Attach the gooseneck mounting bracket to the weapon’s carrying handle using O-Ring (2) and mounting bolt (3).

- Place the CCO (4) atop the mounting bracket.

- Using the thumbscrew (5) on the CCO rail grabber/mount attach the CCO to the mounting bracket.  Tighten thumbscrew until it snaps two times.

# NOTE:  The half-moon shaped spacer should not be installed when mounting the CCO to the M16A2.

#### M16A2—CCO Zero and Boresight Targets

## M16/M203 Grenade Launcher

M16A2 Grenade Launcher Mounting Instructions

The M203 Grenade Launcher must be mounted to the M16A2 by the unit’s armorer IAW TM 9-1010-221-23&P

Individual soldiers should not attempt to either mount or dismount the grenade launcher to the weapon.

### M16/M203—AN/PAQ-4B/C Mounting Instructions and Targets

M203 – AN/PAQ-4B/C Mounting Instructions

Mounting of the AN/PAQ-4B/C to the M203 is accomplished by using the Mounting Knob Assembly from the AN/PVS-4 Sight (NSN 5355-01-039-2834) and the Bracket Adapter (plastic) from the AN/PAQ-4B/C (NSN 5340-01-362-9873).

- Attach the AN/PAQ-4B/C Bracket Adapter to the M16A2 carrying handle of the M203 using the AN/PVS-4 Mounting Knob Assembly.

- Secure the AN/PAQ-4B/C to the Bracket Adapter, using the thumbscrew on the AN/PAQ-4B/C.

- Attach the remote switch to the AN/PAQ-4B/C and locate the switch at a convenient location.

Note:  The laser designator and quadrant sights cannot be mounted at the same time.

#### M16/M203—AN/PAQ-4B/C Zero and Boresight Targets

### M16/M203—AN/PVS-4 Mounting Instructions and Targets

M203 – AN/PVS-4 Mounting Instructions

The AN/PVS-4 is mounted to the M203 using Mounting Bracket Assembly (NSN 5855-01-039-2835) IAW TM 11-5855-213-10.

NOTE

Wingnuts, flat washers and clamp plate cannot be removed.

- Remove the grenade launcher quad sight, if installed (Refer to TM 9-1005-249-10).

- Position the mounting bracket assembly on the left side of the rifle so that the two clamp plates project through the opening under the handle; wingnuts should be fully loosened.

- Turn the clamp plates so that the pointed ends are in the up position and seated against the handle.

- Tighten the wingnuts clockwise until the mounting bracket is secured firmly to the weapon.

- Position the sight in the groove on top of the bracket and align the threaded hole in the base of the sight mounting adapter with the lever screw assembly.  Tighten the screw firmly clockwise to secure the sight to the bracket.

- Set the bracket range to coincide with the target distance.

#### M16/M203—AN/PVS-4 Zero and Boresight Targets

## M4/M4A1 Carbine

### M4/M4A1—Iron Sight Target

### M4/M4A1—AN/PAQ-4B/C Mounting Instructions and Targets

M4/M4A1 – AN/PAQ-4B/C Mounting Instructions

The AN/PAQ-4B/C is mounted to the M4 using the M4/M16A2 Bracket Assembly, Part No. A3186958, NSN 5340-01-390-3812.  The Bracket Assembly (comprising the bracket and bracket caps, hidden under hand guards, and the mounting rail) may only be installed by a Small Arms Repairman MOS 45B.

- Install mounting rail through top hand guard to barrel clamp. (Unit Armorer Installed.)

- Place the switch lever shroud over the mounting rail.

- Secure the AN/PAQ-4B/C to the rail with the thumbscrew.

- Attach the remote switch, at a comfortable location, using the provided cable hangers

NOTE

When mounting the AN/PAQ-4B/C in conjunction with a MILES device a Training Extender (Part No. A3267739) must be attached to the mounting rail before attaching the AN/PAQ-4B/C.  This allows the laser beams to clear the MILES device

#### M4/M4A1—AN/PAQ-4B/C Zero and Boresight Targets

### M4/M4A1—AN/PAS-13 Mounting Instructions and Targets

###### M4/M4A1 – AN/PAS-13, TWS Mounting Instructions

(See Annex B for Target Prep Instructions)

Install the AN/PAS-13 TWS on the M4/M4A1 using the 7/8” spacer (5) (part number 80063-A3268346) and TWS rail grabber/mount (80063-A3170556).  (These items will have already been installed on the AN/PAS-13 by the unit Armorer IAW TM 11-5855-302-12&P.

- Loosen two knobs (1) on carrying handle (2) and remove carrying handle from rail (3) of M4/M4A1 Carbine (4).  Retain carrying handle.

- Spacer (5) and rail grabber/mount (6) are attached to the TWS (7).

- Select a slot on rail (3) for mounting.  Any slot may be used as long as rail grabber/mount does not hang over edge of rail.

- Loosen rail grabber prior to attempting to mount. Place rail grabber/mount on rail and tighten rail grabber/mount knob (8) until two clicks are heard.

NOTE:  Although a M4 Carbine is depicted in the picture to the left mounting procedures are identical for the M4, M16A4, M4 MWS, and M16A4 MWS.

#### M4/M4A1—AN/PAS-13 Zero and Boresight Targets

### M4/M4A1—AN/PEQ-2A Mounting Instructions and Targets

M4/M4A1 – AN/PEQ-2A Mounting Instructions

The AN/PAQ-4B/C is mounted to the M4 using the M4/M16A2 Bracket Assembly, Part No. A3186958, NSN 5340-01-390-38112.  The Bracket Assembly (comprising the bracket and bracket caps, hidden under hand guards, and the mounting rail) may only be installed by the Small Arms Repairman MOS 45B.

- Install mounting rail through top hand guard to barrel clamp. (Unit Armorer Installed.)

- Secure the AN/PEQ-2A to the rail with the thumbscrew.

- Attach the remote switch, at a comfortable location, using the provided cable hangers.

NOTE

When mounting the AN/PEQ-2A in conjunction with a MILES device a Training Extender (Part No. A3267739) must be attached to the mounting rail before attaching the AN/PEQ-2A.  This allows the laser beams to clear the MILES device

#### M4/M4A1—AN/PEQ-2A Zero and Boresight Target

### M4/M4A1—AN/PVS-4 Mounting Instructions and Targets

M4/M4A1 – AN/PVS-4 Mounting Instructions

In order to properly mount the AN/PVS-4 to the M4 Carbine the unit Armorer must first install a spacer (NSN 5365-01-447-8991) and a rail grabber/mount (NSN 5340-01-449-8533).

- Loosen two knobs (1) on carrying handle (2).  Remove carrying handle from upper receiver rail (3).  Retain carrying handle.

Note

Spacer (5) and Grabber/Mount (6) are pre-assembled to the Sight (7) Unit Armorer.

- Loosen the clamping knob (8) until sufficient space exits to place the clamping jaws on

either side of the mounting rail (3).  Tighten clamping knob (8) until two clicks are heard.

- The AN/PVS-4 may be placed wherever on the upper receiver rail is most convenient for the operator, as long as the rail grabber/mount does not extend beyond the rail.

- If the AN/PVS-4 is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

- Item (6) is depicted upside down in order to clearly show the bar, which must fit, into one of the slots on the rail.

#### M4/M4A1—AN/PVS-4 Zero and Boresight Targets

### M4/M4A1—M68 Mounting Instructions and Targets

M4/M4A1 – M68, CCO Mounting Instructions

The sight assembly mounts directly to the accessory mounting rail on top of the M4/M4A1 and M16A4. The mount is not required. Make sure the spacer (1) has been installed before mounting M68 on the M4/M4A1 or M16A4.

- Loosen two knobs on carrying handle item and remove it from the rail (3) of the  M4 Carbine.  Retain carrying handle.

- Install CCO (2) on rail (3).

  - Loosen knob (4) on rail grabber/mount (2) until sufficient space exists to fit the jaws on either side of the rail (3).

  - Select slot on rail (3) for mounting.  Any slot may be used as long as rail grabber/mount does not hang over edge of rail.

  - Place rail grabber/mount on rail and tighten knob (4) until two clicks are heard.

NOTE:  When placing the CCO on the M4/M16A4 the unit Armorer must first install the half-moon shaped spacer on the CCO IAW TM 9-1240-413-12&P.

#### M4/M4A1—CCO Zero and Boresight Targets

## M4/M203 Grenade Launcher

M4 Grenade Launcher Mounting Instructions

The M203A1 Grenade Launcher must be mounted to the M4 by the unit’s supporting DS Maintenance Company IAW instructions contained in TM 9-1010-221-23&P.

#### M4/M203 Back Up Iron Sight 10m Boresight Target Offset

### M4/M203—AN/PAQ-4B/C Mount Procedures

M4/M203 – AN/PAQ-4B/C Mounting Instructions

Mounting of the AN/PAQ-4B/C (1) to the M203 (2) is accomplished by using the Mounting Knob Assembly (3) from the AN/PVS-4 Sight (NSN 5355-01-039-2834) and the Bracket Adapter (plastic) (4) from the AN/PAQ-4B/C (NSN 5340-01-362-9873).

- Remove the M203A1 Quadrant Sight (5).  (The Quadrant Sight and the AN/PAQ-4B/C cannot be mounted at the same time.

- Attach the AN/PAQ-4B/C Bracket Adapter to the M4 carrying handle of the M203 using the AN/PVS-4 Mounting Knob Assembly.  Angle the Mounting Knob through the hole in the top of the Carrying Handle.  Place the Bracket Adapter over the hole and attach it to the handle with the Mounting Knob Assembly.

- Secure the AN/PAQ-4B/C to the Bracket Adapter, using the thumbscrew on the AN/PAQ-4B/C.

- Attach the remote switch (6) to the AN/PAQ-4B/C and locate the switch at a convenient location.

Note:  The AN/PAQ-4B/C will be oriented to designate targets for the Rifle, not the Grenade Launcher.

#### M4/M203—AN/PAQ-4B/C Zero and Boresight Targets

### M4/M203—AN/PVS-4 Mount Procedures

M4/M203 – AN/PVS-4 Mounting Instructions

- Loosen two knobs (1) on carrying handle (2).  Remove carrying handle from upper receiver rail (3).  Retain carrying handle.

Note

Spacer (5) (NSN 5365-01-447-8991) and Grabber/Mount (6) (NSN 5340-01-449-8533) are pre-assembled to the Sight (7) by Unit Armorer.

- Loosen the clamping knob (8) until sufficient space exits to place the clamping jaws on either side of the mounting rail (3).  Tighten clamping knob (8) until two clicks are heard.

- The AN/PVS-4 may be placed at whichever position on the upper receiver rail is most convenient for the operator, as long as the rail grabber/mount does not extend beyond the rail.

- If the AN/PVS-4 is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

- You can not mount both the AN/PVS-4 and quadrant sights at the same time.

NOTE:  Item (6) is depicted upside down in order to clearly show the bar, which must fit, into one of the slots on the rail.

#### M4/M203—AN/PVS-4 Zero and Boresight Targets

## Modular Weapon System, M4 MWS

### M4 MWS Back Up Iron Sight Boresight Target

### M4 MWS—AN/PAQ-4B/C Mounting Instructions and Targets Utilizing Mounting Bracket/Picatinny Rail Grabber

###### M4 MWS – AN/PAQ-4B/C Mounting Instructions

The AN/PAQ-4B/C may be mounted on the left, top or right side rails using the Mounting Bracket/Picatinny Rail Grabber (NSN 5340-01-458-0473) depicted in the diagram at left.

- Attach the Mounting Bracket/Picatinny Rail Grabber(1) to the AN/PAQ-4B/C (2) using the thumbscrew on the AN/PAQ-4B/C.

- Loosen the clamping knob until the rail grabber/mount has sufficient space to fit over the left side rail (3).  Tighten the clamping knob until two clicks are heard.

- The AN/PAQ-4B/C may be placed at whichever position, on the left side rail, is most convenient for the operator.  If however the AN/PAQ-4B/C is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

- Install the remote switch in a convenient location using the provided cable hangers.

The AN/PAQ-4B/C may also be mounted on the top or right rails, following the procedure laid out above.  Supporting target offsets for each configuration follow:

#### M4 MWS—AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Left Rail)

#### M4 MWS—AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Top Rail)

#### M4 MWS—AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Right Rail)

### M4 MWS—AN/PAQ-4B/C Mounting Instructions and Targets Utilizing “Insight” Low Profile Rail Grabber

The Aiming Light is mounted on the front left-hand rail using the Insight rail grabber bracket when it is desired to keep the Aiming Light as close as possible to the barrel.

WARNING

Make sure the weapon is CLEAR and on SAFE before proceeding.

- Loosen the clamping knob until the rail grabber has sufficient space to fit over the left side rail. Hand Tighten the clamping knob.

- Turn the ON/OFF Switch CCW to the #1 OFF/STORAGE position.

- Position the Aiming Light on the bracket mounting rail. Hand tighten the Thumbscrew to secure the Aiming Light.

- Install the remote switch in a convenient location using the provided cable hangers.

NOTE

The Aiming Light may be placed at whichever position on the left side rail is most convenient for the operator. If, however, the Aiming Light is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

Note

The AN/PAQ-4B/C may also be mounted on the top or right rails, following the procedure laid out above.  Supporting target offsets for each configuration follow:

#### M4 MWS—AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Left Rail)

#### M4 MWS—AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Top Rail)

#### M4 MWS—AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Right Rail)

### M4 MWS—AN/PAS-13 (Medium/Heavy) Mounting Instructions and Targets

###### MWS – AN/PAS-13, TWS Mounting Instructions

(See Annex B for Target Prep Instructions)

Install the AN/PAS-13 TWS on the MWS using the 7/8” spacer (5) (part number 80063-A3268346) and TWS rail grabber/mount (80063-A3170556).  (Already installed on the TWS by the Armorer IAW TM 11-5855-302-12&P.

- Loosen knobs (1) on carrying handle (2) and remove carrying handle from rail (3) of MWS Carbine (4).  Retain carrying handle.

- Spacer (5) and rail grabber/mount (6) are attached to the TWS (7).

- Loosen the clamping knob (8) until the jaws move far enough apart to fit over the rail.

- Select a slot on rail (3).  Any slot may be used as long as rail grabber/mount does not hang over edge of rail. If the TWS is removed from the rail the operator must note the position at which the device was zeroed, and return the device to that position in order to retain zero.

- Place rail grabber/mount on rail and tighten rail grabber knob (8) until two clicks are heard.

#### M4 MWS—AN/PAS-13 Zero and Boresight Targets

### M4 MWS—AN/PEQ-2A Mounting Instructions and Targets Utilizing Mounting Bracket/Picatinny Rail Grabber

MWS – AN/PEQ-2A Mounting Instructions

The AN/PEQ-2A is mounted on the left side rail using the Mounting Bracket/Picatinny Rail Grabber (1) (NSN 5340-01-458-0473) depicted in the diagram at left.

- Mount the Mounting Bracket/Picatinny Rail Grabber to the AN/PEQ-2A (2) using thumbscrew as depicted to the left of these instructions.

- Loosen the clamping knob on the Mounting Bracket/Picatinny Rail Grabber until the rail grabber has sufficient space to fit over the left side rail (3).  Tighten the clamping knob until two clicks are heard.

- The AN/PEQ-2A may be placed at whichever position on the left side rail is most convenient for the operator.  If however the AN/PEQ-2A is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

- If desired, connect the remote switch to the AN/PEQ-2A and attach it in a convenient location.

- The AN/PEQ-2A may also be mounted on the top and right side rails, using the same installation method.  Targets supporting each configuration follow these instructions.

Note:  The knob of the Bracket Assembly will be pointing up, when the AN/PEQ-2A and mount have been properly installed on the Left side Rail.

Note:  The AN/PAQ-4B/C may also be mounted on the top or right rails, following the procedure laid out above.  Supporting target offsets for each configuration follow:

#### M4 MWS—AN/PEQ-2A Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Left Rail)

#### M4 MWS—AN/PEQ-2A Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Top Rail)

#### M4 MWS—AN/PEQ-2A Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Right Rail)

### M4 MWS—AN/PEQ-2A Mounting Instructions and Targets Utilizing “Insight” Low Profile Rail Grabber

The AN/PEQ-2A is mounted on the front left rail using the Insight Rail Grabber Bracket (ITP-090).

WARNING

Make sure the weapon is CLEAR and on SAFE before proceeding.

- Mount the rail grabber to the AN/PEQ-2A using the thumbscrew as shown.

- Loosen the clamping knob on the rail grabber until the rail grabber has sufficient space to fit over the left side rail.

- Position and tighten the Rail Grabber by turning the knob clockwise.

Note:  The AN/PEQ-2A may be placed at whichever position is most convenient for the operator. If the AN/PEQ-2A is removed from the rail the operator must note the position at which the device was zeroed and return the device to that same position to insure that zero is retained.

Note:  The AN/PAQ-4B/C may also be mounted on the top or right rails, following the procedure laid out above.  Supporting target offsets for each configuration follow:

#### M4 MWS—AN/PEQ-2A Targets Utilizing “Insight” Low Profile Rail Grabber (Left Rail)

#### M4 MWS—AN/PEQ-2A Targets Utilizing “Insight” Low Profile Rail Grabber (Top Rail)

#### M4 MWS—AN/PEQ-2A Targets Utilizing “Insight” Low Profile Rail Grabber (Right Rail)

### M4 MWS—AN/PVS-14 Mounting Instructions and Targets

Procedures may be found located in TM 11-5855-306-10.

- Loosen knobs on carrying handle (not shown) and remove from the weapon. (Retain carrying handle for later use.)

- Be sure the alignment boss on the adapter lines up with the groove in the AN/PVS-14.  Tighten the thumbscrew to secure the AN/PVS-14 to the small arms mounting adapter.

- Loosen the clamping knob on the Small Arms mounting adapter.  Position the AN/PVS-14 and mounting adapter on the weapon’s mounting rail.  Tighten by turning the clamping knob until two clicks are heard.

- Adjust the fore/aft position of the AN/PVS-14 as necessary by loosening the clamping knob and repositioning the Small Arms mounting adapter on the weapon’s mounting rail.

- The AN/PVS-14 should only be mounted on the weapon if there is no laser designator, or night vision device available for target identification & engagement.  The system can be used for passive targeting when active IR cannot be used.

NOTE:  To use the AN/PVS-14 as an aiming device the M68, CCO, must also be mounted on the weapon.  CCO is mounted forward of the AN/PVS-14, on the top hand guard rail.

### M4 MWS—AN/PVS-4 Mounting Instructions and Targets

MWS – AN/PVS-4 Mounting Instructions

To mount the AN/PVS-4 to the MWS the unit Armorer must install a spacer (NSN 5365-01-447-8991) and a rail grabber/mount (NSN 5340-01-449-8533).

- Loosen two knobs (1) on carrying handle (2).  Remove carrying handle from upper receiver rail (3).  Retain carrying handle.

- Install spacer (5) on AN/PVS-4 (7) using the two screws provided.  Attach rail grabber/mount (6) to the spacer (5) using the two screws provided.  (Pre-assembled by Unit Armorer.)

- Loosen the clamping knob (8) until sufficient space exists to place the clamping jaws on either side of the mounting rail (3).  Tighten clamping knob (8) until two clicks are heard.

- The AN/PVS-4 may be placed on the upper receiver rail in the most convenient slot for the operator, as long as the rail grabber/mount does not extend beyond the rail.

- If the AN/PVS-4 is removed the operator must take note of the position at which the device was zeroed, and return the device to that same position to insure zero is retained.

# NOTE:  Item (6) is depicted upside down in order to clearly show the bar which must fit into one of the slots on the rail.

#### M4 MWS—AN/PVS-4 Zero and Boresight Targets

### M4 MWS—M68 Mounting Instructions and Targets

CAUTION

Hand tighten mounting hardware only.  Using tools to tighten mounting hardware could damage equipment.

NOTE

The sight assembly mounts directly to the upper receiver rail on top of the M4/M4A1 and M16A4.  The mount is not required.  Make sure the spacer (1) has been installed before mounting M68 on M4/M4A1 or M16A4.

- If the same sight (serial number is on battery compartment) is installed in the same position

on the rail on the same weapon, re-zeroing is not required.

- Install sight assembly (2) on the upper receiver rail (3).  Sight may be installed in any position on the upper receiver rail.  Make sure grabber edges area around mounting rail and torque bar is in slot.  To ensure that sight assembly is secure, tighten torque knob (4) (behind M68) until it clicks two times.  Hand tighten only.

#### M4 MWS—M68 CCO Zero and Boresight Targets

## M4 MWS M203 Grenade Launcher

### M4/M203 Back Up Iron Sight 10m Boresight Target Offset

### Mounting—M203 w/Quick Release Bracket to the M4 Carbine

MOUNTING - M203 W/QUICK RELEASE BRACKET TO THE M4 CARBINE

PRINCIPLE OF THE FIVE-POSITION SHIM PLATE

The basic overall length between the barrel nut roll pin at the rear of the M203 receiver, and the starting position shim plate cutout surface at the front, is approximately 11 inches. As noted in step 4, some sliding motion may be detectable between the carbine barrel shoulder and the front of the five-position shim plate at the starting, or minimum, overall length cutout position.

Subsequent re-insertion of the five-position shim plate to its #2, #3, #4, or maximum (fifth) length position (refer to step 1, page 10 of this change) will slightly increase the overall length of the assembly beyond the basic 11 inches, and therefore tend to minimize or eliminate any sliding motion between the barrel shoulder and the five-position shim plate.

At some point, the unit armorer will note that the shim plate will not fit into the cutout of the carbine barrel shoulder (as indicated as INCORRECT in step 4). At this point, go back to the next lowest position and secure, close, and lock the bracket around the carbine.

The following steps describe checking for sliding motion with the next or #2 notch up, and against the carbine barrel shoulder. If the #2 position does not minimize the sliding motion, repeat the procedure with the #3 notch up and so on. If the fifth or maximum position is desired, note that the “back” or smooth face of the shim plate is oriented towards the muzzle. Do not be concerned if only a small amount of sliding motion is still detectable with the shim plate in its apparently optimum setting, because the latch arm will compensate for this when it is closed and locked.

1. Compare the illustration below with the quick release bracket (1) for the purpose of familiarization with all positions of the five-position shim plate (2):

2. Set the five-position shim plate in the bracket to the minimum position as illustrated, with the 2 dots down and facing the muzzle.

3. If present, remove the lower handguard of the M4 adapter rail from the M4 carbine. Move the rear of the M203 receiver into position around the carbine barrel. Confirm that the latch arm (3) of the bracket is fully open. Rotate the muzzle end of the M203 towards the carbine barrel while sliding the M203 firmly to the rear. Confirm that the roll pin in the rear of the M203 receiver

engages the carbine barrel nut at the six o’clock position notch.

4. Firmly hold the M203 in position/back against the barrel nut of the carbine, while also holding the muzzle end of the M203 against the carbine’s barrel.  Inspect the five-position shim plate, looking from the top of the carbine barrel, and also from the front, as illustrated below. The inner notch of the shim plate should rest behind the shoulder of the barrel. Now, try to slide the M203 back and forth if possible, and note the distance of any sliding motion. Some motion will be detectable with most carbine barrels with the shim plate in its starting position. If during this step the cutout in the shim plate does not fit behind the barrel shoulder, it is most probably inserted at its maxi-mum thickness (no dots facing the muzzle), or position #2, #3, or #4 (refer to step 1 on page 10 of the change).

NOTE

Endurance testing indicated that it may be necessary to switch to another shim plate (2) position after several thousand rounds have been fired. The unit armorer should check for excessive sliding motion each time the shim plate is removed for cleaning/ lubrication and the M203 re-mounted to the carbine.

5. Remove the M203 w/quick release bracket from the carbine. Depress the plunger (4) withdraw the shim plate and re-insert it with the #2 position up (refer to step 1, page 10 of this change). Note that the #2 position is indicated by a single dot stamped on its shim plate cutout, and that this side of the shim plate faces the muzzle.

6. Re-mount the M203 w/quick release bracket to the carbine’s barrel nut and barrel shoulder. Without unlatching the bracket, ensure the cutout in the shim plate’s #2 position fits behind the carbine’s barrel shoulder, and attempt to slide the M203 from front to rear.

7. If forward and back motion is detected, repeat step 6 with the #3 notch against the carbine barrel. If the assembly is now too long (it will not engage behind the barrel shoulder, but rides up onto the barrel’s major diameter), go back to the last position tried with the shim plate, and complete the M203 attachment.  When the optimum position of the shim plate is established:

(a) Rotate the latch arm (3) over the carbine barrel.

(b) Catch the hook (5) in the hole of the latch arm.

(c) Rotate the latch lever (6) down.

(d) Depress the plunger (4).

(e) Squeeze the latch lever fully closed (which allows the plunger to be released and snap forward). This will hold the latch lever in the fully closed/locked position.

NOTE

In its final motion, the latch lever may require very firm pressure against the bracket to allow the plunger to snap back into place, locking the latch lever closed. In some instances, finger pressure along against the latch lever will not be sufficient to fully close it. When this occurs, use the side of the bayonet stud for extra leverage against the latch lever.

(f) Rotate the M203 trigger guard (7) to engage the lip of the magazine well.

8. If forward and back motion is detected with the shim plate set to its #3 notch, remove the M203 from the carbine. Remove and re-insert the shim plated with its #4 position up. Note that the #4 position is indicated by three dots stamped adjacent to its shim plate cutout, and that this side of the shim plate faces the muzzle.

9. If the #5 or maximum position is required, insert the shim plate as illustrated

below.

CAUTION

When detaching the M203 for cleaning, inspection, or lubrication, check and note the position of the shim plate for ease of re-attachment.

### M4 MWS M203 —AN/PAQ-4B/C Mounting Instructions and Targets Utilizing Mounting Bracket/Picatinny Rail Grabber

###### MWS/M203 – AN/PAQ-4B/C Mounting Instructions

The AN/PAQ-4B/C may be mounted on the left, top or right side rails using the Mounting Bracket/Picatinny Rail Grabber (NSN 5340-01-458-0473) depicted in the diagram at left.

- Attach the Mounting Bracket/Picatinny Rail Grabber to the AN/PAQ-4B/C (1) using the thumbscrew on the AN/PAQ-4B/C.

Note:  Knob on the rail grabber/mount should be pointing up when installation is complete.

- Loosen the clamping knob (3) until the rail grabber/mount has sufficient space to fit over the left side rail (2).  Tighten the clamping knob until two clicks are heard.

- The AN/PAQ-4B/C may be placed at whichever position on the left side rail is most convenient for the operator.  If however the AN/PAQ-4B/C is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

- Install the remote switch (4) in a convenient location using the provided cable hangers.

NOTE:  M203 Leaf Sight removed to provide a clearer picture of the installation of the AN/PAQ-4B/C

#### M4 MWS M203 —AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Left Rail)

#### M4 MWS M203 —AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Top Rail)

#### M4 MWS M203 —AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Right Rail)

### M4 MWS M203 —AN/PAQ-4B/C Mounting Instructions and Targets Using “Insight” Low Profile Rail Grabber

The “Insight” Low Profile Rail Grabber (NSN 5340-01-458-0990, ITP-090) equipped AN/PAQ-4B/C is mounted to the M4 MWS M203 Grenade Launcher in the same manner as the Mounting Bracket/Picatinny Rail Grabber equipped AN/PAQ-4B/C is mounted.  Please see instructions in the previous section.

Offset targets supporting the various mounting locations for the “Insight” Low Profile Rail Grabber equipped AN/PAQ-4B/C appear on the following pages.

#### M4 MWS M203 —AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Left Rail)

#### M4 MWS M203 —AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Top Rail)

#### M4 MWS M203 —AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Right Rail)

### M4 MWS/M203—AN/PVS-4 Mount Procedures

MWS – AN/PVS-4 Mounting Instructions

In order to properly mount the AN/PVS-4 to the MWS the unit Armorer must first install a spacer (NSN 5365-01-447-8991) and a rail grabber/mount (NSN 5340-01-449-8533) on the AN/PVS-4.

- Loosen two knobs (1) on carrying handle (2).  Remove carrying handle from upper receiver rail (3).  Retain carrying handle.

- Loosen the clamping knob (4) until sufficient space exists to place the clamping jaws on either side of the upper receiver rail (3).  Tighten torque-limiting knob (4) until two clicking sounds are heard.

- The AN/PVS-4 may be placed at whichever rail-cross slot on the upper receiver rail is most convenient for the operator, as long as the rail grabber/mount does not extend beyond the rail.

Note:  If the AN/PVS-4 is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

#### M4 MWS/M203—AN/PVS-4 Zero and Boresight Targets

## M16A4 MWS

NOTE:  Mounting diagrams in the following pages depict a M4 Carbine Modular Weapon System (MWS).  Procedures used for both systems are identical unless otherwise pointed out.

### M16A4 MWS Back Up Iron Sight Boresight Target

### M16A4 MWS—AN/PAQ-4B/C Mounting Instructions and Targets Utilizing Mounting Bracket/Picatinny Rail Grabber

###### M16A4 MWS – AN/PAQ-4B/C Mounting Instructions

The AN/PAQ-4B/C may be mounted on the left, top or right side rails using the Mounting Bracket/Picatinny Rail Grabber (NSN 5340-01-458-0473) depicted in the diagram at left.

- Attach the Mounting Bracket/Picatinny Rail Grabber(1) to the AN/PAQ-4B/C (2) using the thumbscrew on the AN/PAQ-4B/C.

- Loosen the clamping knob until the rail grabber/mount has sufficient space to fit over the left side rail (3).  Tighten the clamping knob until two clicks are heard.

- The AN/PAQ-4B/C may be placed at whichever position, on the left side rail, is most convenient for the operator.  If however the AN/PAQ-4B/C is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

- Install the remote switch in a convenient location using the provided cable hangers.

The AN/PAQ-4B/C may also be mounted on the top or right rails, following the procedure laid out above.  Supporting target offsets for each configuration follow:

#### M16A4 MWS—AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Left Rail)

#### M16A4 MWS—AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Top Rail)

#### M16A4 MWS—AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Right Rail)

### M16A4 MWS—AN/PAQ-4B/C Mounting Instructions and Targets Utilizing “Insight” Low Profile Rail Grabber

The Aiming Light is mounted on the front left-hand rail using the “Insight” low profile rail grabber (NSN 5340-01-458-0990, ITP-090) when it is desired to keep the Aiming Light as close as possible to the barrel.

WARNING

Make sure the weapon is CLEAR and on SAFE before proceeding.

- Loosen the clamping knob until the rail grabber has sufficient space to fit over the left side rail. Hand Tighten the clamping knob.

- Turn the ON/OFF Switch CCW to the #1 OFF/STORAGE position.

- Position the Aiming Light on the bracket mounting rail. Hand tighten the Thumbscrew to secure the Aiming Light.

- Install the remote switch in a convenient location using the provided cable hangers.

NOTE

The Aiming Light may be placed at whichever position on the left side rail is most convenient for the operator. If, however, the Aiming Light is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

Note

The AN/PAQ-4B/C may also be mounted on the top or right rails, following the procedure laid out above.  Supporting target offsets for each configuration follow:

#### M16A4 MWS—AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Left Rail)

#### M16A4 MWS—AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Top Rail)

#### M16A4 MWS—AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Right Rail)

### M16A4 MWS—AN/PAS-13 (Medium/Heavy) Mounting Instructions and Targets

###### MWS – AN/PAS-13, TWS Mounting Instructions

(See Annex B for Target Prep Instructions)

Install the AN/PAS-13 TWS on the MWS using the 7/8” spacer (5) (part number 80063-A3268346) and TWS rail grabber/mount (80063-A3170556).  (Already installed on the TWS by the Armorer IAW TM 11-5855-302-12&P.

- Loosen knobs (1) on carrying handle (2) and remove carrying handle from rail (3) of MWS Carbine (4).  Retain carrying handle.

- Spacer (5) and rail grabber/mount (6) are attached to the TWS (7).

- Loosen the clamping knob (8) until the jaws move far enough apart to fit over the rail.

- Select a slot on rail (3).  Any slot may be used as long as rail grabber/mount does not hang over edge of rail. If the TWS is removed from the rail the operator must note the position at which the device was zeroed, and return the device to that position in order to retain zero.

- Place rail grabber/mount on rail and tighten rail grabber knob (8) until two clicks are heard.

#### M16A4 MWS—AN/PAS-13 Zero and Boresight Targets

### M16A4 MWS—AN/PEQ-2A Mounting Instructions and Targets Utilizing Mounting Bracket/Picatinny Rail Grabber

MWS – AN/PEQ-2A Mounting Instructions

The AN/PEQ-2A is mounted on the left side rail using the Mounting Bracket/Picatinny Rail Grabber (1) (NSN 5340-01-458-0473) depicted in the diagram at left.

- Mount the rail grabber/mount to the AN/PEQ-2A (2) using thumbscrew as depicted to the left of these instructions.

- Loosen the clamping knob on the rail grabber/mount until the rail grabber has sufficient space to fit over the left side rail (3).  Tighten the clamping knob until two clicks are heard.

- The AN/PEQ-2A may be placed at whichever position on the left side rail is most convenient for the operator.  If however the AN/PEQ-2A is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

- If desired, connect the remote switch to the AN/PEQ-2A and attach it in a convenient location.

- The AN/PEQ-2A may also be mounted on the top and right side rails, using the same installation method.  Targets supporting each configuration follow these instructions.

NOTE:  The knob of the Bracket Assembly will be pointing up, when the AN/PEQ-2A and mount have been properly installed on the Left side Rail.

Note:  The AN/PEQ-2A may also be mounted on the top or right rails, following the procedure laid out above.  Supporting target offsets for each configuration follow:

#### M16A4 MWS—AN/PEQ-2A Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Left Rail)

#### M16A4 MWS—AN/PEQ-2A Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Top Rail)

#### M16A4 MWS—AN/PEQ-2A Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Right Rail)

### M16A4 MWS—AN/PEQ-2A Mounting Instructions and Targets Utilizing “Insight” Low Profile Rail Grabber

The AN/PEQ-2A is mounted on the front left rail using the Insight Rail Grabber Bracket (ITP-090).

WARNING

Make sure the weapon is CLEAR and on SAFE before proceeding.

- Mount the rail grabber to the AN/PEQ-2A using the thumbscrew as shown.

- Loosen the clamping knob on the rail grabber until the rail grabber has sufficient space to fit over the left side rail.

- Position and tighten the Rail Grabber by turning the knob clockwise.

NOTE:  The AN/PEQ-2A may be placed at whichever position is most convenient for the operator. If the AN/PEQ-2A is removed from the rail the operator must note the position at which the device was zeroed and return the device to that same position to insure that zero is retained.

Note:  The AN/PAQ-4B/C may also be mounted on the top or right rails, following the procedure laid out above.  Supporting target offsets for each configuration follow:

#### M16A4 MWS—AN/PEQ-2A Targets Utilizing “Insight” Low Profile Rail Grabber (Left Rail)

#### M16A4 MWS—AN/PEQ-2A Targets Utilizing “Insight” Low Profile Rail Grabber (Top Rail)

#### M16A4 MWS—AN/PEQ-2A Targets Utilizing “Insight” Low Profile Rail Grabber (Right Rail)

### M16A4 MWS—AN/PVS-14 Mounting Instructions and Targets

###### MWS – AN/PVS-14 Mounting Instructions

Procedures may be found located in TM 11-5855-306-10.

- Loosen knobs on carrying handle and remove from the weapon. (Retain carrying handle for later use.)

- Be sure the alignment boss on the adapter lines up with the groove in the AN/PVS-14.  Tighten the thumbscrew to secure the AN/PVS-14 to the small arms mounting adapter.

- Loosen the clamping knob on the Small Arms mounting adapter.  Position the AN/PVS-14 and mounting adapter on the weapon’s mounting rail.  Tighten by turning the clamping knob until two clicks are heard.

- Adjust the fore/aft position of the AN/PVS-14 as necessary by loosening the clamping knob and repositioning the Small Arms mounting adapter on the weapon’s mounting rail.

- The AN/PVS-14 should only be mounted on the weapon if there is no laser designator, or night vision device available for target identification & engagement.  The system can be used for passive targeting when active IR cannot be used.

NOTE:  To use the AN/PVS-14 as an aiming device the M68, CCO, must also be mounted on the weapon.  CCO is mounted forward of the AN/PVS-14, on the top hand guard rail.

### M16A4 MWS—AN/PVS-4 Mounting Instructions and Targets

MWS – AN/PVS-4 Mounting Instructions

To mount the AN/PVS-4 to the MWS the unit Armorer must install a spacer (NSN 5365-01-447-8991) and a rail grabber/mount (NSN 5340-01-449-8533).

- Loosen two knobs (1) on carrying handle (2).  Remove carrying handle from upper receiver rail (3).  Retain carrying handle.

- Install spacer (5) on AN/PVS-4 (7) using the two screws provided.  Attach rail grabber/mount (6) to the spacer (5) using the two screws provided.  (Pre-assembled by Unit Armorer.)

- Loosen the clamping knob (8) until sufficient space exists to place the clamping jaws on either side of the mounting rail (3).  Tighten clamping knob (8) until two clicks are heard.

- The AN/PVS-4 may be placed on the upper receiver rail in the most convenient slot for the operator, as long as the rail grabber/mount does not extend beyond the rail.

- If the AN/PVS-4 is removed the operator must take note of the position at which the device was zeroed, and return the device to that same position to insure zero is retained.

# NOTE:  Item (6) is depicted upside down in order to clearly show the bar which must fit into one of the slots on the rail.

#### M16A4 MWS—AN/PVS-4 Zero and Boresight Targets

### M16A4 MWS—M68 Mounting Instructions and Targets

CAUTION

Hand tighten mounting hardware only.  Using tools to tighten mounting hardware could damage equipment.

NOTE

The sight assembly mounts directly to the upper receiver rail on top of the M4/M4A1 and M16A4.  The mount is not required.  Make sure the spacer (1) has been installed before mounting M68 on M4/M4A1 or M16A4.

- If the same sight (serial number is on battery compartment) is installed in the same position  on the rail on the same weapon, re-zeroing is not required.

- Install sight assembly (2) on the upper receiver rail (3).  Sight may be installed in any position on the upper receiver rail.  Make sure grabber edges area around mounting rail and torque bar is in slot.  To ensure that sight assembly is secure, tighten torque knob (4) (behind M68) until it clicks two times.  Hand tighten only.

#### M16A4 MWS—M68 Targets

## M16A4 MWS M203 Grenade Launcher

### M4/M203 Back Up Iron Sight 10m Boresight Target Offset

### Mounting—M203 w/Quick Release Bracket to the M16A4 Rifle

PRINCIPLE OF THE FIVE-POSITION SHIM PLATE

The basic overall length between the barrel nut roll pin at the rear of the M203 receiver, and the starting position shim plate cutout surface at the front, is approximately 11 inches. As noted in step 4, some sliding motion may be detectable between the rifle barrel stop and the front of the five-position shim plate at the starting, or minimum, overall length cutout position.

Subsequent re-insertion of the five-position shim plate to its #2, #3, #4, or maximum (fifth) length position (refer to step 1, page 22 of this change) will slightly increase the overall length of the assembly beyond the basic 11 inches, and therefore tend to minimize or eliminate any sliding motion between the barrel stop and the five-position shim plate.

The following steps describe checking for sliding motion with the next or #2 notch up, and against the rifle barrel stop. If the #2 position does not minimize the sliding motion, repeat the procedure with the #3 notch up and so on. If the fifth or maximum position is desired, note that the “back” or smooth face of the shim plate is oriented towards the muzzle. Do not be concerned if only a small amount of sliding motion is still detectable with the shim plate in its apparently optimum setting, because the latch arm will compensate for this when it is closed and locked.

NOTE

Endurance testing indicated that it may be necessary to switch to another shim plate position after several thousand rounds have been fired. The unit armorer should check for excessive sliding motion each time the shim plate is removed for cleaning/lubrication and the M203 re-mounted to the carbine.

1. Compare the illustration below with the quick release bracket (1) for the purpose of familiarization with all positions of the five-position shim plate (2):

2. Set the five-position shim plate in the bracket to the minimum position as illustrated, with the 2 dots down and facing the muzzle.

3. If present, remove the lower handguard of the M5 adapter rail from the M16A4 rifle. Move the rear of the M203 receiver into position around the rifle barrel.  Confirm that the latch arm (3) of the bracket is fully open. Rotate the muzzle end of the M203 towards the rifle barrel while sliding the M203 firmly to the rear. Confirm that the roll pin in the rear of the M203 receiver engages the rifle barrel nut at the six o’clock position notch.

4. Firmly hold the M203 in position/back against the barrel nut of the rifle, while also holding the muzzle end of the M203 against the rifle’s barrel stop. Now, try to slide the M203 back and forth if possible, and note the distance of any sliding motion. Some motion may be detectable with the shim plate in its starting position.

5. Remove the M203 w/quick release bracket from the rifle. Depress the plunger (4) withdraw the shim plate and re-insert it with the #2 position up (refer to step 1, page 22 of this change). Note that the #2 position is indicated by a single dot stamped on its shim plate cutout, and that this side of the shim plate faces the muzzle.

6. Re-mount the M203 w/quick release bracket to the rifle’s barrel nut and barrel stop. Attempt to slide the M203 from front to rear.

7. If forward and back motion is detected, repeat step 6 with the #3 notch against the rifle barrel. If the assembly is now too long (it will not engage behind the barrel stop), go back to the last position tried with the shim plate, and complete the M203 attachment process as described next.  When the optimum position of the shim plate is established:

a. Carefully work the latch arm (3) between the rifle barrel and the gas tube.

b. Hold the retaining spring away from the plunger (4) and depress the plunger to unlock the latch lever (5).

c. Catch the hook (6) in the hole of the latch arm.

d. Rotate the latch lever (5) down.

e. Depress the plunger (4). Make sure the retaining spring does not engage the plunger during this step.

f. Squeeze the latch lever fully closed (which allows the plunger to be released and snap forward).  This will hold the latch lever in the fully closed/locked position.  In its final motion, the latch lever may require very firm pressure against the bracket to allow the plunger to snap back into place, locking the latch lever closed. In some instances, finger pressure alone against the latch lever will not be sufficient to fully close it. When this occurs, use the side of the bayonet stud for extra leverage against the latch lever.

g. Rotate the M203 trigger guard (7) to engage the lip of the magazine well.

8. If forward and back motion is detected with the shim plate set to its #3 notch, remove the M203 from the rifle. Remove and re-insert the shim plate with its #4 position up. Note that the #4 position is indicated by three dots stamped adjacent to its shim plate cutout, and that this side of the shim plate faces the muzzle.

9. If the #5 maximum position is required, insert the shim plate as illustrated below.

Caution

When detaching the M203 for cleaning, inspection, or lubrication, check and note the position of the shim plate for ease of re-attachment.

### M16A4 MWS M203 —AN/PAQ-4B/C Mounting Instructions and Targets Utilizing Mounting Bracket/Picatinny Rail Grabber

The AN/PAQ-4B/C may be mounted on the left, top or right side rails using the Mounting Bracket/Picatinny Rail Grabber (NSN 5340-01-458-0473) depicted in the diagram at left.

- Attach the Mounting Bracket/Picatinny Rail Grabber to the AN/PAQ-4B/C (1) using the thumbscrew on the AN/PAQ-4B/C.

Note:  Knob on the rail grabber/mount should be pointing up when installation is complete.

- Loosen the clamping knob (3) until the rail grabber/mount has sufficient space to fit over the left side rail (2).  Tighten the clamping knob until two clicks are heard.

- The AN/PAQ-4B/C may be placed at whichever position on the left side rail is most convenient for the operator.  If however the AN/PAQ-4B/C is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

- Install the remote switch (4) in a convenient location using the provided cable hangers.

NOTE:  M203 Leaf Sight removed to provide a clearer picture of the installation of the AN/PAQ-4B/C

#### M16A4 MWS M203 —AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber (Left Rail)

#### M16A4 MWS M203 —AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Picatinny Rail Grabber (Top Rail)

#### M16A4 MWS M203 —AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Picatinny Rail Grabber (Right Rail)

### M16A4 MWS M203 —AN/PAQ-4B/C Mounting Instructions and Targets Using “Insight” Low Profile Rail Grabber

The “Insight” Low Profile Rail Grabber equipped AN/PAQ-4B/C is mounted to the M16A4 MWS M203 Grenade Launcher in the same manner as the Mounting Bracket/Picatinny Rail Grabber equipped AN/PAQ-4B/C is mounted.  Please see instructions in the previous section.

Offset targets supporting the various mounting locations for the “Insight” Low Profile Rail Grabber equipped AN/PAQ-4B/C appear on the following pages.

#### M16A4 MWS M203 —AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Left Rail)

#### M16A4 MWS M203 —AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Top Rail)

#### M16A4 MWS M203 —AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber (Right Rail)

### M16A4 MWS/M203—AN/PVS-4 Mount Procedures

MWS – AN/PVS-4 Mounting Instructions

In order to properly mount the AN/PVS-4 to the MWS the unit Armorer must first install a spacer (NSN 5365-01-447-8991) and a rail grabber/mount (NSN 5340-01-449-8533) on the AN/PVS-4.

- Loosen two knobs (1) on carrying handle (2).  Remove carrying handle from upper receiver rail (3).  Retain carrying handle.

- Loosen the clamping knob (4) until sufficient space exists to place the clamping jaws on either side of the upper receiver rail (3).  Tighten torque-limiting knob (4) until two clicking sounds are heard.

- The AN/PVS-4 may be placed at whichever rail-cross slot on the upper receiver rail is most convenient for the operator, as long as the rail grabber/mount does not extend beyond the rail.

Note:  If the AN/PVS-4 is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

#### M16A4 MWS/M203—AN/PVS-4 Zero and Boresight Targets

## M24 System Diagram

### M24—Sniper System Day Optic Mounting Instructions

### M24—AN/PVS-10, Sight, Night Vision Sniper Scope Mount Procedures

M24 – AN/PVS-10 Mounting Instructions

1.  Before mounting the SNS, lubricate the threads of each mounting nut with Cleaner Lubricant Preservative (CLP) (NSN: 9150-01-102-1473)

2.  Ensure smooth movement of each captive mounting nut and clamp. (Figure 1)

3.  Inspect for burrs and foreign matter between each nut and clamp.  Burrs or foreign matter must be removed prior to mounting.

4.  Mount the SNS to the optical rail of the M24.  (See Figure 2).

5.  Align the square spline in the mounting base of the SNS in one of the two corresponding cross-slots of the optical rail.  (See Figure 3).

6.  Mount the front and rear clamps against the base.  Finger tighten the mounting nuts.

7.  Remove eyepiece protection cap and install eyeguard.

8.  Check the eye relief.  If the sight needs to be adjusted, loosen the mounting nuts and align the square spline with the other set of slots on the optical rail and repeat step 6.

9.  Tighten the rear-mounting nut to 65 inch-pounds using the T-handle torque wrench.

10.  Tighten the front mounting nut to 65 inch-pounds using the T-handle torque wrench.

11.  Repeat steps 9 and 10 for a total of three (3) cycles.

12.  The T-handle Torque wrench is not provided with the AN/PVS-10 Sniper Night Scope.  The wrench is provided with the M24 Sniper Weapon System Deployment Kit.

#### M24—AN/PVS-10 Zero Procedure

There is a slight deviation between day and night zero point of .5 MOA.

- Assume a good prone supported position 100 meters away from the target.

- Verify SNS is in Day mode, uncover the objective lens and if eyeguard is not installed, remove the eyepiece protective cap.

- Adjust the windage and elevation dials as needed to precisely zero the rifle for optimum performance on the target.

- Fire three rounds maintaining the same aim point each time.

- After placement of the rounds has been noted, turn the elevation and windage dials to make the needed adjustments to the sight.

- Repeat this process until a 3-round group is centered on the aim point.

- Once the shot group is centered, loosen the setscrews on the elevation dial.  Slip the elevation dial to the index line marked “0”.  Retighten the setscrews.

- After zeroing at 100 meters, confirm this zero out to 300 meters at 100-meter increments.

## M249 Machine Gun System/Squad Automatic Weapon Diagram

### M249 Iron Sight 25m Zero and 10m Boresight Target Offsets

### M249—AN/PAQ-4B/C Mount Procedures Mounting Bracket/Picatinny Rail Grabber on Feed Tray Cover Rail

M249 – AN/PAQ-4B/C Mounting Instructions

The AN/PAQ-4B/C (1) is mounted on the feed tray cover rail using the Mounting Bracket/Picatinny Rail Grabber (NSN 5340-01-458-0473) depicted in the diagram at left.

- Attach the Bracket Assembly to the AN/PAQ-4B/C (1) using the thumbscrew on the AN/PAQ-4B/C.

- Loosen the clamping knob (3) until the rail grabber has sufficient space to fit over the top cover rail (4).  Tighten the clamping knob until two clicks are heard.

- The AN/PAQ-4B/C may be placed at whichever position on the rail is most convenient for the operator.  If however the AN/PAQ-4B/C is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

# Install the remote switch (5) in a convenient location using the provided cable hangers.

#### M249—AN/PAQ-4B/C Zero and Boresight Tgts, Mounting Bracket/Picatinny Rail Grabber on Feed Tray Cover Rail

### M249—AN/PAQ-4B/C Mount Procedures “Insight” Low Profile Rail Grabber on Feed Tray Cover Rail

The Aiming Light mounts on the top of the mounting rail equipped M249 Squad Automatic Weapon (SAW) using the Insight Low Profile Rail Grabber.

WARNING

Make sure the weapon is CLEAR and on SAFE before proceeding.

NOTE

The Aiming Light may be placed at whichever position on the top rail is most convenient for the operator. If, however, the Aiming Light is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

- Loosen the clamping knob until the rail grabber has sufficient space to fit over the top rail.  Hand Tighten the clamping knob.

- Turn the ON/OFF Switch CCW to the #1 OFF/Storage position.

- Position the Aiming Light on the bracket mounting rail. Hand tighten the Thumbscrew to secure the Aiming Light.

- Install the remote switch in a convenient location using the provided cable hangers.

#### M249—AN/PAQ-4B/C Zero and Boresight Tgts, “Insight” Low Profile Rail Grabber on Feed Tray Cover Rail

### M249—AN/PAQ-4B/C Mounting Instructions w/ AN/PVS-4 Mounting Bracket & Plastic AN/PAQ-4B/C Bracket Adapter

M249 – AN/PAQ-4B/C Mounting Instructions Using an AN/PVS-4 Mounting Bracket

The AN/PAQ-4B/C may also be attached to the M249 using the mounting bracket intended to mount the AN/PVS-4 onto the M249, as detailed below:

- Install the AN/PVS-4 – M249 mounting bracket (1) to the M249 feed tray cover (2), per TM 11-5855-213-10

- Attach Bracket Adapter (3) to AN/PAQ-4B/C (4).

- Attach AN/PAQ-4B/C, with bracket adapter attached, to the mounting bracket (1) using the AN/PVS-4 thumbscrew (5).

- Attach the remote switch (6) to the device and locate it on a convenient location on the weapon for the shooter.

Note: Bracket Adapter is part number A3186952 as shown in TM 11-5855-308-12&P

#### M249—AN/PAQ-4B/C Zero and Boresight Targets Using AN/PVS-4 Mounting Bracket

### M249 —AN/PAQ-4B/C Mounting Instructions Utilizing Mounting Bracket/Picatinny Rail Grabber on Forward Rails

The AN/PAQ-4B/C (1) may be mounted on either the left or right forward rails by using the Mounting Bracket/Picatinny Rail Grabber (NSN 5340-01-458-0473) (2) depicted in the diagram at left.

- Attach the Mounting Bracket/ Picatinny Rail Grabber to the AN/PAQ-4B/C (1) using the thumbscrew on the AN/PAQ-4B/C.

- Loosen the clamping knob (3) until the rail grabber has sufficient space to fit over the rail (4).  Tighten the clamping knob until two clicks are heard.

- The AN/PAQ-4B/C may be placed at whichever position on the rail is most convenient for the operator.  If however the AN/PAQ-4B/C is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

# Install the remote switch in a convenient location using the provided cable hangers.

# Note:  The AN/PAQ-4B/C may be placed on either the left or right rail using the procedure outlined above.  Supporting targets appear on the following pages.

#### M249 —AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber on Left Rail

#### M249 —AN/PAQ-4B/C Targets Utilizing Mounting Bracket/Picatinny Rail Grabber on Right Rail

### M249 —AN/PAQ-4B/C Mounting Instructions Utilizing “Insight” Low Profile Rail Grabber on Forward Rails

The AN/PAQ-4B/C (1) may be mounted on either the left or right forward rails by using the Insight Low Profile Rail Grabber (2) depicted in the diagram at left.

- Attach the Insight Low Profile Rail Grabber to the AN/PAQ-4B/C (1) using the thumbscrew on the AN/PAQ-4B/C.

- Loosen the clamping knob (3) until the rail grabber has sufficient space to fit over the rail (4).  Tighten the clamping until a snug fit is achieved.

- The AN/PAQ-4B/C may be placed at whichever position on the rail is most convenient for the operator.  If however the AN/PAQ-4B/C is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

# Install the remote switch in a convenient location using the provided cable hangers.

# Note:  The AN/PAQ-4B/C may be placed on either the left or right rail using the procedure outlined above.  Supporting targets appear on the following pages.

#### M249 —AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber on Left Rail

#### M249 —AN/PAQ-4B/C Targets Utilizing “Insight” Low Profile Rail Grabber on Right Rail

### M249—AN/PAS-13 TWS Mount Procedures, Feed Tray Cover Rail

M249 – AN/PAS-13 TWS Mounting Instructions

(See Annex B for Target Prep Instructions)

The AN/PAS-13 comes equipped with a spacer and torque limiting rail grabber that allow the device to be rapidly attached to a weapon rail.

- To install the AN/PAS-13 (1) loosen the clamping knob (2) (hidden behind TWS) until sufficient space exits to place the clamping jaws on either side of the mounting rail (3).  Tighten clamping knob (2) until two clicks are heard.

- The AN/PAS-13 may be placed at position number 5 or back (counting from the back of the rail to the front) on the top feed tray cover rail, as long as the rail grabber does not extend beyond the rail.  Should the device be installed forward of the number five slot the sight will interfere with the operator’s ability to raise the barrel handle and the sight’s objective lens will strike the weapon, when the feed tray cover is opened.

- If the AN/PAS-13 is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

#### M249—AN/PAS-13 TWS Zero and Boresight Targets, Feed Tray Cover Rail

### M249—AN/PEQ-2A Mount Procedures, Integrated Feed Tray Cover

M249B – AN/PEQ-2A Mounting Instructions

The AN/PEQ-2A (1) is mounted on the top cover rail (2) using the Mounting Bracket/Picatinny Rail Grabber (3) (NSN 5340-01-458-0473) depicted in the diagram at left.

- Mount the AN/PEQ-2A (1) to the Mounting Bracket/Picatinny Rail Grabber (3) using the thumbscrew on the AN/PEQ-2A.

- Loosen the clamping knob (4) until the rail grabber has sufficient space to fit over the top cover rail (2).  Tighten the clamping knob until two clicks are heard.

- The AN/PEQ-2A may be on the rail wherever is most convenient for the operator.  If removed, the operator must return the device to that same position in order to insure that zero is retained.

- Install the remote switch (5) in a convenient location using the provided cable hangers.

#### M249—AN/PEQ-2A Targets w/ Mounting Bracket/Picatinny Rail Grabber on Feed Tray Cover Rail

#### M249—AN/PEQ-2A Targets w/ “Insight” Low Profile Rail Grabber on Feed Tray Cover Rail

### M249—AN/PEQ-2A Mount Procedures Using AN/PVS-4—M249 Mounting Bracket

M249 – AN/PEQ-2A Mounting Instructions Using an AN/PVS-4 Mounting Bracket

- Install the AN/PVS-4 – M249 mounting bracket (1) to the M249 feed tray cover (2), per TM 11-5855-213-10

- Attach Bracket Adapter (plastic) (3) to AN/PEQ-2A (4).

- Attach AN/PEQ-2A, with bracket adapter attached, to the mounting bracket (1) using the AN/PVS-4 thumbscrew (5).

- If desired, attach the remote switch (6) and fasten it at a convenient location with the provided cable hangers.

#### M249—AN/PEQ-2A Zero and Boresight Targets, (With AN/PVS-4 Mount)

### M249—AN/PEQ-2A Mounting Instructions Utilizing Mounting Bracket/Picatinny Rail Grabber on Forward Rails

The AN/PEQ-2A (1) may be mounted on either the left or right forward rails by using the Mounting Bracket/ Picatinny Rail Grabber (NSN 5340-01-458-0473) (2) depicted in the diagram at left.

- Attach the Mounting Bracket/ Picatinny Rail Grabber to the AN/PEQ-2A (1) using the thumb-screw on the AN/PEQ-2A.

- Loosen the clamping knob (3) until the rail grabber has sufficient space to fit over the rail (4).  Tighten the clamping knob until two clicks are heard.

- The AN/PEQ-2A may be placed at whichever position on the rail is most convenient for the operator.  If however the AN/PEQ-2A is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

# Install the remote switch in a convenient location using the provided cable hangers.

# Note:  The AN/PEQ-2A may be placed on either the left or right rail using the procedure outlined above.  Supporting targets appear on the following pages.

#### M249—AN/PEQ-2A Targets, Using Mounting Bracket/Picatinny Rail Grabber on Left Rail

#### M249—AN/PEQ-2A Targets, Using Mounting Bracket/Picatinny Rail Grabber on Right Rail

### M249 —AN/PEQ-2A Mounting Instructions Utilizing “Insight” Low Profile Rail Grabber on Forward Rails

The AN/PEQ-2A (1) may be mounted on either the left or right forward rails by using the Insight Low Profile Rail Grabber (2) depicted in the diagram at left.

- Attach the Insight Low Profile Rail Grabber to the AN/PEQ-2A (1) using the thumbscrew on the AN/PEQ-2A.

- Loosen the clamping knob (3) until the rail grabber has sufficient space to fit over the rail (4).  Tighten the clamping knob until the device fits snugly on the rail.

- The AN/PEQ-2A may be placed at whichever position on the rail is most convenient for the operator.  If however the AN/PEQ-2A is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

# Install the remote switch in a convenient location using the provided cable hangers.

# Note:  The AN/PEQ-2A may be placed on either the left or right rail using the procedure outlined above.  Supporting targets appear on the following pages.

#### M249—AN/PEQ-2A Targets, Using “Insight” Low Profile Rail Grabber on Left Rail

#### M249—AN/PEQ-2A Targets, Using “Insight” Low Profile Rail Grabber on Right Rail

### M249—AN/PVS-4 Mount Procedures, Integrated Feed Tray Cover

M249—AN/PVS-4 Mounting Instructions

To properly mount the AN/PVS-4 (1) to the M249 (4) the unit Armorer must first install a spacer (NSN 5365-01-447-8991) and a rail grabber (NSN 5340-01-449-8533) on the AN/PVS-4.

- Loosen the clamping knob (2) until sufficient space exists to place the clamping jaws on either side of the mounting rail (3).  Tighten clamping knob (2) until two clicks are heard.

- The AN/PVS-4 may be placed at position number 5 or back (counting from the back of the rail to the front) on the top feed tray cover rail, as long as the rail grabber does not extend beyond the rail.  Installing forward of the number five slot the sight will interfere with the operators ability to raise the barrel handle, and the sight’s objective lens will strike the weapon when the feed tray cover is opened.

- If the AN/PVS-4 is removed from the rail the operator must take not of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

#### M249—AN/PVS-4 Zero and Boresight Targets, Feed Tray Cover Rail

### M249—AN/PVS-4 Mount Procedures, Units without AN/PAS-13 (H/MTWS)

###### M249 – AN/PVS-4 Mounting Instructions

The AN/PVS-4 may also be mounted on the M249 by using the AN/PVS-4—M249 Mounting Bracket (NSN 3040-01-233-0352).  Using this method precludes the need to attach a spacer and a rail grabber to the AN/PVS-4.

- Hook the bracket feet around the feed cover pin and position the bracket on top of the weapon.

- Turn bracket locking screw into the feed cover screw hole to secure bracket.

- Place the sight on the bracket aligning the sight mounting bracket locking screw.

- Tighten locking screw to secure night sight to bracket.

#### M249—AN/PVS-4 Zero and Boresight Targets, with AN/PVS-4 Bracket

### M249—M145 MGO Mount Procedures, Integrated Feed Tray Cover Rail

M249 – M145 MGO Mounting Instructions

The M145 MGO comes with an integrated rail grabber with torque limiting knob.  This allows the MGO to be attached to the M249 with Integrated Feed Tray Cover Rail with a minimum of time and effort.

- To install the MGO (1) loosen the clamping knob (2) until sufficient space exits to place the clamping jaws on either side of the mounting rail (3).  Tighten clamping knob (2) until two clicks are heard.

- Place the M145 approximately 70mm (2-3/4 inches in front of the firing eye.  Ensure that the M145 is securely attached to the feed tray cover rail and begin eye relief adjustment, IAW TM 9-1240-415-13&P.

- If the MGO is removed from the rail the operator must return the device to that same position in order to insure that zero is retained.

#### M249—M145 MGO Zero and Boresight Targets, Feed Tray Cover Rail

## M60 Machine Gun System Diagram

### M60—AN/PAQ-4B/C Mount Procedures

M60 – AN/PAQ-4B/C Mounting Instructions

The AN/PAQ-4B/C mounts on the M60 Machine Gun using the M60 Mounting Bracket (NSN:  5855-01-046-7272) and the Bracket Adapter (NSN:  5340-01-362-9873) IAW TM 11-5855-308-12&P-DRAFT.

- Remove the M60 hinge pin latch and hinge pin from the cover assembly.  Place the pin latch in the aiming guides on the left side of the Mounting Bracket and press together (see Figure).

- Place the Mounting Bracket on top of the machine gun cover so that the holes in the front of the bracket align with the cover assembly pin holes.

- Insert the longer hinge pin supplied with the bracket through the bracket and cover assembly and secure by inserting the hinge pin latch.

- Turning counter clockwise loosen the wing nuts on both leg clamps and position the leg clamps under the cover assembly.  Secure the Mounting Bracket by tightening the wing nuts firmly.  The split washer should be next to the wing nut and the flat washer next to the bracket.

- Place the Bracket Adapter in the AN/PAQ-4B/C mounting groove flush with the front of the AN/PAQ-4B/C.  Tighten the thumbscrew clockwise.

- Position the AN/PAQ-4B/C with Bracket Adapter onto the M60 Mounting Bracket mounting groove.  Align the front edge of the Bracket Adapter and front edge of the groove.  Tighten the lever screw assembly.

#### M60—AN/PAQ-4 B/C Zero and Boresight Targets

### M60—AN/PAS-13 (MTWS) Mount Procedures

M60 – AN/PAS-13, TWS Mounting Instructions

(See Annex B for Target Prep Instructions)

The AN/PAS-13, TWS, is mounted by installing the AN/PAS-13’s M60 Mounting Bracket (P/N 80063A3170620) IAQ TM 11-5855-302-12&P.

- Install the AN/PAS-13’s M60 Mounting Bracket (1) on the M60 Machine Gun (2) IAW instructions contained in TM 11-5855.302-12 &P.

- Loosen the clamping knob (3) on the AN/PAS-13 (4) until there is sufficient space between the jaws of the rail grabber to fit on either side of the rail.

- Select a slot on the rail (5) that provides a convenient location for the AN/PAS-13 to be mounted (i.e. allows the operator to access the controls and to view the target through the eye cup.

CAUTION

Insure the AN/PAS-13 lens does not strike the weapon when the feed tray cover is opened.

- Tighten the torque limiting clamping knob (3) until two clicks are heard.

- If the operator must remove the sight from the rail he must insure that he returns the device to the same rail slot in order to retain zero.

#### M60—AN/PAS-13 Zero and Boresight Targets

### M60—AN/PEQ-2A Mount Procedures

M60 – AN/PEQ-2A Mounting Instructions

The AN/PEQ-2A mounts on the M60 Machine Gun using the M60 Mounting Bracket (NSN:  5855-01-046-7272) and the Bracket Adapter (NSN:  5340-01-362-9873) IAW TM 11-5855-308-12&P-DRAFT.

- Remove the M60 hinge pin latch and hinge pin from the cover assembly.  Place the pin latch in the aiming guides on the left side of the Mounting Bracket and press together (see Figure).

- Place the Mounting Bracket on top of the machine gun cover so that the holes in the front of the bracket align with the cover assembly pin holes.

- Insert the longer hinge pin supplied with the bracket through the bracket and cover assembly and secure by inserting the hinge pin latch.

- Turning counter clockwise loosen the wing nuts on both leg clamps and position the leg clamps under the cover assembly.  Secure the Mounting Bracket by tightening the wing nuts firmly.  The split washer should be next to the wing nut and the flat washer next to the bracket.

- Place the Bracket Adapter in the AN/PEQ-2A mounting groove flush with the front of the AN/PEQ-2A.  Tighten the thumbscrew clockwise.

# Position the AN/PEQ-2A with Bracket Adapter onto the M60 Mounting Bracket mounting groove.  Align the front edge of the Bracket Adapter and front edge of the groove.  Tighten the lever screw assembly.

#### M60—AN/PEQ-2A Zero and Boresight Targets

### M60—AN/PVS-4 Mount Procedures

M60 – AN/PVS-4 Mounting Instructions

The AN/PVS-4 mounts on the M60 Machine Gun using the M60 Mounting Bracket (NSN:  5855-01-046-7272).

- Pull the M60 bolt to the rear and put the weapon on SAFE.

- Raise the M60 feed cover and remove the hinge pin from the cover assembly by removing the latch inside the hinge pin first.  Place the hinge pin in the storage position on the left side of the mounting bracket then insert the latch into the hinge pin to secure.

- Position the mounting bracket assembly on top of the feed cover so that the holes in the front of the bracket align with cover assembly hinge pin holes.

- Insert the longer hinge pin supplied with the bracket from the right side through the bracket and cover assembly and secure by inserting the hinge pin latch into the left side of the pin.

- Loosen the wingnuts on both leg clamps and position the clamp under the cover assembly.  Secure the mounting bracket by tightening the wingnuts firmly.  Close feed cover.

- Mount the sight to the bracket by aligning the scribe line on the sight and the bracket.  Tighten the screw to secure the sight to the bracket.

#### M60—AN/PVS-4 Zero and Boresight Targets

### M60—M145, Machine Gun Optic, Mount Procedures

M60 – M145, MGO Mounting Instructions

The M145, MGO, is mounted by installing the AN/PAS-13’s M60 Mounting Bracket (P/N 80063A3170620).  See TM 11-5855-302-12&P for detailed installation instructions.

- Install the AN/PAS-13’s M60 Mounting Bracket (1) on the M60 Machine Gun (2) IAW instructions contained in TM 11-5855.302-12 &P.

- Loosen the clamping knob (3) on the M145, MGO (4) until there is sufficient space between the jaws of the rail grabber to fit on either side of the rail.

- Place the M145 approximately 70mm (2-3/4 inches) in front of the firing eye.  Tighten the Torque Limitiing Knob on the rail grabber until two clicks are heard.

- Ensure the mount is fastened, begin eye relief adjustment, IAW TM 9-1240-415-13&P.

CAUTION

Insure that the objective lens of the M145 does not strike the weapon when the feed tray cover is raised.

- If the operator must remove the sight from the rail he must take note of the slot and insure that he return the device to the same rail slot in order to retain zero.

#### M60—M145 MGO Zero and Boresight Targets

## M240B Machine Gun System Diagram

### M240B Iron Sight 25m Zero and 10m Boresight Offset Targets

### M240B—AN/PAQ-4B/C Mount Procedures, Feed Tray Cover Rail

M240B – AN/PAQ-4B/C Mounting Instructions

The AN/PAQ-4B/C (1) is mounted on the top cover rail (2) (see arrow) using the AN/PAQ-4B/C Bracket Assembly) (NSN 5340-01-390-3812).

- Mount the bracket assembly to the AN/PAQ-4B/C (1) using the thumbscrew on the AN/PAQ-4B/C.

- Loosen the clamping knob (3) until the rail grabber/mount has sufficient space to fit over the top cover rail (2).  Tighten the clamping knob until two clicks are heard.

- The AN/PAQ-4B/C may be placed at whichever position on the rail is most convenient for the operator.  If however the AN/PAQ-4B/C is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

- Install the remote switch (4) in a convenient location using the provided cable hangers.

#### M240B—AN/PAQ-4B/C Targets Using Mounting Bracket/Picatinny Rail Grabber on Feed Tray Cover Rail

#### M240B—AN/PAQ-4B/C Targets Using “Insight” Low Profile Rail Grabber on Feed Tray Cover Rail

### M240B—AN/PAQ-4B/C Mounting Instructions Utilizing Mounting Bracket/Picatinny Rail Grabber on Forward Rails

The AN/PAQ-4B/C may be mounted on the left or right side rails using the Mounting Bracket/Picatinny Rail Grabber (NSN 5340-01-458-0473) depicted in the diagram at left.

- Attach the Mounting Bracket/Picatinny Rail Grabber(1) to the AN/PAQ-4B/C (2) using the thumbscrew on the AN/PAQ-4B/C.

- Loosen the clamping knob until the rail grabber/mount has sufficient space to fit over the left side rail (3).  Tighten the clamping knob until two clicks are heard.

- The AN/PAQ-4B/C may be placed at whichever position, on the left side rail, is most convenient for the operator.  If however the AN/PAQ-4B/C is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

- Install the remote switch in a convenient location using the provided cable hangers.

The AN/PAQ-4B/C may also be mounted on the top or right rails, following the procedure laid out above.  Supporting target offsets for each configuration follow:

#### M240B—AN/PAQ-4B/C Targets Using Mounting Bracket/Picatinny Rail Grabber on Left Rail

#### M240B—AN/PAQ-4B/C Targets Using Mounting Bracket/Picatinny Rail Grabber on Right Rail

### M240B —AN/PAQ-4B/C Mounting Instructions Utilizing “Insight” Low Profile Rail Grabber on Forward Rails

The AN/PAQ-4B/C (1) may be mounted on either the left or right forward rails by using the Insight Low Profile Rail Grabber (2) depicted in the diagram at left.

- Attach the Insight Low Profile Rail Grabber to the AN/PAQ-4B/C (1) using the thumbscrew on the AN/PAQ-4B/C.

- Loosen the clamping knob (3) until the rail grabber has sufficient space to fit over the rail (4).  Tighten the clamping until a snug fit is achieved.

- The AN/PAQ-4B/C may be placed at whichever position on the rail is most convenient for the operator.  If however the AN/PAQ-4B/C is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

# Install the remote switch in a convenient location using the provided cable hangers.

# Note:  The AN/PAQ-4B/C may be placed on either the left or right rail using the procedure outlined above.  Supporting targets appear on the following pages.

#### M240B—AN/PAQ-4B/C Targets Using “Insight” Low Profile Rail Grabber on Left Rail

#### M240B—AN/PAQ-4B/C Targets Using “Insight” Low Profile Rail Grabber on Right Rail

### M240B—AN/PAS-13 (MTWS) Mount Procedures

M240B – AN/PAS-13, TWS Mounting Instructions

(See Annex B for Target Prep Instructions)

The AN/PAS-13 comes with an integrated rail grabber with torque limiting knob.  This allows the MGO to be attached to the M240B Feed Tray Cover Rail with a minimum of time and effort.

- In order to install the AN/PAS-13 (1) loosen the clamping knob (2) (hidden behind TWS) until sufficient space exits to place the clamping jaws on either side of the mounting rail (3).  Tighten clamping knob (2) until two clicks are heard.

- The AN/PAS-13 may be placed at position number 5 or back (counting from the back of the rail to the front) on the top feed tray cover rail, as long as the rail grabber/mount does not extend beyond the rail.  Should the device be installed forward of the number five slot the sight will interfere with the opera-

tor’s ability to raise the barrel handle and the sight’s objective lens will strike the weapon, when the feed tray cover is opened.

- If the AN/PAS-13 is removed from the rail the operator must return the device to the same position it was zeroed at in order to insure that zero is retained.

#### M240B—AN/PAS-13 Zero and Boresight Targets

### M240B—AN/PEQ-2A Mount Procedures on Feed Tray Cover Rail

M240B – AN/PEQ-2A Mounting Instructions

The AN/PEQ-2A (1) is mounted on the top cover rail (2) (see arrow) by using the Mounting Bracket/ Picatinny Rail Grabber (NSN 5340-01-458-0473) (2) depicted in the diagram at left.

- Mount the bracket assembly to the AN/PEQ-2A (1) using the thumbscrew on the AN/PEQ-2A.

- Loosen the clamping knob (on reverse side of AN/PEQ-2A) until the rail grabber/mount has sufficient space to fit over the top cover rail (2).  Tighten the clamping knob until two clicks are heard.

- The AN/PEQ-2A may be placed at whichever position on the rail is most convenient for the operator.  If however the AN/PEQ-2A is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

- Install the remote switch (not shown) in a convenient location using the provided cable hangers.

Note:  AN/PEQ-2A may also be mounted using the “Insight” Low Profile Rail Grabber using the same mounting procedure outlined above.  Supporting targets for both configurations appear in the following pages.

#### M240B—AN/PEQ-2A Targets Using Mounting Bracket/Picatinny Rail Grabber on Feed Tray Cover Rail

#### M240B—AN/PEQ-2A Targets Using “Insight” Low Profile Rail Grabber on Feed Tray Cover Rail

### M240B—AN/PEQ-2A Mounting Instructions Utilizing Mounting Bracket/Picatinny Rail Grabber on Forward Rails

The AN/PEQ-2A (1) may be mounted on either the left or right forward rails by using the Mounting Bracket/ Picatinny Rail Grabber (NSN 5340-01-458-0473) (2) depicted in the diagram at left.

- Attach the Mounting Bracket/ Picatinny Rail Grabber to the AN/PEQ-2A (1) using the thumb-screw on the AN/PEQ-2A.

- Loosen the clamping knob (3) until the rail grabber has sufficient space to fit over the rail (4).  Tighten the clamping knob until two clicks are heard.

- The AN/PEQ-2A may be placed at whichever position on the rail is most convenient for the operator.  If however the AN/PEQ-2A is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

# Install the remote switch in a convenient location using the provided cable hangers.

# Note:  The AN/PEQ-2A may be placed on either the left or right rail using the procedure outlined above.  Supporting targets appear on the following pages.

#### M240B—AN/PEQ-2A Targets Using Mounting Bracket/Picatinny Rail Grabber on Left Rail

#### M240B—AN/PEQ-2A Targets Using Mounting Bracket/Picatinny Rail Grabber on Right Rail

### M240B—AN/PEQ-2A Mounting Instructions Utilizing “Insight” Low Profile Rail Grabber on Forward Rails

The AN/PEQ-2A (1) may be mounted on either the left or right forward rails by using the Insight Low Profile Rail Grabber (2) depicted in the diagram at left.

- Attach the Insight Low Profile Rail Grabber to the AN/PEQ-2A (1) using the thumbscrew on the AN/PEQ-2A.

- Loosen the clamping knob (3) until the rail grabber has sufficient space to fit over the rail (4).  Tighten the clamping knob until the device fits snugly on the rail.

- The AN/PEQ-2A may be placed at whichever position on the rail is most convenient for the operator.  If however the AN/PEQ-2A is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

# Install the remote switch in a convenient location using the provided cable hangers.

Note:  The AN/PEQ-2A may be placed on either the left or right rail using the procedure outlined

#### M240B—AN/PEQ-2A Targets Using “Insight” Low Profile Rail Grabber on Left Rail

#### M240B—AN/PEQ-2A Targets Using “Insight” Low Profile Rail Grabber on Right Rail

### M240B—AN/PVS-4 Mount Procedures

M240B – AN/PVS-4 Mounting Instructions

In order to properly mount the AN/PVS-4 (1) to the M240B (4) the unit Armorer must first install a spacer (NSN 5365-01-447-8991) and a rail grabber/mount (NSN 5340-01-449-8533) on the AN/PVS-4.

- Loosen the clamping knob (2) until sufficient space exits to place the clamping jaws on either side of the mounting rail (3).  Tighten clamping knob (2) until two clicks are heard.

- The AN/PVS-4 may be placed at position 5 or back (counting from the back of the rail to the front) on the top feed tray cover rail, as long as the rail grabber/mount does not extend beyond the rail.  Should the device be installed forward of the number five slot the sight will interfere with the operators ability to raise the barrel handle, and the sights objective lens will strike the weapon when the feed tray cover is opened.

- If the AN/PVS-4 is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

#### M240B—AN/PVS-4 Zero and Boresight Targets

### M240B—M145, Machine Gun Optic, Mount Procedures

M240B – M145 MGO Mounting Instructions

The M145 MGO comes with an integrated rail grabber with torque limiting knob.  This allows the MGO to be attached to the M240B with Integrated Feed Tray Cover Rail with a minimum of time and effort.

- In order to install the MGO (1) loosen the clamping knob (2) until sufficient space exits to place the clamping jaws on either side of the mounting rail (3).  Tighten clamping knob (2) until two clicks are heard.

- Place the M145 approximately 70mm (2-3/4 inches in front of the firing eye.  Ensure that the M145 is securely attached to the feed tray cover rail and begin eye relief adjustment, IAW TM 9-1240-415-13&P.

- If the MGO is removed from the rail the operator must take note of the position at which the device was zeroed, and return the device to that same position in order to insure that zero is retained.

#### M240B—MGO Zero and Boresight Targets

## M2 Machine Gun System Diagram

### M2 MG Iron Sight Offset Target

### M2—AN/PAS-13 (HTWS) Mount Procedures

##### M2 – AN/PAS-13, TWS Mounting Instructions

(See Annex B for Target Prep Instructions)

Mounting HTWS on M2 Machine Gun.  Refer to Figure for mounting HTWS on M2 machine gun.

- Fold rear sight (1) forward to storage position.

- Release cover latch (2) at side of cover (3) and fully raise cover.

- Mount M2 bracket (Part No. A3170570) (4) on M2 machine gun (5).

  - Release three locking cams (6 and 7) on bracket (4).

  - Place bracket (4) over breech (8) of M2 machine gun (5).

  - Slide bracket (4) over ledge (9) of M2 machine gun (5) until inside edge (10) of bracket touches front edge (11) of rear sight base (12).

  - Swing side locking cam (6) towards rear of M2 machine gun (5).

  - Swing two top locking cams (7) towards rear of M2 machine gun (5).Lower cover (3) until cover latch (2) engages.

- Loosen locking knob (13) and swing range lever (14) to NEAR position.  Hand tighten knob.

- Install HTWS (15) on bracket rail.

  - Loosen knob (16) on rail grabber until there is sufficient space to fit the jaws on either side of the rail.

  - Select slot a on rail for mounting.  Any slot may be used as long as rail grabber/mount does not hang over edge of rail.

  - Place bar (17) of mount in slot of rail and hand tighten knob on rail grabber/mount until two clicks are heard.

#### M2—AN/PAS-13 Zero and Boresight Targets

### M2—AN/PEQ-2A Mount Procedures

M2 – AN/PEQ-2A Mounting Instructions

The AN/PEQ-2A is attached to the M2 Machine Gun using a Bracket Adapter (NSN:  5340-01-362-9873) and an M2 Mounting Bracket (NSN:  5855-01-045-5482).

- Release the catch at the left side of the top cover and raise the cover to the UP position.

- Position the M2 Mounting Bracket assembly over the breech of the Machine Gun and slide it to the rear until it stops beyond the rear edge of the breech (see Figure).

- Swing the three locking cams to the rear to secure the bracket to the weapon (side cam first, followed by two top locking cams).

- Close the top cover and secure with the catch.

- Secure the Bracket Adapter to the underside of the AN/PEQ-2A.

- Place the Bracket Adapter into the M2 bracket mounting groove with the rear of the adapter flush with the rear of the bracket.  Tighten the bracket’s lever screw into the Bracket Adapter hole.

#### M2—AN/PEQ-2A Zero and Boresight Targets

### M2—AN/TVS-5 Mount Procedures

M2 – AN/TVS-5 Mounting Instructions

Install the AN/TVS-5 Mounting Bracket (NSN 5855-01-045-5482) per instructions contained in TM 11-5855-214-10.

- Release the catch at the left side of top cover and raise cover to the UP position.

- Position the M2 mounting bracket assembly over the breech of the machinegun and slide it to the rear until it stops.

- Swing the three locking cams to the rear to secure the bracket to the weapon (side cam first, followed by two top locking cams).

- Close the top cover and secure it with the catch.

- Install the sight on the M2 mounting bracket assembly by positioning it in the groove at the top rear of the bracket so that the scribe line in the sight on the bracket is aligned with the scribe line in the sight-mounting adapter.  Tighten the lever screw to secure the sight to the bracket.  It will be easier to tighten the lever screw if you will place an empty cartridge case over the lever arm to increase the amount of leverage applied.

#### M2—AN/TVS-5 Zero and Boresight Targets

## MK19 Grenade Machine Gun System Diagram

### MK19 Grenade Machine Gun Iron Sight Target Offset

### MK19—AN/PAS-13 (HTWS) Mount Procedures

MK19–AN/PAS-13, TWS Mounting Instructions

(See Annex B for Target Prep Instructions)

- Install MK19 bracket (1) (Part No. A3260830) on MK19 machine gun (2) IAW TM 11-5855-302-12&P.

- Slide MK19 bracket (1) onto mount (3) until locking pin (4) engages in hole (5) of mount.

  - Confirm locking pin (4) is fully engaged.

  - Raise arm (6) of bracket (1).

  - Loosen locking knob (7).

  - Push in locking knob (7) and raise arm (6) to up most position (2057 meters).

  - Hand tighten locking knob (7).

3.	Install HTWS (not shown) on rail.

a.	Loosen TWS grabber knob.

b.	Select slot on rail for mounting.  Any slot may be used as long as mount does not hang over edge of rail.

c.	Place bar of mount in slot of rail and hand tighten knob on mount until two clicks are heard.

Note:  Mount (3) previously installed by supporting direct support maintenance unit.

# MK19—AN/PAS-13 Zero Procedure

- Select a fixed target at 400 to 600 meters.

- Set range on MK19 bracket to range of target.

- Place TWS in operation.

- Set FOV ring to NARROW position.

- Press and release RETICLE SELECT switch until display shows reticle for MK19 machine gun.

- Use the RETICLE ADJUST switch to set Azimuth and Elevation indicators to zero.

- Place reticle aim point on center of mass of target by moving Traverse and Elevation mechanism (T and E) of gun.  Fire one round and observe impact of round.

- Adjust reticle to move impact of round to center of mass of target.

  - If impact of round Is behind target, use the RETICLE ADJUST switch to decrease the up elevation setting or increase the down elevation setting.

  - If impact of round is in front of target, use the RETICLE ADJUST switch to increase the up elevation setting or decrease the down elevation setting.

  - If impact of the round is left of target, use the RETICLE ADJUST switch decrease the left azimuth setting or increase the right azimuth setting.

  - If impact of round is right of target, use the RETICLE ADJUST switch to increase the left azimuth setting or decrease the right azimuth setting.

- Repeat steps 7 and 8 until round impacts target.

- Record setting of Azimuth and Elevation indications.

#### MK19—AN/PAS-13, TWS Zero and Boresight Targets

### MK19—AN/PEQ-2A Mount Procedures

MK19 – AN/PEQ-2A Mounting Instructions

The AN/PEQ-2A is mounted to the MK19 in the same manner that theAN/PEQ-2A is mounted to the M2 machine gun, using the same mounting bracket (NSN 5855-01-045-5482) per instructions contained in TM 11-5855-214-10.

- Release the catch at the left side of top cover and raise cover to the UP position.

- Position the M2 mounting bracket assembly over the breech of the machinegun and slide it to the rear until it stops.

- Swing the three locking cams to the rear to secure the bracket to the weapon (side cam first, followed by two top locking cams).

- Close the cover and secure it with the catch.

- Attach the AN/PEQ-2A to the bracket adapter by using the thumbscrew.

- Install the AN/PEQ-2A on the M2 mounting bracket assembly by positioning it in the groove at the top rear of the bracket so that the scribe line in the sight on the bracket is aligned with the scribe line in the sight-mounting adapter.  Tighten the lever screw to secure the sight to the bracket.  It will be easier to tighten the lever screw if you will place an empty cartridge case over the lever arm to increase the amount of leverage applied.

#### MK19—AN/PEQ-2A Zero and Boresight Targets

### MK19—AN/TVS-5 Mount Procedures

MK19 – AN/TVS-5 Mounting Instructions

The AN/TVS-5 is mounted to the MK19 in the same manner that it is mounted to the M2 machine gun, and uses the same mounting bracket (NSN 5855-01-045-5482) per instructions contained in TM 11-5855-214-10.

- Release the catch at the left side of top cover and raise cover to the UP position.

- Position the M2 mounting bracket assembly over the breech of the machinegun and slide it to the rear until it stops.

- Swing the three locking cams to the rear to secure the bracket to the weapon (side cam first, followed by two top locking cams).

- Close the top cover and secure it with the catch.

- Install the sight on the M2 mounting bracket assembly by positioning it in the groove at the top rear of the bracket so that the scribe line in the sight on the bracket is aligned with the scribe line in the sight-mounting adapter.  Tighten the lever screw to secure the sight.

#### MK19—AN/TVS-5 Zero and Boresight Targets

# Annex A—References

TM 9-1005-201-10	Machine Gun, 5.56mm, M249 W/Equip, dtd July 1991

TM 9-1005-213-10	Machine Gun, caliber 50, Browning, M2 Heavy Barrel, w/ change 2 dtd 6 Aug 1996

TM 9-1005-224-10	Machine Gun, 7.62-MM, M60 W/E (1005-00-605-7710), April 1998

TM 9-1005-306-10	7.62mm M24 Sniper Weapon System (SWS), dtd June 1989

TM 9-1005-313-10	Machine Gun, 7.62mm, M240, M240B, M240C, M240E1, M240G, w/ change 1 dtd 1 Nov 1999

TM 9-1005-319-10	M16A2/M16A3/M16A4 Rifles and M4/M4A1 Carbines, dtd October 1998

TM 9-1010-221-10	Grenade Launcher, 40mm-M203 w/ changes 1-6 dtd 17 Aug 1998

TM 9-1010-230-10	Machine Gun, 40MM, MK19, MOD 3, dtd 30 May 2001

TM 9-1240-413-12&P	M68 Sight, Reflex (Close Combat Optic), w/Quick Release and Mount, dtd October 1997 w/ change 1 dtd 31 August 2001

TM 9-1240-415-13&P	M145 Telescope (Machine Gun Optic), dtd 28 February 2000

TM 11-5855-213-10	AN/PVS-4 (Night Vision Sight, Individual Served Weapon), dtd 1 February 1993

TM 11-5855-214-10	Night Vision Sight, Crew Served Weapon, AN/TVS-5, dtd 15 February 1989

TM 11-5855-301-12&P	Light, Aiming, Infrared, AN/PAQ-4B/C, dtd 15 May 2000

TM 11-5855-302-12&P	Sight-Thermal, AN/PAS-13 (V) 2&3, dtd 1 January 1997

TM 11-5855-303-12&P	Sight, Night Vision Sniper Scope AN/PVS-10, dtd 1 August 1997

TB 11-5855-303-12	Technical Bulletin, Operator’s Pamphlet, Sight, Night Vision Sniper Scope (SNS), AN/PVS-10, dtd 1 August 1997

TM 11-5855-306-10	Monocular Night Vision Device (AN/PVS-14), dtd 1 Jun 2000

TM 11-5855-308-12&P	Target Illuminator/Aiming Light (TPIAL) AN/PEQ-2A, dtd 15 May 2000

http://www.adtdl.army.mil	General Dennis J. Reimer Training and Doctrine Digital Library  (A copy of the Small Arms Integration Book can also be found at this web site.)

http://www.logsa.army.mil	The Logistics Support Activity (LOGSA) Web Site (Where, among other things, copies of Electronic Technical Manuals can be located.)

# Annex B—Sight/Accessory Operating Instructions

## AN/PAQ-4B/C, Light Aiming, Infrared

Operating Instructions

(TM 11-5855-301-12&P, 15 May 00)

Batteries:  BA-3058/U (x2)

General Functional Description

The Aiming Light projects an infrared laser beam which cannot be seen with the eye but can be seen with NVG’s.  The Aiming Light mounts on various weapons with Mounting Brackets and adapters.

The Aiming Light is activated by pressing on either the ON/OFF Switch lever, or the button on the optional Cable Switch.  Either switch connects power from two AA Batteries to an internal electronic circuit, which produces the infrared laser.  Internal lenses focus the infrared light into a narrow beam.

The direction of the beam is controlled by rotating the mechanical Adjusters with click detents. These adjusters are used to zero the Aiming Light to the weapon.  Once zeroed to the weapon, the Aiming Light projects the beam along the line of fire of the weapon.  The Optical Baffle prevents off-axis viewing of the Aiming Light beam by the enemy.

AIMING LIGHT CONTROLS AND INDICATORS

a.  Ajusters.  Adjusters enable the Aiming Light to be zeroed to the weapon. Adjuster movement has audible and tactile clicks.  When mounted on the weapon, each click moves the shot group 0.4 Inches at 25 meters (0.4 mrad). This equals one square on a M16A2 25-meter zeroing target.

- The arrow printed on the flange on either side of the adjuster knobs indicates the direction of shot group movement.

- To move the shot group in the direction of the arrow place a finger on the side of the adjuster knob between the arrows and rotate the knob in the direction which moves the finger towards the arrow.

- At the full clockwise end of travel of either adjuster, the adjuster becomes harder to turn and the white dot on the adjuster knob will align within 2 clicks of the white mark on the knob's front flange.

b. ON/OFF Switch

The ON/OFF switch has five positions (see table). The label printed on top of the Aiming Light only shows the switch function location, not the position number.

The Cable Switch provides momentary "Operation for the Aiming Light when mounted on selected weapons. The ON/OFF Switch must be in the OFF (#1 or #5) position for the button on the Cable Switch to properly activate the Aiming Light. Optional cable hangers are provided for securing the cable to the weapon.

"If environmental conditions are such that the soldier's ability to conduct a 25m zeroing of the device and weapon is being hindered due to "IR Blooming" one to the following methods should be used to reduce the blooming effect:

- Install the Borelight Filter that was issued with the device.  If it is not dark enough for this method to work effectively use method 2, as outlined below.

- Cut a 2 by 2 square block out of the center of the target.  The laser will bloom on the zero target until the aiming laser is emitting through the 2 x 2 hole.  Once the laser is properly centered on the hole the blooming is reduced and zeroing may continue with a higher assurance of completing a successful zero."

## AN/PAS-13 Thermal Weapon Sight

Batteries:  BA-5347A/U (x1) or

BB-2847/U (x1)

AN/PAS-13 Operating Instructions

(TM 11-5855-302-12&P, 1 Jan 97)

Turn the BRIGHTNESS knob clockwise to mid-range position to turn on TWS power. (One click will do.)

Place eye to eyecup and push until flaps inside eyecup open.

Looking at indicators, adjust diopter on eyepiece for best focus.

Remove eye from eyecup and wait for cool-down period to complete.

Open objective lens cover on telescope.

Place eye to eyecup and push until flaps inside eyecup open.

Set CONTRAST knob to AUTO or adjust for best scene.

Adjust FOCUS on telescope for best picture.

Adjust BRIGHTNESS knob for best picture.

Using BLK/WHT switch, select polarity as desired.

Rotate FOV ring to select WIDE or NARROW field of view as desired.

Repeat steps F through K as needed to accomplish mission.

Following operation, turn off power by pushing in and turning BRIGHTNESS knob fully counterclockwise to OFF detent position.

### AN/PAS-13 Zero and Boresight Targets Preparation Procedures

- Modify an M16A2 25-meter target.

  - Cut a square hole 4 squares wide by 4 squares high in a M16A2 25-meter zeroing target

  - Cut out a rectangle from a cardboard box, the same size as the M16A2 25-meter zeroing target (8.5” x 11”)

  - Estimate 1 inch in from each side of cardboard rectangle and cut out a rectangular hole as shown in Figure 2-31.

  - Tape cardboard frame to back of modified M16A2 25-meter zeroing target.

- Affix target to standard E-type silhouette or E-Type thermal silhouette

## AN/PEQ-2A, Target Pointer Illuminator/Aiming Light (TPIAL)

General Functional Description

(Continued)

- Battery Installation.  Unscrew the battery caps and install 2 AA batteries.  Orient the batteries as indicated by the markings on the AN/PEQ-2A body.

- The safety block can be installed in the Training Mode (blue side up) or Tactical Mode (black side up).  The Mode Selector is used to set the mode in which the TPIAL will operate and has 6 positions.  Positions 3, 4 & 5 can only be accessed in the Tactical Mode.   See Table 4-1 for Mode Selector Switch Functions.

- Mode Selector.  The mode selector is used to set the mode in which the AN/PEQ-2A will operate when the cable switch button or push button are depressed.  The mode selector positions are:

  - DUAL LO/HI - The aiming beam operates at low power and the illumination beam operates at full power. – The DUAL mode enables a target to be illuminated and fired upon using an aiming beam.  The illuminator operates at full power in all dual modes of operation.

  - DUAL HI/HI – The aiming beam operates at high power and the illuminator beam operates at full power. – The DUAL modes enable a target to be illuminated and fired upon using an aiming beam. The illuminator operates at full power in all dual modes of operation.

- Button Switch Operation:  Press the button to operate the TPIAL in hand held or mounted mode.  When the button is released the TPIAL turns off.  Press the button twice quickly to latch on for continuous operation.  Press it once again to turn off.  Whenever TPIAL is activated the green LED will light and will stay lit until the unit is turned OFF.

- Cable Switch:  Plug the cable in the back of the TPIAL.  Operation of the Cable Switch is the same as the Button Switch.

- Focus Knob:  Varies the illumination beam spread (Flood/Spot) based on range/size of area to be illuminated.

- Lens Caps:  Illuminator Lens Cap is a diffuser to used to emit a 45 degree cone (10’x10’).  Aiming Lens Cap is used in low power and zeroing.  Black Lens Cap blocks the laser when accidentally activated.

- Adjusters:  TPIAL is equipped with boresight adjusters for zeroing Aiming and Illumination Beams.  See Tables 4-2 &4-3.

| KNOB POSITION | OPERATION | REMARKS |
| --- | --- | --- |
| 0 OFF | The AN/PEQ-2A will not operate | When underwater, the mode switch should be OFF to preclude water pressure on the button switch from inadvertently turning ON the unit. |
| 1 AIM LO | The aiming beam operates at low power. | Low power is useful to reduce night vision device blooming of the aiming spot on close targets. It is also useful for training because the beam power meets the criteria of an eye-safe laser. |
| 2 DUAL LO | The aiming beam operates at low power and the illuminating beam operates at low power | Low power aiming and illuminating is useful to reduce the effects of blooming when engaging targets at close range. It is also useful for training because the beam power meets the criteria of an eye-safe laser. |
| 3 AIM HI | The aiming beam operates at high power. | Hi power is useful for aiming or pointing at distant targets. |
| 4 DUAL LO/HI | The aiming beam operates at low power and the illumination beam operates at full power. | The DUAL mode enables a target to be illuminated and fired upon using an aiming beam. The illuminator operates at full power in all dual modes of operation. |
| 5 DUAL HI/HI | The aiming beam operates at high power and the illumination beam operates at full power. | The DUAL mode enables a target to be illuminated and fired upon using an aiming beam. The illuminator operates at full power in all dual modes of operation. |

Table 4-1

Adjuster Rotation and Shot Group Movement for the Aiming Beam.

| ZEROING THE AIMING SPOT | Adjuster Movement | Shot Group Movement |
| --- | --- | --- |
| Top Adjuster Elevation | CW CCW | Up Down |
| Side Adjuster Azimuth (Windage) | CW CCW | Right Left |

Adjuster Rotation and Illumination Area Movement for the Illumination Beam.

| ZEROING THE ILLUMINATION BEAM | Adjuster Movement | Beam Movement |
| --- | --- | --- |
| Top Adjuster Elevation | CW CCW | Down Up |
| Side Adjuster Azimuth (Windage) | CW CCW | Right Left |

## AN/PVS-4, Night Vision Sight, Individual Served Weapon

Batteries:  BA-5567/U (x1) or BA-3058/U (x2)

AN/PVS-4, Night Vision Sight, Individual Served Weapon

(TM 11-5855-213-10w/c1, 1 Feb 93)

General Functional Description

TheAN/PVS-4 is a passive battery-operated night sight used for observation and accurate firing of individual served weapons during night time conditions (moonlight, starlight, skyglow) against targets out to 400 meters.  This sight is less effective when viewing into rain, fog, sleet, snow, smoke, shadow and other obscurants.

- Turn the ON-OFF/TUBE BRIGHTNESS control and ON—OFF/TUBE BRIGHTNESS switch and ON—OFF/RETICLE BRIGHTNESS control counterclockwise to OFF before installing batteries.

- Install batteries.

- Press your eye against the eyeguard to open the rubber leaves that prevent emission of stray light.

- Turn the ON-OFF/TUBE BRIGHTNESS control as shown, clockwise to turn on the sight.

- Adjust the ON-OFF/TUBE BRIGHTNESS control to the setting that provides the best target-to-background contrast at a minimum distance of 25 meters.

- Turn the ON-OFF/RETICLE BRIGHTNESS control clock-wise to turn on the light emitting diode. Adjust the reticle light intensity so that the reticle is just visible against the background.

- Turn the Diopter Focus Ring until you get the clearest image of the reticle pattern.

- Turn the Objective Focus Ring until the target in the field of view is sharply defined at aiming distance of 25 meters.

- The sight may be zeroed during daylight (w/daylight cover on) or darkness with appropriate reticle adjustment actuators.

- Turn the ON-OFF/RETICLE BRIGHTNESS and ON/OFF/TUBE BRIGHTNESS control fully counterclockwise to off position when you are through using the sight. Remove battery or battery adapter.

## AN/PVS-10, Sight, Night Vision Sniper Scope (SNS)

General Description

Batteries:  AA Alkaline (x2) or AA Lithium (x2)

The SNS System is used with the M24 Sniper Weapon System.  The SNS System is an integrated day/night weapon system providing both day and night firing capability in a single sight.

Weight:	4.7 pounds

Field of View:	3 degrees

Magnification:	8.5X

Minimum Range:	25 meters

Effective Range:

Day:	800 meters

Night:	600 meters

AN/PVS-10 Operating Instructions

(TM 11-5855-303-12&P, 1 Aug 97)

DAY OPERATION

Adjust Diopter (Eyepiece) Focus

NOTE

Eyepiece focus corrects for the individual sniper’s eye and once set should not be reset unless the diopter focus knob is removed.  Adjustment of diopter is intended to focus the reticle only, not the image being viewed.  DO NOT use the eyepiece focus to adjust for a blurred image.

- Place the objective lens cap over the objective lens, so that you will concentrate on the reticle and not a target.

- Unlock diopter focus knob by turning locking ring counterclockwise.

- Adjust eyepiece focus by rotating the diopter focus knob in and out until the reticle is in a clear sharp focus.  Maintain some space between the locking ring and diopter focus knob to ensure your diopter setting is not accidentally changed when tightening the locking ring.

- Secure the eyepiece by turning the diopter-locking ring clockwise.

Adjust Objective (Target) Focus

NOTE

The objective can be focused on objects (targets) from 25 meters to infinity.

            - View an object (target) in the region of interest.

# Adjust the objective focus by rotating the objective focus knob to obtain the sharpest image of the target.  DO NOT adjust the diopter (eyepiece) focus.

# Elevation and Windage Adjustment

NOTE

Once the weapon has been zeroed at specific range and the elevation dial set to this range, all other range markings should be considered approximates.

- Look at the target through SNS and use the mil dot reticle to estimate range to target.  In order to see full FOV (40 degrees) insure that the eyeguard is pushed fully inward.

- Rotate the elevation dial to estimate range.  Each click of elevation adjustment equals one (1) minute of angle (MOA).

- Observe your surroundings and the area around the target and estimate adjustment needed for direction and speed of wind.

- Rotate the windage dial to adjust for wind.  Each click of windage adjustment equals ½ MOA.  Rotating the dial down or clockwise moves the strike of the round to the left as indicated on the dial by L, and rotating the dial up or counterclockwise moves the strike of the round to the right as indicated on the dial by R.

###### NIGHT OPERATION

The operational controls and adjustments described above for DAY OPERATION are the same for NIGHT OPERATION.  The differences are as described below:

NOTE

The ELEVATION and WINDAGE DIALS have a raised pin to help locate Battlesight Zero at night.  The pin is on the index line marked “5” on the Elevation Dial, and on the index line marked “0” on the Windage Dial.

NOTE

The TUBE and RETICLE BRIGHTNESS controls are touch type (button) controls and only require pressing to change the setting.  Maintaining pressure on the UP or DOWN controls causes the function to go to its maximum or minimum slowly.  There may be a short delay before you notice tube or reticle brightness changes.  The ON/OFF buttons are flat, the UP buttons are concave with a teat, and the DOWN buttons are concave.

Turn On and Adjust Image Intensifier Tube

- Turn mode selector to NIGHT mode.

- Turn tube ON by pressing the TUBE ON/OFF button.

- Look at the target through SNS and adjust tube gain by pressing the UP or DOWN buttons to obtain a best image of the target.

Turn On and Adjust Reticle Brightness

- Turn ON and adjust Tube as specified above.

- Turn reticle brightness ON by pressing the RETICLE BRIGHTNESS ON/OFF button.

- Look at the target through SNS and adjust reticle brightness by pressing the UP or DOWN buttons to your preference.

## AN/PVS-14, Monocular Night Vision Device

Batteries: BA-3058/U (x2) or

AA 1.5Vdc Lithium L91 (x2)

AN/PVS-14 Operating Instructions

(TM 11-5855-10, I June 00)

General Functional Description

The MNVD is a hand-held, head mounted, helmet mounted, or weapon mounted night vision system that enables walking, weapon firing, short range surveillance, map reading, vehicle maintenance and administrating first aid in both moonlight and starlight. Each unit allows for vertical adjustment (by using head strap), fore and aft adjustment, objective lens focus and eyepiece focus.  The monocular is also equipped with an IR source, a low-battery indicator and a gain control.  Accessories include Demist Shield, Light Interface Filter (LIF), Sacrificial Window, Compass and Tether Cord.  A 3X Magnifier is an Additional Authorized Item.

NOTE

The AN/PVS-14 can be used in conjunction with a collimated dot aiming device mounted on the forward mounting rail.  The brightness control for the aiming device should be set at or near its minimum setting.

Perform the following procedures for weapon mounted operation:

- Ensure that the batteries are installed per paragraph 2-6, TM 11-5855-306-10.

- Assemble the small arms mounting adapter to the monocular per paragraph 2-15, step 1 and 2, TM 11-5855-306-10.

- Mount the monocular with adapter onto the Ml6/M4 receiver rail per paragraph 2-15, step 3 and 4, TM 11-5855-306-10.

- Turn the power switch ON.

- Rotate the diopter adjustment ring for the clearest view of the image intensifier screen.

- Adjust the objective lens focus while observing an object until the sharpest image is obtained.

- Turn power switch OFF and remove batteries.

INFRARED (IR) ILLUMINATOR OPERATIONS

The IR illuminator is a light that is invisible to the unaided eye for use during conditions of extreme darkness. However, the light from the illuminator can be detected by the enemy using night vision devices.

NOTE

The purpose of the IR illuminator is for viewing at close distances up to 3 meters when additional illumination is needed.

- Pull the RESET/OFF-ON-IR/PULL switch knob out and rotate clockwise to the IR position. With the monocular held to the eye, observe that a red light appears in the eyepiece. This indicates that the IR illuminator is operating.

- For momentary IR, turn the RESET/OFF-ON-IR/PULL switch clockwise (without pulling) past the ON position. Observe that a red light appears in the eyepiece.

## AN/TVS-5, Night Vision Sight, Crew Served Weapon

Batteries:  BA-5567/U (x2) or BA-3058/U (x2)

AN/TVS-5 Operating Instructions

(TM 11-5855-214-10, 15 Feb 89)

General Functional Description

The AN/TVS-5 is a portable, battery operated electro-optical instrument used for observation and aimed fire of weapons at night.  It amplifies reflected light such as moonlight, starlight, and skyglow so that the viewed scene becomes clearly visible to the operator.

The sight does not emit visible or infrared light (except from the eye-piece) that can be detected by the enemy.  See following table for operating instructions.

- Turn the ON-OFF TUBE BRIGHTNESS control and ON-OFF/RETICLE BRIGHTNESS control counter clockwise to OFF before installing batteries.

- Install Batteries

- Press your eye against the eyeguard to open the rubber leaves that prevent emission of stray light.

- Turn the ON-OFF/TUBE BRIGHTNESS control clockwise to turn ON the sight.

- Adjust the ON-OFF/TUBE BRIGHTNESS control to the lowest setting that will provide good target-to-background contrast at a minimum distance of 25 meters.

- Turn the ON-OFF/RETICLE BRIGHTNESS control clockwise to turn on the light emitting diode. Adjust the light intensity so that the reticle is just visible against the background.

- Turn the Diopter Focus Ring until you get the clearest image of the reticle pattern.

- Turn the Object Focus Ring until the target in the field of view is sharply defined.

- The sight may be zeroed during daylight (w/Daylight Cover on) or darkness with the appropriate reticle adjustment actuators and patterns.

- Turn the RETICLE BRIGHTNESS/TUBE BRIGHTNESS controls to OFF when you are through using the sight.  Remove the batteries.

| Name | Function |
| --- | --- |
| ON-OFF/TUBE BRIGHTNESS | Applies power to sight. Enable ON_OFF RETICLE BRIGHTNESS control to function. Controls brightness of image intensifier tube. |
| ON-OFF/RETICLE BRIGHTNESS | Applies power to reticle. Controls brightness of reticle. |
| Objective focus ring | Adjusts system focus from 25 meters to infinity. |
| Diopter focus ring | Adjusts focus of eyepiece |
| Diopter indicator | Indicates direction of rotation of diopter focus ring for + or – diopter |
| Reticle elevation adjustment actuator | Controls reticle adjustment up or down. Each click of adjustment moves strike of round fired 1.0 inch at 100 meters. |
| Reticle azimuth adjustment actuator | Controls reticle adjustment right or left. Each click of adjustment moves strike of round fired 1.0 inch at 100 meters. |
| Reticle patterns | Indicate aiming points of weapons and provide ranging information. |

## M203 Grenade Launcher

# Grenade Launcher Instructions

(TM 9-1010-221-10)

- The M203 Grenade Launcher attaches to either the M16 series Rifle or the M4 series Carbine.

- The M203 launches a 40mm grenade within the following range limitations.

- Maximum Range:  400 meters

- Maximum Effective Range:

  - Area target:  350 meters

  - Point target:  150 meters

- Minimum Safe Range:

  - Combat:  31 meters

  - Training:  130 meters

# WARNING

When you fire high explosive (HE) greandes at targets within 130 meters be in a protected position.  When training, do not fire at targets within 130 meters.  When in combat, do not fire at targets closer than 31 meters.

3.	The M203 is mounted on the M4 Carbine and the M16 Rifle by the unit’s Direct Support Maintenance Company.  Unit personnel are not authorized to, and should not attempt to, install the M203 on the weapon.

## M68-Close Combat Optic

- Elevation Adjustment Screw

- Adjustment Cap

- Battery (Installed in Battery Compartment)

- Batter Cap

- Front Lens Cover

- Adjustment Cap

- Windage Adjustment Screw

- Rotary Switch

- Rear Lens Cover

- Torque Knob (Behind M68)

# CAUTION

Hand tighten adjustment caps only.  Using tools to tighten adjustment caps could damage equipment.

# WARNING

At higher intensity settings, red dot is visible through front of sight.  For night vision operations, close front lens cover before turning rotary switch counterclockwise to OFF position.  Failure to follow this warning could reveal your position to your enemy.

General Functional Description

The M68 sight is a reflex (non-telescopic) sight. It uses a red aiming reference (collimated dot) and is designed for the “two eyes open” method of sighting. The dot follows the horizontal and vertical movement of the gunner’s eye while remaining fixed on the target. No centering is required. Lens covers protect the lenses when the sight is being transported or stored. The lens covers should always be kept closed when the sight is not in use. The adjustment caps and battery cap have O-rings that keep out moisture. Before immersing the sight in water or using it in rain, verify that the caps are snug by hand tightening them.

Zero procedures are as follows:

- Elevation adjustment screw is located on top of sight.  Windage adjustment screw is located on right side of sight.

- The M30 Boresight may be used to transfer zero to weapon/sight combinations identically configured to a master weapon.  The offset of M68 is the same as iron sights for M16 and M4 weapons.

- Adjustment is centered at the factory.  To provide maximum adjustment, do not adjust screws until sight is mounted.

- Sight has a circular sized adjustment area with a diameter of 3.0 in at 100 yards.

- In order to use iron sights for initial zeroing of M68 sight, zero weapon using established procedures in TM 9-1005-319-10.  On M4/M4A1 and M16A4, re-confirm zero if M68 sight is moved to a different slot on the rail.  If not using iron sights for initial zeroing, go directly to step 8.

- Open front and rear lens covers.

- Turn rotary switch clockwise until red dot intensity contrasts suitably with target background.

- Look through sight to get a rough estimate of zeroing adjustment required.  When looking through iron sights, red dot should appear on top of front post.

- If adjustment is required, remove adjustment screw caps from adjustment screws by turning counterclockwise.

- Insert adjustment tool (coin, screwdriver, and knife) in adjustment screw slot.  Turn adjustment screw as follows:

- To move the point of impact to the right, turn windage adjustment screw counterclockwise.

- To move the point of impact to the left, turn windage adjustment screw clockwise.

- To move point of impact up, turn elevation adjustment screw counterclockwise.

- To move the point of impact down, turn elevation adjustment screw clockwise.

- Repeat steps 4 and 6 until sight is roughly zeroed.

- Confirm zeroing by firing at least three shots at a zeroing target.  Check impact points on zeroing target to confirm accuracy.

Note

After initial firing, check to ensure that mount and sight (M16A2) or sight (M4/M4A1/M16A4) are secure.  On M16A2, hand tighten mounting bolt on mount then hand tighten torque knob on sight until it snaps twice.  On M4/M4A1/M16A4, hand tighten torque knob on sight until it clicks twice.

- If zeroing is accurate, fire three more shots to confirm.  If zeroing is not accurate, repeat steps 6 and 8 until zeroing is complete.

- Turn rotary switch to OFF position (counterclockwise).

- Close front and rear lens covers.

Light Adjustment:

- To make light adjustments, turn rotary switch clockwise. The first two positions are low intensity for night vision operations. The third position is the lowest daytime settings. The last position is the extra high intensity setting.

- Close lens cover and turn rotary switch counter-clockwise to OFF position when the sight is not

being used.

Sighting:  Place red dot on target. Red dot does not have to be centered in sight.

NOTE

Duracell lithium-manganese batteries are the "preferred" battery. Eveready 2L76, Kodak K58L, Varta CR 1/3N, and Maxell Gold 2L76 are suitable replacements.  Least preferred non-lithium alternatives: 2 each energizer A76 batteries in series or 2 each energizer 357 batteries in series.

The M68 Close Combat Optic does not require a target offset.  Zero procedures are as follows:

## M145 Machine Gun Optic

Batteries OE890(x1)

MGO Operating Instructions

(TM 9-1240-415-13&P) 28 Feb 00

General Functional Description

The MGO is a fixed 3.4 power, 28mm optical sight that has been designated to engage targets accurately out to 1200m range.  The MGO weights 24 oz and is extremely rugged for field conditions.  It has an 8.2mm diameter exit pulpit, which provides excellent vision in low light levels, i.e. dawn and dusk, and also allows for rapid target acquisition.  The MGO is designed to fit to the Picatinny rail.  It has an eye relief of approximately 3 in. (70mm).  Eye relief is the distance between the eye and the sight’s rear eyepiece lens.  The reticle pattern has a built-in trajectory companion from 300m to 1200m range and can be illuminated.

Elevation Adjustment Dial

Used for zeroing the telescope to the weapon. The dial can only be rotated

when the silver lock (1) is moved to the UP position. Turning the elevation adjustment dial (2) counterclockwise (in the direction of the arrow) one click moves the point of impact up 2.5mm at 10 meters.

Turning the elevation adjustment dial (2) clockwise (opposite direction to the arrow) one click moves the point of impact down 2.5mm at 10 meters. Ensure that the silver lock (1) is moved down to prevent any further movement of the elevation adjustment dial.

Windage Adjustment Dial

Used when zeroing weapon. Turning windage adjustment dial (3) clockwise one click moves the point of impact left 2.5mm at 10 meters. Turning windage adjustment dial (3) counterclockwise one click moves the point of impact right 2.5mm at 10 meters.

### M145, MGO Zero Procedures

Mechanical Zero

- Adjust the Straight Telescope so that the weapon’s barrel and optical sighting axis are in approximate alignment.  The sighting axis will be approximately 2-3 inches above the machine gun barrel and therefore the strike of the bullet at 10m range will also be approximately 2-3 inches low without further zeroing adjustment.

- To bring the strike of the bullet up to meet the line of sight through the M145, lift the silver lock and rotate the elevation adjustment dial clockwise (to the left) approximately one full turn.

- Adjust the windage adjustment dial to center markings on the front of the telescope.

NOTE:

Each click of the zeroing adjustments makes a 2.5 mm movement of the point of impact at 10m.

4.	Make final adjustments as follows:

- To move the point of impact to the right, turn windage adjustment screw counterclockwise.

- To move the point of impact to the left turn the windage adjustment screw clockwise.

- To move point of impact up, turn elevation adjustment screw counterclockwise.

- To move point of impact down, turn elevation adjustment screw clockwise.

10m Range Zeroing

In the zeroing process, groups of three single shot rounds are fired at a target.  After each three rounds, the center of the group has to be determined.

- Look through the telescope and align the reticle’s 800m mark on the center base of the aiming points on the basic machine gun marksmanship target.

- Fire three single rounds loaded individually without making any sight adjustments.

- The three shot group should be within a 4 cm circle to establish the center of the shot group in relation to the center base of the aiming paster.

- Measure the amount of movement required left or right (windage) and either up or down (elevation) to move the three shot group onto the center of the aiming paster.

- Windage correction: upon completion, return to the firing line to make corrections to the weapon and re-fire a three shot group to confirm zero.

Repeat the above steps 1-5 until the strike of the round is coincident with the center of the target.  Close the silver lock down to prevent any further movement of the elevation zeroing adjustment dial.

The M145 Straight Telescope is now 10m zeroed.

500m Range Zeroing

This procedure follows zeroing at 10 meters, as previously described.  Zeroing at 10 meters will provide an M145 weapon zero, which will require re-adjustment at 500m range.

- Look through the telescope and align the reticle’s 500m mark on the center of mass of the double “E” silhouette target.

- A)    M240B weapon = Fire a 6 to 9 round burst.

- M249 weapon = Fire a 5 to 7 round burst.

- Determine strike of the round through the telescope or inspect the target to determine center of shot group.

- Determine direction of impact movement required (up or down, left or right).

- Estimate or measure the amount of movement required to move the strike of the round to the center of the target (at 500 meters; five inches equals one click of adjustment in both windage and elevations).

Repeat the above steps 1-5 until the strike of the round is coincident with the center of the target.  Close the silver lock down to prevent any further movement of the elevation zeroing adjustment dial.

The M145 Straight Telescope is now zeroed and ready for operational shooting.

## MILES – Multiple Integrated Laser Engagement System

MILES 2000 Transmitter positioned on an M16A2 Rifle.

(Consult your local TASC for detailed mounting instructions and supporting offset target data)

MILES 2000 Transmitter positioned on an M4 Carbine, with M203 attached.

(Consult your local TASC for detailed mounting instructions and supporting offset target data)

MILES 2000 Transmitter positioned on an M249 SAW/LMG.

(Consult your local TASC for detailed mounting instructions and supporting offset target data)

MILES 2000 Transmitter positioned on an M240B Medium Machine Gun.

(Consult your local TASC for detailed mounting instructions and supporting offset target data)

# Annex C—Modular Weapon System Reference Data

## M4 Carbine Version

## M16 Version Modular Weapon System

## M203 Components-Modular Weapon System

# Annex D—Battery Quick Reference Guide

| Accessory | Type Battery |
| --- | --- |
|  | AA 1.5Vdc Lithium L91 | AA Alkaline BA-3058/U | AA 1.5Vdc Non Specific | BA-5567/U | BA-5847 or BB-2847/U | BA-5123/U | OE890 Lithium-maganese dioxide |
| AN/PAQ-4B/C |  | 2* |  |  |  |  |  |
| AN/PEQ-2A |  | 2 |  |  |  |  |  |
| AN/PVS-4 |  | 2** |  | 1** |  |  |  |
| AN/TVS-5 |  | 2 |  |  |  |  |  |
| M68-CCO |  |  |  |  |  |  | 1 |
| M 145 MGO |  |  |  |  |  |  | 1 |
| MILES |  |  |  |  |  |  |  |
| AN/PVS-14 | 2*** |  | 2*** |  |  |  |  |
| AN/PAS-13 |  |  |  |  | 1 |  |  |
| AN/PVS-10 | 2**** | 2**** |  |  |  |  |  |
| AN/PSX-1, (CIDDS) |  |  |  |  |  | 1 |  |

*  - Use non-re-chargeable batteries

** - Use either one BA-5567/U or two BA-3085/Us.

*** - Use either two AA 1.5Vdc Lithium or two non-specific AA batteries.  Do not mix types.  DO NOT use two 3.0Vdc batteries as this may result in injury or damage to the equipment.

**** - Use either two AA Lithium or two BA 3058/Us.  Do not mix types.

# Annex E-Machine Gun/Mount Cross Reference

# Annex F—Infantry Platoon Equipment/Organization Guide

## Airborne/Air Assault Infantry Platoon

| Weapon/ Device | Plt Ldr | Plt Sgt | RTO | SL | TL | AR | Gren | R | MG | AMG | AA Spec | Ammo |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| M9 |  |  |  |  |  |  |  |  | X |  |  |  |
| M16A2 |  |  |  |  |  |  |  |  |  |  |  |  |
| M16A4 |  |  |  |  |  |  |  |  |  |  |  |  |
| M4 | X | X | X | X | X |  | X | X |  | X | X | X |
| M203 |  |  |  |  |  |  |  |  |  |  |  |  |
| M203A1 |  |  |  |  |  |  | X |  |  |  |  |  |
| M240B |  |  |  |  |  |  |  |  | X |  |  |  |
| M249 |  |  |  |  |  | X |  |  |  |  |  |  |
| AN/PAQ-4B/C |  |  |  |  | X |  | X | X |  | X | X | X |
| AN/PAS-13 | X-H |  |  | X-H |  | X-M |  | X-L | X-M |  |  |  |
| AN/PEQ-2A | X | X |  | X |  | X |  |  | X |  |  |  |
| AN/PVS-14 | X |  |  | X |  | X |  | X | X |  | X | X |
| AN/PVS-7 |  | X | X |  | X |  | X |  |  | X |  |  |
| BUIS | X | X | X | X | X |  | X | X |  | X | X | X |
| M68 | X | X | X | X | X |  | X | X |  | X | X | X |
| M145 |  |  |  |  |  |  |  |  | X |  |  |  |

## Light Infantry Platoon

| Weapon/ Device | Plt Ldr | Plt Sgt | RTO | SL | TL | AR | Gren | R | MG | AMG | AA Spec | Ammo |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| M9 |  |  |  |  |  |  |  |  | X |  |  |  |
| M16A2 |  |  |  |  |  |  |  |  |  |  |  |  |
| M16A4 |  |  |  |  |  |  |  |  |  |  |  |  |
| M4 | X | X | X | X | X |  | X | X |  | X |  |  |
| M203 |  |  |  |  |  |  |  |  |  |  |  |  |
| M203A1 |  |  |  |  |  |  | X |  |  |  |  |  |
| M240B |  |  |  |  |  |  |  |  | X |  |  |  |
| M249 |  |  |  |  |  | X |  |  |  |  |  |  |
| AN/PAQ-4B/C |  |  | X |  | X |  | X | X |  | X |  |  |
| AN/PAS-13 | X-H |  |  | X-H |  | X-M |  | X-L | X-M |  |  |  |
| AN/PEQ-2A | X | X |  | X |  | X |  |  | X |  |  |  |
| AN/PVS-14 | X |  |  | X |  | X |  | X | X |  |  |  |
| AN/PVS-7 |  | X | X |  | X |  | X |  |  | X |  |  |
| BUIS | X | X | X | X | X |  | X | X |  | X |  |  |
| M68 | X | X | X | X | X |  | X | X |  | X |  |  |
| M145 |  |  |  |  |  |  |  |  | X |  |  |  |

## Mechanized Infantry Platoon (Bradley)

| Weapon/ Device | Plt Ldr | Plt Sgt | RTO | SL | TL | AR | Gren | R | AA Spec | Brad Cdr | Brad Gun | Brad Dvr |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| M9 |  |  |  |  |  |  |  |  |  |  |  |  |
| M16A2 |  |  |  |  |  |  |  |  |  |  |  |  |
| M16A4 |  |  |  | X | X |  | X | X | X | X | X | X |
| M4 | X | X | X |  |  |  |  |  |  |  |  |  |
| M203 |  |  |  |  | X |  | X |  |  |  |  |  |
| M203A1 |  |  |  |  |  |  |  |  |  |  |  |  |
| M240B |  |  |  |  |  |  |  |  |  |  |  |  |
| M249 |  |  |  |  |  | X |  |  |  |  |  |  |
| AN/PAQ-4B/C |  |  | X |  | X |  | X | X |  |  |  |  |
| AN/PAS-13 | X-H |  |  | X-H |  | X-M |  | X-L |  |  |  |  |
| AN/PEQ-2A | X | X |  | X |  | X |  |  |  |  |  |  |
| AN/PVS-14 | X |  |  | X |  | X |  | X |  |  |  |  |
| AN/PVS-7 |  | X | X |  | X |  | X |  | X | X |  | X |
| BUIS | X | X | X | X | X |  | X | X | X | X | X | X |
| M68 | X | X | X | X | X |  | X | X | X | X | X | X |
| M145 |  |  |  |  |  |  |  |  |  |  |  |  |

## Force XXI (3x9) Mechanized Infantry Platoon

| Weapon/ Device | Plt Ldr | Plt Sgt | RTO | SL | TL | AR | Gren | R | AA Spec | Brad Cdr | Brad Gun | Brad Dvr |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| M9 |  |  |  |  |  |  |  |  |  |  |  |  |
| M16A2 |  |  |  |  |  |  |  |  |  |  |  |  |
| M16A4 |  |  |  | X | X |  | X | X |  | X | X | X |
| M4 | X | X | X |  |  |  |  |  |  |  |  |  |
| M203 |  |  |  |  | X |  | X |  |  |  |  |  |
| M203A1 |  |  |  |  |  |  |  |  |  |  |  |  |
| M240B |  |  |  |  |  |  |  |  |  |  |  |  |
| M249 |  |  |  |  |  | X |  |  |  |  |  |  |
| AN/PAQ-4B/C |  |  | X |  | X |  | X | X |  |  |  |  |
| AN/PAS-13 | X-H |  |  | X-H |  | X-M |  | X-L |  |  |  |  |
| AN/PEQ-2A | X | X |  | X |  | X |  |  |  |  |  |  |
| AN/PVS-14 | X |  |  | X |  | X |  | X |  |  |  |  |
| AN/PVS-7 |  | X | X |  | X |  | X |  |  | X |  | X |
| BUIS | X | X | X | X | X |  | X | X |  | X | X | X |
| M68 | X | X | X | X | X |  | X | X |  | X | X | X |
| M145 |  |  |  |  |  |  |  |  |  |  |  |  |

1.  Division XXI Infantry Platoon is organized into 3 squads of nine men each, a vehicle section and the headquarters section.

2.  Platoon Leader is replaced when dismounting by the BC HOP (Plt Master Gunner).

3.  Platoon Sergeant is the Bradley Commander for one of the BFVs.

4.  M240B and Javeling CLU are Platoon Organization Equipment and employed based on METT.

## IBCT Infantry Platoon

| Weapon/ Device | Plt Ldr | Plt Sgt | RTO | SL | TL | AR | Gren | R | IAV Cdr | Driver | AA Spec | Ammo |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| M9 |  |  |  |  |  |  |  |  |  |  |  |  |
| M16A2 |  |  |  |  |  |  |  |  |  |  |  |  |
| M16A4 |  |  |  |  |  |  |  |  |  |  |  |  |
| M4 | X | X | X | X | X |  | X | X | X | X |  |  |
| M203 |  |  |  |  |  |  |  |  |  |  |  |  |
| M203A1 |  |  |  |  |  |  | X |  |  |  |  |  |
| M240B |  |  |  |  |  |  |  |  |  |  |  |  |
| M249 |  |  |  |  |  | X |  |  |  |  |  |  |
| AN/PAQ-4B/C |  |  | X |  |  |  | X | X | X | X |  |  |
| AN/PAS-13 | X-H |  |  | X-H |  | X-M |  | X-L |  |  |  |  |
| AN/PEQ-2A | X | X |  | X | X | X |  |  |  |  |  |  |
| AN/PVS-14 | X | X | X | X |  | X |  | X | X |  |  |  |
| AN/PVS-7 |  |  |  |  | X |  | X |  |  | X |  |  |
| BUIS | X | X | X | X | X |  | X | X | X | X |  |  |
| M68 | X | X | X | X | X |  | X | X | X | X |  |  |
| M145 |  |  |  |  |  |  |  |  |  |  |  |  |

# Annex G—Borelight Dry Zero Procedures

Prepared By

US ARMY

Armament Research, Development and Engineering Center (ARDEC)

Small Caliber Weapon Systems Team   (AMSTA-AR-CCL-A)

And

Fire Control Development Team   (AMSTA-AR-FSF-R)

Picatinny Arsenal, New Jersey 07806

Borelight Dry Zero Procedure for M4 MWS

Use of Borelight

NOTE:     Completely familiarize yourself with the use and operation of the Borelight by reading the Borelight Operators Manual.  A Borelight manual is supplied with each borelight kit.

WARNING:  VISIBLE LASER RADIATION - To reduce the risk of injury AVOID DIRECT EXPOSURE TO THE BEAM - Use Ballistic Laser Eye Protection (BLEPS) when handling/operating the Borelight.

CAUTION:  Do not look at laser Borelight through the BLEPS.

Arms Room Borelight Dry Zero Procedure

1.     WARNING - Before inserting Borelight into weapon,  perform Preventative Maintenance Checks and Service (PMCS), clear weapon and visually inspect the chamber to insure that it is empty and no ammunition is in position to be chambered.  Additionally, inspect rifle bore and muzzle to assure there are no obstructions.  Clean if necessary.

2. Check/Inspect screw on top of rail, rail cross slot T-14,  to assure that it is tight

3.     Attach fire control device(s) to the weapon and assure device(s) are in their correct location -  left rail, right rail, and top rail. (Note: rails are labeled T - Top, R - Right and L - Left). Check to confirm that all device(s) are firmly attached.

4.     Stabilize the weapon.  This can be accomplished by placing the  weapon in a rifle box rest, Gun Vise, or rifle holding device (see FM 23-9, dated July 1989, figure C-6, page C-60).   If these items are not available, go to step 5. If available, go to step 6.

5.     Lay or position weapon on a solid-stable surface such as a heavy table. Choose a weapon position where the weapon is most stable. Ignore  weapon cant at this time.

(Note: Weapon can be stabilized by using a carpenter’s wood clamp set or EZ Hold/ Quick Grip clamps.  If these types of items are not available, apply moderate hand pressure on the weapon.)  An unobstructed line of sight of 10 meters is required. A 10-meter length of cord is included with the laser Borelight kit.  10 meters is measured from top rail cross-slot labeled “T-14”.

6.     WARNING:  DO NOT TURN ON THE LASER BORELIGHT AT THIS TIME. Wipe laser Borelight mandrel with a clean cloth and apply a light film of oil on the mandrel. Insert laser Borelight mandrel in weapon muzzle using a light steady force until the mandrel taper seats in the muzzle. CAUTION: Do not apply an excessive inward force to the laser Borelight once the tapered end of the mandrel has seated in the muzzle.

7.     ZEROING THE BORELIGHT: This procedure is for zeroing the Borelight to the weapon. This procedure requires a minimum of TWO people.  One person to stabilize weapon and rotate and adjust the Borelight and a second person at the target board to call out adjustments. WARNING:  Both individuals MUST wear Ballistic Laser Eye Protection (BLEPS).  CAUTION:  Do not look at laser through the BLEPS.

- DANGER:  DO NOT LOOK DIRECTLY INTO LASER BEAM  -  DO NOT LOOK INTO LASER THROUGH BINOCULARS OR TELESCOPES  OR BLEPS -  DO NOT POINT LASER AT MIRROR SURFACES  -  DO NOT SHINE LASER INTO OTHER INDIVIDUALS’ EYES.

- Select/Place the proper 10 meter dry-zeroing target at a 10-meter distance from the top rail screw - rail cross slot T-14.

- For zeroing the Borelight laser, the target board MUST be kept level.  Ignore weapon orientation at this time.

- Turn on the laser Borelight.  With the help of an assistant, hold a target at 10 meters and place the target board so that the laser dot strikes the center of the laser Borelight dot on the selected target board.

- Note: Rotate Borelight tool clockwise, rotating laser Borelight housing counter-clockwise may cause the Borelight to unscrew from mandrel.  Slowly rotate the Borelight while watching the dot made by the laser on the target area.  If the dot remains stationary the Borelight is aligned and boresighted to the weapon.  Go to step 8.

- If the laser dot rotates in a circular pattern, the Borelight windage or elevation or both MUST be adjusted using the following procedures.  This procedure can be done at the 10-meter distance or you can move the target in as close as 2 meters.

- Slowly rotate the Borelight one-half turn.  Note the new location of the laser dot .

- Adjust the Borelight windage and elevation until the laser dot moves one-half the space from its original location.

- Continue the procedure until the laser dot remains stationary when the Borelight is rotated.  If target board was moved closer to the Borelight, move target back to a distance of 10 meters and re-check boresight.  If boresight is correct the weapon is ready to be dry-zeroed.

8.	ZEROING THE WEAPON: (Note: Do Not Touch or Bump Borelight)  This procedure is for boresighting the weapon for 300 meter dry-zero.

DANGER: Do not stare at or shine visible laser beam into other individuals eyes.

Use this procedure for the 300 meter Back Up Iron Sight, M68 CCO Reflex Sight and the AN/PAS-13 Thermal Weapon Sight (TWS):

- Remove weapon from box rest, Gun Vise,  rifle holding device or flat stable surface.

- From the same 10 meter location place weapon over a sand bag, rucksack or bench rest type stand.

- Manually stabilize the weapon without cant and orient the selected target board in a level-vertical position.  (Note: Proper positioning of the target is CRITICAL for accurate  boresighting results).

- For specific weapon and sight combinations, follow the instructions on the target boards.

- Aim the weapon fire control device(s) at the proper figure on the chart and adjust WEAPON sighting device(s) windage and elevation controls until the laser Borelight is centered on its labeled spot.

- (Optional) Rotate the Borelight one half turn and again aim at the proper device(s) target. If properly boresighted, the laser Borelight spot should still be centered on its spot even after a half turn rotation. If not centered, repeat steps 7.

Use this procedure for the AN/PAQ-4 B/C and the AN/PEQ-2 InfraRed Aiming Lights (Note: Night Vision equipment is required):

- Lay weapon flat on a table, over sandbags, or rucksack and manually stabilize the weapon by applying moderate hand pressure down to center of weapon.

- Select proper 10-meter dry-zero target board.

- Orient target board to match orientation of weapon

(Note: Proper positioning of the target is CRITICAL for accurate  boresighting results).

- Adjust the target board until the laser Borelight is centered on its labeled spot.

- Adjust the windage and elevation controls on the IR Aiming Lights until they are centered on their labeled spot(s).

9.     Turn off the laser Borelight tool and REMOVE from weapon. Weapon is now dry zeroed for 300 meters.  300 meter dry-zero should be confirmed by live fire.

10.     Repeat steps 1 through 9 for each weapon to be boresighted.

Field Location Borelight Dry Zero Procedure

1.     WARNING - Before inserting Borelight into weapon perform Preventative Maintenance Checks and Service (PMCS), clear weapon and visually inspect the chamber to insure that it is empty and no ammunition is in position to be chambered.  Additionally, inspect rifle bore and muzzle to assure there are no obstructions.  Clean if necessary.

2.     Check/Inspect screw on top of rail, rail cross slot T-14,  to assure that it is tight.

3.     Attach fire control device(s) to the weapon and assure device(s) are in their correct location -  left rail, right rail, and top rail. (Note: rails are labeled T - Top, R - Right and L - Left). Check to confirm that all device(s) are firmly attached.

4.     Stabilize the weapon.  The recommended/preferred field method is to place/secure the weapon to a rifle holder similar to what is shown in FM 23-9, Figure C-7, and page C-7,  dated July 1989.    Other alternatives to stabilizing the weapon can be accomplished by placing the weapon over sand bags, rucksack, securing weapon to a sand bagged tripod,  placing the weapon over two fallen trees or ammunition cans and stabilizing with sand bags or rucksack  If the preferred method or the alternatives are not possible and if vehicles are available go to Step 5,  If not go to step 6.

5.     Lay or position weapon on a solid-stable surface such as the tailgate or hood of a vehicle or flat surfaces on tracked vehicles. Choose a weapon position where the weapon is most stable. Ignore  weapon cant at this time.  (Note: Weapon can be stabilized by using combinations of sandbags, rucksacks,  with ammunition cans or tie down straps from vehicles).  An unobstructed line of sight of 10 meters is required. A 10-meter length of cord is included with the laser Borelight kit.  10 meters is measured from top rail cross-slot labeled “T-14”.

6.     WARNING:  DO NOT TURN ON THE LASER BORELIGHT AT THIS TIME. Wipe laser Borelight mandrel with a clean cloth and apply a light film of oil on the mandrel. Insert laser Borelight mandrel in weapon muzzle using a light steady force until the mandrel taper seats in the muzzle. CAUTION: Do not apply an excessive inward force to the laser Borelight once the tapered end of the mandrel has seated in the muzzle

7.     ZEROING THE BORELIGHT: This procedure is for zeroing the Borelight to the weapon. This procedure requires a minimum of THREE people.  One person to stabilize weapon, a second  person to rotate and adjust the Borelight and the third person at the target board to call out adjustments. WARNING:  All individuals MUST wear Ballistic Laser Eye Protection (BLEPS).  CAUTION:  Do not look at laser through the BLEPS.

- DANGER:  DO NOT LOOK DIRECTLY INTO LASER BEAM  -  DO NOT LOOK INTO LASER THROUGH BINOCULARS OR TELESCOPES  OR BLEPS -  DO NOT POINT LASER AT MIRROR SURFACES  -  DO NOT SHINE LASER INTO OTHER INDIVIDUALS’ EYES.

- Select/Place the proper 10 meter dry-zeroing target at a 10 meter distance from the top rail screw - rail cross slot T-14.

- For zeroing the Borelight laser, the target board MUST be kept  level.  Ignore weapon orientation at this time.

- Turn on the laser Borelight.  With the help of an assistant, hold a target at 10 meters and place the target board so that the laser dot strikes the center of the laser Borelight dot on the selected target board.

- Note: Rotate Borelight tool clockwise, rotating laser Borelight housing counter-clockwise may cause the Borelight to unscrew from mandrel.  Slowly rotate the Borelight while watching the dot made by the laser on the target area.  If the dot remains stationary the Borelight is aligned and boresighted to the weapon.  Go to step 8.

- If the laser dot rotates in a circular pattern, the Borelight windage or elevation or both MUST be adjusted using the following procedures.  This procedure can be done at the 10 meter distance or you can move the target in as close as 2 meters.

“Slowly rotate the Borelight one-half turn.  Note the new location of the laser dot.”

“adjust the Borelight windage and elevation until the laser dot moves one-half the space from its original location.”

“Continue the procedure until the laser dot remains stationary when the Borelight is rotated.  If target board was moved closer to the Borelight, move target back to a distance of 10 meters and re-check boresight.  If boresight is correct the weapon is ready to be dry-zeroed. “

8.     ZEROING THE WEAPON: (Note: Do Not Touch or Bump Borelight)  This procedure is for boresighting the weapon for 300 meter dry-zero.

DANGER: Do not stare at or shine visible laser beam into other individuals eyes.

Use this procedure for the 300 meter Back Up Iron Sight, M68 CCO Reflex Sight and the AN/PAS-13 Thermal Weapon Sight (TWS):

- If using the recommended rifle holder, maintain weapon in its place.  If using a flat stable surface,  place weapon over a sand bag, rucksack or other recommended alternatives, and stabilize the weapon so that it has no cant.

- Maintaining 10 meter distance from the top rail screw ( rail cross slot T-14) to the selected target board, orient the selected target board in a level-vertical position.  (Note: Proper positioning of the target is CRITICAL for accurate  boresighting results)

- For specific weapon and sight combinations, follow the instructions on the target boards.

- Aim the weapon fire control device(s) at the proper figure on the chart and adjust WEAPON sighting device(s) windage and elevation controls until the laser Borelight is centered on its labeled spot.

- (Optional) Rotate the Borelight one half turn and again aim at the proper device(s) target. If properly boresighted, the laser Borelight spot should still be centered on its spot even after a half turn rotation. If not centered, repeat steps 7.

Use this procedure for the AN/PAQ-4 B/C and the AN/PEQ-2 Infra-Red Aiming Lights (Note: Night Vision equipment is required):

- Place weapon on flat surface, over sand bags, or rucksack and manually stabilize the weapon by applying moderate hand pressure down to center of weapon.

- Select proper 10-meter dry-zero target board.

- Orient target board to match orientation of weapon  (Note: Proper positioning of the target is CRITICAL for accurate boresighting results).

- Adjust the target board until the laser Borelight is centered on its labeled spot.

- Adjust the windage and elevation controls on the IR Aiming Lights until they are centered on their labeled spot(s).

9.     Turn off the laser Borelight tool and REMOVE from weapon. Weapon is now dry zeroed for 300 meters.  300 meter dry-zero should be confirmed by live fire.

10.     Repeat steps 1 through 9 for each weapon to be boresighted.

Borelight Dry Zero Procedure for M240B MG and M249 SAW with AN/PEQ-2

MachineGun (MG) Borelight Dry Zero Procedure

1.     WARNING - Before inserting Borelight into weapon, clear Machine Gun (MG),  perform Preventative Maintenance Checks and Service (PMCS), and visually inspect the chamber to insure that it is empty and no ammunition is in position to be chambered.  Additionally, inspect bore and muzzle to assure there are no obstructions.  Clean if necessary.

2.     Attach/Mount AN/PEQ-2 IR Pointer to the MG and assure device is tightly secure.  On the M240B, the AN/PEQ-2 is attached to the rail on top of the feed cover.  On the M249 SAW, the AN/PEQ-2 is attached to the rail on top of the M249 TWS bracket.

3.     Stabilize the MG. This can be accomplished by placing the MG  on a tripod. If no tripod is available stabilize MG with bipod open and with sand bags or rucksacks.

4.    An unobstructed line of sight of 10 meters is required. A 10-meter length of cord is included with the laser Borelight kit.  10 meters is measured from the barrel carrying handle.

5.     WARNING:  DO NOT TURN ON THE LASER BORELIGHT AT THIS TIME. Wipe laser Borelight mandrel with a clean cloth and apply a light film of oil on the mandrel. Insert laser Borelight mandrel in MG muzzle using a light steady force until the mandrel taper seats in the muzzle. CAUTION: Do not apply an excessive inward force to the laser Borelight once the tapered end of the mandrel has seated in the muzzle.

6.     ZEROING THE BORELIGHT: This procedure is for zeroing the Borelight to the MG. This procedure requires a minimum of Three  people.  One person to stabilize weapon by applying firm pressure downward with two hands on the MG barrel, a second person to rotate and adjust the Borelight and a third person at the target board to call out adjustments. WARNING:  All individuals MUST wear Ballistic Laser Eye Protection (BLEPS).  CAUTION:  Do not look at laser through the BLEPS.

DANGER:  DO NOT LOOK DIRECTLY INTO LASER BEAM  -  DO NOT LOOK INTO LASER THROUGH BINOCULARS OR TELESCOPES  OR BLEPS -  DO NOT POINT LASER AT MIRROR SURFACES  -  DO NOT SHINE LASER INTO OTHER INDIVIDUALS’ EYES.

- Select/Place the proper 10 meter dry-zeroing target at a 10 meter distance from the carrying handle of the MG barrel.

- For zeroing the Borelight laser, the target board MUST be kept level.  Ignore MG orientation at this time.

- Turn on the laser Borelight.  With the help of an assistant, hold a target at 10 meters and place the target board so that the laser dot strikes the center of the laser Borelight dot on the selected target board.

- Note: Rotate Borelight tool clockwise, rotating laser Borelight housing counter-clockwise may cause the Borelight to unscrew from mandrel.  Slowly rotate the Borelight while watching the dot made by the laser on the target area.  If the dot remains stationary the Borelight is aligned and boresighted to the weapon.  Go to step 7.

- If the laser dot rotates in a circular pattern, the Borelight windage or elevation or both MUST be adjusted using the following procedures.  This procedure can be done at the 10 meter distance or you can move the target in as close as 2 meters.

-	Slowly rotate the Borelight one-half turn.  Note the new location of the laser dot .

-	Adjust the Borelight windage and elevation until the laser dot moves one-half the space from its original location.

-	Continue the procedure until the laser dot remains stationary when the Borelight is rotated.  If target board was moved closer to the Borelight, move target back to a distance of 10 meters and re-check boresight.  If boresight is correct, the weapon is ready to be dry-zeroed.

7.  ZEROING THE MACHINEGUN: (Note: Do Not Touch or Bump Borelight)  This procedure is for boresighting the weapon for 300 meter dry-zero.

DANGER: Do not stare at or shine visible laser beam into other individuals eyes.

Use this procedure for the AN/PEQ-2 InfraRed Aiming/Illumination Lights (Note: Night Vision equipment is required).

- Zeroing from Bipod: Remove MG from Tripod or from sandbags or rucksacks.  From the same 10 meter location, shoulder the MG in a prone firing position with bipod legs contacting the ground, manually stabilize the weapon without cant and orient the selected target board in a level-vertical position.  (Note: Proper positioning of the target is CRITICAL for accurate  boresighting results).

- Zeroing from Tripod: From the same 10 meter location, stabilize the weapon without cant and orient the selected target board in a level-vertical position.  (Note: Proper positioning of the target is CRITICAL for accurate  boresighting results).

- NOTE:  If MG is zeroed from tripod and fired off the bipod, the center of the cone of fire will be “approximately” 18 inches high (+2 MILs) at 300 meters from the center of  the target.  If the MG is zeroed from the bipod and fired from the tripod, the center of the cone of fire will be “approximately” 18 inches low (-2 MILs) at 300 meters from the center of the target.

- Read and follow the instructions on the target boards.

- Aim/Place the borelight at the proper figure on the chart and adjust the windage and elevation controls on the AN/PEQ-2  IR Aiming Lights until they are centered on their labeled spot(s).

- (Optional) Rotate the Borelight one half turn and again aim at the proper device(s) target. If properly boresighted, the laser Borelight spot  should still be centered on its spot even after a half turn rotation. If not centered, repeat steps 6.

8.     Turn off the laser Borelight tool and REMOVE from MG.  MG is now dry zeroed for 300 meters.  300 meter dry-zero should be confirmed by live fire.

# Annex H—Target Offset Summary

| Weapon | Accessory | Mount | Page No. | Range Zeroed To | 25m M16A2/A4 Tgt Zero Offset Squares | 10m Boresight Tgt Offset cm |
| --- | --- | --- | --- | --- | --- | --- |
| M16A2 | Iron sight | NA | 2 | 300m | 0.0 0.0 | 0.0 4.2U |
| M16A2 | AN/PAQ-4B/C | M4/M16A2 Bracket Assembly on top of hand guards | 4 | 300m | 1.5R 0.5U | 1.9L 2.5U |
| M16A2 | AN/PAS-13, TWS (Medium/Heavy) | M16A1/A2 Bracket Assembly mounted on carrying handle | 8 | 300m | 0.0 7.3D | 0.0 11.0U |
| M16A2 | AN/PEQ-2A | M4/M16A2 Bracket Assembly on top of hand guards | 11 | 300m | 1.5L 0.5U | Aiming 1.8R / 2.4U Flood 2.2L / 2.4U |
| M16A2 | AN/PVS-4 | AN/PVS-4 Mounting Knob Assembly on M16A2 carrying handle | 14 | 300m | 0.0 7.0D | 0.0 9.4U |
| M16A2 | M68, CCO | M68 M16A2 Mount, Sight-mounted on carrying handle | 17 | 300m | N/A | 0.0 5.2U |
| M16/M203 | AN/PAQ-4B/C | AN/PAQ-4B/C bracket adapter and AN/PVS-4 mounting knob assembly on carrying handle | 21 | 300m | 1.9R 2.6D | 1.9L 8.6U |
| M16/M203 | AN/PVS-4 | AN/PVS-4’s M203 mounting bracket assembly attached to the carrying handle | 24 | 300m | 4.2R 9.8D | TBD |
| M4/M4A1 | Back Up Iron Sight | Mounted on upper receiver | 27 | 300m | 0.0 | 0.0 4.0U |
| M4/M4A1 | AN/PAQ-4B/C | M4/M16A2 Bracket Assembly on top of hand guards | 29 | 300m | 1.5R 2.5U | 1.9L 2.5U |
| M4/M4A1 | AN/PAS-13, TWS (Medium/Heavy) | With M4 (7/8”) spacer on upper receiver rail | 32 | 300m | 0.0 5.7D | 0.0 9.4U |
| M4/M4A1 | AN/PEQ-2A | M4/M16A2 Bracket Assembly on top of hand guards | 35 | 300m | 1.0L 0.3U | Aiming 1.8R / 2.4U Flood 2.2L / 2.4U |
| M4/M4A1 | AN/PVS-4 | AN/PVS-4 spacer and rail grabber/mount on upper receiver rail | 39 | 300m | 0.0 3.4D | 0.0 7.6U |
| M4/M4A1 | M68, CCO | Mounted on upper receiver rail using CCO rail grabber with half-moon spacer | 42 | 300m | N/A | 0.0 5.6U |
| M4/M203 | Back Up Iron Sight | Mounted on upper receiver | 45 | 300m | 0.0 | 0.0 6.0U |
| M4/M203 | AN/PAQ-4B/C | AN/PAQ-4B/C bracket adapter and AN/PVS-4 mounting knob assembly on carrying handle | 47 | 300m | 1.3R 1.9D | 1.9L 8.6U |
| M4/M203 | AN/PVS-4 | AN/PVS-4 spacer and rail grabber/mount on upper receiver rail | 50 | 300m | 0.0 3.4D | 0.0 9.6U |
| M4 MWS | Back Up Iron Sight | Mounted on upper receiver | 53 | 300m | 0.0 | 0.0 4.0U |
| M4 MWS | AN/PAQ-4B/C | Mounting Bracket/Picatinny Rail Grabber mounted on left side rail | 55 | 300m | 6.5R 8.1U | 6.0L 4.3D |
| M4 MWS | AN/PAQ-4B/C | Mounting Bracket/Picatinny Rail Grabber mounted on top rail. | 57 | 300m | 1.7R 0.7D | 1.8L 3.9U |
| M4 MWS | AN/PAQ-4B/C | Mounting Bracket/Picatinny Rail Grabber mounted on right rail. | 59 | 300m | 5.9L 3.5U | 6.0R 0.9D |
| M4 MWS | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on Left Rail | 63 | 300m | 4.2R 8.6U | 4.3L 4.2D |
| M4 MWS | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on Top Rail | 65 | 300m | 1.7R 1.8U | 1.8L 2.2U |
| M4 MWS | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on Right Rail | 67 | 300m | 4.3L 3.4U | 4.3R 0.7D |
| M4 MWS | AN/PAS-13, TWS (Medium/Heavy) | With M4 (7/8”) spacer on upper receiver rail | 70 | 300m | 0.0 5.7D | 0.0 9.4U |
| M4 MWS | AN/PEQ-2A | Mounting Bracket/Picatinny Rail Grabber mounted on left side rail | 74 | 300m | 4.8R 0.3U | Aiming 6.2L / 0.6D Flood 6.2L / 4.6D |
| M4 MWS | AN/PEQ-2A | Mounting Bracket/Picatinny Rail Grabber mounted on top rail | 76 | 300m | 2.0L 0.8D | Aiming 2.0R / 4.1U Flood 2.0L / 4.1U |
| M4 MWS | AN/PEQ-2A | Mounting Bracket/Picatinny Rail Grabber mounted on right side rail | 78 | 300m | 6.1L 8.6U | Aiming 6.3R / 4.4D Flood 6.3R / 0.4D |
| M4 MWS | AN/PEQ-2A | Insight Low Profile Rail Grabber on Left Rail | 81 | 300m | 5.5R 4.0U | Aiming 4.5L / 1D Flood 4.5L / 5D |
| M4 MWS | AN/PEQ-2A | Insight Low Profile Rail Grabber on top rail | 83 | 300m | 2.0L 1.2U | Aiming 2.0R / 2.3U Flood 2.0L / 2.3U |
| M4 MWS | AN/PEQ-2A | Insight Low Profile Rail Grabber on Right Rail | 85 | 300m | 4.4L 8.5U | Aiming 4.5R / 4.4D Flood 4.5R / 0.4D |
| M4 MWS | AN/PVS-4 | AN/PVS-4 spacer and rail grabber/mount on upper receiver rail | 90 | 300m | 0.0 3.4D | 0.0 7.6U |
| M4 MWS | M68, CCO | Mounted on upper receiver rail using CCO rail grabber with half-moon spacer | 93 | 300m | N/A | 0.0 5.6U |
| M4/M203 MWS | Back Up Iron Sight | Mounted on upper receiver | 96 | 300m | 0.0 | 0.0 6.0U |
| M4/M203 MWS | AN/PAQ-4B/C | Mounting Bracket/Picatinny Rail Grabber mounted on left side rail | 104 | 300m | 4.9R 6.1U | 6.0L 4.0D |
| M4/M203 MWS | AN/PAQ-4B/C | Mounting Bracket/Picatinny Rail Grabber mounted on top rail. | 106 | 300m | 1.7R 0.5D | 1.8L 4.6U |
| M4/M203 MWS | AN/PAQ-4B/C | Mounting Bracket/Picatinny Rail Grabber mounted on right rail. | 108 | 300m | 5.9L 3.5U | 6.0R 0.0 |
| M4/M203 MWS | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on Left Rail | 111 | 300m | 4.2R 8.5U | 4.3L 3.5D |
| M4/M203 MWS | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on Top Rail | 113 | 300m | 1.7R 1.7U | 1.8L 2.9U |
| M4/M203 MWS | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on Right Rail | 115 | 300m | 4.3L 3.3U | 4.4R 0.0 |
| M4/M203 MWS | AN/PVS-4 | AN/PVS-4 spacer and rail grabber/mount on upper receiver rail | 118 | 300m | 0.0 3.4D | 0.0 9.6U |
| M16A4 MWS | Back Up Iron Sight | Mounted on upper receiver | 121 | 300m | 0.0 | 0.0 4.0U |
| M16A4 MWS | AN/PAQ-4B/C | Mounting Bracket/Picatinny Rail Grabber mounted on left side rail | 123 | 300m | 6.5R 8.0U | 6.0L 4.3D |
| M16A4 MWS | AN/PAQ-4B/C | Mounting Bracket/Picatinny Rail Grabber mounted on top rail. | 125 | 300m | 1.7R 0.7D | 1.8L 3.9U |
| M16A4 MWS | AN/PAQ-4B/C | Mounting Bracket/Picatinny Rail Grabber mounted on right rail. | 127 | 300m | 5.9L 3.5U | 6.0R 0.9D |
| M16A4 MWS | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on Left Rail | 131 | 300m | 4.2R 8.6U | 4.3L 4.2D |
| M16A4 MWS | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on Top Rail | 133 | 300m | 1.7R 1.8U | 1.8L 2.2U |
| M16A4 MWS | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on Right Rail | 135 | 300m | 4.3L 3.4U | 4.3R 0.7D |
| M16A4 MWS | AN/PAS-13, TWS (Medium/Heavy) | With M4 (7/8”) spacer on upper receiver rail | 138 | 300m | 0.0 5.5D | 0.0 9.4U |
| M16A4 MWS | AN/PEQ-2A | Mounting Bracket/Picatinny Rail Grabber mounted on left side rail | 142 | 300m | 6.0R 2.0U | Aiming 6.2L / 0.6D Flood 6.2L / 4.6D |
| M16A4 MWS | AN/PEQ-2A | Mounting Bracket/Picatinny Rail Grabber mounted on top rail | 144 | 300m | 2.0L 0.8D | Aiming 2.0R / 4.1U Flood 2.0L / 4.1U |
| M16A4 MWS | AN/PEQ-2A | Mounting Bracket/Picatinny Rail Grabber mounted on right side rail | 146 | 300m | 6.1L 8.6U | Aiming 6.3R / 4.4D Flood 6.3R / 0.4D |
| M16A4 MWS | AN/PEQ-2A | Insight Low Profile Rail Grabber on Left Rail | 149 | 300m | 4.5R 4.1U | Aiming 5.0L / 1.0D Flood 5.0L / 5.0D |
| M16A4 MWS | AN/PEQ-2A | Insight Low Profile Rail Grabber on top rail | 151 | 300m | 2.0L 1.2U | Aiming 2R / 2.3U Flood 2L / 2.3U |
| M16A4 MWS | AN/PEQ-2A | Insight Low Profile Rail Grabber on Right Rail | 153 | 300m | 4.4L 8.5U | Aiming 4.5R / 4.4D Flood 4.5R / 0.4D |
| M16A4 MWS | AN/PVS-4 | AN/PVS-4 spacer and grabber/mount on upper receiver rail | 157 | 300m | 0.0 4.6D | 0.0 7.6U |
| M16A4 MWS | M68, CCO | Mounted on upper receiver rail using CCO rail grabber with half-moon spacer | 160 | 300m | N/A | 0.0 5.6U |
| M16A4/M203 MWS | Back Up Iron Sight | Mounted on upper receiver | 163 | 300m | 0.0 | 0.0 6.0U |
| M16A4/M203 MWS | AN/PAQ-4B/C | Left rail with Mounting Bracket/Picatinny Rail Grabber on left rail | 173 | 300m | 4.9R 6.1U | 6.0L 4.0D |
| M16A4/M203 MWS | AN/PAQ-4B/C | Mounting Bracket/Picatinny Rail Grabber mounted on top rail. | 175 | 300m | 1.7R 0.5D | 1.8L 4.6U |
| M16A4/M203 MWS | AN/PAQ-4B/C | Mounting Bracket/Picatinny Rail Grabber mounted on right rail. | 177 | 300m | 5.9L 3.5U | 6R 0.0 |
| M16A4/M203 MWS | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on Left Rail | 180 | 300m | 4.2R 8.5U | 4.3L 3.5D |
| M16A4/M203 MWS | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on Top Rail | 182 | 300m | 1.7R 1.7U | 1.8L 2.9U |
| M16A4/M203 MWS | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on Right Rail | 184 | 300m | 4.3L 3.3U | 4.4R 0.0 |
| M16A4/M203 MWS | AN/PVS-4 | AN/PVS-4 spacer and grabber/mount on upper receiver rail | 187 | 300m | 0.0 3.4D | 0.0 9.6U |
| M24 Sniper Sys | AN/PVS-10 | Mtd on top of optical rail on the M24 | -- | N/A | N/A | N/A |
| M24 Sniper Sys | Day Optic Sight | Mtd on top of optical rail on the M24 | -- | N/A | N/A | N/A |
| M249 | Iron Sight | N/A | 196 | 400M | 0.0 5.1U | 0.0 1.7U |
| M249 | AN/PAQ-4B/C | Mounting Bracket/Picatinny Rail Grabber mounted on Feed Tray Cover Rail | 199 | 400m | 1.8R 0.0 | 1.8L 5.4U |
| M249 | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on Feed Tray Cover Rail | 202 | 400m | 1.8R 2.0U | 1.8L 4.7U |
| M249 | AN/PAQ-4B/C | AN/PVS4 - M249 Mounting Bracket with Plastic Bracket Adapter over feed tray cover | 205 | 400m | 2.5R 1.5D | 4.1L 6.1U |
| M249 | AN/PAQ-4B/C | Mounting Bracket/Picatinny Rail Grabber mounted on left forward rail. | 208 | 400m | 7.5R 14.0D | 7.6L 8.3D |
| M249 | AN/PAQ-4B/C | Mounting Bracket/Picatinny Rail Grabber mounted on right forward rail. | 210 | 400m | 7.6L 10.7U | 7.7R 4.0D |
| M249 | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on left forward rail | 213 | 400m | 5.9R 14.0D | 6.OL 8.3D |
| M249 | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on right forward rail | 215 | 400m | 5.8L 10.7U | 5.9R 4.0D |
| M249 | AN/PAS13, TWS (Medium) | Mounted on Feed Tray Cover Rail | 218 | 400m | 0.0 2.8D | 0.0 8.6U |
| M249 | AN/PEQ-2A | Mounting Bracket/Picatinny Rail Grabber mounted on Feed Tray Cover Rail | 221 | 400m | 2.0L 0.5D | Aiming 2.0R / 6.5U Flood 2.0L / 6.5U |
| M249 | AN/PEQ-2A | Insight Low Profile Rail Grabber on Feed Tray Cover Rail | 223 | 400m | 2.0L 1.3U | Aiming 2.0R / 4.8U Flood 2.0L / 4.8U |
| M249 | AN/PEQ-2A | AN/PVS-4 – M249 Mounting Bracket mounted with plastic spacer | 226 | 400m | 5.0R 4.0D | Aiming .5L / 6.5U Flood 4.5L / 6.5U |
| M249 | AN/PEQ-2A | Mounting Bracket/ Picatinny Rail Grabber mounted on left forward rail. | 229 | 400m | 7.5R 10.0D | Aiming 7.6L / 4.4D Flood 7.6L / 8.4D |
| M249 | AN/PEQ-2A | Mounting Bracket/Picatinny Rail Grabber mounted on right forward rail. | 231 | 400m | 7.7L 10.0U | Aiming 7.8R / 7.6D Flood 7.8R / 3.6D |
| M249 | AN/PEQ-2A | Insight Low Profile Rail Grabber on left forward rail | 234 | 400m | 5.9R 10.0D | Aiming 6.0L / 4.4D Flood 6.0L / 8.4D |
| M249 | AN/PEQ-2A | Insight Low Profile Rail Grabber on right forward rail | 236 | 400m | 6.0L 14.0U | Aiming 6.1R / 7.6D Flood 6.1R / 3.6D |
| M249 | AN/PVS-4 | AN/PVS-4 spacer and grabber/mount on the feed tray cover rail | 239 | 400M | 0.0 4.3D | 0.0 10.0U |
| M249 | AN/PVS-4 | AN/PVS-4 – M249 Mounting Bracket Assembly | 242 | 400M | 2.5R 4.9D | 2.3L 11.3U |
| M249 | MGO | Feed tray cover rail with MGO organic rail grabber | 245 | 400M | 0.0 2.0D | 0.0 7.9U |
| M60 | AN/PAQ-4B/C | M60-AN/PVS-4 feed tray cover bracket | 250 | 500m | 1.5R 8.0D | 4.0L 14.0U |
| M60 | AN/PAS-13, TWS (Medium) | M60 bracket assembly | 253 | 500m | 0.0 8.1D | 0.0 9.0U |
| M60 | AN/PEQ-2A | M60-AN/PVS-4 feed tray cover bracket | 257 | 500m | 1.5L 8.0D | Aiming 4.0R/14.0U Flood 0.0/14.0U |
| M60 | AN/PVS-4 | M60-AN/PVS-4 mounting bracket assembly | 261 | 500m | 0.0 13.0D | 0.5R 14.5U |
| M60 | M145, MGO | M60-TWS feed tray cover bracket | 264 | 500m | N/A | TBD |
| M240B | IRON SIGHTS | N/A | 267 | 500m | 0.0 9.2U | 0.0 2.5U |
| M240B | AN/PAQ-4B/C | Mounting Bracket/Picatinny Rail Grabber mounted on Feed Tray Cover Rail | 270 | 500m | 1.8R 2.2D | 1.5L 3.5U |
| M240B | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on Feed Tray Cover Rail | 272 | 500m | 1.8R 8.3U | 1.8L 0.8U |
| M240B | AN/PAQ-4B/C | Mounting Bracket/Picatinny Rail Grabber mounted on left forward rail. | 275 | 500M | 7.8R 17.7U | 7.9L 8.1D |
| M240B | AN/PAQ-4B/C | Mounting Bracket/Picatinny Rail Grabber mounted on right forward rail. | 277 | 500M | 7.8L 13.5U | 7.5R 4.4D |
| M240B | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on left forward rail | 280 | 500M | 6.2R 17.7U | 6.2L 8.1D |
| M240B | AN/PAQ-4B/C | Insight Low Profile Rail Grabber on right forward rail | 282 | 500M | 5.9L 13.5U | 6.0R 4.4D |
| M240B | AN/PAS13, TWS (Medium) | Mounted on feed tray cover rail | 286 | 500M | 0.0 2.3U | 0.0 8.0U |
| M240B | AN/PEQ-2A | Mounting Bracket/Picatinny Rail Grabber mounted on Feed Tray Cover Rail | 289 | 500M | 2.0R 1.5D | Aiming 1.7R / 3.7U Flood 2.3L / 3.7U |
| M240B | AN/PEQ-2A | Insight Low Profile Rail Grabber on Feed Tray Cover Rail | 291 | 500M | 1.7L 6.0U | Aiming 1.7R / 2.2U Flood 2.3L / 2.2U |
| M240B | AN/PEQ-2A | Mounting Bracket/Picatinny Rail Grabber mounted on left forward rail. | 294 | 500M | 7.8R 13.5U | Aiming 7.9L / 4.1D Flood 7.9L / 8.1D |
| M240B | AN/PEQ-2A | Mounting Bracket/Picatinny Rail Grabber mounted on right forward rail. | 296 | 500M | 7.8L 17.7U | Aiming 7.9R / 8.0D Flood 7.9R / 4.0D |
| M240B | AN/PEQ-2A | Insight Low Profile Rail Grabber on left forward rail | 299 | 500M | 6.2R 13.5U | Aiming 6.2L / 4.1D Flood 6.2L / 8.1D |
| M240B | AN/PEQ-2A | Insight Low Profile Rail Grabber on right forward rail | 301 | 500M | 6.1L 17.7U | Aiming 6.2R / 7.9D Flood 6.2R / 3.9D |
| M240B | AN/PVS-4 | AN/PVS-4 spacer and grabber/mount on the feed tray cover rail | 304 | 500M | 0.0 6.2D | 0.0 6.0U |
| M240B | M145 MGO | Feed tray cover rail with MGO organic rail grabber | 307 | 500m | N/A | 0.0 0.0 |
| M2 | Iron Sight | N/A | 310 | 500m | TBD | TBD |
| M2 | AN/PAS-13, TWS (Heavy) | M2-TWS bracket assembly | 314 | 500m | 0.0 12.8D | 0.0 16.3U |
| M2 | AN/PEQ-2A | M2—AN/TVS-5 mounting bracket assembly & plastic spacer | 317 | 500m | 1.5L 9.5D | Aiming 2.0R/9.2U Flood 2.0L/9.2U |
| M2 | AN/TVS-5 | M2--AN/TVS-5 mounting bracket assembly | 320 | 500m | 0.0 10.6D | 0.0 13.8U |
| Mk19 | Iron Sight | N/A | 323 | 500m | N/A | 2.4 R 33.9 D |
| Mk19 | AN/PAS-13, TWS (Heavy) | AN/PAS-13—MK19 Bracket Assembly | 327 | 500m | N/A | 17.7 R 24.5 D |
| Mk19 | AN/PEQ-2A | M2—AN/TVS-5 mounting bracket assembly & plastic spacer | 330 | 500m | N/A | Aiming 4.4R/23.4D Flood 0.4R / 23.4D |
| Mk19 | AN/TVS-5 | M2--AN/TVS-5 mounting bracket assembly | 333 | 500m | N/A | 2.4R 14.5D |

# Annex I—Acronyms and Abbreviations

| - A - |
| --- |
| AR | Automatic Rifleman |
| AR | Army Regulation |
| ARTBASS | Army Training Battle Simulation System |
| ASL | Authorized Stockage List |
| ATG | Anti-Tank Gunner |
| ATGA | Anti-Tank Gunner, Assistant |
| - B - |
| BII | Basic Issue Items |
| BIS | Backup Iron Sight |
| BN | Battalion |
| - C - |
| C3 | Command, Control and Communications |
| CCO | Close Combat Optic |
| CO | Company |
| - D - |
| DS | Direct Support |
| - E - |
| EW | Electronic Warfare |
| - G - |
| GREN | Grenadier |
| - H - |
| HB | Heavy Barrel |
| HTWS | Heavy Thermal Weapon Sight |
| - I - |
| IAW | In Accordance With |
| ID | Identification |
| IPR | In-Process Review |
| - L - |
| LMG | Light Machine Gun |
| LW | Land Warrior |
| - M - |
| METT-T | Mission, Enemy, Terrain, Troops and Time Available |
| MGO | Machine Gun Optic |
| MILES | Multiple Integrated Laser Engagement System |
| MM or mm | Millimeter |
| MTWS | Medium Thermal Weapon Sight |
| MWS | Modular Weapon System |
| - N - |
| NCO | Noncommissioned Officer |
| NVS | Night Vision Scope |
| - O - |
| OCIE | Organizational Clothing and Individual Equipment |
| - P - |
| PLL | Prescribed Load List |
| PLT | Platoon |
| PMCS | Preventive Maintenance Checks and Services |
| - R - |
| R | Rifleman |
| RTO | Radio-Telephone Operator |
| - S - |
| SAW | Squad Automatic Weapon |
| SL | Squad Leader |
| SOP | Standing Operating Procedures |
| - T - |
| TASC | Training and Audiovisual Support Center |
| T&E | Traversing and Elevation Mechanism |
| TACSOP | Tactical Standing Operating Procedures |
| TF | Task Force |
| TL | Team Leader |
| TM | Technical Manual |
| AN/PAS-13 (H/MTWS) | Thermal Weapon Sight |
| - U - |
| UBL | Unit Basic Load |

APPROXIMATE CONVERSION FACTORS

TO CHANGE	TO	MULTIPLY BY	TO CHANGE	TO	MULTIPLY BY

In	Cm	2.540	Cms	In	0.394

Feet	Meters	0.305	Meters	Feet	3.280

Yards	Meters	0.914	Meters	Yards	1.094

Miles	Kms	1.609	Kms	Miles	0.621

Sq In	Sq Cms	6.451	Sq Cms	Sq In	0.155

Sq Feet	Sq Meters	0.093	Sq Meters	Sq Feet	10.764

Sq Yards	Sq Meters	0.835	Sq Meters	Sq Yards	1.196

Sq Miles	Sq Kms	2.590	Sq Kms	Sq Miles	0.386

Acres	Sq Hectometers	0.405	Sq Hectometers	Acres	2.471

Cubic Feet	Cubic Meters	0.028	Cubic Meters	Cubic Feet	35.315

Cubic Yards	Cubic Meters	0.765	Cubic Meters	Cubic Yards	1.308

Fluid Ounces	Milliliters	29.573	Milliliters	Fluid Ounces	0.034

Pints	Liters	0.473	Liters	Pints	2.113

Quarts	Liters	0.946	Liters	Quarts	1.057

Gallons	Liters	3.785	Liters	Gallons	0.254

Ounces	Grams	28.349	Grams	Ounces	0.035

Pounds	Kilograms	0.454	Kilograms	Pounds	2.205

Short Tons	Metric Tons	0.907	Metric Tons	Short Tons	1.102

Miles per Gal	Km per Liter	0.425	Kms per liter	Miles per Gal	2.354

Miles per Hour	Kms per Hour	1.609	Kms per Hour	Miles per Hour	0.621

Small Arms

Integration Book

Published:  March 2002

# Text boxes

1

###### MILES Operating Instructions

A wide variety of MILES equipment is available for employment on different weapons systems.  MILES equipment, installation and operating instructions are available from most installation Training and Audiovisual Support Center.  The MILES provides for:

- Tactical engagement simulation for direct fire force-on-force training using eye safe laser "bullets".

- Each individual and vehicle in the training exercise has a detection system to sense hits and perform casualty assessment.

- Laser transmitters are attached to each individual and vehicle weapon system and accurately replicate actual ranges and lethality of the specific weapon systems.

- MILES training has been proven to dramatically increase the combat readiness and fighting effectiveness of military forces.

Various types of MILES transmitters are depicted on previous page.

MILES devices are not required when an AN/PSX-1 AN/PSX-1 (CIDDS) device has been mounted on the weapon.  The AN/PSX-1 performs the MILES training device function.

M4 with M4 Adapter Rail System Installed

M4/M4A1 MWS

M4 Adapter Rails

1

2

3

4

5

6

7

M4/M4A1 Carbine

=

+

M4 Adapter Rail System

(Component List)

| Item No | Nomenclature | Part No./NSN |
| --- | --- | --- |
| 1 | Upper Handguard Assy | 1005-01-453-4227 |
| 2 | Lower Handguard | 1005-01-453-1633 |
| 3 | 11 Rib Rail Cover Assy | 1005-01-453-5386 |
| 4 | 6 Rib Rail Cover Assy | 1005-01-453-4222 |
| 5 | 4 Rib Rail Cover Assy | 1005-01-453-4223 |
| 6 | 2 Rib Rail Cover Assy | 1005-01-453-4228 |
| 7 | Vertical Pistol Grip | 1005-01-453-6655 |

M16 MWS

M16A4 Rifle

M5 Adapter Rails

M16A4 with M4 Adapter Rail System Installed

1

9

=

+

8

7

6

5

4

3

2

9

### M5 Adapter Rail System

(Component List)

| Item No | Nomenclature | Part No./NSN |
| --- | --- | --- |
| 1 | Upper Handguard Assy | 1005-01-453-4225 |
| 2 | Lower Handguard | 1005-01-453-1635 |
| 3 | Barrel Stop Assy | 1005-01-453-4224 |
| 4 | 11 Rib Rail Cover Assy | 1005-01-453-5386 |
| 5 | 9 Rib Rail Cover Assy | 1005-01-453-5383 |
| 6 | 6 Rib Rail Cover Assy | 1005-01-453-4222 |
| 7 | 5 Rib Rail Cover Assy | 1005-01-453-4221 |
| 8 | 4 Rib Rail Cover Assy | 1005-01-453-4223 |
| 9 | Vertical Pistol Grip | 1005-01-453-6655 |

6

1

2

3

4

5

7

M16A4 Modular Weapon with M203 Installed

M4 Modular Weapon with M203 Installed

### M203, MWS Grenade Launcher

(Component List)

| Item No | Nomenclature | Part No./NSN |
| --- | --- | --- |
| 1 | Assembly, Left Bracket | 1005-01-452-8630 |
| 2 | Washer, Spring | 1005-01-452-9635 |
| 3 | Base, Right Half | 1005-01-453-1634 |
| 4 | Screw, Cap Socket Head | 5305-01-452-9639 |
| 5 | Shim, Plate | 5365-01-453-9287 |
| 6 | Assembly, Leaf Sight | 1005-01-453-5384 |
| 7 | Assembly, Rail Grabber | 19200 12598130 |

Note:  The AN/PVS-4 may also be mounted on the M4 handle in the same manner as is used to mount on the handle of the M16A2 (See page 10).  Items 5 & 6 will not be required when using this method.  Insure that the mounting knob is inserted into the hole in the carrying handle at an angle, due to the smaller gap between the top and bottom of the handle (item 2 above).  The AN/PVS-4 may already have a rail grabber/mount installed.

Thumb-screw

Mounting Rail

Remote Switch

Note:  The AN/PVS-4 may also be mounted on the M4 handle in the same manner as is used to mount on the handle of the M16A2 (See page 10).  Items 5 & 6 will not be required when using this method.  Insure that the mounting knob is inserted into the hole in the carrying handle at an angle, due to the smaller gap between the top and bottom of the handle (item 2 above).

3

1

1

1

2

3

Note:  The AN/PVS-4 may also be mounted on the M4 handle in the same manner as is used to mount on the handle of the M16A2 (See page 10).  Items 5 & 6 will not be required when using this method.  Insure that the mounting knob is inserted into the hole in the carrying handle at an angle, due to the smaller gap between the top and bottom of the handle (item 2 above).

1

2

3

3

1

Replace CCO with one showing knob.

Note:  The AN/PVS-4 may also be mounted on the M4 handle in the same manner as is used to mount on the handle of the M16A2 (See page 10).  Items 5 & 6 will not be required when using this method.  Insure that the mounting knob is inserted into the hole in the carrying handle at an angle, due to the smaller gap between the top and bottom of the handle (item 2 above).

Table 4 -  3

Table 4 -  2

##### Laser Target Preparation

If environmental conditions are such that the soldier's ability to conduct a 25m zeroing of the device and weapon is being hindered due to "IR Blooming" one to the following methods should be used to reduce the blooming effect:

1.  Install the Borelight Filter which was issued with the device.  If it is not dark enough for this method to work effectively use method 2, as outlined below.

2.  Cut a 2 by 2 square block out of the center of the target.  The laser will bloom on the zero target until the aiming laser is emitting through the 2 x 2 hole.  Once the laser is properly centered on the hole the blooming is reduced and zeroing may continue with a higher assurance of completing a successful zero.

Batteries:  BA-3058/U (x2)

AN/PEQ-2A Operating Instructions

(TM11-5855-308-12&P, 15 May 00)

General Functional Description

The TPIAL emits a highly collimated beam of infrared light for precise aiming of the weapon as well as a separate infrared illumination beam with adjustable focus.  The beams can be operated individually or in combination and be zeroed to the weapon and each other. The TPIAL is used with Night Vision Devices as either a handheld or weapon mounted illuminator/pointer.

WARNING

The AN/PEQ-2A makes use of a high power aiming laser and presents a serious eye hazard within 25 meters, when used in the training mode, and within 220 meters, when used in the tactical mode.

6

5

4

3

2

1

- AN/PVS-4 is zeroed for the rifle, not the Grenade Launcher.

- M4/M16A4 with M203 zero is the same as the basic weapon, without the Grenade Launcher.

6

5

4

3

2

2

3

1

3

NOTE

There are two sets of mounting slots.  Select the set of slots that provide the proper eye relief.  Once a set of slots is chosen, the same set should always be used in order for the system to retain zero.  Ensure mounting surface of base is free of dirt, oil or grease.

WARNING

Be sure the mounting base is fastened securely to the rifle.  Loose mounting may cause the day optic sight and base mount assembly to come off the rifle when firing, possibly injuring the shooter.

# M24--Day Optic Sight Mounting Instructions

(See TM 9-1005-306-10)

- Before mounting the day optic sight, lubricate the threads of each mounting nut.

- Insure smooth movement of each mounting nut and mount claw.

- Inspect for burrs and foreign matter between each mounting ring nut and mount claw.  Burrs or foreign matter must be removed prior to mounting.

- Mount the day optic sight and rings to the base (See diagram)

- Set each ring bolt spline in the selected slot

- Slide the rear mount claw against the base.  Finger tighten the mounting ring nut.

- Slide the front mount claw against the base.  Finger tighten the mounting ring nut.

3

1. Install Bracket

2.  Install AN/PAQ-4B/C

1

3

1. Install Bracket

2.  Install AN/PEQ-2A

1

3

2

4

5

2

2

1

2

4

4

3

1

2

4

3

1

2

4

1

3

2

4

3

2

1

4

3

1

2

1

2

3

4