| CONDITION: | You are going to operate a CCS at a nuclear accident/incident site. You will be dressed in the proper protective clothing and you will have a film badge; respiratory protection; radiac sets AN/PDR 27, and either an AN/PDR 54, AN/PDR 56 or AN/PDR 60; dosimeters IM9/UD, or IM 93A/UD, IM/147/PD, or equivalents; and unit CCS equipment and material. NOTE: FM 3-15 and FM 9-15 will be available at your command post. |
| --- | --- |
| STANDARD: | CCS is operated correctly to insure all personnel and material at the site are properly processed. |
| PERFORMANCE MEASURES: | 1. Be sure personnel traveling to or from incident site go through the CCS (app K, FM 9-15). 2. Tell personnel returning from the incident site what they have to do at the CCS (app K, FM 9-15). 3. Take dosimeter readings and collect film badges (app K, FM 9-15). 4. Monitor returning personnel for contamination, using a low-range gamma instrument and an alpha instrument (para 8-3 and 11-4, FM 3-15). 5. Process personnel requiring decontamination through wash, dry, and remonitor stations (para K-2(d), FM 9-15). 6. Tell returning personnel when they may go to the redress area, or for medical assistance (app K, FM 9-15). 7. Monitor material removed from the incident site for alpha, beta, and gamma contamination (para 8-3 and chap 11, FM 3-15). 8. Decontaminate and/or pack contaminated material (chap 11 and 12, FM 3-15). 9. Monitor decontaminated or packed material and decontaminate/repack if contamination is above permissable contamination levels (table K-1, FM 9-15). 10. Place material on the clean side of the contamination control line (app K, FM 9-15). |
| REFERENCES: | FM 3-15, Nuclear Accident Contamination Control FM 9-15, Explosive Ordnance Disposal Unit Operations TM 11-6665-208-15, Operator Organizational, DS, GS and Depot Maintenance Manual (Including Repair Parts and Special Tools List):AN/PDR-54 TM 11-6665-209-15, Operator Organizational,DS, GS, and Depot Maintenance Manual (Including Repair Parts and Special Tools List):Radiac Set AN/PDR 27 J and L TM 11-6665-214-10, Operator Manual Radiacmeters IM-9E/PD, IM-93/UD, IM-93A/UD, and IM-147/PD TM 11-6665-221-15, Operator's Organizational, DS, GS and Depot Maintenance Manual (Including Repair Parts and Special Tools List):Radiac Set AN/PDR 60 TM 11-6665-230-15, Operator's, Organizational, DS, GS, and Depot Maintenance Manual (Including Repair Parts and Special Tools List):Radiac Set AN/PDR 27R |

093-401-1347 (continued)