SUBCOURSE	EDITION

IT 0332	A

US ARMY INTELLIGENCE CENTER

POWERS OF TEN

AND

CONVERSION OF ELECTRICAL UNITS

POWERS OF TEN AND CONVERSION OF ELECTRICAL UNITS

Subcourse Number IT 0332

Edition A

US ARMY INTELLIGENCE CENTER

FORT HUACHUCA, AZ 85613-6000

2 Credit Hours

EDITION DATE: February 1996

SUBCOURSE OVERVIEW

This subcourse is designed to teach you to use scientific notation, powers of ten, and common number prefixes which denote powers of ten.  It will be used throughout the subcourses on electronics.

IT 0332 replaces SA 0700 Powers of Ten and Conversion of Electrical Units.

There are no prerequisites for this subcourse.

TERMINAL LEARNING OBJECTIVE:

ACTION:	You will be able to convert numbers between normal notation, powers of ten, and scientific notation; multiply, divide, and find roots of powers of 10; convert numbers expressed by common number prefixes in powers of ten and scientific notation.

CONDITION:	Given the information provided in this subcourse.

STANDARD:	To demonstrate competency of this task, you must achieve a minimum of 70 percent on the subcourse examination.

i	IT 0332

TABLE OF CONTENTS

Section	Page

Subcourse Overview	i

Special Instructions	iv

Lesson 1: Introduction to Powers of Ten	1-1

Lesson 2: Introduction to Conversion of Electrical Units	2-1

IT 0332	ii

SPECIAL INSTRUCTIONS

1.	These lessons contain 62 pages, each of which is divided into one or more frames.  Most pages are divided into three frames consisting of:

a.	TOP frame, containing the answer to the PROBLEM in the preceding frame.

b.	A MIDDLE frame, containing an example problem and its solution.

c.	A BOTTOM frame, containing a PROBLEM for you to solve.

2.	Do not spend a lot of time solving the problem in the middle frame.  The middle frame is meant to be a guide (showing you how to solve different types of problems), so, just examine it carefully step by step until you feel that you understand it.  Next, solve the PROBLEM in the bottom frame of the page and, once finished, compare your answer to the correct answer at the top of the next right-hand page.  (See the instructions in paragraph 3, below.)

3.	This lesson is written in a format which may be unfamiliar to you.  To complete this lesson, you must complete the pages and frames in numerical sequence (pages 1-1 through 1-42, pages 2-1 through 2-20; and frames 1 through 138).

IT 0332	iii

LESSON 1

INTRODUCTION TO POWERS OF TEN

Critical Task: None

OVERVIEW

LESSON DESCRIPTION:

Upon completion of this lesson you will be able to convert numbers between normal notation, powers of ten, and scientific notation; multiply, divide, and find roots of powers of 10; convert numbers expressed by common number prefixes in powers of ten and scientific notation.

TERMINAL LEARNING OBJECTIVE:

ACTION:	Convert numbers between normal notation, powers of ten, and scientific notation; multiply, divide, and find roots of powers of 10.

CONDITION:	Given the information provided in this subcourse.

STANDARD:	To demonstrate competency of this task, you must achieve a minimum of 70 percent on the subcourse examination.

1-1	IT 0332

INTRODUCTION TO POWERS OF TEN

FRAME

NO.  1	Example of a very large whole number: 100,000,000,000

Example of a very small decimal number: .000000000006

Electrical measurements often involve large whole numbers or small decimal numbers.  Working with large whole numbers and small decimal numbers can be time-consuming.  Also, using numbers with many zeros may lead to mistakes.  Powers of 10 are used to express large whole numbers and small decimal numbers as equivalent numbers containing only a few digits.  Obviously, numbers containing fewer digits are easier to use.

Powers of 10 involve the use of exponents.  An exponent is a small number written above and to the right of a number which is the base number.  The exponent indicates the number of times the base is to be taken as a factor.

For example: 103 = 10 X 10 X 10  1,000.

Multiples of 10, greater than one, can be expressed as the base 10 with a positive exponent.

For example: 10 = 101       100 = 102       1,000 = 103, etc.

Multiples of 10, between 0 and 1, can be expressed as the base 10 with a negative exponent.

For example: .1 = 10-1       .01 = 10-2       .001 = 10-3, etc.

The base 10, written without an exponent, actually has an exponent of 1.

Thus, 10 = 101.

The base 10, with an exponent of zero, is equal to one.  Thus, 100 = 1.

No response required.

IT 0332	1-2

FRAME

NO.  2	This table shows some decimals and whole numbers and their equivalent powers of 10.  Study it for a moment.

10,000 = 104

1,000 = 103

100 = 102

10 = 101

1 = 100	Notice that 100 = 1

.1 = 10-1

.01 = 10-2

.001 = 10-3

.0001= 10-4

FRAME

No.  3	Any number can be converted into 2 numbers: A number times a power of 10.  The number times a power of 10 will have the same digit sequence as the original number.  The power of 10 and its sign will be determined by the number of places and the direction the decimal point in the original number is moved.

Examples:   7,900 = 7.9 X 103	because 103	= 1,000

.01 =1 X 10-2	"	10-2	= .01

75 = 7.5 X 101	“	10-1	= 10

.075 = 7.5 X 10-2	“	10-2	= .01

.075 = 75 X 10-3	"	10-3	= .001

.075 = 750 X 10-4	"	10-4	= .0001

No response required

1-3	IT 0332

No response required

FRAME

No.  4	PROBLEM:

Fill in the blanks with the equivalent powers of 10.

.0001	=	1	X	   10-4

.001	=	1	X

.01	=	1	X

.1	=	1	X

1	=	1	X	    100

10	=	1	X

Check your answer with

100	=	1	X			the table on page 1-3.

1,000	=	1	X

FRAME

NO.  5	Any number can be converted into 2 numbers: a number times a power of 10.  The number times a power of 10 will have the same sequence of digits as the original number.  The exponent (power) of the base 10 is always equal to the number of places the decimal point is moved.  The exponent is POSITIVE when the decimal point is moved to the LEFT; the exponent is NEGATIVE when the decimal point is moved to the RIGHT.

PROBLEM:

Fill in the blanks:	To convert a number to a numerical value times a power of 10, move the decimal point ____________________ to make the power of 10

LEFT/RIGHT

POSITIVE, or move the decimal point _____________ to make the

LEFT/RIGHT

power of 10 NEGATIVE.

IT 0332	1-4

FRAME

No.  6	ANSWER:

move the decimal point LEFT: make the power of 10 POSITIVE,

move the decimal point RIGHT: make the power of 10 NEGATIVE.

FRAME

No.  7	Study this problem on equivalent power of 10, then continue.

.000001 = _________

Rule:	To express a decimal as a

whole number times the power

of 10, move the decimal point

to the RIGHT, count the

number of places to the

original point, and use this

count as a NEGATIVE exponent

(or power) of 10.

Solution:	Move the decimal point 6

places to the RIGHT; the

exponent is a NEGATIVE 6.

Thus:	.000001 = 1 X 10-6 = 10-6

FRAME

No.  8	PROBLEM:

Fill in the blank with the equivalent power of 10.

.001 = ________

1-5	IT 0332

FRAME

No.  9	Answer: 10-3

Solution:

Decimal point is moved 3

places to the right; the

exponent is a negative 3.

.001 = 1 X 10-3= 10-3

FRAME

No.  10	Study this problem on equivalent power of 10, then continue.

100,000,000 = ______

Rule:	to express a whole number as

a smaller number times a

power of 10, move the decimal

point to the LEFT, count the

number of places to the

original point, and use this

count as a POSITIVE exponent

(or power) of 10.

Solution: 	Move the decimal point 8

places to the LEFT; the

exponent is a POSITIVE 8.

Thus:	100,000,000 = 1 X 108 = 108

FRAME

NO.  11	PROBLEM:

Fill in the blank with the equivalent power of 10.

1,000 = ______

IT 0332	1-6

FRAME

No.  12	ANSWER: 103

Solution:	Decimal point is moved 3

1,000 = 1 X 103 = 10 3

places to the LEFT; the

exponent is a POSITIVE 3.

FRAME

NO.  13	PROBLEM:

Fill in the blanks with the equivalent powers of 10.  Do both problems before checking answers.

100,000 = _____________

.001 = ____________

1-7	IT 0332

FRAME

NO.  14	ANSWER: 105

Solution:

100,000 = 105	Decimal point is moved 5 places to the LEFT; the

exponent is a POSITIVE 5.

ANSWER 10-3

Solution:	Decimal point is moved 3 places to RIGHT; the

.001 = 10-3	exponent is a NEGATIVE 3.

FRAME

NO.  15	Study the following problem on SCIENTIFIC NOTATION, rounded off to 3 significant digits.

636.42 = ___________________________

Solution:	Converting a whole number to SCIENTIFIC NOTATION (a

number between 1 and 10 times a power of ten) is done by

moving the decimal point LEFT from its position in the

original number to a new position which will be immediately

following the first significant digit, giving you a POSITIVE

power of 10.

NOTE:	Count the number of places you moved the decimal point to

the LEFT in the original number to its new position following

the first significant number.  This will give you the proper

exponent for your POSITIVE power of 10.

Thus: Original number	In scientific	In scientific

notation, but NOT	notation, and

rounded off.	rounded off to 3

significant numbers.

636.42 = 6.3642 X 102 = 6.36 X 102

IT 0332	1-8

FRAME

No.  16	PROBLEM:

Convert this number to SCIENTIFIC NOTATION, rounded off to 3 significant digits.

88,885 = _____________________________-

1-9	IT 0332

FRAME

No.  17	ANSWER: 8.89 X 104

Solution:	8.89 is a number written in SCIENTIFIC NOTATION, a

88,885 =	number between 1 and 10 times a power of ten; the

8.89 X 104	decimal point moved four places LEFT; the exponent

for the power of 10 is a POSITIVE 4.

FRAME

NO.  18.	Study the following problem on SCIENTIFIC NOTATION, rounded off to 3 significant digits.

.0005966 = _________

Solution:	Converting a decimal number to SCIENTIFIC NOTATION (a

number between 1 and 10 times a power of ten) is done by

moving the decimal point RIGHT from its position in the

original number to a new position which will be immediately

following the first significant digit, giving you a NEGATIVE

power of 10.

NOTE:	Count the number of places you moved the decimal point to

the RIGHT in the original number to its new position

following the first significant number.  This will give you the

proper exponent for your NEGATIVE power of 10.

Thus:	Original number	In scientific	In scientific

notation, but	notation, and

NOT rounded	rounded off to 3

off.	significant

numbers.

.0005966      = 5.966 X 104    = 5.97 X 104

FRAME

NO.  19	PROBLEM:

Convert this number to SCIENTIFIC NOTATION, rounded off to 3 significant digits.

.000088885 = ______________

IT 0332	1-10

FRAME

NO.  20	ANSWER: 8.89 X 10-5

Solution:	8.89 is a number between 1 and 10;

.00008885 = 8.89 X 10-5	the decimal point moves RIGHT 5 places;

the exponent is a NEGATIVE 5.

FRAME

NO.  21	Study the following problem on SCIENTIFIC NOTATION, rounded off to 3 significant digits.

45,667 = ___________________

Solution:	Place the decimal point between 4 and 5 so the number has a

value between 1 and 10.  Since the decimal point moved 4

places LEFT, the power of 10 is a POSITIVE 104.  Remember, a

number in Scientific Notation is a number between 1 and 10

times a power of 10.

Thus:	45,667 = 4.5667 X 104 = 4.57 X 104

FRAME

NO.  22	PROBLEM:

Convert this number to SCIENTIFIC NOTATION, rounded off to 3 significant digits.

4,444.3 = ______________

1-11	IT 0332

FRAME

NO.  23	ANSWER:	4.44 X 103

Solution:		4.44 is between 1 and 10; the decimal

4,444	4.44 X 103	point moved 3 places LEFT; the

exponent is a +3.

FRAME

NO.  24	Study the following problem on SCIENTIFIC NOTATION, rounded off to 3 significant digits.

665,878 = ___________

Solution:	6.65878 is a number between 1 and 10.  Since the decimal

point moved 5 places LEFT, the exponent of the power of 10

is a POSITIVE 5.  6.65878 is now 6.66 rounded off to 3

significant digits.

Thus:	665,878 = 6.65878 X 105 = 6.66 X 105

FRAME

NO.  25	PROBLEM:

Convert this number to SCIENTIFIC NOTATION, rounded off to 3 significant digits.

.00008887 = ______________

IT 0332	1-12

FRAME

NO.  26	ANSWER: 8.89 X 10-5

Solution: .00008887 = 8.887 X 10-5 = 8.89 X 10-5

FRAME

NO.  27	PROBLEM:

Convert this number to SCIENTIFIC NOTATION, rounded off to 3 significant digits, times the proper power of 10.  Do both problems before checking answers.

.000034567 = ________________

881.238 = ________________

1-13	IT 0332

FRAME

NO.  28	ANSWER: 3.46 X 10-5

Solution: .000034567 = 3.46 X 10-5

ANSWER: 8.81 X 102

Solution: 881.238 = 8.81 X 102

FRAME

NO.  29	Study the problems below, then continue.

3,200 = _____ X104

3,200 = _____ X 10-4

Solution:	Move the decimal point to the LEFT when the exponent is POSITIVE; and to the RIGHT when the exponent is NEGATIVE.

Thus:	3,200 = .3200 X 104

3,200 = 32,000,000 X 10-4

FRAME

NO.  30	PROBLEM:

Fill in the blank with the proper numerical value.

50,000 = _____ x 107

IT 0332	1-14

FRAME

NO.  31	ANSWER: .005

Solution:	The decimal point moves 7 places

50,000 = .005 X 107	LEFT when the exponent is a +7.

FRAME

NO.  32	Study the problem below, then continue.

.000000000045 = ______________________ X 10-12

Solution:	Move the decimal point 12 places RIGHT when the exponent is a NEGATIVE 12.

Thus:	.000000000045 = 45 X 10-12

FRAME

NO.  33	PROBLEM:

Fill in the blank with the proper value.

.00056 = ________________ x 10-6

1-15	IT 0332

FRAME

NO.  34	ANSWER: 560

Solution:	Exponent is a NEGATIVE 6; the decimal point

.00056 = 560 X 10-6	moves 6 places to the RIGHT.

FRAME	Study the problem below, then continue.

NO.  35

.1 = _____________________

Solution:	Move decimal point one place to the right; the exponent is a NEGATIVE one.

Thus:	.1= 1 x 10-1 = 10-1

FRAME

NO.  36	PROBLEM:

Fill in the blank with the equivalent power of 10.

.00000001 = 1 X ______ = _____

IT 0332	1-16

FRAME

NO.  37	ANSWER: 10-8

Solution:	Exponent is a NEGATIVE 8 when the

.00000001 = 1 X 10-8 = 10-8	decimal point moves 8 places to the RIGHT.

FRAME

NO.  38	Study the problems below, then continue.

9.15X 103 = ________ X 106

9.15 X 10-3 = ________ X 10-6

Solution:	Move the decimal point to the LEFT when the change in exponent is in a POSITIVE direction.  Move the decimal point to the RIGHT when the change in exponent is in a NEGATIVE direction.

Thus:	9.15 X 103 = .00915X 106

9.15 X 10-3 = 9,150 X 10-6

NOTE:	Changing from 103 to 106 means the exponent changes by 3 in a POSITIVE direction.  Changing form 10-3 to 10-6 means the exponent changes by 3 in a NEGATIVE direction.

FRAME

NO.  39	PROBLEM:

Fill in the blank with the proper value.

2.2 X 10-2 = ______ X 100

1-17	IT 0332

FRAME

NO.  40	ANSWER: .022

Solution:	Changing from 10-2 to 100 means the exponent

2.2 X 10-2 = .022 X 100	changes by 2 in a POSITIVE direction; so the

decimal	point moves 2 places to the LEFT.

FRAME

NO.  41	PROBLEM:

Study the problem below, then continue.

3.33 X 10-4 = ____________________________ X 10-6

Solution:	Changing from 10-4 to 10-6 means the exponent changes by 2 in a NEGATIVE direction; so the decimal point in 3.33 moves 2 places to the RIGHT.

Thus:	3.33 X 10-4 = 333 X 10-6

FRAME

NO.  42	PROBLEM:

Fill in the blank with the proper value.

5.83 X 102 = _____ X 10-1

IT 0332	1-18

FRAME

NO.  43	ANSWER: 5,830

Solution:	Changing from 102 to 10-1

5.83 X 102 = 5,830 X 10-1	means the exponent changes by 3 in a

NEGATIVE direction; so the decimal point in

5.83 moves 3 places to the RIGHT.

FRAME

NO.  44	Study the problem below, then continue.

250,000 = ______ X 105

Solution:	Move the decimal point 5 places to the LEFT when the exponent is a POSITIVE 5.

Thus:	250,000 = 2.5 X 105

FRAME

NO.  45	PROBLEM:

Fill in the blank with the proper value.

13,460 = ______ X 10-12

1-19	IT 0332

FRAME

NO.  46	ANSWER: 13,460,000,000,000,000

Solution:

13,460 = 13,460,000,000,000,000 X 10-12	When the

exponent is a

NEGATIVE 12, the

decimal point is

moved 12 places

to the RIGHT.

FRAME

NO.  47	Study the problem below, then continue.

6.660 X 10-4 = _________________________ X 10-7

Solution:	Changing from 10-4 to 10-7 means the exponent changes by 3 in a NEGATIVE direction; so the decimal point in the original number 6.660 moves 3 places to the RIGHT.

Thus:	6.660 X 10-4 = 6,660 X 10-7

FRAME

NO.  48	PROBLEM:

Fill in the blank with the proper value.

7.09 X 104 = ____________________ X 10-1

IT 0332	1-20

FRAME

NO.  49	ANSWER: 709,000

SOLUTION:

7.09 X 104 = 709,000 X 10-1	Changing from 104 to 10-1 means the

exponent changes by 5 in a NEGATIVE

direction; so the decimal point in 7.09

moves 5 places to the right.

FRAME

NO.  50	PROBLEM:

Fill in the blanks with the proper values.  Do both problems before checking answers.

83,000 = _________________ X 106

.0000525 _________________ X 10-12

1-21	IT 0332

FRAME

NO.  51	ANSWER: .083

Solution:	POSITIVE 6 exponent; decimal point

83,000 = .083 X 106	moves 6 places to the LEFT.

ANSWER: 52,500,000

Solution:	NEGATIVE 12 exponent; decimal point

.0000525 = 52,500,000 X 10-12	moves 12 places to the RIGHT

FRAME

NO.  52	PROBLEM:

Fill in the blanks with the proper values

4.24 X 10-6 = ___________________ X 10-3

6.28 X 104 = ____________________ X 10-2

IT 0332	1-22

FRAME

NO.  53	ANSWER: .00424

Solution:	Changing from 10-6 to 10-3 means the

4.24 X 10-6 = .00424 X 10-3	exponent changes by 3 in a POSITIVE

direction; so the decimal point in 4.24

ANSWER: 6,280,000	moves 3 places to the LEFT.  Changing

from 104 to 10-2 means the exponent

Solution:	changes by 6 in a NEGATIVE direction;

6.28 X 104 - 6,280,000 X 10-2	so the decimal point in 6.28 moves 6

places to the RIGHT.

FRAME

NO.  54	Powers of 10 simplify problem solving.  For example:

Multiplication: 2,000 X 45,000 = (2 X 103) X (4.5 X 104) =

9X 107

Division: 66.000 = 6.6 X 104 = 6.6 X 104 X 10-3 = 2.2 X 101 or 22

3,000	3 X 103	3

Extracting square root:

4,000,000	=	4 X 106	=	2 X 106+2 = 2 X 103

Squaring a

number:	(20,000)2 = (2 X 104)2 = 4 X 104x2 = 4 X 108

Study the examples above for a moment.

No response required

1-23	IT 0332

FRAME

NO.  55	Study the problems below, then continue.

10,000 X 100	= ______________

·0000001 X .001	= ______________

10,000 X .001	= ______________

23,000 X 500	= ______________

6,200 X .02.X 2,000	= ______________

Solution:	To MULTIPLY two or more numbers using powers of 10, ADD the EXPONENTS (power) and retain the base 10.

Thus:

10,000 X 100 = 1 X 104+2 = 106

.0000061 X .001 = 1 X 10-7+(-3) = 10-10

10,000 X .001 = 1 X 104+(-3) = 101

23,000 X 500 = 2.3 X 104 X 5 X 102 = 11.5 X 104+2 = 11.5 X 104+2

= 11.5 X 106

6,200 X .02 X 2,000 = 6.2 X 103 X 2 X 10-2 X 2 X 103

= 24.8 X 103+(-2)+3 = 24.8 X 104

FRAME

NO.  56	PROBLEM:

Solve using powers of 10.

(1 X 106)(1 X 103)(1 X 10-3)(1 X 106) =

IT 0332	1-24

FRAME

NO.  57	ANSWER: 1012

Solution:	To multiply powers of 10, add

106 X 103 X 10-3 X 106	exponents and retain the base

= 106+3+(-3)+6 = 1012	10.

Study the problem below, then continue.

300 X 2,200 X .001 =

Solution:	To multiply, convert each number to SQENTIFIC NOTATION;

multiply the numerical values together and add the exponents

(powers of 10).

Thus:

300 X 2,200 X .001 = (3 X 102) X (2.2 X 103) X (1X 10-3)

= 3 X 2.2 X 102+3+(-3) = 6.6 X 102

FRAME

NO.  58	PROBLEM:

Solve using powers of 10.

3,500 X .0035 X 8,000 =

1-25	IT 0332

FRAME

NO.  59	ANSWER: 98 X 103 or 9.8 X 104

Solution:

3,500 X .0035 X 8,000 = (3.5 X 103) X (3.5 X 10-3) X (8 X 103)

= (3.5 X 3.5 X 8) X 103+(-3)+3

= 98 X 103 or 9.8 X 104

FRAME

NO.  60	Study the problem below, then continue.

107 =

103

Solution:	To DIVIDE, move 103 from the denominator to the numerator; CHANGE the SIGN OF THE EXPONENT 3, then add the exponents.

Thus:	107 = 107 X 10-3 = 107+(-3) = 104

103	1

FRAME

NO.  61	PROBLEM:

Solve using powers of 10.

660.000 = ____________

.0002

IT 0332	1-26

FRAME

NO.  62	ANSWER: 3.3 X 109

Solution:

660.000 = 6.6 X 105 = X 6.6 X 105 X 104 = 3.3 X 109

.0002	2X10-4	2

FRAME

NO.  63	Study the problem below, then continue.

66.000 =

.000003

Solution:	Convert to SCIENTIFIC NOTATION (or small, easy-to-divide numbers); then divide, using laws of exponents.

Thus:	66.000	= 6.6 X 104	= 6.6 X 104 X 106 = 2.2 X 1010

.000003	3 X 10-6	3

FRAME

NO.  64	PROBLEM:

Solve using powers of 10.

45.000.000   =  __________________

.005

1-27	IT 0332

FRAME

NO.  65	ANSWER: 9 X 109

Solution:

45.000.000 = 4.5 X 107 = 4.5 X 107 X 103 = .9 X 1010

.005	5 X 10-3	5	or 9 X 109

FRAME

NO.  66	Study the problem below, then continue.

.00006 X .144 X .02 =

Solution:	Convert the numbers to SCIENTIFIC NOTATION; multiply the numerical values and add the exponents (powers of 10).

Thus:

.00006 X .144 X .02 = (6 X 10-5) X (1.44 X 10-1) X (2 X 10-2)

= (6 X 1.44 X 2) X 10-5+(-1) +(-2) = 17.28 X 10-8

FRAME

NO.  67	PROBLEM:

Solve using powers of 10.

1,200 X 200 X .0003 =

IT 0332	1-28

FRAME

NO.  68	ANSWER: 7.2 x 101

Solution:

1,200 X 200 X .0003 = (1.2 X 103) X (2 X 102) X (3 X 104)

= (1.2 X 2 X 3) X 103+2+(-4)

= 7.2 X 101

FRAME

NO.  69	Study the problem below, then continue.

(104)2 =

Solution:	To raise a power of 10 to the second power, MULTIPLY the power of 10 by 2.

Thus:	(104)2 = 104X2 = 108

FRAME

NO.  70	PROBLEM:

Solve using powers of 10.

(106)2 =

1-29	IT 0332

FRAME

NO.  71	ANSWER: 1012

Solution: (106)2 = 106X2 = 1012

FRAME

NO.  72	Study the problem below, then continue.

(30,000)2 =

Solution:	Convert to SCIENTIFIC NOTATION; Square the numerical Value And Multiply the power of 10 by the exponent 2.

Thus:	(30,000)2 = (3X104)2 = 32 X 104x2 = 9 X 108

FRAME

NO.  73	Problem:

Solve using powers of 10.

(6X103)2 =

IT 0332	1-30

FRAME

NO.  74	ANSWER: 36 X 106 or 3.6 X 107

Solution (6 X 103)2 = 62 X 103X2 = 36 X 106 or 3.6 X 107

FRAME

NO.  75	Study the problem below, then continue.

.159     =

.00003

Solution:	Convert to easily divisible numbers times powers of 10; then divide.

Thus:	.159     = 159X 10-3 = 159 X 10-3 X 105 = 53 X 102

.00003	3X 10-5	3

FRAME

NO.  76	PROBLEM:

Solve using powers of 10.

1      =

.000005

1-31	IT 0332

FRAME

NO.  77	ANSWER: 2X105

Solution:	           1        =       1           = 1 X 106 = 10 X 105 = 2 X 105

.000005	5 X 10-6	5	5

NOTE: By converting 1 X 106 to 10 X 105, it becomes easier to divide by 5.

FRAME

NO.  78	PROBLEM:

Solve using powers of 10.  Do both problems before checking answers.

107 X 5 X 10-2 X 106 =

.225 X .002 X .04 =

IT 0332	1-32

FRAME

NO.  79	ANSWER: 5 X 1011

Solution: 107 X 5 X 10-2 X 106 = 5 X 107+(-2)+6 = 5 X 1011

ANSWER: 18 X 10-6 or 1.8 X 10-5

Solution:

.225X .002 X .04 = (2.25 X 10-1) X (2 X 10-3) X (4 X 10-2)

= 18 X 10-6 or 1.8 X 10-5

FRAME

NO.  80	Study the problem below, then continue.

108   =

Solution:	To extract the SQUARE ROOT of a power of 10, DIVIDE the EXPONENT by 2, and retain the base 10.

Thus:	108   = 108 ÷ 2 = 104

FRAME

No.  81	PROBLEM:

Solve using powers of 10.

106    =

1-33	IT 0332

FRAME

NO.  82	ANSWER: 103

Solution:

106   =   106 ÷ 2   =   103

FRAME

NO.  83	Study the problem below, then continue.

30 X 20 X 2 X 3 X 102 =

Solution:	Combine and convert the numbers under the radical sign into 2 numbers, a numerical value and an "EVEN" power of 10.  By even, we mean that the power can be divided evenly by 2.

THUS:

30 X 20 X 2 X 3 X 102	=   3,600 X 102

=   36 X 102 X 102

=   36 X 104

=   6 X 104+2 = 6 X 102

FRAME

NO.  84	PROBLEM:

Solve using powers of 10.

1,000 X 107 =

IT 0332	1-34

FRAME

NO.  85	ANSWER: 105

Solution:

1,000 X 107 =    103 X 107 =    1010  =  1010 + 2 = 105

FRAME

NO.  86	Study the problem below, then continue.

(400 X 104)2 =

Solution:	Convert quantity in parentheses to SCIENTIFIC NOTATION; square the numerical value; multiply the power of 10 by 2.

Thus:	(400 X 104)2 = (4 X 102 X 104)2 =

42 X 106X2 = 16 X 1012 or 1.6 X 1013

FRAME

NO.  87	PROBLEM:

Solve using powers of 10.

(12 X 10-3)2 =

1-35	IT 0332

FRAME

NO.  88	ANSWER: 144 X 10-6 or 1.44 X 10-4

Solution:

(12 X 10-3)2 = 122 X 10-3x2 = 144 X 10-6 or 1.44 X 10-4

FRAME

NO.  89	PROBLEM:

Solve using powers of 10.  Do both problems before checking answers.

1       =

500,000

108 X 10       =

10-5 X 1,000

IT 0332	1-36

FRAME

NO.  90	ANSWER: 2 X 10-6

Solution:

1          = 10 X 10-1 = 10 X 10-8 = 2 X 10-6

500,000	5 X 10-5	5

ANSWER: 1011

Solution:

1 X 109             =     109 X 105 X 10-3 = 1011

1 X 10-5 X 103

FRAME

NO.  91	Study the problem below, then continue.

81,000 X 103 =

Solution:	Convert the numbers under the radical sign to a numerical value times an "EVEN" power of 10 (divisible by 2).  If it is not EVEN, it must be made EVEN.

Thus:

81,000 X 103 =    81 X 103 X 103

=    81 X 106

=    9 X 106   2 = 9 X 103

FRAME

NO.  92	PROBLEM:

Solve using powers of 10.

2,500 X 104 =

1-37	IT 0332

FRAME

NO.  93	ANSWER: 5 X 103

Solution:

2,500 X 104   =    25 X 102 X 104 =    25 X 106  =

5 X 106+2  =  5 X 103

FRAME

NO. 94	PROBLEM:

Solve using powers of 10.  Do both problems before checking answers.

(100 X 10,000)2 =

(3 X 105)2 =

IT 0332	1-38

FRAME

NO.  95	ANSWER: 1012

Solution:

(100 X 10,000)2 = (102 X 104)2 = (106)2 = 106x2 = 1012

ANSWER: 9 X 1010

Solution: (3 X 105)2 = 32 X 105X2 = 9 X 1010

FRAME

NO.  96	PROBLEM:

Solve using powers of 10.  Do both problems before checking answers.

4 X 3 X 12 X 104 =

160 X 105 =

1-39	IT 0332

FRAME

NO.  97	ANSWER: 12 X 102 or 1.2 X 103

Solution:

4 X 3 X 12 X 104 =    144 X 104 =    12 X 102 OR 1.2 X 103

ANSWER: 4 X 103

Solution:

160 X 105 =    16 X 106 =   4 X 103

FRAME

NO.  98	Electrical and electronic problems are often combinations of multiplication, division, and extracting square roots.  It is suggested that combination problems be solved in this order:

(1) Convert all numbers to SCIENTIFIC NOTATION, or to small, easy-to-handle numbers; multiply by the proper powers of 10.

(2) Extract square roots (thus removing the radical signs).

(3) Multiply, divide, etc., until solution is reached.  Study the above information, then continue below.

FRAME

NO.  99	PROBLEM:

Fill in the blanks:

To extract the square root of a power of 10, the power of 10 must be _______.

odd/even

If it is not _______, it must be made _______.

odd/even	odd/even

IT 0332	1-40

NO.  100 ANSWERS: even, even, even

1-41	IT 0332

LESSON 2

INTRODUCTION TO CONVERSION OF ELECTRICAL UNITS

CRITICAL TASK: None

OVERVIEW

LESSON DESCRIPTION:

Upon completion of this lesson, you will be able to convert numbers expressed by common number prefixes in powers of ten and scientific notation.

TERMINAL LEARNING OBJECTIVE:

ACTION:	Convert numbers expressed by common number prefixes in powers of 10 and scientific notation.

CONDITION:	Given the information provided in this subcourse.

STANDARD:	To demonstrate competency of this task, you must achieve a minimum of 70 percent on the subcourse examination.

2-1	IT 0332

NO 101	INTRODUCTION TO CONVERSION OF ELECTRICAL UNITS

The volt, the ohm, and the ampere are the basic units of electrical measurements.  You previously learned that one ampere of current flows through one ohm of resistance when one volt of electrical force is applied across the resistance.

Often, the unit of measurement (volt, ohm, and ampere) is expressed with a prefix to enable the handling of extremely large or extremely small electrical measurements.  For example, electrical values expressed in basic units, such as 40,000 volts and .005 ampere, could be expressed in units with prefixes, such as 40 kilovolts and 5 milliamperes.

Thus, it can be seen that any unit of electrical measurement can be expressed with or without a prefix.

No response required

2-3	IT 0332

FRAME

NO.  102	There are 5 metric prefixes commonly used with electrical measurements; these are: mega, kilo, milli, micro, and pico.

(1)	Mega, abbreviated M, means million.  Since 1,000,000 can be expressed as 106, we can substitute mega or M for 106.

For example: 88,000,000 Ω  = 88 X 106 Ω = 88 M Ω.

(2)	Kilo, abbreviated k, means thousand.  Since 1,000 can be expressed as 103, we can substitute kilo or k for 103.

For example: 35,000 V = 35 X 103 V = 35 kV.

(3)	Milli, abbreviated m, means one thousandth part of.  Since .001 can be expressed as 10-3, we can substitute milli or m for 10-3.

For example: .002 A = 2 X 10-3 A = 2 mA.

(4)	Micro, abbreviated µ , means one millionth part of.  Since .000001 can be expressed as 10-6, we can substitute micro or µ for 10-6.

For example: .0000026 V = 2.6 X 10-6 V = 2.6 µV.

(5)	Pico, abbreviated p, means one millionth of a millionth part of.  Since .000000000001 can be expressed as 10-12, we can substitute pico or p for 10-12.

For example: .000000000155 A = 155 X 10-12 A = 155 pA.

No response required

IT 0332	2-4

FRAME

NO.  103	This chart shows the relationship between metric prefixes and their equivalent powers of 10.  Study it for a moment.

Numerical Value	Prefix	Abbreviation	Power of 10

.000000000001	pico	p	10-12

.000001	micro	µ	10-6

.001	milli	m	10-3

1	none	none	100

1,000	kilo	k	103

1,000,000	mega	M	106

FRAME

NO.  104	PROBLEM:

Cover the above chart with your hand and fill in the blocks below.

Numerical Value	Prefix	Abbreviation	Power of 10

.000000000001

.000001

.001

1

1,000

1,000,000

Correct any mistakes in this chart, then continue on the next page.

2-5	IT 0332

FRAME

NO.  105	Metric prefixes can be substituted for powers of 10 and vice versa:

106	=	mega or M

103	=	kilo or k

10-3	=	milli or m

10-6	=	micro or µ

10-12	=	pico or p

FRAME

NO.  106	PROBLEM:

Cover the information above and fill in the blocks below.

Numerical Value  Prefix      Abbreviation    Power of 10

.000000000001

.000001

.001

1

1,000

1,000,000

Correct any mistakes in this chart, then continue on the next page.

IT 0332	2-6

FRAME

NO.  107

Numerical Value	Prefix	Abbreviation	Power of 10

.0000000000000001	Pico	p	10-12

.00000001	micro	µ	10-6

.001	milli	m	10-3

1	none	none	100

1,000	kilo	K	103

1,000,000	mega	M	106

FRAME

NO.  108	Study the problem below, then continue.

220 mA = _______ µA

Solution:	Substitute 10-3 for m and 10-6 for µ.  Converting from 10-3 to 10-6 is a NEGATIVE 3 change in exponent, so the decimal point in 220 must move 3 places to the RIGHT.

NOTE:	Remember, when converting a metric prefix to a smaller metric prefix, always move the decimal point to the RIGHT.

Thus:	220 milli amps becomes 220 X 10-3 amps when substituting 10-3 for milli and 220,000 X 10-6 amps when substituting 10-6 for micro.  Your answer then becomes 220 milli amps = 220,000 micro amps.

FRAME

NO.  109	PROBLEMS:

Fill in the blank with the proper value.

3,000  µA = ___________________ mA

2-7	IT 0332

3,000  µA= _______________________ mA

FRAME

NO.  110	ANSWER:	3 mA

Solution:	Converting from 10-6

3,000 µA = 3,000 X 10-6 A = 3 X 10-3 A = 3mA	to 10-3 is a +3 change in

exponent; the decimal point

moves 3 places to the

LEFT.

FRAME

NO 111	Study the problem below, then continue.

.002 mA = _______________________ uA

Solution:	Substitute 10-3 for m and 10-6 for µ.  You will then see that 10-3 to 10-6 is a NEGATIVE 3 change in exponent, so the decimal point in .002 moves 3 places to the RIGHT.

Thus:	.002 mA = .002 X 10-3 A = 2 X 10-6 A = 2 µA

FRAME

NO.  112	PROBLEM:

Fill in the blank with the proper value.

110MΩ= ___________________ Ω

IT 0332	2-8

FRAME

NO 113	ANSWER: 110,000,000 Ω

Solution:

110 M Ω = 110 X 10-6 Ω = 110,000,000 X 100

= 110,000,000 Ω

NOTE: 106 to 100 is a NEGATIVE 6 change in exponent.

FRAME

NO 114	PROBLEM:

Fill in the blocks.

Numerical Value	Prefix	Abbreviation	Power of 10

.000000000001

.000001

.001

1

1,000

1,000,000

FRAME

NO 115	Numerical Value	Prefix	Abbreviation	Power of 10

.000000000001	pico	P	10-12

.00000	micro	µ	10-6

.001	milli	m	10-3

1	none	none	100

1,000	kilo	k	103

1,000,000	mega	M	106

2-9	IT 0332

FRAME

NO.116	We have seen that either METRIC PREFIXES or POWERS of 10 may be used to replace the zero digits in very large or small measurements.

For example: .000000000005 V = 5 X 10-12 V or 5 pV

33,000,000 Ω =33 X 106 Ω  or 33 mΩ

Usually, to solve a problem involving electrical measurements, all numbers with prefixes are converted to basic units times powers of 10.  After the problem is solved, the answer may be expressed with a prefix if required or desired.

FRAME

NO.  117	PROBLEM:

Which of the following expressions are equivalent to .0000068 mA?

A.  6.8 pA

B.  .0000000068 A

C.  6,800 pA

D.  6.8 X 10-12 A

E.  6.8 X 10-9 A

IT 0332	2-10

FRAME

NO.  118	ANSWER: B, C, and E are equivalent.

FRAME

NO.  119	Study the problem below, then continue.

100 mV = 20 ______ A

5k Ω

Solution:	Substitute equivalent powers of 10 for m and k; fill in the blank with the proper power of 10; then substitute a metric prefix for equivalent power of 10.

Thus:	100 mV = 100 X 10-3 V = 20 X 10-6 A= 20 µA

5k Ω 	5 X 103 Ω

NOTE:	This is a practical electrical problem working with Ohm's law:

volts (V) = amperes (A)

ohms (Ω)

FRAME

NO.  120	PROBLEM:

Fill in the blank with the proper metric prefix.

24 kV = 12 _______ Ω

2 mA

2-11	IT 0332

FRAME

NO.  121	ANSWER: M

Solution:	24 kV = 24 X 103 V =12 X 106 Ω = 12M Ω

2 mA	2 X 10-3 A

FRAME

NO.  122	Study the problem below, then continue.

3 k Ω X 8 µA = 24 _______ V

Solution:	Substitute powers of 10 for the metric prefixes; fill in the blank with the proper power of 10; then substitute.  a metric prefix for the power of 10 in the blank.

Thus:	3 k Ω X 8 µA = 3 X 103 Ω X 8 X 10-6 A = 24 X 10-3 V

= 24 mV

FRAME

NO.  123	PROBLEM:

Fill in the blank with the proper metric prefix

4M Ω X 4 mA = 16 _______ V

IT 0332	2-12

FRAME

NO.  124	ANSWER:

Solution:

4 M Ω X 4 mA = 4 X 106 Ω X 4 X 10-3 A = 16 X 103 V = 16 kV

FRAME

NO.  125	Study the problem below, then continue.

38 K Ω = _______ M Ω

Solution:	Substitute 103 for k and 108 for M.  You will then see that 103 to 106 is a POSITIVE 3 change in exponent.  So the decimal point in 38 moves 3 places to the LEFT.

NOTE:	Remember, when converting a metric prefix to a larger metric prefix, move the decimal point to the LEFT.

Thus:	38 kilohms becomes 38 X 103 ohms when substituting 103 for kilo and .038 X 108 ohms substituting 106 for mega.  Your answer then becomes 38 kilohms = .038 megohms.

FRAME

NO.  126	PROBLEM:

Fill in the blank with the proper value.

15,000 Ω= _______ k Ω

2-13	IT 0332

FRAME

NO.  127	ANSWER: 15 k Ω

Solution:	15,000 Ω = 15,000 X 100 Ω = 15 X 103 Ω= 15 k Ω

NOTE:	100 to 103 is a POSITIVE 3 change in exponent.

FRAME

NO.  128	PROBLEM:

Fill in the blocks.

Numerical Value	Prefix	Abbreviation	Power of 10

.000000000001

.000001

.001

1

1,000

1,000,000

IT 0332	2-14

FRAME

NO.  129	ANSWER:

Numerical Value	Prefix	Abbreviation	Power of 10

.000000000001	pico	p	10-12

.000001	micro	µ	10-6

.001	milli	m	10-3

1	none	none	100

1,000	kilo	k	103

1,000,000	mega	M	106

FRAME

NO.  130	Study the problem below, then continue.

30 kV = 5 ___________ Ω

6 mA

Solution:	Substitute 103 for k and 10-3 for m; complete division of powers of 10 by inserting proper power of 10 in blank; substitute metric prefix in the blank.

Thus:	30 X 103 V = 5 X 106 A = 5 M Ω

6 X 10-3 A

FRAME

NO.  131	PROBLEM:

Fill in the blank with the proper metric prefix.

3 M Ω X 300 µ A = 900 _______________ V

2-15	IT 0332

FRAME

NO.  132	ANSWER: 900 V

Solution:

3 M Ω X 300 µ A = 3 X 106 Ω X 300 X 10-6 Ω = 900 X 100 V =

900 X 1 V = 900 V

NOTE:	There is no metric prefix for 100 power; therefore, the numerical value of one (1) is substituted for 100 power and 900 X 1 is 900.

FRAME

NO.  133	PROBLEM:

Fill in the blanks with the proper values.

33 K  Ω = _______ M Ω

2,400 Ω = _______ k Ω

4  M   Ω = _______ Ω

IT 0332	2-16

FRAME

NO.  134	ANSWER: .033 M Ω

Solution: 33 k Ω = .033 M Ω	Converting k to M is a +3 exponent change.

ANSWER: 2.4 k Ω

Solution: 2,400 Ω  = 2.4 k Ω	Converting basic units to k is a +3 exponent change.

ANSWER: 4,000,000 Ω

Solution: 4 M Ω = 4,000,000 Ω	Converting M to basic units is a -6 exponent change.

FRAME

NO.  135	PROBLEM:

Fill in the blanks with the proper metric prefixes.

3 k Ω X 9 µ A = 27 _______ V

25 k V = 5 ______ Ω

5 mA

2-17	IT 0332

FRAME

NO 136	ANSWER: m

Solution:

3 k Ω X 9  µ A = 3 X 103 Ω  X 9 X 10-6 A = 27 X 10-3 = 27 mV

ANSWER: M

Solution: 25 kV = 25 X 103 V = 5 X 106 Ω = 5 M Ω

5mA	5 X 10-3 A

FRAME

NO.  137	PROBLEM:

Fill in the blanks with the proper values.

30 mV = _______________ V

350 pV =  ______________µ V

.04 mA = _____________ µ A

IT 0332	2-18

FRAME

NO.  138	ANSWER: .030 V

.000350 µ V

40 µ A

You have now completed this lesson.  Review the objectives.  If you do not understand the lesson, return to the frames which gave you trouble and repeat the examples given.  Review this lesson completely before taking the examination on Page E-1.

2-19	IT 0332