STP 9-63B14-SM-TG

SOLDIER'S MANUAL and TRAINER'S GUIDE

MOS 63B

LIGHT WHEELED VEHICLE MECHANIC

Skill Levels 1, 2, 3 and 4

_________________________

DISTRIBUTION RESTRICTION: Approved for public release; distribution is unlimited.

DESTRUCTION NOTICE:  Destroy by any means that leaves contents unreadable.

HEADQUARTERS, DEPARTMENT OF THE ARMY

THIS PAGE INTENTIONALLY LEFT BLANK

SOLDIER TRAINING                                                                                    HEADQUARTERS

PUBLICATION                                                                                              DEPARTMENT OF THE ARMY

No. 9-63B14-SM-TG                                                                                     Washington, DC, 23 June 2001

SOLDIER'S MANUAL and TRAINER'S GUIDE

MOS 63B

LIGHT WHEELED VEHICLE MECHANIC

Skill Levels 1, 2, 3 and 4

TABLE OF CONTENTS

PAGE

Table of Contents	i

PREFACE	vii

Chapter 1.  Introduction	1-1

Chapter 2.  Trainer's Guide	2-1

2-1.  General	2-1

2-2.  Subject Area Codes	2-3

2-3.  Duty Position Training Requirements	2-4

2-4.  Critical Tasks List	2-5

Chapter 3.  MOS/Skill Level Tasks	3-1

DISTRIBUTION RESTRICTION: Approved for public release; distribution is unlimited.

DESTRUCTION NOTICE:  Destroy by any means that leaves contents unreadable.

Supersedes STP 9-63B12-SM-TG, dated 17 September 1990, and STP 9-63B35 SM-TG, dated 3 October  1990.

Skill Level 1

Subject Area 1: ENGINE

091-63B-1001  Service Engine Assembly on a Light Wheeled Vehicle	3-1

091-63B-1003  Replace Engine Oil Filter on a Light Wheeled Vehicle	3-2

Subject Area 2: ENGINE LUBRICATION SYSTEM

091-63B-1005  Correct Malfunction of Engine Oil Cooler and Lines on a Light Wheeled Vehicle	3-3

Subject Area 3: FUEL SYSTEM

091-63B-1007  Troubleshoot Fuel System Malfunctions on a Light Wheeled Vehicle	3-4

091-63B-1009  Correct Malfunction of Fuel Pump on a Light Wheeled Vehicle	3-5

091-63B-1012  Replace Fuel Fitting and Lines on a Light Wheeled Vehicle	3-6

091-63B-1013  Replace Fuel Tank on a Light Wheeled Vehicle	3-7

091-63B-1014  Replace Fuel Filter Assembly on a Light Wheeled Vehicle	3-8

091-63B-1015  Troubleshoot Glow Plug System on a Light Wheeled Vehicle	3-9

091-63B-1016  Correct Malfunction of Glow Plug System on a Light Wheeled Vehicle	3-10

Subject Area 4: EXHAUST SYSTEM

091-63B-1021  Troubleshoot Exhaust System Malfunctions on a Light Wheeled Vehicle	3-11

091-63B-1022  Replace  Muffler on a Light Wheeled Vehicle	3-12

091-63B-1023  Replace Crossover Pipe on a Light Wheeled Vehicle	3-13

Subject Area 5: COOLING SYSTEM

091-63B-1025  Troubleshoot Cooling System Malfunctions on a Light Wheeled Vehicle	3-14

091-63B-1026  Replace Radiator on a Light Wheeled Vehicle	3-15

091-63B-1029  Replace Radiator Hoses, Lines and Clamps on a Light Wheeled Vehicle	3-16

091-63B-1031  Correct Malfunction of Fan and Drive on a Light Wheeled Vehicle	3-17

091-63B-1033  Correct Malfunction of Drive Belts on a Light Wheeled Vehicle	3-19

Subject Area 6: ELECTRICAL SYSTEM

091-63B-1036  Troubleshoot Charging System Malfunction on a Light Wheeled Vehicle	3-20

091-63B-1037  Correct Malfunction of Alternator on a Light Wheeled Vehicle	3-21

091-63B-1038  Troubleshoot Starting System Malfunction on a Light Wheeled Vehicle	3-22

091-63B-1039  Replace Starter on a Light Wheeled Vehicle	3-23

091-63B-1041  Troubleshoot Electrical System Malfunctions on a Light Wheeled Vehicle	3-24

091-63B-1044  Replace Protective Control Box on a Light Wheeled Vehicle	3-25

091-63B-1047  Correct Malfunction of Sending Units and Warning Switches on a Light Wheeled Vehicle	3-26

091-63B-1050  Correct Malfunction of Batteries on a Light Wheeled Vehicle	3-27

Subject Area 7: INSTRUMENT PANEL

091-63B-1053  Troubleshoot Electrical Gauges on a Light Wheeled Vehicle	3-28

Subject Area 8: WIRING HARNESS

091-63B-1055  Repair Engine Wiring Harness on a Light Wheeled Vehicle	3-29

091-63B-1057  Repair Chassis Wiring Harness on a Light Wheeled Vehicle	3-30

Subject Area 9: TRANSMISSION

091-63B-1058  Troubleshoot Transmission Malfunctions on a Light Wheeled Vehicle	3-31

091-63B-1059  Service Transmission Assembly on a Light Wheeled Vehicle	3-32

091-63B-1061  Replace Neutral Safety Switch on a Light Wheeled Vehicle	3-33

Subject Area 10: TRANSFER

091-63B-1066  Troubleshoot Transfer Malfunctions on a Light Wheeled Vehicle	3-34

Subject Area 11: PROPELLER SHAFTS

091-63B-1075  Replace Propeller Shafts on a Light Wheeled Vehicle	3-35

091-63B-1076  Replace Universal Joints on a Light Wheeled Vehicle	3-36

091-63B-1077  Replace Center Bearings on a Light Wheeled Vehicle	3-37

Subject Area 12: AXLES

091-63B-1078  Troubleshoot Axle Malfunctions on a Light Wheeled Vehicle	3-38

091-63B-1081  Replace Front Axle Spindle on a Light Wheeled Vehicle	3-39

091-63B-1082  Replace Halfshaft on a Light Wheeled Vehicle	3-40

091-63B-1083  Correct Malfunction of Knuckle and Geared Hub on a Light Wheeled Vehicle	3-41

091-63B-1084  Adjust Geared Hub Spindle Bearing on a Light Wheeled Vehicle	3-42

091-63B-1088  Replace Upper and Lower Ball Joints on a Light Wheeled Vehicle	3-43

091-63B-1091  Replace Dust Boot (CV) on a Light Wheeled Vehicle	3-44

Subject Area 13: BRAKES

091-63B-1097  Troubleshoot Brake System Malfunctions	3-45

091-63B-1098  Replace Brake Lines and Fittings on a Light Wheeled Vehicle	3-47

091-63B-1100  Replace Hand  Brake Shoes on a Light Wheeled Vehicle	3-48

091-63B-1105  Replace Service Brake Shoes on a Light Wheeled Vehicle	3-49

091-63B-1106  Replace Front and Rear Calipers on a Light Wheeled Vehicle	3-50

091-63B-1107  Replace Front and Rear Brake Pads on a Light Wheeled Vehicle	3-51

091-63B-1108  Replace Front and Rear Brake Rotors on a Light Wheeled Vehicle	3-52

091-63B-1109  Replace Master Cylinder on a Light Wheeled Vehicle	3-53

091-63B-1110  Replace Air Hydraulic Cylinder on a Light Wheeled Vehicle	3-54

091-63B-1112  Replace Treadle Valve on a Light Wheeled Vehicle	3-55

091-63B-1114  Replace Hydro-Boost on a Light Wheeled Vehicle	3-56

091-63B-1117  Replace Air Compressor and  Belts on a Light Wheeled Vehicle	3-57

091-63B-1124  Inspect Air Brake Control Valves on a Light Wheeled Vehicle	3-58

Subject Area 14: WHEELS AND HUBS

091-63B-1129  Correct Malfunction of  Wheel and Tire Assembly on a Light Wheeled Vehicle	3-59

Subject Area 15: STEERING

091-63B-1139  Troubleshoot Steering System Malfunctions on a Light Wheeled  Vehicle	3-60

091-63B-1141  Correct Malfunction of Tie Rod Assembly on a Light Wheeled Vehicle	3-61

091-63B-1142  Correct Malfunction of Drag Link Assembly  on a Light Wheeled Vehicle	3-62

091-63B-1143  Correct Malfunction of  Power Assist Cylinder on a Light Wheeled Vehicle	3-63

091-63B-1154  Replace Power Steering Lines and Fittings on a Light Wheeled Vehicle	3-64

Subject Area 16: SPRINGS AND SHOCKS

091-63B-1161  Replace Shock Absorbers on a Light Wheeled Vehicle	3-65

Subject Area 17: BODY, HOOD, AND CAB

091-63B-1172  Replace Seat Belt on a Light Wheeled Vehicle	3-66

Subject Area 18: HOIST, WINCH, AND POWER TAKE OFF

091-63B-1191  Troubleshoot Winch Malfunction on a Light Wheeled Vehicle	3-67

Subject Area 19: SPECIAL PURPOSE KITS

091-63B-1213  Correct Malfunction of 100 AMP Alternator on a Light Wheeled Vehicle	3-69

Subject Area 20: CENTRAL TIRE INFLATION SYSTEM (CTIS)

091-63B-1218  Troubleshoot Central Tire Inflation System on a Light Wheeled Vehicle	3-70

091-63B-1219  Replace Air Lines and Fittings on a Light Wheeled Vehicle	3-71

091-63B-1220  Correct Malfunction of Air Dryer With Filter on a Light Wheeled Vehicle	3-72

091-63B-1224  Replace CTIS Pressure Switch on a Light Wheeled Vehicle	3-73

091-63B-1226  Correct Malfunction of CTIS Front and Rear Air Seals on a Light Wheeled Vehicle	3-74

Subject Area 21: GENERAL MAINTENANCE TASKS

091-63B-1228  Maintain Test, Measurement, and Diagnostic Equipment on a Light Wheeled Vehicle	3-75

091-63B-1229  Maintain Assigned Vehicle	3-76

091-63B-1230  Maintain Assigned Tool Kit	3-77

091-63B-1231  Prepare Equipment Inspection Maintenance Worksheet (DA Form 2404 or ULLS Equivalent)	3-78

091-63B-1234  Perform Scheduled Preventive Maintenance Checks and Services on a Light Wheeled Vehicle	3-79

Subject Area 22: RECOVERY  (ASI H8 Tasks ONLY)

091-H8C-2001  Locate a Recovery Site	3-80

091-H8C-2002  Determine Recovery Methods	3-81

091-H8C-2003  Operate Tactical Communications Equipment	3-82

091-H8C-2004  Operate Metal Cutting Equipment	3-83

091-H8W-2001  Perform Preventive Maintenance Checks And Services (PMCS) On Wheeled Recovery Vehicle	3-84

091-H8W-2002  Use And Maintain Basic Issue Items (BII) Related To Wheeled Recovery Operations	3-85

091-H8W-2003  Drive Wheeled Recovery Vehicle	3-86

091-H8W-2004  Operate Boom/Hoist, Wheeled Recovery Vehicle	3-87

091-H8W-2005  Operate The Retrieval System on a Wheeled Vehicle	3-88

091-H8W-2006  Operate Winches on a Wheeled Recovery Vehicle	3-89

091-H8W-2007  Recover a Mired Wheeled Vehicle	3-90

091-H8W-2008  Recover an Overturned Vehicle	3-91

091-H8W-2009  Tow a Wheel Vehicle Using a Retrieval System	3-92

091-H8W-2010  Tow a Wheel Vehicle Using the Boom and Tow Bar	3-93

091-H8W-2011  Perform Self Recovery On A Wheeled Vehicle	3-94

091-H8W-2012  Perform Field Expedient Recovery on a Wheeled Vehicle	3-95

Skill Level 3

Subject Area 23: COMMON LOGISTIC TASKS (SL 3)

091-CLT-3001  Manage a Shop Safety Program	3-96

091-CLT-3002  Maintain a Publications Library	3-97

091-CLT-3003  Establish Maintenance Facilities	3-99

091-CLT-3004  Assist in Preparing a Standing Operating Procedure	3-100

091-CLT-3005  Manage Tool Control Procedures	3-101

091-CLT-3006  Manage Key Control Procedures	3-102

091-CLT-3007  Manage the TMDE Calibration Program	3-103

091-CLT-3008  Recon Terrain/Route	3-104

091-CLT-3009  Supervise Maintenance Operations	3-105

091-CLT-3010  Interpret Maintenance Operational Overlay	3-107

091-CLT-3013  Manage the Unit Level Logistics System (ULLS)	3-108

091-CLT-3014  Manage the Unit Army Oil Analysis Program (AOAP)	3-109

091-CLT-3015  Deploy Company Maintenance Team/Recovery Support Team	3-110

091-CLT-3016  Review the Army Materiel Status System (AMSS) Reports	3-111

Subject Area 24: TECHNICAL TASKS (SL 3)

091-63B-3001  Perform Diagnostic Procedures of  Track Vehicle's Fire Extinguisher/Suppression System	3-112

091-63B-3002  Perform Diagnostic Procedures of Track Vehicle's NBC System	3-113

091-63B-3003  Perform Diagnostic Procedures of Vehicle's Fuel System	3-114

091-63B-3004  Perform Diagnostic Procedures of  Vehicle's Electrical System	3-115

091-63B-3005  Perform Diagnostic Procedures of Diesel Engines	3-117

091-63B-3006  Perform Diagnostic Procedures of Vehicle Cooling System	3-118

091-63B-3007  Perform Diagnostic Procedures on Track Vehicle Transmission	3-120

091-63B-3009  Perform Diagnostic Procedures on  Wheel Vehicle Transmission	3-121

091-63B-3011  Perform Diagnostic Procedures on Track Vehicle's Brake System	3-122

091-63B-3012  Perform Diagnostic Procedures on Wheel Vehicle's Brake System	3-123

091-63B-3015  Perform Diagnostic Procedures on Track Vehicle's Steering Systems	3-124

091-63B-3016  Perform Diagnostic Procedures on Wheel Vehicle's Steering Systems	3-125

091-63B-3017  Perform Diagnostic Procedures on  Vehicle's Hydraulic  Systems	3-126

091-63B-3021  Perform Battlefield Damage Assessment and Repair (BDAR) on Tracked Vehicles	3-127

091-63B-3022  Perform Battlefield Damage Assessment and Repair (BDAR) on Wheeled Vehicles	3-128

091-63B-3033  Perform Diagnostic Procedures of  Vehicle's Winch System	3-129

091-63B-3050  Perform Diagnostic Procedures on  Wheel Vehicle's Air System	3-130

091-63B-3057  Perform Diagnostic Procedures on  M113A3 Steering Braking Controls	3-131

091-63B-3058  Perform Diagnostic Procedures on M578 Hydraulic System	3-132

091-63B-3062  Perform Diagnostic Procedures on M88A1/M88A2 Hydraulic System	3-133

091-63B-3064  Perform Diagnostic Procedures on M911 Air System	3-134

091-63B-3071  Perform Diagnostic Procedures on M936A2WW/M1089 Hydraulic System	3-135

091-63B-3084  Perform Diagnostic Procedures on Material Handling Equipment (MHE) Hydraulic System	3-136

091-63B-3088  Perform Diagnostic Procedures on Material Handling Equipment (MHE)Electrical System	3-137

091-63B-3092  Perform Diagnostic Procedures on Armored Vehicle Launched Bridge (AVLB) Hydraulic Systems	3-138

091-63B-3099  Perform Diagnostic Procedures on M984A1WW Hydraulic System	3-139

091-63B-3103  Perform Diagnostic Procedures on M1074 Trailer Brake	3-140

091-63B-3104  Perform Diagnostic Procedures on M1074 Hydraulic System	3-141

091-63B-3125  Perform Diagnostic Procedures on M1000 Suspension System	3-142

091-63B-3127  Perform Diagnostic Procedures on M1000 Steering System	3-143

091-63B-3128  Perform Diagnostic Procedures on Wheel Vehicle Central Tire Inflation System (CTIS)	3-144

091-63B-3129  Perform Diagnostic Procedures on M984A1 Electrical  System	3-145

091-63B-3130  Perform Diagnostic Procedures on M1070 Fuel System	3-146

091-63B-3131  Perform Diagnostic Procedures on M1000 Hydraulic System	3-147

091-63B-3132  Lift and Tow a Disabled Vehicle	3-148

091-63B-3133  Determine Recovery Method	3-149

091-63B-3200  Recover an Overturned Vehicle	3-150

091-63B-3330  Operate Oxyacetylene Equipment	3-151

Skill Level 4

Subject Area 25: COMMON LOGISTIC TASKS (SL 4)

091-CLT-4001  Perform Senior Rater Responsibilities for a Maintenance Section	3-152

091-CLT-4002  Supervise Platoon/Section Administrative Procedures	3-153

091-CLT-4003  Manage Combat Stress	3-154

091-CLT-4004  Ensure Maintenance Operations are in Compliance With the Army Environmental Program	3-155

091-CLT-4005  Enforce Compliance With the Shop Safety Program	3-156

091-CLT-4006  Coordinate Support for the Maintenance Platoon/Section	3-157

091-CLT-4007  Select a Field Maintenance Site	3-158

091-CLT-4008  Prepare an Operational Overlay for Maintenance Operations	3-159

091-CLT-4009  Control Flow of Work Through the Maintenance Shop	3-159

091-CLT-4010  Integrate Automated Logistics Support Systems	3-159

091-CLT-4011  Plan Logistics Support for Maintenance Operations	3-159

091-CLT-4012  Monitor the Preparation and Disposition of the Army Materiel Status System (AMSS) Reports	3-159

091-CLT-4013  Analyze the Prescribed Load List (PLL) Report	3-159

091-CLT-4014  Monitor Quality Control Program	3-159

091-CLT-4015  Analyze Bench Stock Listing	3-159

091-CLT-4016  Analyze Open Work Request Reconciliation Listing	3-159

091-CLT-4017  Analyze Completed Shop Workload Summary	3-159

091-CLT-4018  Analyze Shop Deadline and Deferred Workload Listing	3-159

091-CLT-4019  Analyze Shop Workload Summary Listing	3-159

091-CLT-4020  Maintain Property Accountability	3-159

091-CLT-4021  Prepare Standing Operating Procedures for Maintenance Operations	3-159

091-CLT-4022  Supervise the Deployment of Company Maintenance Team/Recovery Support Team/Maintenance Support Team	3-159

091-CLT-4023  Conduct a Route Reconnaissance for a Maintenance Mission	3-159

091-CLT-4024  Conduct an Area Reconnaissance for a Maintenance Mission	3-159

091-CLT-4025  Manage Battlefield Maintenance Support	3-159

091-CLT-4026  Perform Support Operations NCO Duties	3-159

091-CLT-4027  Manage Maintenance Operations at a Maintenance Collection Point	3-159

091-CLT-4028  Provide Maintenance Support During Tactical Operations	3-159

APPENDIX A	A-159

APPENDIX B	B-159

Glossary	Glossary-159

Supporting References	References-159

PREFACE

This soldier training publication (STP) is intended for soldiers holding MOS 63B, Skill Levels 1,  2, 3, and 4, their supervisors, trainers, and commanders.  It contains an MOS Training Plan providing information needed to plan, conduct, and evaluate unit training, one of the most important jobs of military leaders.  It includes standardized training objectives in the form of task summaries that can be used to train and evaluate soldiers on critical tasks supporting unit missions during wartime.

Soldiers holding MOS 63B should have access to this publication.  Trainers and first line supervisors should actively plan for soldiers’ access, making it available in work areas, unit learning centers, and unit libraries.  However, it is not intended for an individual copy to be provided to each MOS holder.  The STP is obtainable on line from the Reimer Digital Library (RDL) at www.adtdl.army.mil.

Tasks in this manual apply to both Active and Reserve Component soldiers.

The proponent of this publication is CASCOM. Submit comments and recommendations on DA Form 2028 (Recommended Changes to Publications and Blank Forms) directly to: Department of the Army, Training Directorate, Ordnance Training Division, ATTN: ATCL-AO, 401 First Street, Suite 227, Fort Lee, VA 23801-1511.

Unless this publication states otherwise, masculine nouns and pronouns do not refer exclusively to men.

THIS PAGE INTENTIONALLY LEFT BLANK

1CHAPTER 1

Introduction

1-1.  General.  This soldier training publication (STP) identifies individual MOS training requirements for soldiers holding MOS 63B. Commanders, trainers, and soldiers should use it to plan, conduct, and evaluate individual training in units.  The STP is the primary MOS reference for supporting self-development, evaluating MOS proficiency, and training of 63B soldiers. Commanders employ two primary methods to evaluate soldiers' proficiency:

	Commander's evaluation.  Commander’s evaluations are local tests or assessments of soldiers' performance of MOS-specific and common tasks critical to the unit mission. They may be conducted year-round.

	Common task test (CTT).  CTTs are hands-on tests used to evaluate proficiency on common tasks.  Alternate written tests are provided if equipment is not available for hands-on testing.

This publication is the soldier's primary reference to prepare for a commander's evaluation of MOS-specific tasks.  It contains task summaries for all critical tasks specific to the MOS and skill level (SL).  Commanders and trainers will use this soldier's manual/trainer's guide (SM/TG) to plan and conduct training and commander's evaluations.

Chapter 2, Training Guide, contains information needed to plan training requirements for this MOS.  The trainer's guide

	Identifies subject areas in which soldiers must be trained.

	Identifies critical tasks for each subject area.

	Specifies where soldiers are initially trained on each task.

	Recommends how often each task should be trained to sustain proficiency.

	Recommends a strategy for cross-training soldiers.

	Recommends a strategy for training soldiers to perform higher-level tasks.

Use this STP along with STP 21-1-SMCT (Soldier’s Manual of Common Tasks, Skill Level 1), STP 21-24-SMCT (Soldier’s Manual of Common Tasks, Skill Levels 2-4), Army training and evaluation programs (ARTEPs), FM 25-4 (How to Conduct Training Exercises), FM 25-5 (Training for Mobilization and War), FM 25-100 (Training the Force), and FM 25-101 (Battle-Focused Training) to establish effective training plans and programs that integrate soldier, leader, and collective tasks.

1-2.  Task Summaries.  Task summaries outline wartime performance requirements for each critical task in the STP.  They provide both soldier and trainer with the information necessary to prepare, conduct, and evaluate critical task training.  As a minimum, task summaries include information soldiers must know and skills they must perform to standard for each task.  Following is the task summary format:

	Task number.  The task number is a 10-digit number that identifies the task, MOS and skill level.  Include the task number and title in any correspondence relating to the task.

	Task title.  The task title identifies the action to be performed.

	Conditions.  The task conditions statement describes the field or garrison conditions under which the task will be performed and identifies the equipment, tools, references, job aids, and supporting personnel that the soldier needs to perform the task in wartime.

	Standards.  The task standards describe how well and to what level of proficiency the soldier must perform the task under wartime conditions.  Standards are typically expressed in terms of accuracy, completeness, duration, sequence, speed, and tolerance.

	Performance measures.  This section identifies specific actions that the soldier must accomplish to complete the task successfully.  Performance measures appear in a GO/NO GO rating format for easy evaluation.  Some tasks may also include detailed training information in a Training Information Outline and an Evaluation Preparation Section.  The Evaluation Preparation Section indicates necessary modifications to task performance in order to train and evaluate a task that can not be trained to the wartime standard under wartime conditions.  It may also include special training and evaluation preparation instructions to accommodate these modifications and any instructions that should be given to the soldier before evaluation.

	References.  This section identifies references that provide more detailed explanations of task performance requirements than are given in the task summary.

	Warnings.  Warnings alert users to the possibility of immediate personal injury or equipment damage.

	Notes.  Notes provide additional supportive explanations or tips relating to task

performance.

1-3.  Soldier’s Responsibilities.  Each soldier is responsible for performing individual tasks identified by the first-line supervisor based on the unit’s mission-essential task list (METL).  Soldiers must perform tasks to the standards included in the task summary.  If soldiers have questions about tasks or which tasks in this manual they must perform, they are responsible for asking their first-line supervisor for clarification.  First-line supervisors know how to perform each task or can direct soldiers to appropriate training materials, including current field manuals, technical manuals, and Army regulations.  Soldiers are responsible for using these materials to maintain performance.  They are also responsible for maintaining performance of all common tasks listed in the SMCTs at their current skill level and below.

Periodically, soldiers should ask their supervisor or another solder to check their performance to ensure that they can perform the tasks.

1-4.  NCO Self-Development and the STP.  Self-development is a key component of leader development.  Leaders follow planned, progressive, sequential self-development programs developed by the individual NCO and his or her first-line supervisor to enhance and sustain military competencies.  Self-development consists of individual study, research, professional reading, practice, and self-assessment.  The self-development concept requires NCOs, as Army professionals, to take responsibility for remaining current in all phases of their MOS.  The STP is the NCO’s primary source for maintaining MOS proficiency.

1-5.  Commander’s Responsibilities.  Commanders must ensure that their unit training plans prepare the unit for war by enabling soldiers to develop and sustain proficiency in their MOS and skill level tasks.  Commanders should design unit training programs to provide individual training for all soldiers assigned to the unit and to evaluate soldier proficiency routinely as part of the commander’s evaluation program.  The unit training program should also integrate individual training with crew drills and other collective training.  The MOS training plan provides information on which to base integration, cross-train, train-up, and sustainment training programs.  Commanders should use the MOS training plan when developing unit training plans.

1-6.  Trainer’s Responsibilities.  Training is the business of all unit leaders.  First-line leaders are the principal trainers in the unit because they directly supervise soldiers and lead crews, squads, sections, and teams.

Trainers can use the MOS training plan to determine the critical tasks each soldier is responsible for.  They should tell each soldier which tasks he or she must be able to perform.  Trainers should evaluate task performance to determine which tasks each soldier can or cannot perform to standard.  Soldiers who cannot perform a task to standard need further training.  Developing effective training is explained in detail in FM 25-100 and FM 25-101.

Every task summary in this STP includes performance measures, which trainers may use year-round to determine if soldiers can perform critical tasks to the specified standards.  The performance measures identify what the trainer needs to observe to score a soldier’s performance.  A blank space is provided for the trainer to check either the GO or NO GO column for each performance measure.  Some tasks require the trainer to watch the soldier perform them (evaluate the process).  Other tasks call for the trainer to focus on the results of the soldier’s performance (evaluate the product).  Comments should not be written on the task summary.

Trainers can monitor the progress of their soldiers by recording task go/no-go results.  Trainers may use DA Form 5164-R (Hands-on Evaluation) to record the performance measures a soldier passed or failed.  The form, which may be locally reproduced, applies to all tasks in this STP.  Trainers may have DA Form 5164-R overprinted with information unique to their training requirements before reproducing it.  See Appendix A of this STP for a sample DA Form 5164-R with instructions.

	Trainers may use DA Form 5165-R (Field Expedient Squad Book) to record hands-on go/no-go results for a group of soldiers (for example, a crew, section, or squad) having the same MOS and skill level.  This form supports conduct of commander’s evaluations, and can be used to record training results gathered in the field during slack time for all MOSs and skill levels.  Use of this form is optional.  See Appendix B for a sample DA Form 5165-R with instructions.  Trainers should work with each soldier until tasks can be performed to specific task summary standards.

1-7.  Training Support.  References have been identified for each task to assist in planning and conducting training.  A consolidated list of references identified by type, publication number, and title and a comprehensive glossary of acronyms, abbreviations, and definitions are included in this STP.

CAREER PROGRESSION CHART

HEAVY WHEEL		LIGHT WHEEL	            TRACK

VEHICLE		     VEHICLE	                       VEHICLE

MECHANIC		  MECHANIC		        MECHANIC

This page intentionally left blank

2CHAPTER 2

Trainer's Guide

MOS Training Plan

MOS 63B

PART I

Duty Position Training Requirements

| Skill Level | Duty Position | Subject Area | Cross Train | Train Up/Merger |
| --- | --- | --- | --- | --- |
| SL 1/2 | Light Wheel Vehicle Mechanic *Recovery Vehicle Operator * (ASI H8) | 1-21 22 | N/A | Light Wheel Vehicle Mechanic *Recovery Vehicle Operator |
| SL 3 | Senior Wheel Vehicle Mechanic Maintenance/Recovery Supervisor/Motor Sergeant | 23 24 | N/A | Senior Mechanic Motor Sergeant |
| SL 4 | Maintenance/Recovery Supervisor/Motor Sergeant | 25 | N/A | Senior Maintenance Supervisor Motor Sergeant |

2-1.  General.  The MOS Training Plan (MTP) identifies the essential components of a unit training plan for individual training.  Units have different training needs and requirements based on differences in environment, location, equipment, dispersion, and similar factors.  Therefore, the MTP should be used as a guide for conducting unit training and not a rigid standard.  The MTP consists of two parts.  Each part is designed to assist the commander in preparing a unit training plan which satisfies integration, cross training, and sustainment training requirements for soldiers in this MOS.

Part One of the MTP shows the relationship of an MOS skill level between duty position and critical tasks.  These critical tasks are grouped by task commonality into subject areas.

Section I lists subject area numbers and titles used throughout the MTP.  These subject areas are used to define the training requirements for each duty position within an MOS.

Section II identifies the total training requirement for each duty position within an MOS and provides a recommendation for cross training and train-up/merger training.

(	Duty Position column.  This column lists the duty positions of the MOS, by skill level, which have different training requirements.

(	Subject Area column.  This column lists, by numerical key (see Section I), the subject areas a soldier must be proficient in to perform in that duty position.

(	Cross Train column.  This column lists the recommended duty position for which soldiers should be cross trained.

(	Train-up/Merger column.  This column lists the corresponding duty position for the next higher skill level or MOSC the soldier will merge into on promotion.

Part Two lists, by general subject areas, the critical tasks to be trained in an MOS and the type of training required (resident, integration, or sustainment).

(	Subject Area column.  This column lists the subject area number and title in the same order as Section I, Part One of the MTP.

(	Task Number column.  This column lists the task numbers for all tasks included in the subject area.

(	Title column.  This column lists the task title for each task in the subject area.

(	Training Location column.  This column identifies the training location where the task is first trained to soldier training publications standards.  If the task is first trained to standard in the unit, the word “Unit” will be in this column.  If the task is first trained to standard in the training base, it will identify, by brevity code (ANCOC, BNCOC, etc.), the resident course where the task was taught.  Figure 2-1 contains a list of training locations and their corresponding brevity codes.

ASI/SD	Additional Skill Identifier/Special Duty

AIT	Advanced Individual Training

UNIT	Trained in the Unit

BNCOC	Basic NCO Course

ANCOC	Advanced NCO Course

Figure 2-1.  Training Locations

(	Sustainment Training Frequency column.  This column indicates the recommended frequency at which the tasks should be trained to ensure soldiers maintain task proficiency.  Figure 2-2 identifies the frequency codes used in this column.

BA	-	Biannually

AN	-	Annually

SA	-	Semiannually

QT	-	Quarterly

MO	-	Monthly

BW	-	Bi-weekly

WK	-	Weekly

Figure 2-2.  Sustainment Training Frequency Codes

(	Sustainment Training Skill Level column.  This column lists the skill levels of the MOS for which soldiers must receive sustainment training to ensure they maintain proficiency to soldier’s manual standards.

2-2.  Subject Area Codes.

Skill Level 1

1	ENGINE

2	ENGINE LUBRICATION SYSTEM

3	FUEL SYSTEM

4	EXHAUST SYSTEM

5	COOLING SYSTEM

6	ELECTRICAL SYSTEM

7	INSTRUMENT PANEL

8	WIRING HARNESS

9	TRANSMISSION

10	TRANSFER

11	PROPELLER SHAFTS

12	AXLES

13	BRAKES

14	WHEELS AND HUBS

15	STEERING

16	SPRINGS AND SHOCKS

17	BODY, HOOD, AND CAB

18	HOIST, WINCH, AND POWER TAKE OFF

19	SPECIAL PURPOSE KITS

20	CENTRAL TIRE INFLATION SYSTEM (CTIS)

21	GENERAL MAINTENANCE TASKS

22	RECOVERY  (ASI H8 Tasks ONLY)

Skill Level 3

23	COMMON LOGISTIC TASKS (SL 3)

24	TECHNICAL TASKS (SL 3)

Skill Level 4

25	COMMON LOGISTIC TASKS (SL 4)

2-3.  Duty Position Training Requirements.

See  Chapter 2, Training Guide

2-4.  Critical Tasks List.

MOS TRAINING PLAN

63B14

| CRITICAL TASKS |
| --- |
| Subject Area | Task Number | Title | Training Location | Sust Tng Freq | Sust Tng SL |
| Skill Level 1 |
| 1. ENGINE | 091-63B-1001 | Service Engine Assembly on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
|  | 091-63B-1003 | Replace Engine Oil Filter on a Light Wheeled Vehicle | UNIT | QT | 1-2 |
| 2. ENGINE LUBRICATION SYSTEM | 091-63B-1005 | Correct Malfunction of Engine Oil Cooler and Lines on a Light Wheeled Vehicle | AIT | QT | 1-2 |
| 3. FUEL SYSTEM | 091-63B-1007 | Troubleshoot Fuel System Malfunctions on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1009 | Correct Malfunction of Fuel Pump on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1012 | Replace Fuel Fitting and Lines on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1013 | Replace Fuel Tank on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
|  | 091-63B-1014 | Replace Fuel Filter Assembly on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
|  | 091-63B-1015 | Troubleshoot Glow Plug System on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1016 | Correct Malfunction of Glow Plug System on a Light Wheeled Vehicle | AIT | SA | 1-2 |
| 4. EXHAUST SYSTEM | 091-63B-1021 | Troubleshoot Exhaust System Malfunctions on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
|  | 091-63B-1022 | Replace Muffler on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
|  | 091-63B-1023 | Replace Crossover Pipe on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
| 5. COOLING SYSTEM | 091-63B-1025 | Troubleshoot Cooling System Malfunctions on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1026 | Replace Radiator on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1029 | Replace Radiator Hoses, Lines and Clamps on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1031 | Correct Malfunction of Fan and Drive on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1033 | Correct Malfunction of Drive Belts on a Light Wheeled Vehicle | AIT | SA | 1-2 |
| 6. ELECTRICAL SYSTEM | 091-63B-1036 | Troubleshoot Charging System Malfunction on a Light Wheeled Vehicle | AIT | SA | 1-3 |
|  | 091-63B-1037 | Correct Malfunction of Alternator on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1038 | Troubleshoot Starting System Malfunction on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1039 | Replace Starter on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1041 | Troubleshoot Electrical System Malfunctions on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1044 | Replace Protective Control Box on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1047 | Correct Malfunction of Sending Units and Warning Switches on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1050 | Correct Malfunction of Batteries on a Light Wheeled Vehicle | AIT | SA | 1-3 |
| 7. INSTRUMENT PANEL | 091-63B-1053 | Troubleshoot Electrical Gauges on a Light Wheeled Vehicle | AIT | SA | 1-2 |
| 8. WIRING HARNESS | 091-63B-1055 | Repair Engine Wiring Harness on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1057 | Repair Chassis Wiring Harness on a Light Wheeled Vehicle | AIT | SA | 1-2 |
| 9. TRANSMISSION | 091-63B-1058 | Troubleshoot Transmission Malfunctions on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
|  | 091-63B-1059 | Service Transmission Assembly on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
|  | 091-63B-1061 | Replace Neutral Safety Switch on a Light Wheeled Vehicle | AIT | SA | 1-2 |
| 10. TRANSFER | 091-63B-1066 | Troubleshoot Transfer Malfunctions on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
| 11. PROPELLER SHAFTS | 091-63B-1075 | Replace Propeller Shafts on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1076 | Replace Universal Joints on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1077 | Replace Center Bearings on a Light Wheeled Vehicle | AIT | SA | 1-2 |
| 12. AXLES | 091-63B-1078 | Troubleshoot Axle Malfunctions on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
|  | 091-63B-1081 | Replace Front Axle Spindle on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
|  | 091-63B-1082 | Replace Halfshaft on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1083 | Correct Malfunction of Knuckle and Geared Hub on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1084 | Adjust Geared Hub Spindle Bearing on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1088 | Replace Upper and Lower Ball Joints on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
|  | 091-63B-1091 | Replace Dust Boot (CV) on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
| 13. BRAKES | 091-63B-1097 | Troubleshoot Brake System Malfunctions | AIT | SA | 1-2 |
|  | 091-63B-1098 | Replace Brake Lines and Fittings on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1100 | Replace Hand Brake Shoes on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1105 | Replace Service Brake Shoes on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1106 | Replace Front and Rear Calipers on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1107 | Replace Front and Rear Brake Pads on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1108 | Replace Front and Rear Brake Rotors on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1109 | Replace Master Cylinder on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1110 | Replace Air Hydraulic Cylinder on a Light Wheeled Vehicle | AIT | AN | 1-2 |
|  | 091-63B-1112 | Replace Treadle Valve on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
|  | 091-63B-1114 | Replace Hydro-Boost on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1117 | Replace Air Compressor and Belts on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
|  | 091-63B-1124 | Inspect Air Brake Control Valves on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
| 14. WHEELS AND HUBS | 091-63B-1129 | Correct Malfunction of Wheel and Tire Assembly on a Light Wheeled Vehicle | AIT | SA | 1-2 |
| 15. STEERING | 091-63B-1139 | Troubleshoot Steering System Malfunctions on a Light Wheeled Vehicle | AIT | SA | 1-3 |
|  | 091-63B-1141 | Correct Malfunction of Tie Rod Assembly on a Light Wheeled Vehicle | AIT | SA | 1-3 |
|  | 091-63B-1142 | Correct Malfunction of Drag Link Assembly on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
|  | 091-63B-1143 | Correct Malfunction of Power Assist Cylinder on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1154 | Replace Power Steering Lines and Fittings on a Light Wheeled Vehicle | AIT | SA | 1-2 |
| 16. SPRINGS AND SHOCKS | 091-63B-1161 | Replace Shock Absorbers on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
| 17. BODY, HOOD, AND CAB | 091-63B-1172 | Replace Seat Belt on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
| 18. HOIST, WINCH, AND POWER TAKE OFF | 091-63B-1191 | Troubleshoot Winch Malfunction on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
| 19. SPECIAL PURPOSE KITS | 091-63B-1213 | Correct Malfunction of 100 AMP Alternator on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
| 20. CENTRAL TIRE INFLATION SYSTEM (CTIS) | 091-63B-1218 | Troubleshoot Central Tire Inflation System on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1219 | Replace Air Lines and Fittings on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1220 | Correct Malfunction of Air Dryer With Filter on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1224 | Replace CTIS Pressure Switch on a Light Wheeled Vehicle | UNIT | SA | 1-2 |
|  | 091-63B-1226 | Correct Malfunction of CTIS Front and Rear Air Seals on a Light Wheeled Vehicle | AIT | SA | 1-2 |
| 21. GENERAL MAINTENANCE TASKS | 091-63B-1228 | Maintain Test, Measurement, and Diagnostic Equipment on a Light Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-63B-1229 | Maintain Assigned Vehicle | UNIT | SA | 1-2 |
|  | 091-63B-1230 | Maintain Assigned Tool Kit | AIT | SA | 1-2 |
|  | 091-63B-1231 | Prepare Equipment Inspection Maintenance Worksheet (DA Form 2404 or ULLS Equivalent) | AIT | SA | 1-2 |
|  | 091-63B-1234 | Perform Scheduled Preventive Maintenance Checks and Services on a Light Wheeled Vehicle | AIT | SA | 1-2 |
| 22. RECOVERY (ASI H8 Tasks ONLY) | 091-H8C-2001 | Locate a Recovery Site | ASI/SD | SA | 1/2 |
|  | 091-H8C-2002 | Determine Recovery Methods | ASI/SD | SA | 1-2 |
|  | 091-H8C-2003 | Operate Tactical Communications Equipment | ASI/SD | SA | 1-2 |
|  | 091-H8C-2004 | Operate Metal Cutting Equipment | ASI/SD | SA | 1-2 |
|  | 091-H8W-2001 | Perform Preventive Maintenance Checks And Services (PMCS) On Wheeled Recovery Vehicle | ASI/SD | AN | 1-3 |
|  | 091-H8W-2002 | Use And Maintain Basic Issue Items (BII) Related To Wheeled Recovery Operations | AIT | SA | 1-2 |
|  | 091-H8W-2003 | Drive Wheeled Recovery Vehicle | ASI/SD | SA | 1-2 |
|  | 091-H8W-2004 | Operate Boom/Hoist, Wheeled Recovery Vehicle | AIT | SA | 1-2 |
|  | 091-H8W-2005 | Operate The Retrieval System on a Wheeled Vehicle | ASI/SD | SA | 1-2 |
|  | 091-H8W-2006 | Operate Winches on a Wheeled Recovery Vehicle | AIT | SA | 1-2 |
|  | 091-H8W-2007 | Recover a Mired Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-H8W-2008 | Recover an Overturned Vehicle | ASI/SD | SA | 1-2 |
|  | 091-H8W-2009 | Tow a Wheel Vehicle Using a Retrieval System | ASI/SD | SA | 1-2 |
|  | 091-H8W-2010 | Tow a Wheel Vehicle Using the Boom and Tow Bar | ASI/SD | SA | 1-2 |
|  | 091-H8W-2011 | Perform Self Recovery On A Wheeled Vehicle | AIT | SA | 1-2 |
|  | 091-H8W-2012 | Perform Field Expedient Recovery on a Wheeled Vehicle | ASI/SD | SA | 1-2 |
| Skill Level 3 |
| 23. COMMON LOGISTIC TASKS (SL 3) | 091-CLT-3001 | Manage a Shop Safety Program | BNCOC | AN | 3 |
|  | 091-CLT-3002 | Maintain a Publications Library | BNCOC | AN | 3 |
|  | 091-CLT-3003 | Establish Maintenance Facilities | BNCOC | AN | 3 |
|  | 091-CLT-3004 | Assist in Preparing a Standing Operating Procedure | BNCOC | AN | 3 |
|  | 091-CLT-3005 | Manage Tool Control Procedures | BNCOC | AN | 3 |
|  | 091-CLT-3006 | Manage Key Control Procedures | BNCOC | AN | 3 |
|  | 091-CLT-3007 | Manage the TMDE Calibration Program | BNCOC | AN | 3 |
|  | 091-CLT-3008 | Recon Terrain/Route | BNCOC | AN | 3 |
|  | 091-CLT-3009 | Supervise Maintenance Operations | BNCOC | AN | 3 |
|  | 091-CLT-3010 | Interpret Maintenance Operational Overlay | BNCOC | AN | 3 |
|  | 091-CLT-3013 | Manage the Unit Level Logistics System (ULLS) | BNCOC | AN | 3 |
|  | 091-CLT-3014 | Manage the Unit Army Oil Analysis Program (AOAP) | BNCOC | AN | 3 |
|  | 091-CLT-3015 | Deploy Company Maintenance Team/Recovery Support Team | BNCOC | AN | 3 |
|  | 091-CLT-3016 | Review the Army Materiel Status System (AMSS) Reports | BNCOC | AN | 3 |
| 24. TECHNICAL TASKS (SL 3) | 091-63B-3001 | Perform Diagnostic Procedures of Track Vehicle's Fire Extinguisher/Suppression System | BNCOC | AN | 3-4 |
|  | 091-63B-3002 | Perform Diagnostic Procedures of Track Vehicle's NBC System | BNCOC | AN | 3-4 |
|  | 091-63B-3003 | Perform Diagnostic Procedures of Vehicle's Fuel System | BNCOC | AN | 3-4 |
|  | 091-63B-3004 | Perform Diagnostic Procedures of Vehicle's Electrical System | BNCOC | AN | 3-4 |
|  | 091-63B-3005 | Perform Diagnostic Procedures of Diesel Engines | BNCOC | AN | 3-4 |
|  | 091-63B-3006 | Perform Diagnostic Procedures of Vehicle Cooling System | BNCOC | AN | 3-4 |
|  | 091-63B-3007 | Perform Diagnostic Procedures on Track Vehicle Transmission | BNCOC | AN | 3-4 |
|  | 091-63B-3009 | Perform Diagnostic Procedures on Wheel Vehicle Transmission | BNCOC | AN | 3-4 |
|  | 091-63B-3011 | Perform Diagnostic Procedures on Track Vehicle's Brake System | BNCOC | AN | 3-4 |
|  | 091-63B-3012 | Perform Diagnostic Procedures on Wheel Vehicle's Brake System | BNCOC | AN | 3-4 |
|  | 091-63B-3015 | Perform Diagnostic Procedures on Track Vehicle's Steering Systems | BNCOC | AN | 3-4 |
|  | 091-63B-3016 | Perform Diagnostic Procedures on Wheel Vehicle's Steering Systems | BNCOC | AN | 3-4 |
|  | 091-63B-3017 | Perform Diagnostic Procedures on Vehicle's Hydraulic Systems | BNCOC | AN | 3-4 |
|  | 091-63B-3021 | Perform Battlefield Damage Assessment and Repair (BDAR) on Tracked Vehicles | BNCOC | AN | 3-4 |
|  | 091-63B-3022 | Perform Battlefield Damage Assessment and Repair (BDAR) on Wheeled Vehicles | BNCOC | AN | 3-4 |
|  | 091-63B-3033 | Perform Diagnostic Procedures of Vehicle's Winch System | BNCOC | AN | 3-4 |
|  | 091-63B-3050 | Perform Diagnostic Procedures on Wheel Vehicle's Air System | BNCOC | BA | 3-4 |
|  | 091-63B-3057 | Perform Diagnostic Procedures on M113A3 Steering Braking Controls | BNCOC | AN | 3-4 |
|  | 091-63B-3058 | Perform Diagnostic Procedures on M578 Hydraulic System | BNCOC | AN | 3-4 |
|  | 091-63B-3062 | Perform Diagnostic Procedures on M88A1/M88A2 Hydraulic System | BNCOC | AN | 3-4 |
|  | 091-63B-3064 | Perform Diagnostic Procedures on M911 Air System | BNCOC | AN | 3-4 |
|  | 091-63B-3071 | Perform Diagnostic Procedures on M936A2WW/M1089 Hydraulic System | BNCOC | AN | 3-4 |
|  | 091-63B-3084 | Perform Diagnostic Procedures on Material Handling Equipment (MHE) Hydraulic System | BNCOC | AN | 3-4 |
|  | 091-63B-3088 | Perform Diagnostic Procedures on Material Handling Equipment (MHE)Electrical System | BNCOC | AN | 3-4 |
|  | 091-63B-3092 | Perform Diagnostic Procedures on Armored Vehicle Launched Bridge (AVLB) Hydraulic Systems | BNCOC | AN | 3-4 |
|  | 091-63B-3099 | Perform Diagnostic Procedures on M984A1WW Hydraulic System | BNCOC | AN | 3-4 |
|  | 091-63B-3103 | Perform Diagnostic Procedures on M1074 Trailer Brake | BNCOC | AN | 3-4 |
|  | 091-63B-3104 | Perform Diagnostic Procedures on M1074 Hydraulic System | BNCOC | AN | 3-4 |
|  | 091-63B-3125 | Perform Diagnostic Procedures on M1000 Suspension System | BNCOC | AN | 3-4 |
|  | 091-63B-3127 | Perform Diagnostic Procedures on M1000 Steering System | BNCOC | AN | 3-4 |
|  | 091-63B-3128 | Perform Diagnostic Procedures on Wheel Vehicle Central Tire Inflation System (CTIS) | BNCOC | AN | 3-4 |
|  | 091-63B-3129 | Perform Diagnostic Procedures on M984A1 Electrical System | BNCOC | QT | 3-4 |
|  | 091-63B-3130 | Perform Diagnostic Procedures on M1070 Fuel System | BNCOC | AN | 3-4 |
|  | 091-63B-3131 | Perform Diagnostic Procedures on M1000 Hydraulic System | BNCOC | AN | 3-4 |
|  | 091-63B-3132 | Lift and Tow a Disabled Vehicle | BNCOC | AN | 3-4 |
|  | 091-63B-3133 | Determine Recovery Method | BNCOC | AN | 3-4 |
|  | 091-63B-3200 | Recover an Overturned Vehicle | BNCOC | AN | 3-4 |
|  | 091-63B-3330 | Operate Oxyacetylene Equipment | BNCOC | AN | 3-4 |
| 25. COMMON LOGISTIC TASKS (SL 4) | 091-CLT-4001 | Perform Senior Rater Responsibilities for a Maintenance Section | ANCOC | AN | 4 |
|  | 091-CLT-4002 | Supervise Platoon/Section Administrative Procedures | ANCOC | AN | 4 |
|  | 091-CLT-4003 | Manage Combat Stress | ANCOC | AN | 4 |
|  | 091-CLT-4004 | Ensure Maintenance Operations are in Compliance With the Army Environmental Program | ANCOC | AN | 4 |
|  | 091-CLT-4005 | Enforce Compliance With the Shop Safety Program | ANCOC | AN | 4 |
|  | 091-CLT-4006 | Coordinate Support for the Maintenance Platoon/Section | ANCOC | AN | 4 |
|  | 091-CLT-4007 | Select a Field Maintenance Site | ANCOC | AN | 4 |
|  | 091-CLT-4008 | Prepare an Operational Overlay for Maintenance Operations | ANCOC | AN | 4 |
|  | 091-CLT-4009 | Control Flow of Work Through the Maintenance Shop | ANCOC | AN | 4 |
|  | 091-CLT-4010 | Integrate Automated Logistics Support Systems | ANCOC | AN | 4 |
|  | 091-CLT-4011 | Plan Logistics Support for Maintenance Operations | ANCOC | AN | 4 |
|  | 091-CLT-4012 | Monitor the Preparation and Disposition of the Army Materiel Status System (AMSS) Reports | ANCOC | AN | 4 |
|  | 091-CLT-4013 | Analyze the Prescribed Load List (PLL) Report | ANCOC | AN | 4 |
|  | 091-CLT-4014 | Monitor Quality Control Program | ANCOC | AN | 4 |
|  | 091-CLT-4015 | Analyze Bench Stock Listing | ANCOC | AN | 4 |
|  | 091-CLT-4016 | Analyze Open Work Request Reconciliation Listing | ANCOC | AN | 4 |
|  | 091-CLT-4017 | Analyze Completed Shop Workload Summary | ANCOC | AN | 4 |
|  | 091-CLT-4018 | Analyze Shop Deadline and Deferred Workload Listing | ANCOC | AN | 4 |
|  | 091-CLT-4019 | Analyze Shop Workload Summary Listing | ANCOC | AN | 4 |
|  | 091-CLT-4020 | Maintain Property Accountability | ANCOC | AN | 4 |
|  | 091-CLT-4021 | Prepare Standing Operating Procedures for Maintenance Operations | ANCOC | AN | 4 |
|  | 091-CLT-4022 | Supervise the Deployment of Company Maintenance Team/Recovery Support Team/Maintenance Support Team | ANCOC | AN | 4 |
|  | 091-CLT-4023 | Conduct a Route Reconnaissance for a Maintenance Mission | ANCOC | AN | 4 |
|  | 091-CLT-4024 | Conduct an Area Reconnaissance for a Maintenance Mission | ANCOC | AN | 4 |
|  | 091-CLT-4025 | Manage Battlefield Maintenance Support | ANCOC | AN | 4 |
|  | 091-CLT-4026 | Perform Support Operations NCO Duties | ANCOC | AN | 4 |
|  | 091-CLT-4027 | Manage Maintenance Operations at a Maintenance Collection Point | ANCOC | AN | 4 |
|  | 091-CLT-4028 | Provide Maintenance Support During Tactical Operations | ANCOC | AN | 4 |

3CHAPTER 3

MOS/Skill Level Tasks

Skill Level 1

Subject Area 1: ENGINE

Service Engine Assembly on a Light Wheeled Vehicle

091-63B-1001

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Serviced  engine assembly on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission  capable, and/or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected and used the applicable publications. | —— | —— |
| 2. Followed prescribed safety procedures. | —— | —— |
| 3. Practiced maintenance discipline. | —— | —— |
| 4. Checked for leaks. | —— | —— |
| 5. Checked for proper torque of engine mounting bolts. | —— | —— |
| 6. Serviced breather, if applicable. | —— | —— |
| 7. Changed oil, if required, by service or the Army Oil Analysis Program (AOAP). | —— | —— |
| 8. Annotated Test Measurement Diagnostic Equipment (TAMMS) forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-272-12 | AR 385-10 |
| LO9-2320-280-12 | AR 750-1 |
| TM 9-2320-272-10 | AR 750-43 |
| TM 9-2320-272-24-1 | DA PAM738-750 |
| TM 9-2320-272-24-2 | TM 9-243 |
| TM 9-2320-272-24-3 | TM 9-8000 |
| TM 9-2320-272-24-4 |  |
| TM 9-2320-272-24P-1 |  |
| TM 9-2320-272-24P-2 |  |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |

Replace Engine Oil Filter on a Light Wheeled Vehicle

091-63B-1003

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced engine oil filter on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected and used applicable publications. | —— | —— |
| 2. Selected and used correct tools and/or TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed oil drain plug and drained oil in a suitable container. | —— | —— |
| 6. Inspected oil for grit, foaminess or milkiness. | —— | —— |
| 7. Installed oil drain plug to correct torque specifications. | —— | —— |
| 8. Removed oil filter. | —— | —— |
| 9. Selected correct lubricant and quantity from applicable lubrication order and replenished system. | —— | —— |
| 10. Inspected for leaks. | —— | —— |
| 11. Verified fault is corrected. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-272-12 | AR 385-10 |
| LO 9-2320-280-12 | AR 750-1 |
| TM 9-2320-272-10 | DA PAM 738-750 |
| TM 9-2320-272-24-1 | TM 9-243 |
| TM 9-2320-272-24-2 | TM 9-8000 |
| TM 9-2320-272-24-3 |  |
| TM 9-2320-272-24-4 |  |
| TM 9-2320-272-24P-1 |  |
| TM 9-2320-272-24P-2 |  |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |

Subject Area 2: ENGINE LUBRICATION SYSTEM

Correct Malfunction of Engine Oil Cooler and Lines on a Light Wheeled Vehicle

091-63B-1005

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Corrected malfunction of engine oil cooler and lines on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were  identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected and used applicable publications. | —— | —— |
| 2. Selected and used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Inspected engine oil cooler and lines for leaks. | —— | —— |
| 6. Replaced engine oil cooler and lines, if necessary. | —— | —— |
| 7. Checked for proper engine oil level. | —— | —— |
| 8. Verified fault is corrected. | —— | —— |
| 9. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-272-12 | AR 385-10 |
| LO 9-2320-280-12 | AR 750-1 |
| TM 9-2320-272-10 | AR 750-43 |
| TM 9-2320-272-24-1 | DA PAM 738-750 |
| TM 9-2320-272-24-2 | TM 9-243 |
| TM 9-2320-272-24-3 | TM 9-8000 |
| TM 9-2320-272-24-4 |  |
| TM 9-2320-272-24P-1 |  |
| TM 9-2320-272-24P-2 |  |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |

Subject Area 3: FUEL SYSTEM

Troubleshoot Fuel System Malfunctions on a Light Wheeled Vehicle

091-63B-1007

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostics on fuel system malfunctions on a light wheeled vehicle  IAW the applicable technical publications, procedures and specifications.  When this task was completed, the vehicle was fully mission-capable, or maintenance actions required to be performed by other than 63B personnel were identified

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected and used applicable publications. | —— | —— |
| 2. Selected and used correct tool/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Checked fuel level. | —— | —— |
| 6. Checked for fuel contamination. | —— | —— |
| 7. Checked for leaking fuel tank. | —— | —— |
| 8. Checked for leaking fuel lines. | —— | —— |
| 9. Checked for proper fuel pressure. | —— | —— |
| 10. Checked for proper fuel to injector. | —— | —— |
| 11. Verified fault was corrected. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| DA PAM 738-750 | AR 385-10 |
| TM 9-2320-272-10 | AR 750-1 |
| TM 9-2320-272-24-1 | AR 750-43 |
| TM 9-2320-272-24-2 | TM 9-243 |
| TM 9-2320-272-24-3 | TM 9-8000 |
| TM 9-2320-272-24-4 |  |
| TM 9-2320-272-24P-1 |  |
| TM 9-2320-272-24P-2 |  |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |

Correct Malfunction of Fuel Pump on a Light Wheeled Vehicle

091-63B-1009

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Corrected malfunction of fuel pump on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission-capable, or maintenance actions required to be performed by other than 63B personnel were identified

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Checked fuel level. | —— | —— |
| 6. Checked for kinks fuel line. | —— | —— |
| 7. Checked for clogged fuel filter. | —— | —— |
| 8. Checked for leaking fuel lines. | —— | —— |
| 9. Checked fuel pump for leaks. | —— | —— |
| 10. Replaced fuel pump. | —— | —— |
| 11. Verified fault was corrected. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-280-12 | AR 385-10 |
| TM 9-2320-280-10 | AR 750-1 |
| TM 9-2320-280-20-1 | AR 750-43 |
| TM 9-2320-280-20-2 | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Replace Fuel Fitting and Lines on a Light Wheeled Vehicle

091-63B-1012

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced  fuel fitting and lines on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission-capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Located leaking fuel line/fitting. | —— | —— |
| 6. Removed line and fitting. | —— | —— |
| 7. Drained excess fuel into a container. | —— | —— |
| 8. Selected proper fitting and line. | —— | —— |
| 9. Installed fitting and line. | —— | —— |
| 10. Checked for leaks. | —— | —— |
| 11. Verified fault was corrected. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-280-12 | AR 385-10 |
| TM 9-2320-280-10 | AR 750-1 |
| TM 9-2320-280-20-1 | AR 750-43 |
| TM 9-2320-280-20-2 | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Replace Fuel Tank on a Light Wheeled Vehicle

091-63B-1013

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the fuel tank on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Drained fuel tank. | —— | —— |
| 6. Removed lines and fittings. | —— | —— |
| 7. Removed fuel tank. | —— | —— |
| 8. Installed new fuel tank. | —— | —— |
| 9. Installed line and fittings. | —— | —— |
| 10. Filled fuel tank. | —— | —— |
| 11. Checked for leaks. | —— | —— |
| 12. Verified fault was corrected. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-272-12 | AR 385-10 |
| LO 9-2320-280-12 | AR 750-1 |
| TM 9-2320-272-10 | AR 750-43 |
| TM 9-2320-272-24-1 | DA PAM 738-750 |
| TM 9-2320-272-24-2 | TM 9-243 |
| TM 9-2320-272-24-3 | TM 9-8000 |
| TM 9-2320-272-24-4 |  |
| TM 9-2320-272-24P-1 |  |
| TM 9-2320-272-24P-2 |  |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |

Replace Fuel Filter Assembly on a Light Wheeled Vehicle

091-63B-1014

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced fuel filter assembly on a light  wheeled vehicle  IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission-capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed line and fittings. | —— | —— |
| 6. Removed fuel filter. | —— | —— |
| 7. Applied sealing compound to fittings. | —— | —— |
| 8. Tightened cap screws to 15 lb ft. | —— | —— |
| 9. Bled system. | —— | —— |
| 10. Checked for leaks. | —— | —— |
| 11. Verified fault was corrected. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-272-12 | AR 385-10 |
| LO 9-2320-280-12 | AR 750-1 |
| TM 9-2320-272-10 | AR 750-43 |
| TM 9-2320-272-24-1 | DA PAM 738-750 |
| TM 9-2320-272-24-2 | TM 9-243 |
| TM 9-2320-272-24-3 | TM 9-8000 |
| TM 9-2320-272-24-4 |  |
| TM 9-2320-272-24P-1 |  |
| TM 9-2320-272-24P-2 |  |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |

Troubleshoot Glow Plug System on a Light Wheeled Vehicle

091-63B-1015

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references. 

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostics on the glow plug system on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this was completed, the vehicle was fully mission-capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Ran battery test. Checked glow plug circuit connections. | —— | —— |
| 6. Checked for 75-125 AMPS with rotary switch in run position. | —— | —— |
| 7. Checked glow plug cycle. | —— | —— |
| 8. Checked current with glow plug controller disconnected. | —— | —— |
| 9. Measured voltage at socket 6 of glow plug controller. | —— | —— |
| 10. Verified fault had been corrected. | —— | —— |
| 11. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
| TM 9-2320-280-24P-1 | TM 9-243 |
| TM 9-2320-280-24P-2 | TM 9-8000 |

Correct Malfunction of Glow Plug System on a Light Wheeled Vehicle

091-63B-1016

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Corrected  malfunction of glow plug system on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Completed troubleshooting procedures. | —— | —— |
| 6. Disconnected negative battery cable. | —— | —— |
| 7. Replaced defective component(s). | —— | —— |
| 8. Connected negative battery cable. | —— | —— |
| 9. Verified fault had been corrected. | —— | —— |
| 10. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 11-6625-3052-14 | AR 385-10 |
| TM 9-2320-280-10 | AR 750-1 |
| TM 9-2320-280-20-1 | AR 750-43 |
| TM 9-2320-280-20-2 | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Subject Area 4: EXHAUST SYSTEM

Troubleshoot Exhaust System Malfunctions on a Light Wheeled Vehicle

091-63B-1021

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostics of exhaust system malfunctions on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was  fully mission-capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Checked for unusual noises while vehicle was running. | —— | —— |
| 6. Inspected exhaust system for leaks and rust. | —— | —— |
| 7. Inspected exhaust system for loose components. | —— | —— |
| 8. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
| TM 9-2320-280-24P-1 | TM 9-243 |
| TM 9-2320-280-24P-2 | TM 9-8000 |

Replace  Muffler on a Light Wheeled Vehicle

091-63B-1022

Conditions: In a field or garrison environment given a representative light wheel vehicle, ( M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced  muffler on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission-capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed tailpipe. | —— | —— |
| 6. Removed locknuts and U-bolt | —— | —— |
| 7. Removed and discarded gasket. | —— | —— |
| 8. Removed muffler. | —— | —— |
| 9. Installed new muffler with new gasket. | —— | —— |
| 10. Tightened lock nuts to 26 lb -ft. | —— | —— |
| 11. Verified fault had been corrected. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
| TM 9-2320-280-24P-1 | TM 9-243 |
| TM 9-2320-280-24P-2 | TM 9-8000 |

Replace Crossover Pipe on a Light Wheeled Vehicle

091-63B-1023

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced crossover pipe on a light  wheeled vehicle  IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission-capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Allowed vehicle to cool off. | —— | —— |
| 6. Removed access cover. | —— | —— |
| 7. Removed heat shield. | —— | —— |
| 8. Removed locknuts, washer, cap screws securing crossover pipe to exhaust manifold and muffler. | —— | —— |
| 9. Removed crossover pipe. | —— | —— |
| 10. Installed new gasket and crossover pipe. | —— | —— |
| 11. Installed locknuts, washers, cap screws, and tightened to 26 lb-ft. | —— | —— |
| 12. Verified fault had been corrected. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
|  | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Subject Area 5: COOLING SYSTEM

Troubleshoot Cooling System Malfunctions on a Light Wheeled Vehicle

091-63B-1025

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostics on the cooling system on a light  wheeled vehicle  IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission- capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Checked coolant level and mixture. | —— | —— |
| 6. Checked fan belts. | —— | —— |
| 7. Inspected radiator cap, hoses, surge tank, radiator, oil cooler, and fittings for damage, blockage, or large leaks. | —— | —— |
| 8. Checked thermostat. | —— | —— |
| 9. Checked fan for proper operation. | —— | —— |
| 10. Checked head gasket for leaks. | —— | —— |
| 11. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-272-12 | AR 385-10 |
| LO 9-2320-280-12 | AR 750-1 |
| TM 9-2320-272-10 | AR 750-43 |
| TM 9-2320-272-24-1 | DA PAM 738-750 |
| TM 9-2320-272-24-2 | TM 9-243 |
| TM 9-2320-272-24-3 | TM 9-8000 |
| TM 9-2320-272-24-4 |  |
| TM 9-2320-272-24P-1 |  |
| TM 9-2320-272-24P-2 |  |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |

Replace Radiator on a Light Wheeled Vehicle

091-63B-1026

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced radiator on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Drained cooling system by opening drain cocks on radiator and engine. | —— | —— |
| 5. Disconnected lines and hoses. | —— | —— |
| 6. Filled and checked antifreeze level and mixture. | —— | —— |
| 7. Verified fault had been corrected. | —— | —— |
| 8. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-272-12 | AR 385-10 |
| LO 9-2320-280-12 | AR 750-1 |
| TM 9-2320-272-10 | AR 750-43 |
| TM 9-2320-272-24-1 | DA PAM 738-750 |
| TM 9-2320-272-24-2 | TM 9-243 |
| TM 9-2320-272-24-3 | TM 9-8000 |
| TM 9-2320-272-24P-1 |  |
| TM 9-2320-272-24P-2 |  |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |

Replace Radiator Hoses, Lines and Clamps on a Light Wheeled Vehicle

091-63B-1029

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced radiator hoses, lines and clamps on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission- capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Drained cooling system by opening drain cock on radiator and engine. | —— | —— |
| 6. Disconnected any lines, or hoses to radiator. | —— | —— |
| 7. Removed locknuts and tilted radiator away from engine while removing. | —— | —— |
| 8. Ensured drain cock was closed on radiator and engine. | —— | —— |
| 9. Installed radiator and tightened locknuts. | —— | —— |
| 10. Connected lines and hoses. | —— | —— |
| 11. Filled and checked antifreeze level and mixture. | —— | —— |
| 12. Verified fault had been corrected. | —— | —— |
| 13. Completed TAMMS form, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-272-12 | AR 385-10 |
| LO 9-2320-280-12 | AR 750-1 |
| TM 9-2320-272-10 | AR 750-43 |
| TM 9-2320-272-24-1 | DA PAM 738-750 |
| TM 9-2320-272-24-2 | TM 9-243 |
| TM 9-2320-272-24-3 | TM 9-8000 |
| TM 9-2320-272-24-4 |  |
| TM 9-2320-272-24P-1 |  |
| TM 9-2320-272-24P-2 |  |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |

Correct Malfunction of Fan and Drive on a Light Wheeled Vehicle

091-63B-1031

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Corrected malfunction of fan and drive on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed radiator and shroud. | —— | —— |
| 6. Marked position of blade. | —— | —— |
| 7. Removed fan drive assembly. | —— | —— |
| 8. Removed fan and fan drive. | —— | —— |
| 9. Aligned fan blade onto fan drive and tightened bolts to 26 lb-ft. | —— | —— |
| 10. Installed fan drive assembly to water pump. | —— | —— |
| 11. Installed radiator and shroud. | —— | —— |
| 12. Connected any lines and hoses. | —— | —— |
| 13. Verified fault had been corrected. | —— | —— |
| 14. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-272-12 | AR 385-10 |
| LO 9-2320-280-12 | AR 750-10 |
| TM 9-2320-272-10 | AR 750-43 |
| TM 9-2320-272-24-1 | DA PAM 738-750 |
| TM 9-2320-272-24-2 | TM 9-243 |
| TM 9-2320-272-24-3 | TM 9-8000 |
| TM 9-2320-272-24-4 |  |
| TM 9-2320-272-24P-1 |  |
| TM 9-2320-272-24P-2 |  |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |

Correct Malfunction of Drive Belts on a Light Wheeled Vehicle

091-63B-1033

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Corrected malfunction of drive belts on a light  wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission- capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Checked condition of belts. | —— | —— |
| 6. Loosened adjustment and bracket belts. | —— | —— |
| 7. Removed belts. | —— | —— |
| 8. Installed new belts. | —— | —— |
| 9. Pretightened bolts. | —— | —— |
| 10. Adjusted belt tension using belt tension gauge. | —— | —— |
| 11. Torqued bolts to specified lb-ft. | —— | —— |
| 12. Verified fault had been corrected. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed. Score the soldier NO GO if any step is failed . If the soldier failed any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-280-12 | AR 385-10 |
| TM 9-2320-280-10 | AR 750-1 |
| TM 9-2320-280-20-1 | AR 750-43 |
| TM 9-2320-280-20-2 | DA PAM 738-750 |
| TM 9-2320-280-20-3 | TM 9-243 |
|  | TM 9-8000 |

Subject Area 6: ELECTRICAL SYSTEM

Troubleshoot Charging System Malfunction on a Light Wheeled Vehicle

091-63B-1036

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostics of charging system malfunction on a light wheeled vehicle  IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected /used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Checked condition of belts. | —— | —— |
| 6. Checked all electrical connections. | —— | —— |
| 7. Checked protective control box. | —— | —— |
| 8. Checked voltage at alternator. | —— | —— |
| 9. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
|  | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Correct Malfunction of Alternator on a Light Wheeled Vehicle

091-63B-1037

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Corrected  malfunction of alternator on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission- capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected /used applicable publications. | —— | —— |
| 2. Selected /used correct tools /TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Performed diagnostic procedures on to locate charging system malfunctions. | —— | —— |
| 6. Adjusted alternator to 28.5 volts. | —— | —— |
| 7. Replaced alternator. | —— | —— |
| 8. Adjusted belt tension. | —— | —— |
| 9. Verified fault had been corrected. | —— | —— |
| 10. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Troubleshoot Starting System Malfunction on a Light Wheeled Vehicle

091-63B-1038

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostics on starting system malfunction on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission- capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools /TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Performed diagnostic procedures to locate charging system malfunctions. | —— | —— |
| 6. Adjusted alternator to 28.5 volts. | —— | —— |
| 7. Replaced alternator. | —— | —— |
| 8. Adjusted belt tension. | —— | —— |
| 9. Verified fault had been corrected. | —— | —— |
| 10. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Replace Starter on a Light Wheeled Vehicle

091-63B-1039

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series and M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced starter on a light  wheeled vehicle IAW the applicable technical publications procedures, and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools and TMDE. | —— | —— |
| 3. Followed prescribed safety precautions. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Performed diagnostic procedures to verify fault. | —— | —— |
| 6. Removed starter assembly. | —— | —— |
| 7. Repaired/replaced starter assembly. | —— | —— |
| 8. Installed starter assembly. | —— | —— |
| 9. Verified fault was corrected and vehicle was fully mission-capable. | —— | —— |
| 10. Completed TAMMS forms, as necessary. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| DA PAM 738-750 | AR 385-10 |
| TM 9-2320-272-10 | AR 750-1 |
| TM 9-2320-272-24-1 | AR 750-43 |
| TM 9-2320-272-24-2 | TM 9-243 |
| TM 9-2320-272-24-3 | TM 9-8000 |
| TM 9-2320-272-24-4 |  |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |

Troubleshoot Electrical System Malfunctions on a Light Wheeled Vehicle

091-63B-1041

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Peformed diagnostics of electrical system malfunctions on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Disconnected negative battery cable. | —— | —— |
| 6. Checked light bulbs. | —— | —— |
| 7. Checked for voltage at light socket. | —— | —— |
| 8. Checked ground. | —— | —— |
| 9. Checked light switch. | —— | —— |
| 10. Checked wires for breaks. | —— | —— |
| 11. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Replace Protective Control Box on a Light Wheeled Vehicle

091-63B-1044

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced protective control box on a light  wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected /correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Performed diagnostic procedures on protective control box. | —— | —— |
| 6. Disconnected negative battery cable. | —— | —— |
| 7. Removed protective control box. | —— | —— |
| 8. Aligned the slot on the harness to the protective control box while connecting the harness. | —— | —— |
| 9. Installed the negative battery cable. | —— | —— |
| 10. Verified fault had been corrected. | —— | —— |
| 11. Completed TAMMS forms, as required | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| DA PAM 738-750 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | TM 9-2320-280-10 |
|  | TM 9-243 |
|  | TM 9-8000 |

Correct Malfunction of Sending Units and Warning Switches on a Light Wheeled Vehicle

091-63B-1047

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Corrected  malfunction of sending units and warning switches on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Performed diagnostic procedures on switches/sending units. | —— | —— |
| 6. Replaced defective switch/sending unit. | —— | —— |
| 7. Verified fault had been corrected. | —— | —— |
| 8. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-20-1 | AR 385-10 |
| TM 9-2320-280-20-2 | AR 750-1 |
| TM 9-2320-280-20-3 | AR 750-43 |
|  | DA PAM 738-751 |
|  | TM 9-2320-272-10 |
|  | TM 9-2320-272-24-1 |
|  | TM 9-2320-272-24-2 |
|  | TM 9-2320-272-24-3 |
|  | TM 9-2320-272-24-4 |
|  | TM 9-243 |
|  | TM 9-8000 |

Correct Malfunction of Batteries on a Light Wheeled Vehicle

091-63B-1050

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Corrected malfunction of batteries on a light  wheeled vehicle  IAW the applicable technical publications, procedures  and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Checked battery terminals. | —— | —— |
| 6. Conducted specific gravity test on battery cells. | —— | —— |
| 7. Disconnected negative battery cable first. | —— | —— |
| 8. Installed new batteries. | —— | —— |
| 9. Verified fault had been corrected. | —— | —— |
| 10. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-6140-200-14 |
| TM 9-2320-280-10 | TM 9-8000 |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-243 |  |

Subject Area 7: INSTRUMENT PANEL

Troubleshoot Electrical Gauges on a Light Wheeled Vehicle

091-63B-1053

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Peformed diagnostics of electrical gauges on a light  wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Visually inspected all wires leading to gauges. | —— | —— |
| 6. Checked for voltage at gauge. | —— | —— |
| 7. Checked resistance at gauge. | —— | —— |
| 8. Replaced defective gauge or repaired wire. | —— | —— |
| 9. Verified fault had been corrected. | —— | —— |
| 10. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-280-10 | TM 9-243 |
| TM 9-2320-280-20-1 | TM 9-8000 |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |

Subject Area 8: WIRING HARNESS

Repair Engine Wiring Harness on a Light Wheeled Vehicle

091-63B-1055

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Repaired the engine wiring harness on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Visually inspected all wires. | —— | —— |
| 6. Checked for voltage at component. | —— | —— |
| 7. Checked ground. | —— | —— |
| 8. Repaired wire. | —— | —— |
| 9. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-272-24P-1 | TM 9-8000 |
| TM 9-2320-272-24P-2 |  |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |

Repair Chassis Wiring Harness on a Light Wheeled Vehicle

091-63B-1057

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Repaired the chassis wiring harness on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Visually inspected all wires. | —— | —— |
| 6. Checked for voltage at component. | —— | —— |
| 7. Checked ground. | —— | —— |
| 8. Repaired wire. | —— | —— |
| 9. Verified fault had been corrected. | —— | —— |
| 10. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-3 | AR 750-1 |
| TM 9-2320-272-24-4 | AR 750-43 |
| TM 9-2320-280-20-1 | DA PAM 738-750 |
|  | TM 9-2320-280-10 |
|  | TM 9-2320-280-20-2 |
|  | TM 9-2320-280-20-3 |
|  | TM 9-243 |
|  | TM 9-8000 |

Subject Area 9: TRANSMISSION

Troubleshoot Transmission Malfunctions on a Light Wheeled Vehicle

091-63B-1058

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures on the transmission malfunctions on a light  wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Checked fluid level. | —— | —— |
| 6. Checked for bent or broken linkage. | —— | —— |
| 7. Adjusted linkage. | —— | —— |
| 8. Verified fault had been corrected. | —— | —— |
| 9. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-280-10 | TM 9-8000 |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |

Service Transmission Assembly on a Light Wheeled Vehicle

091-63B-1059

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Serviced the transmission assembly on a light  wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Set vehicle parking brake. | —— | —— |
| 6. Verified vehicle was at operating temperature. | —— | —— |
| 7. Inspected oil for grit, foaminess, or milkiness. | —— | —— |
| 8. Removed and discarded filter. | —— | —— |
| 9. Installed new filter. | —— | —— |
| 10. Torqued transmission pan bolts to standard. | —— | —— |
| 11. Checked for leaks. | —— | —— |
| 12. Completed TAMMS forms as, required. | —— | —— |
| 13. Verified fault had been corrected. | —— | —— |
| 14. Verified vehicle was fully mission-capable. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-280-10 | TM 9-8000 |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |

Replace Neutral Safety Switch on a Light Wheeled Vehicle

091-63B-1061

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the neutral safety switch on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected /used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Tagged all leads. | —— | —— |
| 6. Removed switch. | —— | —— |
| 7. Adjusted switch or replaced switch, as applicable. | —— | —— |
| 8. Verified fault had been corrected. | —— | —— |
| 9. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-280-10 | TM 9-8000 |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |

Subject Area 10: TRANSFER

Troubleshoot Transfer Malfunctions on a Light Wheeled Vehicle

091-63B-1066

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic proceedures to locate transfer malfunctions on a light  wheeled vehicle  IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Performed diagnostic procedures and verified problem/fault. | —— | —— |
| 6. Checked fluid level. | —— | —— |
| 7. Checked for bent or broken linkage. | —— | —— |
| 8. Adjusted linkage. | —— | —— |
| 9. Verified fault had been corrected. | —— | —— |
| 10. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-272-24P-1 | TM 9-8000 |
| TM 9-2320-272-24P-2 |  |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |

Subject Area 11: PROPELLER SHAFTS

Replace Propeller Shafts on a Light Wheeled Vehicle

091-63B-1075

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced propeller shafts on a light  wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Jacked up front wheels to release sprag (M35A2). | —— | —— |
| 6. Marked propeller shaft flange position for installation. | —— | —— |
| 7. Loosened cap and slid propeller shaft away from flange. | —— | —— |
| 8. Inspected U-joints. | —— | —— |
| 9. Coated splines with GAA. | —— | —— |
| 10. Installed propeller shaft and torqued bolts to specified torque. | —— | —— |
| 11. Verified fault had been corrected. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-272-24P-1 | TM 9-8000 |
| TM 9-2320-272-24P-2 |  |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |

Replace Universal Joints on a Light Wheeled Vehicle

091-63B-1076

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the universal joints on a light  wheeled  vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission  capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected /used applicable publications. | —— | —— |
| 2. Selected /used correct tools /TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed propeller shaft. | —— | —— |
| 6. Marked mating yoke position for installation. | —— | —— |
| 7. Removed C-Rings from spider cross. | —— | —— |
| 8. Removed old bearings from propeller shaft. | —— | —— |
| 9. Coated bearing caps with GAA. | —— | —— |
| 10. Installed new U-Joints. | —— | —— |
| 11. Installed propeller shaft. | —— | —— |
| 12. Verified fault had been corrected. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-272-24P-1 | TM 9-8000 |
| TM 9-2320-272-24P-2 |  |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |

Replace Center Bearings on a Light Wheeled Vehicle

091-63B-1077

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the center bearings on a light  wheeled  vehicle IAW the applicable technical publications, procedures and, specifications.  When this task was completed, the vehicle was fully mission  capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected /used applicable publications | —— | —— |
| 2. Selected /used correct tools /TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed rear propeller and forward -rear propeller shafts. | —— | —— |
| 6. Removed center bearing companion flange, dust cover, spacer, center bearing mounting bracket, spacer and dust cover. | —— | —— |
| 7. Installed new parts on forward propeller shaft and tightened to 100-115 lb-ft. | —— | —— |
| 8. Installed rear- rear propeller shaft yoke flange on forward rear axle and tightened to 30-40 lb-ft. | —— | —— |
| 9. Installed transfer case drive shaft flange to brake drum and tighten to 30-40 lb-ft. | —— | —— |
| 10. Installed center bearing mounting bracket on cross member. | —— | —— |
| 11. Installed propeller shafts 90 degrees from each other. | —— | —— |
| 12. Verified fault had been corrected. | —— | —— |
| 13. Completed TAMMS Forms as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
| TM 9-243 | TM 9-8000 |

Subject Area 12: AXLES

Troubleshoot Axle Malfunctions on a Light Wheeled Vehicle

091-63B-1078

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures to locate axle malfunctions on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Checked if front wheel drive was engaged. | —— | —— |
| 6. Checked for loose lug nuts. | —— | —— |
| 7. Checked lubrication level in differentials. | —— | —— |
| 8. Checked for damaged wheel bearings. | —— | —— |
| 9. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM738-750 |
| TM 9-2320-272-24P-1 | TM 9-243 |
| TM 9-2320-272-24P-2 | TM 9-8000 |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |

Replace Front Axle Spindle on a Light Wheeled Vehicle

091-63B-1081

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series/ M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the front axle spindle on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission-capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed caliper. | —— | —— |
| 6. Removed locking hub. | —— | —— |
| 7. Removed outer adjusting nut, adjusting lock, and inner adjusting nut. | —— | —— |
| 8. Removed outer wheel bearing, rotor, seal, and inner wheel bearing. | —— | —— |
| 9. Removed nuts, splash shield and caliper bracket from spindle. | —— | —— |
| 10. Installed components in reverse order. | —— | —— |
| 11. Verified fault had been corrected. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-272-24P-1 | TM 9-8000 |
| TM 9-2320-272-24P-2 |  |

Replace Halfshaft on a Light Wheeled Vehicle

091-63B-1082

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the halfshaft on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed tire and supported vehicle. | —— | —— |
| 6. Removed access plug and washer from geared hub. | —— | —— |
| 7. Removed cap screw from geared hub and rotor. | —— | —— |
| 8. Removed half shaft. | —— | —— |
| 9. Installed new half shaft into geared hub. | —— | —— |
| 10. Applied sealing compound to retaining cap screw and tightened to 37 lb-ft. | —— | —— |
| 11. Installed cap screws to rotor and tightened to 48 lb-ft. | —— | —— |
| 12. Installed tire. | —— | —— |
| 13. Verified fault had been corrected. | —— | —— |
| 14. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
| TM 9-2320-280-24P-1 | TM 9-243 |
| TM 9-2320-280-24P-2 | TM 9-8000 |

Correct Malfunction of Knuckle and Geared Hub on a Light Wheeled Vehicle

091-63B-1083

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Corrected the malfunction of knuckle and geared hub on a light  wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed tire and supports vehicle. | —— | —— |
| 6. Removed steering arm cover from geared hub. | —— | —— |
| 7. Bent tab on lock washer away from locknut. | —— | —— |
| 8. Used locknut wrench to remove locknut and washer from spindle. | —— | —— |
| 9. Installed lock washer and locknut on spindle and tightened to 35-45 lb-ft and seated bearing. | —— | —— |
| 10. Loosened and retighten locknut to 25 lb-ft and bent tab on lock washer. | —— | —— |
| 11. Installed steering arm cover. | —— | —— |
| 12. Verified fault had been corrected. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | TM 9-243 |
| TM 9-2320-280-24P-1 | TM 9-8000 |

Adjust Geared Hub Spindle Bearing on a Light Wheeled Vehicle

091-63B-1084

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Adjusted the geared hub spindle bearing on a light  wheeled vehicle IAW the applicable technical publications, procedures and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed tire and supported vehicle. | —— | —— |
| 6. Removed drain plug from geared hub and drained fluid in into container. | —— | —— |
| 7. Removed vent line. | —— | —— |
| 8. Removed tie rod end using a puller. | —— | —— |
| 9. Removed half shaft. | —— | —— |
| 10. Supported geared hub and removed upper and lower ball joints. | —— | —— |
| 11. Removed geared hub. | —— | —— |
| 12. Supported geared hub during installation. | —— | —— |
| 13. Installed ball joints and torqued cap screws to proper specification. | —— | —— |
| 14. Installed tie rod end and torqued it to proper specification. | —— | —— |
| 15. Installed half shaft. | —— | —— |
| 16. Filled geared hub. | —— | —— |
| 17. Verified fault had been corrected. | —— | —— |
| 18. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
| TM 9-2320-280-24P-1 | TM 9-243 |
|  | TM 9-8000 |

Replace Upper and Lower Ball Joints on a Light Wheeled Vehicle

091-63B-1088

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the upper and lower ball joints on a light wheeled vehicle IAW the applicable technical publications, procedures and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected /used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed tire and supported lower control arm. | —— | —— |
| 6. Removed locknuts from upper and lower control arm. | —— | —— |
| 7. Disconnected ball joint from lower control arm. | —— | —— |
| 8. Used puller to separate ball joint from geared hub and removed ball joint. | —— | —— |
| 9. Installed ball joint to lower control arm and ensured ball joint was placed below lower control arm and tightened to 35 lb-ft. | —— | —— |
| 10. Secured ball joint to geared hub with slotted nut and tightened to 73 lb-ft. | —— | —— |
| 11. Lubricated lower ball joint. | —— | —— |
| 12. Verified fault had been corrected. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-280-12 | AR 385-10 |
| TM 9-2320-280-10 | AR 750-1 |
| TM 9-2320-280-20-1 | AR 750-43 |
| TM 9-2320-280-20-2 | DA PAM 738-750 |
| TM 9-2320-280-20-3 | TM 9-243 |
| TM 9-2320-280-24P-1 | TM 9-8000 |

Replace Dust Boot (CV) on a Light Wheeled Vehicle

091-63B-1091

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the dust boot (CV) on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed guard from steering knuckle. | —— | —— |
| 6. Removed screws, inner retaining clamp, and dust boot. | —— | —— |
| 7. Installed dust boot on axle housing with fabric side of zipper facing steering knuckle. | —— | —— |
| 8. Closed zipper and applied sealant to zipper. | —— | —— |
| 9. Installed inner clamp of dust boot. | —— | —— |
| 10. Laced zipper locks with fine wire and twists. | —— | —— |
| 11. Installed screws to steering knuckle, threaded wire around each of the screws, and tied off laces. | —— | —— |
| 12. Verified fault had been corrected. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-280-12 | AR 385-10 |
| TM 9-2320-280-10 | AR 750-1 |
| TM 9-2320-280-20-1 | AR 750-43 |
| TM 9-2320-280-20-2 | DA PAM 738-750 |
| TM 9-2320-280-20-3 | TM 9-243 |
| TM 9-2320-280-24P-1 | TM 9-8000 |

Subject Area 13: BRAKES

Troubleshoot Brake System Malfunctions

091-63B-1097

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M44A2 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures on the brake system malfunctions IAW the applicable technical publications, procedures and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required was performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Checked all lines and hoses for leaks. | —— | —— |
| 6. Checked service brake chambers for air escaping from vents. | —— | —— |
| 7. Checked front service brake chambers for proper pressure. | —— | —— |
| 8. Checked service brake chambers for proper pressure. | —— | —— |
| 9. Checked spring and service brake chambers for proper pressure. | —— | —— |
| 10. Checked limiting valve for venting. | —— | —— |
| 11. Checked limiting valve for proper air delivery. | —— | —— |
| 12. Checked limiting valve for proper air supply pressure. | —— | —— |
| 13. Checked service brake pedal valve. | —— | —— |
| 14. Checked primary and secondary air system relay valves for proper pressure. | —— | —— |
| 15. Inspected brake mechanisms. | —— | —— |
| 16. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-280-12 | AR 385-10 |
| LO 9-2320-386-12 | AR 750-1 |
| TM 9-2320-280-10 | AR 750-43 |
| TM 9-2320-280-20-1 | DA PAM 738-750 |
| TM 9-2320-280-20-2 | TM 9-243 |
| TM 9-2320-361-10 | TM 9-8000 |
| TM 9-2320-361-20 |  |
| TM 9-2320-386-10 |  |
| TM 9-2320-386-24 |  |

Replace Brake Lines and Fittings on a Light Wheeled Vehicle

091-63B-1098

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M44A2 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the brake lines and fittings on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Performed diagnostic procedures to determine fault. | —— | —— |
| 3. Selected/used correct tools/TMDE. | —— | —— |
| 4. Followed prescribed safety procedures. | —— | —— |
| 5. Practiced maintenance discipline. | —— | —— |
| 6. Set parking brake. | —— | —— |
| 7. Drained air pressure. | —— | —— |
| 8. Used a line wrench to disconnect defective brake line from fitting. | —— | —— |
| 9. Drained fluid into container. | —— | —— |
| 10. Removed defective fitting. | —— | —— |
| 11. Installed new fitting and line. | —— | —— |
| 12. Filled and bled brake system. | —— | —— |
| 13. Checked for leaks. | —— | —— |
| 14. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-280-12 | AR 385-10 |
| LO 9-2320-386-12 | AR 750-1 |
| TM 9-2320-280-10 | AR 750-43 |
| TM 9-2320-280-20-1 | DA PAM 738-750 |
| TM 9-2320-280-20-2 | TM 9-243 |
| TM 9-2320-280-20-3 | TM 9-8000 |
| TM 9-2320-386-10 |  |
| TM 9-2320-386-24 |  |

Replace Hand  Brake Shoes on a Light Wheeled Vehicle

091-63B-1100

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M44A2series/ M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the hand brake shoes on a light  wheeled vehicle IAW the applicable technical publications, procedures and specifications. When this task was completed, the vehicle was fully mission  capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Chocked vehicle wheels. | —— | —— |
| 6. Removed propeller shaft. | —— | —— |
| 7. Removed transfer output shaft and park brake drum (M939). | —— | —— |
| 8. Removed springs (M35A2). | —— | —— |
| 9. Removed parking brake cable. | —— | —— |
| 10. Removed parking brake shoes. | —— | —— |
| 11. Installed brake shoes in reverse order. | —— | —— |
| 12. Adjusted parking brake. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-272-24P-1 | TM 9-8000 |
| TM 9-2320-272-24P-2 |  |
| TM 9-2320-361-10 |  |
| TM 9-2320-361-20 |  |
| TM 9-2320-386-10 |  |
| TM 9-2320-386-24 |  |
| TM 9-2320-386-24P |  |

Replace Service Brake Shoes on a Light Wheeled Vehicle

091-63B-1105

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M44A2 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the service brake shoes on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected /used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Caged brake springs. | —— | —— |
| 6. Removed hub and drum assembly. | —— | —— |
| 7. Removed springs and brake components. | —— | —— |
| 8. Removed brake shoes. | —— | —— |
| 9. Installed new brake shoes. | —— | —— |
| 10. Installed springs and brake components. | —— | —— |
| 11. Installed hub and drum assembly. | —— | —— |
| 12. Performed brake adjustment. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-2320-386-24P |
| TM 9-2320-272-24P-1 | TM 9-243 |
| TM 9-2320-272-24P-2 | TM 9-8000 |
| TM 9-2320-361-10 |  |
| TM 9-2320-361-20 |  |
| TM 9-2320-386-10 |  |
| TM 9-2320-386-24 |  |

Replace Front and Rear Calipers on a Light Wheeled Vehicle

091-63B-1106

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the front and rear calipers on a light  wheeled vehicle IAW the applicable technical publications, procedures and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Disconnected lines. | —— | —— |
| 6. Used crowfoot to remove cap screws. | —— | —— |
| 7. Removed yoke, caliper, and brake pads. | —— | —— |
| 8. Replaced brake pads, if worn. | —— | —— |
| 9. Installed caliper in reverse order. | —— | —— |
| 10. Connected lines and bled the brake system. | —— | —— |
| 11. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Replace Front and Rear Brake Pads on a Light Wheeled Vehicle

091-63B-1107

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the front and rear brake pads on a light  wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed and supports caliper. | —— | —— |
| 6. Noted position of brake pad surfaces for installation. | —— | —— |
| 7. Removed brake pads. | —— | —— |
| 8. Ensured brake pads are installed with lining facing the rotor. | —— | —— |
| 9. Used a "C" clamp and a block of wood to bottom out position in caliper. | —— | —— |
| 10. Used the crowfoot, secure yoke, and caliper to adapter, tightened two cap screws to 30 ft-lb. | —— | —— |
| 11. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is  failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Replace Front and Rear Brake Rotors on a Light Wheeled Vehicle

091-63B-1108

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the front and rear brake rotors on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed brake pad. | —— | —— |
| 6. Removed half shaft. | —— | —— |
| 7. Removed rotor. | —— | —— |
| 8. Installed rotor. | —— | —— |
| 9. Installed half shaft and torque to specifications. | —— | —— |
| 10. Installed brake pads. | —— | —— |
| 11. Verified fault had been corrected. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed. Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Replace Master Cylinder on a Light Wheeled Vehicle

091-63B-1109

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the master cylinder on a light  wheeled vehicle IAW the applicable technical publications, procedures and specifications.  When this task was completed, the vehicle was fully mission-capable, or maintenance actions required was performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected /used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed and plugged all lines. | —— | —— |
| 6. Removed master cylinder and drained fluid into a container. | —— | —— |
| 7. Installed new master cylinder and torqued bolts. | —— | —— |
| 8. Bled system. | —— | —— |
| 9. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
|  | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Replace Air Hydraulic Cylinder on a Light Wheeled Vehicle

091-63B-1110

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M44A2 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced air hydraulic cylinder on a light wheeled vehicle IAW the applicable technical publications, procedures and specifications. When this task was completed, the vehicle was fully mission-capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected /used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Drained air reservoirs. | —— | —— |
| 6. Removed and plugged all lines. | —— | —— |
| 7. Noted position of all brass fittings. | —— | —— |
| 8. Removed air-hydraulic cylinder and drained fluid into a container. | —— | —— |
| 9. Wrapped fitting with tape and installed onto air -hydraulic cylinder. | —— | —— |
| 10. Installed air-hydraulic cylinder. | —— | —— |
| 11. Bled system. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-272-12 | AR 385-10 |
| LO 9-2320-386-12 | AR 750-1 |
| TM 9-2320-272-10 | AR 750-43 |
| TM 9-2320-272-24-1 | DA PAM 738-750 |
| TM 9-2320-272-24-2 | TM 9-243 |
| TM 9-2320-272-24-3 | TM 9-8000 |
| TM 9-2320-272-24-4 |  |
| TM 9-2320-361-10 |  |
| TM 9-2320-361-20 |  |
| TM 9-2320-386-10 |  |
| TM 9-2320-386-24 |  |

Replace Treadle Valve on a Light Wheeled Vehicle

091-63B-1112

Conditions: In a field or garrison environment given a representative light wheel vehicle, ( M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the treadle valve on an light wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission-capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected /used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Drained air reservoirs. | —— | —— |
| 6. Removed brake pedal and protective control box. | —— | —— |
| 7. Removed all lines and fittings from treadle valve. | —— | —— |
| 8. Inspected lines and fittings for damage. | —— | —— |
| 9. Removed three studs securing treadle valve to fire wall. | —— | —— |
| 10. Installed new treadle valve. | —— | —— |
| 11. Wrapped fittings with sealing tape. | —— | —— |
| 12. Reconnected all lines, and fittings. | —— | —— |
| 13. Installed brake pedal and protective control box. | —— | —— |
| 14. Charged air system and checked the brakes. | —— | —— |
| 15. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| DA PAM 738-750 | AR 385-10 |
| TM 9-2320-272-10 | AR 750-1 |
| TM 9-2320-272-24-1 | AR 750-43 |
| TM 9-2320-272-24-2 | TM 9-243 |
| TM 9-2320-272-24-3 | TM 9-8000 |
| TM 9-2320-272-24-4 |  |

Replace Hydro-Boost on a Light Wheeled Vehicle

091-63B-1114

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the hydro-boost on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected /used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed master cylinder. | —— | —— |
| 6. Marked and disconnected the high pressure lines and one return line from hydro-boost. | —— | —— |
| 7. Used container to catch brake fluid. | —— | —— |
| 8. Removed push rod from bell crank. | —— | —— |
| 9. Removed hydro-boost. | —— | —— |
| 10. Installed hydro-boost. | —— | —— |
| 11. Installed master cylinder. | —— | —— |
| 12. Filled and bled system. | —— | —— |
| 13. Verified fault had been corrected. | —— | —— |
| 14. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
|  | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Replace Air Compressor and  Belts on a Light Wheeled Vehicle

091-63B-1117

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M44A2 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the air compressor and belts on a light wheeled vehicle IAW the applicable technical publications, procedures and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected /used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Drained air tanks, and removed radiator and alternator belts. | —— | —— |
| 6. Removed air compressor pulley bolts and used air compressor pulley wrench to loosen belts. | —— | —— |
| 7. Removed air line and fuel return line clamp. | —— | —— |
| 8. Removed air compressor and discarded gasket. | —— | —— |
| 9. Removed air compressor pulley. | —— | —— |
| 10. Installed pulley on new air compressor. | —— | —— |
| 11. Installed new air compressor. | —— | —— |
| 12. Reconnected air line and fuel return line clamp. | —— | —— |
| 13. Installed new belts and adjusted tension. | —— | —— |
| 14. Installed alternator belts and radiator. | —— | —— |
| 15. Verified fault had been corrected. | —— | —— |
| 16. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-361-10 | TM 9-8000 |
| TM 9-2320-361-20 |  |
| TM 9-2320-386-10 |  |
| TM 9-2320-386-24 |  |

Inspect Air Brake Control Valves on a Light Wheeled Vehicle

091-63B-1124

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M44A2 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Inspected the air brake control valves on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected /used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Listened for leaks while applying parking brake. | —— | —— |
| 6. Applied soapy water to lines and fittings and checked for leaks. | —— | —— |
| 7. Inspected valve for cracked fittings. | —— | —— |
| 8. Verified fault had been corrected. | —— | —— |
| 9. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-2 | AR 750-1 |
| TM 9-2320-272-24-3 | AR 750-43 |
| TM 9-2320-272-24-4 | DA PAM 738-750 |
| TM 9-2320-361-10 | TM 9-2320-272-24-1 |
| TM 9-2320-361-20 | TM 9-2320-386-24 |
| TM 9-2320-386-10 | TM 9-243 |
|  | TM 9-8000 |

Subject Area 14: WHEELS AND HUBS

Correct Malfunction of  Wheel and Tire Assembly on a Light Wheeled Vehicle

091-63B-1129

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Corrected  malfunction of  wheel and tire assembly on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected /used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Checked for leaks by applying soapy water on the tire and valve stem. | —— | —— |
| 6. Checked tire wear by using tire depth gauge. | —— | —— |
| 7. Replaced worn tire or repaired inner tube. | —— | —— |
| 8. Used tire cage when inflating tire. | —— | —— |
| 9. Verified fault had been corrected. | —— | —— |
| 10. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-280-10 | TM 9-8000 |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |

Subject Area 15: STEERING

Troubleshoot Steering System Malfunctions on a Light Wheeled  Vehicle

091-63B-1139

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures to locate steering system malfunctions on a light  wheeled  vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Checked tire pressure. | —— | —— |
| 6. Checked suspension system for serviceability. | —— | —— |
| 7. Checked hydraulic fluid level. | —— | —— |
| 8. Inspected components of drag link. | —— | —— |
| 9. Checked steering gear box mounting. | —— | —— |
| 10. Checked power steering pump belt for looseness. | —— | —— |
| 11. Checked wheel bearings. | —— | —— |
| 12. Checked leaf spring. | —— | —— |
| 13. Installed rim halves. | —— | —— |
| 14. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
|  | DA PAM 738-750 |
|  | LO 9-2320-280-12 |
|  | TM 9-2320-280-20-3 |
|  | TM 9-243 |
|  | TM 9-8000 |

Correct Malfunction of Tie Rod Assembly on a Light Wheeled Vehicle

091-63B-1141

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Corrected malfunction of tie rod assembly on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Set parking brake. | —— | —— |
| 6. Raised vehicle off of the ground. | —— | —— |
| 7. Removed cotter pin, and castle nut securing tie rod to center link. | —— | —— |
| 8. Removed tie rod using puller. | —— | —— |
| 9. Installed new tie rod in reverse order and torqued to 70 ft lb. | —— | —— |
| 10. Installed new cotter pin. | —— | —— |
| 11. Lubed vehicle. | —— | —— |
| 12. Conducted a front end alignment. | —— | —— |
| 13. Verified fault had been corrected. | —— | —— |
| 14. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO- GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-280-12 | AR 385-10 |
| TM 9-2320-280-10 | AR 750-1 |
| TM 9-2320-280-20-1 | AR 750-43 |
| TM 9-2320-280-20-2 | DA PAM 738-750 |
| TM 9-2320-280-20-3 | TM 9-243 |
|  | TM 9-8000 |

Correct Malfunction of Drag Link Assembly  on a Light Wheeled Vehicle

091-63B-1142

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Corrected  malfunction of drag link assembly  on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed drag link assembly. | —— | —— |
| 6. Removed ball seats, springs, and safety plugs in drag link in correct order. | —— | —— |
| 7. Installed drag link assembly. | —— | —— |
| 8. Lubricated drag link assembly. | —— | —— |
| 9. Adjusted drag link. | —— | —— |
| 10. Verified fault had been corrected. | —— | —— |
| 11. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
|  | LO 9-2320-280-12 |
|  | TM 9-243 |
|  | TM 9-8000 |

Correct Malfunction of  Power Assist Cylinder on a Light Wheeled Vehicle

091-63B-1143

Conditions: In a field or garrison environment given a representative light wheel vehicle, ( M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Corrected malfunction of  power assist cylinder on a light  wheeled vehicle IAW the applicable technical publications, procedures,and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed splash shield. | —— | —— |
| 6. Removed plugs and tagged pressure lines. | —— | —— |
| 7. Removed cylinder. | —— | —— |
| 8. Disassembled socket assembly. | —— | —— |
| 9. Installed components in reverse order. | —— | —— |
| 10. Checked travel adjustment. | —— | —— |
| 11. Verified fault had been corrected. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-272-12 | AR 385-10 |
| TM 9-2320-272-10 | AR 750-1 |
| TM 9-2320-272-24-1 | AR 750-43 |
| TM 9-2320-272-24-2 | DA PAM 738-750 |
| TM 9-2320-272-24-3 | TM 9-243 |
| TM 9-2320-272-24-4 | TM 9-8000 |

Replace Power Steering Lines and Fittings on a Light Wheeled Vehicle

091-63B-1154

Conditions: In a field or garrison environment given a representative light wheel vehicle, ( M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the power steering lines and fittings on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed steering cylinder stone shield. | —— | —— |
| 6. Tagged all lines. | —— | —— |
| 7. Used container to catch fluid. | —— | —— |
| 8. Installed components in reverse order. | —— | —— |
| 9. Checked for leaks. | —— | —— |
| 10. Verified fault had been corrected. | —— | —— |
| 11. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-272-12 | AR 385-10 |
| TM 9-2320-272-10 | AR 750-1 |
| TM 9-2320-272-24-1 | AR 750-43 |
| TM 9-2320-272-24-2 | DA PAM 738-750 |
| TM 9-2320-272-24-3 | TM 9-243 |
| TM 9-2320-272-24-4 | TM 9-8000 |

Subject Area 16: SPRINGS AND SHOCKS

Replace Shock Absorbers on a Light Wheeled Vehicle

091-63B-1161

Conditions: In a field or garrison environment given a representative light wheel vehicle, ( M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the shock absorbers on a light wheeled vehicle IAW the applicable technical publications, procedures and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Raised and supported vehicle. | —— | —— |
| 6. Removed wheel. | —— | —— |
| 7. Removed locknuts and discards. | —— | —— |
| 8. Marked alignment of shock absorbers. | —— | —— |
| 9. Installed wheel and lowered vehicle. | —— | —— |
| 10. Verified fault had been corrected. | —— | —— |
| 11. Complete TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all step s are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-280-10 | TM 9-8000 |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |

Subject Area 17: BODY, HOOD, AND CAB

Replace Seat Belt on a Light Wheeled Vehicle

091-63B-1172

Conditions: In a field or garrison environment given a representative light wheel vehicle, ( M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced the seat belt on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Removed anchor bolt to bracket. | —— | —— |
| 6. Removed buckle assembly. | —— | —— |
| 7. Removed anchor bolt to body. | —— | —— |
| 8. Removed connector assembly. | —— | —— |
| 9. Installed components in reverse order. | —— | —— |
| 10. Verified fault had been corrected. | —— | —— |
| 11. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed. Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-280-10 | TM 9-8000 |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |

Subject Area 18: HOIST, WINCH, AND POWER TAKE OFF

Troubleshoot Winch Malfunction on a Light Wheeled Vehicle

091-63B-1191

Conditions: In a field or garrison environment given a representative light wheel vehicle, ( M998 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures of  the winch malfunction on a light  wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Checked reservoir for proper oil level. | —— | —— |
| 6. Checked if power takeoff (PTO) engages. | —— | —— |
| 7. Checked PTO linkage for brakes or adjustment. | —— | —— |
| 8. Checked drum clutch. | —— | —— |
| 9. Checked drum lock. | —— | —— |
| 10. Checked winch control cable for damage. | —— | —— |
| 11. Checked oil lines for damage. | —— | —— |
| 12. Checked oil return line oil filter for leaks. | —— | —— |
| 13. Checked if bypass was indicated on hydraulic oil tank filter. | —— | —— |
| 14. Checked pump for leaks or overheating. | —— | —— |
| 15. Checked winch motor for leaks. | —— | —— |
| 16. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed. Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-272-12 | AR 385-10 |
| LO 9-2320-280-12 | AR 750-1 |
| TM 9-2320-272-10 | AR 750-43 |
| TM 9-2320-272-24-1 | DA PAM 738-750 |
| TM 9-2320-272-24-2 | FM 9-43-2 |
| TM 9-2320-272-24-3 | TC 43-35 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-280-10 | TM 9-8000 |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |

Subject Area 19: SPECIAL PURPOSE KITS

Correct Malfunction of 100 AMP Alternator on a Light Wheeled Vehicle

091-63B-1213

Conditions: In a field or garrison environment given a representative light wheel vehicle, ( M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Corrected  malfunction of 100 AMP alternator on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Checked for loose, broken or missing alternator belts. | —— | —— |
| 6. Tested alternator circuit 568 for proper voltage. | —— | —— |
| 7. Repaired or replaced faulty wires. | —— | —— |
| 8. Replaced alternator. | —— | —— |
| 9. Verified fault had been corrected. | —— | —— |
| 10. Completed TAMMS form, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Subject Area 20: CENTRAL TIRE INFLATION SYSTEM (CTIS)

Troubleshoot Central Tire Inflation System on a Light Wheeled Vehicle

091-63B-1218

Conditions: In a field or garrison environment given a representative light wheel vehicle, ( M44A2/3 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures on the Central Tire Inflation System (CTIS) on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used Applicable publications. | —— | —— |
| 2. Selected /used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Released air pressure before removing air system components. | —— | —— |
| 5. Followed troubleshooting procedures outlined in vehicle technical manual. | —— | —— |
| 6. Wrapped all male threads with antisieze tape. | —— | —— |
| 7. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-361-10 | TM 9-8000 |
| TM 9-2320-361-20 |  |
| TM 9-2320-386-10 |  |
| TM 9-2320-386-24 |  |
| TM 9-2320-386-24P |  |

Replace Air Lines and Fittings on a Light Wheeled Vehicle

091-63B-1219

Conditions: In a field or garrison environment given a representative light wheel vehicle, ( M44A2/3 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced  air lines and fittings on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Released air pressure before removing air system components. | —— | —— |
| 6. Removed air line and fitting. | —— | —— |
| 7. Wrapped all male threads with antisieze tape. | —— | —— |
| 8. Installed new line and fitting. | —— | —— |
| 9. Verified fault had been corrected. | —— | —— |
| 10. Complete TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-361-10 | TM 9-8000 |
| TM 9-2320-361-20 |  |
| TM 9-2320-386-10 |  |
| TM 9-2320-386-24 |  |

Correct Malfunction of Air Dryer With Filter on a Light Wheeled Vehicle

091-63B-1220

Conditions: In a field or garrison environment given a representative light wheel vehicle, ( M44A2/3 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Corrected malfunction of air dryer With filter on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications.  When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Released air pressure before removing air system components. | —— | —— |
| 6. Plugged ends of air lines and tags for installation | —— | —— |
| 7. Used scribe to mark components for alignment. | —— | —— |
| 8. Removed filter. | —— | —— |
| 9. Installed new filter and installed components. | —— | —— |
| 10. Wrapped sealing tape around fitting. | —— | —— |
| 11. Completed TAMMS forms, as required. | —— | —— |
| 12. Tied back air line using plastic tie downs. | —— | —— |
| 13. Verified fault had been corrected. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-361-10 | TM 9-8000 |
| TM 9-2320-361-20 |  |
| TM 9-2320-386-10 |  |
| TM 9-2320-386-24 |  |

Replace CTIS Pressure Switch on a Light Wheeled Vehicle

091-63B-1224

Conditions: In a field or garrison environment given a representative light wheel vehicle, ( M44A2/3 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Replaced Central Tire Inflation System (CTIS) pressure switch on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission capable, or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Released air pressure before removing air system components. | —— | —— |
| 6. Disconnected battery ground cable. | —— | —— |
| 7. Removed air lines from pressure switch. | —— | —— |
| 8. Disconnect pressure switch from wiring harness. | —— | —— |
| 9. Wrapped fittings with sealing tape. | —— | —— |
| 10. Installed lines and connected wiring harness. | —— | —— |
| 11. Tied lines back with new plastic tie downs. | —— | —— |
| 12. Verified fault had been corrected. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-361-10 | TM 9-8000 |
| TM 9-2320-361-20 |  |
| TM 9-2320-386-10 |  |
| TM 9-2320-386-24 |  |

Correct Malfunction of CTIS Front and Rear Air Seals on a Light Wheeled Vehicle

091-63B-1226

Conditions: In a field or garrison environment given a representative light wheel vehicle, (M44A2/3 series / M939 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Corrected malfunction of Central Tire Inflation System (CTIS) front and rear air seals on a light wheeled vehicle IAW the applicable technical publications, procedures, and specifications. When this task was completed, the vehicle was fully mission capable or maintenance actions required to be performed by other than 63B personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Released air pressure before removing air system components. | —— | —— |
| 6. Removed malfunctioning wheel valve. | —— | —— |
| 7. Ensured compressed air source did not exceed 30 psi. | —— | —— |
| 8. Inspected wheel valve assembly for cracks, leaks, or stripped threads. | —— | —— |
| 9. Wrapped all fittings with sealing tape. | —— | —— |
| 10. Verified fault had been corrected. | —— | —— |
| 11. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-361-10 | TM 9-8000 |
| TM 9-2320-361-20 |  |
| TM 9-2320-386-10 |  |
| TM 9-2320-386-24 |  |

Subject Area 21: GENERAL MAINTENANCE TASKS

Maintain Test, Measurement, and Diagnostic Equipment on a Light Wheeled Vehicle

091-63B-1228

Conditions: In a field or garrison given required materials, general mechanic's tool kit,(M998 series) vehicle, and applicable TM(s).

Standards: Maintained test, measurement, and diagnostic equipment on a light wheeled vehicle  IAW technical publications, procedures, and specifications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Followed prescribed safety procedures. | —— | —— |
| 3. Practiced maintenance discipline. | —— | —— |
| 4. Inspected/tested TMDE. | —— | —— |
| 5. Checked TMDE calibration records as required by MAC. | —— | —— |
| 6. Performed required PMCS. | —— | —— |
| 7. Conducted operational check of TMDE. | —— | —— |
| 8. Completed TAMMS form, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TB 9-4910-555-35 | AR 385-10 |
| TM 11-6625-3052-14 | AR 750-1 |
| TM 9-2320-280-10 | AR 750-43 |
| TM 9-2320-280-20-1 | DA PAM 738-750 |
| TM 9-2320-280-20-2 | TM 9-243 |
| TM 9-2320-280-20-3 | TM 9-8000 |

Maintain Assigned Vehicle

091-63B-1229

Conditions: In a field or garrison given required materials,(M998 series) vehicle, general mechanic's tool kit, and applicable TM(s).

Standards: Maintained assigned vehicle IAW technical publications, procedures, and specifications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Followed prescribed safety procedures. | —— | —— |
| 3. Practiced maintenance discipline. | —— | —— |
| 4. Used the operator -10 manual PMCS table to inspect vehicle. | —— | —— |
| 5. Identified shortcomings and deficiencies. | —— | —— |
| 6. Checked the uncorrected fault record for noted shortcomings. | —— | —— |
| 7. Made adjustments, repairs, or replacements outlined in the -10 manual. | —— | —— |
| 8. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-280-12 | AR 385-10 |
| TM 9-2320-280-10 | AR 750-1 |
|  | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Maintain Assigned Tool Kit

091-63B-1230

Conditions: In a field or garrison environment given required materials, general mechanic's tool kit, and applicable TM(s).

Standards: Maintained assigned tool kit  IAW technical publications, procedures, and specifications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Followed prescribed safety procedures. | —— | —— |
| 3. Practiced maintenance discipline. | —— | —— |
| 4. Inspected tool box for broken rivets or welds. | —— | —— |
| 5. Repaired any broken rivets or welds with rivet gun. | —— | —— |
| 6. Inventoried and inspected tools for serviceability. | —— | —— |
| 7. Repaired or replaced any unserviceable tools. | —— | —— |
| 8. Cleaned tools using applicable lubricants. | —— | —— |
| 9. Stored tool box. | —— | —— |
| 10. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-243 | AR 750-1 |
|  | AR 750-43 |
|  | DA PAM 738-750 |

Prepare Equipment Inspection Maintenance Worksheet (DA Form 2404 or ULLS Equivalent)

091-63B-1231

Conditions: In a field or garrison environment given a representative light wheel vehicle, M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Prepared  Equipment Inspection Maintenance Worksheet (DA Form 2404 or ULLS equivalent) IAW technical publications, procedures, and specifications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Followed prescribed safety procedures. | —— | —— |
| 3. Practiced maintenance discipline. | —— | —— |
| 4. Performed operator PMCS outlined in the -10 manual. | —— | —— |
| 5. Performed all only the items that pertained to the designated service interval. | —— | —— |
| 6. Followed correct sequence outlined in the -20 maintenance manual. | —— | —— |
| 7. Identified a minimum of 80percent of shortcomings and deficiencies. | —— | —— |
| 8. Performed lubrication of vehicle IAW lube order. | —— | —— |
| 9. Annotated TAMMS forms, as required, | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-280-12 | AR 385-10 |
| TM 9-2320-280-10 | AR 750-1 |
| TM 9-2320-280-20-1 | DA PAM 738-750 |
| TM 9-2320-280-20-2 | TM 9-243 |
| TM 9-2320-280-20-3 | TM 9-8000 |

Perform Scheduled Preventive Maintenance Checks and Services on a Light Wheeled Vehicle

091-63B-1234

Conditions: In a field or garrison environment given a representative light wheel vehicle,  (M998 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Perform scheduled Preventive Maintenance Checks and Services (PMCS) on a light wheeled vehicle IAW technical publications, procedures, and specifications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Followed prescribed safety procedures. | —— | —— |
| 3. Practiced maintenance discipline. | —— | —— |
| 4. Performed operator PMCS outlined in the -10 manual. | —— | —— |
| 5. Performed only the items that pertained to the designated service interval. | —— | —— |
| 6. Followed correct sequence out lined in the - 20 maintenance manual. | —— | —— |
| 7. Identified a minimum of 80percent of the shortcomings and deficiencies. | —— | —— |
| 8. Performed lubrication of vehicle IAW lube order. | —— | —— |
| 9. Annotated TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-280-12 | AR 385-10 |
| TM 9-2320-280-10 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Subject Area 22: RECOVERY  (ASI H8 Tasks ONLY)

Locate a Recovery Site

091-H8C-2001

Conditions: In a classroom/field environment, given assistance, a military map 1:50,000  scale, protractor, straight edge and FM 21-26.

Standards: Locate a recovery site to within 10 meters and identify primary and alternate recovery routes determining distance for both with no greater than a 10% error.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Identified terrain features. | —— | —— |
| 3. Identified map symbols and colors. | —— | —— |
| 4. Located site using military grid reference system. | —— | —— |
| 5. Calculated distance. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 21-26 | TC 43-35 |
| FM 21-31 |  |

Determine Recovery Methods

091-H8C-2002

Conditions: In a classroom and field environment, given FM 9-43-2, FM 5-125, Rigging Card, pencil and paper, snatch blocks, wire ropes and cables.

Standards: Determine Recovery Methods, source of effort and mechanical advantage needed IAW references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected and used applicable publications. | —— | —— |
| 2. Reconnoitered area. | —— | —— |
| 3. Estimated situation. | —— | —— |
| 4. Calculated ratios. | —— | —— |
| 5. Obtained resistance. | —— | —— |
| 6. Verified solution. | —— | —— |
| 7. Erected rigging. | —— | —— |
| 8. Rechecked rigging. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 5-125 |  |
| FM 9-43-2 |  |
| TC 43-35 |  |

Operate Tactical Communications Equipment

091-H8C-2003

Conditions:  In a classroom/field environment given a FM radio,  recovery vehicle, TM 11-5820-890-10-3, FM 24-35, and training SOI/DRYAD.

Standards: The soldier will state the procedures to install, operate, use correct radio procedures for clear concise and secure communication IAW the appropriate publications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Prepared communication equipment for operation. | —— | —— |
| 3. Send tactical communications. | —— | —— |
| 4. Received tactical communications. | —— | —— |
| 5. Shut down tactical communication operation. | —— | —— |
| 6. Followed prescribed safety procedures. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 24-35 | FM 24-18 |
| TM 11-5820-890-10-3 | TC 43-35 |
|  | TM 11-5820-401-10-1 |
|  | TM 11-5820-401-10-2 |
|  | TM 11-5820-401-10-4 |
|  | TM 11-5830-340-12 |

Operate Metal Cutting Equipment

091-H8C-2004

Conditions: In a classroom/shop environment with assistance, given oxyacetylene equipment, tools, safety equipment, and applicable references.

Standards: Set up the oxyacetylene equipment, cut metal, and practice shop safety IAW the procedures in the applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Determined the method to cut metal. | —— | —— |
| 3. Prepared metal cutting equipment as required. | —— | —— |
| 4. Cut metal. | —— | —— |
| 5. Secured metal cutting equipment. | —— | —— |
| 6. Followed prescribed safety procedures. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TC 9-237 | AR 385-10 |
|  | AR 750-1 |
|  | DA PAM 738-750 |
|  | TC 43-35 |
|  | TM 9-243 |

Perform Preventive Maintenance Checks And Services (PMCS) On Wheeled Recovery Vehicle

091-H8W-2001

Conditions: In a garrison or field environment with assistance and supervision,given applicable recovery vehicle with BII, general mechanic's tool kit, lubricants if required, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts, if needed.

Standards: The PMCS must be performed IAW the applicable technical publications' procedures and specifications. When this task is completed, the vehicle must be fully mission capable or maintenance actions required to be performed by other than recovery personnel must be identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used proper tools/TMDE. | —— | —— |
| 3. Described operation of vehicle systems/subsystems. | —— | —— |
| 4. Determined readiness of system components. | —— | —— |
| 5. Identified deficiencies and shortcomings. | —— | —— |
| 6. Corrected shortcomings identified as operator maintenance. | —— | —— |
| 7. Followed prescribed safety procedures. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-260-10 | DA PAM 738-750 |
|  | TM 11-5820-401-10-1 |
|  | TM 11-5820-401-10-2 |
|  | TM 11-5820-401-10-4 |
|  | TM 11-5820-498-12 |
|  | TM 11-5830-340-12 |
|  | TM 9-243 |
|  | TM 9-8000 |

Use And Maintain Basic Issue Items (BII) Related To Wheeled Recovery Operations

091-H8W-2002

Conditions: In a garrison or field environment with assistance and supervision, given applicable recovery vehicle with BII, general mechanic's tool kit, lubricants if required, applicable special tools/TMDE, required safety equipment, applicable forms and references. Use and maintain basic issue items (BII) related to wheeled recovery operations.

Standards: Use and maintain basic issue items (BII) Related To Wheeled Recovery Operations IAW applicable FM procedures and specifications. NOTE: All safety precautions must have been observed.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used correct publications. | —— | —— |
| 2. Used M578 to recover mired vehicle. | —— | —— |
| 3. Use winch. | —— | —— |
| 4. Used block and tackle. | —— | —— |
| 5. Used BII to recover mired vehicle. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TC 43-35 | AR 385-10 |
| TM 9-2320-260-10 | AR 750-1 |
| TM 9-2320-272-10 | AR 750-43 |
| TM 9-2320-280-10 | DA PAM 738-750 |
|  | TM 9-243 |

Drive Wheeled Recovery Vehicle

091-H8W-2003

Conditions: In a garrison or field environment with assistance and supervision, given applicable recovery vehicle with BII, general mechanic's tool kit, lubricants if required, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts, if needed.

Standards: Drive a  wheeled recovery vehicle, tow a disabled vehicle to a predetermined location using the boom and tow bar without causing damage to the equipment or injury to personnel IAW applicable publications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used correct publications. | —— | —— |
| 2. Performed PMCS. | —— | —— |
| 3. Operated vehicle IAW TM. | —— | —— |
| 4. Completed TAMMS forms as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| DA PAM 738-750 | AR 385-10 |
| TM 9-2320-260-10 | TC 43-35 |
| TM 9-2320-272-10 |  |
| TM 9-2320-279-10-1 |  |
| TM 9-2320-279-10-2 |  |

Operate Boom/Hoist, Wheeled Recovery Vehicle

091-H8W-2004

Conditions: In a garrison or field environment with assistance and supervision, given applicable recovery vehicle with BII, general mechanic's tool kit, lubricants if required, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts, if needed.

Standards: Operate boom/hoist to recovery a disabled vehicle and tow bar without causing damage to the equipment or injury to personnel IAW applicable publications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used correct publications. | —— | —— |
| 2. Used/operated boom/hoist IAW TMs and FM. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-260-10 | AR 385-10 |
| TM 9-2320-272-10 | DA PAM 738-750 |
| TM 9-2320-279-10-1 | DA PAM 738-751 |
| TM 9-2320-279-10-2 | TC 43-35 |

Operate The Retrieval System on a Wheeled Vehicle

091-H8W-2005

Conditions: In a garrison or field environment with assistance and supervision, given applicable recovery vehicle with BII, general mechanic's tool kit, lubricants if required, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts, if needed. Operate wheeled recovery vehicle retrieval system (HEMTT).

Standards: Operate wheeled recovery vehicle retrieval system (HEMTT)recover a vehicle and tow  without causing damage to the equipment or injury to personnel IAW applicable publications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Position recovery vehicle. | —— | —— |
| 2. Select proper vehicle hookup devices. | —— | —— |
| 3. Connect hookup devices to disabled vehicle. | —— | —— |
| 4. Connect retrieval system to disabled vehicle. | —— | —— |
| 5. Tow disabled vehicle. | —— | —— |
| 6. Disconnect retrieval system. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-279-10-1 | AR 385-10 |
| TM 9-2320-279-10-2 | AR 750-1 |
|  | DA PAM 738-750 |
|  | FM 21-60 |
|  | FM 4-30.3 (FM 9-43-1) |
|  | FM 9-43-2 |
|  | TC 43-35 |

Operate Winches on a Wheeled Recovery Vehicle

091-H8W-2006

Conditions: In a garrison or field environment with assistance and supervision, given applicable recovery vehicle with BII, general mechanic's tool kit, lubricants if required, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts, if needed.

Standards: Operate winches to recover an wheeled vehicle and tow  without causing damage to the equipment or injury to personnel IAW applicable publications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used correct publications. | —— | —— |
| 2. Used/operated winches IAW TMs and FM. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-279-10-1 | AR 750-1 |
| TM 9-2320-279-10-2 | DA PAM 738-750 |
|  | FM 21-60 |
|  | FM 4-30.3 (FM 9-43-1) |
|  | FM 9-43-2 |
|  | TM 9-243 |

Recover a Mired Wheeled Vehicle

091-H8W-2007

Conditions: In a garrison or field environment with assistance and supervision, given applicable recovery vehicle with BII, general mechanic's tool kit, lubricants if required, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts, if needed.

Standards: recover an mired wheeled vehicle and tow to a predetermined location using the boom and tow bar without causing damage to the equipment or injury to personnel IAW applicable publications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used correct publications. | —— | —— |
| 2. Determined recovery methods. | —— | —— |
| 3. Recovered mired vehicle IAW TM and FM. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-279-10-1 | DA PAM 738-750 |
| TM 9-2320-279-10-2 | TC 43-35 |

Recover an Overturned Vehicle

091-H8W-2008

Conditions: In a garrison or field environment with assistance and supervision, given applicable recovery vehicle with BII, general mechanic's tool kit, lubricants if required, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts, if needed.

Standards: recover an overturned vehicle and tow to a predetermined location using the boom and tow bar without causing damage to the equipment or injury to personnel IAW applicable publications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Performed PMCS. | —— | —— |
| 3. Started engine. | —— | —— |
| 4. Placed vehicle in motion. | —— | —— |
| 5. Drove vehicle, maintaining proper engine speed when descending and ascending grades. | —— | —— |
| 6. Drove vehicle in reverse. | —— | —— |
| 7. Stopped vehicle. | —— | —— |
| 8. Parked vehicle. | —— | —— |
| 9. Stopped engine (normal and emergency procedures). | —— | —— |
| 10. Completed TAMMS forms as required. | —— | —— |
| 11. Followed prescribed safety procedures. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO- GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-211-20P | AR 385-10 |
| TM 9-2320-211-35 | DA PAM 738-750 |
| TM 9-2320-272-10 | TC 43-35 |
| TM 9-2320-279-10-1 |  |
| TM 9-2320-279-10-2 |  |
| TM 9-2320-280-10 |  |

Tow a Wheel Vehicle Using a Retrieval System

091-H8W-2009

Conditions: In a garrison or field environment with assistance and supervision, given applicable recovery vehicle with BII, general mechanic's tool kit, lubricants if required, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts, if needed.

Standards: Tow a disabled wheeled vehicle to a predetermined location using the retrieval system without causing damage to the equipment or injury to personnel IAW applicable publications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Positioned recovery vehicle. | —— | —— |
| 2. Selected proper vehicle hookup devices. | —— | —— |
| 3. Connected hookup devices to disabled vehicle. | —— | —— |
| 4. Connected retrieval system to disabled vehicle. | —— | —— |
| 5. Towed disabled vehicle. | —— | —— |
| 6. Disconnected retrieval system. | —— | —— |
| 7. Disconnected hookup devices to disabled vehicle. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| DA PAM 738-750 | AR 385-10 |
| TM 9-2320-270-10 |  |
| TM 9-2320-272-10 |  |
| TM 9-2320-279-10-1 |  |
| TM 9-2320-279-10-2 |  |

Tow a Wheel Vehicle Using the Boom and Tow Bar

091-H8W-2010

Conditions: In a garrison or field environment with assistance and supervision, given applicable recovery vehicle with BII, general mechanic's tool kit, lubricants if required, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts, if needed.

Standards: Tow a disabled vehicle to a predetermined location using the boom and tow bar without causing damage to the equipment or injury to personnel IAW applicable publications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Followed prescribed safety procedures. | —— | —— |
| 3. Positioned recovery vehicle. | —— | —— |
| 4. Prepared vehicle for towing. | —— | —— |
| 5. Prepared recovery vehicle for towing operation. | —— | —— |
| 6. Attached towing bar to disabled vehicle. | —— | —— |
| 7. Operated boom. | —— | —— |
| 8. Towed disabled vehicle. | —— | —— |
| 9. Disconnected towed vehicle. | —— | —— |
| 10. Secured recovery equipment. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 9-43-2 | AR 385-10 |
| TM 9-2320-260-10 | DA PAM 738-750 |
| TM 9-2320-272-10 |  |
| TM 9-2320-279-10-1 |  |
| TM 9-2320-279-10-2 |  |

Perform Self Recovery On A Wheeled Vehicle

091-H8W-2011

Conditions: Given a wheel vehicle requiring self/ field expedient recovery, Bll, general mechanic's tool kit and applicable
references to perform self recovery on a wheel vehicle.

Standards: Perform self recovery on a wheeled vehicle.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used correct publications. | —— | —— |
| 2. Performed expedient recovery using applicable references. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-260-10 | AR 385-10 |
| TM 9-2320-272-10 | DA PAM 738-750 |
|  | TC 43-35 |

Perform Field Expedient Recovery on a Wheeled Vehicle

091-H8W-2012

Conditions: Given a wheel vehicle requiring field expedient recovery, Bll, general mechanic's tool kit and applicable
references to perform self recovery on a wheel vehicle,

Standards: Perform Field Expedient Recovery on a Wheeled Vehicle

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Determined method of field expedient recovery. | —— | —— |
| 3. Prepared vehicle for field expedient recovery as required. | —— | —— |
| 4. Performed vehicle field expedient recovery. | —— | —— |
| 5. Secured recovery equipment. | —— | —— |
| 6. Followed prescribed safety procedures. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 9-43-2 | AR 385-10 |
| TC 43-35 | DA PAM 738-750 |
| TM 9-2320-279-10-1 |  |
| TM 9-2320-279-10-2 |  |

Skill Level 3

Subject Area 23: COMMON LOGISTIC TASKS (SL 3)

Manage a Shop Safety Program

091-CLT-3001

Conditions: In a field or garrison environment, given a maintenance site/facility, maintenance personnel, and applicable references.

Standards: Ensured personnel followed all safety procedures, that preventable accidents were avoided, and if accidents occurred that they were properly recorded and reported, IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured all safety references were on hand. | —— | —— |
| 2. Established and documented goals and requirements for a successful shop safety and accident prevention program. | —— | —— |
| 3. Briefed and regularly updated subordinates on shop safety program. | —— | —— |
| 4. Conducted initial safety inspections. | —— | —— |
| 5. Ensured initial safety concerns and violations were corrected. | —— | —— |
| 6. Conducted scheduled and unscheduled safety inspections. | —— | —— |
| 7. Documented safety violations, reported the violations as required, and conducted follow-up inspections to ensure violations were/remained corrected. | —— | —— |
| 8. Kept necessary records of safety inspections and accident reports. | —— | —— |
| 9. Ensured MSDS were prepared and maintained as required in applicable work areas. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AR 190-13 | AR 385-10 |
| AR 220-1 | AR 385-40 |
| AR 700-138 | AR 385-55 |
| AR 750-1 |  |
| DA PAM 738-750 |  |
| FM 4-30.3 (FM 9-43-1) |  |
| TB 43-180 |  |

Maintain a Publications Library

091-CLT-3002

Conditions: In a field or garrison environment, given publications and storage location, local and higher headquarters publications indexes and publications procedures, SOP, and applicable forms and references.

Standards: Ensured required publications were on hand or ordered, publications were arranged and maintained properly, forms/records were properly maintained, and changes were posted IAW applicable references and local procedures.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Determined all publications required by the maintenance shop or section. | —— | —— |
| 2. Reviewed and updated publications library SOP as needed. | —— | —— |
| 3. Ensured that technical publications on hand/on order were the most current IAW DA Pam 25-30. | —— | —— |
| 4. Ensured that doctrinal, training, and organizational publications on hand/on order were the most current IAW DA Pam 25-30 and local listings. | —— | —— |
| 5. Ensured that administrative publications on hand/on order were the most current IAW DA Pam 25-30. | —— | —— |
| 6. Ensured that local and higher headquarters publications on hand/on order were the most current IAW DA Pam 25-30 and local listings. | —— | —— |
| 7. Prepared DA Form 4569 IAW DA Pam 25-33. | —— | —— |
| 8. Prepared the required transmittal form IAW DA Pam 25-33. | —— | —— |
| 9. Prepared DA Forms 17 and 17-1 to request local and higher headquarters publications, IAW DA Pam 25-33 and local/higher headquarters' publications requisitioning procedures. | —— | —— |
| 10. Ensured that published changes were posted to applicable publications IAW DA PAM 25-40 and publication change instructions. | —— | —— |
| 11. Removed obsolete/rescinded/superseded publications from library IAW DA Pam 25-40 and publication change instructions. | —— | —— |
| 12. Arranged publications in proper order and in a suitable location IAW DA Pam 25-40. | —— | —— |
| 13. Labeled binders used for storing library publications IAW AR 25-400-2 applicable) and DA Pam 25-40. | —— | —— |
| 14. Notified personnel to return loaned publications to the library in a timely manner IAW SOP. | —— | —— |
| 15. Updated US Army Publishing Agency (USAPA), local, and higher headquarters publications accounts as required IAW DA Pam 25-33 and local/higher headquarters publication account instructions. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AR 25-400-2 | AR 25-11 |
| DA PAM 25-30 |  |
| DA PAM 25-33 |  |

Establish Maintenance Facilities

091-CLT-3003

Conditions: In a field or garrison environment, given a maintenance site, maintenance personnel, applicable equipment, maintenance shop/section SOP, and applicable references.

Standards: Set up a maintenance shop facility suitable for accomplishing necessary maintenance functions IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured applicable references and publications were available. | —— | —— |
| 2. Identified commander's maintenance requirements for the accomplishment of the unit's mission. | —— | —— |
| 3. Set up the maintenance facility IAW SOP. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 4-30.3 (FM 9-43-1) |  |

Assist in Preparing a Standing Operating Procedure

091-CLT-3004

Conditions: In a field or garrison environment, given FM 9-43-1, higher headquarters  SOP(s), and commander's guidance.

Standards: Prepared a draft copy of a maintenance shop/section internal or external SOP for supervisor's review, comment, and approval IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured applicable publications were available. | —— | —— |
| 2. Ensured unit policies and commander's guidance were followed. | —— | —— |
| 3. Ensured shop operation policies were adequately addressed. | —— | —— |
| 4. Updated the shop SOP as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 4-30.3 (FM 9-43-1) |  |

Manage Tool Control Procedures

091-CLT-3005

Conditions: In a field or garrison environment, given applicable supply catalog(s), applicable references, and hand receipt forms.

Standards: Managed tool control procedures IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured applicable references were available. | —— | —— |
| 2. Established policies and procedures for the control of tools. | —— | —— |
| 3. Ensured all DA Form 2062s were properly filled out and updated. | —— | —— |
| 4. Ensured tools and equipment were inventoried IAW applicable references. | —— | —— |
| 5. Ensured tool shortages were annotated on a shortage annex. | —— | —— |
| 6. Ensured subordinates applied property accountability procedures. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AR 190-13 | DA PAM 738-750 |
| AR 220-1 |  |
| AR 385-10 |  |
| AR 385-40 |  |
| AR 700-138 |  |
| AR 750-1 |  |
| DA PAM 710-2-1 |  |
| FM 101-5-1 |  |
| FM 4-30.3 (FM 9-43-1) |  |

Manage Key Control Procedures

091-CLT-3006

Conditions: In a field or garrison environment, given keys, key control rosters, key boxes/cabinets, and applicable publications.

Standards: Managed key control procedures IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured necessary publications were available. | —— | —— |
| 2. Established key control policies and procedures. | —— | —— |
| 3. Established key control access rosters. | —— | —— |
| 4. Ensured personnel were aware of their responsibilities for the security and accountability of keys. | —— | —— |
| 5. Ensured key control access rosters were properly maintained and adhered to. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AR 190-13 |  |
| AR 190-51 |  |

Manage the TMDE Calibration Program

091-CLT-3007

Conditions: In a field or garrison environment, given TMDE, maintenance personnel, and applicable references.

Standards: Managed the TMDE calibration program IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured necessary publications were available. | —— | —— |
| 2. Reviewed and updated TMDE computer printout list. | —— | —— |
| 3. Ensured PMCS and inventory of all TMDE and auxiliary equipment are conducted, as required. | —— | —— |
| 4. Ensured TMDE was turned in for calibration IAW computer printouts. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AR 750-43 |  |
| TB 43-180 |  |

Recon Terrain/Route

091-CLT-3008

Conditions: In a field environment, given a maintenance situation/operations order (OPORD), operational overlay, grid coordinates of destination, vehicle with personnel, and applicable references.

Standards: Performed a route/terrain reconnaissance, and selected the most appropriate route to follow or the most appropriate location to set up a maintenance site, IAW maintenance situation/OPORD and applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured necessary equipment and publications were available. | —— | —— |
| 2. Performed a map recon of the terrain and route. | —— | —— |
| 3. Selected personnel for recon team. | —— | —— |
| 4. Reconned route to determine best access to destination and to ensure safety of personnel and equipment. | —— | —— |
| 5. Reconned terrain to determine suitability for maintenance site use, to determine best avenues of entry and exit, and to ensure safety of personnel and equipment. | —— | —— |
| 6. Reported findings and conclusions to supervisors. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 4-30.3 (FM 9-43-1) |  |
| FM 5-170 |  |

Supervise Maintenance Operations

091-CLT-3009

Conditions: In a field or garrison environment, given maintenance personnel, equipment, maintenance facility/site, SOPs, and applicable references.

Standards: Established and maintained an effective maintenance shop operation IAW SOPs and applicable references.

Performance Steps

1. Ensure unit maintenance procedures are IAW AR 750-1, DA Pam 750-35 and local major command (MACOM) policies.

a. Review unit standing operating procedures (SOP) for maintenance.

b. Inform unit personnel of changes in policy and new policy that impacts unit SOP

2. Provide technical assistance to unit maintenance activities.

a. Inspect unit maintenance operations

b. Identify shortcomings

c. Make recommendations for corrective action.

d. provide training in maintenance procedures.

3. Provide maintenance management to units.

a. Review reports (MCRS and ULLS-G).

b. Coordinate with higher level maintenance activities

c. Direct cross-leveling of maintenance assets/workload.

d. Prioritize maintenance efforts of units.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Reviewed unit SOP as scheduled | —— | —— |
| 2. Compared unit SOP against standards set in 750-35-35 (Aug 94), Pg. | —— | —— |
| 3. Completed regular inspection of unit operations. | —— | —— |
| 4. Compared unit operations against standards in AR 750-1, Da Pam 738-750 and DA 750, and DA Pam 750-35. | —— | —— |
| 5. Inspect environmental protection practices for compliance. | —— | —— |
| 6. Review safety program practices for compliance with AR 220-1. | —— | —— |
| 7. Recorded and submitted deficiencies to proper personnel for correction. | —— | —— |
| 8. Recorded training needs. | —— | —— |
| 9. Coordinated with appropriate personnel to provide needed training. | —— | —— |
| 10. Reviewed MCSR for accuracy and compliance with standards in AR 700-138, ADSM-25-L3N-AWA-EUM, and AISM -25-L3Q-AWC-ZZZ-CG. | —— | —— |
| 11. Coordinated with appropriate maintenance level to correct maintenance discrepancies. | —— | —— |
| 12. Coordinated with TRADOC and AMC to ensure that emerging issues are addressed appropriately at the unit. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AR 190-51 |  |
| AR 385-10 |  |
| AR 385-40 |  |
| AR 385-55 |  |
| AR 600-55 |  |
| AR 700-4 |  |
| AR 710-2 |  |
| AR 725-50 |  |
| AR 735-11-1 |  |
| AR 735-5 |  |
| AR 750-43 |  |
| DA PAM 25-30 |  |
| DA PAM 710-2-2 |  |
| DA PAM 738-750 |  |
| DA PAM 750-1 |  |
| FM 4-30.3 (FM 9-43-1) |  |

Interpret Maintenance Operational Overlay

091-CLT-3010

Conditions: In a field or garrison environment, given an operational overlay, map, maintenance situation/OPORD, and applicable references.

Standards: Interpreted the maintenance operational overlay by identifying key features and elements of the area of operation IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured necessary references and materials were available. | —— | —— |
| 2. Identified mapping symbols on the operational overlay. | —— | —— |
| 3. Identified key features of the map and operational overlay. | —— | —— |
| 4. Identified key elements of the area of operation on the map and operational overlay. | —— | —— |
| 5. Updated the operational overlay, as necessary. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 101-5-1 |  |
| FM 4-30.3 (FM 9-43-1) |  |
| FM 5-170 |  |

Manage the Unit Level Logistics System (ULLS)

091-CLT-3013

Conditions: In a field or garrison environment, given a computer system(s) with Unit Level Logistics System-Ground (ULLS-G) software, database of equipment files, associated Army Materiel Status System (AMSS) software, ULLS operator, and applicable references.

Standards: Supervised ULLS-G functions of a unit-level maintenance shop IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured necessary equipment and references were available. | —— | —— |
| 2. Ensured ULLS operator was properly trained. | —— | —— |
| 3. Reviewed the ULLS system flow of information to and from system interfaces. | —— | —— |
| 4. Reviewed ULLS-G maintenance forms for accuracy. | —— | —— |
| 5. Analyzed ULLS-G reports and data to identify maintenance trends and problems. | —— | —— |
| a. Document register. |  |  |
| b. PLL inventory report. |  |  |
| c. Zero balance report. |  |  |
| d. PLL excess management report. |  |  |
| e. PLL inquiry. |  |  |
| f. Not mission capable (NMC) report. |  |  |
| 6. Analyzed AMSS reports and data to identify maintenance trends and problems. | —— | —— |
| a. AMSS Authorization Report. |  |  |
| b. Projected fully mission capable ( FMC) Rates Report. |  |  |
| c. Equipment exception report. |  |  |
| d. System status summary. |  |  |
| e. Class IX failure data by administrative number. |  |  |
| f. Rollup by equipment identification code ( EIC). |  |  |
| g. Rollup by unit identification code (UIC). |  |  |
| h. Non mission capable (NMC) Report. |  |  |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AR 710-2 |  |
| DA PAM 710-2-1 |  |

Manage the Unit Army Oil Analysis Program (AOAP)

091-CLT-3014

Conditions: In a field or garrison environment, given Automated Oil Analysis Log Printout, unit and higher headquarters' AOAP SOPs and policies, and applicable references.

Standards: Managed the unit AOAP IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured necessary publications were available. | —— | —— |
| 2. Reviewed the objectives and policies of the AOAP Program. | —— | —— |
| 3. Identified responsibilities of key AOAP personnel. | —— | —— |
| 4. Ensured sampling intervals and procedures were followed. | —— | —— |
| 5. Ensured samples are processed IAW applicable references and SOPs. | —— | —— |
| 6. Ensured lab results are processed IAW applicable references and SOPs, and follow-up actions were completed. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO-GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| DA PAM 738-750 |  |
| TB 43-0211 |  |

Deploy Company Maintenance Team/Recovery Support Team

091-CLT-3015

Conditions: In a field or garrison environment, given a request for maintenance support/maintenance situation, map, operational overlay, grid coordinates of destination, vehicle(s), equipment, maintenance personnel, and applicable references.

Standards: Deployed the company maintenance team/recovery support team IAW the maintenance situation/request for maintenance support and applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Reviewed the request for maintenance support/maintenance situation. | —— | —— |
| 2. Determined personnel and equipment requirements necessary to perform the mission. | —— | —— |
| 3. Identified available resources for the company maintenance team/recovery support team, including personnel with applicable MOSs, vehicle(s), tools, test equipment, publications, repair parts, time, and facilities, as necessary. | —— | —— |
| 4. Determined requirements for defending the team. | —— | —— |
| 5. Briefed the team on the mission: | —— | —— |
| a. Reviewed the operational overlay. |  |  |
| b. Conducted a map recon of the route and destination. |  |  |
| 6. Deployed the maintenance support team. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 101-5-1 |  |
| FM 4-30.3 (FM 9-43-1) |  |
| FM 5-170 |  |

Review the Army Materiel Status System (AMSS) Reports

091-CLT-3016

Conditions: In a field or garrison environment, given AMSS reports produced from an ULLS-G system, and applicable references.

Standards: Analyzed AMSS reports and data to identify maintenance trends and problems IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured necessary ULLS equipment and references were available. | —— | —— |
| 2. Analyzed AMSS reports and data to identify maintenance trends and problems. | —— | —— |
| a. AMSS authorization report. |  |  |
| b. Projected FMC rates report. |  |  |
| c. Equipment exception report. |  |  |
| d. System status summary. |  |  |
| e. Class IX failure data by administrative number. |  |  |
| f. Rollup by EIC. |  |  |
| g. Rollup by UIC. |  |  |
| h. NMC report. |  |  |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AR 710-2 |  |
| DA PAM 710-2-1 |  |

Subject Area 24: TECHNICAL TASKS (SL 3)

Perform Diagnostic Procedures of  Track Vehicle's Fire Extinguisher/Suppression System

091-63B-3001

Conditions: In a field or garrison environment given a representative(M88A1, M88A2) track vehicle,  required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures of  track vehicle's fire extinguisher/suppression system IAW technical publications, procedures and specifications and after completion the vehicle's fire suppression/fire extinguisher system was fully mission capable.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Determined maintenance action to be performed. | —— | —— |
| 3. Verified applicable technical publications were available. | —— | —— |
| 4. Ensured proper tools, TMDE and equipment were available to inspect, repair/replace and test the fire extinguisher/suppression system. | —— | —— |
| 5. Performed initial inspection of fire extinguisher system. | —— | —— |
| 6. Performed troubleshooting of the fire extinguisher system in the engine compartment and in the crew compartment. | —— | —— |
| 7. Replaced/repaired or adjusted defective components (as necessary). | —— | —— |
| 8. Performed required PMCS. | —— | —— |
| 9. Performed a final operational test to verify fire extinguisher/suppression system fault(s) were corrected. | —— | —— |
| 10. Followed all safety precautions. | —— | —— |
| 11. Performed task to standards. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2350-256-10 | AR 385-10 |
| TM 9-2350-256-20 | AR 750-1 |
| TM 9-2350-256-24P-1 | AR 750-43 |
| TM 9-2350-256-24P-2 | DA PAM 738-750 |
| TM 9-2350-292-10 | TM 9-243 |
| TM 9-2350-292-20-1 | TM 9-8000 |
| TM 9-2350-292-20-2 |  |
| TM 9-2350-292-24P |  |

Perform Diagnostic Procedures of Track Vehicle's NBC System

091-63B-3002

Conditions: In a field or garrison environment given a representative (M88A1, M88A2) track vehicle,  required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures of  track vehicle's NBC System IAW  technical publications, procedures and specifications and when task was completed the vehicle's NBC system was fully mission capable.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Determined maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 5. Performed initial inspection. | —— | —— |
| 6. Diagnosed NBC system fault(s) and determined maintenance action to be performed. | —— | —— |
| 7. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 8. Verified applicable publications were available. | —— | —— |
| 9. Repaired/replaced or adjusted malfunctioning components. | —— | —— |
| 10. Followed all safety precautions. | —— | —— |
| 11. Performed task to acceptable standards. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2350-256-10 | AR 385-10 |
| TM 9-2350-256-20 | AR 750-1 |
| TM 9-2350-256-24P-1 | AR 750-43 |
| TM 9-2350-256-24P-2 | DA PAM 738-750 |
| TM 9-2350-292-10 | TM 9-243 |
| TM 9-2350-292-20-1 | TM 9-8000 |
| TM 9-2350-292-20-2 |  |
| TM 9-2350-292-24P |  |

Perform Diagnostic Procedures of Vehicle's Fuel System

091-63B-3003

Conditions: In a field or garrison environment given a representative (M998 series/ M1070 series) wheel vehicle,  required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures of a light wheeled vehicle's fuel system IAW technical publications, procedures and specifications.  When this task was completed, the fuel system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Determined maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 5. Performed initial inspection. | —— | —— |
| 6. Insured repair parts were identified and requisitioned, as required. | —— | —— |
| 7. Verified applicable publications were available. | —— | —— |
| 8. Diagnosed fuel system fault(s) and determined maintenance action to be performed. | —— | —— |
| 9. Ensured task was performed to acceptable standards. | —— | —— |
| 10. Followed all safety precautions. | —— | —— |
| 11. Performed a final inspection to ensure the fuel system was fully mission capable. | —— | —— |
| 12. Followed TAMMS procedures. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
| TM 9-2320-280-24P-1 | TM 9-243 |
| TM 9-2320-280-24P-2 | TM 9-8000 |
| TM 9-2320-360-10 |  |
| TM 9-2320-360-20-1 |  |
| TM 9-2320-360-20-2 |  |

Perform Diagnostic Procedures of  Vehicle's Electrical System

091-63B-3004

Conditions: In a field or garrison environment given a representative (M977series /M998 series) wheel vehicle,  required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures of vehicle's electrical system IAW technical publications, procedures and specifications.  When this task was completed, the electrical system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Determined maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test, and adjust components. | —— | —— |
| 5. Performed initial inspection. | —— | —— |
| 6. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 7. Verified applicable publications were available. | —— | —— |
| 8. Repaired/replaced or adjusted malfunctioning components. | —— | —— |
| 9. Followed all safety precautions . | —— | —— |
| 10. Performed PMCS. | —— | —— |
| 11. Verified system operated correctly. | —— | —— |
| 12. Completed tasks to acceptable standards. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-279-10-1 | AR 385-10 |
| TM 9-2320-279-10-2 | AR 750-1 |
| TM 9-2320-279-20-1 | AR 750-43 |
| TM 9-2320-279-20-2 | DA PAM 738-750 |
| TM 9-2320-279-20-3 | TM 9-2320-364-20-4 |
| TM 9-2320-279-24P-1 | TM 9-243 |
| TM 9-2320-280-10 | TM 9-8000 |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |
| TM 9-2320-364-10 |  |
| TM 9-2320-364-20-1 |  |
| TM 9-2320-364-20-2 |  |
| TM 9-2320-364-20-3 |  |
| TM 9-2320-364-24P-1 |  |
| TM 9-2320-364-24P-2 |  |
| TM 9-2350-256-20 |  |

Perform Diagnostic Procedures of Diesel Engines

091-63B-3005

Conditions: In a field or garrison environment given a representative (M998 /M1074) wheel vehicle,  required materials, general mechanic's tool kit, common #1 shop equipment, TMDE, Contact Test Set (CTS), Prolink Scan Tool  and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures of diesel engines IAW technical publications, procedures and specifications.  When this task was completed, the diesel engine was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Determined maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 5. Diagnosed engine fault(s) and determined maintenance action(s) to be performed. | —— | —— |
| 6. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 7. Verified applicable publications were available. | —— | —— |
| 8. Repaired/replaced or adjusted engine components as necessary to correct malfunction. | —— | —— |
| 9. Ensued task was performed to standards. | —— | —— |
| 10. Followed all safety precautions. | —— | —— |
| 11. Performed final inspection to ensure system was fully mission capable. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
| TM 9-2320-280-24P-1 | LO 9-2320-280-12 |
| TM 9-2320-364-10 | LO 9-2320-364-12 |
| TM 9-2320-364-20-1 | TM 9-2320-364-24P-1 |
| TM 9-2320-364-20-3 | TM 9-2320-364-24P-2 |
| TM 9-2320-364-20-4 | TM 9-243 |
|  | TM 9-8000 |

Perform Diagnostic Procedures of Vehicle Cooling System

091-63B-3006

Conditions: In a field or garrison environment given a representative (M998 series,/ M977 series) wheel vehicle,  required materials, general mechanic's tool kit, common #1 shop equipment, TMDE, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures to locate malfunction(s) of vehicle's cooling system IAW technical publications, procedures and specifications.  When this task was completed, the cooling system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Diagnosed system to verify/identify fault(s). | —— | —— |
| 3. Determined maintenance action to be performed. | —— | —— |
| 4. Verified task was within shop capability/authorization. | —— | —— |
| 5. Verified proper tools were was available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 6. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 7. Verified applicable publication(s) were available. | —— | —— |
| 8. Repaired/replaced or adjusted system components as required. | —— | —— |
| 9. Performed PMCS. | —— | —— |
| 10. Followed all safety precautions. | —— | —— |
| 11. Performed task to acceptable standards. | —— | —— |
| 12. Tested system to ensure vehicle was fully mission capable. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-279-10-1 | AR 385-10 |
| TM 9-2320-279-10-2 | AR 750-1 |
| TM 9-2320-279-20-1 | AR 750-43 |
| TM 9-2320-279-20-2 | DA PAM 738-750 |
| TM 9-2320-279-20-3 | TM 9-243 |
| TM 9-2320-279-24P-1 | TM 9-8000 |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-1 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |

Perform Diagnostic Procedures on Track Vehicle Transmission

091-63B-3007

Conditions: In a field or garrison environment given a representative (M88 series,/ M113 series) track vehicle,  required materials, general mechanic's tool kit, common #1 shop equipment, TMDE,  and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures on track vehicle's transmission IAW technical publications, procedures and specifications.  When this task was completed, the transmission was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Diagnosed transmission to determine problem or malfunctions. | —— | —— |
| 3. Determined maintenance action to be performed. | —— | —— |
| 4. Verified task is within shop capability/authorization. | —— | —— |
| 5. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 6. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 7. Verified applicable publications were available. | —— | —— |
| 8. Repaired/replaced or adjusted of components or transmission as necessary to correct fault(s). | —— | —— |
| 9. Tested transmission to ensure vehicle was fully mission capable. | —— | —— |
| 10. Followed all safety precautions. | —— | —— |
| 11. Performed task to acceptable standards. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2350-256-10 | AR 385-10 |
| TM 9-2350-256-20 | AR 750-1 |
| TM 9-2350-256-24P-1 | AR 750-43 |
| TM 9-2350-256-24P-2 | DA PAM 738-750 |
| TM 9-2350-261-10 | TM 9-243 |
| TM 9-2350-261-20-1 | TM 9-8000 |
| TM 9-2350-261-20-2 |  |
| TM 9-2350-261-20-3 |  |
| TM 9-2350-261-24P |  |

Perform Diagnostic Procedures on  Wheel Vehicle Transmission

091-63B-3009

Conditions: In a field or garrison environment given a representative (M998series, /M1074) wheel vehicle,  required materials, general mechanic's tool kit, common #1 shop equipment, TMDE, applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures on track vehicle's transmission IAW technical publications, procedures and specifications.  When this task was completed, the transmission was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Diagnosed transmission to determine problem or malfunctions. | —— | —— |
| 3. Determined maintenance action to be performed. | —— | —— |
| 4. Verified task was within shop capability/authorization. | —— | —— |
| 5. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 6. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 7. Verified applicable publications were available. | —— | —— |
| 8. Repaired/replaced or adjusted transmission or its components. | —— | —— |
| 9. Tested transmission to ensure vehicle was fully mission capable. | —— | —— |
| 10. Followed all safety precautions. | —— | —— |
| 11. Performed task to acceptable standards. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
| TM 9-2320-280-24P-1 | TM 9-243 |
| TM 9-2320-280-24P-2 | TM 9-8000 |
| TM 9-2320-364-10 |  |
| TM 9-2320-364-20-1 |  |
| TM 9-2320-364-20-2 |  |
| TM 9-2320-364-20-3 |  |
| TM 9-2320-364-20-4 |  |
| TM 9-2320-364-24P-1 |  |
| TM 9-2320-364-24P-2 |  |

Perform Diagnostic Procedures on Track Vehicle's Brake System

091-63B-3011

Conditions: In a field or garrison environment given a representative (M88 series,/M113 series) track  vehicle,  required materials, general mechanic's tool kit, common #1 shop equipment, TMDE,  and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Perform diagnostic procedures on track vehicle's brake system IAW technical publications, procedures and specifications.  When this task was completed, the brake system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Diagnosed vehicle brake system to determine malfunction(s). | —— | —— |
| 3. Determined maintenance action to be performed. | —— | —— |
| 4. Verified task was within shop capability/authorization. | —— | —— |
| 5. Verified proper tools were available to inspect, repair/replace, test, and adjust brake system components. | —— | —— |
| 6. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 7. Verified applicable publications were available. | —— | —— |
| 8. Repaired/replaced or adjusted brake system components as needed to correct malfunction. | —— | —— |
| 9. Tested brake system to ensure vehicle was fully mission capable. | —— | —— |
| 10. Followed all safety precautions. | —— | —— |
| 11. Used TMDE correctly. | —— | —— |
| 12. Performed task to acceptable standards. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2350-256-10 | AR 385-10 |
| TM 9-2350-256-20 | AR 750-1 |
| TM 9-2350-256-24P-1 | AR 750-43 |
| TM 9-2350-256-24P-2 | DA PAM 738-750 |
| TM 9-2350-261-10 | TM 9-243 |
| TM 9-2350-261-20-1 | TM 9-8000 |
| TM 9-2350-261-20-2 |  |
| TM 9-2350-261-20-3 |  |
| TM 9-2350-261-24P |  |

Perform Diagnostic Procedures on Wheel Vehicle's Brake System

091-63B-3012

Conditions: In a field or garrison environment given a representative (M998 series,/M915 series) wheel  vehicle,  required materials, general mechanic's tool kit, common #1 shop equipment, TMDE, ABS Scan tool and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references. 

Standards: Performed diagnostic procedures on a light wheel vehicle's brake system IAW technical publications, procedures and specifications.  When this task was completed, the brake system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Diagnosed brake system to determine malfunction of system or components. | —— | —— |
| 3. Determined maintenance action to be performed. | —— | —— |
| 4. Verified task was within shop capability/authorization. | —— | —— |
| 5. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 6. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 7. Verified applicable publications were available. | —— | —— |
| 8. Repaired/replaced or adjusted brake system components as necessary to correct malfunction. | —— | —— |
| 9. Tested brake system to ensure vehicle was fully mission capable. | —— | —— |
| 10. Followed all safety precautions. | —— | —— |
| 11. Performed task to acceptable standards. | —— | —— |
| 12. Completed TAMMS forms as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| DA PAM 738-750 | AR 385-10 |
| TM 9-2320-280-10 | AR 750-1 |
| TM 9-2320-280-20-1 | AR 750-43 |
| TM 9-2320-280-20-2 | TM 9-243 |
| TM 9-2320-280-20-3 | TM 9-8000 |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |
| TM 9-2320-283-10 |  |
| TM 9-2320-283-20-1 |  |
| TM 9-2320-283-20-2 |  |
| TM 9-2320-283-20-3 |  |
| TM 9-2320-283-24P |  |

Perform Diagnostic Procedures on Track Vehicle's Steering Systems

091-63B-3015

Conditions: In a field or garrison environment given a representative (M88 series,/M113 series) track  vehicle,  required materials, general mechanic's tool kit, common #1 shop equipment, TMDE,  and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures on track vehicle's steering systems IAW technical publications, procedures and specifications.   When this task was completed, the steering system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or equivalent. | —— | —— |
| 2. Diagnosed vehicle steering system to determine malfunction. | —— | —— |
| 3. Determined maintenance action to be performed. | —— | —— |
| 4. Verified task was within shop capability/authorization. | —— | —— |
| 5. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 6. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 7. Verified applicable publications were available. | —— | —— |
| 8. Repaired/replaced or adjusted steering system components as necessary to correct malfunction(s). | —— | —— |
| 9. Tested steering system to ensure vehicle was fully mission capable. | —— | —— |
| 10. Followed all safety precautions. | —— | —— |
| 11. Used TMDE correctly. | —— | —— |
| 12. Performed task to acceptable standards. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2350-256-10 | AR 385-10 |
| TM 9-2350-256-20 | AR 750-1 |
| TM 9-2350-256-24P-1 | AR 750-43 |
| TM 9-2350-256-24P-2 | DA PAM 738-750 |
| TM 9-2350-261-10 | TM 9-243 |
| TM 9-2350-261-20-1 | TM 9-8000 |
| TM 9-2350-261-20-2 |  |
| TM 9-2350-261-20-3 |  |
| TM 9-2350-261-24P |  |

Perform Diagnostic Procedures on Wheel Vehicle's Steering Systems

091-63B-3016

Conditions: In a field or garrison environment given a representative (M977 series,/M1070 series) wheel  vehicle,  required materials, general mechanic's tool kit, common #1 shop equipment, TMDE,  and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures on wheel vehicle's steering systems IAW applicable technical publications, procedures and specifications.  When this task was completed, the steering system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Diagnosed steering system to determine system problems. | —— | —— |
| 3. Determined maintenance action to be performed. | —— | —— |
| 4. Verified task was within shop capability/authorization. | —— | —— |
| 5. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 6. Verified repair parts were identified and requisitioned, as required. | —— | —— |
| 7. Verified applicable publications were available. | —— | —— |
| 8. Repaired/replaced or adjusted steering system components as needed to correct malfunction(s). | —— | —— |
| 9. Tested steering system to ensure vehicle was fully mission capable. | —— | —— |
| 10. Followed all safety precautions. | —— | —— |
| 11. Used TMDE correctly. | —— | —— |
| 12. Performed task to acceptable standards. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-279-10-1 | AR 385-10 |
| TM 9-2320-279-10-2 | AR 750-1 |
| TM 9-2320-279-20-1 | AR 750-43 |
| TM 9-2320-279-20-2 | DA PAM 738-750 |
| TM 9-2320-279-20-3 | TM 9-243 |
| TM 9-2320-279-24P-1 | TM 9-8000 |
| TM 9-2320-360-10 |  |
| TM 9-2320-360-20-1 |  |
| TM 9-2320-360-20-2 |  |

Perform Diagnostic Procedures on  Vehicle's Hydraulic  Systems

091-63B-3017

Conditions: In a field or garrison environment given a representative M977 series,wheel vehicle/  or VRRTF,  required materials, general mechanic's tool kit, common #1 shop equipment, TMDE,  and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures on a vehicle's hydraulic systems IAW applicable technical publications, procedures and specifications.  When this task was completed, the hydraulic system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Diagnosed vehicle hydraulic system to determine/verify malfunction(s). | —— | —— |
| 3. Determined maintenance action to be performed. | —— | —— |
| 4. Verified task was within shop capability/authorization. | —— | —— |
| 5. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 6. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 7. Verified applicable publications were available. | —— | —— |
| 8. Repaired/replaced or adjusted system components as needed to correct malfunction(s). | —— | —— |
| 9. Tested vehicle hydraulic system to ensue that it was fully mission capable. | —— | —— |
| 10. Followed all safety precautions. | —— | —— |
| 11. Verified proper TMDE was used correctly. | —— | —— |
| 12. Ensured environmental regulations were followed. | —— | —— |
| 13. Performed task to acceptable standards. | —— | —— |
| 14. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-279-12 | AR 385-10 |
| TM 10-3930-660-10 | AR 750-1 |
| TM 10-3930-660-20 | AR 750-43 |
| TM 9-2320-279-20-1 | DA PAM 738-750 |
| TM 9-2320-279-20-2 | TM 9-243 |
| TM 9-2320-279-20-3 | TM 9-8000 |

Perform Battlefield Damage Assessment and Repair (BDAR) on Tracked Vehicles

091-63B-3021

Conditions: In a field or garrison environment given a representative (M88 series,/M113 series) track  vehicle,  required materials, general mechanic's tool kit, common #1 shop equipment, TMDE,  and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed Battlefield Damage Assessment and Repair (BDAR) on tracked vehicles IAW applicable BDAR technical publications, procedures and specifications and after completion the vehicle  was fully mission capable..

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Performed a BDAR initial inspection. | —— | —— |
| 2. Determined recovery/BDAR/repair action(s) to be performed to correct vehicle malfunction(s). | —— | —— |
| 3. Identified and requisitioned repair parts, as required. | —— | —— |
| 4. Used applicable publications to perform BDAR maintenance action. | —— | —— |
| 5. Performed BDAR/recovery or repair as needed to correct vehicle malfunction. | —— | —— |
| 6. Followed all safety precautions. | —— | —— |
| 7. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 9-43-2 | AR 385-10 |
| TC 43-35 | AR 750-1 |
| TM 9-2350-256-20 | AR 750-43 |
| TM 9-2350-261-10 | DA PAM 738-750 |
| TM 9-2350-261-20-1 | TM 9-243 |
|  | TM 9-8000 |

Perform Battlefield Damage Assessment and Repair (BDAR) on Wheeled Vehicles

091-63B-3022

Conditions: In a field or garrison environment given a representative (M988 series,/M977 series) wheel  vehicle,  required materials, general mechanic's tool kit, common #1 shop equipment, TMDE,  and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed  Battlefield Damage Assessment and Repair (BDAR) on Wheeled Vehicles IAW applicable BDAR technical publications, procedures and specifications and after completion the  vehicle was fully mission capable..

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Performed BDAR initial inspection. | —— | —— |
| 2. Diagnosed vehicle malfunction to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to perform BDAR action. | —— | —— |
| 5. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 6. Verified applicable publications were available to perform BDAR maintenance actions. | —— | —— |
| 7. Performed BDAR/recovery or repairs needed to correct vehicle malfunction(s). | —— | —— |
| 8. Followed all safety precautions. | —— | —— |
| 9. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 9-43-2 | AR 385-10 |
| TC 21-306 | AR 750-1 |
| TM 9-2320-279-10-1 | AR 750-43 |
| TM 9-2320-279-10-2 | DA PAM 738-750 |
| TM 9-2320-279-20-1 | TM 9-2320-280-20-1 |
| TM 9-2320-279-20-2 | TM 9-243 |
| TM 9-2320-279-20-3 | TM 9-8000 |
| TM 9-2320-279-24P-1 |  |
| TM 9-2320-280-10 |  |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-280-20-3 |  |
| TM 9-2320-280-24P-1 |  |
| TM 9-2320-280-24P-2 |  |

Perform Diagnostic Procedures of  Vehicle's Winch System

091-63B-3033

Conditions: In a field or garrison environment given a representative (M977 series) wheel vehicle,  required materials, general mechanic's tool kit, common #1 shop equipment, TMDE,  and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures of  vehicle's winch system IAW applicable technical publications, procedures and specifications.  When this task  was completed, the winch assembly  was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or equivalent. | —— | —— |
| 2. Performed troubleshooting of vehicle winch system to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test, and adjust system. components | —— | —— |
| 5. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 6. Verified applicable publications were available. | —— | —— |
| 7. Repaired/replaced or adjusted winch system or components as necessary to correct malfunction. | —— | —— |
| 8. Followed all safety precautions. | —— | —— |
| 9. Used TMDE correctly. | —— | —— |
| 10. Tested vehicle winch system to ensure it was fully mission capable. | —— | —— |
| 11. Performed task to acceptable standards. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |
| 13. Ensured all environmental policies and procedures were followed. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-279-10-1 | AR 385-10 |
| TM 9-2320-279-10-2 | AR 750-1 |
| TM 9-2320-279-20-1 | AR 750-43 |
| TM 9-2320-279-20-2 | DA PAM 738-750 |
| TM 9-2320-279-20-3 | TM 9-243 |
| TM 9-2320-279-24P-1 | TM 9-8000 |
| TM 9-2320-279-34-1 |  |
| TM 9-2320-279-34-2 |  |
| TM 9-2320-279-34-3 |  |

Perform Diagnostic Procedures on  Wheel Vehicle's Air System

091-63B-3050

Conditions: In a field or garrison environment given a representative (M998 series,/M1070 series) wheel  vehicle,  required materials, general mechanic's tool kit, common #1 shop equipment, TMDE,  and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Performed diagnostic procedures on wheel vehicle's air induction system IAW applicable technical publications, procedures and specifications.  When this task was completed, the air induction system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Performed diagnostics to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools was available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 5. Verified repair parts was identified and requisitioned as required. | —— | —— |
| 6. Verified applicable publications available. | —— | —— |
| 7. Repaired/replaced or adjusted air induction system components as necessary to correct malfunction. | —— | —— |
| 8. Tested system to ensure vehicle air induction system was fully mission capable. | —— | —— |
| 9. Followed all safety precautions. | —— | —— |
| 10. Used TMDE correctly. | —— | —— |
| 11. Followed all environmental regulations or policies. | —— | —— |
| 12. Performed task to acceptable standards. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-280-10 | AR 385-10 |
| TM 9-2320-280-20-1 | AR 750-1 |
| TM 9-2320-280-20-2 | AR 750-43 |
| TM 9-2320-280-20-3 | DA PAM 738-750 |
| TM 9-2320-280-24P-1 | TM 9-243 |
| TM 9-2320-280-24P-2 | TM 9-8000 |
| TM 9-2320-360-10 |  |
| TM 9-2320-360-20-1 |  |
| TM 9-2320-360-20-2 |  |

Perform Diagnostic Procedures on  M113A3 Steering Braking Controls

091-63B-3057

Conditions: In a field or garrison given M113A3 vehicle, required materials, general mechanic's  tool kit, common #1 shop equipment, TMDE and TM 9-2350-261- series  technical  manuals.

Standards: Performed diagnostic procedures on M113A3's steering braking controls IAW applicable technical publications, procedures and specifications.  When this task was completed, the equipment was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or equivalent. | —— | —— |
| 2. Performed diagnostics of vehicle's steering brake control system to determine maintenance action(s) required. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 5. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 6. Verified applicable publications were available. | —— | —— |
| 7. Repaired/replaced or adjusted system component(s) as necessary to correct malfunction(s). | —— | —— |
| 8. Tested vehicle steering braking system to ensure it and the vehicle were fully mission capable. | —— | —— |
| 9. Verified all safety precautions were followed. | —— | —— |
| 10. Used TMDE correctly. | —— | —— |
| 11. Followed all environmental regulations, practices and policies. | —— | —— |
| 12. Verified task was performed to acceptable standards. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| DA PAM 738-750 | AR 385-10 |
| TM 9-2350-277-20-1 | AR 750-1 |
| TM 9-2350-277-20-2 | AR 750-43 |
| TM 9-2350-277-20-3 | TM 9-243 |
|  | TM 9-8000 |

Perform Diagnostic Procedures on M578 Hydraulic System

091-63B-3058

Conditions: In a field or garrison environment given a (M578 series) track  vehicle,  required materials, general mechanic's tool kit, common #1 shop equipment, TMDE,  and applicable TM(s).

Standards: Performed diagnostic procedures on M578 hydraulic system IAW applicable technical publications, procedures and specifications.  When this task was completed, the hydraulic system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or equivalent. | —— | —— |
| 2. Performed diagnostics of M578 hydraulic system to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 5. Verified repair parts were identified and requisitioned, as required. | —— | —— |
| 6. Verified applicable publications were available. | —— | —— |
| 7. Repaired/replaced or adjusted system components as necessary to correct malfunction. | —— | —— |
| 8. Tested the M578 hydraulic system to ensure it and the vehicle were fully mission capable. | —— | —— |
| 9. Followed all safety precautions. | —— | —— |
| 10. Used TMDE correctly. | —— | —— |
| 11. Followed all environmental policies, regulations and practices. | —— | —— |
| 12. Performed task to acceptable standards. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2350-238-10 | AR 385-10 |
| TM 9-2350-238-20-1 | AR 750-1 |
| TM 9-2350-238-20-2 | AR 750-43 |
|  | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Perform Diagnostic Procedures on M88A1/M88A2 Hydraulic System

091-63B-3062

Conditions: In a field or garrison given an M88A1/M88A2, required materials, general mechanic's  tool kit, common #1 shop equipment, TMDE and applicable technical  manual(s).

Standards: Performed  diagnostic procedures on M88A1/M88A2 hydraulic systems IAW applicable technical publications, procedures and specifications.  When this task was completed, the hydraulic systems were fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Performed diagnostics on M88A1/M88A2 hydraulic system to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 5. Verified repair parts were identified and requisitioned, as required. | —— | —— |
| 6. Verified applicable publications were available. | —— | —— |
| 7. Replaced/repaired or adjusted system components as necessary to correct malfunction(s). | —— | —— |
| 8. Tested system to ensure that it and the vehicle was fully mission capable. | —— | —— |
| 9. Verified all safety precautions were followed. | —— | —— |
| 10. Verified TMDE was used correctly. | —— | —— |
| 11. Followed all environmental policies, regulations and practices. | —— | —— |
| 12. Performed task to acceptable standards. | —— | —— |
| 13. Completed TAMMS forms. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2350-256-10 | AR 385-10 |
| TM 9-2350-256-20 | AR 750-1 |
| TM 9-2350-256-24P-1 | AR 750-43 |
| TM 9-2350-256-24P-2 | DA PAM 738-750 |
| TM 9-2350-292-10 | TM 9-243 |
| TM 9-2350-292-20-1 | TM 9-8000 |
| TM 9-2350-292-20-2 |  |
| TM 9-2350-292-24P |  |

Perform Diagnostic Procedures on M911 Air System

091-63B-3064

Conditions: In a field or garrison given an M911, required materials, general mechanic's  tool kit, common #1 shop equipment, TMDE and applicable technical  manual(s).

Standards: Performed  diagnostic procedures on the M911's  air induction system IAW applicable technical publications, procedures and specifications.  When this task was completed, the air induction system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Performed diagnostics on M911air system to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 5. Verified repair parts were identified and requisitioned, as required. | —— | —— |
| 6. Verified applicable publications were available. | —— | —— |
| 7. Replaced/repaired or adjusted system components as necessary to correct malfunction. | —— | —— |
| 8. Tested system to ensure vehicle was fully mission capable. | —— | —— |
| 9. Verified all safety precautions were followed. | —— | —— |
| 10. Used TMDE correctly . | —— | —— |
| 11. Followed all environmental regulations, practices and policies. | —— | —— |
| 12. Performed task to acceptable standards. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-270-10 | AR 385-10 |
| TM 9-2320-270-20-1 | AR 750-1 |
| TM 9-2320-270-20-2 | AR 750-43 |
| TM 9-2320-270-20-3 | DA PAM 738-750 |
| TM 9-2320-270-20P | TM 9-243 |
|  | TM 9-8000 |

Perform Diagnostic Procedures on M936A2WW/M1089 Hydraulic System

091-63B-3071

Conditions: In a field or garrison given a M936A2WW/M1089 vehicle, required materials, general mechanic's tool kit, common #1 shop equipment, TMDE and applicable technical manual(s).

Standards: Performed diagnostic procedures on M936A2WW/M1089 hydraulic system IAW applicable technical publications, procedures and specifications.  When this task was completed, the hydraulic system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Diagnosed hydraulic system and components to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified repair parts were identified and requisitions as required. | —— | —— |
| 5. Verified applicable publications were available. | —— | —— |
| 6. Replaced/repaired or adjusted hydraulic system components as required to correct malfunction(s). | —— | —— |
| 7. Tested vehicle hydraulic system to ensure vehicle was fully mission capable. | —— | —— |
| 8. Verified all safety precautions were followed. | —— | —— |
| 9. Verified proper TMDE was used correctly. | —— | —— |
| 10. Followed all environmental regulations, practices and policies. | —— | —— |
| 11. Performed task to acceptable standards. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
| TM 9-2320-272-24-3 | DA PAM 738-750 |
| TM 9-2320-272-24-4 | TM 9-243 |
| TM 9-2320-272-24P-1 | TM 9-8000 |
| TM 9-2320-272-24P-2 |  |
| TM 9-2320-366-10-1 |  |
| TM 9-2320-366-10-2 |  |
| TM 9-2320-366-20-1 |  |
| TM 9-2320-366-20-2 |  |
| TM 9-2320-366-20-3 |  |
| TM 9-2320-366-20-4 |  |
| TM 9-2320-366-20-5 |  |
| TM 9-2320-366-24P-1 |  |

Perform Diagnostic Procedures on Material Handling Equipment (MHE) Hydraulic System

091-63B-3084

Conditions: In a field or garrison environment given a VRRTF,  required materials, general mechanic's tool kit, common #1 shop equipment, TMDE,  and applicable TM(s).

Standards: Performed diagnostic procedures on Material Handling Equipment (MHE )hydraulic system IAW applicable technical publications, procedures and specifications.  When this task was completed, the MHE hydraulic system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Performed diagnostics to MHE hydraulic system and components to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 5. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 6. Verified applicable publications were available. | —— | —— |
| 7. Replaced/repaired or adjusted system components as needed to correct system malfunction(s). | —— | —— |
| 8. Tested MHE hydraulic system to ensure equipment is fully mission capable. | —— | —— |
| 9. Followed all safety precautions. | —— | —— |
| 10. Used TMDE correctly. | —— | —— |
| 11. Followed all environmental regulations, practices and policies. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 10-3930-660-10 | AR 385-10 |
| TM 10-3930-660-20 | AR 750-1 |
|  | AR 750-43 |
|  | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Perform Diagnostic Procedures on Material Handling Equipment (MHE)Electrical System

091-63B-3088

Conditions: In a field or garrison environment given a VRRTF,  required materials, general mechanic's tool kit, common #1 shop equipment, TMDE,  and applicable TM(s).

Standards: Perform diagnostic procedures on Material Handling Equipment (MHE) electrical system IAW applicable technical publications, procedures and specifications.  When this task was completed, the hydraulic system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Performed diagnostics to MHE electrical system to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 5. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 6. Verified applicable publications were available. | —— | —— |
| 7. Replaced/repaired or adjusted MHE system components as needed to correct malfunction(s). | —— | —— |
| 8. Tested electrical system and MHE to ensure it was fully mission capable. | —— | —— |
| 9. Followed all safety precautions. | —— | —— |
| 10. Used TMDE correctly. | —— | —— |
| 11. Followed all environmental regulations, practices and policies. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 10-3930-660-10 | AR 385-10 |
| TM 10-3930-660-20 | AR 750-1 |
|  | AR 750-43 |
|  | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Perform Diagnostic Procedures on Armored Vehicle Launched Bridge (AVLB) Hydraulic Systems

091-63B-3092

Conditions: In a field or garrison given an AVLB, required materials, general mechanic's tool kit, common #1 shop equipment, TMDE and applicable technical  manual(s).

Standards: Performed diagnostic procedures on Armored Vehicle Launched Bridge (AVLB) hydraulic systems IAW applicable technical publications, procedures and specifications.  When this task was completed, the Armored Vehicle Launched Bridge hydraulic system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Perform diagnostics on AVLB hydraulic system to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair, replace, test or adjust components as needed. | —— | —— |
| 5. Verified all necessary repair parts were available or requisitioned. | —— | —— |
| 6. Verified applicable publications were available. | —— | —— |
| 7. Repaired/replaced or adjusted AVLB hydraulic system components as needed to correct malfunction(s). | —— | —— |
| 8. Tested AVLB hydraulic system and its components to ensure equipment was fully mission capable. | —— | —— |
| 9. Followed all safety precautions. | —— | —— |
| 10. Followed all environmental regulations, practices and policies. | —— | —— |
| 11. Completed all TAMMS forms. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 5-5420-202-10 | AR 385-10 |
| TM 5-5420-202-20-1 | AR 750-1 |
| TM 5-5420-202-20-2 | AR 750-43 |
| TM 5-5420-202-20-3 | DA PAM 738-750 |
| TM 5-5420-202-20-4 | TM 9-243 |
| TM 5-5420-203-14 | TM 9-8000 |
| TM 5-5420-226-10 |  |
| TM 5-5420-226-20-1 |  |
| TM 5-5420-226-20-2 |  |
| TM 5-5420-226-20-3 |  |
| TM 5-5420-226-20-4 |  |

Perform Diagnostic Procedures on M984A1WW Hydraulic System

091-63B-3099

Conditions: In a field or garrison given an M984A1/WW vehicle, required materials, general mechanic's  tool kit, common #1 shop equipment, TMDE and applicable technical  manual(s).

Standards: Performed  diagnostic procedures on M984A1WW hydraulic system IAW applicable technical publications, procedures and specifications.  When this task was completed, the hydraulic system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Performed diagnostics on M984A1 WW hydraulic system to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 5. Verified repair parts were identified requisitioned as required. | —— | —— |
| 6. Verified applicable publications were available. | —— | —— |
| 7. Replaced/repaired or adjusted M984A1 WW hydraulic system components as needed to correct system malfunction(s). | —— | —— |
| 8. Tested vehicle hydraulic system to ensure vehicle was fully mission capable. | —— | —— |
| 9. Followed all safety precautions. | —— | —— |
| 10. Used TMDE correctly. | —— | —— |
| 11. Followed all environmental regulations, practices and policies. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-279-10-1 | AR 385-10 |
| TM 9-2320-279-10-2 | AR 750-1 |
| TM 9-2320-279-20-1 | AR 750-43 |
| TM 9-2320-279-20-2 | DA PAM 738-750 |
| TM 9-2320-279-20-3 | TM 9-243 |
| TM 9-2320-279-24P-1 | TM 9-8000 |

Perform Diagnostic Procedures on M1074 Trailer Brake

091-63B-3103

Conditions: In a field or garrison given M1074 vehicle, required materials, general mechanic's  tool kit, common  #1 shop equipment, TMDE and applicable technical  manual(s).

Standards: Performed diagnostic procedures on M1074 trailer brake IAW applicable technical publications, procedures and specifications.  When this task was completed, the trailer brake was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or equivalent. | —— | —— |
| 2. Performed diagnostic procedures on M1074 trailer brake components to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 5. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 6. Verified applicable publications were available. | —— | —— |
| 7. Replaced/repaired or adjusted M1074 trailer brake components as required to correct malfunction(s). | —— | —— |
| 8. Tested trailer brake to ensure equipment is fully mission capable. | —— | —— |
| 9. Verified all safety precautions were followed. | —— | —— |
| 10. Used TMDE correctly. | —— | —— |
| 11. Followed all environmental regulations, practices and policies. | —— | —— |
| 12. Verified that TAMMS forms were completed, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-364-10 | AR 385-10 |
| TM 9-2320-364-20-1 | AR 750-1 |
| TM 9-2320-364-20-2 | AR 750-43 |
| TM 9-2320-364-20-3 | DA PAM 738-750 |
| TM 9-2320-364-20-4 | TM 9-243 |
|  | TM 9-8000 |

Perform Diagnostic Procedures on M1074 Hydraulic System

091-63B-3104

Conditions: In a field or garrison given an M1074 vehicle, required materials, general mechanic's  tool kit, common  #1 shop equipment, TMDE, Contact Test Set (CTS) and applicable technical  manual(s).

Standards: Performed  diagnostic procedures on M1074 hydraulic system IAW applicable technical publications, procedures and specifications.  When this task was completed, the hydraulic system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or equivalent. | —— | —— |
| 2. Performed diagnostics on the M1074 Hydraulic system to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace. | —— | —— |
| 5. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 6. Verified applicable publications were available. | —— | —— |
| 7. Repaired/replaced or adjusted M1074 hydraulic system components as necessary to correct malfunction(s). | —— | —— |
| 8. Tested M1074 hydraulic system to ensure vehicle was fully mission capable. | —— | —— |
| 9. Followed all safety precautions. | —— | —— |
| 10. Used TMDE correctly. | —— | —— |
| 11. Followed all environmental regulations, practices and policies. | —— | —— |
| 12. Completed TAMMS forms as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| LO 9-2320-364-12 | AR 385-10 |
| TM 9-2320-364-10 | AR 750-1 |
| TM 9-2320-364-20-1 | AR 750-43 |
| TM 9-2320-364-20-2 | DA PAM 738-750 |
| TM 9-2320-364-20-3 | TM 9-243 |
| TM 9-2320-364-20-4 | TM 9-8000 |
| TM 9-2320-364-24P-1 |  |
| TM 9-2320-364-24P-2 |  |

Perform Diagnostic Procedures on M1000 Suspension System

091-63B-3125

Conditions: In a field or garrison given an M1000 vehicle, required materials, general mechanic's  tool kit, common #1 shop equipment, TMDE and applicable technical  manual(s).

Standards: Perform diagnostic procedures on M1000 suspension system IAW applicable technical publications, procedures and specifications.  When this task was completed, the suspension system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Diagnosed M1000 suspension system to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 5. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 6. Verified applicable publications were available. | —— | —— |
| 7. Replaced/repaired or adjusted M1000 system suspension components as needed to correct malfunction(s). | —— | —— |
| 8. Tested M1000 suspension system to ensure equipment was fully mission capable. | —— | —— |
| 9. Followed all safety precautions. | —— | —— |
| 10. Used TMDE correctly. | —— | —— |
| 11. Followed all environmental regulations, practices and policies. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2330-381-14 | AR 385-10 |
| TM 9-2330-384-14&P | AR 750-1 |
|  | AR 750-43 |
|  | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Perform Diagnostic Procedures on M1000 Steering System

091-63B-3127

Conditions: In a field or garrison given M1000 vehicle, required materials, general mechanic's tool kit, common #1 shop equipment, TMDE and applicable technical  manual(s).

Standards: Performed diagnostic procedures on M1000 steering system IAW applicable technical publications, procedures and specifications.  When this task was completed, the steering system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Diagnosed M1000 steering system components to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 5. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 6. Verified applicable publications were available. | —— | —— |
| 7. Replaced/repaired or adjusted M1000 steering system components as necessary to correct malfunction(s). | —— | —— |
| 8. Tested M1000 steering system to ensure vehicle was fully mission capable. | —— | —— |
| 9. Followed all safety precautions. | —— | —— |
| 10. Used TMDE correctly. | —— | —— |
| 11. Followed all environmental regulations, practices and policies. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2330-381-14 | AR 385-10 |
| TM 9-2330-384-14&P | AR 750-1 |
|  | AR 750-43 |
|  | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Perform Diagnostic Procedures on Wheel Vehicle Central Tire Inflation System (CTIS)

091-63B-3128

Conditions: In a field or garrison given M939 vehicle with  CTIS, required materials, general mechanic's  tool kit, common #1 shop equipment, TMDE, Contact Test Set (CTS) and applicable technical  manual(s).

Standards: Performed diagnostic procedures on wheel vehicle Central Tire Inflation System (CTIS) IAW applicable technical publications, procedures and specifications.  When this task was completed, the CTIS was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Diagnosed vehicle CTIS to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test , and adjust system components. | —— | —— |
| 5. Verified repair parts were identified and requisitioned, as required. | —— | —— |
| 6. Verified applicable publications were available. | —— | —— |
| 7. Replaced/repaired or adjusted CTIS components as necessary to correct system malfunction(s). | —— | —— |
| 8. Tested vehicle CTIS to ensure system and vehicle were fully mission capable. | —— | —— |
| 9. Followed all safety precautions. | —— | —— |
| 10. Used TMDE correctly. | —— | —— |
| 11. Followed all environmental regulations, practices and policies. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-272-10 | AR 385-10 |
| TM 9-2320-272-24-1 | AR 750-1 |
| TM 9-2320-272-24-2 | AR 750-43 |
|  | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Perform Diagnostic Procedures on M984A1 Electrical  System

091-63B-3129

Conditions: In a field or garrison environment given an M984A1 vehicle  required materials, general mechanic's  tool kit, common #1 shop equipment, TMDE and applicable technical  manual(s).

Standards: Performed diagnostic procedures on M984A1 electrical system IAW applicable technical publications, procedures and specifications.  When this task was completed, the electrical system was fully functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or equivalent. | —— | —— |
| 2. Diagnosed malfunctions of M984A1 WW electrical system to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 5. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 6. Verified applicable publications were available. | —— | —— |
| 7. Repaired/ replaced or adjusted M984A1 WW electrical system component(s) as required to correct system malfunction(s). | —— | —— |
| 8. Tested M984A1 WW electrical system to ensure vehicle was fully mission capable. | —— | —— |
| 9. Followed all safety precautions. | —— | —— |
| 10. Used TMDE correctly. | —— | —— |
| 11. Followed all environmental regulations, practices and policies. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-279-10-1 | AR 385-10 |
| TM 9-2320-279-10-2 | AR 750-1 |
| TM 9-2320-279-20-1 | AR 750-43 |
| TM 9-2320-279-20-2 | DA PAM 738-750 |
| TM 9-2320-279-20-3 | TM 9-243 |
| TM 9-2320-280-20-1 | TM 9-8000 |
| TM 9-2320-280-20-2 |  |
| TM 9-2320-364-20-1 |  |
| TM 9-2320-364-20-3 |  |

Perform Diagnostic Procedures on M1070 Fuel System

091-63B-3130

Conditions: In a field or garrison environment given a M1070 vehicle, required materials, general mechanic tool kit, common  #1 shop equipment, TMDE, Contact Test Set (CTS), Prolink Scan Tool and applicable technical  manual(s).

Standards: Performed diagnostic procedures on M1070 fuel system IAW applicable technical publications, procedures and specifications.  When this task was completed, the fuel system was fully  functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 or ULLS equivalent. | —— | —— |
| 2. Performed diagnostics of M1070 fuel system to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test , and adjust system components. | —— | —— |
| 5. Verified repair parts were identified and requisitioned, as required. | —— | —— |
| 6. Verified applicable publications were available. | —— | —— |
| 7. Replaced/repaired or adjusted M1070 fuel system components as required to correct malfunctions. | —— | —— |
| 8. Tested M1070 fuel system to ensure vehicle was fully mission capable. | —— | —— |
| 9. Followed all safety precautions. | —— | —— |
| 10. Used TMDE correctly. | —— | —— |
| 11. Followed all environmental regulations, practices and policies. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2320-360-10 | AR 385-10 |
| TM 9-2320-360-20-1 | AR 750-1 |
| TM 9-2320-360-20-2 | AR 750-43 |
|  | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Perform Diagnostic Procedures on M1000 Hydraulic System

091-63B-3131

Conditions: In a field or garrison environment  given an M1000 vehicle, given required materials, general mechanic's tool kit, common  #1shop equipment, TMDE and applicable technical  manual(s).

Standards: Performed  diagnostic procedures on M1000 hydraulic system IAW applicable technical publications, procedures and specifications.  When this task was completed, the hydraulic system was fully  functional.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Verified accuracy of DA Form 2404 of ULLS equivalent. | —— | —— |
| 2. Performed diagnostics of M1000 hydraulic system components to determine maintenance action to be performed. | —— | —— |
| 3. Verified task was within shop capability/authorization. | —— | —— |
| 4. Verified proper tools were available to inspect, repair/replace, test, and adjust system components. | —— | —— |
| 5. Verified repair parts were identified and requisitioned as required. | —— | —— |
| 6. Verified applicable publications were available. | —— | —— |
| 7. Replaced/repaired or adjusted M1000 hydraulic system component(s) as needed to correct system malfunction(s). | —— | —— |
| 8. Tested M1000 hydraulic system to ensure vehicle was fully mission capable. | —— | —— |
| 9. Followed all safety precautions. | —— | —— |
| 10. Used TMDE correctly. | —— | —— |
| 11. Followed all environmental regulations, practices and policies. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2330-381-14 | AR 385-10 |
|  | AR 750-1 |
|  | AR 750-43 |
|  | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Lift and Tow a Disabled Vehicle

091-63B-3132

Conditions: n a garrison or field environment with assistance and supervision, given applicable recovery vehicle (Track M88 or Wheel M984A1) with BII, general mechanic's tool kit, lubricants if required, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts, if needed.

Standards: Lifted and towed a disabled vehicle IAW applicable technical publications, procedures and specifications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected and used applicable publications. | —— | —— |
| 2. Determined method for towing. | —— | —— |
| 3. Prepared vehicle for towing. | —— | —— |
| 4. Hooked up vehicle for towing. | —— | —— |
| 5. Followed prescribed safety procedures. | —— | —— |
| 6. Established communication between vehicles. | —— | —— |
| 7. Towed vehicle to predetermined site. | —— | —— |
| 8. Disconnected vehicle. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 9-43-2 | AR 385-10 |
| TM 9-2320-270-10 | AR 750-1 |
| TM 9-2320-272-10 | AR 750-43 |
| TM 9-2350-256-10 | DA PAM 738-750 |
|  | FM 5-125 |
|  | TM 9-243 |
|  | TM 9-8000 |

Determine Recovery Method

091-63B-3133

Conditions: In a field or garrison given a recovery vehicle, tools and equipment, recovery situation/field recovery problems  , required materials, and FM 9-43-2

Standards: Determined recovery method IAW applicable technical publications, procedures and specifications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected and used applicable publications. | —— | —— |
| 2. Reconnoitered area. | —— | —— |
| 3. Estimated situation. | —— | —— |
| 4. Calculated ratios. | —— | —— |
| 5. Obtained resistance. | —— | —— |
| 6. Verified solution. | —— | —— |
| 7. Erected rigging. | —— | —— |
| 8. Rechecked rigging. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 5-125 | AR 385-10 |
| FM 9-43-2 | AR 750-1 |
|  | AR 750-43 |
|  | DA PAM 738-750 |
|  | TM 9-243 |
|  | TM 9-8000 |

Recover an Overturned Vehicle

091-63B-3200

Conditions: In a garrison or field environment with assistance and supervision, given applicable recovery vehicle (Track M88 or Wheel M984A1) with BII, general mechanic's tool kit, lubricants if required, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts, if needed.

Standards: Recovered an overturned vehicle IAW applicable technical publications, procedures and specifications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Reconnoitered the area where over turned vehicle was located. | —— | —— |
| 3. Estimated the situation. | —— | —— |
| 4. Calculated the ratio. | —— | —— |
| 5. Obtained resistance. | —— | —— |
| 6. Obtained solution to recovery problem. | —— | —— |
| 7. Obtained necessary vehicles and personnel. | —— | —— |
| 8. Positioned vehicles and personnel. | —— | —— |
| 9. Rigged for recovery. | —— | —— |
| 10. Re-checked rigging. | —— | —— |
| 11. Performed recovery operations according to the procedures in referenced recovery manual. | —— | —— |
| 12. Recovered the overturned vehicle. | —— | —— |
| 13. Followed all safety procedures. | —— | —— |
| 14. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| DA PAM 738-750 | AR 750-1 |
| TM 9-2320-272-10 | AR 750-43 |
| TM 9-2320-272-24-1 | TM 9-243 |
| TM 9-2350-256-10 | TM 9-8000 |
| TM 9-2350-256-20 |  |

Operate Oxyacetylene Equipment

091-63B-3330

Conditions: In a classroom/shop environment with assistance, given oxyacetylene equipment, tools, safety equipment, and applicable references.

Standards: Operated oxyacetylene equipment IAW applicable technical publications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected and used applicable technical publications. | —— | —— |
| 2. Followed all required safety procedures. | —— | —— |
| 3. Installed oxygen regulator and hoses. | —— | —— |
| 4. Installed acetylene regulator and hoses. | —— | —— |
| 5. Installed cutting torch. | —— | —— |
| 6. Adjusted oxygen acetylene working pressures. | —— | —— |
| 7. Checked for leaks with soap and water. | —— | —— |
| 8. Selected appropriate cutting tip. | —— | —— |
| 9. Lit and adjusted torch flame. | —— | —— |
| 10. Cut low carbon steel. | —— | —— |
| 11. Shut down, disassembled, and stowed equipment. | —— | —— |
| 12. Followed all environmental regulations, practices and policies. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AR 385-10 | AR 750-1 |
| TC 9-237 | DA PAM 738-750 |
|  | TC 43-35 |

Skill Level 4

Subject Area 25: COMMON LOGISTIC TASKS (SL 4)

Perform Senior Rater Responsibilities for a Maintenance Section

091-CLT-4001

Conditions: In a field or garrison environment, given an NCOER with the rater's portion completed, accompanying counseling statements, and AR 623-205.

Standards: Performed senior rater's responsibilities IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured all materials and references were available. | —— | —— |
| 2. Reviewed quarterly counseling that supported the NCOER. | —— | —— |
| 3. Reviewed the administrative data and rater's portions of the NCOER for accuracy and content. | —— | —— |
| 4. Prepared the senior rater's portion of the NCOER. | —— | —— |
| 5. Ensured the NCOER was submitted for review and further processing. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AR 623-205 |  |

Supervise Platoon/Section Administrative Procedures

091-CLT-4002

Conditions: In a field or garrison environment, given situation(s) requiring platoon/section administrative procedures supervision and applicable forms, records, and publications.

Standards: Supervised platoon/section administrative procedures IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Established files using the Modern Army Record Keeping System (MARKS). | —— | —— |
| a. Prepared file folders and guides. |  |  |
| b. Arranged file folders and guides. |  |  |
| c. Prepared file drawer labels. |  |  |
| d. Prepared a list of file numbers. |  |  |
| 2. Processed a recommendation for award. | —— | —— |
| 3. Processed and updated a flag on records. | —— | —— |
| 4. Verified the accuracy of Suspension of Favorable Action Report. | —— | —— |
| 5. Processed and updated a bar to reenlistment. | —— | —— |
| 6. Processed a chapter action. | —— | —— |
| a. Selected appropriate type of chapter action and identified separation guidelines. |  |  |
| b. Initiated and follow-up the chapter action. |  |  |
| 7. Processed a recommendation for advancement/promotion. | —— | —— |
| 8. Verified accuracy of Enlisted Promotion Report (AAC-C01). | —— | —— |
| 9. Assisted a subordinate NCO who had received notice of selection to be released under the Qualitative Management Program (QMP). | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AR 25-400-2 |  |
| AR 600-8-2 |  |
| AR 614-200 |  |
| AR 635-200 |  |

Manage Combat Stress

091-CLT-4003

Conditions: In a field or garrison environment, given a situation requiring stress management and FM 22-51.

Standards: Managed combat stress IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Identified sources of combat stress. | —— | —— |
| 2. Identified the signs and classifications of battle fatigue. | —— | —— |
| 3. Identified signs of stress in self, others, and the unit. | —— | —— |
| 4. Took appropriate steps to reduce and/or prevent stress. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 22-51 |  |

Ensure Maintenance Operations are in Compliance With the Army Environmental Program

091-CLT-4004

Conditions: In a field or garrison environment, given a maintenance facility/site, maintenance personnel and equipment, and applicable references.

Standards: Ensured maintenance operations were in compliance with the Army Environmental Program and other regulatory publications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured all publications were available. | —— | —— |
| 2. Reviewed maintenance SOP to ensure environmental policies and procedures were adequately addressed concerning the following: | —— | —— |
| a. Environmental strategies of compliance, restoration, prevention, and conservation. |  |  |
| b. Federal, state, local, and host nation laws and regulations. |  |  |
| 3. Updated/changed/amended SOP as necessary. | —— | —— |
| 4. Ensured all soldiers had received training on environmental laws, regulations, policies, and procedures. | —— | —— |
| 5. Ensured inspections for hazardous waste and HAZMAT were conducted as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AR 385-10 |  |
| AR 40-5 |  |
| FM 4-30.3 (FM 9-43-1) |  |

Enforce Compliance With the Shop Safety Program

091-CLT-4005

Conditions: In a field or garrison environment, given a maintenance site/facility, maintenance personnel, unit safety SOP, and applicable references.

Standards: Enforced compliance with the shop safety program IAW applicable references and unit safety SOP.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured all safety references were on hand. | —— | —— |
| 2. Ensured all safety equipment was on hand, accessible, and properly maintained. | —— | —— |
| 3. Ensured all soldiers were regularly updated on the shop safety program. | —— | —— |
| 4. Ensured periodic safety inspections were being conducted, and safety concerns and violations were being corrected. | —— | —— |
| 5. Ensured safety violations were being documented and reported as required, and follow-ups were being conducted. | —— | —— |
| 6. Inspected records of safety inspections and accident reports for accuracy and completeness. | —— | —— |
| 7. Inspected to ensure Material Safety Data Sheets (MSDS) were posted and maintained in applicable work areas. | —— | —— |
| 8. Performed periodic safety spot checks and inspections for safety awareness and systemic safety problems. | —— | —— |
| a. Performed on-the-spot corrections. |  |  |
| b. Performed follow-ups. |  |  |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AR 385-10 |  |
| AR 385-40 |  |
| AR 385-55 |  |
| AR 614-200 |  |
| DA PAM 385-1 |  |
| TB 43-0142 |  |
| TB MED 524 |  |

Coordinate Support for the Maintenance Platoon/Section

091-CLT-4006

Conditions: In a field environment, given a OPORD/maintenance situation, a maintenance platoon or section with personnel and equipment, SOP, and applicable references.

Standards: Coordinated support for the maintenance platoon/section IAW SOP and applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Evaluated the tactical situation and OPORD requirements. | —— | —— |
| 2. Determined support needed at each location. | —— | —— |
| 3. Notified parent/supported units of support requirements. | —— | —— |
| 4. Followed up to ensure support had been coordinated/was being provided. | —— | —— |
| a. Notified appropriate parent/supported units to resolve any problems. |  |  |
| b. Addressed problems in after action review (AAR). |  |  |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 4-30.3 (FM 9-43-1) |  |

Select a Field Maintenance Site

091-CLT-4007

Conditions: In a field environment, given an OPORD to establish a field maintenance site, maintenance personnel, equipment, and references.

Standards: Selected a field maintenance site IAW the OPORD and applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Considered the following elements of a good field maintenance site during the selection process: | —— | —— |
| a. Area should be reasonably flat and have good drainage. |  |  |
| b. Area should have firm soil to permit parking and movement of heavy vehicles and equipment. |  |  |
| c. Area should be accessible to support units. |  |  |
| d. Terrain should facilitate defense. |  |  |
| e. Area should be near built-up areas that can be used for mission support. |  |  |
| 2. Performed a map reconnaissance to determine possible sites. | —— | —— |
| 3. Performed an area reconnaissance and site recons to determine the best site. | —— | —— |
| 4. Informed higher headquarters of the field maintenance site location. | —— | —— |
| 5. Relocated to the new field maintenance site. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 4-30.3 (FM 9-43-1) |  |

Prepare an Operational Overlay for Maintenance Operations

091-CLT-4008

Conditions: In a field or garrison environment, given a map, overlay material, maintenance situation/OPORD, and applicable references.

Standards: Prepared an operational overlay for maintenance operations by depicting key activities and elements within the area of operation IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured necessary references and materials were available. | —— | —— |
| 2. Placed units/activities on the maintenance operations overlay using the appropriate symbols. | —— | —— |
| 3. Placed key features of the area of operation on the overlay. | —— | —— |
| 4. Updated the operational overlay, as necessary. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 101-5-1 |  |
| FM 4-30.3 (FM 9-43-1) |  |
| FM 5-170 |  |

Control Flow of Work Through the Maintenance Shop

091-CLT-4009

Conditions: In a field or garrison environment, given a maintenance shop including personnel, work orders, and applicable references.

Standards: Controlled the flow of work within the maintenance shop to ensure maximum production, effective use of personnel and facilities, and orderly progression of work so that overloads were prevented or corrected, and the shop was working near capacity with a manageable backlog.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Screened maintenance requests. | —— | —— |
| 2. Assigned work to the appropriate shop section. | —— | —— |
| 3. Maintained work load status for the various sections. | —— | —— |
| 4. Directed repair priorities and additional actions(evacuation, operational readiness float (ORF), intra-shop, deferred) as applicable. | —— | —— |
| 5. Ensured shop supply section orders/maintained repair parts, as required. | —— | —— |
| 6. Improved operational procedures where necessary. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 4-30.3 (FM 9-43-1) |  |
| TC 43-4 |  |

Integrate Automated Logistics Support Systems

091-CLT-4010

Conditions: In a field or garrison environment, given a Unit Level Logistics System-Ground (ULLS-G) computer system with software and equipment data base in a unit-level maintenance shop, a Standard Army Maintenance System-1 (SAMS-1) computer system with software and database in a direct support (DS)-level maintenance shop, a Standard Army Maintenance System -2 (SAMS-2) computer system with software and data base in a support operations section, and applicable publications.

Standards: Integrated automated logistics support systems in a maintenance shop IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Identified the architecture/interface of Army automated logistics systems. | —— | —— |
| 2. Supervised ULLS-G functions in a unit-level maintenance shop. | —— | —— |
| 3. Supervised SAMS-1 functions in a DS-level maintenance shop. | —— | —— |
| 4. Supervised SAMS-2 functions in a support operations section. | —— | —— |
| 5. Interfaced with Standard Army Retail Supply System-Objective (SARSS-O) for supply functions. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AISM 18-L21-AHN-BUR-UM |  |
| AISM 18-L26-AHO-BUR-EM |  |
| AR 710-2 |  |
| DA PAM 710-2-1 |  |
| DA PAM 738-750 |  |

Plan Logistics Support for Maintenance Operations

091-CLT-4011

Conditions: In a field or garrison environment, given an OPORD/maintenance situation, maintenance personnel and equipment, and applicable references.

Standards: Planned logistics support for maintenance operations IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Appraised the combat situation. | —— | —— |
| 2. Determined support needed. | —— | —— |
| a. People (skills and numbers). |  |  |
| b. Equipment (transportation, tools, TMDE, and communications). |  |  |
| c. Supplies (components, assemblies, and repair parts). |  |  |
| 3. Organized resources to provide needed support. | —— | —— |
| 4. Followed these planning considerations: | —— | —— |
| a. Number and type of units supported. |  |  |
| b. Stock levels for repair parts. |  |  |
| c. Forward displacement of maintenance support teams/maintenance collection points. |  |  |
| d. Channels and procedures for recovery, collection, evacuation, and disposition of captured or abandoned materiel. |  |  |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 4-30.3 (FM 9-43-1) |  |

Monitor the Preparation and Disposition of the Army Materiel Status System (AMSS) Reports

091-CLT-4012

Conditions: In a field or garrison unit-level maintenance shop, given a unit level logistics system-ground ( ULLS-G) computer system with AMSS software, AMSS reports produced from a ULLS-G system, and applicable references.

Standards: Verified accuracy of AMSS report data, identified maintenance trends and problems, and ensured timely completion and forwarding of reports IAW applicable references and SOP.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured necessary ULLS equipment and references were available. | —— | —— |
| 2. Checked AMSS report data for accuracy and completeness. | —— | —— |
| 3. Analyzed AMSS reports and data to identify maintenance trends and problems. | —— | —— |
| 4. Notified supported units, logistics assistance office/logistics assistance representative, and chain of command, (as necessary), to resolve problems and prevent future occurrences. | —— | —— |
| 5. Ensured AMSS reports were completed and forwarded through appropriate channels IAW SOP. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AR 710-2 |  |
| DA PAM 710-2-1 |  |
| DA PAM 738-750 |  |

Analyze the Prescribed Load List (PLL) Report

091-CLT-4013

Conditions: In a field or garrison unit-level maintenance shop, given PLL reports produced by ULLS-G system and applicable references.

Standards: Analyzed the PLL reports to ensure inventory accuracy and identified potential supply shortages/problems impacting on maintenance readiness IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured reports and references were available. | —— | —— |
| a. PLL inventory report. |  |  |
| b. Zero balance report. |  |  |
| c. PLL excess management report. |  |  |
| d. PLL inquiries (as needed). |  |  |
| e. NMC report. |  |  |
| 2. Performed random inventory checks and resolved discrepancies. | —— | —— |
| 3. Determined expedient measures necessary to resolve not mission capable supply (NMC-S) equipment awaiting PLL items on the zero balance report. | —— | —— |
| 4. Resolved discrepancies in report data within the ULLS-G system. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AR 710-2 |  |
| DA PAM 710-2-1 |  |
| DA PAM 738-750 |  |

Monitor Quality Control Program

091-CLT-4014

Conditions: In a field or garrison maintenance shop, given a maintenance facility/site, maintenance personnel, maintenance SOP, and applicable references.

Standards: Monitored the quality control program to ensure quality of work IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured quality assurance/quality control (QA/QC) inspectors were adequately trained and knowledgeable in their respective maintenance areas and were on orders from the commander, if required by SOP. | —— | —— |
| 2. Ensured QA/QC inspectors followed maintenance SOP guidelines and procedures and TM procedures for initial and final inspections. | —— | —— |
| 3. Performed periodic checks of inspectors' work for accuracy of initial diagnosis and quality of final inspections. | —— | —— |
| 4. Ensured supervisors were conducting in-process inspections of work done by mechanics/technicians. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AR 710-2 |  |
| DA PAM 710-2-1 |  |
| FM 4-30.3 (FM 9-43-1) |  |

Analyze Bench Stock Listing

091-CLT-4015

Conditions: In a field or garrison DS-level maintenance shop, given a SAMS-1 generated bench stock listing (AHN-023) and applicable references.

Standards: Analyzed bench stock listing to identify supply problems that may impact maintenance readiness IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured report and references were available. | —— | —— |
| 2. Performed random bench stock inventory checks. | —— | —— |
| 3. Determined expedient measures necessary to resolve NMC-S equipment awaiting bench stock items. | —— | —— |
| 4. Resolved any discrepancies in report data in the SAMS-1. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AISM 18-L21-AHN-BUR-UM |  |
| AR 710-2 |  |
| DA PAM 710-2-1 |  |
| DA PAM 738-750 |  |

Analyze Open Work Request Reconciliation Listing

091-CLT-4016

Conditions: In a field or garrison DS-level maintenance shop, given a SAMS-1 generated open work request reconciliation listing and applicable references.

Standards: Analyzed the open work request reconciliation listing IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured references and equipment were available. | —— | —— |
| 2. Conducted face-to-face reconciliation with team chief. | —— | —— |
| 3. Supervised SAMS operator on purging operations. | —— | —— |
| 4. Supervised SAMS operator on mail status returned on organizational disk. | —— | —— |
| 5. Improved operational procedures where necessary. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AISM 18-L21-AHN-BUR-UM |  |
| AISM 18-L26-AHO-BUR-EM |  |

Analyze Completed Shop Workload Summary

091-CLT-4017

Conditions: In a field or garrison DS-level maintenance shop, given a SAMS-1 generated completed shop workload summary report and applicable references.

Standards: Analyzed the completed shop workload summary report IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured references and equipment were available. | —— | —— |
| 2. Assigned workload to personnel, as required. | —— | —— |
| 3. Tracked status of all jobs requiring parts. | —— | —— |
| 4. Ensured once job was completed, parts were turned in and paperwork completed IAW local SOP. | —— | —— |
| 5. Improved operational procedures, where necessary. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AISM 18-L21-AHN-BUR-UM |  |
| AISM 18-L26-AHO-BUR-EM |  |

Analyze Shop Deadline and Deferred Workload Listing

091-CLT-4018

Conditions: In a field or garrison DS-level maintenance shop, given a SAMS-1 generated shop deadline and deferred workload listing report and applicable references.

Standards: Analyzed the shop deadline and deferred workload listing report IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured references and equipment were available. | —— | —— |
| 2. Prioritized jobs by the status and priority code. | —— | —— |
| 3. Tracked workload listing for proper status of operation and maintenance (O/M). | —— | —— |
| 4. Supervised AHN-006, AHN-022, and AHN-026 reports. | —— | —— |
| 5. Improved operational procedures where necessary. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AISM 18-L21-AHN-BUR-UM |  |
| AISM 18-L26-AHO-BUR-EM |  |

Analyze Shop Workload Summary Listing

091-CLT-4019

Conditions: In a field or garrison DS-level maintenance shop, given a SAMS-1 generated shop workload summary listing and applicable references.

Standards: Analyzed the shop workload summary listing IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured references and equipment were available. | —— | —— |
| 2. Assigned workload to personnel, as required. | —— | —— |
| 3. Tracked status of all jobs requiring parts. | —— | —— |
| 4. Ensured once job was completed, parts were turned in and paperwork completed IAW local SOP. | —— | —— |
| 5. Improved operational procedures where necessary. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AISM 18-L21-AHN-BUR-UM |  |
| AISM 18-L26-AHO-BUR-EM |  |

Maintain Property Accountability

091-CLT-4020

Conditions: In a field or garrison environment, given property and tools, property book listing and/or hand receipts, blank forms, and applicable references.

Standards: Maintained property accountability IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured all references, technical bulletins (TBs), supply catalogs (SCs), and forms were available. | —— | —— |
| 2. Performed initial inventory of all property, tools, and equipment. | —— | —— |
| a. Completed shortage annexes, as necessary. |  |  |
| b. Reported all shortages, as necessary. |  |  |
| c. Initiated report of survey or other property loss actions, as necessary. |  |  |
| d. Ordered replacement items. |  |  |
| 3. Prepared sub-hand receipts for subordinate sections. | —— | —— |
| 4. Had subordinates inventory all property, tools, and equipment on each respective subhand receipt and shortage annex and sign for property on hand. | —— | —— |
| 5. Signed for property on property book or hand receipts, as applicable. | —— | —— |
| 6. Performed periodic inventories of tools and sensitive items, as required. | —— | —— |
| 7. Performed periodic partial or full inventories, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| AR 710-2 |  |
| DA PAM 710-2-1 |  |

Prepare Standing Operating Procedures for Maintenance Operations

091-CLT-4021

Conditions: In a field or garrison environment, given FM 9-43-1, higher headquarters SOP(s), and commander's guidance.

Standards: Prepared a maintenance shop internal or external SOP for the commander's review, comment, and approval IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured applicable publications were available. | —— | —— |
| 2. Prepared a maintenance shop internal or external SOP. | —— | —— |
| 3. Ensured unit policies and commander's guidance were followed. | —— | —— |
| 4. Ensured shop operation policies were adequately addressed. | —— | —— |
| 5. Updated the shop SOP as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 4-30.3 (FM 9-43-1) |  |

Supervise the Deployment of Company Maintenance Team/Recovery

SupportTeam/Maintenance Support Team

091-CLT-4022

Conditions: In a field or garrison environment, given a request for maintenance support/maintenance situation, map, operational overlay, grid coordinates of destination, vehicle(s), equipment, maintenance personnel, and applicable references.

Standards: Supervised the deployment of company maintenance team/recovery support team(s) IAW the maintenance situation/request for maintenance support and applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Reviewed the request for maintenance support/maintenance situation. | —— | —— |
| 2. Ensured personnel and equipment to perform the mission were available. | —— | —— |
| 3. Ensured resources for the company maintenance team/recovery support team/maintenance support team, including personnel with applicable MOSs, vehicle(s), tools, test equipment, publications, repair parts, time, and facilities were appropriately identified. | —— | —— |
| 4. Ensured requirements for defending the team had been properly determined and arranged. | —— | —— |
| 5. Ensured team leader(s) were briefed on the mission. | —— | —— |
| a. Reviewed the operational overlay. |  |  |
| b. Conducted a map recon of the route and destination. |  |  |
| 6. Ensured the company maintenance team/recovery support team/maintenance support team was deployed. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 101-5-1 |  |
| FM 4-30.3 (FM 9-43-1) |  |
| FM 5-170 |  |

Conduct a Route Reconnaissance for a Maintenance Mission

091-CLT-4023

Conditions: In a field environment, given a maintenance situation/OPORD, operational overlay, grid coordinates for a proposed route, map, vehicle with personnel, and applicable references.

Standards: Conducted a route reconnaissance for a given route identifying distances/times, problem areas along the route, possible bypasses or alternate routes, and prepared strip maps IAW the maintenance situation/OPORD and applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured necessary equipment and publications were available. | —— | —— |
| 2. Determined the route to be used for the maintenance mission. | —— | —— |
| 3. Performed a map recon of the route. | —— | —— |
| 4. Contacted units along the route and coordinated passage. | —— | —— |
| 5. Selected personnel to conduct the reconnaissance. | —— | —— |
| 6. Reconned the route identifying key features to include: | —— | —— |
| a. Potential problem areas (i.e., possible enemy contact, trafficability, etc.). |  |  |
| b. Possible bypasses/alternate routes. |  |  |
| 7. Recorded information on a strip map for use by the maintenance team. | —— | —— |
| 8. Advised the commander/staff officer on use of the route for maintenance missions. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 4-30.3 (FM 9-43-1) |  |
| FM 5-170 |  |

Conduct an Area Reconnaissance for a Maintenance Mission

091-CLT-4024

Conditions: In a field environment, given a maintenance situation/OPORD, operational overlay, grid coordinates for a proposed occupation area, map, vehicle with personnel, and applicable references.

Standards: Performed an area reconnaissance, selecting the most appropriate location to establish a maintenance site IAW the maintenance situation/OPORD and applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Ensured necessary equipment and publications were available. | —— | —— |
| 2. Performed a map recon of the area. | —— | —— |
| 3. Selected personnel to conduct the reconnaissance. | —— | —— |
| 4. Reconned the area to determine suitability for maintenance operations, accessibility in and out of the site, defendability, and actions required for the safety of personnel and equipment. | —— | —— |
| 5. Advised the commander/staff officer on occupying the area of operations based upon the reconnaissance. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 4-30.3 (FM 9-43-1) |  |
| FM 5-170 |  |

Manage Battlefield Maintenance Support

091-CLT-4025

Conditions: In a field maintenance shop, given an OPORD/maintenance situation, maintenance personnel, equipment, and applicable references.

Standards: Managed battlefield maintenance support IAW applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Appraised the combat situation and organized and prioritized support based on type of operation: | —— | —— |
| a. Offensive operation. |  |  |
| b. Defensive operation. |  |  |
| 2. Planned for and executed appropriate maintenance support: | —— | —— |
| a. Identified requirements. |  |  |
| b. Identified available resources. |  |  |
| (1) Personnel and skills. |  |  |
| (2) Publications. |  |  |
| (3) Time. |  |  |
| (4) Facilities. |  |  |
| (5) TMDE and tools. |  |  |
| (6) Parts. |  |  |
| c. Managed resources for maximum return, with priority on the following: |  |  |
| (1) Maintenance support forward. |  |  |
| (2) Commander's guidance. |  |  |
| (3) Battle damage repair. |  |  |
| (4) Controlled exchange. |  |  |
| (5) Cannibalization. |  |  |
| (6) Evacuation. |  |  |
| (7) Recovery. |  |  |
| 3. Followed priorities for repair of battle damaged systems: | —— | —— |
| a. Most essential for completion of the immediate mission. |  |  |
| b. Least amount of time to repair. |  |  |
| c. Reparable, but not in time to continue the immediate mission. |  |  |
| d. Damaged beyond repair candidate for cannibalization. |  |  |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 4-30.3 (FM 9-43-1) |  |

Perform Support Operations NCO Duties

091-CLT-4026

Conditions: In a field or garrison environment, given a position as a support operations maintenance NCO, and applicable references.

Standards: Performed the duties of a support operations maintenance NCO, ensuring that the direct support (DS) maintenance mission is effectively coordinated and integrated within the battalion or support group.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Provided guidance on maintenance priorities within the unit. | —— | —— |
| 2. Set objectives for maintenance shop production. | —— | —— |
| 3. Monitored maintenance shop workflow and status of repair part requisitions. | —— | —— |
| 4. Supervised, controlled, and directed the operation of battalion units for: | —— | —— |
| a. DS maintenance. |  |  |
| b. Evacuation. |  |  |
| c. Repair parts supply. |  |  |
| d. Reparable exchange (RX). |  |  |
| e. Technical assistance. |  |  |

Evaluation Guidance:  Score the soldier GO if all steps are passed. Score the soldier NO GO if any step is failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 100-16 |  |
| FM 4-30.3 (FM 9-43-1) |  |

Manage Maintenance Operations at a Maintenance Collection Point

091-CLT-4027

Conditions: In a field maintenance environment, given an OPORD/maintenance situation, a maintenance collection point (MCP) site, maintenance personnel and equipment, and applicable references.

Standards: Managed maintenance operations at an MCP IAW the OPORD and applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Set up the MCP. | —— | —— |
| 2. Managed flow of equipment for repair. | —— | —— |
| a. Focused efforts toward repairing systems for current battle or start of next battle. |  |  |
| b. Fixed 4 to 6 hour jobs at unit maintenance collection point (UMCP). |  |  |
| c. Evacuated other equipment to brigade MCP or farther rear location. |  |  |
| d. Maximized battle damage assessment repair ( BDAR), cannibalization, and controlled exchange at central MCP. |  |  |
| 3. Managed company maintenance teams/recovery support teams/maintenance support teams held at MCP. | —— | —— |
| 4. Managed prescribed load list (PLL) assets for forward combat units. | —— | —— |
| 5. Relocated forward (as necessary) to continue fix-forward support. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 4-30.3 (FM 9-43-1) |  |

Provide Maintenance Support During Tactical Operations

091-CLT-4028

Conditions: In a field environment, given an operation order (OPORD)/maintenance situation, maintenance personnel and equipment, and applicable references.

Standards: Provided maintenance support during tactical operations IAW the OPORD and applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Provided maintenance support during offensive operations. | —— | —— |
| 2. Provided maintenance support during defensive operations. | —— | —— |
| 3. Provided maintenance support during retrograde operations. | —— | —— |
| 4. Provided maintenance support during reconstitution operations. | —— | —— |
| 5. Provided maintenance support during night operations. | —— | —— |
| 6. Provided maintenance support in NBC environment. | —— | —— |
| 7. Provided maintenance support during stability and support operations (SASO). | —— | —— |
| a. Peace operations. |  |  |
| b. Humanitarian operations. |  |  |
| c. Disaster relief operations. |  |  |
| 8. Provided maintenance support in the following adverse conditions. | —— | —— |
| a. Desert operations. |  |  |
| b. Cold weather operations. |  |  |
| c. Jungle operations. |  |  |
| d. Mountain operations. |  |  |
| e. Urban terrain operations. |  |  |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 4-30.3 (FM 9-43-1) |  |

This page intentionally left blank

90APPENDIX A

HANDS-ON EVALUATION (DA FORM 5164-R)

INSTRUCTIONS

(Excerpted from STP 21-24-SMCT, Appendix C)

DA Form 5164-R (Hands-On Evaluation) allows the trainer to keep a record of the performance measures a soldier passes or fails on each task.

Before evaluation:

1.  Obtain a blank copy of DA Form 5164-R, which you may locally reproduce on 8 ½ x 11 paper.

2.  Enter the task title and 10-digit number from the STP task summary.

3.  In Column a, enter the performance measure numbers from the task summary.

4.  In Column b, enter the performance measure corresponding to the number in Column a (you may

abbreviate this information if necessary).

5.  Locally reproduce the partially completed form when evaluating more than one soldier on the task or

when evaluating the same soldier more than once.

During evaluation:

1.  Enter the date just before evaluating the soldier's task performance.

2.  Enter the evaluator's name, the soldier's name, and the unit.

3.  For each performance measure in Column b, enter a check in Column c (PASS) or Column d (FAIL),

as appropriate.

4.  Compare the number of performance measures the soldier passes (and, if applicable, which ones)

against the task standards specified in the task summary.  If the standards are met or exceeded,

check the GO block under STATUS; otherwise, check the NO-GO block.

| HANDS-ON EVALUATION For use of this form, see AR 350-57; the proponent agency is ODCSOPS | DATE |
| --- | --- |
| TASK TITLE | TASK NUMBER |
| ITEM a | PERFORMANCE STEP TITLE b | SCORE (Check One) |
|  |  | PASS c | FAIL d |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
| EVALUATOR'S NAME | UNIT |
| SOLDIER'S NAME | STATUS GO NO GO |

DA FORM 5164-R, SEP 85                        EDITION OF DEC 82 IS OBSOLETE                                                            USAPPC V2.00

91APPENDIX B -

FIELD EXPEDIENT SQUAD BOOK (DA FORM 5165-R)

INSTRUCTIONS

DA Form 5165-R (Field Expedient Squad Book) allows the trainer to keep a record of task proficiency for a group of soldiers.

Before evaluation:

1.  Obtain a blank copy of DA Form 5165-R, which you may locally reproduce on 8 ½“ x 11“ paper.

2.  Locally reproduce the partially completed form if you are evaluating more than nine soldiers.

During evaluation:

1.  Enter the names of the soldiers you are evaluating, one name per column, at the top of the form.

2.  Under STATUS, record (in pencil) the date in the GO block if the soldier demonstrated task

proficiency to soldier's manual standards.  Keep this information current by always recording the most

recent date on which the soldier demonstrated task proficiency.  Record the date in the NO-GO block

if the soldier failed to demonstrate task proficiency to soldier's manual standards.  Soldiers who failed

to perform the task should be retrained and reevaluated until they can meet the standards. When the

standards are met, enter the date in the appropriate GO block and erase the previous entry from the

NO-GO block.

After evaluation:

1.  Read down each column (GO/NO-GO) to determine the training status of an individual. This will give

you a quick indication of which tasks a soldier needs training on.

2.  Read across the rows for each task to determine the training status of all soldiers.  You can readily

see which tasks to focus training on.

3.  Line through the STATUS column of any soldier who leaves the unit.

This page intentionally left blank

88GLOSSARY

Section I

Abbreviations

AAVP	Army Audiovisual Program

ACCP	Army Correspondence Course Program

AIT	advanced individual training

AN	annually

ARTEP-MTP	Army Training and Evaluation Program Mission Training Plan

ASI	additional skill identifier

AVLB	armored vehicle launched bridge

BDAR	battle damage assessment and repair

BM	bimonthly (once every two months)

C-HET	commercial heavy equipment transporter

HEMTT	heavy expanded mobility vehicle

HMMWV	high mobility multipurpose wheeled vehicle

HET	heavy equipment transporter

PLS	palletized load system

IAW	in accordance with

IET	Initial Entry Training

NCO-ER	noncommissioned officer evaluation report

NCOES	NCO Education System

QT	quarterly

SL	skill level

SMCT	soldier's manual of common tasks

STE/ICE	simplified test equipment/internal combustion engine

TAMMS	the army maintenance management system

TMDE	test measurement and diagnostic equipment

VRRTFL			  variable reach rough terrain forklift

Section II

Terms

Condition

Task condition-The task condition describes the field conditions under which the task will be performed.  The condition expands on the information in the task title by identifying when, where, and why the soldier performs the task and what materials, personnel, and equipment the soldier must have to perform the task.   Learning objective condition--The learning objective condition describes the training situation or environment under which the student must perform the learning action statement.  It includes any pertinent influence on learning objective performance, including identification of materials, facilities, and equipment the student must have to perform the objective.

Critical task

See "task," critical collective task," and "critical individual task."

Duty Position

Duty positions are determined by military occupational specialties (MOSs), which are subdivided into five major skill levels (SLs). These SLs are further subdivided into related individual tasks which identify a soldier's SL or job.

Duty Position Task

A task identified with and related to a particular position at a given SL within a specified MOS or area of concentration (AOC).

GO/NO-GO

This is a pass/fail evaluation whereby the soldier (student) cannot be partially correct.  Either he meets the standard or he does not meet the standard.

Jobs

The tasks performed by a single worker constitute his job.  If identical tasks are performed by several individuals, they all hold the same job.  Job is the same as duty position.  An MOS is made up of skill levels.  Skill levels are made up of jobs, also called duty positions.

Knowledge

Information or fact required to perform a skill or supported task.

Performance measures

The actions that can be objectively observed and measured to determine if a task performer has performed the task to the prescribed standard.  These measures are derived from the task performance steps during task analysis.  See "Task performance specifications."

Skills

The ability to perform a job related activity which contributes to the effective performance of a task.

Standard

A statement which establishes a criteria for how well a task or learning objective must be performed.  The standard specifies how well, completely, or accurately a process must be performed or product produced.  The task standard reflects task performance requirements on the job.  The learning objective standard reflects the standard that must be achieved in the formal learning environment.

Task

A clearly defined and measurable activity accomplished by individuals and organizations.  It is the lowest behavioral level in a job or unit that is performed for its own sake.  It must be specific; usually has a definite beginning and ending; may support or be supported by other tasks; has only one action and, therefore, is described using only one verb;  generally is performed in a relatively short time (however, there may be no time limit or there may be a specific time limit); and it must be observable and measurable.   The task title must contain an action verb and object and may contain a qualifier.  Types: (subsequent entries)

Task summary

A listing in the soldiers' training publications of the conditions, standards, and performance measures, references, and proponent for each individual critical task.  Information is extracted from the individual critical task analysis.  See "Task performance specifications."  Reference-dependent task summary-A summary written for those tasks which require the trained soldier to refer to one or more publications while performing all or part of a task in wartime conditions.  Reference-independent task summary-A summary written for those tasks which require the trained soldier to perform the task in wartime conditions from memory, without reference to any publications.

This page intentionally left blank

99REFERENCES

Required Publications

Required publications are sources that users must read in order to understand or to comply with this publication.

Army Regulations

AR 190-13	The Army Physical Security Program (This Item is Included on EM 0001).  30 September 1993

AR 190-51	Security of Unclassified Army Property (Sensitive and Non-sensitive) (This Item is Included on EM 0001)  30 September 1993

AR 220-1	Unit Status Reporting (This Item is Included on EM 0001)  1 September 1997

AR 25-400-2	The Modern Army Record Keeping System (MARKS) (This Item is Included on EM 0001)  26 February 1993

AR 385-10	The Army Safety Program (This item is included on EM 0001)  23 May 1988

AR 385-40	Accident Reporting and Records (This Item is Included on EM 0001)  1 November 1994

AR 385-55	Prevention of Motor Vehicle Accidents (This item is Included on EM 0001)  12 March 1987

AR 40-5	Preventive Medicine (This Item is Included on EM 0001)  15 October 1990

AR 600-55	The Army Driver and Operator Standardization Program (Selection, Training, Testing, and Licensing) (This Item is Included on EM 0001)  31 December 1993

AR 600-8-2	Suspension of Favorable Personnel Actions (FLAGS) (This Item is Included on EM 0001)  30 October 1987

AR 614-200	Enlisted Assignments and Utilization Management (This Item is Included on EM 0001)  31 October 1997

AR 623-205	Enlisted Evaluation Reporting System (This Item is Included on EM 0001)  31 March 1992

AR 635-200	Enlisted Personnel (This Item is Included on EM 0001)  5 July 1984

AR 700-138	Army Logistics Readiness and Sustainability (This Item is Included on EM 0001)  16 September 1997

AR 700-4	Logistics Assistance (This Item is Included on EM 0001)  30 June 1995

AR 710-2	Inventory Management Supply Policy Below the Wholesale Level (This Item is on EM 0001)  31 October 1997

AR 725-50	Requisition, Receipt, and Issue System (This Item is Included on EM 0001)  15 November 1995

AR 735-11-1	Uniform Settlement of Military Freight Loss and Damage Claims (This Item is Included on EM 0001)  1 January 1988

AR 735-5	Policies and Procedures for Property Accountability (This Item is Included on EM 0001)  31 January 1998

AR 750-1	Army Materiel Maintenance Policy and Retail Maintenance Operations (This Item is Included on EM 0001)  1 August 1994

AR 750-43	Army Test, Measurement and Diagnostic Equipment Program (This Item Is Included on EM 0001)  28 November 1997

Department of Army Pamphlets

DA PAM 25-30	Consolidated Index of Army Publications and Blank Forms (ISSUED QUARTERLY)(No Printed Copies Exist)(Formerly DA Pam 310-1)(This Item is Included on EM 0001)  1 April 2001

DA PAM 25-33	User's Guide for Army Publications and Forms  (This Item is Included on EM 0001)  15 September 1996

DA PAM 385-1	Small Unit Safety Officer/NCO Guide  22 September 1993

DA PAM 710-2-1	Using Unit Supply System (Manual Procedures) (Standalone Pub) (This Item is on EM 0001)  31 December 1997

DA PAM 710-2-2	Supply Support Activity Supply System:  Manual Procedures (This Item is on EM 0001)  30 September 1998

DA PAM 738-750	Functional Users Manual for The Army Maintenance Management System (TAMMS) (This Item is Included on EM 0001)  1 August 1994

DA PAM 750-1	Leader's Unit Level Maintenance Handbook (This Item is Included on EM 0001)  15 February 1994

DA PAMPHLET 738-750	Functional Users Manual for the Army Maintenance Management System (TAMMS)  1 August 1994

DA PAMPHLET 750-35	Functional Users Guide for Motor Pool Operations. 30 May 1989.

Field Manuals

FM 100-16	Army Operational Support  31 May 1995

FM 101-5-1	Operational Terms and Graphics (MCRP 5-2A)  30 September 1997

FM 21-26	Map Reading and Land Navigation  7 May 1993

FM 21-305	Manual for the Wheeled Vehicle Driver [AFMAN 24-306]  27 August 1993

FM 21-31	Topographic Symbols (Reprinted w/ Basic Incl C1) (This item is included on EM 0028)  19 June 1961

FM 22-51	Leader's  Manual for Combat Stress Control  29 September 1994

FM 24-35	(O) Signal Operation Instructions "The SOI"  26 October 1990

FM 25-4	How to Conduct Training Exercises (This Item is Included on EM 0028)  10 September 1984

FM 25-5	Training for Mobilization and War (This Item is Included on EM 0028)  25 January 1985

FM 4-30.3 (FM 9-43-1)	Maintenance Operations and Procedures  1 September 2000

FM 5-125	Rigging Techniques, Procedures, and Applications (This Item is Included on EM 0028)  3 October 1995

FM 5-170	ENGINEER RECONNAISSANCE  5 May 1998

FM 9-43-2	Recovery and Battlefield Damage Assessment and Repair (FMFRP 4-34; TO 36-1-181)  3 October 1995

Lubrication Orders

LO 9-2320-272-12	Truck, 5-Ton, 6x6, M939, M939A1 and M939A2 Series (Diesel) Truck, Cargo, 5-Ton, 6x6, Dropside, M923 (NSN 2320-01-050-2084), M923A1 (2320-01-206-4087), M923A2 (2320-01-230-0307), M925 (2320-01-047-8769), M925A1 (2320-01-206-4088), M925A  11 June 1990

LO 9-2320-279-12	M977 Series, 8x8 Heavy Expanded Mobility Tactical Trucks (HEMTT) Truck, with Winch, M977 (NSN 2320-01-097-0260), Truck, Cargo,  without Winch M977 (2320-01-099-6426), Truck Tank, Fuel with Winch M978, (This item is included on EM 0030)  15 December 1998

LO 9-2320-280-12	Truck, Utility: Cargo/Troop Carrier, 1 1/4 Ton, 4 X 4, M998 Truck, Utility: Cargo/Troop Carrier, 1-1/4 Ton, 4 X 4, W/Winch, M1038; Truck Utility: TOW Carrier, Armored, 1-1/4 Ton, 4 X 4, M966 (This Item is Included on EM 0030)  19 January 1990

LO 9-2320-364-12	Palletized Load System (PLS) M1074/M1075 (NSN 2320-01-304-2277) (2320-01-304-2278) (This Item is Included on EM 0052)  1 October 1993

LO 9-2320-386-12	Extended Service Program for 2-1/2 Ton, 6X6, M44A3 ESP Vehicle: Truck, Cargo, Fixed Side: M35A3; Truck, Cargo, Drop side: M35A3C; Truck, Cargo, Long, Wheel base: M36A3 [TO 36A12-1B-112LC-1]  26 January 1996

LO9-2320-280-12	LO9-2320-280-12

Other Product Types

Applicable equipment publications

AISM 18-L21-AHN-BUR-UM	Standard Army Maintenance System Level 1 (SAMS-1) End User Manual

AISM 18-L26-AHO-BUR-EM	Standard Army Maintenance System Level 2 (SAMS-2) End User Manual

Soldier Training Publications

STP 21-1-SMCT	Soldier's Manual Of Common Tasks Skill Level 1  1 October 1994

STP 21-24-SMCT	Soldier's Manual Of Common Tasks (SMCT) Skill Level 2-4  1 October 1992

STP 21-2-SMCT	Soldier's Manual of Common Tasks (Skill Level 1)

Technical Bulletins

TB 43-0142	Safety Inspection and Testing of Lifting Devices (This Item is Included on EM 0055 and EM 0178)  28 February 1997

TB 43-0211	AOAP Army Oil Analysis Program Guide For Leaders and Users  4 June 1998

TB 43-180	Calibration and Repair Requirements for the Maintenance of Army Materiel (This Item is Included on EM 0022)  1 December 2000

TB 9-4910-555-35	Calibration Procedure for Simplified Test Equipment For Internal Combustion Engine (STE/ICE-R) (This Item is Included on EM 0172)  6 January 1997

TB MED 524	Occupational and Environmental Health: Control of Hazards to Health From Laser Radiation  20 June 1985

Technical Manuals

TM  9-243	Use and Care of Hand Tools and Measuring Tools M6290-AJ-MAN-010; TO 32-1-101; TM-10209-10/1 (Reprinted W/Basic Incl C1-2)

TM 10-3930-660-10	Operators Maintenance Manual for Truck, Forklift, 6000 lbs, Variable Reach, Rough Terrain, (NSN 3930-01-158-0849)  30 March 1993

TM 10-3930-660-20	Unit Maintenance Manual for Truck, Forklift, 6000 lbs, Variable Reach, Rough Terrain, (NSN 3930-01-158-0849) (This Item is Included on EM 0055)  25 March 1993

TM 11-5820-890-10-3	Operator for Radio Set AN/PRC 119 VRC 87-92

TM 11-5830-340-12	Operator's and Unit  Organizational Maintenance Manual for Intercommunication Set AN/VIC-1 and Control, Intercommunication Set, C-10456/VRC (This Item is Included on EM 0063)  15 January 1986

TM 11-6625-3052-14	Operator's, Unit, Direct Support and General Support Maintenance Manual for Digital Multimeter AN/PSM-45 (NSN 6625-01-139-2512) (Reprinted w/Basic Incl C1-2)  10 January 1984

TM 11-6625-3052-24P	Organizational, Direct Support and General Support Maintenance Repair Parts and Special Tools List for Multimeter, Digital, AN/PSM-45 (NSN 6625-01-139-2512) (This Item is Included on EM 0068)  3 February 1984

TM 11-6625-3055-14	Operator's, Organizational, Direct Support and General Support Maintenance Manual for Digital Multimeter, AN/USM-486/U. 30 July 1984.

TM 5-5420-202-10	Operator's Manual for Launcher and M60A1 Tank Chassis, Transporting for Bridge, Armored-Vehicle-Launched, Scissoring Type, Class 60 (This Item is Included on EM 0044)  30 August 1985

TM 5-5420-202-20-1	Organizational Maintenance, M60A1 Tank Chassis, Transporting for Bridge, Armored-Vehicle-Launched, Scissoring Type, Class 60  25 October 1985

TM 5-5420-202-20-2	Organizational Maintenance, M60A1 Tank chassis, Transporting for Bridge, Armored-Vehicle-Launched, Scissoring Type, Class 60  28 October 1985

TM 5-5420-202-20-3	Organizational Maintenance, M60A1 Tank Chassis, Transporting for Bridge, Armored-Vehicle-Launched, Scissoring Type, Class 60  28 October 1985

TM 5-5420-202-20-4	Organizational Maintenance, M60A1 Tank Chassis, Transporting for Bridge, Armored-Vehicle-Launched, Scissoring Type, Class 60  28 October 1985

TM 5-5420-203-14	Operator's, Unit, Direct Support and General Support Maintenance Manual for Bridge, Armored-Vehicle-Launched:  Scissoring Type; Aluminum, 60 FT Span for M-48A5 and M-60 Launcher (All Makes and Models)  3 June 1991

TM 5-5420-226-10	Operator's Manual for Launcher and M48A5 Tank Chassis, Transporting for Bridge, Armored Vehicle-Launched, Scissoring Type, Class 60  (This Item is Included on EM 0044)  20 February 1981

TM 5-5420-226-20-1	Organizational Maintenance Manual M48A5 Tank Chassis, Transporting: for Bridge, Armored Vehicle-Launched, Scissoring Type, Class 60 (This item is Included on EM 0044)  20 November 1981

TM 5-5420-226-20-2	Organizational Maintenance Manual M48A5 Tank Chassis, Transporting for Bridge, Armored-Vehicle-Launched, Scissoring Type, Class 60 (This Item is Included on EM 0044)  20 November 1981

TM 5-5420-226-20-3	Organizational Maintenance,  for M48A5 Tank Chassis, Transporting: for Bridge, Armored Vehicle-Launched, Scissoring Type, Class 60 (This Item is Included on EM 0044)  20 November 1981

TM 5-5420-226-20-4	Organizational Maintenance for M48A5 Tank Chassis, Transporting for Bridge, Armored-Vehicle-Launched, Scissoring Type, Class 60 (This Item Included on EM 0044)  20 November 1981

TM 9-2320-211-20P	Organization Parts and Special Tools List for Truck, 5-Ton, M51-Series

TM 9-2320-211-35	Direct Support, General Support, and Depot Maintenance Manual for Truck, 5-Ton, M51-Series

TM 9-2320-260-10	Operator's Manual for Truck, 5-Ton, 6X6, M809 Series (Diesel): Truck, Cargo: M813, M813A1 and M814; Truck Bolster, Logging; M815; Truck, Wrecker, Medium: M816, Truck Dump: M817; Truck Tractor: M818; Truck, Tractor, Wrecker: M819;  14 June 1985

TM 9-2320-270-10	Operator's Manual for Truck, Tractor, Commercial Heavy Equipment Transporter (C-HET), 85,000 GVWR, 8x6, M911 (NSN 2320-01-025-3733) (Reprinted W/Basic Incl C1-7)  2 December 1983

TM 9-2320-270-20-1	Organizational Maintenance for Truck, Tractor, Commercial  Heavy Equipment Transporter (C-HET); 85,000 GVWR, 8x6, M911 (NSN 2320-01-025-3733) Volume 1 Of 3 (Reprinted W/Basic Incl  C1)  14 June 1986

TM 9-2320-270-20-2	Organizational Maintenance Manual for Truck, Tractor, 22 1/2-Ton, Commercial-Heavy Equipment Transporter (C-HET), M911-, M915-Series

TM 9-2320-270-20-3	Organizational Maintenance Manual for Truck, Tractor, 22 1/2-Ton, Commercial-Heavy Equipment Transporter (C-HET), M911-, M915-Series

TM 9-2320-270-20P	Organizational Parts and Special Tools List for Truck, Tractor, 22 1/2-Ton, Commercial-Heavy Equipment Transporter (C-HET), M911-, M915-Series

TM 9-2320-272-10	Operator's Manual for Truck, 5-Ton,6X6, M939, M939A1, and M939A2 Series Truck (Diesel), Truck Cargo: 5-Ton, 6X6 Dropside, M923/A1/A2; M925/A1/A2; M927/A1/A2; M928/A1/A2; M929/A1/A2; (This Item is Included on EM 0039)  15 August 1996

TM 9-2320-272-24-1	Unit, Direct Support and General Support Maintenance Manual for Truck,5-Ton,6X6, M939, M939A1, M939A2 Series Trucks (Diesel) Truck, Cargo: 5-Ton, 6X6, Dropside, M923; M923A1; M923A (This Item is Included on EM 0039)  30 June 1998

TM 9-2320-272-24-2	Unit, Direct Support and General Support Maintenance Manual for Truck, 5-Ton, 6X6, M939, M939A1, M939A2 Series Trucks (Diesel) Truck, Cargo: 5-Ton, 6X6, Dropside, M923; M923A1; M923A (This Item is Included on EM 0039)  30 June 1998

TM 9-2320-272-24-3	Unit, Direct Support and General Support Maintenance Manual for Truck,5-Ton,6X6, M939, M939A1, M939A2 Series Trucks (Diesel) Truck, Cargo: 5-Ton, 6X6, Dropside, M923; M923A1; M923A (This Item is Included on EM 0039)  30 June 1998

TM 9-2320-272-24-4	Unit, Direct Support and General Support Maintenance Manual for Truck,5-Ton,6X6, M939, M939A1, M939A2 Series Trucks (Diesel) Truck, Cargo: 5-Ton, 6X6, Dropside, M923; M923A1; M923A (This Item is Included on EM 0039)  30 June 1998

TM 9-2320-272-24P-1	Unit, Direct Support and General Support Maintenance Repair Parts and Special Tools List for Truck, 5-Ton, 6X6, M939, M939A1, M939A2 Series Trucks (Diesel) Truck, Cargo: 5-Ton, 6X6, Dropside, M923 (NSN 2320-01-050-2084)(EIC:BRY);  1 February 1999

TM 9-2320-272-24P-2	Unit, Direct Support and General Support Maintenance Repair Parts and Special Tools List for Truck, 5-Ton, 6X6, M939, M939A1, M939A2 Series Trucks (Diesel) Truck, Cargo: 5-Ton, 6X6, Dropside, M923 (NSN 2320-01-050-2084)(EIC:BRY); M923A1  1 February 1999

TM 9-2320-279-10-1	Operators Manual for M977 Series 8X8 Heavy Expanded, Mobility Tactical Trucks (HEMTT), Truck, Cargo, with Winch, M977 (NSN 2320-01-097-0260) Truck, Cargo, without Winch , M977 (2320-01-099-6426) Truck, Tank, Fuel With Winch, M978  21 November 1986

TM 9-2320-279-10-2	Operator's Manual for M977 Series, 8X8 Heavy Expanded Mobility Tactical Truck (HEMTT) Truck, Cargo, With Wench, M977, (2320-01-097-0260) Truck, Cargo, Without Wench, M977 (2320-01-099-6426) Truck, Tank, Fuel, With Winch, M978  15 June 1987

TM 9-2320-279-20-1	Maintenance Instructions for Organizational Maintenance M977 Series, 8X8 Heavy Expanded Mobility Tactical Trucks (HEMTT) Truck, Cargo, with Winch M977 (NSN 2320-01-097-0260) Truck, Cargo, without Winch M977 (2320-01-099-6426) Truck, Tank  7 April 1987

TM 9-2320-279-20-2	Volume 2 - Maintenance Instructions for Organizational Maintenance M977 Series, 8X8 Heavy Expanded Mobility Tactical Trucks (HEMTT) Truck Cargo, With Winch M977 (NSN 2320-01-097-0260) Truck, Cargo, Without Winch M977 (2320-01-099-6426)  7 April 1987

TM 9-2320-279-20-3	Maintenance Instructions for Organizational Maintenance 977 Series, 8X8 Heavy Expanded Mobility Tactical Trucks (HEMTT) Truck Cargo, With Winch M977 (NSN 2320-01-097-0260) Truck, Cargo, Without Winch M977 (2320-01-099-6426)  8 April 1987

TM 9-2320-279-24P-1	Direct Support and General Support Maintenance Repair Parts and Special Tools List for M977 Series, 8x8 Heavy Expanded Mobility Tactical Trucks (HEMTT), Truck Cargo, with Winch M977 (NSN 2320-01-097-0260) (EIC:B2G) Truck, Tank  15 December 1998

TM 9-2320-279-34-1	Maintenance Instructions Direct Support and General Support  for M977Series, 8X8 Heavy Expanded Mobility Tactical Trucks (HEMTT) Truck, Cargo, With Winch M977(2320-01-097-0260) Truck, Cargo Without Winch M977 (2320-01-099-6426)  3 June 1987

TM 9-2320-279-34-2	Technical Manual Maintenance Instructions Direct Support and General Support  for M977Series, 8X8 Heavy Expanded Mobility Tactical Trucks (HEMTT) Truck, Cargo, With Winch M977(2320-01-097-0260) Truck, Cargo Without Winch M977  3 June 1987

TM 9-2320-279-34-3	Technical Manual Maintenance Instructions Direct Support and General Support  for M977Series, 8X8 Heavy Expanded Mobility Tactical Trucks (HEMTT) Truck, Cargo, With Winch M977(2320-01-097-0260) Truck, Cargo Without Winch M977  3 June 1987

TM 9-2320-280-10	Operator's Manual for Truck, Utility: Cargo/Troop Carrier, 1 1/4-Ton, 4X4, M998  (EIC:BBD); M998A1 (EIC:BBN); Truck, Utility; Cargo/Troop Carrier; 1-1/4 Ton, 4X4, W/Winch; M1038, 1038A1; M1097 (This Item is Included on EM 0030 & EM 0034)  31 January 1996

TM 9-2320-280-20-1	Unit Maintenance Volume 1 of 3 for Truck, Utility: Cargo/Troop Carrier, 1-1/4 Ton, 4 X 4, M998 (EIC:BBD); M998A1 (EIC: BBD); Truck, Utility: Cargo/Troop Carrier, 1-1/4Ton, 4 X 4, W/Winch, M1038 (This Item is Included on EM 0030)  31 January 1996

TM 9-2320-280-20-2	Unit Maintenance Volume 2 of 3 for Truck, Utility: Cargo/Troop Carrier, 1-1/4 Ton, 4 X 4, M998; M998A1; Truck, Utility: Cargo/Troop Carrier, 1-1/4Ton, 4 X 4, W/Winch, M1038 (This Item is Included on EM 0030 & EM 0034)  31 January 1996

TM 9-2320-280-20-3	Unit Maintenance manual for Truck, Utility: Cargo/Troop Carrier, 1-1/4 Ton, 4 X 4, M998 (EIC:BBD); M998A1(EIC: BBD); Truck, Utility: Cargo/Troop Carrier, 1-1/4Ton, 4 X 4, W/Winch, M1038 (This Item is Included on EM 0030)  31 January 1996

TM 9-2320-280-24P-1	Unit, Direct Support/General Support Maintenance, Repair Parts and Special Tools List, Volume 1 of 2, for Truck Utility, Cargo/Troop Carrier, 1 1/4 Ton, 4X4, M998 (This Item is Included on EM 0030)  31 January 1996

TM 9-2320-280-24P-2	Unit, Direct Support/General Support Maintenance, Repair Parts and Special Tools List, Volume 2 of 2, for Truck, Utility, Cargo/Troop Carrier, 1 1/4 Ton, 4X4, M998 (This Item is Included on EM 0030)  31 January 1996

TM 9-2320-283-10	Operator's Manual for Truck Tractor, Line Haul; 50,000 GVWR, 6x4, M915A1 (NSN 2320-01-125-2640) (Reprinted W/Basic Incl C1-3) (This Item is Included on EM 0048)  27 June 1983

TM 9-2320-283-20-1	Organizational Maintenance for Truck Tractor, Line Haul, 50, 000 GVWR, 6x4, M915A1 (NSN 2320-01-125-2640) (Reprinted W/ Basic Incl C1) (This Item is Included On EM 0048)  8 December 1983

TM 9-2320-283-20-2	Organizational Maintenance for Truck Tractor, Line Haul, 50, 000 GVWR, 6x4, M915A1 (NSN 2320-01-125-2640) (This Item is Included On EM 0048)  8 December 1983

TM 9-2320-283-20-3	Organizational Maintenance for Truck Tractor, Line Haul; 50, 000 GVWR, 6x4, M915A1 (NSN 2320-01-125-2640) (Reprinted W/ Basic Incl C1) (This Item is Included On EM 0048)  8 December 1983

TM 9-2320-283-24P	Unit Maintenance, Direct Support and General Support Maintenance Repair Parts and Special Tools List for Truck, Tractor, Line Haul, 50,00 GVWR, 6X4, M915A1

TM 9-2320-289-20	Unit Maintenance Manual for Truck, Cargo Tactical, 1-1/4 Ton, 4x4, M1008 (2320-01-123-6827) Truck, Cargo, Tactical, 1-1/4 Ton, 4x4, M1008A1 (2320-01-123-2671) Truck, Utility, Tactical, 3/4 Ton, 4x4, M1009 (2320-01-123-2665) Truck  20 January 1988

TM 9-2320-360-10	Operator's Manual for Truck, Tractor, M1070, 8X8, Heavy Equipment Transporter (HET) (NSN 2320-01-318-9902)(EIC:B5C)  31 March 1994

TM 9-2320-360-20-1	Unit Maintenance Manual for Truck, Tractor, M1070, 8X8, heavy Equipment Transporter (HET) (NSN 2320-01-318-9902)(EIC:B5C)  31 March 1994

TM 9-2320-360-20-2	Unit Maintenance Manual for Truck, Tractor, M1070, 8X8, heavy Equipment Transporter (HET) (NSN 2320-01-318-9902)(EIC:B5C)  31 March 1994

TM 9-2320-361-10	Operator's Manual for 2 1/2Ton, 6X6, M44A2 Series Trucks (Multifuel); Truck, Cargo: 2 1/2 Ton, 6X6, M35A2, M35A2C, M36A2, Truck, Tank, Fuel: 2 1/2 Ton, 6X6 M50A2, M50A3; Truck, Van, Shop: 2 1/2 Ton, 6X6, M109A3; Truck Instrument Repair Shop  15 December 1988

TM 9-2320-361-20	Unit Maintenance for 2-1/2 Ton 6 X 6, M44A2 Series Trucks (Multifuel) Model Truck, Cargo M35A2 W/O Winch (NSN 2320-00-077-1616) W/Winch (2320-00-077-1617) M35A2C W/O Winch (2320-00-926-0873) W/Winch (2320-00-926-0875) M36A2 W/O Winch  25 October 1991

TM 9-2320-364-10	Operators Manual for Truck, Tractor, M1074 and M1075 Palletized Load System (PLS) (NSN 2320-01-304-2277) (2320-01-304-2278)  1 August 1999

TM 9-2320-364-20-1	Unit Maintenance Manual, Volume I for Palletized Load System M1074/M1075 (NSN 2320-01-304-2277)(2320-01-304-2278) (This item is included on EM 0052)  1 August 1999

TM 9-2320-364-20-2	Unit Maintenance Manual, Volume I I for Palletized Load System M1074/M1075 (NSN 2320-01-304-2277)(2320-01-304-2278) (This item is included on EM 0052)  4 August 1999

TM 9-2320-364-20-3	Unit Maintenance Manual, Volume III for Palletized Load System M1074/M1075 (NSN 2320-01-304-2277)(2320-01-304-2278) (This item is included on EM 0052)  1 August 1999

TM 9-2320-364-20-4	Unit Maintenance Manual, for Palletized Load System Model M1074/M1075 (NSN 2320-01-304-2277)(2320-01-304-2278) (This item is included on EM 0052)  1 August 1999

TM 9-2320-364-24P-1	Unit, Direct Support and General Support Maintenance Repair Parts and Special Tools List for Palletized Load System (PLS) M1074/M1075 (NSN 2320-01-304-2277)(2320-01-304-2278) (This item is included on EM 0052)  1 August 1999

TM 9-2320-364-24P-2	Unit, Direct Support and General Support Maintenance Repair Parts and Special Tools List for Palletized Load System (PLS) M1074/M1075 (NSN 2320-01-304-2277)(2320-01-304-2278) (This item is included on EM 0052)  1 August 1999

TM 9-2320-366-10-1	Operator's Instructions Manual for M1083 Series, 5-Ton, 6X6, Medium Tactical Vehicles (MTV) Volume 1 of 2 Trk, Car., MTV, M1083 w/Wn (NSN 2320-01-360-1895)(EIC:BT3) w/o Wn (2320-01-354-3386)(EIC:BR2) Trk, Car., MTV w/MATL HDLG EQPT (MHE)  15 September 1998

TM 9-2320-366-10-2	Operator's Instructions Manual for M1083 Series, 5-Ton, 6X6, Medium Tactical Vehicles (MTV) Volume 2 of 2 Trk, Car., MTV, M1083 w/Wn (NSN 2320-01-360-1895)(EIC:BT3) w/o Wn (2320-01-354-3386)(EIC:BR2) Trk, Car., MTV w/MATL HDLG EQPT (MHE)  15 September 1998

TM 9-2320-366-20-1	Maintenance Instructions Unit Maintenance for M1083 Series, 5-Ton, 6X6, Medium Tactical Vehicles (MTV) for Trk, Car., MTV, M1083 w/Wn (NSN 2320-01-360-1895)(EIC:BT3) w/o Wn (2320-01-354-3386)(EIC:BR2) Trk, Car., MTV, w/MATL HDLG EQPT (MHE),  15 September 1998

TM 9-2320-366-20-2	Maintenance Instructions Unit Maintenance for M1083 Series, 5-Ton, 6X6, Medium Tactical Vehicles (MTV) VOL NO. 2 of 5 Trk, Car., MTV, M1083 w/Wn (NSN 2320-01-360-1895)(EIC:BT3) w/o Wn (2320-01-354-3386)(EIC:BR2) Trk, Car., MTV, w/M  15 September 1998

TM 9-2320-366-20-3	Maintenance Instructions Unit Maintenance for M1083 Series, 5-Ton, 6X6, Medium Tactical Vehicles (MTV) VOL NO. 3 of 5 for Trk, Car., MTV, M1083 w/Wn (NSN 2320-01-360-1895)(EIC:BT3) w/o Wn (2320-01-354-3386)(EIC:BR2) Trk, Car., MTV, w/M  15 September 1998

TM 9-2320-366-20-4	Maintenance Instructions Unit Maintenance for M1083 Series, 5-Ton, 6X6, Medium Tactical Vehicles (MTV) VOL NO. 4 of 5 for Trk, Car., MTV, M1083 w/Wn (NSN 2320-01-360-1895)(EIC:BT3) w/o Wn (2320-01-354-3386)(EIC:BR2) Trk, Car., MTV, w/M  15 September 1998

TM 9-2320-366-20-5	Maintenance Instructions Unit Maintenance for M1083 Series, 5-Ton, 6X6, Medium Tactical Vehicles (MTV) VOL NO. 5 of 5 for Trk, Car., MTV, M1083 w/Wn (NSN 2320-01-360-1895)(EIC:BT3) w/o Wn (2320-01-354-3386)(EIC:BR2) Trk, Car., MTV, w/M  15 September 1998

TM 9-2320-366-24P-1	Unit, Direct Support and General Support Maintenance Repair Parts and Special Tools List for M1083 Series 5 Ton, 6X6 Medium Tactical Vehicle (MTV) Volume NO. 1 of 2,Model  TRK, CAR., M1083 W/WN (NSN 2320-01-360-1895) (EIC:BT3);  15 September 1998

TM 9-2320-386-10	Expended Service Program (ESP) Operator's Manual for ,2-1/2 Ton, 6X6, M44A3 Series Trucks (Diesel) Truck, Cargo; 2-1/2 Ton, 6X6, M35A3, (NSN 2320-01-383-2047) (EIC:BHK); (2320-01-383-3850)(EIC:BHL) M35A3C (2320-01-383-2050) (EIC:BHP);  26 January 1996

TM 9-2320-386-24	Expended Service Program (ESP) Unit, Direct Support and General Support Maintenance Manual for 2-1/2 Ton, 6X6, M44A3 Series Trucks (Diesel) Truck, Cargo; 2-1/2 Ton, 6X6, M35A3, (NSN 2320-01-383-2047) (EIC:BHK); (2320-01-383-3850)(EIC:BHL);  26 January 1996

TM 9-2320-386-24P	Expended Service Program (ESP) Unit, Direct Support and General Support Maintenance Repair Parts and Special Tools List  for 2-1/2 Ton, 6X6, M44A3 Series Trucks (Diesel) Truck, Cargo; Fixed Side, W/Winch, M35A3 (2320-01-383-2050)  26 January 1996

TM 9-2330-202-14&P	Operator's, Unit, Direct Support, and General Support Maintenance Manual (Including Repair Parts and Special Tools Lists) for Trailer, Cargo: 3/4 Ton, 2-Wheel M101A2 (NSN 2330-01-102-4697) M101A3 (2330-01-372-5641) Trailer, Chassis  12 May 1997

TM 9-2330-205-14&P	Operator's, Organizational, Direct Support, and General Support Maintenance (Including Repair Parts and Special Tools List) for Chassis, Trailer: Generator, 2-1/2-Ton, Two-Wheel, M200A1(NSN 2330-00-331-2307)(Reprinted w/Basic Incl C1)  11 September 1984

TM 9-2330-267-14&P	Operator's, Organizational, Direct Support, and General Support Maintenance Manual (Including Repair Parts and Special Tools List) for Trailer, Tank, Water, 400-Gallons, 1 1/2-Ton, 2-Wheel, M149 (NSN 2330-00-542-2039) M149A1  30 July 1991

TM 9-2330-381-14	Operator's, Unit, Direct Support and General Support Maintenance Manual  for Heavy Equipment Transporter Semitrailer, 70 Ton, M1000 (NSN 2330-01-303-8832) (EIC:CXU) [TM 09295A-14/1] (This Item is Included on EM 0049)  30 November 1994

TM 9-2330-384-14&P	Operator's, Unit, Direct Support and General Support Maintenance Manual Including Repair Parts and Special Tools Lists for Semitrailer Tank, Fuel, 7500 Gallon M1062 (NSN 2330-01-275-7475)  9 July 1990

TM 9-2350-238-10	Operator's Manual for Recovery Vehicle, Full Tracked: Light, Armored, M578 (NSN 2350-00-439-6242) (EIC: 3LA) (Reprinted W/Basic Incl C1-4) (This Item is Included on EM 0036)  27 April 1990

TM 9-2350-238-20-1	Unit Maintenance Manual for Hull and Related Components Recovery Vehicle, Full Tracked: Light, Armored, M578 (NSN 2350-00-439-6242) (EIC: 3LA)  (This Item is Included on EM 0036)  15 May 1994

TM 9-2350-238-20-2	Unit Maintenance Manual for Crane (CAB) Components Recovery Vehicle, Full Tracked: Light, Armored, M578 (NSN 2350-00-439-6242) (EIC: 3LA) (This Item is Included on EM 0036)  5 March 1992

TM 9-2350-256-10	Operator's Manual for Recovery Vehicle, Full Tracked, Medium, M88A1 (NSN 2350-00-122-6826) (Reprinted w/Basic Incl C1) (This item is included on EM 0036)  31 March 1998

TM 9-2350-256-20	Unit Maintenance Manual for Recovery Vehicle, Full Tracked, Medium, M88A1 (NSN 2350-00-122-6826) (This Item is Included on EM 0036)  15 July 1996

TM 9-2350-256-24P-1	Unit, Direct Support and General Support Maintenance Repair Parts and Special Tools List (Including DEPOT Maintenance Repair Parts and Special Tools) for Recovery Vehicle, Full Tracked; Medium M88A1(NSN 2350-00-122-6826)  29 May 1992

TM 9-2350-256-24P-2	Unit, Direct Support and General Support Maintenance Repair Parts and Special Tools List (Including DEPOT Maintenance Repair Parts and Special Tools) for Recovery Vehicle, Full Tracked; Medium, M88A1(NSN 2350-00-122-6826) Winch, Power  8 May 1992

TM 9-2350-261-10	Operator's Manual for Carrier, Personnel, Full-Tracked, Armored, M113A2 (NSN 2350-01-068-4077); Carrier, Command Post, Light: Tracked M577A2 (2350-01-068-4089) (Reprinted w/ Basic Incl 1-5) (This item included on EM 0040 and EM 0078  12 July 1990

TM 9-2350-261-20-1	Unit Maintenance Manual for Carrier, Personnel, Full-Tracked, Armored, M113A2 (NSN 2350-01-068-4077); Carrier, Command Post, Light: Tracked M577A2 (2350-01-068-4089) (Reprinted w/ Basic Incl 1-4)(This item included on EM 0040 and EM 0078)  11 July 1990

TM 9-2350-261-20-2	Unit Maintenance Manual for Carrier, Personnel, Full-Tracked, Armored, M113A2 (NSN 2350-01-068-4077); Carrier, Command Post, Light: Tracked M577A2 (2350-01-068-4089) (Reprinted w/ Basic Incl 1-4)(This item included on EM 0040 and EM 0078)  11 July 1990

TM 9-2350-261-20-3	Unit Maintenance Manual for Carrier, Personnel, Full-Tracked, Armored, M113A2, (NSN 2350-01-068-4077; Carrier Command Post, Light Tracked , M577A2, (  11 July 1990

TM 9-2350-261-24P	Unit Maintenance Direct Support and General Support Maintenance Repair Parts and Special Tools List for Carrier, Personnel, Full Tracked, Armored, M113A2  25 November 1995

TM 9-2350-277-20-1	Unit Maintenance for Carrier, Personnel, Full Tracked, Armored, M113A3  Carrier, Anti-Tank (TOW) Full, Tracked, Armored, M901A3  (This Item is Included on EM 0040)  25 July 1994

TM 9-2350-277-20-2	Unit Maintenance for Carrier, Personnel, Full Tracked, Armored, M113A3 (NSN 2350-01-219-7577) Carrier, Command Post, Light , Tracked, M577A3 (2350-01-369-6085) Carrier, Anti-Tank (TOW) Full, Tracked, Armored, M901A3 (2350-01-369-7253)  25 July 1994

TM 9-2350-277-20-3	Unit Maintenance for Carrier, Personnel, Full Tracked, Armored, M113A3 (NSN 2350-01-219-7577) Carrier, Command Post, Light , Tracked, M577A3 (2350-01-369-6085) Carrier, Anti-Tank (TOW) Full, Tracked, Armored, M901A3 (2350-01-369-7253)  24 July 1994

TM 9-2350-292-10	Operator's Manual for Recovery Vehicle, Heavy, Full-Tracked: M88A2 (NSN 2350-01-390-4683)(EIC:ACQ) [TM 0769B-10/1] (This Item is Included on EM 0160)(Reprinted W/Basic Incl C1)  11 July 1998

TM 9-2350-292-20-1	Unit Maintenance Manual for Recovery Vehicle, Heavy Full-Tracked, M882A (NSN 2350-01-390-4683)(EIC:ACQ) VOL 1of 2 [TM 07769B-20/2-1] (This Item is Included on EM 0160)  11 July 1998

TM 9-2350-292-20-2	Unit Maintenance Manual for Recovery Vehicle, Heavy Full-Tracked: M882A (NSN 2350-01-390-4683)(EIC:ACQ) VOL 2 of 2 [TM 07769B-20/2-1] (This Item is Included on EM 0160)  11 July 1998

TM 9-2350-292-24P	Unit, Direct Support and General Support  Maintenance Repair Parts and Special Tools Lists (Including DEPOT Maintenance Repair Parts and Special Tools) for Recovery Vehicle, Full Tracked: Heavy  M882A (NSN 2350-01-390-4683) (EIC:AQC)  1 June 2000

TM 9-243	Use And Care of Hand Tools And Measuring Tools [M6290-AJ-MAN-010; To 32-1-101; TM-10209-10/1] (Reprinted W/Basic InclC1-2) (This Item is Included on EM 0178)  12 December 1983

TM 9-8000	Principles of Automotive Vehicles (Reprinted W/Basic Incl C1)  25 October 1985

Training Circulars

TC 21-306	Tracked Combat Vehicle Driver Training  10 February 2000

TC 43-35	Recovery Training  3 October 1995

TC 43-4	Commander's and Shop Officer's Guide for Support Maintenance Management  8 May 1996

TC 9-237	Operator's Circular Welding Theory and Application (This item is included on EM 0028)  7 May 1993

Related Publications

Related publications are sources of additional information.  They are not required in order to understand this publication.

Army Regulations

AR 25-11	Record Communications and the Privacy Communications System (This Item is Included on EM 0001)  4 September 1990

AR 385-10	The Army Safety Program (This item is included on EM 0001)  23 May 1988

AR 385-40	Accident Reporting and Records (This Item is Included on EM 0001)  1 November 1994

AR 385-55	Prevention of Motor Vehicle Accidents (This item is Included on EM 0001)  12 March 1987

AR 750-1	Army Materiel Maintenance Policy and Retail Maintenance Operations (This Item is Included on EM 0001)  1 August 1994

AR 750-10	Maintenance of Supplies and Equipment (Included on EM 0001)  8 August 2000

AR 750-43	Army Test, Measurement and Diagnostic Equipment Program (This Item Is Included on EM 0001)  28 November 1997

Department of Army Pamphlets

DA PAM 738-750	Functional Users Manual for The Army Maintenance Management System (TAMMS) (This Item is Included on EM 0001)  1 August 1994

DA PAM 738-751	Functional Users Manual for the Army Maintenance Management System-Aviation (TAMMS-A) (This Item is Included on EM 0001)  15 March 1999

Field Manuals

FM 101-5-1	Operational Terms and Graphics (MCRP 5-2A)  30 September 1997

FM 21-60	Visual Signals

FM 24-18	Tactical Single-Channel Radio Communications Techniques  30 September 1987

FM 4-30.3 (FM 9-43-1)	Maintenance Operations and Procedures  1 September 2000

FM 5-125	Rigging Techniques, Procedures, and Applications (This Item is Included on EM 0028)  3 October 1995

FM 5-170	ENGINEER RECONNAISSANCE  5 May 1998

FM 9-43-2	Recovery and Battlefield Damage Assessment and Repair (FMFRP 4-34; TO 36-1-181)  3 October 1995

Lubrication Orders

LO 9-2320-280-12	Truck, Utility: Cargo/Troop Carrier, 1 1/4 Ton, 4 X 4, M998 Truck, Utility: Cargo/Troop Carrier, 1-1/4 Ton, 4 X 4, W/Winch, M1038; Truck Utility: TOW Carrier, Armored, 1-1/4 Ton, 4 X 4, M966 (This Item is Included on EM 0030)  19 January 1990

LO 9-2320-364-12	Palletized Load System (PLS) M1074/M1075 (NSN 2320-01-304-2277) (2320-01-304-2278) (This Item is Included on EM 0052)  1 October 1993

Other Product Types

DA PAM738-750	DA PAM738-750

Technical Manuals

TM 11-5820-401-10-1	Operator's Manual for Radio Sets AN/VRC-12 (NSN 5820-00-223-7412),  AN/VRC-43  (NSN 5820-00-223-7415), AN/VRC-44  (NSN 5820-00-223-7417), AN/VRC-45  (NSN 5820-00-223-7418), AN/VRC-45 (NSN 5820-00-223-7418), AN/VRC-46, -47, -48, and -49  15 January 1986

TM 11-5820-401-10-2	Operator's Manual for Radio Sets AN/VRC-12 (NSN 5820-00-223-7412),  AN/VRC-43  (NSN 5820-00-223-7415), AN/VRC-44  (NSN 5820-00-223-7417), AN/VRC-45  (NSN 5820-00-223-7418), AN/VRC-45 (NSN 5820-00-223-7418), AN/VRC-46, -47, -48, and -49  23 November 1982

TM 11-5820-401-10-4	Operator's Quick Checks for Receiver-Transmitter, RT-246 ( )/VRC (NSN 5820-00-892-0623) and RT-524 ( )/ (5820-00-892-0622) (This item Included on EM 0062 & EM 0079)  16 October 1980

TM 11-5820-498-12	Operator's And Organizational Maintenance Manual: Radio Sets, An/Vrc-53 (NSN 5820-00-223-7467), AN/VRC-64 (5820-00-223-7475), AN/GRC-125 (5820-00-223-7411) and AN/GRC-160 (5820-00-223-7473)  31 May 1967

TM 11-5830-340-12	Operator's and Unit  Organizational Maintenance Manual for Intercommunication Set AN/VIC-1 and Control, Intercommunication Set, C-10456/VRC (This Item is Included on EM 0063)  15 January 1986

TM 9-2320-272-10	Operator's Manual for Truck, 5-Ton,6X6, M939, M939A1, and M939A2 Series Truck (Diesel), Truck Cargo: 5-Ton, 6X6 Dropside, M923/A1/A2; M925/A1/A2; M927/A1/A2; M928/A1/A2; M929/A1/A2; (This Item is Included on EM 0039)  15 August 1996

TM 9-2320-272-24-1	Unit, Direct Support and General Support Maintenance Manual for Truck,5-Ton,6X6, M939, M939A1, M939A2 Series Trucks (Diesel) Truck, Cargo: 5-Ton, 6X6, Dropside, M923; M923A1; M923A (This Item is Included on EM 0039)  30 June 1998

TM 9-2320-272-24-2	Unit, Direct Support and General Support Maintenance Manual for Truck, 5-Ton, 6X6, M939, M939A1, M939A2 Series Trucks (Diesel) Truck, Cargo: 5-Ton, 6X6, Dropside, M923; M923A1; M923A (This Item is Included on EM 0039)  30 June 1998

TM 9-2320-272-24-3	Unit, Direct Support and General Support Maintenance Manual for Truck,5-Ton,6X6, M939, M939A1, M939A2 Series Trucks (Diesel) Truck, Cargo: 5-Ton, 6X6, Dropside, M923; M923A1; M923A (This Item is Included on EM 0039)  30 June 1998

TM 9-2320-272-24-4	Unit, Direct Support and General Support Maintenance Manual for Truck,5-Ton,6X6, M939, M939A1, M939A2 Series Trucks (Diesel) Truck, Cargo: 5-Ton, 6X6, Dropside, M923; M923A1; M923A (This Item is Included on EM 0039)  30 June 1998

TM 9-2320-280-10	Operator's Manual for Truck, Utility: Cargo/Troop Carrier, 1 1/4-Ton, 4X4, M998  (EIC:BBD); M998A1 (EIC:BBN); Truck, Utility; Cargo/Troop Carrier; 1-1/4 Ton, 4X4, W/Winch; M1038, 1038A1; M1097 (This Item is Included on EM 0030 & EM 0034)  31 January 1996

TM 9-2320-280-20-1	Unit Maintenance Volume 1 of 3 for Truck, Utility: Cargo/Troop Carrier, 1-1/4 Ton, 4 X 4, M998 (EIC:BBD); M998A1 (EIC: BBD); Truck, Utility: Cargo/Troop Carrier, 1-1/4Ton, 4 X 4, W/Winch, M1038 (This Item is Included on EM 0030)  31 January 1996

TM 9-2320-280-20-2	Unit Maintenance Volume 2 of 3 for Truck, Utility: Cargo/Troop Carrier, 1-1/4 Ton, 4 X 4, M998; M998A1; Truck, Utility: Cargo/Troop Carrier, 1-1/4Ton, 4 X 4, W/Winch, M1038 (This Item is Included on EM 0030 & EM 0034)  31 January 1996

TM 9-2320-280-20-3	Unit Maintenance manual for Truck, Utility: Cargo/Troop Carrier, 1-1/4 Ton, 4 X 4, M998 (EIC:BBD); M998A1(EIC: BBD); Truck, Utility: Cargo/Troop Carrier, 1-1/4Ton, 4 X 4, W/Winch, M1038 (This Item is Included on EM 0030)  31 January 1996

TM 9-2320-364-20-4	Unit Maintenance Manual, for Palletized Load System Model M1074/M1075 (NSN 2320-01-304-2277)(2320-01-304-2278) (This item is included on EM 0052)  1 August 1999

TM 9-2320-364-24P-1	Unit, Direct Support and General Support Maintenance Repair Parts and Special Tools List for Palletized Load System (PLS) M1074/M1075 (NSN 2320-01-304-2277)(2320-01-304-2278) (This item is included on EM 0052)  1 August 1999

TM 9-2320-364-24P-2	Unit, Direct Support and General Support Maintenance Repair Parts and Special Tools List for Palletized Load System (PLS) M1074/M1075 (NSN 2320-01-304-2277)(2320-01-304-2278) (This item is included on EM 0052)  1 August 1999

TM 9-2320-386-24	Expended Service Program (ESP) Unit, Direct Support and General Support Maintenance Manual for 2-1/2 Ton, 6X6, M44A3 Series Trucks (Diesel) Truck, Cargo; 2-1/2 Ton, 6X6, M35A3, (NSN 2320-01-383-2047) (EIC:BHK); (2320-01-383-3850)(EIC:BHL);  26 January 1996

TM 9-2320-386-24P	Expended Service Program (ESP) Unit, Direct Support and General Support Maintenance Repair Parts and Special Tools List  for 2-1/2 Ton, 6X6, M44A3 Series Trucks (Diesel) Truck, Cargo; Fixed Side, W/Winch, M35A3 (2320-01-383-2050)  26 January 1996

TM 9-243	Use And Care of Hand Tools And Measuring Tools [M6290-AJ-MAN-010; To 32-1-101; TM-10209-10/1] (Reprinted W/Basic InclC1-2) (This Item is Included on EM 0178)  12 December 1983

TM 9-6140-200-14	Operator's, Unit, Direct Support and General Support Maintenance Manual for Lead-Acid Storage Batteries; 4HN, 24 Volt  M11188/2-24V; 4HN, 24 Volt (WET) M11188/2-24V; 2HN, 12Volt (DRY) (This Item is Included on M0178)  11 September 1998

TM 9-8000	Principles of Automotive Vehicles (Reprinted W/Basic Incl C1)  25 October 1985

Training Circulars

TC 43-35	Recovery Training  3 October 1995

THIS PAGE INTENTIONALLY LEFT BLANK

Order of the Secretary of the Army:

ERIC K. SHINSEKI

General, United States Army

Chief of Staff

Official:

# Administrative Assistant to the

Secretary of the Army

0124101

DISTRIBUTION:

Active Army, US Army Reserve, and National Guard: To be distributed In accordance with initial distribution number 114459, requirements for STP9-63B14-SM-TG.