STP 9-63G12-SM-TG

# SOLDIER'S MANUAL and TRAINER'S GUIDE

# FUEL AND ELECTRICAL SYSTEMS REPAIRER

# Skill Levels 1 and 2

MOS 63G

DISTRIBUTION RESTRICTION: Approved for public release; distribution is unlimited

DESTRUCTION NOTICE: Destroy by any method that will prevent disclosure of contents or

reconstruction of the document.

HEADQUARTERS, DEPARTMENT OF THE ARMY

# This page was intentionally left blank.

SOLDIER TRAINING	HEADQUARTERS

PUBLICATION	DEPARTMENT OF THE ARMY

No. 9-63G12-SM-TG	Washington, DC, 16 Jun 2001

# SOLDIER'S MANUAL and TRAINER'S GUIDE

# MOS 63G

# FUEL AND ELECTRICAL SYSTEMS REPAIRER

# Skill Levels 1 and 2

TABLE OF CONTENTS

# PAGE

Table of Contents	i

PREFACE	iii

Chapter 1.  Introduction	1-1

Chapter 2.  Training Guide	2-1

2-1.  General	2-1

2-2.  Subject Area Codes	2-3

2-3.  Duty Position Training Requirements	2-4

2-4.  Critical Tasks List	2-5

Chapter 3.  MOS/Skill Level Tasks	3-1

Skill Level 1

Subject Area 1: ALTERNATORS TASKS

091-63G-2071  Repair Alternators/Generators	3-1

Subject Area 2: REPAIR PERSONNEL HEATERS TASKS

091-63G-2073  Repair Personnel Heaters	3-2

Subject Area 3: CORRECT MALFUNCTION IN STARTING SYSTEM TASKS

091-63G-2072  Repair Starters	3-3

Subject Area 4: WIRING HARNESSES TASKS

091-63G-2074  Repair Wiring Harness	3-4

Subject Area 5: REPAIR BATTERIES TASKS

091-63G-2064  Repair Battery	3-5

091-63G-2067  Store Batteries	3-6

Subject Area 6: TEST MEASUREMENT AND DIAGNOSTIC EQUIPMENT TASKS

091-63G-2075  Operate 500-Amp Test Stand	3-7

APPENDIX A 	A-1

APPENDIX B 	B-1

Glossary	Glossary-1

Supporting References	References-1

DISTRIBUTION RESTRICTION: Approved for public release; distribution is unlimited.

DESTRUCTION NOTICE: Destroy by any method that will prevent disclosure of contents or reconstruction of the document.

Supersedes STP 9-63G12-SM-TG Dated 30 October 1989.

PREFACE

This soldier training publication (STP) is intended for soldiers holding MOS 63G, Skill Levels 1 and 2, their supervisors, trainers, and commanders.  It contains an MOS Training Plan providing information needed to plan, conduct, and evaluate unit training, one of the most important jobs of military leaders.  It includes standardized training objectives in the form of task summaries that can be used to train and evaluate soldiers on critical tasks supporting unit missions during wartime.

Soldiers holding MOS 63G should have access to this publication.  Trainers and first-line supervisors should actively plan for soldiers’ access, making it available in work areas, unit learning centers, and unit libraries.  However, it is not intended for an individual copy to be provided to each MOS holder.  The STP is obtainable on- line from the Reimer Digital Library (RDL) .

# Tasks in this manual apply to both Active and Reserve Component soldiers.

The proponent of this publication is HQ TRADOC.  Submit comments and recommendations on DA Form 2028 (Recommended Changes to Publications and Blank Forms) directly to: Department of the Army, Training Directorate, Ordnance Training Division, ATTN: ATCL-AO, 401 First Street, Suite 227, Fort Lee, VA 23801-1511.

Unless this publication states otherwise, masculine nouns and pronouns do not refer exclusively to men.

1CHAPTER 1

# Introduction

1-1.  General. This soldier training publication (STP) identifies individual MOS training requirements for soldiers holding MOS 63G.  Commanders, trainers, and soldiers should use it to plan, conduct, and evaluate individual training in units.  The STP is the primary MOS reference for supporting self-development, evaluating MOS proficiency, and training of 63G soldiers.  Commanders employ two primary methods to evaluate soldiers' proficiency:

	Commander's evaluation.  Commander’s evaluations are local tests or assessments of soldiers' performance of MOS-specific and common tasks critical to the unit mission.  They may be conducted year-round.

	Common task test (CTT).  CTTs are hands-on tests used to evaluate proficiency on common tasks.  Alternate written tests are provided if equipment is not available for hands-on testing.

This publication is the soldier's primary reference to prepare for a commander's evaluation of MOS-specific tasks.  It contains task summaries for all critical tasks specific to the MOS and skill level (SL).  Commanders and trainers will use this soldier's manual/trainer's guide (SM/TG) to plan and conduct training and commander's evaluations.

Chapter 2, Trainer’s Guide, contains information needed to plan training requirements for this MOS.  The trainer's guide:

	Identifies subject areas in which soldiers must be trained.

	Identifies critical tasks for each subject area.

	Specifies where soldiers are initially trained on each task.

	Recommends how often each task should be trained to sustain proficiency.

	Recommends a strategy for cross-training soldiers.

	Recommends a strategy for training soldiers to perform higher-level tasks.

Use this STP along with STP 21-1-SMCT (Soldier’s Manual of Common Tasks, Skill Level 1), STP 21-24-SMCT (Soldier’s Manual of Common Tasks, Skill Levels 2-4), Army training and evaluation programs (ARTEPs), FM 25-4 (How to Conduct Training Exercises), FM 25-5 (Training for Mobilization and War), FM 25-100 (Training the Force), and FM 25-101 (Battle-Focused Training) to establish effective training plans and programs that integrate soldier, leader, and collective tasks.

1-2.  Task Summaries.  Task summaries outline wartime performance requirements for each critical task in the STP.  They provide both soldier and trainer with the information necessary to prepare, conduct, and evaluate critical task training.  As a minimum, task summaries include information soldiers must know and skills they must perform to standard for each task.  Following is the task summary format:

	Task number.  The task number is a 10-digit number that identifies the task and skill level.  Include the task number and title in any correspondence relating to the task.

	Task title.  The task title identifies the action to be performed.

	Conditions.  The task conditions statement describes the field or garrison conditions under which the task will be performed and identifies the equipment, tools, references, job aids, and supporting personnel that the soldier needs to perform the task in wartime.

	Standards.  The task standards describe how well and to what level of proficiency the soldier must perform the task under wartime conditions.  Standards are typically expressed in terms of accuracy, completeness, duration, sequence, speed, and tolerance.

	Performance measures.  This section identifies specific actions that the soldier must accomplish to complete the task successfully.  Performance measures appear in a GO/NO-GO rating format for easy evaluation.  Some tasks may also include detailed training information in a Training Information Outline and an Evaluation Preparation Section.  The Evaluation Preparation Section indicates necessary modifications to task performance in order to train and evaluate a task that can not be trained to the wartime standard under wartime conditions.  It may also include special training and evaluation preparation instructions to accommodate these modifications and any instructions that should be given to the soldier before evaluation.

	References.  This section identifies references that provide more detailed explanations of task performance requirements than are given in the task summary.

	Warnings.  Warnings alert users to the possibility of immediate personal injury or equipment damage.

	Notes.  Notes provide additional supportive explanations or tips relating to task performance.

1-3.  Soldier’s Responsibilities.  Each soldier is responsible for performing individual tasks identified by the first-line supervisor based on the unit’s mission-essential task list (METL).  Soldiers must perform tasks to the standards included in the task summary.  If soldiers have questions about tasks or which tasks in this manual they must perform, they are responsible for asking their first-line supervisor for clarification.  First-line supervisors know how to perform each task or can direct soldiers to appropriate training materials, including current field manuals, technical manuals, and Army regulations.  Soldiers are responsible for using these materials to maintain performance.  They are also responsible for maintaining performance of all common tasks listed in the SMCTs at their current skill level and below.

Periodically, soldiers should ask their supervisor or another soldier to check their performance to ensure that they can perform the tasks.

1-4.  NCO Self-Development and the STP.  Self-development is a key component of leader development.  Leaders follow planned, progressive, sequential self-development programs developed by the individual NCO and his or her first-line supervisor to enhance and sustain military competencies.  Self-development consists of individual study, research, professional reading, practice, and self-assessment.  The self-development concept requires NCOs, as Army professionals, to take responsibility for remaining current in all phases of their MOS.  The STP is the NCO’s primary source for maintaining MOS proficiency.

Another important resource for self-development is the Army Correspondence Course Program (ACCP).  Refer to DA Pamphlet 351-20 (Army Correspondence Course Program Catalog) for detailed eligibility requirements and enrollment information.  The catalog is available at local education centers or on- line through the Army Institute for Professional Development (AIPD) web site, http.//www.atsc.army.mil/accp/aipd.htm. The web site offers on-line enrollment.

1-5.  Commander’s Responsibilities.  Commanders must ensure that their unit training plans prepare the unit for war by enabling soldiers to develop and sustain proficiency in their MOS and skill level tasks.  Commanders should design unit training programs to provide individual training for all soldiers assigned to the unit and to evaluate soldier proficiency routinely as part of the commander’s evaluation program.  The unit training program should also integrate individual training with crew drills and other collective training.  The MOS training plan provides information on which to base integration, cross-train, train-up, and sustainment training programs.  Commanders should use the MOS training plan when developing unit training plans.

1-6.  Trainer’s Responsibilities.  Training is the business of all unit leaders.  First-line leaders are the principal trainers in the unit because they directly supervise soldiers and lead crews, squads, sections, and teams.

Trainers can use the MOS training plan to determine the critical tasks each soldier is responsible for.  They should tell each soldier which tasks he or she must be able to perform.  Trainers should evaluate task performance to determine which tasks each soldier can or cannot perform to standard.  Soldiers who cannot perform a task to standard need further training.  Developing effective training is explained in detail in FM 25-100 and FM 25-101.

Every task summary in this STP includes performance measures, which trainers may use year-round to determine if soldiers can perform critical tasks to the specified standards.  The performance measures identify what the trainer needs to observe to score a soldier’s performance.  A blank space is provided for the trainer to check either the GO or NO-GO column for each performance measure.  Some tasks require the trainer to watch the soldier perform them (evaluate the process).  Other tasks call for the trainer to focus on the results of the soldier’s performance (evaluate the product).  Comments should not be written on the task summary.

Trainers can monitor the progress of their soldiers by recording task go/no-go results.  Trainers may use DA Form 5164-R (Hands-On Evaluation) to record the performance measures a soldier passed or failed.  The form, which may be locally reproduced, applies to all tasks in this STP.  Trainers may have DA Form 5164-R overprinted with information unique to their training requirements before reproducing it.  See Appendix A of this STP for a sample DA Form 5164-R with instructions.

Trainers may use DA Form 5165-R (Field Expedient Squad Book) to record hands-on go/no-go results for a group of soldiers (for example, a crew, section, or squad) having the same MOS and skill level.  This form supports conduct of commander’s evaluations, and can be used to record training results gathered in the field during slack time for all MOSs and skill levels.  Use of this form is optional.  See Appendix B for a sample DA Form 5165-R with instructions.  Trainers should work with each soldier until tasks can be performed to specific task summary standards.

1-7.  Training Support.  References have been identified for each task to assist in planning and conducting training.  A consolidated list of references identified by type, publication number, and title and a comprehensive glossary of acronyms, abbreviations, and definitions are included in this STP.

2CHAPTER 2

# Training Guide

| 63G CAREER FIELD DUTY POSITIONS |
| --- |
| Duty Position | Subject Area | Cross Train | Train-up/Merger |
| Skill Level 1 |
| Fuel & Electric Systems Repairer | 1 - 6 | NA | 63G20/Fuel & Electric Systems Repairer |
| Skill Level 2 |
| Fuel & Electric Systems Repairer | 1 - 6 | NA | 63H30/Senior Automotive Repairer 63H30/Senior Fuel & Electric Systems Repairer 63H30/Recovery Supervisor 63H30/Automotive Repair Supervisor 63H30/Technical Inspector 63H30/Maintenance Analyst 63H30/Mechanical Maintenance Supervisor 63H30/MHE Maintenance NCO 63H30/Operations NCO |

2-1.  General.  The MOS Training Plan (MTP) identifies the essential components of a unit training plan for individual training.  Units have different training needs and requirements based on differences in environment, location, equipment, dispersion, and similar factors.  Therefore, the MTP should be used as a guide for conducting unit training and not a rigid standard.  The MTP consists of two parts.  Each part is designed to assist the commander in preparing a unit training plan which satisfies integration, cross training, train up, and sustainment training requirements for soldiers in this MOS.

Part One of the MTP shows the relationship of an MOS skill level between duty position and critical tasks.  These critical tasks are grouped by task commonality into subject areas.

Section I lists subject area numbers and titles used throughout the MTP.  These subject areas are used to define the training requirements for each duty position within an MOS.

Section II identifies the total training requirement for each duty position within an MOS and provides a recommendation for cross training and train-up/merger training.

(	Duty Position column.  This column lists the duty positions of the MOS, by skill level, which have different training requirements.

(	Subject Area column.  This column lists, by numerical key (see Section I), the subject areas a soldier must be proficient in to perform in that duty position.

(	Cross Train column.  This column lists the recommended duty position for which soldiers should be cross trained.

(	Train-up/Merger column.  This column lists the corresponding duty position for the next higher skill level or MOSC the soldier will merge into on promotion.

Part Two lists, by general subject areas, the critical tasks to be trained in an MOS and the type of training required (resident, integration, or sustainment).

(	Subject Area column.  This column lists the subject area number and title in the same order as Section I, Part One of the MTP.

(	Task Number column.  This column lists the task numbers for all tasks included in the subject area.

(	Title column.  This column lists the task title for each task in the subject area.

(	Training Location column.  This column identifies the training location where the task is first trained to soldier training publications standards.  If the task is first trained to standard in the unit, the word “Unit” will be in this column.  If the task is first trained to standard in the training base, it will identify, by brevity code (ANCOC, BNCOC, etc.), the resident course where the task was taught.  Figure 2-1 contains a list of training locations and their corresponding brevity codes.

AIT	Advanced Individual Training

# Figure 2-1.  Training Locations

(	Sustainment Training Frequency column.  This column indicates the recommended frequency at which the tasks should be trained to ensure soldiers maintain task proficiency.  Figure 2-2 identifies the frequency codes used in this column.

BA	-	Biannually

AN	-	Annually

SA	-	Semiannually

QT	-	Quarterly

MO	-	Monthly

BW	-	Bi-weekly

WK	-	Weekly

# Figure 2-2.  Sustainment Training Frequency Codes

(	Sustainment Training Skill Level column.  This column lists the skill levels of the MOS for which soldiers must receive sustainment training to ensure they maintain proficiency to soldier’s manual standards.

2-2.  Subject Area Codes.

# Skill Level 1

1	ALTERNATORS TASKS

2	REPAIR PERSONNEL HEATERS TASKS

3	CORRECT MALFUNCTION IN STARTING SYSTEM TASKS

4	WIRING HARNESSES TASKS

5	REPAIR BATTERIES TASKS

6	TEST MEASUREMENT AND DIAGNOSTIC EQUIPMENT TASKS

2-3.  Duty Position Training Requirements.

# Note: See chapter 2, section 2-1

2-4.  Critical Tasks List.

# MOS TRAINING PLAN

63G12

| CRITICAL TASKS |
| --- |
| Subject Area | Task Number | Title | Training Location | Sust Tng Freq | Sust Tng SL |
| Skill Level 1 |
| 1. ALTERNATORS TASKS | 091-63G-2071 | Repair Alternators/Generators | AIT | AN | 1/2 |
| 2. REPAIR PERSONNEL HEATERS TASKS | 091-63G-2073 | Repair Personnel Heaters | AIT | AN | 1/2 |
| 3. CORRECT MALFUNCTION IN STARTING SYSTEM TASKS | 091-63G-2072 | Repair Starters | AIT | AN | 1/2 |
| 4. WIRING HARNESSES TASKS | 091-63G-2074 | Repair Wiring Harness | AIT | AN | 1/2 |
| 5. REPAIR BATTERIES TASKS | 091-63G-2064 | Repair Battery | AIT | AN | 1/2 |
|  | 091-63G-2067 | Store Batteries | AIT | AN | 1/2 |
| 6. TEST MEASUREMENT AND DIAGNOSTIC EQUIPMENT TASKS | 091-63G-2075 | Operate 500-Amp Test Stand | AIT | AN | 1/2 |

This page was intentionally left blank.

3CHAPTER 3

# MOS/Skill Level Tasks

Skill Level 1

Subject Area 1: ALTERNATORS TASKS

Repair Alternators/Generators

091-63G-2071

Conditions: In a field or garrison environment, given an alternator/generator, repair parts, applicable technical publications, 500-Amp test stand, multimeter, fuel and electrical tool kit, additional tools and equipment as indicated in the TMs, and supervision/assistance.

Standards: Repair the alternator/generator IAW applicable technical publications and successfully complete a final operational test.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Select and use applicable technical manuals. | —— | —— |
| 2. Select and use applicable tools and TMDE. | —— | —— |
| 3. Practice shop safety and maintenance discipline. | —— | —— |
| 4. Inspect the alternator/generator for internal/external damage. | —— | —— |
| 5. Disassemble the alternator/generator. | —— | —— |
| 6. Replace defective components (as necessary). | —— | —— |
| 7. Reassemble the alternator/generator. | —— | —— |
| 8. Perform a final operational test to test current and voltage output and verify alternator/generator has been repaired to specifications. | —— | —— |
| 9. Complete TAMMS forms as required. | —— | —— |
| 10. Maintain tools and equipment. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO-GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| ST 9-4910-663-12 | TM 9-8000 |
| TM 9-2320-280-34 |  |
| TM 9-2320-365-34-1 |  |
| TM 9-2920-224-34&P |  |
| TM 9-2920-225-34 |  |
| TM 9-4910-663-12 |  |

Subject Area 2: REPAIR PERSONNEL HEATERS TASKS

Repair Personnel Heaters

091-63G-2073

Conditions: In a field or garrison environment, given a personnel heater, repair parts, applicable technical publications, fuel and electrical tool kit, heater test stand, multimeter, additional tools and equipment as indicated in the TMs, and supervision/assistance.

Standards: Correct the malfunction of the personnel heater IAW applicable technical publications and successfully complete a final operational test.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Select and use applicable technical publications. | —— | —— |
| 2. Select and use applicable tools and TMDE. | —— | —— |
| 3. Practice shop safety and maintenance discipline. | —— | —— |
| 4. Inspect for secure electrical connections. | —— | —— |
| 5. Inspect for restricted exhaust system. | —— | —— |
| 6. Test start heater system. | —— | —— |
| 7. Test operate heater system. | —— | —— |
| 8. Replace defective components (as necessary). | —— | —— |
| 9. Perform a final operational test to verify personnel heater is repaired to specifications. | —— | —— |
| 10. Complete TAMMS forms as required. | —— | —— |
| 11. Maintain tools and equipment. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed.  Score the soldier NO-GO if any step is failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2540-205-24&P |  |
| TM 9-4910-755-13&P |  |

Subject Area 3: CORRECT MALFUNCTION IN STARTING SYSTEM TASKS

Repair Starters

091-63G-2072

Conditions: In a field or garrison environment, given a starter assembly, repair parts, applicable technical publications, fuel and electrical tool kit, general mechanic's tool kit, armature tester, test light, test stand, multimeter, additional tools and equipment as indicated in the TMs, and supervision/assistance.

Standards: Repair the starter IAW applicable technical publications and successfully complete a final operational test.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Select and use applicable technical publications. | —— | —— |
| 2. Select and use applicable tools and TMDE. | —— | —— |
| 3. Practice shop safety and maintenance discipline. | —— | —— |
| 4. Inspect starter for external damage. | —— | —— |
| 5. Disassemble the starter. | —— | —— |
| 6. Replace defective components (as necessary). | —— | —— |
| 7. Reassemble the starter. | —— | —— |
| 8. Perform a final operational test to verify starter repaired to specifications. | —— | —— |
| 9. Complete TAMMS forms as required. | —— | —— |
| 10. Maintain tools and equipment. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed. Score the soldier NO-GO if any step is failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| ST 9-4910-663-12 | TM 9-8000 |
| TM 9-2320-280-34 |  |
| TM 9-2320-365-34-1 |  |
| TM 9-4910-663-12 |  |

Subject Area 4: WIRING HARNESSES TASKS

Repair Wiring Harness

091-63G-2074

Conditions: In a field or garrison environment, given a wiring harness, applicable technical publications, fuel and electrical tool kit, multimeter, harness and connector repair kit, additional tools and equipment as indicated in the TMs, and supervision/assistance.

Standards: Correct the malfunction of the wiring harness IAW applicable technical publications and successfully complete a final operational test.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Select and use applicable technical publications. | —— | —— |
| 2. Select and use applicable tools and TMDE. | —— | —— |
| 3. Practice shop safety and maintenance discipline. | —— | —— |
| 4. Inspect/perform continuity check. | —— | —— |
| 5. Inspect for connector corrosion. | —— | —— |
| 6. Repair wiring harness as required. | —— | —— |
| 7. Perform a final operational test to verify wiring harness is repaired to specifications. | —— | —— |
| 8. Complete TAMMS forms as required. | —— | —— |
| 9. Maintain tools and equipment. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed. Score the soldier NO-GO if any step is failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| MIL STD 1460(MU) | TM 9-8000 |
| TB SIG 222 |  |
| TM 9-2350-264-34-1-2 |  |

Subject Area 5: REPAIR BATTERIES TASKS

Repair Battery

091-63G-2064

Conditions: In a field or garrison environment, given a battery, general mechanic's tool kit, fuel and electrical tool kit, electrolyte, battery post molds, rubber gloves, apron, face shield, applicable technical publications, repair materials, necessary tools and equipment as indicated in the TMs, and supervision/assistance.

Standards: Repair the battery IAW applicable technical publications and successfully complete a final operational test.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Select and use applicable technical publications. | —— | —— |
| 2. Select and use applicable tools and TMDE. | —— | —— |
| 3. Practice shop safety and maintenance discipline. | —— | —— |
| 4. Inspect battery. | —— | —— |
| 5. Perform applicable tests: | —— | —— |
| a. Cell probe test. |  |  |
| b. Specific gravity test. |  |  |
| c. Load test. |  |  |
| 6. Repair battery. | —— | —— |
| 7. Charge battery. | —— | —— |
| 8. Perform final operational test to verify battery repaired to specifications. | —— | —— |
| 9. Complete TAMMS forms as required. | —— | —— |
| 10. Maintain tools and equipment. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed. Score the soldier NO-GO if any step is failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| MIL STD 1460(MU) | TM 9-8000 |
| TM 9-6140-200-14 |  |

Store Batteries

091-63G-2067

Conditions: In a field or garrison environment, given rubber gloves, apron, face shield, applicable technical publications, designated battery storage area, supply of batteries, necessary tools and equipment as indicated in the TMs, and supervision/assistance.

# Standards: Store batteries IAW applicable technical publications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Select and use applicable technical publications. | —— | —— |
| 2. Select and use correct tools and TMDE. | —— | —— |
| 3. Practice shop safety and maintenance discipline. | —— | —— |
| 4. Store batteries correctly. | —— | —— |
| 5. Complete TAMMS forms as required. | —— | —— |
| 6. Maintain tools and equipment. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed. Score the soldier NO-GO if any step is failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-6140-200-14 |  |

Subject Area 6: TEST MEASUREMENT AND DIAGNOSTIC EQUIPMENT TASKS

Operate 500-Amp Test Stand

091-63G-2075

Conditions: In a field or garrison environment, given a 500-amp test stand, applicable technical publications, alternator/generator, regulator and starter, and supervision/assistance.

# Standards: Operate the 500-amp test stand IAW applicable technical publications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Select and use applicable technical publications. | —— | —— |
| 2. Practice shop safety and maintenance discipline. | —— | —— |
| 3. Set controls and switches to the base setting: | —— | —— |
| a. DC load ammeter range switch (x 10). |  |  |
| b. DC field ammeter range switch (x 6). |  |  |
| 4. Millivoltmeter | —— | —— |
| a. Range switch (x 10). |  |  |
| b. Millivoltmeter (press to read switch) off. |  |  |
| 5. DC voltmeter | —— | —— |
| a. Range switch (x 5). |  |  |
| b. Select switch RECT/GEN. |  |  |
| 6. Tachometer | —— | —— |
| a. Select switch DIRECT DRIVE. |  |  |
| b. Pulley calibration knob COUNTERCLOCKWISE. |  |  |
| 7. AC ammeter | —— | —— |
| a. Range switch (x 5). |  |  |
| b. Select switch T1. |  |  |
| 8. AC voltmeter | —— | —— |
| a. Range switch (x 2). |  |  |
| b. Select switch T1- T2. |  |  |
| 9. External field exciter switch (AC system) off. | —— | —— |
| 10. Generator field INT GND. | —— | —— |
| 11. Polarity reversing switch NEG GND. | —— | —— |
| 12. Field circuit off. | —— | —— |
| 13. Field control switch (0-5) off. | —— | —— |
| 14. Field current increase (0-5) COUNTERCLOCKWISE. | —— | —— |
| 15. Field circuit (rheostat 0-30) COUNTERCLOCKWISE. | —— | —— |
| 16. Battery circuit selector off. | —— | —— |
| 17. Circuit breakers DOWN. | —— | —— |
| 18. Regulator check; fixed resistance method off. | —— | —— |
| 19. DC variable volts off. | —— | —— |
| 20. Load selection (all switches) off. | —— | —— |
| 21. Master load disconnect off. | —— | —— |
| 22. Variable load increase off. | —— | —— |
| 23. Voltage adjusting increase (VAR) COUNTERCLOCKWISE. | —— | —— |
| 24. Field shorting (spring-loaded) off. | —— | —— |
| 25. Starter rheostat approximately three turns from fully clockwise. | —— | —— |
| 26. Starter test off. | —— | —— |
| 27. Equalizer coil test off. | —— | —— |
| 28. Auxiliary test off. | —— | —— |
| 29. Ignition switch off. | —— | —— |
| 30. Bus bars off. | —— | —— |
| a. B+ and G+ in place. |  |  |
| b. B- and G- in place. |  |  |
| 31. DC variable power supply COUNTERCLOCKWISE. | —— | —— |
| 32. Charger time control off. | —— | —— |
| 33. Battery charger variable load COUNTERCLOCKWISE. | —— | —— |
| 34. D-sensing switch off. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps are passed. Score the soldier NO-GO if any step is failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| ST 9-4910-663-12 |  |
| TM 9-4910-663-12 |  |

90APPENDIX- A

# HANDS-ON EVALUATION (DA FORM 5164-R)

INSTRUCTIONS

(Excerpted from STP 21-24-SMCT, Appendix C)

DA Form 5164-R (Hands-On Evaluation) allows the trainer to keep a record of the performance measures a soldier passes or fails on each task.

# Before evaluation:

1.  Obtain a blank copy of DA Form 5164-R, which you may locally reproduce on 8 ½“ x 11“ paper.

2.  Enter the task title and 10-digit number from the STP task summary.

3.  In Column a, enter the performance measure numbers from the task summary.

4.  In Column b, enter the performance measure corresponding to the number in Column a (you may

abbreviate this information if necessary).

5.  Locally reproduce the partially completed form when evaluating more than one soldier on the task or

when evaluating the same soldier more than once.

# During evaluation:

1.  Enter the date just before evaluating the soldier's task performance.

2.  Enter the evaluator's name, the soldier's name, and the unit.

3.  For each performance measure in Column b, enter a check in Column c (PASS) or Column d (FAIL),

as appropriate.

4.  Compare the number of performance measures the soldier passes (and, if applicable, which ones)

against the task standards specified in the task summary.  If the standards are met or exceeded,

check the GO block under STATUS; otherwise, check the NO-GO block.

| HANDS-ON EVALUATION For use of this form, see AR 350-57; the proponent agency is ODCSOPS | DATE |
| --- | --- |
| TASK TITLE | TASK NUMBER |
| ITEM a | PERFORMANCE STEP TITLE b | SCORE (Check One) |
|  |  | PASS c | FAIL d |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
| EVALUATOR'S NAME | UNIT |
| SOLDIER'S NAME | STATUS GO NO GO |

DA FORM 5164-R, SEP 85                        EDITION OF DEC 82 IS OBSOLETE                                                            USAPPC V2.00

91APPENDIX- B

# FIELD EXPEDIENT SQUAD BOOK (DA FORM 5165-R)

INSTRUCTIONS

(Excerpted from STP 21-24-SMCT, Appendix C)

DA Form 5165-R (Field Expedient Squad Book) allows the trainer to keep a record of task proficiency for a group of soldiers.

# Before evaluation:

1.  Obtain a blank copy of DA Form 5165-R, which you may locally reproduce on 8 ½“ x 11“ paper.

2.  Locally reproduce the partially completed form if you are evaluating more than nine soldiers.

# During evaluation:

1.  Enter the names of the soldiers you are evaluating, one name per column, at the top of the form.

2.  Under STATUS, record (in pencil) the date in the GO block if the soldier demonstrated task

proficiency to soldier's manual standards.  Keep this information current by always recording the most

recent date on which the soldier demonstrated task proficiency.  Record the date in the NO-GO block

if the soldier failed to demonstrate task proficiency to soldier's manual standards.  Soldiers who failed

to perform the task should be retrained and reevaluated until they can meet the standards. When the

standards are met, enter the date in the appropriate GO block and erase the previous entry from the

NO-GO block.

# After evaluation:

# 1.  Read down each column (GO/NO-GO) to determine the training status of an individual. This will give

you a quick indication of which tasks a soldier needs training on.

# 2.  Read across the rows for each task to determine the training status of all soldiers.  You can readily

see which tasks to focus training on.

# 3.  Line through the STATUS column of any soldier who leaves the unit.

# This page was intentionally left blank.

88GLOSSARY

# Section I

# Abbreviations

AC	Active Component

ACCP	Army Correspondence Course Program

AIPD	Army Institute for Professional Development

AIT	Advanced Individual Training

AN	Annually

ANCOC	Advanced Noncommissioned Officers Course

AR	Army Regulation

ARTEP	Army training and evaluation program

BA	Biannually

BNCOC	Basic Noncommissioned Officers Course

BW	Biweekly

CTT	Common Task Test

DA	Department of the Army

DC	Direct Current

HQ	Headquarters

IAW	In Accordance With

METL	Mission Essential Task List

MO	Monthly

MOS	Military Occupational Specialty

MOSC	military occupational specialty code

MTP	MOS Training Plan

NCO	Noncommissioned Officer

ODCSLOG	Office of the Deputy Chief of Staff for Logistics

PAM	Pamphlet

QT	Quarterly

RC	Reserve Component

SA	Semiannual

SL	Skill Level

SM/TG	Soldier's Manual/trainer's Guide

SMCT	Soldier's Manual of Common Tasks

STP	Soldier Training Publication

TAMMS	The Army Maintenance Management System

TM	Technical Manual

TMDE	Test Measurement and Diagnostic Equipment

TRADOC	Training and Doctrine Command

USAPPC	United States Army Publications and Printing Command

VAR	Variable

WK	Weekly

# Section II

# Terms

# Ampere

The fundamental unit of measure for electric current. One ampere is defined as the current that flows when a potential of one volt is impressed on a resistance of one Ohm.

99REFERENCES

# Required Publications

Required publications are sources that users must read in order to understand or to comply with this publication.

# Other Product Types

MIL STD 1460(MU)	Soldering of Electrical Connectors and Printed Wiring Assembly Procedures.

ST 9-4910-663-12	ST 9-4910-663-12

# Technical Bulletins

TB SIG 222	Solder and Soldering (This Item is Included on EM 0178)  5 March 1985

# Technical Manuals

TM 9-2320-280-10	Operator's Manual for Truck, Utility: Cargo/Troop Carrier, 1 1/4-Ton, 4X4, M998  (EIC:BBD); M998A1 (EIC:BBN); Truck, Utility; Cargo/Troop Carrier; 1-1/4 Ton, 4X4, W/Winch; M1038, 1038A1; M1097 (This Item is Included on EM 0030 & EM 0034)  31 January 1996

TM 9-2320-280-20-1	Unit Maintenance Volume 1 of 3 for Truck, Utility: Cargo/Troop Carrier, 1-1/4 Ton, 4 X 4, M998 (EIC:BBD); M998A1 (EIC: BBD); Truck, Utility: Cargo/Troop Carrier, 1-1/4Ton, 4 X 4, W/Winch, M1038 (This Item is Included on EM 0030)  31 January 1996

TM 9-2320-280-20-2	Unit Maintenance Volume 2 of 3 for Truck, Utility: Cargo/Troop Carrier, 1-1/4 Ton, 4 X 4, M998; M998A1; Truck, Utility: Cargo/Troop Carrier, 1-1/4Ton, 4 X 4, W/Winch, M1038 (This Item is Included on EM 0030 & EM 0034)  31January 1996

TM 9-2320-280-20-3	Unit Maintenance manual for Truck, Utility: Cargo/Troop Carrier, 1-1/4 Ton, 4 X 4, M998 (EIC:BBD); M998A1(EIC: BBD); Truck, Utility: Cargo/Troop Carrier, 1-1/4Ton, 4 X 4, W/Winch, M1038 (This Item is Included on EM 0030)  31 January 1996

TM 9-2320-280-24P-1	Unit, Direct Support/General Support Maintenance, Repair Parts and Special Tools List, Volume 1 of 2, for Truck Utility, Cargo/Troop Carrier, 1 1/4 Ton, 4X4, M998 (This Item is Included on EM 0030)  31 January 1996

TM 9-2320-280-24P-2	Unit, Direct Support/General Support Maintenance, Repair Parts and Special Tools List, Volume 2 of 2, for Truck, Utility, Cargo/Troop Carrier, 1 1/4 Ton, 4X4, M998 (This Item is Included on EM 0030)  31 January 1996

TM 9-2320-280-34	Direct and General Support Maintenance Manual for Truck, Cargo and Utility, 1 1/4-Ton, HMMWV (This Item is Included on EM 0030)  31 January 1996

TM 9-2320-365-10	Operator's Instructions Manual for M1078 Series, 2 1/2-Ton, 4X4 Light Medium Tactical Vehicles (LMTV) Trk, Car., LMTV, M1078 w/Wn (NSN 2320-01-360-1898) (EIC:BHH) w/o Wn (2320-01-354-3385) (EIC:BHD) Trk, Van, LMTV, M1078 w/Wn  17 June 1998

TM 9-2320-365-20-1	Maintenance Instructions for Unit Maintenance M1078 Series, 2 1/2-Ton, 4X4 Light Medium Tactical Vehicle (LMTV) Trk, Car, LMTV, M1078 w/Wn 2320-01-360-1898) (EIC:BHH) w/o Wn (2320-01-354-3385) (EIC:BHD) Trk, Van, LMTV, M1079 w/Wn  17 June 1998

TM 9-2320-365-20-2	Maintenance Instructions for Unit Maintenance M1078 Series, 2 1/2-Ton, 4X4 Light Medium Tactical Vehicle (LMTV) Vol No. 2 of 5 for Trk, Car., LMTV, M1078 w/Wn (NSN 2320-01-360-1898)(EIC:BHH) w/o Wn (2320-01-354-3385) (EIC:BHD)Trk, Van, LMTV  17 June 1998

TM 9-2320-365-20-3	Maintenance Instructions for Unit Maintenance M1078 Series, 2 1/2-Ton, 4X4 Light Medium Tactical Vehicle (LMTV) Vol No. 3 of 5 for Trk, Car., LMTV, M1078 w/Wn (NSN 2320-01-360-1898)(EIC:BHH) w/o Wn (2320-01-354-3385)  (EIC:BHD)Trk, Van, LMTV  17 June 1998

TM 9-2320-365-20-4	Technical Manual Maintenance Instructions for Unit Maintenance M1078 Series, 2 1/2-Ton , 4X4 Light Medium Tactical Vehicle(LMTV) Vol No. 4 of 5 for Trk, Car, LMTV, M1078 w/Wn (NSN 2320-01-360-1898) (EIC:BHH) w/o Wn (2320-01-354-3385)  17 June 1998

TM 9-2320-365-20-5	Technical Manual Maintenance Instructions for Unit Maintenance M1078 Series, 2 1/2-Ton , 4X4 Light Medium Tactical Vehicle(LMTV) VOL NO. 5 of 5 for Trk, Car., LMTV, M1078 w/Wn (NSN 2320-01-360-1898)(EIC:BHH) w/o Wn (2320-01-354-3385)  17 June 1998

TM 9-2320-365-24P	Unit, Direct Support and General Support Maintenance Repair Parts and Special Tools List for M1078 Series 2-1/2 Ton, 4X4 Light Medium Tactical Vehicle (LMTV) TRK, CAR, LMTV, M1078 W/WN (NSN 2320-01-360-1898) (EIC:BHH) W/O WN  17 June 1998

TM 9-2320-365-34-1	Maintenance Instructions Direct Support Maintenance For M1078 Series, 2 1/2-Ton, 4x4, Light Medium Tactical Vehicles (LMTV) Trk, Car., LMTV, M1078 W/Wn (NSN 2320-01-360-1898) (EIC: BHH) W/O Wn (2320-01-354-3385) (EIC: BHD) Trk, Van   17 June 1998

TM 9-2350-264-24-1	Unit, Direct Support and General Support Maintenance Manual Systems Schematics Tank, Combat, Full-Tracked: 120-MM Gun, M1A1, General Abrams Hull (This Item is Included on EM 0069)  12 May 1999

TM 9-2350-264-34-1-2	Direct Support and General Support Maintenance Manual VOL 2 of 2 for Tank, Combat, Full-Tracked: 120-MM, M1A1 (NSN 2350-01-087-1095) General Abrams Hull (TM 08953A-34/5-2) (Reprinted W/Basic Incl C1-8) (This Item is Included on EM 0069)  28 October 1987

TM 9-243	Use And Care of Hand Tools And Measuring Tools [M6290-AJ-MAN-010; To 32-1-101; TM-10209-10/1] (Reprinted W/Basic InclC1-2) (This Item is Included on EM 0178)  12 December 1983

TM 9-2540-205-24&P	Organizational, Direct Support and General Support Maintenance Manual (Including Repair Parts and Special Tools) for Heaters, Vehicular Compartment: Stewart-Warner 10560M (NSN 2540-01-071-0651), 10560M24B1(2540-01-169-5159), 10560C24  10 April 1992

TM 9-2920-224-34&P	Direct Support and General Support Maintenance Manual Including Repair Parts and Special Tools List for Generator Assembly, Engine (300 AMP) 8717421 (NSN 2920-00-795-6627); 1088971 (2920-00-830-6660),  and 11642898 (2920-00-169-5715)

TM 9-2920-225-34	Maintenance Direct and General Support Level Generator Assembly (Prestolite Model AMA-5102UT) (Leece-Neville Models 3002AC, 3002AD, and 3002AE) (NSN 2920-00-909-2483), (Models 5504AA, 5504AB) (2920-00-475-1446), (Model 2148AC),  20 February 1981

TM 9-4910-571-12&P	Operator's and Organizational Maintenance Manual Including Repair Parts and Special Tools List for Simplified Test Equipment for Internal Combustion Engines (Reprinted W/Basic Incl C1-2)(This Item is Included on EM 0068)  25 March 1988

TM 9-4910-663-12	Operator's and Organizational Maintenance Manual for Test Stand, Automotive Generator, Alternator Starter and Associated Equipment, Model GASR-500, Part No. 7458-2  Part No. 7458-4  (This Item is Included on EM 0072)  10 June 1981

TM 9-4910-755-13&P	Operator, Unit and Direct Support Maintenance Manual Including Repair Parts and Special Tools for Heater Test Stand, Model VHTS-89102 (NSN 4910-01-318-4508)(This Item is Included on EM 0072)  9 December 1991

TM 9-6140-200-14	Operator's, Unit, Direct Support and General Support Maintenance Manual for Lead-Acid Storage Batteries; 4HN, 24 Volt  M11188/2-24V; 4HN, 24 Volt (WET) M11188/2-24V; 2HN, 12Volt (DRY) (This Item is Included on M0178)  11 September 1998

# Related Publications

Related publications are sources of additional information.  They are not required in order to understand this publication.

TM 9-8000	Principles of Automotive Vehicles (Reprinted W/Basic Incl C1)  25 October 1985

# STP 9-63G12-SM-TG

16 JUNE 2001

By Order of the Secretary of the Army:

# ERIC K. SHINSEKI

General, United States Army

Chief of Staff

Official:

# Administrative Assistant to the

Secretary of the Army

0124006

DISTRIBUTION:

Active Army, US Army Reserve, and Army National Guard: To be distributed in accordance with initial distribution number 114459, requirements for STP 9-63G12-SM-TG.