# SOLDIER'S MANUAL and TRAINER'S GUIDE

# MOS 63Y

# TRACK VEHICLE MECHANIC

# Skill Levels 1 and 2

## This publication is available on the

General Dennis J. Reimer Training

And Doctrine Digital Library at

www.adtdl.army.mil

SOLDIER TRAINING	HEADQUARTERSPUBLICATION

No. 9-63Y12-SM-TG	DEPARTMENT OF THE ARMY

Washington, DC, 23 June 2001

# SOLDIER'S MANUAL and TRAINER'S GUIDE

# MOS 63Y

# TRACK VEHICLE MECHANIC

# Skill Levels 1 and 2

TABLE OF CONTENTS

# PAGE

Table of Contents	i

PREFACE	iii

Chapter 1.  Introduction	1-1

Chapter 2.  Training Guide	2-1

2-1.  General	2-1

2-2.  Subject Area Codes	2-3

2-3.  Duty Position Training Requirements	2-4

2-4.  Critical Tasks List	2-5

Chapter 3.  MOS/Skill Level Tasks	3-1

DISTRIBUTION RESTRICTION: Approved for public release; distribution is unlimited.

Supersedes STP 9-63Y12-SM-TG, dated 3 October 1990.

Skill Level 1

Subject Area 1: TechnicalTasks

091-63Y-2001  Maintain Track Vehicle Diesel Power Plant/Pack	3-1

091-63Y-2002  Maintain Track Vehicle Fuel Systems	3-2

091-63Y-2003  Maintain Track Vehicle Liquid Cooling Systems	3-3

091-63Y-2004  Maintain Track Vehicle Starting Systems	3-4

091-63Y-2005  Maintain Track Vehicle Charging Systems	3-5

091-63Y-2006  Maintain Track Vehicle  Hull Electrical Systems	3-6

091-63Y-2007  Maintain Track Vehicle Suspension Systems	3-7

091-63Y-2008  Maintain Track Vehicle Steering/brake Systems	3-8

091-63Y-2009  Maintain Track Vehicle Hydraulic Systems	3-9

091-63Y-2010  Maintain Fire Extinguisher/Suppression Systems	3-10

091-63Y-2011   Maintain Auxiliary Power Unit (APU)                                                                 	3-11

091-H8C-2001  Locate a Recovery Site	3-12

091-H8C-2002  Determine Recovery Methods	3-13

091-H8C-2003  Operate Tactical Communications Equipment	3-14

091-H8C-2004  Operate Metal Cutting Equipment	3-15

091-H8T-2001  Maintain Recovery Vehicle Weapons	3-16

091-H8T-2002  Perform Preventive Maintenance Checks and Services on Tracked Recovery Vehicle	3-17

091-H8T-2003  Use Basic Issue Items Related to Tracked Recovery Vehicle	3-18

091-H8T-2004  Drive Tracked Recovery Vehicle	3-19

091-H8T-2005  Operate Auxiliary Power Unit	3-20

091-H8T-2006  Operate the Boom and Hoist Winch on a Tracked Recovery Vehicle	3-21

091-H8T-2007  Operate the Spade on a Tracked Recovery Vehicle	3-22

091-H8T-2008  Operate the Winch on a Tracked Recovery Vehicle	3-23

091-H8T-2009  Recover a Mired Tracked Vehicle	3-24

091-H8T-2010  Recover an Overturned Tracked Vehicle	3-25

091-H8T-2011  Lift and Tow a Disabled Vehicle	3-26

091-H8T-2012  Cross Country Tow of a Tracked Vehicle	3-27

091-H8T-2013  Perform Field Expedient Recovery on a Tracked Vehicle	3-28

# APPENDIX A………………………………………………………………………………………………………A-1

APPENDIX B………………………………………………………………………………………………………B-1

Glossary………………………………………………………………………………………………….Glossary-1

Supporting References	….References-1

# PREFACE

This soldier training publication (STP) is intended for soldiers holding MOS 63Y, Skill Levels 1 and 2, their supervisors, trainers, and commanders.  It contains an MOS Training Plan providing information needed to plan, conduct, and evaluate unit training, one of the most important jobs of military leaders.  It includes standardized training objectives in the form of task summaries that can be used to train and evaluate soldiers on critical tasks supporting unit missions during wartime.

Soldiers holding MOS 63Y should have access to this publication.  Trainers and first line supervisors should actively plan for soldiers’ access, making it available in work areas, unit learning centers, and unit libraries.  However, it is not intended for an individual copy to be provided to each MOS holder.  The STP is obtainable on line from the Reimer Digital Library (RDL) at www.adtdl.army.mil.

# Tasks in this manual apply to both Active and Reserve Component soldiers.

The proponent of this publication is CASCOM.  Submit comments and recommendations on DA Form 2028 (Recommended Changes to Publications and Blank Forms) directly to: Department of the Army, Training Directorate, Ordnance Training Division, ATTN: ATCL-AO, 401 First Street, Suite 227, Fort Lee, VA 23801-1511.

Unless this publication states otherwise, masculine nouns and pronouns do not refer exclusively to men.

This page intentionally left blank

1CHAPTER 1

# Introduction

1-1.  General. This soldier training publication (STP) identifies individual MOS training requirements for soldiers holding MOS 63Y.  Commanders, trainers, and soldiers should use it to plan, conduct, and evaluate individual training in units.  The STP is the primary MOS reference for supporting self-development, evaluating MOS proficiency, and training of 63Y soldiers. Commanders employ two primary methods to evaluate soldiers' proficiency:

	Commander's evaluation.  Commander’s evaluations are local tests or assessments of soldiers' performance of MOS-specific and common tasks critical to the unit mission. They may be conducted year-round.

	Common task test (CTT).  CTTs are hands-on tests used to evaluate proficiency on common tasks.  Alternate written tests are provided if equipment is not available for hands-on testing.

This publication is the soldier's primary reference to prepare for a commander's evaluation of MOS-specific tasks.  It contains task  summaries for all critical tasks specific to the MOS and skill level (SL).  Commanders and trainers will use this soldier's manual/trainer's guide (SM/TG) to plan and conduct training and commander's evaluations.

Chapter 2, Training Guide, contains information needed to plan training requirements for this MOS.  The trainer's guide

	Identifies subject areas in which soldiers must be trained.

	Identifies critical tasks for each subject area.

	Specifies where soldiers are initially trained on each task.

	Recommends how often each task should be trained to sustain proficiency.

	Recommends a strategy for cross-training soldiers.

	Recommends a strategy for training soldiers to perform higher-level tasks.

Use this STP along with STP 21-1-SMCT (Soldier’s Manual of Common Tasks, Skill Level 1), STP 21-24-SMCT (Soldier’s Manual of Common Tasks, Skill Levels 2-4), Army training and evaluation programs (ARTEPs), FM 25-4 (How to Conduct Training Exercises), FM 25-5 (Training for Mobilization and War), FM 25-100 (Training the Force), and FM 25-101 (Battle-Focused Training) to establish effective training plans and programs that integrate soldier, leader, and collective tasks.

1-2.  Task Summaries.  Task summaries outline wartime performance requirements for each critical task in the STP.  They provide both soldier and trainer with the information necessary to prepare, conduct, and evaluate critical task training.  As a minimum, task summaries include information soldiers must know and skills they must perform to standard for each task.  Following is the task summary format:

	Task number.  The task number is a 10-digit number that identifies the task, MOS and skill level.  Include the task number and title in any correspondence relating to the task.

	Task title.  The task title identifies the action to be performed.

	Conditions.  The task conditions statement describes the field or garrison conditions under which the task will be performed and identifies the equipment, tools, references, job aids, and supporting personnel that the soldier needs to perform the task in wartime.

	Standards.  The task standards describe how well and to what level of proficiency the soldier must perform the task under wartime conditions.  Standards are typically expressed in terms of accuracy, completeness, duration, sequence, speed, and tolerance.

	Performance measures.  This section identifies specific actions that the soldier must accomplish to complete the task successfully.  Performance measures appear in a GO/NO GO rating format for easy evaluation.  Some tasks may also include detailed training information in a Training Information Outline and an Evaluation Preparation Section.  The Evaluation Preparation Section indicates necessary modifications to task performance in order to train and evaluate a task that can not be trained to the wartime standard under wartime conditions.  It may also include special training and evaluation preparation instructions to accommodate these modifications and any instructions that should be given to the soldier before evaluation.

	References.  This section identifies references that provide more detailed explanations of task performance requirements than are given in the task summary.

	Warnings.  Warnings alert users to the possibility of immediate personal injury or equipment damage.

	Notes.  Notes provide additional supportive explanations or tips relating to task

performance.

1-3.  Soldier’s Responsibilities.  Each soldier is responsible for performing individual tasks identified by the first-line supervisor based on the unit’s mission-essential task list (METL).  Soldiers must perform tasks to the standards included in the task summary.  If soldiers have questions about tasks or which tasks in this manual they must perform, they are responsible for asking their first-line supervisor for clarification.  First-line supervisors know how to perform each task or can direct soldiers to appropriate training materials, including current field manuals, technical manuals, and Army regulations.  Soldiers are responsible for using these materials to maintain performance.  They are also responsible for maintaining performance of all common tasks listed in the SMCTs at their current skill level and below.

Periodically, soldiers should ask their supervisor or another solder to check their performance to ensure that they can perform the tasks.

1-4.  NCO Self-Development and the STP.  Self-development is a key component of leader development.  Leaders follow planned, progressive, sequential self-development programs developed by the individual NCO and his or her first-line supervisor to enhance and sustain military competencies.  Self-development consists of individual study, research, professional reading, practice, and self-assessment.  The self-development concept requires NCOs, as Army professionals, to take responsibility for remaining current in all phases of their MOS.  The STP is the NCO’s primary source for maintaining MOS proficiency.

1-5.  Commander’s Responsibilities.  Commanders must ensure that their unit training plans prepare the unit for war by enabling soldiers to develop and sustain proficiency in their MOS and skill level tasks.  Commanders should design unit training programs to provide individual training for all soldiers assigned to the unit and to evaluate soldier proficiency routinely as part of the commander’s evaluation program.  The unit training program should also integrate individual training with crew drills and other collective training.  The MOS training plan provides information on which to base integration, cross-train, and sustainment training programs.  Commanders should use the MOS training plan when developing unit training plans.

1-6.  Trainer’s Responsibilities.  Training is the business of all unit leaders.  First-line leaders are the principal trainers in the unit because they directly supervise soldiers and lead crews, squads, sections, and teams.

Trainers can use the MOS training plan to determine the critical tasks each soldier is responsible for.  They should tell each soldier which tasks he or she must be able to perform.  Trainers should evaluate task performance to determine which tasks each soldier can or cannot perform to standard.  Soldiers who cannot perform a task to standard need further training.  Developing effective training is explained in detail in FM 25-100 and FM 25-101.

Every task summary in this STP includes performance measures, which trainers may use year-round to determine if soldiers can perform critical tasks to the specified standards.  The performance measures identify what the trainer needs to observe to score a soldier’s performance.  A blank space is provided for the trainer to check either the GO or NO GO column for each performance measure.  Some tasks require the trainer to watch the soldier perform them (evaluate the process).  Other tasks call for the trainer to focus on the results of the soldier’s performance (evaluate the product).  Comments should not be written on the task summary.

Trainers can monitor the progress of their soldiers by recording task go/no-go results.  Trainers may use DA Form 5164-R (Hands-on Evaluation) to record the performance measures a soldier passed or failed.  The form, which may be locally reproduced, applies to all tasks in this STP.  Trainers may have DA Form 5164-R overprinted with information unique to their training requirements before reproducing it.  See Appendix A of this STP for a sample DA Form 5164-R with instructions.

	Trainers may use DA Form 5165-R (Field Expedient Squad Book) to record hands-on go/no-go results for a group of soldiers (for example, a crew, section, or squad) having the same MOS and skill level.  This form supports conduct of commander’s evaluations, and can be used to record training results gathered in the field during slack time for all MOSs and skill levels.  Use of this form is optional.  See Appendix B for a sample DA Form 5165-R with instructions.  Trainers should work with each soldier until tasks can be performed to specific task summary standards.

1-7.  Training Support.  References have been identified for each task to assist in planning and conducting training.  A consolidated list of references identified by type, publication number, and title and a comprehensive glossary of acronyms, abbreviations, and definitions are included in this STP.

# CAREER PROGRESSION CHART

HEAVY WHEEL		LIGHT WHEEL	            TRACK

VEHICLE		     VEHICLE	                       VEHICLE

MECHANIC		  MECHANIC		        MECHANIC

This page intentionally left blank

This page intentionally left blank

2CHAPTER 2

# Training Guide

# MOS Training Plan

2-1.  General.  The MOS Training Plan (MTP) identifies the essential components of a unit training plan for individual training.  Units have different training needs and requirements based on differences in environment, location, equipment, dispersion, and similar factors.  Therefore, the MTP should be used as a guide for conducting unit training and not a rigid standard.  The MTP consists of two parts.  Each part is designed to assist the commander in preparing a unit training plan which satisfies integration, cross training, and sustainment training requirements for soldiers in this MOS.

Part One of the MTP shows the relationship of an MOS skill level between duty position and critical tasks.  These critical tasks are grouped by task commonality into subject areas.

Section I lists subject area numbers and titles used throughout the MTP.  These subject areas are used to define the training requirements for each duty position within an MOS.

Section II identifies the total training requirement for each duty position within an MOS and provides a recommendation for cross training and train-up/merger training.

(	Duty Position column.  This column lists the duty positions of the MOS, by skill level, which have different training requirements.

(	Subject Area column.  This column lists, by numerical key (see Section I), the subject areas a soldier must be proficient in to perform in that duty position.

(	Cross Train column.  This column lists the recommended duty position for which soldiers should be cross trained.

(	Train-up/Merger column.  This column lists the corresponding duty position for the next higher skill level or MOSC the soldier will merge into on promotion.

Part Two lists, by general subject areas, the critical tasks to be trained in an MOS and the type of training required (resident, integration, or sustainment).

(	Subject Area column.  This column lists the subject area number and title in the same order as Section I, Part One of the MTP.

(	Task Number column.  This column lists the task numbers for all tasks included in the subject area.

(	Title column.  This column lists the task title for each task in the subject area.

(	Training Location column.  This column identifies the training location where the task is first trained to soldier training publications standards.  If the task is first trained to standard in the unit, the word “Unit” will be in this column.  If the task is first trained to standard in the training base, it will identify, by brevity code (ANCOC, BNCOC, etc.), the resident course where the task was taught.  Figure 2-1 contains a list of training locations and their corresponding brevity codes.

ASI/SD	Additional Skill Identifier/Special Duty

AIT	Advanced Individual Training

UNIT	Trained in the Unit

ANCOC	Advanced NCO Course

# Figure 2-1.  Training Locations

(	Sustainment Training Frequency column.  This column indicates the recommended frequency at which the tasks should be trained to ensure soldiers maintain task proficiency.  Figure 2-2 identifies the frequency codes used in this column.

BA	-	Biannually

AN	-	Annually

SA	-	Semiannually

QT	-	Quarterly

MO	-	Monthly

BW	-	Bi-weekly

WK	-	Weekly

# Figure 2-2.  Sustainment Training Frequency Codes

(	Sustainment Training Skill Level column.  This column lists the skill levels of the MOS for which soldiers must receive sustainment training to ensure they maintain proficiency to soldier’s manual standards.

2-2.  Subject Area Codes.

# Skill Level 1

1	Technical Tasks

2	Recovery (ASI)

2-3.  Duty Position Training Requirements.

# See Chapter 2, Training Guide

2-4.  Critical Tasks List.

# MOS TRAINING PLAN

63Y12

| CRITICAL TASKS |
| --- |
| Subject Area | Task Number | Title | Training Location | Sust Tng Freq | Sust Tng SL |
| Skill Level 1 |
| 1. Technical Tasks | 091-63Y-2001 | Maintain Track Vehicle Diesel Power Plant/Pack | AIT | SA | 1-2 |
|  | 091-63Y-2002 | Maintain Track Vehicle Fuel Systems | AIT | SA | 1-2 |
|  | 091-63Y-2003 | Maintain Track Vehicle Liquid Cooling Systems | AIT | SA | 1-2 |
|  | 091-63Y-2004 | Maintain Track Vehicle Starting Systems | AIT | SA | 1-2 |
|  | 091-63Y-2005 | Maintain Track Vehicle Charging Systems | AIT | SA | 1-2 |
|  | 091-63Y-2006 | Maintain Track Vehicle Hull Electrical Systems | AIT | SA | 1-2 |
|  | 091-63Y-2007 | Maintain Track Vehicle Suspension Systems | AIT | SA | 1-2 |
|  | 091-63Y-2008 | Maintain Track Vehicle Steering/Brake Systems | AIT | SA | 1-2 |
|  | 091-63Y-2009 | Maintain Track Vehicle Hydraulic Systems | AIT | SA | 1-2 |
|  | 091-63Y-2010 | Maintain Fire Extinguisher/Suppression Systems | UNIT | SA | 1-2 |
|  | 091-63Y-2011 | Maintain Auxiliary Power Unit (APU) | AIT | SA | 1-2 |
| 2. Recovery (ASI) | 091-H8C-2001 | Locate a Recovery Site | ASI/SD | SA | 1-2 |
|  | 091-H8C-2002 | Determine Recovery Methods | ASI/SD | SA | 1-2 |
|  | 091-H8C-2003 | Operate Tactical Communications Equipment | ASI/SD | SA | 1-2 |
|  | 091-H8C-2004 | Operate Metal Cutting Equipment | ASI/SD | SA | 1-2 |
|  | 091-H8T-2001 | Maintain Recovery Vehicle Weapons | ASI/SD | SA |  |
|  | 091-H8T-2002 | Perform Preventive Maintenance Checks and Services on Tracked Recovery Vehicle | ASI/SD | SA | 1-2 |
|  | 091-H8T-2003 | Use Basic Issue Items Related to Tracked Recovery Vehicle | ASI/SD | SA | 1-2 |
|  | 091-H8T-2004 | Drive Tracked Recovery Vehicle | ASI/SD | SA | 1-2 |
|  | 091-H8T-2005 | Operate Auxiliary Power Unit | ASI/SD | SA | 1-2 |
|  | 091-H8T-2006 | Operate the Boom and Hoist Winch on a Tracked Recovery Vehicle | ASI/SD | SA | 1-2 |
|  | 091-H8T-2007 | Operate the Spade on a Tracked Recovery Vehicle | AIT | SA | 1-2 |
|  | 091-H8T-2008 | Operate the Winch on a Tracked Recovery Vehicle | ASI/SD | SA | 1-2 |
|  | 091-H8T-2009 | Recover a Mired Tracked Vehicle | ASI/SD | SA | 1-2 |
|  | 091-H8T-2010 | Recover an Overturned Tracked Vehicle | ASI/SD | SA | 1-2 |
|  | 091-H8T-2011 | Lift and Tow a Disabled Vehicle | ASI/SD | SA | 1-2 |
|  | 091-H8T-2012 | Cross Country Tow of a Tracked Vehicle | ASI/SD | SA | 1-2 |
|  | 091-H8T-2013 | Perform Field Expedient Recovery on a Tracked Vehicle | ASI/SD | SA | 1-2 |

3CHAPTER 3

# MOS/Skill Level Tasks

Skill Level 1

Subject Area 1: Technical Tasks

Maintain Track Vehicle Diesel Power Plant/Pack

091-63Y-2001

Conditions: In a garrison or field environment, with assistance and under supervision, given equipment required, M88 series vehicle, general mechanic's tool kit, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts if needed.

Note. If representative equipment is not available, use applicable equipment and associated references.

Standards: Maintained track vehicle diesel power plant/pack IAW the applicable technical publications procedures, and specifications. When this task was completed, the vehicle was fully mission-capable, or maintenance actions required to be performed by other than 63Y personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Described how systems/components operate and function. | —— | —— |
| 6. Inspected power plant (pack), engine transmission assembly on a track vehicle. | —— | —— |
| 7. Tested power plants pack, engine transmission assembly on a track vehicle. | —— | —— |
| 8. Replaced power plant pack, engine transmission assembly on a track vehicle. | —— | —— |
| 9. Adjusted systems/components. | —— | —— |
| 10. Performed required PMCS. | —— | —— |
| 11. Verified fault had been corrected. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
|  | AR 385-10 |
| AR 750-43 | AR 750-1 |
| TM 9-1450-500-10 | DA PAM 738-750 |
| TM 9-1450-500-20 |  |
| TM 9-1450-500-24P |  |
| TM 9-1450-646-10 |  |
| TM 9-1450-646-20-1 |  |
| TM 9-2350-256-10 |  |
| TM 9-2350-256-24P-1 |  |

Maintain Track Vehicle Fuel Systems

091-63Y-2002

Conditions: In a garrison or field environment, with assistance and under supervision, given equipment required, M88 series vehicle, general mechanic's tool kit, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts if needed.

Note. If representative equipment is not available, use applicable equipment and associated references.

Standards: Maintained track vehicle fuel systems IAW the applicable technical manual procedures and specifications. When this task was completed, the vehicle was fully mission-capable or maintenance actions required to be performed by other than 63Y personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Described how systems/components operate and function. | —— | —— |
| 6. Inspected track vehicle fuel system and components. | —— | —— |
| 7. Performed diagnostics on track vehicle fuel system and components. | —— | —— |
| 8. Repaired track vehicle fuel system and components. | —— | —— |
| 9. Replaced track vehicle fuel system components, as required. | —— | —— |
| 10. Performed required PMCS. | —— | —— |
| 11. Verified fault had been corrected. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
|  | AR 385-10 |
| TM 9-1450-500-10 | AR 750-1 |
| TM 9-1450-500-20 | AR 750-43 |
| TM 9-1450-500-24P |  |
| TM 9-1450-646-10 |  |
| TM 9-1450-646-20-1 |  |
| TM 9-2350-256-10 |  |
| TM 9-2350-256-20 |  |
| TM 9-2350-256-24P-1 |  |

Maintain Track Vehicle Liquid Cooling Systems

091-63Y-2003

Conditions: In a garrison or field environment, with assistance and under supervision, given equipment required, M88 series vehicle, general mechanic's tool kit, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts if needed.

Note. If representative equipment is not available, use applicable equipment and associated references.

Standards: Maintained track vehicle liquid cooling system IAW the applicable technical publications procedures and specifications. When this task was completed the vehicle was fully mission-capable or maintenance actions required to be performed by other than 63Y personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Described how system/components operate and function. | —— | —— |
| 6. Inspected cooling system and components on a track vehicle. | —— | —— |
| 7. Performed diagnostics on cooling system and components on a track vehicle. | —— | —— |
| 8. Replaced cooling system components on a track vehicle. | —— | —— |
| 9. Performed required PMCS. | —— | —— |
| 10. Verified fault had been corrected. | —— | —— |
| 11. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
|  | AR 385-10 |
| TM 9-1450-500-10 | AR 750-1 |
| TM 9-1450-500-20 | AR 750-43 |
| TM 9-1450-500-24P | DA PAM 738-750 |
| TM 9-1450-646-10 |  |
| TM 9-1450-646-20-1 |  |
| TM 9-2350-256-10 |  |
| TM 9-2350-256-20 |  |
| TM 9-2350-256-24P-1 |  |

Maintain Track Vehicle Starting Systems

091-63Y-2004

Conditions: In a garrison or field environment, with assistance and under supervision, given equipment required, M88 series vehicle, general mechanic's tool kit, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts if needed.

Note. If representative equipment is not available, use applicable equipment and associated references.

Standards:  Maintained track vehicle  starting systems  IAW the applicable technical publications procedures and specifications. When this task was completed, the vehicle was fully mission-capable or the maintenance actions required to be performed by other than 63Y personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Described how systems/components operate and function. | —— | —— |
| 6. Performed diagnostic procedures on the starting system/components on a track vehicle. | —— | —— |
| 7. Replaced starting system components fuel on a track vehicle. | —— | —— |
| 8. Repaired defective starting system components on a track vehicle. | —— | —— |
| 9. Adjusted starting system components on a track vehicle. | —— | —— |
| 10. Performed required PMCS. | —— | —— |
| 11. Verified fault had been corrected. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
|  | AR 385-10 |
| TM 9-1450-500-10 | AR 750-1 |
| TM 9-1450-500-20 | AR 750-43 |
| TM 9-1450-500-24P | DA PAM 738-750 |
| TM 9-1450-646-10 | TM 9-2350-256-20 |
| TM 9-1450-646-20-1 | TM 9-2350-256-24P-1 |
| TM 9-2350-256-10 |  |

Maintain Track Vehicle Charging Systems

091-63Y-2005

Conditions: In a garrison or field environment, with assistance and under supervision, given equipment required, M88 series vehicle, general mechanic's tool kit, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts if needed.


Note. If representative equipment is not available, use applicable equipment and associated references.

Standards: Maintained track vehicle charging systems IAW the applicable technical publications procedures and specifications. When this task was completed, the vehicle was fully mission-capable or maintenance actions required to be performed by other than 63Y personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Described how system/components operate and function. | —— | —— |
| 6. Inspected charging system on track vehicle. | —— | —— |
| 7. Performed diagnostic procedures on charging systems/components on a track vehicle. | —— | —— |
| 8. Repaired charging system components on track vehicle. | —— | —— |
| 9. Replaced charging system components on a track vehicle. | —— | —— |
| 10. Adjusted charging system components on a track vehicle. | —— | —— |
| 11. Performed required PMCS. | —— | —— |
| 12. Verified fault had been corrected. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-1450-500-10 |  |
| TM 9-1450-500-20 | AR 385-10 |
| TM 9-1450-500-24P | AR 750-1 |
| TM 9-1450-646-10 | AR 750-43 |
| TM 9-1450-646-20-1 | DA PAM 738-750 |
| TM 9-2350-256-20 |  |
| TM 9-2350-256-24P-1 |  |
| TM 9-2350-256-24P-2 |  |

Maintain Track Vehicle  Hull Electrical Systems

091-63Y-2006

Conditions: In a garrison or field environment, with assistance and under supervision, given equipment required, M88 series vehicle, general mechanic's tool kit, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts if needed.

Note. If representative equipment is not available, use applicable equipment and associated references.

Standards: Maintained track vehicle  hull electrical systems IAW the applicable technical publications procedures and specifications. When this task was completed, the vehicle was fully mission-capable or maintenance actions required to be performed by other than 63Y personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Described how system/components operate and function. | —— | —— |
| 6. Inspected hull electrical system on a track vehicle. | —— | —— |
| 7. Repaired defective components of the hull electrical system on a track vehicle. | —— | —— |
| 8. Performed diagnostic procedures on hull electrical system components on a track vehicle. | —— | —— |
| 9. Replaced hull electrical system components on track vehicle. | —— | —— |
| 10. Performed required PMCS. | —— | —— |
| 11. Verified fault had been corrected. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
|  | AR 385-10 |
| TM 9-1450-500-10 | AR 750-1 |
| TM 9-1450-500-20 | AR 750-43 |
| TM 9-1450-500-24P | DA PAM 738-750 |
| TM 9-1450-646-10 |  |
| TM 9-1450-646-20-1 |  |
| TM 9-2350-256-20 |  |
| TM 9-2350-256-24P-1 |  |
| TM 9-2350-256-24P-2 |  |

Maintain Track Vehicle Suspension Systems

091-63Y-2007

Conditions: In a garrison or field environment, with assistance and under supervision, given equipment required, M88 series vehicle, general mechanic's tool kit, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts if needed.


Note. If representative equipment is not available, use applicable equipment and associated references.

Standards: Maintained track vehicle suspension systems IAW the applicable technical publications procedures, and specifications. When this task was completed, the vehicle was fully mission-capable or maintenance actions required to be performed by other than 63Y personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. `Selected/used applicable publications. | —— | —— |
| 2. Selected/used proper tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Described how systems/components operate and function. | —— | —— |
| 6. Inspected suspension system components on a track vehicle. | —— | —— |
| 7. Performed diagnostic procedures on suspension system components on a track vehicle. | —— | —— |
| 8. Repaired/replaced defective suspension system components on a track vehicle. | —— | —— |
| 9. Adjusted suspension system components as required on a track vehicle. | —— | —— |
| 10. Performed required PMCS. | —— | —— |
| 11. Verified fault had been corrected. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
|  | AR 385-10 |
| TM 9-2350-256-10 | AR 750-1 |
| TM 9-2350-256-20 | AR 750-43 |
| TM 9-2350-256-24P-1 | DA PAM 738-750 |
| TM 9-2350-261-20-2 |  |
| TM 9-2350-261-20-3 |  |

Maintain Track Vehicle Steering/Brake Systems

091-63Y-2008

Conditions: In a garrison or field environment, with assistance and under supervision, given equipment required, M88 series vehicle, general mechanic's tool kit, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts if needed.

Note. If representative equipment is not available, use applicable equipment and associated references.

Standards: Maintained track vehicle steering/brake systems IAW the applicable technical publications procedures and specifications. When this task was completed, the vehicle was fully mission-capable or maintenance actions required to be performed by other than 63Y personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Follow prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Described how system/components operate and function. | —— | —— |
| 6. Inspected the steering and brake system on a track vehicle. | —— | —— |
| 7. Performed diagnostic procedures on a steering and brake system on a track vehicle. | —— | —— |
| 8. Repaired/replaced defective steering and brake system components on a track vehicle. | —— | —— |
| 9. Adjusted system/components if required. | —— | —— |
| 10. Performed required PMCS. | —— | —— |
| 11. Verified fault had been corrected. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
|  | AR 385-10 |
| TM 9-1450-500-10 | AR 750-1 |
| TM 9-1450-500-20 | AR 750-43 |
| TM 9-1450-500-24P | DA PAM 738-750 |
| TM 9-1450-646-10 |  |
| TM 9-1450-646-20-1 |  |
| TM 9-2350-256-20 |  |
| TM 9-2350-256-24P-1 |  |
| TM 9-2350-261-20-1 |  |
| TM 9-2350-261-20-2 |  |

Maintain Track Vehicle Hydraulic Systems

091-63Y-2009

Conditions: In a garrison or field environment, with assistance and under supervision, given equipment required, M88 series vehicle, general mechanic's tool kit, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts if needed.

Note. If representative equipment is not available, use applicable equipment and associated references.

Standards: Maintained track vehicle hydraulic systems IAW the applicable technical publications procedures and specifications. When this task was completed, the vehicle was fully mission-capable, or maintenance actions required to be performed by other than 63Y personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Described how systems/components operate and function. | —— | —— |
| 6. Inspected hydraulic system on a track vehicle. | —— | —— |
| 7. Performed diagnostic procedures on a hydraulic system on a track vehicle. | —— | —— |
| 8. Replaced hydraulic system components on a track vehicle. | —— | —— |
| 9. Repaired hydraulic system components on a track vehicle. | —— | —— |
| 10. Performed required PMCS. | —— | —— |
| 11. Verified fault had been corrected. | —— | —— |
| 12. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
|  | AR 385-10 |
| TM 9-1450-500-10 | AR 750-1 |
| TM 9-1450-500-20 | AR 750-43 |
| TM 9-1450-646-10 | DA PAM 738-750 |
| TM 9-1450-646-20-1 |  |
| TM 9-2350-256-10 |  |
| TM 9-2350-256-20 |  |
| TM 9-2350-256-24P-1 |  |
| TM 9-2350-261-10 |  |

Maintain Fire Extinguisher/Suppression Systems

091-63Y-2010

Conditions: In a garrison or field environment, with assistance and under supervision, given equipment required, M88 series vehicle, general mechanic's tool kit, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts if needed.

Note. If representative equipment is not available, use applicable equipment and associated references.

Standards: Maintained fire extinguisher suppression systems IAW the applicable technical publications procedures and specifications. When this task was completed, the vehicle was fully mission-capable or maintenance actions required to be performed by other than 63Y personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Described how systems/components operate and function. | —— | —— |
| 6. Inspected fire extinguisher/suppression systems. | —— | —— |
| 7. Tested fire extinguisher/suppression systems. | —— | —— |
| 8. Repaired defective components on fire extinguisher/suppression system. | —— | —— |
| 9. Replaced fire extinguisher/suppression systems/components. | —— | —— |
| 10. Adjusted fire extinguisher/suppression systems/components. | —— | —— |
| 11. Performed required PMCS. | —— | —— |
| 12. Verified fault had been corrected. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-1450-500-10 | AR 385-10 |
| TM 9-1450-500-20 | AR 750-1 |
| TM 9-1450-646-10 | AR 750-43 |
| TM 9-1450-646-20-1 | DA PAM 738-750 |
| TM 9-1450-646-20-2 |  |
| TM 9-2350-256-10 |  |
| TM 9-2350-256-20 |  |
| TM 9-2350-256-24P-1 |  |
| TM 9-2350-261-10 |  |
| TM 9-2350-261-20-1 |  |

Maintain Auxiliary Power Unit (APU)

091-63Y-2011

Conditions: In a garrison or field environment, with assistance and under supervision, given equipment required, M88 series vehicle, general mechanic's tool kit, applicable special tools/TMDE, required safety equipment, applicable forms and references, and repair parts if needed.

Standards: Maintained Auxiliary Power Unit (APU) IAW the applicable technical publications procedures and specifications. When this task was completed, the vehicle was fully mission capable or maintenance actions required to be performed by other than 63Y personnel were identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used correct tools/TMDE. | —— | —— |
| 3. Followed prescribed safety procedures. | —— | —— |
| 4. Practiced maintenance discipline. | —— | —— |
| 5. Described how systems/components operate and function. | —— | —— |
| 6. Inspected APU. | —— | —— |
| 7. Performed diagnostic procedures on APU. | —— | —— |
| 8. Serviced APU. | —— | —— |
| 9. Repaired defective component on a auxiliary power unit (APU). | —— | —— |
| 10. Adjusted APU components. | —— | —— |
| 11. Performed required PMCS. | —— | —— |
| 12. Tested APU. | —— | —— |
| 13. Completed TAMMS forms, as required. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2350-256-10 | AR 385-10 |
| TM 9-2350-256-20 | AR 750-1 |
| TM 9-2350-256-24P-1 | AR 750-43 |
| TM 9-2350-261-10 | DA PAM 738-750 |
| TM 9-2350-261-20-1 |  |

Subject Area 2: Recovery (ASI)

Locate a Recovery Site

091-H8C-2001

Conditions: In a field or garrison environment given a representative track vehicle (M88 series), required materials, general mechanic's tool kit, and applicable TM(s).

Standards: Locate a recovery site to within 10 meters and identify primary and alternate recovery routes determining distance for both with no greater than a 10% error.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Identified terrain features. | —— | —— |
| 3. Identified map symbols and colors. | —— | —— |
| 4. Located site using military grid reference system. | —— | —— |
| 5. Calculated distance. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 21-26 | TC 43-35 |
| FM 21-31 |  |

Determine Recovery Methods

091-H8C-2002

Conditions: In a field or garrison environment given a representative track vehicle (M88 series), required materials, general mechanic's tool kit, and applicable TM(s).

Standards: Determine Recovery Methods, source of effort and mechanical advantage needed IAW references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected and used applicable publications. | —— | —— |
| 2. Reconnoitered area. | —— | —— |
| 3. Estimated situation. | —— | —— |
| 4. Calculated ratios. | —— | —— |
| 5. Obtained resistance. | —— | —— |
| 6. Verified solution. | —— | —— |
| 7. Erected rigging. | —— | —— |
| 8. Rechecked rigging. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 5-125 |  |
| FM 9-43-2 |  |
| TC 43-35 |  |

Operate Tactical Communications Equipment

091-H8C-2003

Conditions:  In a field or garrison environment given a representative track vehicle (M88 series), required materials, general mechanic's tool kit, and applicable TM(s).

Standards: The soldier will state the procedures to install, operate, use correct radio procedures for clear concise and secure communication IAW the appropriate publications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Prepared communication equipment for operation. | —— | —— |
| 3. Send tactical communications. | —— | —— |
| 4. Received tactical communications. | —— | —— |
| 5. Shut down tactical communication operation. | —— | —— |
| 6. Followed prescribed safety procedures. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 24-35 | FM 24-18 |
| TM 11-5820-890-10-3 | TC 43-35 |
|  | TM 11-5820-401-10-1 |
|  | TM 11-5820-401-10-2 |
|  | TM 11-5820-401-10-4 |
|  | TM 11-5830-340-12 |

Operate Metal Cutting Equipment

091-H8C-2004

Conditions: In a field or garrison environment given a representative track vehicle (M88 series), required materials, general mechanic's tool kit, and applicable TM(s).

Standards: Set up the oxyacetylene equipment, cut metal, and practice shop safety IAW the procedures in the applicable references.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Determined the method to cut metal. | —— | —— |
| 3. Prepared metal cutting equipment as required. | —— | —— |
| 4. Cut metal. | —— | —— |
| 5. Secured metal cutting equipment. | —— | —— |
| 6. Followed prescribed safety procedures. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO-GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TC 9-237 | AR 385-10 |
|  | AR 750-1 |
|  | DA PAM 738-750 |
|  | TC 43-35 |
|  | TM 9-243 |

Maintain Recovery Vehicle Weapons

091-H8T-2001

Conditions: In a field or garrison environment given a representative track  vehicle (M88 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Maintain the M88 series vehicle weapons in accordance with the Preventive Maintenance Checks and Services table, procedures and specifications of the applicable technical manual.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Use proper safety methods. | —— | —— |
| 3. Disassemble machine gun. | —— | —— |
| 4. Checked for broken or missing parts. | —— | —— |
| 5. Ensured all parts are clean and lubricated. | —— | —— |
| 6. Assemble machine gun. | —— | —— |
| 7. Set head-space and timing. | —— | —— |
| 8. Inspected machine gun mount for missing, cracked, or broken parts. | —— | —— |
| 9. Ensured launcher tubes are free of rust, dirt, and corrosion. | —— | —— |
| 10. Ensured that grenade launcher wiring harness connectors are connected. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO- GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2350-256-10 | AR 385-10 |
| TM 9-2350-256-20 | AR 750-1 |
| TM 9-2350-256-24P-1 | AR 750-43 |
| TM 9-2350-256-24P-2 | TM 9-8000 |
|  | TM-9-243 |

Perform Preventive Maintenance Checks and Services on Tracked Recovery Vehicle

091-H8T-2002

Conditions: In a field or garrison environment given a representative track vehicle (M88 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Inspect the M88 series vehicle in accordance with the Preventive Maintenance Checks and Services table of the applicable technical manual, and record deficiencies on DA Form 2404/5988-E IAW with DA Pam 738-750.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Selected/used proper tools/TMDE. | —— | —— |
| 3. Described operation of vehicle systems/subsystems. | —— | —— |
| 4. Determined readiness of system components. | —— | —— |
| 5. Identified deficiencies and shortcomings. | —— | —— |
| 6. Corrected shortcomings identified as operator maintenance. | —— | —— |
| 7. Followed prescribed safety procedures. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2350-256-10 | AR 385-10 |
| TM 9-2350-256-20 | AR 750-1 |
| TM 9-2350-256-24P-1 | AR 750-43 |
| TM 9-2350-256-24P-2 | TM 9-243 |
| TM 9-2350-292-10 | TM 9-8000 |

Use Basic Issue Items Related to Tracked Recovery Vehicle

091-H8T-2003

Conditions: In a field or garrison environment given a representative track vehicle (M88 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Remove, clean and store the recovery related COEI and selected BII IAW the procedures in TM 9-2350-256-10 and TM 9-2350-292-10.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Select/use applicable publications. | —— | —— |
| 2. Inventory and determine serviceability of BII. | —— | —— |
| 3. Repaired BII as required. | —— | —— |
| 4. Replaced BII as required. | —— | —— |
| 5. Used BII as required. | —— | —— |
| 6. Serviced BII as required | —— | —— |
| 7. Properly store BII. | —— | —— |
| 8. Followed prescribed safety procedures. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 9-43-2 | AR 750-1 |
| TM 9-2350-256-10 | AR 750-43 |
| TM 9-2350-256-20 | DA FORM 2404 |
| TM 9-2350-256-24P-1 | DA FORM 5988-E |
| TM 9-2350-256-24P-2 | TM 9-8000 |
| TM 9-2350-292-10 |  |

Drive Tracked Recovery Vehicle

091-H8T-2004

Conditions: In a field or garrison environment given a representative track vehicle (M88 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Negotiate obstacles in forward and reverse gears without stalling, jerking, getting stuck, or causing damage to the vehicle while obeying all safety procedures, traffic regulations and hand signals.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Select/use applicable publications. | —— | —— |
| 2. Perform PMCS. | —— | —— |
| 3. Start engine. | —— | —— |
| 4. Place vehicle in motion. | —— | —— |
| 5. Drive vehicle, maintaining proper engine speed when descending and ascending grades. | —— | —— |
| 6. Drive vehicle in reverse. | —— | —— |
| 7. Stop vehicle. | —— | —— |
| 8. Park vehicle. | —— | —— |
| 9. Stop engine ( normal and emergency procedures). | —— | —— |
| 10. Complete TAMMS forms as required. | —— | —— |
| 11. Follow prescribed safety procedures. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2350-256-10 | AR 385-10 |
| TM 9-2350-256-20 | AR 750-1 |
| TM 9-2350-256-24P-1 | AR 750-43 |
| TM 9-2350-256-24P-2 | TM 9-243 |
|  | TM 9-8000 |

Operate Auxiliary Power Unit

091-H8T-2005

Conditions: In a field or garrison environment given a representative track vehicle (M88 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Operate the APU and BII powered by the APU In accordance with the procedures in TM 9-2350-256-10 and TM 9-2350-292-10 without damage to the equipment.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Select/use applicable publications. | —— | —— |
| 2. Start APU. | —— | —— |
| 3. Actuated generator switch to charge batteries. | —— | —— |
| 4. Engaged hydraulic control levers to start refuel / defuel pump. | —— | —— |
| 5. Connected and operate hydraulic equipment. | —— | —— |
| 6. Shut down APU. | —— | —— |
| 7. Followed prescribed safety procedures. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2350-256-10 | AR 385-10 |
| TM 9-2350-256-20 | AR 750-1 |
| TM 9-2350-292-10 | AR 750-43 |
|  | TM 9-2350-256-24P-1 |
|  | TM 9-2350-256-24P-2 |
|  | TM 9-2350-256-34-1 |
|  | TM 9-2350-256-34-2 |
|  | TM 9-243 |
|  | TM 9-8000 |

Operate the Boom and Hoist Winch on a Tracked Recovery Vehicle

091-H8T-2006

Conditions: In a field or garrison environment given a representative track  vehicle (M88 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Rig and operate the Boom on the M88A1/M88A2 track recovery vehicle IAW the procedures in TM 9-2350-256-10 or TM 9-2350-292-10.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected / used applicable publications. | —— | —— |
| 2. Prepared vehicle for use of hydraulic equipment. | —— | —— |
| 3. Operated boom. | —— | —— |
| 4. Operated hoist winch. | —— | —— |
| 5. Secured hydraulic equipment as required. | —— | —— |
| 6. Followed prescribed safety procedures. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2350-256-10 | AR 385-10 |
| TM 9-2350-256-20 | AR 750-1 |
| TM 9-2350-256-34-2 | AR 750-43 |
|  | TM 9-2350-256-24P-1 |
|  | TM 9-2350-256-24P-2 |
|  | TM 9-2350-256-34-1 |
|  | TM 9-2350-292-10 |
|  | TM 9-243 |
|  | TM 9-8000 |

Operate the Spade on a Tracked Recovery Vehicle

091-H8T-2007

Conditions: In a field or garrison environment given a representative track vehicle (M88 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: The  spade must be operated IAW the applicable technical publications' procedures and specifications without injury to personnel or damage to equipment.  When this task is completed, the vehicle must be fully mission capable, or maintenance actions required to be performed by other than H8 SL 1/2 personnel must be identified.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Prepared vehicle for use of hydraulic equipment. | —— | —— |
| 3. Operated spade. | —— | —— |
| 4. Secured hydraulic equipment as required. | —— | —— |
| 5. Followed prescribed safety procedures. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2350-256-10 | AR 385-10 |
| TM 9-2350-256-20 | AR 750-1 |
| TM 9-2350-256-24P-1 | AR 750-43 |
| TM 9-2350-256-24P-2 | TM 9-243 |
| TM 9-2350-292-10 | TM 9-8000 |

Operate the Winch on a Tracked Recovery Vehicle

091-H8T-2008

Conditions: In a field or garrison environment given a representative track vehicle (M88 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Operate the main winch and auxiliary winch IAW the procedures in TM 9-2350-256-10 and TM 9-2350-292-10 without causing damage to the equipment or injury to personnel.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Prepared vehicle for use of hydraulic equipment. | —— | —— |
| 3. Operate main winch. | —— | —— |
| 4. Secured hydraulic equipment as required. | —— | —— |
| 5. Followed prescribed safety procedures. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2350-256-10 | AR 385-10 |
| TM 9-2350-256-20 | AR 750-1 |
| TM 9-2350-256-24P-1 | AR 750-43 |
| TM 9-2350-256-24P-2 | TM 9-243 |
| TM 9-2350-256-34-1 | TM 9-8000 |
| TM 9-2350-256-34-2 |  |
| TM 9-2350-292-10 |  |

Recover a Mired Tracked Vehicle

091-H8T-2009

Conditions: In a field or garrison environment given a representative track vehicle (M88 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Task must be accomplished IAW applicable technical publication's procedures and specifications. All safety precautions must be observed.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Determined method of rigging. | —— | —— |
| 3. Attached cables to the mired vehicle. | —— | —— |
| 4. Prepared recovery vehicle for recovery operations. | —— | —— |
| 5. Establish communication between vehicles. | —— | —— |
| 6. Recovered mired vehicle, ensuring that all safety practices are followed. | —— | —— |
| 7. Secured recovery equipment. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed. If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2350-256-10 | AR 385-10 |
| TM 9-2350-256-20 | AR 750-10 |
| TM 9-2350-256-24P-1 | AR 750-43 |
| TM 9-2350-256-24P-2 | DA PAM 738-750 |
| TM 9-2350-256-34-1 | TM 9-243 |
| TM 9-2350-256-34-2 | TM 9-8000 |

Recover an Overturned Tracked Vehicle

091-H8T-2010

Conditions: In a field or garrison environment given a representative track  vehicle (M88 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: The vehicle must be recovered from the overturned position IAW applicable technical publication's.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Positioned recovery vehicle. | —— | —— |
| 3. Attached cables to the overturned vehicle. | —— | —— |
| 4. Prepared recovery vehicle for recovery operations. | —— | —— |
| 5. Established communication with ground guide. | —— | —— |
| 6. Recovered overturned vehicle, ensuring that all safety practices are followed. | —— | —— |
| 7. Secured recovery equipment. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| TM 9-2350-256-10 | AR 385-10 |
| TM 9-2350-256-20 | AR 750-1 |
|  | AR 750-10 |
|  | AR 750-43 |
|  | TM 9-2350-256-24P-1 |
|  | TM 9-2350-256-24P-2 |
|  | TM 9-2350-256-34-1 |
|  | TM 9-2350-256-34-2 |

Lift and Tow a Disabled Vehicle

091-H8T-2011

Conditions: In a field or garrison environment given a representative track  vehicle (M88 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Lift and tow a disabled vehicle IAW applicable technical publications, procedures and specifications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Determined method for towing. | —— | —— |
| 3. Prepared vehicle for towing. | —— | —— |
| 4. Hooked up vehicle for towing. | —— | —— |
| 5. Followed prescribed safety procedures. | —— | —— |
| 6. Establish communication between vehicles. | —— | —— |
| 7. Towed vehicle to predetermined site. | —— | —— |
| 8. Disconnect vehicle. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed.  Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 5-125 | AR 385-10 |
| FM 9-43-2 | AR 750-1 |
| TM 9-2350-256-10 | AR 750-43 |
| TM 9-2350-256-20 | TM 9-243 |
| TM 9-2350-256-24P-1 | TM 9-8000 |
| TM 9-2350-256-24P-2 |  |

Cross Country Tow of a Tracked Vehicle

091-H8T-2012

Conditions: In a field or garrison environment given a representative track  vehicle (M88 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: Tow a disabled vehicle to a predetermined location without causing damage to the equipment or injury to personnel IAW applicable publications.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Followed prescribed safety procedures. | —— | —— |
| 3. Positioned recovery vehicle. | —— | —— |
| 4. Prepared vehicle for towing. | —— | —— |
| 5. Prepared recovery vehicle for towing operation. | —— | —— |
| 6. Attached towing bar to disabled vehicle. | —— | —— |
| 7. Operated boom. | —— | —— |
| 8. Towed disabled vehicle. | —— | —— |
| 9. Disconnected towed vehicle. | —— | —— |
| 10. Secured recovery equipment. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 5-125 | AR 385-10 |
| FM 9-43-2 | AR 750-1 |
| TM 9-2350-256-10 | AR 750-43 |
|  | TM 9-243 |
|  | TM 9-8000 |

Perform Field Expedient Recovery on a Tracked Vehicle

091-H8T-2013

Conditions: In a field or garrison environment given a representative track  vehicle (M88 series), required materials, general mechanic's tool kit, and applicable TM(s).

Note.  If representative equipment is not available, use applicable equipment and associated references.

Standards: The vehicle must be recovered using self/field expedient procedures IAW applicable technical publication's.

| Performance Measures | GO | NO GO |
| --- | --- | --- |
| 1. Selected/used applicable publications. | —— | —— |
| 2. Determined method of field expedient recovery. | —— | —— |
| 3. Prepared vehicle for field expedient recovery, as required. | —— | —— |
| 4. Performed vehicle field expedient recovery. | —— | —— |
| 5. Secured recovery equipment. | —— | —— |
| 6. Followed prescribed safety procedures. | —— | —— |

Evaluation Guidance:  Score the soldier GO if all steps were passed. Score the soldier NO GO if any step was failed.  If the soldier fails any step, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| FM 9-43-2 | AR 385-10 |
| TM 9-2350-256-10 | AR 750-1 |
| TM 9-2350-256-20 | AR 750-43 |

# APPENDIX A

# HANDS-ON EVALUATION (DA FORM 5164-R)

INSTRUCTIONS

(Excerpted from STP 21-24-SMCT, Appendix C)

DA Form 5164-R (Hands-On Evaluation) allows the trainer to keep a record of the performance measures a soldier passes or fails on each task.

# Before evaluation:

1.  Obtain a blank copy of DA Form 5164-R, which you may locally reproduce on 8 ½ x 11 paper.

2.  Enter the task title and 10-digit number from the STP task summary.

3.  In Column a, enter the performance measure numbers from the task summary.

4.  In Column b, enter the performance measure corresponding to the number in Column a (you may

abbreviate this information if necessary).

5.  Locally reproduce the partially completed form when evaluating more than one soldier on the task or

when evaluating the same soldier more than once.

# During evaluation:

1.  Enter the date just before evaluating the soldier's task performance.

2.  Enter the evaluator's name, the soldier's name, and the unit.

3.  For each performance measure in Column b, enter a check in Column c (PASS) or Column d (FAIL),

as appropriate.

4.  Compare the number of performance measures the soldier passes (and, if applicable, which ones)

against the task standards specified in the task summary.  If the standards are met or exceeded,

check the GO block under STATUS; otherwise, check the NO-GO block.

| HANDS-ON EVALUATION For use of this form, see AR 350-57; the proponent agency is ODCSOPS | DATE |
| --- | --- |
| TASK TITLE | TASK NUMBER |
| ITEM a | PERFORMANCE STEP TITLE b | SCORE (Check One) |
|  |  | PASS c | FAIL d |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
|  |  | P | F |
| EVALUATOR'S NAME | UNIT |
| SOLDIER'S NAME | STATUS GO NO GO |

DA FORM 5164-R, SEP 85                        EDITION OF DEC 82 IS OBSOLETE                                                            USAPPC V2.00

91APPENDIX B

# FIELD EXPEDIENT SQUAD BOOK (DA FORM 5165-R)

INSTRUCTIONS

DA Form 5165-R (Field Expedient Squad Book) allows the trainer to keep a record of task proficiency for a group of soldiers.

# Before evaluation:

1.  Obtain a blank copy of DA Form 5165-R, which you may locally reproduce on 8 ½ x 11 paper.

2.  Locally reproduce the partially completed form if you are evaluating more than nine soldiers.

# During evaluation:

1.  Enter the names of the soldiers you are evaluating, one name per column, at the top of the form.

2.  Under STATUS, record (in pencil) the date in the GO block if the soldier demonstrated task

proficiency to soldier's manual standards.  Keep this information current by always recording the most

recent date on which the soldier demonstrated task proficiency.  Record the date in the NO-GO block

if the soldier failed to demonstrate task proficiency to soldier's manual standards.  Soldiers who failed

to perform the task should be retrained and reevaluated until they can meet the standards. When the

standards are met, enter the date in the appropriate GO block and erase the previous entry from the

NO-GO block.

# After evaluation:

# 1.  Read down each column (GO/NO-GO) to determine the training status of an individual. This will give

you a quick indication of which tasks a soldier needs training on.

# 2.  Read across the rows for each task to determine the training status of all soldiers.  You can readily

see which tasks to focus training on.

# 3.  Line through the STATUS column of any soldier who leaves the unit.

# This page intentionally left blank

88GLOSSARY

# Terms

# Advanced individual training (AIT)

Training given to enlisted personnel upon completion of basic training that will qualify them for award of a military occupational specialty (MOS).

# Common core training

Direct training requirement for specific courses, grade levels, or organization levels.  It consists of critical tasks performed by individuals at specific grade levels regardless of MOS or career field.  Common core tasks are common soldier, common skill level, and organizational level shared tasks.

# Common soldier task

# See "Task" and "Individual critical task."

# Critical task

# See "task," critical collective task," and "critical individual task."

# Evaluation

Measurement of the demonstrated ability of soldiers or units to perform a task, and supporting skill and knowledge; or learning objective against the established standard.

# Soldier Manual of Common Tasks (SMCT)

A publication listing the critical tasks for each skill level of an MOS.  It provides the performance steps (measures), the condition under which the tasks are performed, the standards that must be met, and an instrument for evaluating task performance.

# Student Evaluation Plan

A plan that details how the proponent school will determine if the student has demonstrated a sufficient level of competency to pass the specified course or training.  It specifically identifies course completion requirements to include the minimum passing score (GO/NO GO) for each written or performance examination, final grade requirement, minimum course attendance requirements (if applicable); and specific tests that must be satisfactorily completed to graduate.  It very specifically identifies how the student's performance will be evaluated.  Specific lessons tested in each test are identified.  Counseling and retesting policy are delineated.  Other evaluations, such as the Army Weight Control Program and Army Physical Fitness Test, that impact on graduation are identified, and their requirements are included.

# Support Unit

Unit that acts with, and assists, or protects another unit.  A support unit does not act under the orders of the commander of the protected unit, because it is not an organic part.

# THE Army Training System (TATS) Course

A course designed to train the same MOS/AOC skill level or ASI, LIC, SQI, SI within the Army.  The course ensures standardization by training all course critical tasks to task performance standard.  It may be trained at different sites and may involve use of different media/methods to train the various phases/modules/lessons.

This page intentionally left blank

99REFERENCES

Required Publications

# Army Regulations

AR 385-10	The Army Safety Program (This item is included on EM 0001)  23 May 1988

AR 750-1	Army Materiel Maintenance Policy and Retail Maintenance Operations (This Item is Included on EM 0001)  1 August 1994

AR 750-10	Maintenance of Supplies and Equipment (Included on EM 0001)  8 August 2000

AR 750-43	Army Test, Measurement and Diagnostic Equipment Program (This Item Is Included on EM 0001)  28 November 1997

# Field Manuals

FM 21-26	Map Reading and Land Navigation  7 May 1993

FM 21-31	Topographic Symbols (Reprinted w/ Basic Incl C1) (This item is included on EM 0028)  19 June 1961

FM 24-35	(O) Signal Operation Instructions "The SOI"  26 October 1990

FM 5-125	Rigging Techniques, Procedures, and Applications (This Item is Included on EM 0028)  3 October 1995

FM 9-43-2	Recovery and Battlefield Damage Assessment and Repair (FMFRP 4-34; TO 36-1-181)  3 October 1995

# Training Circulars

TC 43-35	Recovery Training  3 October 1995

TC 9-237	Operator's Circular Welding Theory and Application (This item is included on EM 0028)  7 May 1993

# Technical Manuals

TM 9-243	Use And Care of Hand Tools And Measuring Tools [M6290-AJ-MAN-010; To 32-1-101; TM-10209-10/1] (Reprinted W/Basic InclC1-2) (This Item is Included on EM 0178)  12 December 1983

TM 9-8000	Principles of Automotive Vehicles (Reprinted W/Basic Incl C1)  25 October 1985

TM-9-243	TM-9-243

TM 9-1450-1431-14&P	Operation and Maintenance Instructions With Illustrated Parts Breakdown Field Level for Guided Missile Coolant Recharge Unit, GCU-31A/E PN 9138019  1 June 1993

TM 9-1450-500-10	Operator's Manual for Loader-Transporter, Guided Missile  17 March 1988

TM 9-1450-500-20	Organizational Maintenance Manual for Loader-Transporter, Guided Missile  29 June 1979

TM 9-1450-500-24P	Organizational, Direct Support, and General Support Maintenance Repair Parts and Special Tools List for  Loader-Transporter , Guided Missile  8 November 1993

TM 9-1450-500-34	Direct and General Support Maintenance Manual: Loader-Transporter, Guided Missile  29 June 1979

TM 9-1450-646-10	Operator's Manual For Carrier, Multiple Rocket Launch System,  M993 (NSN 2350-01-091-5405) (Reprinted w/ Basic Incl C1-11) (This item is included on EM 0062)  3 August 1984

TM 9-1450-646-20-1	Unit Maintenance For Carrier, Multiple Rocket Launch System,  M993 (NSN 2350-01-091-5405) (Reprinted w/ Basic Incl C1-6) (This item is included on EM 0062)  1 July 1988

TM 9-1450-646-20-2	Unit Maintenance For Carrier, Multiple Rocket Launch System,  M993 (NSN 2350-01-091-5405) (Reprinted w/ Basic Incl C1-7) (This item is included on EM 0062)  7 July 1988

TM 9-1450-646-20-3	Unit Maintenance For Carrier, Multiple Rocket Launch System,  M993 (NSN 2350-01-091-5405) (Reprinted w/ Basic Incl C1-7) (This item is included on EM 0062)  8 July 1998

TM 9-1450-646-20-4	Unit Maintenance For Carrier, Multiple Rocket Launch System,  M993 (NSN 2350-01-091-5405) (Reprinted w/ Basic Incl C1-7) (This item is included on EM 0062)  8 July 1988

TM 9-1450-646-20-5	Unit Maintenance For Carrier, Multiple Rocket Launch System,  M993 (NSN 2350-01-091-5405) (Reprinted w/ Basic Incl C1-7) (This item is included on EM 0062)  8 July 1988

TM 9-1450-646-BD	Battlefield Damage Assessment and Repair for Carrier, MLRS, M993 (NSN 2350-01-091-5405) (This item is included on EM 0062)  18 July 1989

TM 9-2350-256-10	Operator's Manual for Recovery Vehicle, Full Tracked, Medium, M88A1 (NSN 2350-00-122-6826) (Reprinted w/Basic Incl C1) (This item is included on EM 0036)  31 March 1998

TM 9-2350-256-20	Unit Maintenance Manual for Recovery Vehicle, Full Tracked, Medium, M88A1 (NSN 2350-00-122-6826) (This Item is Included on EM 0036)  15 July 1996

TM 9-2350-261-10	Operator's Manual for Carrier, Personnel, Full-Tracked, Armored, M113A2 (NSN 2350-01-068-4077); Carrier, Command Post, Light: Tracked M577A2 (2350-01-068-4089) (Reprinted w/ Basic Incl 1-5) (This item included on EM 0040 and EM 0078  12 July 1990

TM 9-2350-261-20-1	Unit Maintenance Manual for Carrier, Personnel, Full-Tracked, Armored, M113A2 (NSN 2350-01-068-4077); Carrier, Command Post, Light: Tracked M577A2 (2350-01-068-4089) (Reprinted w/ Basic Incl 1-4)(This item included on EM 0040 and EM 0078)  11 July 1990

TM 9-2350-261-20-2	Unit Maintenance Manual for Carrier, Personnel, Full-Tracked, Armored, M113A2 (NSN 2350-01-068-4077); Carrier, Command Post, Light: Tracked M577A2 (2350-01-068-4089) (Reprinted w/ Basic Incl 1-4)(This item included on EM 0040 and EM 0078)  11 July 1990

TM 9-4910-571-12&P	Operator's and Organizational Maintenance Manual Including Repair Parts and Special Tools List for Simplified Test Equipment for Internal Combustion Engines (Reprinted W/Basic Incl C1-2)(This Item is Included on EM 0068)  25 March 1988

TM 11-5820-401-10-1	Operator's Manual for Radio Sets AN/VRC-12 (NSN 5820-00-223-7412),  AN/VRC-43  (NSN 5820-00-223-7415), AN/VRC-44  (NSN 5820-00-223-7417), AN/VRC-45  (NSN 5820-00-223-7418), AN/VRC-45 (NSN 5820-00-223-7418), AN/VRC-46, -47, -48, and -49  15 January 1986

TM 11-5820-401-10-2	Operator's Manual for Radio Sets AN/VRC-12 (NSN 5820-00-223-7412),  AN/VRC-43  (NSN 5820-00-223-7415), AN/VRC-44  (NSN 5820-00-223-7417), AN/VRC-45  (NSN 5820-00-223-7418), AN/VRC-45 (NSN 5820-00-223-7418), AN/VRC-46, -47, -48, and -49  23 November 1982

TM 11-5820-401-10-4	Operator's Quick Checks for Receiver-Transmitter, RT-246 ( )/VRC (NSN 5820-00-892-0623) and RT-524 ( )/ (5820-00-892-0622) (This item Included on EM 0062 & EM 0079)  16 October 1980

TM 11-5830-340-12	Operator's and Unit  Organizational Maintenance Manual for Intercommunication Set AN/VIC-1 and Control, Intercommunication Set, C-10456/VRC (This Item is Included on EM 0063)  15 January 1986

# Training Circulars

TC 43-35	Recovery Training  3 October 1995

# Department of Army Pamphlets

DA PAM 738-750	Functional Users Manual for The Army Maintenance Management System (TAMMS) (This Item is Included on EM 0001)  1 August 1994

# THIS PAGE INTENTIONALLY LEFT BLANK

Order of the Secretary of the Army:

# ERIC K. SHINSEKI

General, United States Army

Chief of Staff

Official:

# JOEL B. HUDSON

# Administrative Assistant to the

Secretary of the Army

0123309

DISTRIBUTION:

Active Army, US Army Reserve, and National Guard:  Not to be distributed.

Electronic Means Only

# Footnotes

DISTRIBUTION RESTRICTION: Approved for public release; distribution is unlimited.

HEADQUARTERS, DEPARTMENT OF THE ARMY